## Slide 1
Bioreaction

## Slide 2: Bioreactors
Biofilters
Biotrickling filters
Bioscrubbers

## Slide 3
Microbial Population Requirements
Sufficient moisture
Sufficient nutrients
Temperature of 60°F to 85°F
pH of 6 to 8

## Slide 4: Biofilter System

## Slide 5: Biotrickling Filter System

## Slide 6: Bioscrubber System

## Slide 7
Chapter 6
Oxidation

## Slide 8
Types of Oxidization Processes
Flares
Thermal oxidizers
  Dedicated units
  Process heaters and boilers
Catalytic oxidizers

## Slide 9: Elevated Flare

## Slide 10: Enclosed Ground Flare

## Slide 11: Thermal Oxidizer

## Slide 12
Parameters Affecting Performance
Temperature
Residence time
VOC composition and concentration

## Slide 13: Temperature
>100°F above auto-ignition temperature
Reaction rate increases with temperature
>1,300°F to convert CO to CO2
• Typically 1,300-1,800°F

## Slide 14: Auto-ignition Temperatures
Compound | Temperature (F)
Acetone | 870
Acetonitrile | 970
Isopropyl Alcohol (IPA) | 780
Methanol | 878
Methyl Ethyl Ketone | 759
Toluene | 896
Xylene | 867

## Slide 15: Residence Time
Q = actual volumetric flow rate V = effective volume
Typically 0.3-2.0 seconds

## Slide 16
80
0
...
c
Residence time
...
<.>
60
...
"C1>'
".'.C.
0.001
c
.."...'.
0
D..
40
20
100
600
800 1000
1800
1200 1400
Temperature , °F
1600

## Slide 17
VOC Composition and Concentration
Composition affects oxidation temperature
Reaction rate increases with concentration
Source of energy
  100% LEL vapors contain about 50 Btu/scf
  Oxidizing 1% LEL causes about a 27°F temperature rise in the gas stream

## Slide 18
Recuperative Thermal Oxidizer

## Slide 19
Regenerative Thermal Oxidizer
Induced draft fan
Ceramic media
Valves

## Slide 20: Flameless Thermal Oxidizer

## Slide 21: Process Heaters and Boilers
Boiler must operate at 40-100% of full load
Contaminated gas stream flow rate should be small portion of total
Nothing corrosive or that causes deposits

## Slide 22: Catalytic Oxidizer

## Slide 24: Catalyst Materials
Noble metal oxides
  Platinum
  Palladium
  Rhodium
Base metal oxides
  Manganese
  Chromium
  Vanadium

## Slide 25: Catalyst Configurations
Fixed bed
  Beaded
  Monolithic
Fluidized bed

## Slide 26
Active precious metal site Exhaust gas

## Slide 29
Parameters Affecting Performance
Temperature
Space velocity
VOC composition and concentration
Presence of poisons or inhibitors

## Slide 30: Temperature
~100°F above light-off temperature
Reaction rate increases with temperature
Typical inlet temperature: 500-600°F
Typical outlet temperature: 700-900°F
Maximum outlet temperature: 1,100-1,200°F

## Slide 31
Generic Light-Off Curve

## Slide 32: Space Velocity
Qstd = standard volumetric flow rate (60°F) BV = catalyst bed volume
Efficiency increases with decreasing space velocity
Typically 30,000-40,000 hr-1 for noble metals 10,000-15,000 hr-1 for base metals

## Slide 33
VOC Composition and Concentration
Composition affects oxidation temperature
Reaction rate increases with concentration
Source of energy
  100% LEL vapors contain about 50 Btu/scf
  Oxidizing 1% LEL causes about a 27°F temperature rise in the gas stream

## Slide 34
Catalyst Performance Problems
Fouling
Poisoning
Masking
Thermal aging

## Slide 35: Catalytic Oxidizer

## Slide 36: Instrumentation
Temperatures
VOC concentration

## Slide 37: Design Review
Temperature
Combustion air requirements
Residence time
Fuel requirements
  Required temperature increase
  Heat from combustion of contaminants
  Available heat from combustion of fuel

## Slide 38: Design Review
Temperature
Combustion air requirements
Residence time
Fuel requirements
  Required temperature increase
  Heat from combustion of contaminants
  Available heat from combustion of fuel

## Slide 39: Combustion Air Requirements
Stoichiometric air
CH4 + 2O2  CO2 + 2H2O
Excess air

## Slide 40: Residence Time
Q = actual volumetric flow rate V = effective volume

## Slide 41
Problems 6-1 & 6-2

## Slide 42: Design Review
Temperature
Combustion air requirements
Residence time
Fuel requirements
  Required temperature increase
  Heat from combustion of contaminants
  Available heat from combustion of fuel

## Slide 43
Heat Content or Enthalpy
(Btu/lbm)
Sensible heat
Latent heat

## Slide 44: Heat Content Change
H = Cp(T - To)
H = Cp2 (T2 - To) - Cp1 (T1
- To)
where:
H = change in enthalpy, Btu/lbm
H = Cp (T2 - T1)
q = m H = m Cp (T2 - T1)
where: | H | = enthalpy, Btu/lbm
 | Cp | = specific heat at temperature T, Btu/lbmF
 | T To | = temperature of the substance, F = reference temperature, F
where: | q | = heat rate, Btu/hr
 | m | = mass flow rate of gases, lbm/hr

## Slide 45: Sensible Heats
Gas Temp. (F) | O2 | N2 | CO2 | H2O | Air
60 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
100 | 8.8 | 6.4 | 5.8 | 17.8 | 9.6
200 | 30.9 | 34.8 | 29.3 | 62.7 | 33.6
300 | 53.4 | 59.8 | 51.3 | 108.2 | 57.8
400 | 76.2 | 84.9 | 74.9 | 154.3 | 82.1
500 | 99.5 | 110.1 | 99.1 | 201.0 | 106.7
600 | 123.2 | 135.6 | 124.5 | 248.7 | 131.6
700 | 147.2 | 161.4 | 150.2 | 297.1 | 156.7
800 | 171.7 | 187.4 | 176.8 | 346.4 | 182.2
900 | 196.5 | 213.8 | 204.1 | 396.7 | 211.4
1000 | 221.6 | 240.5 | 231.9 | 447.7 | 234.1
1100 | 247.0 | 267.5 | 260.2 | 499.7 | 260.5
1200 | 272.7 | 294.9 | 289.0 | 552.9 | 287.2
1300 | 298.5 | 326.1 | 318.0 | 606.8 | 314.2
1400 | 324.6 | 350.5 | 347.6 | 661.3 | 341.5
1500 | 350.8 | 378.7 | 377.6 | 717.6 | 369.0
2000 | 484.5 | 523.0 | 531.4 | 1003.1 | 509.5
2500 | 621.0 | 672.3 | 690.2 | 1318.1 | 654.3

## Slide 46
Heat Produced by Combustion
Gross heating value
  Sensible and latent heat lost in flue gases
  Available heat
Net heating value
  Sensible heat lost in flue gases
  Available heat

## Slide 47
:::- 140 000 r-
"T"'"""---
---.
.-- .....--- --.
--
Q I
-
C'3
120.000
_,
_,
_,
100.000
c.s
v
.c
v
...0
80,000
nl
..,
;...
<
60 .000
40 .000
I kavy fuel oil 14 ° A Pl I °J('.. 000 Bt u gal
Light fuel oil 36.5° A P!
138.000 Etu 'ga l
Commercial buta ne
32 10 Btu/ cf
1800
Commercial propa ne
2558 Bt u 1cf
1200
o---- ----, --
300 900
. .......... . -- ---
1500 2100 2700
Flue gas exi t lt>m pt•rc1 t t11<'. 0 f

## Slide 48
Problem 6-3

## Slide 49
Chapter 7
Condensation

## Slide 50: Types of Condensation Systems
Conventional systems
Refrigeration systems
Cryogenic systems

## Slide 51: Types of Condensers
Direct contact condensers
Surface condensers

## Slide 52
Direct Contact Condenser

## Slide 53: Ejector Condenser

## Slide 54: Shell and Tube Condenser

## Slide 55: Tube and Fin Condenser

## Slide 56: Refrigeration Cycle

## Slide 57: Refrigeration System

## Slide 58
Single Heat Exchanger Cryogenic System

## Slide 59
Dual Heat Exchanger Cryogenic System

## Slide 60
Direct Contact Cryogenic Condenser

## Slide 61: Instrumentation
Outlet gas temperature
Coolant flow rate
Coolant temperatures

## Slide 62: Design Review
Outlet concentration
Contact condenser coolant flow rate
Surface condenser surface area

## Slide 63: Vapor Pressure

## Slide 64
Problem 7-1

## Slide 65: Vapor Pressure
Antoine equation:
where:
P T
= vapor pressure, mm Hg
= temperature, °C
A,B,C = constants

## Slide 66
Problem 7-2

## Slide 67
Contact Condenser Coolant Flow Rate
q = mCpg (TGi - Tcond) + mHl + mCpc (Tcond - TLo) = LCpl(TLo - TLi)
where:
q = heat transfer rate, Btu/hr
m = mass flow rate of vapor, lbm/hr
L = mass flow rate of liquid coolant, lbm/hr
Cp= average specific heat of a gas, condensate or coolant, Btu/lbm F
T = temperature of gas or liquid streams, F Hl = heat of condensation, Btu/lbm

## Slide 68
Surface Condenser Surface Area
q = U A (Tm)
where:
Tm= log mean temperature difference, F
q | = | heat transfer rate, Btu/hr
U A | = = | overall heat transfer coefficient, Btu/hr·ft2·°F heat transfer surface area, ft2

## Slide 69: Heat Transfer Resistances

## Slide 70
Overall Heat Transfer Coefficients
Condensing Material | Cooling Liquid | U, Btu/hr·ft2·F
Organic vapor with high percent of noncondensables | Water | 20 - 60
High boiling hydrocarbon vapor (vacuum) | Water | 20 - 50
Low boiling hydrocarbon vapor | Water | 80 - 200
Hydrocarbon vapor and steam | Water | 80 - 100
Steam | Feedwater | 400 - 1000
Water | Water | 200 - 250

## Slide 71
Log Mean Temperature Difference

## Slide 72
(a) Cocurrent flow
TG1 r;----------.-._ _j
6T2
TL2
:::I
-
r..o...
Q)
a.
E
Q)
F TL1
TG1
TL2
TG2
Q....).
:::I
-
ro
.....
Q)
a.
E
Length of exchanger
(b) Countercurrent flow
Length of exchanger
(c) Isothermal condensation with countercurrent flow
Length of exchanger

## Slide 73
Problem 7-3

## Slide 74
Chapter 8
Control Techniques for Nitrogen Oxides

## Slide 75
NOX Formation Mechanisms
Thermal NOX
Formed by oxidation of nitrogen in the combustion air
Fuel NOX
Formed by oxidation of nitrogen in the fuel
Prompt NOX
Formed by early free-radical reactions in the flame

## Slide 76
Thermal NOx Formation
N2 + O2  2NO
NO + ½ O2  NO2

## Slide 77
Factors Affecting Thermal NOX Formation
Flame Temperature
Residence time of combustion gases in peak temperature zone of the flame
Amount of oxygen present in peak temperature zone of the flame

## Slide 78
...-...
M
20----
---+-
--+- -
----1
..E.....
C)
.:_1..
><
0
z 10 ----
---+-
---+-
0
1600
1700
1800 1900
Temperature (°C)
2000
2100

## Slide 79
Techniques for Reducing Thermal NOx
Reduce peak flame temperature
Reduce residence time at peak flame temperature
Reduce oxygen concentration in maximum temperature zone

## Slide 80
Fuel NOx Formation
Occurs by oxidation of organically bound nitrogen contained in the fuel
  Coal: 0.2-3.5 weight percent
  Fuel oil: 0.01-0.5 weight percent
  Natural gas: None
Approximately 20-60% of the fuel nitrogen is oxidized
Amount oxidized decreases as nitrogen content increases

## Slide 81
Factors Affecting Fuel NOx Formation
Combustion zone temperature
Oxygen levels in the vicinity of the flame
Fuel nitrogen content

## Slide 82
Techniques for Reducing Fuel NOX Formation
Decrease combustion temperature
Decrease oxygen concentration
Decrease fuel nitrogen content

## Slide 83
Prompt NOx Formation
Forms early in the combustion process due to free-radical reactions in the flame
Residence time is usually too short to generate high concentrations
Mechanism has greatest impact in fuel rich combustion zones
Mechanism is of minor importance in large-scale combustion systems

## Slide 84: Reducing Prompt NOX
Prompt reactions are not sensitive to peak gas temperatures. Therefore, combustion modifications do not have a strong influence on the NOX formed by this mechanism.

## Slide 85
NOx Control Systems
Combustion modifications
Fuel switching
Add-on control devices

## Slide 86
Boiler Combustion Modifications
Low excess air combustion
Off-stoichiometric combustion
Flue gas recirculation
Low NOx burners
Gas reburning

## Slide 87
Boiler Combustion Modifications
Low excess air combustion
Off-stoichiometric combustion
Flue gas recirculation
Low NOx burners
Gas reburning

## Slide 88
Effect of Oxygen on NOx Formation

## Slide 89
NOx Reduction with Low Excess Air Combustion
16-20% for gas- and oil-fired boilers with 2-7% excess air
~20% for coal-fired boilers with 20% excess air

## Slide 90
Off-Stoichiometric Combustion
Combustion occurs in two zones
  A primary zone with less than stoichiometric air (fuel rich)
  A secondary zone where the remaining combustion air is added (air rich)

## Slide 91: Use of Overfire Air (OFA)

## Slide 92
NOx Reduction with
Off-Stoichiometric Combustion
30-40% for gas- and oil-fired boilers
30-50% for coal-fired boilers

## Slide 93: Flue Gas Recirculaton (FGR)

## Slide 94
NOx Reduction with Flue Gas Recirculation
40-50% with recirculation of 20-30% of the exhaust gas in gas- and oil-fired boilers

## Slide 95
Low NOX Burners
Control techniques
Low excess air
Off-stoichiometric combustion
Combustion gas recirculation

## Slide 96: Dual Register Burner

## Slide 97
NOx Reduction with Low NOx Burners
Typically, 25-60%. Ultra Low NOx Burners have efficiencies approaching 80% and outlet concentrations less than 10 ppmv

## Slide 98: Gas Reburning

## Slide 99
NOx Reduction with Gas Reburning
Reductions of 50-70% have been demonstrated at full boiler load

## Slide 100
Gas Turbine Combustion Modifications
Lean, pre-mixed combustors
Rich/quench/lean combustors
Water or steam injection

## Slide 101: Fuel Switching
Coal nitrogen content
Fuel substitution
Gas co-firing

## Slide 102: Flue Gas Treatment
Selective non-catalytic reduction (SNCR)
Selective catalytic reduction (SCR)

## Slide 103
Selective Non-Catalytic Reduction

## Slide 104: SNCR Reactions

## Slide 105
100
80
zN
0
60
-
c:
0
-
40
(J
::::J
"C
Cl)
0:::
20
><
0z
0
0
-20
-40
1400
1800
Gas Temperature, Degrees Fahrenheit
2200

## Slide 106
100
Note:
Efficiencies are as shown only when injection occurs in proper
zN
.....
c
80
temperature range.
0
60
.....
(.)
:::::s
'tl
Q)
D::
><
40
0
z
20
0
0.2 0.4 0.6 0.8 1.0 1.2
Urea I NOx Molar Ratios
0.4 0.8 1.2 1.6 2.0 2.4
NH3 I NOx Molar Ratios

## Slide 107
NOx Reduction with SNCR
Typical reduction efficiencies for SNCR systems are 20-60%

## Slide 108: Selective Catalytic Reduction

## Slide 109: SCR Reactions
Temperature range: 550-750°F

## Slide 110
80
c
0
:.;:::;
(.)
::::s
'"O
Q)
et::
60
><
0
:z
0
40
0.8
0.9
1.0
1.1
1.2

## Slide 111: Catalyst Materials
Noble metals (e.g., platinum, palladium, rhodium)
Vanadium pentoxide
Titanium dioxide
Tungsten trioxide

## Slide 112: Sulfur Dioxide Oxidation

## Slide 113
Formation of Sulfate Compounds

## Slide 114: Common Catalyst Problems
Poisoning
Fouling
Masking
Sintering
Erosion

## Slide 115
NOx Reduction with SCR
Typical reduction efficiencies for SCR systems are 60-90%
Some gas turbines have outlet concentrations less than 4 ppm corrected to 15% oxygen

## Slide 116
Control Technique | Typical Applications | NOx Reduction Efficiencies, %
Combustion Modifications |  | 
Low Excess Air | Coal-Fired Boilers, Municipal Waste Incinerators | 15-30%
Staged Combustion | Coal-, Oil-, and Gas-Fired Boilers | 30-40%. 15-50%
Flue Gas Recirculation | Coal-, Oil- and Gas-Fired Boilers | 15-50%
Low NOx Burners | Coal-, Oil-, and Gas-Fired Boilers | 25-60%
Gas Rebuming | Coal-, Oil-, and Gas-Fired Boilers | 30-70%
Lean Combustors | Gas-Fired Turbines | > 90%
Water/Steam Injection | Gas-Fired Turbines | 60-75%
Flue Gas Treatment |  | 
SNCR | Coal-Fired Boilers, Municipal Waste Incinerators | 20-60 %
SCR | Coal-Fired Boilers, Gas Turbines | 80-90%
Fuel Switching |  | 
Low Nitrogen Coal | Coal-Fired Boilers Coal-Fired Boilers | No Data
Co-Firing | Coal-Fired Boilers | No Data

## Slide 117: Instrumentation
Reagent feed rates and injection conditions
Gas temperatures
Static pressure drop
Gas turbine steam or water flow rates

## Slide 118
Chapter 9
Control of Sulfur Oxides

## Slide 119
Sulfur Oxides Formation Mechanisms
S + O2  SO2 S + 1.5 O2  SO3
SO3 + H2O  H2SO4

## Slide 120
Air Coal
(100 units
of sulfur)
Burn
Flue gas so2 (94 to 95 units of sulfur)
Flue gas H2so4 (0.5 to 2 units
of sulfur)
Boiler ash
Economizer
Air preheater
Air preheater ash
Bottom ash (3 to 5.5 units of sulfur)

## Slide 121
SOx Control Systems
Flue gas desulfurization
Fuel treatment
Low sulfur fuel firing

## Slide 122
Flue Gas Desulfurization (FGD)

## Slide 123: Wet FGD Systems

## Slide 124
Non-Regenerative FGD Systems
Wet Systems:
Dry Systems:
Lime Spray Dryer
8%
Limestone | 50%
Lime | 20%
Dual-Alkali | 3%

## Slide 125: Regenerative FGD Systems
Wet Systems:
Limestone Wellman-Lord
4%
3%

## Slide 126: Limestone Scrubbing
SO2 + CaCO3  CaSO3 + CO2 CaSO3 + 0.5O2  CaSO4

## Slide 127
Clean flue gas
Mist eliminator
., --I...-..- wash water
Inlet flue gas
Lime/ --­ limestone
slurry
Makeup water
Solids to ill(
disposal
Thickener overflow tank

## Slide 128: Lime Scrubbing
SO2 + Ca(OH)2  CaSO3 + H2O CaSO3 + 0.5O2  CaSO4

## Slide 129: Reagent Preparation

## Slide 131: Dual Alkali Scrubbing
Absorption Reactions:
SO2 + Na2SO3 + H2O 2NaHSO3 NaHSO3 + 0.5O2  NaHSO4

## Slide 132: Dual Alkali Scrubbing
Regeneration Reactions:
2NaHSO3 +Ca(OH)2  Na2SO3 + CaSO3 + 2H2O NaHSO4 +Ca(OH)2  NaOH + CaSO3 + H2O

## Slide 133
Lime
Clean flue gas
Demister
Inlet flue gas
Absorption loop
- Recirculation -
tank
Liquid regeneration
loop
Lime addition tank
Clarifier
Underflow
Rotary
Vacuum Filter
Filtered solids to landfill

## Slide 134: Wellman-Lord Process
Absorption Reaction:
SO2 + Na2SO3 + H2O 2NaHSO3
Regeneration Reaction:
2NaHSO3  Na2SO3 + H2O + SO2

## Slide 135: Spray Dryer Dry Scrubbing

## Slide 136: Types of Atomizers
Rotary atomizers
Compressed air assisted nozzles

## Slide 137: Acid Gas Removal Reactions
SO2 + Ca(OH)2  CaSO3 + H2O 2HCl + Ca(OH)2  CaCl2 + 2H2O

## Slide 138
100
(.)
c
(])
(.)
&::::
(])
C'O
80
E
(])
L..
0N 70
en
90
T approach to saturation 18°F
22°F
0.5
1.0
1.5
2.0
Alkalinity ratio

## Slide 139
Dry Injection Dry Scrubbing

## Slide 140
Fluidized Bed Combustion

## Slide 141: Fuel Treatment
Coal gasification
Coal liquefaction
Coal cleaning
  Physical methods
  Chemical methods

## Slide 142
SOx Control Systems
Flue gas desulfurization
Fuel treatment
Low sulfur fuel firing

## Slide 143: Instrumentation
Flue gas oxygen concentration
Static pressure drop
pH
Alkali feed rates
Inlet and outlet gas temperatures

## Slide 144
Control of Greenhouse Gas Emissions
Chapter 10

## Slide 145: The Greenhouse Effect Wien’s Law
max T = 2,897 m-K
Sun @ 6,000 K: max = 0.5 m Earth @ 255 K: max = 11.4 m

## Slide 146: Greenhouse Gases (GHG)
Carbon Dioxide (CO2)
Methane (CH4)
Nitrous Oxide (N2O)
Fluorinated Gases

## Slide 147: Radiation Transmitted by the Atmosphere
0.2
1 10
70
c Downgoing Solar Radiation
V'I 70-75% Transmitted
c
Q)
+-'
c
Upgoing Thermal Radiation 15-30% Transmitted
100-+-+---'-_, ._.......................
.......----r-.rL-.,............_.....,..,.......,..._,_......,.................
.........,mn-r-t --
--..._.._,...
1= 75
50
Q)
0... 25
Q)
o+- ..-----
Ll!........!6
-.-----i.-.---..-.-.,::!!..::..._-.-
..--.--.---J..
V'I
+-'
c
Q)
c
0
a.
E
0
u
i....
0
ro
i....
+u-'
Q)
a.
V1
Total Absorption
and Scattering
0.2
1
10
Wavelength (µm)
70
 | Water Vapor Carbon Dioxide Oxygen and Ozone
Methane | 
Nitrous Oxide Rayleigh Scattering | 

## Slide 148: Global Warming Potential
Gas | Atmospheric Lifetime (Years) | 100-Year GWP
Carbon Dioxide | 50-200 | 1
Methane | 12±3 | 28-36
Nitrous oxide | 120 | 265-298
Fluorinated gases as a group | 1.5-209 | 124-22,800

## Slide 149
U.S. Environmental Protection Agency (2017}.Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015.

## Slide 150
Global Greenhouse Gas Emissions by Gas
F-gases 2%

## Slide 151
2015_,U.S._Carbon Dioxide_Emissions, BY. Source
Other (Non-Fossil Fuel Combustion) 7%
Residential &
Commercial
10%
U.S. EnvironmentalProtection Agency (2017). Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015.

## Slide 152
G) c
ib j.11
lb m
:::> :J
::r <
0 -·
f;; a
lb :J
G) 3
Q fl)
(/) :J
ni .....
3· !a!!..
a· n>
ii: a
§ o'
Q. :J
':!>
:::>' fl)
,,.... :J
!..'.?... _
l.l) "'
l.l) 0
0 ......
"s' '--:......J.
Vi :::>
.
0
.Q,
!-tl
0
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001 1
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
Carbon Dioxide Emissions
(Million Metric Tons C02 Equivalent)
..
..
0
0
0
..
0
0
0
0
0
0
.U. 1 .O. "I
0
0
0
.w.
0
0
0
0
0
0
.-....J
0
0
0

## Slide 153: Metba ne-Em1issions, BM Sou1r:ce
2015 U.S.
1
Manure Management 10%
U.S. Environmental Protection Agency {2017). Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015.

## Slide 154
Cl
c
;
I.I'
Ill
::i
•
m
::i
0c:
l6
Cl
s.
...
g
3
QI
Ill
"m'-::i
3
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
"-'·"..t.i
- 0
a a
o·
Q. ::i
Vl )>
_ .OQ
::i Ill
::i
.
.... _
:8
0 ....
. ""'
,... _
o ·
.... -
V'I :<:i
.
Ill
::i
-
0
<
0
-
c
Methane Emissions
(Million Metric Tons C02 Equivalent)
N
8 8
W
8
m
8 8
8
8
8
8

## Slide 155: 2015 1u.s.Nitr:ous Oxide Emissions, B Sou1r:ce
1
Manure Management 5%
Transportation
Other
2%
5%
"""'
Industry or Chemical Production 6%
Stationary Combustion 7%
U.S.Environmental Protection Agency (2017).Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015.

## Slide 156
C...i..)c.
(I) V>
(I) •
:::i m
:::l
0c: s......
Cl! 0
(I) :::l
Ci) 3
Q) (I)
Cl! :::l
m -
3
C-l!· ".....
!!?. 0
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
0:::l (I)
Cl! (")
Q) O'.
:::l 0
a. :::l
V> l>
:::l C(7IQ)
;ti:' :::l
.... _
\0 N
\0 0
0 ....
' .....
oN
·
.... -
V.1 :<::l
(I)
:::l
-
0
<
0
-
c
(n
Nitrous Oxide Emissions (Million Metric Tons C02 Equivalent)
N
0
0 0
N
0
W
W 0
0
0 0
0
0
0
0
0

## Slide 157
HCFC-22
Production 2%
Electrical Transmission and
Distribution 2%
Production and Processing of Aluminum and
Semiconductor Manufacture 3%
U.S. Environmental Protection Agency (2017). Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015.

## Slide 158
(..;.)c.
(·/)
::I m
':1" ::I
c0: ...
s.
V> 0
::I
(;) 3
Q)
V> ::I m ,...
3
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
-V>·-..0.
!!:!. 0
0 ....
::I
V>
Q)
(")
.
::I 0
c.. ::I
(/) )>
-::I·O'Q
';It:" ::I
!'?
.... _
IQ N
IQ 0
0 ....
'
....,
,
..., _
o....-·
V'I ::I
. <
:..:.I.
0...
<
0
-
c
Fluorinated Gas Emissions (Million Metric Tons C02 Equivalent)
N
0
+;:. m
0
oo
0
o
0
N +::-
0 0
m
0
0
N
0
0
00
0

## Slide 159
Commercial & Residential
12%
U.S.Environmental Protection Agency {2017). Inventory of U.S. Greenhouse Gas Emissions and Sinks: 1990-2015

## Slide 160
GHG Emissions by Industrial Sector

## Slide 161
Figure 1-2: Total 2002 U.S. Greenhouse Gas Emissions from Industrial Sources,by Sector (MMTC02E), Factorin in Purchased Electricity
Cement
4 %
Oil and Gas
24 %
Alumna and Aluninum
3%
I
Other Industrial Sectors
16%
2%
/ '
Metal Casting
1%
Total:

## Slide 162
GHG Emissions from Industrial Sources
EPA produced “white papers” that focus on the industrial sectors that emit the highest amounts of GHGs:
  Coal Fired Electric Generating Units (EGUs)
  Large Industrial/Commercial/Institutional Boilers
  Pulp and Paper
  Cement
  Iron and Steel Industry
  Refineries
  Nitric Acid Plants
These paper are located at: http://www.epa.gov/nsr/ghgpermitting.html

## Slide 163
Ci)c.
rt> Vl
rt> •
::i m
:::r ::l
0c:
s.
II> 0
rt> ::l
Ci) 3
Q) rt>
ImI>
:,.:.l.
3-·
II>
!!?. 0
0
0 ...
::l rt>
II> a
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
Q) •
::l 0
c.. ::l
Vl l>
-::l·Cr1tQ>
'11'" ::l
!'?
..... _
IO N
IO 0
0 .....
.....,
o·
,.., _
..... -
(..n :<:l
rt>
::l
...
0
-<
0
-
c
!n
Total GHG Emissions
( Million Metric Tons of C02 Equivalents)
"
8
0
N
"
8
0
w
"
8
0
...
8
0
,V'I
8
0
..°. '
8
0
......i
"
8
0
,oo
8
0

## Slide 164
Global Carbon Emissions from Fossil Fuels, 1900-2014
11,000
10,000
9,000
c
0
.0
'-
utO
8,000
7,000
Cl\
c
6,000
.....
5,000
4,000
·-
'-
-
Q>
c
3,000
·-
·-
2,000
1,000
0
1900 1910
1920
1930
1940
1950
1960
1970
1980
1990
2000
2010

## Slide 165
Emissions firom EossU F.uel
Japan 4%
Russian Federation 5%
2014 Global |  | 
 | 1(0 | 2

## Slide 166
0
t
China • •
United States
Russia India •
Japan Germany Canada
UK
Australia
Italy France
Ukraine Spain
Poland
Turkey Netherlands Romania Czech Rep.
Belgium Greece Belarus Austria Portugal
New Zealand
Bulgaria
Hungary Finland Ireland
Denmark SWeden Norway
Switzerland
GHG emissions (million tonnes C02 equivalent)
.....
0
0
0
N
0
0
0
0
0
0
<.n
0
0
0
O')
0
0
0
.......
0
0
0
0""
0
0
•0
N -"
0 CJ)
0 CJ)
00 0
00
0
0
0

## Slide 167: 406.53 ppm
410
400
390
380
370
360
350
340
330
320
.-.
E
Q.
.Q_..
c
·.-..
.c.u.
c
Q)
CcJ
0
(.)
N
0
(.)
Late t CO reading
2
October 25, 2018
Carbon dioxide concentration at Mauna Loa Observatory
Full Record ending October 27, 2018
SCRIPPS 10111•t1....
OCEANOGRAPHY --
2010 2015
1960
1965
1970
1975
1980
1985
1990
1995
2000
2005

## Slide 168: Global Temperatures

## Slide 169: Regulation of GHG
April 2, 2007: U.S. Supreme Court held that EPA has authority to regulate CO2 & other GHGs from new motor vehicles
Even though GHGs are “air pollution”, EPA still needed further findings to regulate them under CAA Title I (stationary sources) or Title II (mobile).
December 17, 2009: EPA Administrator found that current and projected GHG concentrations endanger the public health and welfare of current and future generations (the “endangerment finding”)

## Slide 170: GHG Reporting Program
October 30, 2009: EPA issued 40 CFR Part 98, which requires reporting of greenhouse gas (GHG) emissions
Suppliers of fossil fuels or industrial GHGs, manufacturers of vehicles and engines, and facilities that emit ≥ 25,000 metric tons per year of GHG emissions are required to submit annual reports to EPA. First reports were due September 30, 2011.

## Slide 171
Mobile Source GHG Regulation
May 7, 2010: EPA passed the first ever CO2 emission standards for light duty vehicles for years 2012 to 2016
Sept 15, 2011: GHG emissions standards
& fuel efficiency standards for medium & heavy-duty vehicles for years 2017 to 2025
March 7, 2017: Notice of intent to reconsider standards for years 2022 to 2025

## Slide 172: GHG Tailoring Rule
June 3, 2010: EPA sets thresholds for GHG emissions that define when permits under PSD & Title V Operating Permit programs are required
PSD: New:100,000 tpy of CO2e ; Modified: 75,000 tpy of CO2e
Title V: Existing or new sources with PTE ≥ 100,000 tpy of CO2e

## Slide 173
Revised NSPS for Oil and Gas Sector
August 2, 2016
Sets percent reduction and work-practice standards for reducing emissions of methane and VOCs from specific oil and gas sector operations

## Slide 174
NSPS for New EGUs
October 23, 2015
New steam generating units
  1,400 lb CO2/MWh gross
Modified/reconstructed steam generating units
  1,800 lb CO2/MWh gross for larger units (> 2,000 mmBtu/hr)
  2,000 lb CO2/MWh gross for smaller units (≤ 2,000 mmBtu/hr)
New/reconstructed stationary turbines
  1,000 lb CO2/MWh gross for base load units
  120 lb CO2/MWh gross for non-base load units
  120-160 lb CO2/MWh gross for multi-fuel units

## Slide 175
Clean Power Plan
December 22, 2015
Stayed by Supreme Course February 2016 Repeal Proposed October 10, 2017
Guidelines for states to follow in developing plans to control existing steam generating units and stationary turbines
Sets emission performance rates
  1,305 lb CO2/MWh for steam generating units
  771 lb CO2/MWh stationary turbines
Sets state-specific rate- and mass-based emission goals
By 2030, 32% emission reduction from 2005 expected

## Slide 176: Affordable Clean Energy Rule Proposed August 21, 2018
Defines BSER as on-site efficiency improvements
Provides states with a list of candidate technologies
Updates EPA’s New Source Review permitting program
Revises the implementing regulations

## Slide 177: GHG Emission Reduction Strategy
Reduce energy use
Reduce the use of fossil fuels, particularly coal, in the production of energy

## Slide 178: Reducing GHG Emissions
Alternative and renewal energy sources
Energy efficiency improvements
  EPA’s Energy Star Program incentives
  Energy Management Systems (EnMSs)
  Benchmarking/Energy Performance Indicators (EPI)
Carbon Capture and Storage (CCS)

## Slide 179: Alternative and Renewable Energy Sources
Alternative and Renewable Energy can:
  Improve efficiency
  Reduce GHG emissions
Solar, wind, geothermal, nuclear, and biomass technologies reduce GHG emissions from traditional combustion processes

## Slide 180: EPA’s Energy Star Program
Used by hundreds of U.S. manufacturers
Assists with stronger energy management
Emphasizes continuous improvement of energy performance

## Slide 181: Energy Management Systems (EnMSs)
Framework to manage energy
Facilitates improvement

## Slide 182: Benchmarking/Energy Performance Indicators (EPI)
Benchmarking
  Measures improvements in energy efficiency
  Set and track progress toward goals based on individual performance, or the industry
Plant Energy Performance Indicators (EPI)
  Part of the U.S. EPA ENERGY STAR Program
    Benchmarking tools establish ‘best in class’ for specific industrial sectors.

## Slide 183
Carbon Capture and Storage (CCS)
Separation of CO2 from other gases
Transportation of CO2 to storage location
Injection and long-term geologic storage

## Slide 184
CO2 Capture
Pre-combustion capture
Post-combustion capture
Oxy-combustion

## Slide 185: Pre-Combustion Capture

## Slide 186: Post-Combustion Capture

## Slide 187
CO2 Capture Media
Amine-based scrubbing systems
  Monoethanolamine
  Diethanolamine
  Methyldiethanolamine
  Diglycolamine
Mineral-based scrubbing systems
  Sodium hydroxide
  Lithium hydroxide
Solid sorbents (MOFs)
Membrane-based capture

## Slide 188: Oxy-Combustion

## Slide 189
Schematic diagram of possible CCS systems
Gas to domestic supply
-

## Slide 190
co2 Stored in Saline Formation