## Slide 1: Hot Mix Asphalt (HMA) Facilities

## Slide 2: Overview
Introduction
Emissions
Process
Control
Permit Requirements
Inspection Procedures
Notes: Discuss outline
Background: FIRST RECORDE USE OF ASPHAL BY HUMANS WAS BY THE Sumerians around 3,000 B.C. STATURES FROM THAT TIME PERIOD USED ASPHALT AS A BINDING SUBSTANCE INLAYING SHELLS, STONES OR PEARLS.
ANCIENT ASPHAL WAS USED TO PRESERVE MUMMIES, WATERPROOFING AND CEMENTING (THE BRICKS OF BABYLONIA.
1500 AD THE INCAS USED A COMPOSITION SIMILAR TO MODERN BITUMINOUS MACADAM TO PAVE PARTS OF THEIR HIGHWAY SYSTEM
1830 IT WAS USED FOR FOOT PATHS, 1850S ASPHALT ROADWAYS. THE FIRST IN THE US WERE IN 1870s. THE SOURCE WAS IN TRINIDAD NEAR THE COAST OF VENEZUELA

## Slide 3: Introduction
Industry Background
Over 125 Hot Mix Asphalt (HMA) facilities in CA
  Stationary
  Some transportable
HMA is combination of
  Hot aggregate,
  Hot liquid asphalt binder
  Filler
Recycled Hot Mix (RHM) is HMA with
  Crumb rubber (rubberized asphalt concrete)
  Reclaimed asphalt
Notes: DEFINITION OF HOT MIX ASPHALT
40 CFR…MEANS ANY FACILITY, USED TO MANUFACTURE HOT MIX ASPHALT BY HEATING AND DRYING AGGREGATE AND MIXING WITH ASPHALT CEMENTS.
RHM=recycled hot mix
RAP=reclaimed asphalt pavement

## Slide 4: Introduction
Industry Background
Two basic processes
  Batch
  Continuous mix
Batch change recipe based on customers order
Continuous mix one recipe at a time stored for up to 7 days in insulated silo
Notes: Differences between drum dryer has a Pugmill
Drum Mix—aggregate and asphalt combined in drum/Mixer

## Slide 5: Introduction
Permit Process Requirements
District issues an
“Authority to Construct”
Inspection conducted
  Usually includes a source test
All conditions met “Permit to Operate” is issued
Notes: NSPS FOR HMA JUNE 1973.
UNDER 40 CFR PART 60 SUBPART I STANDARDS FOR HOT MIX ASPHALT FACIITES.
NEW OR MODIFIED SOURCES
UNDER NSPS NO PM GREATER THAN .04 GR/DSCF (DEMONSTRATE THROUGH A SOURCE TEST) OR 20 PERCENT. LOCAL DISTRICTS MAYBE MORE STRINGENT.

## Slide 6: Emissions and Effects
HMA facilities emit pollutants such as PM, CO, NOx, SOx, VOCs and other toxic substances
NOx and VOCs are Ozone (O3) precursors each reacts with sunlight to form O3
Notes: CO INCOMPLETE COMBUSTION
NOX FUEL AND AIR NITROGEN
SULFUR FOUND IN FUELS
VOC ASPHALT AND FUEL
Pm FROM AGGREGATE

## Slide 7: Emissions
Typical HMA Pollutants | Emissions (tons/yr)
PM (total for all size categories) | 1500
PM10 | 700
PM2.5 | 400
CO | 800
NOx | 450
Total Organic Compounds | 200
Reactive Organic Gas | 200
SOx | 100
VOCs | 200
Notes: PM is all particulate matter in the HMA inventory.

## Slide 8: Emissions
AB 2588 Emission Inventory
Requires HMA facilities to submit an emission inventory
HMA emit 78 of the 730 listed “Toxic Substances”
Emission Estimates
  US EPA, AP-42;
  District; or
  Source Test
Notes: 25 tons of 1 criteria pollutants or combination of…

## Slide 9: Emissions
Criteria and Precursor Pollutants
Created during production, storage, and transport of HMA
PM from aggregate
Notes: Cutback and emulsified asphalt are considered area sources when applied at job sites.
BLUE SMOKE…ORGANIC GAS MEETS ATMOSPHERIC WATER AND PARTICULATES TO CREATE BLUE SMOKE

## Slide 10: Emissions
Criteria and Precursor Pollutants (cont.)
PM, CO, NOx, VOCs, and SOx from fuel combustion and storage of asphalt binder and HMA
Blue Smoke (VOCs) from production and loading
Notes: SET THE STAGE
SWITCH GEARS
TALK ABOUT THE INGREDIENTS, DIFFERENT PROCESS AND EQUIPMENT.
IMPORTANT TO REMEMBER THAT THERE ARE VAROUS SYSTEMS USED. GET FAMILIAR WITH THE SITE PRIOR TO THE INSPECTION BY GOING THROUGH THE FACILITY PERMIT.

## Slide 11: Process/Control
Hot Mix Facilities are Regulated Under Subpart OOO
  How much aggregate is processed
  Moisture content of the processed material
  Control efficiency of the air pollution control equipment
  Opacity
Notes: Focus will be to make visual observations
HAND OUT PERMIT AND OPEN UP DISCUSSION ABOUT -651-2-1 #2

## Slide 12: Process
Binder
Filler
Aggregate
Composition of HMA
Notes: RECIPE …HMAs BASIC INGREDIENTS
CAL TRANS HAS SPECIED STANDARDS USED FOR QAQC.
QUALITY CONTROL AND QUALITY ASSURANCE MANUAL FOR ASPHALT CONCRETE PRODUTION AND PLACEMENT. INITIAL TESTING OF THE MATERIAL AND DAILY REPORTS ARE REQUIRED.
BINDER HOLDS AGGREGATE IN PLACE AS IT CHANGES PHYSICAL STATES FROM A LIQUID TO A SOLID
THE AGGREGATE USED IS ROUGH EDGED TO ENSURE GOOD ADHESION.
ROUNDED AGGREGATE WHICH IS BETTER FOR CONCRETE.
SAND AND FILLERS, LIKE BAG HOUSE DUST,
ADD STRINGTH BY MAKING A SOLD MEDIAN RATHER THAN LEVING ANY GAPS THAT ALLOW SLIPPAGE OF THE AGGRETATE. GLUE

## Slide 13: The Process
Notes: Insert movie

## Slide 14: Process Binder Composition
Binder Terms
Asphalt Binder
  Includes asphalt cement and any material added to modify properties
Bitumen
  Class of dark colored (solid, semi solid, or viscous)
Notes:   Bitumen:
  1. cementitious substances natural or manufactured
  composed of high molecular weight hydrocarbons
…the original asphalt cement
Natural asphalt binder was used in the 19th century. In the US Trinidad (near Venezuela)
was the source of 90 % world wide.
It came from a lake.
Once free of water was to hard to use so flux was added using a petroleum distillation solvent from crude oil.
By the early 20th century used crude oil from CA and Texas. Today HMA binder is almost entirely from petroleum refining.

## Slide 15: Process Binder Composition
Crude Petroleum Distillation Fractions
Petroleum Gases
Aviation
Gasoline
Petrol
Kerosene jet fuel
Heating Oil
Furnace Oil Bitumen
Lubricants waxes
Diesel Fuel
Notes: Bitumens consist of the least volatile group of hydrocarbons and is crude oil heated in a large furnace to about 650F and partially vaporized.
Then fed into a distillation tower where the lighter ends are driven off.
The residue from the process is usually fed into a vacuum distillation unit where the heavier ends are driven off.
Additional desired prosperities can be obtained by blending crude oils before distillation or asphalt cements after distillation

## Slide 16: Process Asphalt Grading
Two grading methods
  Viscosity Grading of Binder
  Superpave Performance Grade (PG)
Notes: Viscosity is a measure of a fluids resistance to flow and asphalt binder viscosity is typically measured at 140 because it approximates to max.
HMA pavement surface temperature during the summer in the US.
PG = Superpave performance grade testes specifically designed to address HMA performance for rutting fatigue cracking and thermal cracking based on climate.
WHAT IS WRONG WITH THIS PICTURE? DO You think it is adequate secondary containment?
Temporary AST (30 days to 1yr) must have date, phone number. Most portable HMA plants are considered temporary storage.

## Slide 17: Process
Viscosity Grading of Binder
Viscosity test developed during the early part of the 20th century.
  AC
    Tests viscosity of binder to characterize viscosity as supplied (simulating condition before used)
  AR
    Tests viscosity of binder aged in a rolling thin-film oven (simulating HMA production)
Notes: Grading is performed on as supplied binders (AC grading) and aged residue samples (AR grading) at 140 F
Viscosity is a measure of a fluids resistance to flow and asphalt binder viscosity is typically measured at 140 because it approximates to max. temperature in the environment. Disadvantage it does not account for climate. Is suppose to simulate HMA pavement surface temperature during the summer in the US.
The picture is an illustration of tar in its natural state from the labrea tar pits
HANDOUT PAPER FROM WASHING EDU

## Slide 18: Process
Viscosity Grading of Binder (cont'd.)
PG (Superpave Performance Grade)
  Test developed in 1980-1990
  Based on performance of binder in relation to climate
  Temperature range is 115 to 180 F
  Address rutting, fatigue cracking, and thermal cracking
Notes: Laboratory test developed in the 1980s
PG = Superpave performance grade testes specifically designed to address HMA performance for rutting fatigue cracking and thermal cracking based on climate.
Asphalt binders are more stringent due to Superpave specification. Some refineries have reevaluated their commitment to asphalt production to de-emphasize or renew their efforts to produce high-quality binders

## Slide 19: Process
Conventional HMA Binder
Solid at room temperature
250 and 325 F from point of origin to the final destination
Softening binder adds VOCs by
  Adding softer grade asphalt
  Adding lighter petroleum oils
Notes: SOFENING BINDERS BECAUSE FLOW IS DESIRED FOR HANDLING BUT STRENGTH IS DESIRED IN USE
Basically, asphalt chemistry can be described as a microstructure as a dispersed polar fluid. A continuous three-dimensional association of polar molecules or asphaltenes in a fluid of non-polar or low-polarity molecule. All of the molecules are capable of forming dipolar intermolecular bonds of varying strength. The result is a material that behaves 1. elastically through the effects of polar molecule networks and 2. viscously because the various parts of the polar molecule network can move relative to one another due to their dispersion in the fluid non-polar molecules.
THEREFORE SOFTNESS IS DUE TO TEMPERATURE…
Higher temp results in oxidation…more brittle binder
see MSDS for temp, mixing and storage temp
SOFENING BINDERS BECAUSE FLOW IS DERSIRED FOR HANDLING BUT STRENGTH IS DESIRED IN USE
THEREFORE SOFTNESS IS DUE TO TEMPERATURE…
Higher temp results in oxidation…more brittle binder
see MSDS for temp, mixing and storage temp

## Slide 20: Process
Typical Alternative Asphalt Binder
Reclaimed asphalt pavement (RAP)
Used tires (crumb rubber)
Proprietary polymers
Anti-stripping agents (hydrated lime)
Recycled baghouse dust
Notes: Some asphalt cements require modification in order to meet specifications. Asphalt cement modification has been practiced for over 50 years but has received added attention in the past decade or so. The added attention can be attributed to the following factors (Roberts et al., 1996):
Increased demand on HMA pavements. Traffic volume, loads and tire pressures have increased substantially in recent years, which can cause increased rutting and cracking. Many modifiers can improve the asphalt binder's stiffness at normal service temperatures to increase rut resistance, while decreasing its stiffness at low temperatures to improve its resistance to thermal cracking.
Superpave asphalt binder specifications. Superpave asphalt binder specifications developed in the 1990s require asphalt binders to meet stiffness requirements at both high and low temperatures. In regions with extreme climatic conditions this is not possible without asphalt binder modification.
Environmental and economic issues. It is both environmentally and economically sound to recycle waste and industrial byproducts (such as tires, roofing shingles, glass and ash) in order to gain added benefit. Thus, when they can benefit the final product without creating an environmental liability they are often used as additives in HMA.
Public agency willingness to fund higher-cost asphalt additives. Modified asphalt cement is usually higher in initial cost than unmodified asphalt cement, but it should provide a longer service life with less maintenance.
There are numerous binder additives available on the market today. The benefits of modified asphalt cement can only be realized by a judicious selection of the modifier(s); not all modifiers are appropriate for all applications.

## Slide 21: Process
Polymer Modified Binders
proprietary blends added to bitumen
Formula varies depending on desired result of end product
Notes: In general, asphalt cement should be modified to achieve the following types of improvements (Roberts et al., 1996):
Lower stiffness (or viscosity) at the high temperatures associated with construction. This facilitates pumping of the liquid asphalt binder as well as mixing and compaction of HMA.
Higher stiffness at high service temperatures. This will reduce rutting and shoving.
Lower stiffness and faster relaxation properties at low service temperatures. This will reduce thermal cracking.
Asphalt is a complex chemical substance. Asphalts chemical microstructure is most influenced by its physical behaviors.
In general, asphalt cement should be modified to achieve the following types of improvements (Roberts et al., 1996):
Lower stiffness (or viscosity) at the high temperatures associated with construction. This facilitates pumping of the liquid asphalt binder as well as mixing and compaction of HMA.

## Slide 22: Process
Filler
Dust added to asphalt binder and aggregate to improve adhesion
Notes: Basically dust added with binder to clean, dry, hot aggregate. Filler prevents stripping of the binder from the agg. Over time
Asphalt adheres to aggregate because the polar molecules with the asphalt are attracted to the polar molecule on the aggregate surface or dust. Certain polar attractions are known to be disrupted by water (a polar molecule) the polar molecules with asphalt will vary in their ability to adhere to any on particular type of aggregate.

## Slide 23: Process

## Slide 24: Process
Hydrated Lime
Caltrans requires a lime-slurry-marination (LSM) where climate promotes stripping
Requires that mixture be stockpiled for 24 hours before use “marinated”

## Slide 25: Process
Hydrated Lime
Anti-stripping agent:
Added dry with binder
Added dry to wet or dry aggregate and “marinated” for several days
Added as lime slurry for immediate use or “marinated”
Notes: Is an anti-stripping agent designed to reduces cracks during freeze thaw cycles at higher elevation
Moisture damage. Since it is a polar molecule, water is readily accepted by the polar asphalt molecules. Water cause stripping and/or can decrease asphalt viscosity. It typically acts like a solvent in asphalt and results in reduced strength and increased rutting. When taken io the extreme, this same property can be used to produce asphalt emulsions. Interestingly, from a chemical point-of-view water should have a greater effect on polder asphalt. Oxidation causes aged asphalts to contain more polar molecules. The more polar molecules an asphalt contains, the more readily it will accept water. However, the oxidation aging effects probably counteract any moisture-related aging effects.

## Slide 26: Process
Anit-stripping Agents
Illustration of binder with anti- stripping agent and without anti-stripping agent
Notes: HMA with anti-stripping agents are stored at lower temperatures than conventional binder
Increased adhesion between the asphalt binder and aggregate in the presence of moisture.
Reduce the likelihood of stripping.
2 aggregate samples from the same source after they have been coated with asphalt binder.
The asphalt binder on left contain no anti-stripping modifier results in almost no aggregate-asphalt binder adhesion.
The asphalt binder used with the sample on the right contains 0.5% (by weight of asphalt binder) an anti-stripping modifier, which results in good aggregate-asphalt binder adhesion.

## Slide 27: Process
Alternative Binders
Kept at temperatures higher than conventional binder
Two types
  Polymer-modified asphalt cement
  Crumb rubber modified
Notes: View of a transportable HMA unit.
The customer brings in the unit when working on contracts for CALTRANS and moves to another location when the contract is finished.
This operation is often run at night and numerous nuisance complaints have been reported.
Name why nuisance might be an issue with type of operation.

## Slide 28: Process
Crumb Rubber
Added to binder to make crumb rubber modified (CRM)
75% scrap tire and 25% virgin rubber
Non-hazardous hydrocarbon polymer
Rubber-modified asphalt concrete (RAC)
Notes: Rubber is a polymer. PMAC provides better
rut resistance in high temperature,
protects from thermal cracking in low temp, costly…
styrene butadiene styrene (SBS) or styrene butadiene rubberized latex (SBR) have not been researched and there are no emission estimates in AP-42

## Slide 29: Process
Advantages of Crumb Rubber
Waste reduction
Less water
Quiet
Lasts Longer
BUT No regulatory relief from visible emission evaluation (VEE)
Notes: Cal Trans and the Highway Patrol like this stuff!!!
Improve pavement
durability,
reduce noise,
reduce temperature susceptibility, reduce cost
Less water on roads during rains/less accident/fatalities
And reduces scrap tire stockpiles
Major landfill problem

## Slide 30: Process

## Slide 31: Process Reclaimed Asphalt Pavement
RAP is
  Top layer of asphalt pavement removed
Developed because of energy, economic, and environmental concerns
RAP could be 30% of mix
Increases asphalt lifetime
May increase generation of Blue Smoke
Notes: Last longer than Conventional or Rubber
Reclaimed asphalt pavement (RAP) is added to HMA and called Recycled Hot Mix (RHM).
RAP is 10 to 30 % of mix.
CALTRANS allows for up to 15% in the recipe
AP42 states up to 50% RAP can be added without changing emissions.
Sometimes limited in use due to generation of blue smoke.

## Slide 32: Process RAP
Production temp of virgin aggregate is 500-800 F
RAP is heated through conductive heat transfer
RHM is 350 F
Notes: The aggregate is SUPER heated from virgin aggregate. Typical temp is 500 F
Convection heating of fluid
Rotary dryer. Super heater.
Hot recycling is so named because RAP is used as an aggregate in HMA (hot mix asphalt). In hot recycling, old HMA pavement is removed, broken down into aggregate-sized chunks (see Figure 2.16) and then incorporated into new HMA as an aggregate. There are two basic methods for accomplishing this: conventional recycled hot mix (RHM) and hot in-place recycling.
4.1.1 Recycled Hot Mix (RHM)
Recycled hot mix (RHM) is the most common way of using RAP. Basically, new HMA is produced at a batch or drum plant to which a predetermined percentage of RAP is added. RAP addition is typically 10 to 30 percent by weight although additions as high as 80 percent by weight have been done and additions as high as 90 to 100 percent by weight are feasible (FHWA, 2001c). There is ample evidence that HMA which incorporates RAP performs as well as HMA without RAP. Figure 2.17 shows two dense-graded HMA cores, one with RAP and one without.

## Slide 33: Process

## Slide 34: Process
Warm Mix Asphalt
Advantages
  Lower Production temp. 220 to 275 F
  Less energy
  Reduced cracking
Disadvantages
  Further testing to ensure QA/QC
  Rutting
  Workability
  Longer setting=traffic delays
Notes: EXERCISE 1
Hand out the article form HMA association
Lower temperature means lower emissions

## Slide 35: Process HMA Facility Types
Batch
Continuous Mix

## Slide 36: Process Batch Mix

## Slide 37: Control Equipment Emission Points from Batch Facilities
HMA Batch Mix Process
With Emission Points

## Slide 38: Process Batch Facility
Aggregate
  Stored in cold bins
  Moved by conveyor
  Sorted and weighted
  Dropped into dryer
  Elevated to top of batch tower and
  Separated

## Slide 39: Process Cold Bins Aggregate Stockpiles
Notes: Aggregate is sorted by size
and stored in piles or in cold storage bins prior to entering the dryer.
What areas are important to check…?Check to ensure the feed systems are working properly and that the dust suppression systems work.

## Slide 40
Process Cold Bins

## Slide 41: Process Cold Bins and Conveyors
Notes: Cold aggregate storage bins (cold bins) are directly connected to the hot mix asphalt plant via conveyor (Figure 303-7).
Each bin holds rocks of a specific size, e.g., 3/8 inch, 1/2 inch, 3/4 inch.
feeder below each bin.
fed onto the conveyor in measured amounts
dependent on the specifications of the hot mix asphalt. Crucial part of COUNTINOUS MIX Facility.
Batch
aggregate delivered to rotary dryer. A
Aggregate separated again before mixing with asphalt binder, in pugmill not critical that the proportions be exact at this point in the process.

## Slide 42: Batch Process Aggregate Dryer
Notes: Large ROTARY DRYER

## Slide 43: Batch Process Rotary Dryer
Notes: Rotary dryer counter flow design
flame at bottom of the dryer so aggregate is exposed to higher temperatures as moving down the dryer.
flights designed to keep aggregate out of flame so flame is not quenched

## Slide 44: Process Combustion and Basic Burner Design
FD Fan
WHY?
Notes: Forced Draft….Atomize and combine fuel and air to provide an air fuel mixture that produces a flame. Products of combustion are heat, water, carbon dioxide. But because air is approximately 78% Nitrogen, oxides of nitrogen are formed.
The choice of the fuel burned affects the amount of sulfur oxides (SOx) and nitrogen oxides (NOx) that will be produced. Because natural gas contains minimal fuel-bound sulfur and nitrogen, it is the cleanest burning fuel. Fuel oil has higher sulfur and nitrogen content. Natural gas or propane is used for the majority of facilities
Because combustion is an incomplete process other air pollutants produced are CO, VOCs, Sox, and particulate mater.
Time, temperature and turbulence are the keys to optimizing combustion.
HMA PLANTS USUALLY HAVE TWO FANS, THE BURNER BLOWER AND THE EXHAUST FAN.
BOTH OF THESE FANS MUST OPERATE EFFICIENTLY TO ENSURE PROPER COMBUSTION AND AIR FLOW IN THE HMA PROCESS.
BURNER BLOWER PROVED AIR AND BURNS FUEL. THE EXHAUST FAN PROVIDES ARI FOR COMUSTION AND REMOVES EXHAUST GASES, EXCESS AIR AND STEM FROM THE DRYER.

## Slide 45: Batch Process Rotary Dryer Counterflow Design
Notes: BATCH DESIGN: Rotary dryers use a counterflow design In the counterflow design, the burner is positioned at the exit end, the lower end, so aggregate is subjected to progressively hotter flames as it moves from the entry to the exit. This assures the aggregate achieves the desired temperature and moisture content. The flights near the burner end are designed to keep the aggregate out of the direct flame. Quenching the flame results in the release of unburned fuel.
Air Pollution Issues There are fewer problems with blue smoke production and with exit temperature of exhaust gases. Because the asphalt binder is in the drum, however, it is more susceptible to producing blue smoke than if it is introduced in a separate container.
Accessibility of the embedded burner is a major issue. Maintenance is difficult. Poor burner operation can result in increased emissions.
Control Methods Ducting from the higher, entrance end of the drum (the end opposite the burner) transports pollutants to the air pollution control equipment. Lower exhaust gas temperatures create fewer problems with baghouse operation (For details, see Subsection 307.2).
If problems persist with maintenance of the embedded burner or blue smoke, abandon the design for a newer one.

## Slide 46: Batch Process (cont’d)
Hot aggregate dropped from elevator to vibrating screens, sorted by size
Weighed, and dropped into pugmill for mixing with
Hot liquid asphalt binder and filler until coated
Dropped into truck for delivery

## Slide 47
Process

## Slide 48: Batch Process Hot Aggregate Conveyor to Pugmill
Conveyor from Dryer
Pugmill

## Slide 49
Covered Conveyor

## Slide 51
Batch Process
View of Pugmills
Hot Aggregate
Conveyor
HMA Drop
Notes: Batch Mix View of Pug mill and discharge shoot into trucks. Note blue smoke.

## Slide 54: Batch Mix Process without Pugmill
Newer design
All ingredients are mixed together in the drum and sent to silos
Better controls

## Slide 55: Batch Process Rotary Dryer/Mixer Combined
Notes: Utilizes a burner that applies heat directly to the aggregate as it tumbles.
Aggregate must be preheated before it and is mixed with the binder at the end of the drum. This system is a batch operation, but operates on the same principles as a continuous mix drum.
It usually lined with a brick refractory. The aggregate is heated to reduce the moisture content.

## Slide 56: View of Batch Operated Double Drum Mixer Down for Maintenance

## Slide 57: Inside View of Double Drum Mixer

## Slide 58: Continuous Mix Process
Notes: On of the differences between a batch operation and continuous mix is the view on the horizon. Batch mix operation tend to be horizontal because the mixing is done in a pugmill. where continuous mix the mixing is done in the drum and will tend to be vertical on the horizon…due to the HMA storage tanks.
HMA storage tanks at a continuous mix will be insulated.

## Slide 59: Emission Points from Continuous Feed
HMA Continuous Mix Process
With Emission Points

## Slide 60: Process Continuous Mix Facility Characteristics
HMA is continuously produced
No batch towers to segregate hot aggregate
Insulated heated storage silos are used instead of surge bins to store HMA
Production is horizontal verses vertical
Notes: KEY POINTS
HORIZONTAL VS VERTICAL
MOST R BATCH

## Slide 61
Process

## Slide 62: Process HMA Drum Design
Notes: One of the differences between a batch operation and continous mix is the view on the horizon. Batch mix operation tend to be horizonatal because the mixing is done in a pugmill. Where continous mix the mixing is done in the drum and will tend to be vertical on the horizon…due to the HMA storage tanks,
HMA storage tankds at a contious mix will be insulated silos and HMA can be stored for up to 7 days in the silos.
Typical storage of HMA at a batch operation is no more than 48 hours. The silos are not insulated.

## Slide 63: Process Drum Design
4 general designs
  Counter Flow Dryer Coater
  Parallel Flow Drum Mixer
  Double Barrel Drum Mixer
  Triple-Drumtm Mixer
Drum mixers two zones:
  primary for aggregate drying and heating
  secondary for mixing heated aggregate with binder and filler
Notes: Not having to lift the hot aggregate, asphalt binder, and filler up a batch tower allows for more compact HMA production. There are a variety of designs for equipment to dry and heat aggregate and then coat it with asphalt binder and filler to make HMA. Six different designs will be discussed in this subsection: · Parallel Flow Drum Mixer · Parallel Flow Dryer and Coater · Counterflow Drum Mixer with Embedded Burner · Counterflow Dryer and Coater · Double Barrel Drum Mixer · Triple-Drum™ Mixer
Regardless of design, most drum mixers have two zones: a primary zone for aggregate drying and heating zone, and a secondary zone for mixing hot aggregate with binder and filler to make HMA

## Slide 64: Counterflow Dryer and Coater
Notes: 2. Continuous Mix
WATER FROM COMBUSTION AND AGGREGATE MAY BE 1 TO 3 % BY WEIGHT THAT IS WHY THE binder is added in a separate drum than the burner flame, there are fewer problems with blue smoke production than with the previously mentioned designs. There are fewer problems with exit temperature of exhaust gases. The aggregate can be dried and heated for the entire length of the dryer before binder is added, increasing the effectiveness of the dryer.
Control Measures Ducting from the higher, entrance end of the drum (the end opposite the burner) transports pollutants to the air pollution control equipment. Lower exhaust gas temperatures create fewer problems with baghouse operation (For details, see Subsection 307.2).
Proper operation and maintenance of the equipment, especially the burner, minimizes air pollution problems with these components.

## Slide 65
Notes: TYPE CONINTOUS
HOT LIQUID ASPHALT AND BINDER INJECTED DISTANCE PROPORTIOAN TO BLUE SOME EIMISSIONS FROM FLAME FARTHER AWAY THE LESS CHANCE FOR BLUE SMOKE FORMATION T
aggregate is dried and heated in the first section of the drum as it tumbles through the flame
. Hot liquid asphalt binder and filler are injected into the last section of the drum. They are mixed with the aggregate until the aggregate is evenly coated with binder. HMA exits the lower end of the drum (Figure 304-5).
The aggregate is dried and heated in the first section of the drum as it tumbles through the flame of the burner. Hot liquid asphalt binder and filler are injected into the last section of the drum. They are mixed with the aggregate until the aggregate is evenly coated with binder. HMA exits the lower end of the drum (Figure 304-5).

## Slide 66: Double Barrel Drum Mixer
Notes: 3 MECHANICAL PUG MILL ENERGY & HEAT EFFIC. MIXING DRYER FLAME DOES NOT COME IN CONTACT WITH LIQUID ASPHALT AND GASES ARE RECIRCULATED BACK TO BURNER. LOWER EMISSIONS AND HEAT IS OIL NEVER COMES IN CONTACT WITH FLAME LITTLE OR NO BLUE SMOKE. Continuous batch he Double Barrel® uses the counterflow system to heat and dry aggregate in the inner drum. Hot aggregate then passes into the outer drum where it is mixed with asphalt binder and filler. Paddles are mounted on the outside of the inner drum. As the inner drum turns the paddles mix the components into HMA in the outer drum (Figure THE HOT FLUE GASES are recirculated back into the drum
There are fewer problems with blue smoke production and with exit temperature of exhaust gases than with the previously mentioned designs. Additionally, gases from the outer drum are drawn into the inner drum for more complete burning prior to ducting to the control equipment.
Control Methods Ducting from the higher, entrance end of the drum (the end opposite the burner) transports pollutants to the air pollution control equipment. Lower exhaust gas temperatures create fewer problems with baghouse operation (For details, see Subsection 307.2).
The design of the Double Barrel® appears to effectively address issues of air pollution and energy efficiency. This design appears to be an improvement over other drum mixer and dryer/coater designs because asphalt binder is not exposed to excess heat.

## Slide 67: Inside View of Double Drum Dryer Section

## Slide 68: Inside View of Double Drum Mixer Section

## Slide 69
Notes: SPECIFALLY DESIGNED TO MEET THE AIR POLLUTION CONTROL REQUIREMENTS WHEN PROCESSING RECYCLED ASPHALT
CONVECTION…THING OF THREE TYPES OF HEAT
RADIATION. W/O MEDIUM IN A VACUUM AN EXAMPLE IS A TRIPLE PAIN WINDOW YOU CAN STILL FEEL THE HEAT FRO THE SUN RADIATION.
CONCECTION…HEAT TRANSFER THROUGH A MOVING FLUID (HOT AIR IN THIS CASE IS THE FLUID) HEAT TRANSFER FROM ON PLACE TO ANOTHER DUE TO MOVEMENT OF THE OBJECT THROUGH THE FLUID. INTHIS CASE THE AGGREGATE MOVING THROUGH THE HOT AIR CREATED BY THE FLAME. HOT AIR IS BEING CARRED FROM THE TOP OF THE FLAME.
CONDUCTION…PHYSICAL CONTACT WITH THE FLAME. IN THE TRIPPLE DRUM PROCESS ALL THREE TYPES OF HEAT TRANSFER ARE HAPPENING AT ONCE.

## Slide 70: Triple-Drum
Notes: Triple-Drum™ Mixer is a design owned by the CMI Corporation. The Triple-Drum™ Mixer uses the counterflow system with an embedded burner to heat and dry aggregate in three zones and mix it with asphalt binder in the fourth zone (Figure 304-10). Cold, wet aggregate enters the higher end of the drum. The first zone veils the aggregate for drying and heating by convection. The second zone directs the aggregate to the outside of the drum in preparation for entering the third zone as it continues to heat by convection and conduction. The third zone is an expanded area of the drum that surrounds the housing for the burner and flame where the aggregate is further heated by radiation and conduction from the burner housing. This design prevents aggregate from quenching the flame (other uses will be discussed later in regard to adding reclaimed asphalt pavement). It also decreases heat loss from the shell into the atmosphere. Hot aggregate then passes into the fourth zone where it is mixed with hot asphalt binder. Hot mix asphalt exits the lower end of the drum (Figure 304-11).
Ducting from the higher, entrance end of the drum (the end opposite the burner) transports pollutants to the air pollution control equipment. Lower exhaust gas temperatures create fewer problems with baghouse operation (For details, see Subsection 307.2).
CMI claims that, when operated per manufacturer's recommendations, emissions of particulate from the exhaust stack of a HMA facility are 0.01 grain/DSCF or less when a Triple-Drum™ Mixer is used in conjunction with the CMI Roto-Aire baghouse. The U.S. EPA New Source Performance Standard is 0.04 grain/DSCF.3

## Slide 71: Process Asphalt Binder Storage
Notes: Asphalt binder is transferred from trucks to heated storage tanks. Hot oil is circulated through coils in the tank.
Asphalt binder is transferred from trucks to heated storage tanks. Hot oil is circulated through coils in the tank.
Tanks are individually labeled, and are equipped with secondary containment. Typically the secondary containment area can hold 110 % of the volume of the largest AST. Precipitation must be removed as needed to ensure adequate containment capacity. The liner must be free of crack and tears
Tanks should be in good shape with no rust. Pipes and valves are not are free of cracks and leaks.

## Slide 73
Underground Asphalt Storage Tanks
Notes: Or at older facilities the storage tanks may be underground storage for HMA.

## Slide 74: Emission Controls

## Slide 75: Control Aggregate
Wind-blown dust
Fugitive dust
Common Control methods
Notes: Wind-blown dust
  Nuisance
  Opacity
Fugitive dust
  Transfer of aggregate
Common Control methods
  Wetting,
  Applying a crusting agent
  Enclosed storage
  Windbreaks
Crusting agents can cause chemical reactions. Depending on the quality of the product a crusting agent may not be used.

## Slide 76: Process Cold Bin Dust Collection System
Notes: Ductwork from feeders and conveyor below bins to control emissions such as a baghouse.

## Slide 80
Dust Suppression?

## Slide 81: Emission Control Hot Aggregate Handling
Hot Aggregate Elevator
Discarded Aggregate Pile
Discard Chute
Notes: Hot dry aggregate exits the rotary dryer into an enclosed elevator that transports it to the top of the batch tower. Tiered vibrating screens segregate the hot aggregate by size. Hot bins store the segregated aggregate.
When the appropriate mix is decided upon, hot aggregate is dropped from specific bins onto weigh hoppers and released into the pugmill for mixing with the hot liquid asphalt binder and filler.

## Slide 82: Emission Control Hot Aggregate Handling
Notes: There is the potential for significant aggregate dust emissions from the hot aggregate elevator, vibrating screens, and hot aggregate bins. There are also emissions of other criteria pollutants, organic hazardous substances, (AP-42 Table 11.1-9), and hazardous metals (AP-42 Table 11.1-11).
At times too much…so discarded hot aggregate is dropped to the ground, a combined vapor plume ( i.e., a plume containing water vapor and air pollutants) may release fugitive dust briefly into the air (Figure 303-24). If discarded hot aggregate is transferred to a holding bin, there will be fugitive dust emissions when the aggregate is loaded into a haul truck.
IDEALLY DISCHARGES SHOULD BE MADE WHERE?
ANSWER IN A TRANSPROT DEVICE AND NOT ONTO THE GROUND.
DISCHARDED SHOOTS SHOULD BE INCLOSED AND SEALED IN GOOD WORKING CONDITION. AND ARE DESIGNED TO MINIZE DROP HEIGHT. A SHROUD AND A WATER SPRAY SHOULD BE INSTALLED TO MINIZIAE EXCESS DUST EMISSIONS.

## Slide 83: Emission Control Flue Gas Recirculation
Blue Smoke
Flue/Blue Gas Ducting
Induced Draft Fan
Notes: It is important to control the gase as well as particulates from the process. NOx control (flue gas rec.) and fuel economy. No different from gas exhaust recir. Valve in our cars
Fuel gas recirculation (FRG) involves returning flue gases to the burner. Recycled flue gas contains a large amount of combustion products which act as inert gases during combustion of the air/fuel mixture LESS FUEL IS REQUIRED due to recycled flue gas.
NOx is reduced 2 ways
1. add air to the combustion zone
2. Lower oxygen concentration is lower in flame
Can result in a 70% reduction of NOx

## Slide 84: Emission Control
Cyclone
Ducting to Baghouse
Baghouse
Rotary Dryer
Notes: Dust and products of combustion are usually drawn into a primary control device (either a knockout box or cyclone) and then a secondary (either a baghouse or wet scrubber)

## Slide 85: Small Binder Storage Tank
Notes: 99 % do but need a permit due to small size less than 2 mil BTUs during inspection check the burner rating Used to keep tank hot. Primarily the storage tank and in the jacketed piping. fuel is usually natural gas, although propane and fuel oil
Emissions consist of the products of combustion, e.g., water, carbon dioxide, carbon monoxide, oxides of nitrogen, sulfur dioxide, volatile organic compounds, and particulate matter. Hazardous organic pollutants may also be emitted (AP-42 Table 11.1-13).
Operators have an incentive to maintain to maximize thermal efficiency. The higher the efficiency, the less fuel burned. Visible emissions may be seen at the stack if the burner is not operating correctly.
303.5.3 Control Methods
The burner for the hot oil heater is much smaller than the burner for the rotary dryer. Also, the rotary dryer burner involves direct heating of product, whereas the hot oil heater burner involves indirect heating. Because both these factors decrease potential emissions, the hot oil heater burner may be equipment that is exempt from permitting. There may be restrictions on the type of fuel that can be burned in the hot oil heater. Of course, visible emissions are always subject to the opacity rule.
Expansion tank allows for thermal expansion of the oil.
Fuel is usually natural gas.

## Slide 86: Hot Oil Heater Coils
Notes: Temperatures of the coils are heated to keep the binder at 325 F
There is a sampling valve that can be used to collect a sample to verify the composition of the binder.

## Slide 87: Process Underground Storage Tanks

## Slide 88: Uncontrolled RAC Binder Storage Tank
Notes: Vapors coming from a transportable tank used to heat rubber prior to mixing with bitumen, aggregate and binder to make rubberized asphalt for based on Cal Trans Recipe.

## Slide 89: Controlled Binder Storage Tank Vent Condenser
Notes: Slide shows a vent condenser on an asphalt storage tank.
Vent condensers can be used to control blue smoke emissions from asphalt storage tanks. The vent condenser itself consists of a number of tubes with external fins. Ambient air circulates through the fins, cooling the tubes and the gases passing through them. Hydrocarbons in the gas stream condense and drain back down into the tank. Purified air is released into the atmosphere through the vent.

## Slide 90: Dust Silo
Notes: The dust silo is used to store dust from the baghouse that is mixed as filler into the hot mix. The dust is transferred from the baghouse through the screw conveyor.
Check to make sure that dust is not emitting from the pneumatic systems which should be fine unless there are leaks in the duck work or valves.
A vent at the top of the dust silo allows displaced air to escape as dust pours in. Usually, there is a small baghouse on top of the dust silo to prevent visible dust emissions. Compliance assurance monitoring calls for as much focus as much on the control device as on production. pressure gauge at ground level and 10 to 20 % spare set of bags be available onsite for all the baghouse

## Slide 91
Blue Smoke
Pug Mill
Blue Smoke
Control Duct
Incline Conveyor

## Slide 92: Control Draft Air
Notes: HMA PLANTS USUALLY HAVE TWO FANS, THE BURNER BLOWER AND THE EXHAUST FAN.
BOTH OF THESE FANS MUST OPERATE EFFICIENTLY TO ENSURE PROPER COMBUSTION AND AIR FLOW IN THE HMA PROCESS.
BURNER BLOWER PROVED AIR AND BURNS FUEL. THE EXHAUST FAN PROVIDES ARI FOR COMUSTION AND REMOVES EXHAUST GASES, EXCESS AIR AND STEM FROM THE DRYER.

## Slide 93: Control Draft Air
Draft air passes through ducting due to pressure differential
Draft air affects
Combustion efficiency
How a system develops leaks
Control effectiveness

## Slide 94: Control Types of Draft Air
4 Type
Forced Draft Air
  Air that is pushed resulting in positive pressure
Induced Draft
  Air is pulled by a fan resulting in negative pressure
Notes: Run through figures to demonstrate types of draft air and leaks in chapter 307.1

## Slide 95: Control Draft Air (cont'd)
3. Natural Draft Air
  Difference in temp between flue gases and the ambient air.
4. Balanced Draft
  Forced draft fan pushes combustion air into combustion chamber.
Notes: Natural draft….Negative pressure created by stack height and the
Balanced Draft forced draft fan negative pressure prevents leaks

## Slide 96: Control
Notes: Because burners atomize fuel in air and ignite the mixture, the draft air provided by a burner blower is forced air. Blower air provides oxygen for combustion and movement of the products of combustion away from the blower. If air is not pulled through the dryer/drum (induced draft), the blower will push it until the positive pressure forces air out the exit opening.
Another example of forced air is a fan is pushing air into a baghouse. This forced draft in the baghouse results in positive pressure. The air in the baghouse will have greater pressure than the ambient air. There will be pressure pushing out on the structure of the baghouse. Positive pressure does not require special structural changes to a baghouse.
Visible emissions are more likely to occur through leaks in ducting systems with forced draft than those with induced draft. This is because the increased air pressure is pushing air through the system and some escapes through the leaks (Figure 307-7).

## Slide 97: Control
Notes: It is possible to create an induced draft in a dryer/drum. The burner blower provides forced air initially. Often, an exhaust fan located at the base of the exhaust stack draws air through the dryer/drum and the control equipment.
In this situation, a baghouse will have induced draft as well. A fan is pulling air into a baghouse, creating an induced draft in the baghouse. The walls of the baghouse need to be reinforced to prevent collapse of the building structure because of decreased air pressure inside.
If a fan is positioned, instead, between the dryer/drum and the dust control equipment, the exhaust fan that acts as an induction fan to draw gases from the dryer/drum will act as a forced draft fan to push the same gases into the dust control equipment. A fan located in the gas stream that is constantly bombarded with particles is subject to much more wear and tear than a blower that only pushes air.
Visible emissions are more likely to occur through leaks in ducting systems with forced draft than those with induced draft. This is because the increased air pressure is pushing air through the system and some escapes through the leaks (Figure 307-7).

## Slide 98: Control
Notes: In a balanced draft system, a forced draft fan is used to push (or blow) combustion air into the combustion chamber and an induced draft fan and a natural draft stack are used to pull the combustion gases through the combustion chamber and exit from the stack. The draft is balanced so that the combustion chamber is maintained at a slightly negative pressure. This negative pressure prevents emissions from leaking from the combustion chamber (Figure 307-6).1

## Slide 99: Leak in a Rotary Dryer
Notes: The rotary dryer produces the largest amount of ducted emissions in a batch plant. Emissions consist of large amounts of aggregate dust and products of combustion, e.g., water, carbon dioxide, carbon monoxide, oxides of nitrogen, sulfur dioxide, volatile organic compounds, and particulate matter (AP-42 Tables 11.1-1,2,5,6). of hazardous substances (AP-42 Tables 11.1-9, 11). Note in the Tables that the products of combustion vary depending on the type of fuel burned.
If there are leaks in the dryer or associated ducting, there may be visible emissions. Below is an example of a leak from an incompletely repaired section of a rotary dryer.
A phenomenon termed "puff back" may be seen at the rotary dryer. Visible emissions may be emitted from the dryer. This is actually not a problem with the burner but with the primary air pollution control equipment. This phenomenon will be discussed in detail in Subsection 307.1, Primary Air Pollution Control Equipment.

## Slide 101: Control Drum/Dryer Emission
Drum/Dryer produce large amounts of PM
Two control devices
  Primary for large particles and
  Secondary for small particles
Combined efficiency is 99% or greater
Ask for manufacturer or facility guarantee
Notes: Drying of aggregated causes the fine particulate that is still adhearing to the rock to come off and creates high particulate emissions

## Slide 102: Primary Controls Cyclone
Notes: A. K. A. PRE-CLEANERS
30 to 40 + % efficiency for larger particles
Also,
>> acts to cool hot combustion gases prior to entering baghouse.

## Slide 103: Primary Control Cyclone

## Slide 104: Primary Control Wet Scrubber
Notes: WET SCRUBBERS RARELY SEEN TODAY…SECONDARY CONTROL DEVICE. NAME SOME ADVANTAGES AND DISADVANTAGES OF A SCRUBBER AND WHAT DO YOU THINK YOU SHOULD CHECK FOR?
INSPECT PUMPS, PIPING, VALVES, SPRAY NOXXLES PIPES AND MANIFOLD,
MAIN BODY FOR ABRASION, CORROSION, MATERIAL FEED BUILDUP
FINES SYSTEM FOR LEAKS AND PRPER DICSHARGE. ENSURE PROPER HANDLING OF LIQUIR FROM SCRUBBER
CLEAN WATER SHOULD ALWAYS BE USED TO AVOID PLUGGING

## Slide 105
Wet Scrubber?

## Slide 106: Process/Control Wet Scrubber
Used to control stack emissions
  Must meet the emission requirements specified in Subpart OOO
  Continuous emissions pressure monitor
    + 250 pascals + 1inch water gauge pressure
  Continuous measurement of scrubbing liquid flow rate to scrubber
Notes: Certified by manufacturer
Annual calibration

## Slide 107: Control Techniques Wet Scrubber
General description
  Particles get trapped in liquids
    Inertial impaction and diffusion
  Liquids must contact particles and dirty liquids must be removed from exhaust gas

## Slide 108: Particle Scrubbers
Initial quench – use clean water
Water drops and particles must contact (impact)
  Requires water flow and mixing energy
Dirty water collection
Water treatment & recirculation

## Slide 109: Wet Scrubber Operation
Particles collected by impaction
Gasses collected by diffusion & absorption
Venturi Scrubber
Packed Bed Scrubber

## Slide 110
Scrubber
Liquor

## Slide 111: Primary Control Knock Out Box

## Slide 112: Primary Controls Knock-out Box

## Slide 113
Secondary Control Baghouse
Notes: Used extensively : last 15 years
 Very efficient at dust collection
 Over 99% control
 Often the most cost effective method available
Located downstream of air preheater
 Just before the stack

## Slide 114: Secondary Control Baghouses
General description
  Particles trapped on filter media, then removed
  Either interior or exterior filtration systems
  Up to 99.9% efficiency
  Fabric filters are big vacuum cleaners with a cleaning mechanism
Notes: Filter Bag Maintenance Filter bags wear out. They may develop pinhole leaks, gross tears, or burn holes. Bags need to be inspected regularly and replaced as necessary. If bags need to be replaced too often, a bag with different composition should be considered. Different cleaning methods stress the bags differently. The choice of filter bag should correspond with the cleaning method chosen.
Top of Page
Valve Seal Maintenance Dust is removed from the baghouse hopper by various means. Special attention must be given to the seal at the bottom of a baghouse to avoid drawing air into the system as fines are removed. Figure 307-19 displays four different types of valve seals. If there is minimal suction, a gravity chute may be used. A gravity tipping valve has a counter-balance weight to keep it closed until the weight of the dust collected opens it. A second valve below works the same way to provide an air lock. A motorized pneumatic tipping valve works similarly to the gravity tipping valve except that it is driven by a motor. A rotary air lock is designed like a revolving door, with compartments. As a motor turns the valve, a compartment filled with dust revolves from the bottom of the hopper. An empty compartment revolves into the hopper and starts to fill with dust. As the full compartment rotates, it transfers the dust from the hopper.

## Slide 115: Secondary Control Baghouse
Notes: The pulse jet method allows the baghouse to remain in operation. These bags use an exterior filtration system, where the dust cake collects on the outside of the bags from air flowing from outside to inside the bags. Occasionally a pulse of compressed air is forced down the inside of the bag. The shock wave knocks off some of the dust cake as it travels down and back up the bag (Figure 307-17).

## Slide 116
Clean Air
Clean Air Plenum
Pulse Pipe
Bag
Cage
Venturi
Solenoids
Dust-Laden Air
Inlet Baffle
Pulse Jet Baghouse

## Slide 117: Secondary Control Pulse Jet Baghouse

## Slide 118: Secondary Control Inside a Pulse Jet Baghouse

## Slide 119
Pulse Jet
Bag

## Slide 120
Measuring Pressure Drop
Notes: Magnehelic gauge typically use to determine pressure drop as shown. Pressure drop is difference between clean side and dirty side.
Number should rise slowly until cleaning cycle initiated. Sudden decrease or very slow rise may indicate leak. Sudden increase or increase beyond design value indicates possible blinding of bags.

## Slide 121: Baghouse Design Considerations
Pressure Drop
Air-To-Cloth Ratio
Collection Efficiency
Fabric Type
Cleaning
Temperature Control
Bag Spacing
Compartment Design
Space and Cost
Notes: Based on what’s going in and what you want out, namely, emissions in compliance with regulations.
We’ll discuss the first 2 in some detail. These are fundamental to all baghouses.
Collection Efficiency not really an issue. Baghouses operate at 99+% efficency in most applications if functioning properly.
Temperature Control will be discussed later. Not used in all BHs.
Last 3 are important, but not for this course.

## Slide 122: Secondary Control Shaker Method
Notes: Switch to figure 307-16 for reverse air method and 307-17 for pulse jet
General description (cont.)
  4 types of cleaning systems
    Shaker (off-line)
    Reverse air (low pressure, long time, off line)
    Pulse jet (60 to 120 psi air, on line)
    Sonic horn (150 to 550 Hz @ 120 to 140 dB, on line)

## Slide 123: Secondary Control PM Control Techniques – Fabric Filter
In
Out
P

## Slide 124: Secondary Control PM Control Techniques – Fabric Filter
Factors affecting efficiency
  Filter media
    Abrasion
    High temperature
    Chemical attack
  Gas flow
  Broken or worn-out bags

## Slide 125: Secondary Control PM Control Techniques – Fabric Filter
Factors affecting efficiency (continued)
  Cleaning system failure
  Leaks
  Re-entrainment
  Damper or discharge equipment malfunction
  Corrosion

## Slide 126: Secondary Control PM Control Techniques – Fabric Filter
Performance indicators
  Outlet PM concentration
  Bag leak detectors
  Outlet opacity
  Pressure differential
  Inlet temperature
  Temperature differential

## Slide 127: Secondary Control PM Control Techniques – Fabric Filter
Performance indicators (cont'd)
  Exhaust gas flow rate
  Cleaning mechanism operation
  Fan current
  Inspections and maintenance

## Slide 128: Secondary Control Bag House Monitoring
Normal bag house emissions are very low.
  Opacity sensors Continuous Opacity Monitor (COM) aren’t very good below 1-2%, so they don’t detect initial problems.
  Opacity will show a major particulate emissions increase.
  COM or Method 9 may be OK for loose emission limits.

## Slide 129: Inspection Procedures Instrumentation
What types of instruments are being used to monitor for permit conditions?
  Magnehelic Gauge
  Triboelectric Monitor
Notes: If the differential pressure indicators are reading lower than the manufacturer’s specs, there may be a tear in the bag.
Triboelectric Monitor detects changes in PM mass loading
If the differential pressure indicators are reading higher than the manufacturer’s specs, this could be a sign of caking.
In either case, check the manufacturer’s specs either before your inspection or at the time of your inspection.
If VEE are occurring, chances are it’s a result of a tear in the bag. There will be intermittent puffing.

## Slide 130: Inspection Procedures Magnehelic Gauge
Notes: A good thing to do here is to include in your permit to operate low and high pressure reading limits.
If the permit does not include a limit, check the manufacturer’s recommended operating limit.

## Slide 131
What’s wrong with this picture?
Inspection Procedures

## Slide 132: Baghouse Monitoring Triboelectric Sensor (TES)
TESs are a newer technology
  Primary use in cement, coal fired power plants, and food manufacturing
  US EPA encourages use of TESs as CAM (compliance assistance monitoring, 40 CFR 64) or
  As a performance indicator in lieu of a source test
Districts are adopting TES as BACT or compliance measurement tool

## Slide 133: Baghouse Monitoring Triboelectric Sensor
Triboelectric sensors (TES) work well at very low particle concentrations (very sensitive).
TES detects micro amp current from particles hitting a metal probe.
TES is simple and inexpensive.
TES is an effective monitor when a small to moderate increase in emissions is of concern.

## Slide 134: Baghouse Monitoring Triboelectric Sensor
Operates on the principle of electric conductivity
  Triboelectric Principle: When 2 solids contact an electrical charge is transferred between the 2
  Current generated is proportional to the particulate mass flow rate
  Instrument tuned to produce continuous analog output and/or an alarm at a specific signal level

## Slide 135: Control Devices PM CEMS/TES Devices

## Slide 136: Control Device Triboelectric Sensor Schematic
Notes: Factors effecting operations
Composition of PM and Probe: example stainless steal probe and insulating particles rather than metalic
Velocity: greater the velocity of a particle, the greater the signal gnerated. Can be linear to exponential. Signal output is sensitive to changes in gas stream flow rate.
Particle Size: all things being equal…the triboelectric signal per unit mass is greater for smaller particles. Due to larger surface area of smaller particles. Denser materials are detected at smaller size range than less dense materials
Charge: charged particles generate a signal independent of the triboelectric effect when they strike the probe. Instrument is more sensitive to charge particles. Conditions that cause a variations in the charge on the PM will result in variable sensitivity.
Accumulation of PM on the Probe: accumulation of material will redluce the sensitivity of the probe. Harder material accumulate slowly, soft, damp and sticky particles accumulate at a faster rate. Accumulation of conductive PM on the probe can cause an electric bridge between the probe and ground generating a large signal.
Particle shape: Particle with a large surface area per unit mass are expected to generate a stronger signal. No data is available to quanitify this effect.
Temperature: Operates best between the dew point and below 1100 F.
Relative Humidity: No problems as long as the gas stream temperature is above the dew point.

## Slide 137: Triboelectric Sensor Installation for a Negative Pressure Monitoring System
Notes: Instillation for a negative pressure fabric filter.

## Slide 138: Monitoring Device Triboelectric Sensor
TES works well at low particulate concentrations
Detects micro amp current from particles hitting a metal probe
Simple and inexpensive
Effective monitor when a small to moderate increase in emissions is of concern

## Slide 139: Baghouse Monitoring Device Triboelectric Sensor
Establish baseline
Monitor detects gradual or instantaneous increases in the signal from baseline
Baseline emissions can be as low as 0.1 mg/dscm (0.00005 gr/dscf)
Notes: All bags allow some particles to pass through

## Slide 140: Inspection Procedures Fans/Blowers
Horsepower
Number of Engines
Notes: Check to make sure the number, model, and horsepower of the engines identified on the permit match.
Also, check to see if there have been any additions. What types of engines are there?
Internal combustion, electrical?
And, are the engines they have capable of performing the required task?
ON THE FANS, MAKE SURE THAT YOU INSPECT AN MAINTAIN

## Slide 141: Control Scavenger System
Collects fugitive
emissions from:
  Hot aggregate
  elevator
  Vibrating screens
  Hot bins
Notes: CHECK THE HOUSEING FOR HOLES, CORROSION, VIBRATION
SHAFT FOR WEAR AND BALANCE
BEARINGS FOR PROPER LUBRICATION
SHEAVES FOR WEAR,
FAN WEEL FOR WEAR AND BUILDUP
BELTS FOR WEAR AND TENSION
BEARINGS FOR MOISTURE AND DUST
MOTOR FOR PROPER OPERATION

## Slide 142: Control Asphalt Binder Storage
May or may not be controlled
Controls include
  Condensers,
  Vapor recovery system (similar to gas station)
    Vapors returned to refinery for incineration
Delivery truck lines are flushed with non-hazardous cleaners
Notes: State law prohibits the use of diesel to flush lines. NO longer allowed
Use citrus peels, vegetable oils or organic ester-based formulations.

## Slide 143: Control Asphalt Binder Storage
Notes: CONTROL GASEOUS EMISSION SOURCES
RUNNING THE PLANT ‘TOO HOT’ CAN CAUSE GASEOUS EMISSIONFROM THE PROCESS…GASEOUS EMISSIONS CAN BE RELEASED AT THE BURN, ASPHALT AND FUEL STORAGE, HOT PRODUCT ELEVATOR, AND TRUCK LOADING.
NOTE: IF LIMITATION FOR SULFUR CONTENT OF FUELS, NITROGEN OXIDE EMISSION, ANC CO CHECK DISTRICT REGULATIONS.
ON TANKS THE COVERS SHOULD BE CLOSED. VALVES SHOULD HAVE GOOD SEALS AND CLEAN. FREQUENTLY CHECK FOR LEAKS

## Slide 144
Notes: CONTROL OF GASEOUS EMISSION POINTS
Running the plant ‘TOO HOT’ can cause gaseous emissions from the process:
>> burner
>> asphalt oil & fuel storage tanks
        >> hot product elevators
        >> truck loadout

## Slide 145: Control Blue Smoke
Notes: TRUCK LOADOUT GASEOUS EMISSIONS
CAN BE REDUCED by:
>> minimizing drop heights (free-fall)
>> capturing and ducting emissions to controls

## Slide 146: Control Blue Smoke
An aerosol of condensed organic particles adsorbed to dust or water particles

## Slide 147: Control Blue Smoke
Some organic compounds begin to
vaporize at 300 F
Condense in ambient air
Adsorb to dust and water particles
To form visible emissions
Visible emissions are formed until the air becomes saturated

## Slide 148
Blue Smoke
Emission Points
Notes: LET’S TALK ABOUT BLUE SMOKE …
AND EMISSION POINTS

## Slide 149: Control Blue Smoke Emissions Points
Drop points of HMA from pugmill
On top of surge bins/silos
At the base of surge bins/silos
Drag slat conveyors
Truck load out
Challenge to capture and control
Primary reason for complaints
Perception !!
Notes: Blue Smoke Emissions Points
>> Drop points of HMA from pugmill
>> On top of surge bins/silos
>> At the base of surge bins/silos
>> Drag slat conveyors
>> Truck loadout
Challenge to capture and control
Primary reason for complaints
Perception !!

## Slide 150
Notes: Control of blue smoke emissions is one of the most difficult challenges for HMA facility operators. However, emissions of blue smoke from the drop points of HMA at the base of the pugmill, on the top of surge bins, or at the base of surge bins can be reduced. The first challenge is to capture the emissions. The second is to process them.
One way to process emissions is to re-circulate them from the top of the surge bins through the rotary dryer. Ducting is installed on the top of the surge bins with an induction fan to pull the emissions towards the dryer (Figure 303-46).

## Slide 151
Blue Smoke Control Device??
Notes: Slot hood and ductwork assembly used to capture Blue Smoke
>> during truck loadout from pugmill

## Slide 152
Blue Smoke
Controls
Notes: Drop zone, vented periphery hood and ductwork assembly used to capture Blue Smoke
>> during truck loadout from continuous mix plant

## Slide 153
Truck Load Out & Blue Smoke Controls
Notes: Slot hood, ductwork assembly and control device used to capture and remove Blue Smoke
>> during truck loadout from continuous mix plant

## Slide 154
Silo/Truck Load Out & Blue Smoke Controls??
Notes: Blue Smoke capture system
>> atop silos and drag slat conveyor

## Slide 155
Blue Smoke Controls

## Slide 156
Blue Smoke Control Device

## Slide 157
Fiberbed Filtration
Notes: Fiberbed mist collectors operate similarly to a particulate baghouse.
Figure above depicts a fiberbed unit in an outdoor environment. A damper or a variable frequency drive is used to regulate airflow. The pressure drop across the collection filters is monitored. It generally ranges between 5 and 10 in WC during normal operation.
Filter replacement is required when the pressure drop reaches the specified maximum with the damper fully open. Otherwise, airflow through the system will decrease. Filtered air is exhausted to the atmosphere at the outlet of the fan.
Appropriate pressure drop ranges should be incorporated into permits since capture efficiencies could drop significantly without filter changeout.

## Slide 158
Fiberbed Filtration
Notes: [ABOVE]
TRUCK LOAD-OUT BLUE SMOKE CAPTURE AND CONTROL SYSTEM.
[BELOW]
FIBERBED FILTRATION CARTRIDGES

## Slide 159: Control of Blue Smoke Truck Entrance

## Slide 160: Control Blue Smoke Enclosed Load Out
Notes: n the photographs below, emissions are drawn from the top of the surge bins as well as from the load-out area. The load-out area is shrouded to promote capture of emissions. An induction fan pulls emissions through an oil impingement pre-filter then into the electrically charged area where particulates are removed. The cleaned air is then released via stack emissions (Figure 303-48).

## Slide 161: Control Side View of HMA Drop with ESP/Smog Hog for Blue Smoke
Notes: Side View of HMA Load-Out Zone Enclosure
with ESP/Smog Hog for Blue Smoke

## Slide 162: Control Ducting to ESP/Smog Hog

## Slide 163: Two-Stage ESP

## Slide 164: Controls Innovations in HMA Production
Four areas where the technology has improved
  burner design,
  fuels,
  dryer/drum design, and
  blue smoke controls
Notes: The hot mix asphalt industry is constantly trying to improve the quality, desirability, and safety of their products, limit costs (especially energy), and comply with environmental regulations.1
There are four areas where HMA facility technology has improved dramatically over the years:. These improvements generally result in energy savings and well as fewer detrimental environmental effects.
Optional controls for burner design and operation include: · Low NOx burners · Ultra-low NOx burners · Flue gas recirculation · Oxygen controller system · Water injection · Afterburner
Natural gas and liquid propane are cleaner burning than diesel, fuel oil, or any other optional fuels. Because of difficulties with transport and safety, less desirable optional fuels have been used at portable facilities. Now some portable facilities are developing the capability to use natural gas or propane.
The largest potential source of air pollutants is the dryer/drum. many technological improvements over the years. The most recent examples of innovative drum designs include Astec Industries Inc.'s Double Barrel® Drum Mixer, the Turbo Double Barrel® Drum Mixer, and CMI Corporation's Triple-Drum™.

## Slide 165: Controls Triple-Drum Mixer
Notes: WE DISCUSSED THE TRIPLE DRUM CONCEPT EARLIER. DURING INSPECTIONS. ENSURE THE YOU FREQUENTLY CHECK THE BURNER.
MAKE SURE THE SHUT-OFF VLAVES DO NOT LEAK AND THEY OPERATE
FUEL ATOMIZING PRESSURE IS ADEQUAT
FUEL PRE-HEAT TEMPERATURE IS ADEQUATE
AIR VANES FOR TIGHTNESS/OPERATION
NOZZLES FOR WEAR AND CLOGGING
AIR SUPPLY LINES FOR PLUGGING
BURNER ADJUSTMENTS FOR OPERATION
REFRACTORY FOR CRACKS AND HOLES AND THE DRUM

## Slide 166: ASPHALT SEAL COAT AND PAVING Reading a Moving Plume

## Slide 167: Moving Source

## Slide 168: Permit Conditions
Emission Controls
  Emission Limits
  Process Limits
  Emission Rate Limits
  Requirements to Minimize Emissions
  Source Test
  CAM (gauges on baghouse)
Notes: Permit conditions are specific to the district and the facility. However, the following elements may be included:
Emissions Control 2) Fuel Type and Use 3) Visible Emission Limits / Nuisance Regulation 4) Notification of Breakdown 5) General Permit Requirements
The permit contains many elements to control emissions. These elements include requirements that limit the operation. ‘There are operating hour restrictions
Emission rate limitations that c daily, monthly, annual process rate limits
A source test is done to verify emissions. Hourly limits for particulate cannot be measured only through a source test. Emissions are measure by the inspector using method 9 for VEE (the permit will specify specific opacity ratings. This permit specifies 5% opacity. We will talk about that in a minute.

## Slide 169: Permit Conditions (cont'd)
Fuel Requirements
  Type
  Nitrogen or Sulfur content
  Amount of fuel
  Type of backup fuel
  Method of measurement
  Recordkeeping of fuels purchased and used
Notes: AP-42 DEFINES BACT AS 93 %. NEW TECHNOLOGY IS SURPASSES AND CAN REACH 99%.
HOT MIX BACT IS TRIGGERED FOR A NEW SOURCE OR ANY MODIFCATION THAT INCREASES EMISSIONS BY 2 POUNDS PER DAY…FOR EXAMPLE IF A FACILITY CHANGED TO MAKING RUBBERIZED ASPAHLT THE INCREASE IN EMISSIONS WITH THE SAME PROCESS RATE WOULD BE GREATER THAN 2 POUNDS PER DAY. A AUTHORITY TO CONSTURCT TO MODIFY WOULD BE REQUIRED.
BACT WOULD HAVE TO BE APPLIED. TO REDUCE CO A NATURAL GAS OR LPG BURNER WOULD BE REQUIRED
NOX BURNER OF 0.088 LBS PER/MM BTU MUST BE USED COVERED WITH A LOW NOX BURNER USING NATURAL GAS OR LPG
SELLECTIVE CATALYTIC REDUCTION (SCR) IS ACHIVING LOWER EMISSION RATES THAN TRADITIONAL LOW NOX BURNERS.
PARTICULATES ARE CONTRULLED TO 99% WITH THE NEW ROTARY DRYERS AND BAGHOUSES MANUFACTURES ARE SELLING THESE UNIT WITH A GUARANTEE EFFICIENCY RATING. CONTROL EQUIPMENT IS A FABRIC FILTER, WITH A CENTRAFRUGAL SEPARATER (FANCY NAME FOR A NEW CYCLONE) AND FACITLY MUST CONDUCT SOURCE TEST. ENCLOSED CONVEYORS, SILOS ENCLOSED, PUGMILL, HOT MIX SILOS AND LOAD OUT AND VENTED TO OIL MIST COLLECTOR AND OR VENTED BACK TO BURNER OR ESP OR FILTER PACKS ARE USED.

## Slide 170: Permit Conditions (cont'd)
Visible Emissions Limits
  NSR lists are 20% or No. 1 on Ringleman
  Sources permitted before NSR maybe 40% or No. 2 on Ringleman
Notes: Don’t forget notification of breakdown and general permit conditions that were discussed during our aggregate discussion
WHAT IS WRONG IN THIS PICTURE? THERE ARE TWO THINGS HAPPENING. ONE THE TANK IS COATED WITH RESIDUE (A SOURCE OF RELEASE) TWO THE LID IS OPEN.

## Slide 171: Process/Control Dry Collection Systems
Baghouses are regulated in terms of
  Source Test Requirements and Methods
  Visual Test Method?

## Slide 172: Process/Control Wet Scrubber
Used to control stack emissions
  Must meet the emission requirements specified in Subpart OOO
  Continuous emissions pressure monitor
    + 250 pascals + 1inch water gauge pressure
  Continuous measurement of scrubbing liquid flow rate to scrubber
Notes: Certified by manufacturer
Annual calibration

## Slide 173: Permitting/Inspection HMA Source Test
Notes: Click on picture to reveal short description…follow text. Close when done.
Source tests must follow approved test methods and safety regulations. Test methods must be approved either by the CARB or the U.S. EPA . Table 403-B shows the test methods mentioned in the fictitious permit.
Table 403-B Source Test MethodsNumberTitleCARB
Method 1Sample and Velocity Traverses for Stationary Sources
CARB Method 2Determination of Stack Gas Velocity and Volumetric Flow Rate (Type S Pitot Tube)
CARB Method 2A Direct Measurement of Gas Volume Through Pipes and Small Ducts
CARB Method 3 Gas Analysis for Carbon Dioxide, Oxygen, Excess Air, and Dry Molecular Weight
CARB Method 4 Determination of Moisture Content in Stack Gas
EPA Method 3Gas Analysis for the Determination of Dry Molecular Weight
EPA Method 3A Determination of Oxygen and Carbon Dioxide Concentrations in Emissions from Stationary Sources (Instrumental Analyzer Procedure)
EPA Method 5 Determination of Particulate Matter Emissions from Stationary Sources
EPA Method 7EDetermination of Nitrogen Oxides Emissionsfrom Stationary Sources (Instrumental Analyzer Procedure)
EPA Method 10 Determination of Carbon Monoxide Emissionsfrom Stationary Sources
EPA Method 19Determination of Sulfur Dioxide Removal Efficiency and Particulate Matter, Sulfur Dioxide, and Nitrogen Oxide Emission Rates
EPA Method 202 Determination of Condensible Particulate Emissions from Stationary Sources

## Slide 174: Control Equipment Emission Points from Batch Facilities
HMA Batch Mix Process
Emission Points

## Slide 175: Emission Points from Continuous Feed
HMA Continuous Mix Process
Emission Points

## Slide 176: Permit/Inspection Objectives
Determine compliance with Local rules, State laws, Federal regulations & permit conditions
Fugitive emissions
Stack emissions
Visible emission tests
Oxides of nitrogen (for fuel burning equipment)
Notes: Permit conditions describe equipment and conditions of operation to be in compliance with emission limits.
SC rule 1157