## Slide 1
Concrete Batching Operations

## Slide 2: Concrete Batch Plants
Concrete Batching Operations

## Slide 3: Typical Concrete Batching Operation
Concrete Batching Operations
Notes: The basic equipment in a concrete batch plant includes conveyors, elevators, silos, weigh batchers, and mixers

## Slide 4: Wet Mix Batching Operation
Dry Mix Batching Operations

## Slide 5: Dry Mix Batching Operation

## Slide 6: Wet Mix Batching Operation

## Slide 7: Wet Mix Batching Operation

## Slide 8: Violations?

## Slide 9
Introduction
Industry History
Emissions and Health Impacts
Concrete Industry Description
Inspection Procedures
Engineering Evaluation/Permit Process
Overview

## Slide 10
Hoover Dam
How many cubic yards did it take to build?
Notes: 1936
Hoover Dam Built
First Major Concrete Dam
3,220,000 cubic yards of concrete in Hoover Dam
Concrete consists of sand, rocks (or aggregate), cement (which acts as the paste that holds everything together), and not as much water as you might think. This makes the concrete very dense. Imagine jumping onto a pile of sand or rock; you would only sink into it a couple of inches. The same is true with fresh concrete. Typically, concrete has a density of 150 pounds per cubic foot, which means that a block of concrete that is one foot wide, one foot long, and one foot high would weigh 150 pounds. Water has the density of only 62.4 pounds per cubic foot.
In addition, the concrete blocks were built along side of each other as the dam was being constructed, so falling from one concrete block into fresh concrete in the next block would have only been 5 to 10 feet. There is no record of anyone falling into a concrete placement. In fact, if you look at pictures of concrete being placed into one of these blocks you will see men inside the forms working the fresh concrete. They were known as "puddlers," and their job was to use their shovels and feet to spread the concrete around and make sure the concrete completely filled up the form. These puddlers could easily walk on the fresh concrete because it was so dense that they would sink in only a couple inches. Concrete takes 12 hours to become hard, so there was no way for the puddlers to become stuck in the fresh concrete.

## Slide 11: Concrete Batch Plant Dry Mix
Concrete Batching Operations

## Slide 12: Constitutes
Basic Ingredients
11% Portland Cement
41% Aggregate or Course Stone
26% Sand
16% Water
Balance: Inert Material

## Slide 13: What is Concrete?
A combination of water, sand, rock, and
portland cement mixed together to harden.
Notes: The term concrete refers to a product formed from two principle components: aggregate and paste.
Concrete hardens by a chemical reaction known as hydration.
Aggregate, which can be either natural or man made, consists of various grades of sand, gravel, crushed stone, or slag.
Paste, is composed of cement, water, and sometimes entrained air. The cement paste makes up approximately 25 to 40 percent by volume of concrete.

## Slide 14: Composition of Portland cement with chemical composition and weight percent.
Cement Compound
Weight Percentage
Chemical Formula
Tricalcium silicate
50 %
Ca3SiO5 or 3CaO.SiO2
Dicalcium silicate
25 %
Ca2SiO4 or 2CaO.SiO2
Tricalcium aluminate
10 %
Ca3Al2O6 or 3CaO .Al2O3
Tetracalcium aluminoferrite
10 %
Ca4Al2Fe2 or 4CaO.Al2O3.Fe2O3
Gypsum
5 %
CaSO4.2H2O
Notes: When water is added to cement, each of the compounds undergoes hydration and contributes to the final concrete product. Only the calcium silicates contribute to strength. Tricalcium silicate is responsible for most of the early strength (first 7 days). Dicalcium silicate, which reacts more slowly, contributes only to the strength at later times. Tricalcium silicate will be discussed in the greatest detail.

## Slide 15: Tricalcium silicate + Water  Calcium silicate hydrate + Calcium hydroxide + heat 2 Ca3SiO5 + 7 H2O  3 CaO.2SiO2.4H2O + 3 Ca(OH)2 + 173.6kJ

## Slide 16
Dicalcium silicate + Water 
Calcium silicate hydrate +
Calcium hydroxide +heat
2 Ca2SiO4 + 5 H2O 
3 CaO.2SiO2.4H2O + Ca(OH)2 + 58.6 kJ

## Slide 17: Cement from a Cement Manufacturing Process
Concrete Batching Operations
Notes: Flash showing the making of cement. Click on picture and roll cursor over each step to reveal process. Hit escape to return to slides

## Slide 18: Cement Delivery Pneumatically

## Slide 19: Cement Delivery Pneumatically

## Slide 20: Dust Collectors Serving Cement/Fly Ash/Slag Silos

## Slide 21: Purpose/Utility

## Slide 22: Aggregate from a Rock Quarry
Stacking Conveyors

## Slide 23: Aggregate from a Crushing Plant

## Slide 24: Concrete Sand From a Wash Plant

## Slide 25: Aggregate Delivery via Conveyors

## Slide 26: Aggregate Delivery via Conveyors: Safety

## Slide 27: Concrete Batching Process
Store, convey, measure, and then discharge the ingredients to make concrete into equipment that mixes, packages, or transports the mixture for use

## Slide 28: Dry Ingredients
Aggregates, cement and additives
Notes: Aggregate, sand and additives such as flyash
Plasticizers
Polymers
Color Pigments
Reinforcing Fibers and cement

## Slide 29: Additive Ingredients
Notes: Admixtures Admixtures are typically batched by volume through a dispenser. Usually an admixture supplier will provide the dispensers
Some producers batch admixtures by hand.

## Slide 30: Ingredients
Air retaining Agents - Provides resistance
Water Reducing - Reduces the amount of water needed
Accelerating Agents - Shortens setting or cure time
Retarding Agents - Slows the setting/cure time
Fungicides - Prevents fungus or bacterial growth

## Slide 31
75% of U.S. concrete is produced at plants that
Store
Convey
Measure
Mix
Discharge into trucks
Concrete Batching Process
Notes: The remaining 25% are manufactured products cast in a factory setting. Precast products include concrete bricks, paving stones, bridge girders, structural components, and panels for cladding.

## Slide 32
Central Mix
Ready Mix
Transit Mix
Types of Concrete
Batching Process
Notes: Three types we are going to cover are: Click
Transit Mix: 75% of US concrete batching. Also referred to as dry batch operation.
Click
Central Mix: 1/4 of the industry is central mix. Also referred to as wet batching. Used for quality control. Preferred by civil engineers (high rise buildings).
Click
Ready Mix: Concrete is manufactured and sold to stores such as Home Depot. The product is usually in 50 lb bags/sacks.

## Slide 33: Place holder for process
Twin Shaft Mixtures
Load Out
Batching Controls
Moisture Sensors
Scales,
load cells
Silo Weighing
and Inventory
Mixer
Mixer
Moisture Controls
Concrete Batching Process
Notes: NAME 5 DUST CONTROL METHODS.
Raw materials are delivered to the plant. Cement is transferred to storage silos. The sand and coarse aggregate are transferred to elevated bins by front end loader, clam shell crane, belt conveyor, or bucket elevator. From the elevated bins, the ingredients are fed by gravity or screw conveyor to weigh hoppers, which combine the proper amounts of each material.
Name five dust control measures

## Slide 34
Particulate Matter
Combustion Emissions
Concrete Batching Process: Types of Emissions
Notes: Paint wastes are from?
The dies that are added
There are some metal emissions which originate from the cement. Metals such as chromium, lead, and nickel

## Slide 35
Sprinkler and
Load Out Grizzly
Concrete Batching Process

## Slide 36
Concrete Batching: Stockpiles
Notes: Don’t like the fixed drop points. Why?
Good housekeeping practices. Clean and wet.

## Slide 37
Concrete Batching: Aggregate Conveyors
Notes: Some facilities are located adjacent to an aggregate facility. The aggregate and sand is moved via conveyor to from the cement storage silos.
Most precasters batch aggregates by weight. Aggregates can be weighed in hoppers, on weigh belts, or in or directly from aggregate storage bins. Hoppers have load cells attached to them to measure the weight of the aggregates. Typically aggregates are moved to the weigh hopper by conveyor belts and weighed cumulatively.

## Slide 38
Concrete Batching: Storage of Dry Ingredients
Notes: Some systems may also incorporate adjustable gates. These are knife-like gates that help blend aggregates on the belt before getting to the mixer, thereby reducing mixing time and improving homogeneity of the mixture.
Storage bins may also have load cells attached to them that weigh the amount of aggregate remaining in the bin. The difference between the starting and final weights is assumed to be the aggregate weight going into the mixer. This is called a decumulative weighing system and is an indirect method of measuring the aggregates to be batched. This type of system is usually done with smaller batching systems and reduces costs by eliminating additional gates, weigh hoppers and LBWHs. The theory of this mechanism assumes that all the aggregates leaving the bin go into the mixer. This may not be accurate, since aggregates can deflect or ricochet elsewhere from freefall.
Volumetric measuring is typically used in continuous mixing systems. There is also volumetric batching, which is another means of measuring raw materials for a single batch. Concrete produced by volumetric batching should meet ASTM C 685, “Standard Specification for Concrete Made by Volumetric Batching and Continuous Mixing.” This type of batching is used in some precast operations. It should be noted that while volumetric batching can produce good quality concrete, it is not yet universally accepted.

## Slide 39
Concrete Batching: Raw Material Receiving & Storage
Notes: Moisture Sensors It is very important to make adjustments for the moisture in the aggregates, especially the fine aggregate or sand. Surface moisture in sand typically can contribute large amounts of water, which dramatically increases the w/c ratio and weakens the concrete. Usually a moisture probe is located in the sand bin(s) to determine the sand’s moisture content. The weight of moisture-laden sand by volume will be heavier than normal, so you must add more sand to attain the required volume and then reduce the amount of mix water as necessary.
Another probe is typically located in the mixer. This sensor corrects for the additional moisture from both fine and coarse aggregates in the mixer. Another concern is that when aggregates are less than Saturated Surface Dry (SSD), more water should be added to compensate for the aggregates’ absorption and achieve SSD. SSD is the condition when aggregates will neither absorb nor give off moisture. This condition is not generally found outside the laboratory and is used for calculation purposes. It is important to note that moisture probes measure the total amount of water in aggregates or concrete. As such, adjustments should also be made for absorption of the aggregate.

## Slide 40
Concrete Batching: Raw Material Receiving & Storage
Aggregate Screen & Surge Bin
Notes: Sand, aggregate, cement and water are gravity fed from the weight hopper into the mixer trucks.
At most plants the sand, aggregate, cement, and water are gravity fed from the weight hopper into the mixer truck. To the site. The concrete is mixed in to truck on the way
Maintenance Batching equipment should be maintained and operated in accordance with ASTM C 94 or ASTM C 685. Hoppers and scales should be calibrated annually or whenever there is reason to question their accuracy. Refer to the “NPCA Quality Control Manual for Precast Concrete Plants” for more details.

## Slide 41
Concrete Batching: Moisture Sensor
Notes: 2 common types of probes or sensors:
Electrical resistant probes This type of system uses a set of two probes working together. Additional sets of probes may be used as well. These can be installed in aggregate bins and/or mixers. Work by sending a small electrical charge into the aggregates and measuring the strength of the charge at the other probe. These devices do not measure the amount of water directly, since water does not conduct electricity. The charge is conducted through minerals or contaminates in the water. Therefore, a change in mineral content will change the conductivity for the same amount of water, changing the measurement. This is a potential problem when using city water, since the mineral content may vary or change without notice.
Microwave probes The most common is a microwave probe. These can be installed in aggregate bins and/or mixers. Originally developed by NASA, microwaves emit frequencies that spin the hydrogen atoms in water molecules and thus generate heat. Moisture sensors emit a higher-frequency microwave into the aggregate. These waves begin to spin the hydrogen atoms slightly, and the sensors measure the transmission of energy required to do this. As moisture increases, the sensor absorbs more waves and transmit greater energy. Essentially, these measure the true number of hydrogen atoms and therefore the water content.
Microwave probes require calibration when initial installation. Calibration requires several measurements from dry to wet aggregates and correlated to probe measurements. Follow-up verification testing should be performed every couple of days to confirm that the correlation of the measurement to moisture content is still accurate. See the “NPCA Quality Control Manual for Precast Concrete Plants” for more details on calibration frequency requirements.

## Slide 42
Concrete Batching: Cement Receiving & Storage
Notes: Cement delivery system at cement plant.

## Slide 43
Concrete Batching: Cement Receiving & Storage
Notes: Off loading of cement PM 2.5

## Slide 44
Concrete Batching: Cement Receiving Pneumatic Pumps
Notes: Pneumatic pumps and hoses are used in conjunction with a baghouse in the cement silo to transport and contain particulate emissions from the concrete batch plant. The cement and aggregate are typically loaded to the elevated bins/storage silo by pneumatic pumps and hoses, and a baghouse or bin vent filter connected to the silo provide further dust suppression.

## Slide 45
Dense-phase Pneumatic Conveying
  Moves material at low velocity to prevent material degradation and equipment wear
  Reduces segregation and promotes flow
  Dry bulk material is typically loaded into a vessel called a transporter
    Pressurized from 15 to 60 psi
Concrete Batching: Cement Receiving Pneumatic Pumps
Notes: Dense-phase (slug-flow) pneumatic conveying can provide. Moves material at low velocity to prevent material degradation and equipment wear…

## Slide 46
Concrete Batching: Cement Receiving Pneumatic Pump

## Slide 47
Concrete Batching: Cement Receiving Silo
Notes: Cementitious materials Cementitious materials are usually weighed in a separate hopper. Cement is commonly moved by means of a screw drive or auger, and sometimes pneumatically. Cement silos may also be located above a weigh hopper using gravity to load the hopper. Typically, cement is weighed first along with any supplementary cementitious materials in the same hopper. It is important when installing or replacing a cement auger that the auger is designed for use with cement. Storage silos should be inspected routinely to ensure there are no holes or water leaks. Moisture will activate the cement, which will waste material and possibly lead to system shutdown.

## Slide 48
Concrete Batching:
Cement Loadout

## Slide 49
Weigh Hopper
Concrete Batching: Weigh Hopper
Notes: After the dry ingredients are weighted they are placed in the hopper before dropping in the mixer.
Hoppers and scales should be calibrated annually or whenever there is reason to question their accuracy.
Refer to the “NPCA Quality Control Manual for Precast Concrete Plants” for more details.

## Slide 50
Bulk-Weighing Scale
Notes: The materials are weighed in a bin called the "Weigh Hopper," which in modern automatic scales is supported by load cells. The load cells generate an electrical signal proportional to the weight they support. A device called a "Scale Indicator" supplies power to the load cells, sums their output, and produces a digital signal which represents the combined weight of the grain and weigh hopper. The flow of grain into or out of the weigh hopper is controlled by slide gates. A scale control computer records the output of the scale indicator, subtracts off the weight of the hopper itself, and operates the gates.
After the scale control computer has recorded a valid tare, it opens the upper garner gates to allow grain into the weigh hopper. The indicator continually sends weight readings to the computer, which closes the upper garner gates when the weight passes a pre-set cutoff value. The computer again waits until the weight is stable and records the weight of the material and hopper combined (the GROSS weight).
After recording a valid gross weight, the scale control computer opens the weigh hopper gates. The dry ingredients drain rapidly into the lower garner, which normally is simultaneously discharging to a duct or a conveyor. The lower garner discharges at a slower rate than the weigh hopper, preventing it from overloading the conveyors downstream. When the weight readings from the indicator go below a pre-set lower cutoff value, the computer closes the weigh hopper gates and records another tare. Then the cycle repeats.
The net weight is the difference between the gross and the tare. When a scale is receiving the control computer takes a gross weight and subtracts the preceding tare weight to obtain the net weight.

## Slide 51
Load Out
Area

## Slide 52
Bin Vent Filter Serving Loadout

## Slide 53
Bin Vent Filter Serving Silos

## Slide 54
Bin Vent Filter Serving Loadout

## Slide 55
Bin Vent Filters

## Slide 56
Bin Vent Filters
Notes: During the filtering cycle, dust laden air is drawn into the bin vent filter by a positive air source such as a pneumatic conveying system. Air enters the bin vent filter through the hopper or storage bin and passes up through the filter cartridge. The clean air then passes through the plenum into the atmosphere. During the cleaning cycle, compressed air is injected through the cleaning nozzle to clean the cartridge. This energy charged air is directed downward against the interior of the filter cartridge, creating a positive back pressure and a shock wave. This action is immediately followed by an inrush of secondary atmospheric air that helps create a compression zone, causing the accumulated dust to be quickly released from the cartridge.

## Slide 57
Bin Vent Filters

## Slide 58
Bin Vent Filters

## Slide 59
Bin Vent Filters
Notes: Principles of Operation — Previous Page
Particles collect on the outside surface of the bags as the air stream passes through the filter media and up to the clean air plenum.
At timed intervals a selected solenoid valve actuates a diaphragm valve, releasing a predetermined volume or pulse of compressed air into distribution pipe, producing a shock wave along the length of the bag, flexing the fabric and dislodging dust particles from the surface.
The cleaning cycle can also be initiated by monitoring the differential pressure across the filter media as a result of dust build-up. Referred to as "cleaning on demand," this pulsing system only operates when bags require cleaning, minimizing compressed air consumption and lengthening bag life. Optional Smart Timer™ also available for these units. Top Access Units: Bags and cages are removed and installed from Flex-Kleen patented Trap 10 above the tube sheet. Our Trap 10 design provides the most effective tube sheet/bag seal available anywhere.
Bottom Access Units: Bags are removed from beneath the tube sheet. Broad range of filter media and surface finishes are available to handle high temperatures, smaller particle sizes, corrosive environments, sticky materials, etc. Venturies have multiple functions: 1) aspirate filtered air into the bag to create the cleaning pulse, and 2) retard the escape of the pressure wave from the top of the bag, causing multiple and repetitive pulses.
— Previous Page Flex-Kleen Division 955 Hawthorn Drive Itasca, Illinois 60143-2641 E-mail: info@flex-kleen.com

## Slide 60
Concrete Batching Process: Central Mix
Notes: Many concrete batch facilities will operate as a transit mix and central mix combined. The central mix will have a mixer that adds the water and dry ingredients together. A transit mix will weight and mix the dry ingredients only. A small amount of water is added as the load is placed in the truck…to minimize fugitive dust. The driver will then add water at the job site or prior to leaving the plant.

## Slide 61
Concrete Batching Process: Ready Mix

## Slide 62
Concrete Batching Process: Ready Mix

## Slide 63
Wait a minute before you loadout!

## Slide 64
Not acceptable!!

## Slide 65
Central Mix
Batch Mix
Concrete Batching Process

## Slide 66
Concrete Batching Process:
Batch Mix
Notes: Dry batch process/batch process. The mixer truck replaces the mixer and Aggregate, cement, sand water and add mixtures are dropped into the truck directly. The cement is mixed as it travels to the job site and most of the water is added after it is dropped into the truck.

## Slide 67
Concrete Batching Process:
Central Mix
Notes: Central mix. The concrete is mixed in the central mixer and dropped into the truck. Central mixes generate a more homogeneous mixture preferred by civil engineers. Water and admixtures are added directly to the dry ingredients before discharging into the delivery truck. The aggregates are dropped from the weigh batcher onto a conveyor belt, which charges the central mixer. If the cement’s weigh batcher is elevated sufficiently, it may discharge directly into the central mixer. Otherwise, the cement may discharge onto the aggregate conveyor belt charging the mixer.

## Slide 68
water
Central Mix
Notes: Water Water may be batched by volume or weight. Volumetric batching or metering of water is common, usually using a flow meter. The flow meter measures the volume of water that passes through the valve. One concern is that a flow meter does not distinguish the difference between air and water, and therefore some error may be introduced. Error may also result from leaky valves that allow water to dribble through when they are closed.
Considering the importance of water-cementitious ratio (w/c ratio), make every effort to ensure the accuracy of the water content. The most accurate method for measuring water is by weight as an alternative to a flow-meter.

## Slide 69
Concrete Batching Process: Rinsing
Notes: The US EPA as part of the US Clean Water Act requires Best Management Practices for rinsing of concrete trucks and equipment. BMPs are designed to prevent run-off into storm drains. The water generated is caustic and considered to be corrosive with a pH of 12, similar to drain cleaner.

## Slide 70
Concrete Ready Mix: Bagging Operation
Notes: Check for leaks, puffs, etc.

## Slide 71
Concrete Ready Mix: Bagging Operation

## Slide 72
Concrete Batching Operation
Portable Plant

## Slide 73
Not Portable Equipment
Remains in same location more than 12 consecutive month
Remains in same location less than 12 consecutive months, but production is equal to annual source operations (seasonal sources)
Unit is moved and returned to the same location
PERP vs Non-PERP

## Slide 74: Industry Description Concrete Recycling

## Slide 75
Concrete Recycling

## Slide 76
Crusher separates
metal from
Concrete

## Slide 77
Concrete Recycling

## Slide 78: Dust Control
Water Spray

## Slide 79: Magnate Used to remove material

## Slide 80: Screens

## Slide 81: Screening Operations
Screening Operations
Notes: Wire is the most popular. Who uses what is facility-dependent.
The rest include: Rubber-clad perforated screen plate, all rubber panels, profile screens, small parallel tapered bars for de-watering and fine screening, and high tensile steel wire screen decks.

## Slide 82: Screens
Notes: Wire is the most popular. Who uses what is facility-dependent.
The rest include: Rubber-clad perforated screen plate, all rubber panels, profile screens, small parallel tapered bars for de-watering and fine screening, and high tensile steel wire screen decks.

## Slide 83
Aggregate Storage Piles

## Slide 84
Aggregate Storage Piles

## Slide 85
PM from cement dust & concrete batching process
10% to 20% are smaller than 5 microns in diameter
PM10 & PM2.5 have health impacts
Air Quality Concerns
Notes: When cement is off loaded from a truck too fast puffing can occur. This picture is a good example of puffing out the baghouse. How can concrete batch plants affect our air quality?

## Slide 86
Inspection Procedures: Bags

## Slide 87
Inspection Procedures: Puffing Due to Improper Maintenance

## Slide 88
Inspection Procedures: Clogged Bags

## Slide 89
Inspection Procedures: Storage Hoppers
Notes: Compliance with Regulations. Check compliance with the regulations commonly
associated with concrete batch plants, including the requirements related
to visible emissions, fugitive dust, and particulate matter. (Compliance
Assistance technical manuals are also available for Aggregates, Hot Mix
Asphalt Facilities, and Baghouses.)
1. Visible Emissions (3%) Checklist (A CAP VE handbook is available.)
a. VE from the facility - Do you see any which violate opacity or
Ringelmann limits for your district?
b. Emission points - Check all possible points.

## Slide 90
Inspection Procedures: Fugitive Dust

## Slide 91
Passive enclosures
Wet suppression & baghouse maintenance
Paved surfaces Work practices
Housekeeping
Inspection Procedures: Preventative Measures

## Slide 92
Water sprays
Maintaining good housekeeping
Covers & wind barriers
Enclosures or hooding transfer points and screening operations
Air pollution control systems in order
Inspection Procedures: Preventative Measures

## Slide 93
Discharge from Conveyor
Inspection Procedures: Preventative Measures

## Slide 94
Discharge from Piping
Inspection Procedures: Preventative Measures

## Slide 95
Inspection Procedures: Preventative Measures
Packaging

## Slide 96
Inspection Procedures: Preventative Measures
Lack of Dust Control
Notes: Check the permit…would this be a potential violation…Remember we can’t use photos…hypothetically. Permit condition 10.

## Slide 97
Inspection Procedures: Preventative Measures
Lack of Dust Control
Notes: Check the permit…would this be a potential violation…Remember we can’t use photos…hypothetically. Permit condition 10.

## Slide 98
Inspection Procedures: Preventative Measures
Dust Control

## Slide 99
Inspection Procedures: Water Spray System
Notes: What should you check? Ensure that nozzles are not clogged and working properly Concrete is sufficiently wet that there are no visible emissions.

## Slide 100
Inspection Procedures: Water Spray/Enclosures

## Slide 101
Inspection Procedures: Load out
Notes: What it all looks like. What should you check?
Drop height, condition of shroud, dust.

## Slide 102
Inspection Procedures: Ducting to Baghouse
Notes: The two outside hoses are connected to a baghouse. Seen with a dry batch. When the raw materials are pumped into the truck (through the middle pipe) the two outside hoses are operating under a vacuum to pull the uncaptured raw products into a baghouse.
Check for tears, cracks, drop height, pressure of system.

## Slide 103
Inspection Procedures: Ducting to Baghouse
Notes: Siding curtains add additional mitigation to reduce fugitive dust.

## Slide 104
Inspection Procedures: Flexible Shroud
Notes: Shroud.
Mixer on top, flexible hose positions over the lip of the mixing truck.
If the fit is not snug, product will escape.

## Slide 105
Inspection Procedures: Flexible Shroud
Notes: Shroud.
Curtain-like device is used to further control dust during gravity drop.

## Slide 106
Engineering Evaluation
Air Emission Points
  6. Reclaim/Slurry Areas
  1. Deliveries
  2. Conveying/Transfer Points
  4. Mixing
  3. Ducting
  5. Shipping/Packaging
7. Stacks
Notes: “Particulate matter, consisting primarily of cement dust but
including some aggregate and sand dust emissions, is the pollutant of concern. In AP-42 all but one of the emission points are fugitive in nature. The only point source is the transfer of cement to the silo, and this is usually vented to a baghouse, fabric filter or ‘sock.’ Fugitive sources include the transfer of sand and aggregate, truck loading, mixer loading, vehicle traffic, and wind erosion from sand and aggregate storage piles. The amount of fugitive emissions generated during the transfer of sand and aggregate depends primarily on the surface moisture.” The types of pollutants emitted from each plant also depend on its peripheral operations and components, assorted machinery, internal combustion engines, and motor vehicles. Basically, most opportunities for pollutants to escape into the air occur at points where ingredients are transferred from one place or carrier to another, and where control equipment is not operating properly.

## Slide 107
Engineering Evaluation Typical Process With AP-42 Emission Factors
Notes: Predictive equation allow for emission factor adjustment based on plant specific conditions are given in the Background Document for Chapter 11.12 and Chapter 13. Whenever plant specific conditions are available, these should be used with the predictive equations (e.g. Equations 11.12-1 through 11.12-3) in lieu of the general fugitive emission factors presented in Table 11.12-1 through 11-12.-5 in order to adjust to site specific conditions, such as moisture levels and localized wind speeds.
Hand out Chapter with tables and emission estimate explanations. Develop an exercise based on these factors and a sample permit.
Reference. AP-42. Concrete Batch Plants 11.12 June, 2006

## Slide 108
Material | Composition by Weight (lbs/yd3)
Coarse Aggregate | 1865
Sand | 1428
Cement | 491
Cement Supplement | 73
Water | 20 gallons
Total Quantity Concrete Produced | 4024
Engineering Evaluation: Composition of 1 Cubic Yard of Concrete
(from AP-42)
Notes: Information on the composition and maximum annual quantity of the concrete to be produced. If that information is not available then the following information is used for 1 yard of concrete. But you should check with your district estimated may be different.
Reference. BAAQMD Permit Handbook. Concrete Batch Plants April 25, 2007

## Slide 109
Total PM* equation
Total PM emissions
0.282(Equation 11.12-1 or Table 11.12-2)
*Total PM= PM,PM10,PM10-2.5,PM2.5
yd3 of concrete
pounds
=
Engineering Evaluation: PM Emissions from 1 Cubic Yard of Concrete (from AP-42)
Notes: PARTICULATE EMISSION FACTORS PER YARD OF CONCRETE FOR AN AVERAGE BATCH FORMULATION AT A TYPICAL FACILITY ARE GIVEN IN TABLES 11.12-5 AND 11.12-6. FOR TRUCK MIX LOADING AND CENTRAL MIX LOADING, THE EMISSIONS OF PM,PM-10, PM-10-2.5 AND PM-2.5 ARE CALCULATED BY MULTIPLYING THE EMISSIONFACTOR CALCULATED USING EQUATION 11.12-2 BY A FACTOR OF 0.282 TO CONVERT FROM EMISSIONS PER TON OF CEMENT AND CEMENT SUPPLEMENT TO EMISSIONS PER YARD OF CONCRETE. THIS EQUAITON IS BASED ON A TYPICAL CONCRETE FORMULATION OF 564 POUNDS OF CEMENT AND CEMENT SUPPLEMENT IN A TOATAL OF 4,024 POUNDS OF MATERIAL (INCLUDING AGGREGATE, SAND, AND WATER). THIS CALCULATION IS SUMMARIZED IN EQUIATON 11.12-2

## Slide 110
E = k(0.0032) Ua + c
Mb
E = Emission factor in lbs/ton of cement and cement supplements
k = Particle size multiplier (dimensionless)
U = Wind speed at the material drop point (mph)
M = Minimum moisture (% by weight) of cement and cement supplement
a,b = Exponents
c = Constant
* (Equation 11.12-1 from Chapter 11.12 of AP-42)
Engineering Evaluation: Site Specific Emission Factor Truck Mix and Central Mix Loading*
Notes: The particle matter emissions from truck mix and central mix loading operations are calculated in accordance with the values in Table 11.12-1 or 11.12-2 or by Equation 11.12-1 when site specific data are available. Emission factors are expressed in lbs/ton of cement and cement supplement.
Reference. AP-42. Concrete Batch Plants 11.12 June, 2006

## Slide 111
Where:
E=Emission Factor (lb/VMT)
k=Particle size multiplier (dimensionless); PM10 k=0.36
s=Silt content of road surface (%); 12% average
S=Mean vehicle speed (mph); 20 mph
W=Mean vehicle weight (tons); 20 tons
w=mean number of wheels;14 wheels
P=Number of days with greater than or equal to, 0.01 inches of precipitation per year; 50.7 days
E=k(5.9)(s/12)(S/30)(W/3)0.7(w/4)0.5(365-P/365)lb/VMT
Engineering Evaluation: Unpaved Roads (added to emissions from storage piles & represent national average values)
Notes: Actual district values are typically more conservative (i.e., silt 10%, speed 5 mph, number of days of rain less than 50.7). VEHICLE TRAFFIC ON UPAVED ROADS TO AND FROM THE STROAGE PILES SHOULD ALSO BE ACCOUNTED IN THE EMISSIONS FOR THE STRAGE PILES. THE PERMIT ENGINEER SHOULD GET THE APPLICANT TO PROVIDE INFROMATION ON THE MAXIMUM VEHICLE MILES TRAVELED PER YEAR BY ALL VEHICLED INVOLVED IN DRIVING ON THE UNPAVED ROADS AT THE FACILITY. WATER USED TO SUPRESS DUST CAN ACHIEVE A MAXIMUM ABATEMENT EFFICEINCY OF 70%.
SAMPLE CALCULATION: EPM10=0.8(5.9)(12/12)(20/30)(20/30)0.7(14/4)0.5(365/50/365LB/vmt=6.9LABS/VMT
Reference. BAAQMD Permit Handbook. Concrete Batch Plants April 25, 2007
Chapter 13.2.2. Unpaved Roads of AP-42 (fifth edition, Volume I)

## Slide 112
AP-42 8.19, Table 8.19.1-1.
Loading into storage piles, equipment traffic in storage pile area and wind erosion
Assume:
    3.5lb/acre/day emission for TSP
    50% or 1.7 lb/acre/day for wind blown dust
Engineering Evaluation: Emissions from Storage Piles
Notes: THE PERMIT ENGINEER SHOULD OBTAIN INFORMATION FOR THE APPLICANT REGARDING THE MAXIMUM AREA (IN ACRES) OF STORAGE PILES AND THE NUMBER OF DAYS PER YEAR THAT THE STORAGE PILES WILL EXIST AT THE PLANT.
RAILCARS OR SHIPS ARE INVOLVED IN THE TRASPORATION OF MATERIALS, THEN INCLUDE THE COMBUSTION EMISSIONS FROM THE USE OF THESE TRASPORT VEHICLES AND INCLUDED IN THE FACILITY CUMULATIVE INCREASE.
Reference. BAAQMD Permit Handbook. Concrete Batch Plants April 25, 2007

## Slide 113
  Only the transfer points of cement and cement supplement into the storage silos are point source
    Storage silos abated by fabric filter, baghouse or binvent filter
Engineering Evaluation: Emissions Characterization
Notes: Reference. BAAQMD Permit Handbook. Concrete Batch Plants April 25, 2007

## Slide 114
  2. Transfer of sand & aggregate, truck loading, mixer loading, vehicle traffic, and wind erosion from sand and aggregate storage piles
    Water sprays, enclosures, and baghouse devices and good housekeeping, maintenance and wetting of unpaved surfaces
Engineering Evaluation: Emissions Characterization

## Slide 115
Baghouses are regulated in terms of
Grains/dry standard cubic foot of air emitted or
Pounds/ton of aggregate produced
Opacity
Engineering Evaluation: Dust Collection Systems

## Slide 116
IDL-ODL/IDL x 100 = CE
Where:
  IDL = inlet dust loading
  ODL = outlet dust loading
  CE = collection efficiency
Units = Grains/dry standard cubic foot
Engineering Evaluation: Dust Collection Control Efficiency
Notes: Efficiency
older equipment 95 to 99
Newer 99 to 99.9
Efficiency calculated based on size
Capture for particles less than 1 micron is minimal

## Slide 117
Baghouse
Baghouse Stack
Engineering Evaluation

## Slide 118: Inspection Objectives & Safety
Determine compliance with District, Federal regulations & permit conditions
Fugitive emissions
Dust Collector emissions
Visible emissions tests
General Maintenance
Records & logs
Corrective actions

## Slide 119
Dust Emissions?

## Slide 120
Thank You