## Slide 1
Aggregate Plants
NACT 246
Notes: Sand and gravel exist in natural deposits such as:
Read Slide.
Fluvial: Active or former stream channels.
Marine: Beaches.
Estuary: Estuary and harbor areas.
Glacial formed by glacial processes. They are deposited by melted water flowing along, under, or away from ice.
Alluvial fan: Mouths of canyons in arid and semi-arid areas of southwestern US.

## Slide 2
Course Overview: Aggregate Plants
Introduction
Emissions and Health Impacts
Aggregate Industry
Aggregate Process
Engineering Evaluation
Inspection Procedures
Notes: Cover course overview.

## Slide 3
Let’s Talk Rock

## Slide 4
Who?
How?
Emissions and Health Impacts
Notes: Groups most susceptible children, elderly and infants

## Slide 5
Emissions from Nonmetallic Mining
Particulate Matter
PM
PM10 & PM2.5
Gases
Toxics, ROGs,
CO, NOx & SOx
Asbestos & Heavy Metals
Notes: Significant impact on air pollution if it is not controlled or toxic fibers like asbestos from serpentine rock

## Slide 6
Total Organic Gases (TOG) | 0.22
Reactive Organic Gases (ROG) | 0.15
Carbon Monoxide (CO2) | 0.05
Oxides of Nitrogen (NOx) | 0.10
Oxides of Sulfur (SOx) | 0.01
Total Particulate Matter (PM) | 25.19
Particulate Matter PM10 | 11.73
Particulate Matter PM2.5 | 4.46
Emissions from Nonmetallic
Mining in California (tons/day)
Notes: The CO, NOx, & Sox are from combustion engines and other equipment at these operations. Small contribution relative to PM
Generates inert material larger than 10 microns and settles within the plant property
0.1 to 300 microns in size

## Slide 7: How Small is PM?
Human Hair
(60 m diameter)
PM10
(10 m)
PM2.5
(2.5 m)
Hair cross section (60 m)
Notes: To give you a perspective on how small these particles are, the left side of this slide shows an electron micrograph of a human hair.
On the right is a representation of the cross-section of the hair compared with two particles, one a 10-micron particle, and the other a 2.5-micron particle.
The majority of ultrafine particles are many times smaller than the PM2.5 particle shown in the picture.
Individually, these particles (coarse, fine, and ultrafine) are not visible to the naked eye. Together, however, fine particles can cause reduced visibility which we associate with “haze.”
PM is divided into many size fractions
PM10 is usually originates from fugitive dust
PM2.5 typically from combustion

## Slide 8
11 Microns and larger
7 to 11 Microns
4.7 to 7 Microns
3.3 to 4.7 Microns
2.1 to 3.3 Microns
1.1 to 2.1 Microns
0.65 to 1.1 Microns
0.43 to 0.65 Microns
Alveoli
Skin
Hair
Primary bronchus
Secondary bronchi
Pharynx
Trachea
Bronchioles
Notes: Discuss various PM sizes:
Particles come in all shapes and sizes. Aerodynamic diameter (PM#) depends on size and density.
1 inch = 25,400 microns
Raindrop = 1000 microns
Head of pin = 100 microns
Human hair = 50 microns
Limit of visible particles = 10 microns
Explain diagram:
Emphasize that >10 micron can be expelled by healthy body, <10 cannot and lodge at various levels as shown.
Studies showing that PM 2.5 probably the most problematic component affecting human health.
EPA as promulgated new standards for PM10 and PM2.5

## Slide 9: Health Effects of PM
The Cilia have been damaged from particulate exposure

## Slide 10
Asbestos
Emissions/Health Impacts

## Slide 11: Emissions/Health Impacts
X-ray of a lung exposed to asbestos
Results in mesothelioma

## Slide 12
Health Effects of PM10/PM2.5
Aggravated asthma
Respiratory Distress
Decreased Lung Function
Chronic Bronchitis
Notes: Particulates aggravate people with allergies or asthma as well as lead to early death in people with existing heart and lung disease

## Slide 13
Concerns???
Notes: So, how do we balance protection of human health while manufacturing the products we need to make our life more enjoyable?

## Slide 14
Concerns???

## Slide 15
Concerns???
Proximity to homes/parks?

## Slide 16
Concerns???

## Slide 17
Concerns???
Notes: The basic equipment in a concrete batch plant includes conveyors, elevators, silos, weigh batchers, and mixers

## Slide 18
Concerns?
NOV?

## Slide 19
Perception

## Slide 20
Perception

## Slide 21
Perception

## Slide 22
Perception

## Slide 23
Perception

## Slide 24
Perception

## Slide 25
Perception
Perception

## Slide 26
Let’s Discuss Aggregate Processing

## Slide 27
Let’s Discuss Aggregate Processing
Notes: Aggregate process

## Slide 28
Aggregate Processing: Wet or Dry?
Notes: The basic equipment in a concrete batch plant includes conveyors, elevators, silos, weigh batchers, and mixers

## Slide 29
Aggregate Industry
Notes: We are going to go through each step, explaining the operation, how it works, and the emissions associated with that step, if applicable.
Major rock types process by the aggregate industry include limestone, granite dolomite, traprock, sandstone, quartz and quartzite.
Minor types include calcareous marl, marble shell, and slate.
Major mineral types processed by the pulverized minerals industry include calcium carbonate, talc, and barite.
Industry classifications vary considerably and in many cases do not reflect actual geological definitions.

## Slide 30
Aggregate Industry
Definition of Natural Aggregate:
A material composed of rock fragments (sand, gravel, and crushed stone) that may be used in its natural state or crushed, washed and sized.

## Slide 31
Aggregate Industry
Sand and Aggregate are:
Loose mineral and rock particles
Transported by water and erosion
Key Differences:
Aggregate…passes through 2 inch screen
Sand…passes through1/4 inch opening (retained on a 200 mesh per squarer inch screen)
Notes: Particles larger than 2” are usually crushed
Large particles maybe used for
mass concrete in dames
riprap (large stone used for jetties or protecting slopes
Stream and beaches

## Slide 32
Crushed by
Mechanical Means
Natural
Aggregate Industry Type:

## Slide 33
Over the top??

## Slide 34
Benefits of Aggregate Processing

## Slide 35
Aggregate Processing and Control
Emissions and Control

## Slide 36
Aggregate Processing and Control
Notes: Bulk of the dust emission will settle close to the source
Even though fine particulate from sand and grave operations is small fraction of total…this may have significant effect on downwind air quality. Opacity is used as standard
Each facility is unique THEREFORE
Control efficiency based on visible observations of total particulate matter
Complaints tend to be about settled dust verses health possible effects

## Slide 37
Lack of Controls???

## Slide 38
Emission Sources
Plant Generated Dust
  Drilling
  Crushing
  Conveying
  Screening
  Stockpiling
Fugitive Dust
  Geologic material generated by:
    Wind
    Human activity

## Slide 39
Process & Controls
  Emissions are measured by knowing:
  How much aggregate is processed over time?
  How much moisture is in the material being processed?
  The control efficiency of the air pollution control device…
  Resulting in:
  Total Emissions (mass based…pounds/day or tons/year)
Notes: Focus will be to make visual observations

## Slide 40
Calculating Emissions
General equation from EPA AP-42 is:
E = A x EF x (1-ER/100)
where:
E = emissions
A = activity rate
EF = emission factor
ER = % overall emission reduction efficiency
Notes: Emissions estimated from each stage
Process rates express how much is produced over time
Emission factors are the amount of emissions per process unit
By knowing the process rate and and the emsision factor then you can get emission per unit of material processed

## Slide 41
Aggregate Mining
Two General Types:
  Sand and Gravel & Crushed Stone

## Slide 42
Aggregate Mining
Sand and Gravel Mining

## Slide 43
Aggregate Mining
Crushed Stone Mining

## Slide 44
Crushed Stone Mining
Drilling
Blasting

## Slide 45: Heavy Metals
Associated with quartz or volcanic deposits
Metals include nickel, cadmium and antimony
Become airborne during blasting or crushing
Questionable sources should be sampled for presence of heavy metals

## Slide 46
Aggregate Mining

## Slide 47
Material Dumping from Trucks

## Slide 48
Haul Road & Emissions

## Slide 49
SCALPING
SCREEN
PRIMARY
CRUSHER
SURGE
PILE
RECLAIM
TUNNEL
PRIMARY
CRUSHER
SECONDARY
CRUSHER
SECONDARY
SCREENS
SCREEN
PRODUCT SORTED
BY SIZE
SCREEN
Process from the Mine

## Slide 54
Aggregate Mining
Wash Plant

## Slide 55
Aggregate Mining
Wash plant with trommel screen

## Slide 56
Aggregate Mining
Recycled water from wash plant

## Slide 57
Wash Plant, Screen & Truck Loadout

## Slide 58
Aggregate Mining

## Slide 59
Process/Control, Crushing, Screening & Transfer Points
Notes: Each plant is going to have their specific type of equipment to meet the demands of that facility. For example, at this facility, there is so much clay in the ground, they use this double deck screen to wash off all the clay before conveying the raw material over for processing.

## Slide 60
Materials Handling
Feeders/Conveyors
  Primary
  Secondary
Crushers
  Primary
  Secondary
  Tertiary

## Slide 61
Feeders
Feeders are used to:
  Absorb the impact from dumping large quarried stone
  Feed the plant with a controlled, steady stream of raw material Used to handle muddy or sticky material
  They are located ahead of large, stationary primary crushers

## Slide 62
Application of Feeders

## Slide 63
Primary
Apron
Grizzly Belt
Feeders and Conveyors
Notes: Stationary grizzly - primary feeder.
Shot taken from top of feeder. Truck dumps a load on to the primary feeder.
Smaller-size material fall through grates, larger size are removed.

## Slide 64
Apron Feeders
Apron feeders are used where:
  Extremely rugged machines handling large feed are required
  Used to handle muddy or sticky material
  They are located ahead of large, stationary primary crushers

## Slide 65
Vibrating Feeder & Vibrating Grizzly Feeders
These feeders are used where:
  Used where a compact feeder with variable speed control is required
  Vibrating Grizzly feeder is similar plus grizzly bars for separating fines the crushed feed
  They help bypass fines around
  the primary crushers increasing
  production & reduces
  crusher liner wear.

## Slide 66
Vibrating Grizzly Feeders
Grizzly
  Vibrating Grizzly
  Step deck Grizzly
Notes: The vibrating action moves the material forward over the grizzly section so the fines fall through and bypass the crusher.
The grizzly portion (teeth) is adjustable for diverse feed sizes.

## Slide 67
Vibrating Grizzly Feeders
Reduces crusher liner wear

## Slide 68
Grizzly Feeder
Notes: Transported to the processing plant
Then raw s and G is stockpiled in the processing area
Crushing when used…reduce production of fines that must be removed by washing
Most feed does not get crushed
Some plants do none at all

## Slide 69
Grizzly Feeder

## Slide 70
Vibrating Grizzly Feeder
Jaw Crusher

## Slide 71
Belt Feeders
Belt feeders are used:
  Under a hopper or trap with 6” maximum feed size
  They have an infinite variable speed control for optimum plant feed rate

## Slide 72
Belt Feeders & Conveyors
Feeder with Spray Bar

## Slide 73
Vibrating Pan
Notes: Vibrating Pan - secondary feeder.
Sloped trough w/flat or slightly rounded bottom w/shallow sides and an open end.
The device hanging is a flow switch/tilting mercury switch. The switch informs the operator there’s material in the pan.

## Slide 74
Primary Conveyor
Conveyor with Spray Bar

## Slide 75
Wobble Feeder
Combined feeder and scalper
Effective in handling clay or fine sticky feed material

## Slide 76
Wash Plant
Notes: The next step in the process involves washing the raw materials or rocks to remove any excess dirt, clay or sand.

## Slide 77
Wash Plant

## Slide 78
Wash Plant w/trommel screen

## Slide 79
Recycled Water from Wash Plant

## Slide 80
Wash Plant, Screens, & Truck Loadout

## Slide 81
Wash Plant
Notes: Not all facilities washing systems are going to look the same.
This facility uses a log washer.
The logger is slightly tilted so that the product (rock) moves upstream against the flow of the water rinsing off or washing off the dirt as a result of force/pressure.
The log washer is attached to a cyclone separator which captures the water and sends it over to a settling pond so that the facility can reuse the water.

## Slide 82
Secondary Wash
Notes: Depending on the location, a facility may have two or more washing tubs.

## Slide 83
Conveyors

## Slide 84
Conveyors
Notes: A facility can have miles of conveyors. As a plant operator as well as an inspector, a plant like this could take an entire morning or day to inspect.
Conveyors are run off electric motors

## Slide 85
Conveyors with Baghouse

## Slide 86
Conveyor with Baghouse

## Slide 87
Conveyor Belt Feeder
Conveyor Belt
Belt feeder with adjustable feed gate

## Slide 88
Crushing
Fracture Mechanisms
Crushing Equipment
Factors Influencing Crushed Product

## Slide 89
Fracture Mechanisms
Particle Breaking:
  Abrasion
  Cleavage
  Shatter

## Slide 90
Primary or Jaw Crusher

## Slide 91
Jaw Crusher
Notes: Bulk of the dust emission will settle close to the source
Even though fine particulate from sand and grave operations is small fraction of total…this may have significant effect on downwind air quality. Opacity is used as standard
Each facility is unique THEREFORE
Control efficiency based on visible observations of total particulate matter
Complaints tend to be about settled dust verses health possible effects

## Slide 92
Jaw Crusher

## Slide 93
Jaw Crusher

## Slide 94
Jaw Crusher
3” to 8” Rock

## Slide 95
Jaw Crusher
No spray bars

## Slide 96
Spray bars to reduce emissions

## Slide 97
Jaw Crusher

## Slide 98
Cone Crusher

## Slide 99
Cone Crusher

## Slide 100
Cone Crusher

## Slide 101
Cone Crusher

## Slide 102
Cone Crusher

## Slide 103
2”
1 ¾”
1 ½”
1 ¼”
1”
¾”
5/8”
½”
3/8
size
rock
Cone Crusher

## Slide 104
Cone Crusher

## Slide 105
Cone Crusher
Baghouse
???

## Slide 106
Impact Crusher

## Slide 107: Impact Crusher
Upper Apron
Adjustable Apron Supports
Alloy Steel Liners
Wedges
Hammers
Lower Apron
Rotor
Impact Crusher

## Slide 108
  Hammer Mill
Tertiary Crusher

## Slide 109
Grinding Mill or Ball Mill
Dry ball mills most popular, due to economics
Used for finer material separation

## Slide 110
Grinding Mill or Ball Mill
Media are rods or balls
Rods are for coarse material
  manufactured sand
  cement clinker

## Slide 111
Screening Operations

## Slide 112
Screening
FROM THE MINE
SCALPING
SCREEN
PRIMARY
CRUSHER
SURGE
PILE
PRIMARY
CRUSHER
SECONDARY
CRUSHER
SECONDARY
SCREENS
SCREENS
PRODUCT SORTED
BY SIZE
RECLAIM
TUNNEL
Notes: Feeders, conveyors, chutes, hoppers, and storage bins are all elements of the “Materials Handling” component of the aggregate industry.

## Slide 113
Screening Operations

## Slide 114
Screening Operations

## Slide 115
Screening Operations

## Slide 116
Screening Operations

## Slide 117: Screening Surface

## Slide 118
Screening Operations

## Slide 119
Screens
Notes: Wire is the most popular. Who uses what is facility-dependent.
The rest include: Rubber-clad perforated screen plate, all rubber panels, profile screens, small parallel tapered bars for de-watering and fine screening, and high tensile steel wire screen decks.

## Slide 120
Screening Operations
Notes: There can be several screens in one screening unit. These are used to separate sizes. Let’s say there are 3 screens. They can produce up to 3 sizes of rock. Each level has the different size screen. The rocks which can’t pass through the first screen are called “overs” (larger size rocks).
Rocks which can pass through the first screen but not the second are called “between”. The rocks that go through both screens are referred to as “unders”.

## Slide 121
Fugitive Dust from Screening Operations

## Slide 122
Screens

## Slide 123
Screen Tests @ Lab

## Slide 124
Screens and Baghouses

## Slide 125
Point Emissions
Point emissions originate from stacks
  Control Devices
  Where aggregate is dried
Stack emissions
  Moisture
  Gases
  PM/PM10/PM2.5
  All of the above

## Slide 126
Point Emissions

## Slide 127
Stock Piling
Could be a potential source of fugitive dust emissions

## Slide 128
Screening, Storage, and Loadout Operations

## Slide 129
Storage & Loadout Operations
Notes: You will see a lot of these at sand and gravel facilities.
They are usually connected to an air pollution control device or they may have individual collection system on top.
At this particular facility, the silos are connected to a baghouse.

## Slide 130
Air Pollution Control Measures
Preventative Measures
  Passive Enclosures
  Wet/Chemical Suppression
  Paved Surface/Cleaning
Dry Collection Systems
  baghouse
  cyclone

## Slide 131: Process & Control Measures
Control
Moving conveyors or trucks (passive control is wind screens
Operations
Crushing (active control is water)
Transfer (active control is water)

## Slide 132: Air Pollution & Control Measures
Water sprays
Maintaining good housekeeping
Covers
Enclosure or cover at transfer points and screening operations
Exhausting air to air pollution control systems

## Slide 133
Preventative Measures
Passive enclosures
Wet suppression
Stabilization of unpaved surfaces
Minimizing drop height
Paved surfaces cleaning
Work practices
Housekeeping

## Slide 134
Preventative Measures

## Slide 135
Belt Conveyors
Crusher
Spray
Header
nozzle
Rubber
Skirt
Belt
Idlers
Suppressant
Rubber Skirt
Filter
Preventative Measures

## Slide 137
Baghouses are regulated in terms of:
Grains/cubic foot or air emitted (gr./dscf)
Pounds/Ton of Aggregate produced
Opacity
Dry Collection Systems

## Slide 138
Baghouse
in
Disrepair

## Slide 139
Combination Systems
Dry collection and wet suppression
  When fine particulates have an economic value in addition to meeting air pollution control laws
  Due to screen blinding
  Due to plant location or local pollution control codes, which is not economically feasible

## Slide 140: Other Processing Equipment
Rock Breaker
Magnets
Metal detector
Pugmills
PERP equipment
Washing equipment
Rotary Scrubber
Wet classifiers
Pumps Grinding Mills

## Slide 141: Inspection Objectives
Determine compliance with:
District regulations & permit conditions
Fugitive dust
Visible emissions
Oxides of nitrogen (for fuel burning equipment)
Control devices

## Slide 142: Pre-Inspection
Regulation Review
Equipment Check
  Safety goggles and earplugs
  Safety shoes, hard had, and gloves
  ID and business cards

## Slide 143
Permit application
Approved permit
Equipment
Permit condition for each unit
Previous inspection reports
NTC/NOV
Compliance action
Complaints
Variance history
Abatement orders
Date of last source test
Pre-Inspection File Review
Notes: Use…Compliance checklist or rule specific compliance forms

## Slide 144
Observe the site
  Note odors or visible emissions
  Size and layout
  Environmental demeanor
ID potential problem areas
Enter through normal public access
Introduce yourself, ask to see contact listed in file, & present business card
Pre - Entry & Entry
Notes: Know and follow your district’s policy when the site refuses entry

## Slide 145: Pre – Inspection Meeting
State purpose of inspection and identify equipment to be inspected
Discuss any outstanding business
Obtain
  Company name
  Ownership information
  Address
  Contact information
  Operating schedule, date of last source test and fuel usage

## Slide 146: Pre-Inspection Meeting
Date of last break down
Determine the statues of:
  Dust suppression equipment
  Air pollution control equipment
  Monitoring and recording devices
Check permit

## Slide 147
Non - Compliance
A NTC/NOV is issued when:
The permit is not:
  Current or no permit
  Posted properly
Or conditions on permit are not followed
Or blatant disregard for the permit conditions

## Slide 148
Post - Inspection
Make compliance determination
Inform site of inspection (NOVs, and advise on areas of concern)
Document pending NOVs due to additional info request etc.

## Slide 149
Safety