## Slide 1: Module 1: Introduction to Continuous Monitoring Systems (CMS)
Photo reprinted with permission from Alabama Dept of Environmental Management

## Slide 2: Module 1 Outline

## Slide 3: Module 1 Learning Objectives
At the end of Module 1, learners will be able to:
  Recognize the different types and uses of CMS
  Identify the regulations that contain CMS requirements
  Recognize, in general, what performance specifications are and how they are used
  Recall enforcement aspects of CMS

## Slide 4: What are CMS?
Continuous monitoring systems (CMS) means “the total equipment, required under the emission monitoring sections in applicable subparts, used to sample and condition (if applicable), to analyze, and to provide a permanent record of emissions...”40 CFR Part 60

## Slide 5: Why CMS?
CMS are required under some of the EPA regulations for either continual compliance determinations or determination of exceedances of the emissions standards.
The individual subparts of the EPA rules specify the reference methods that are used to substantiate the accuracy and precision of the CMS.

## Slide 6: Basis for CMS Programs
As a result of the Clean Air Act (CAA), many pollution control devices such as baghouses, scrubbers, and electrostatic precipitators have been installed.
After the equipment is installed and operating, an air pollution control agency needs to know if the equipment is actually reducing emissions and if the facility is meeting its emissions standards.
CMS programs are one of the methods used to measure emissions from stationary sources.

## Slide 7: Basis for CMS Programs (Cont’d)
EPA established two methods to measure concentrations of pollutants from regulated sources:

## Slide 8: Reference Methods
Reference methods are beneficial, but may have disadvantages when compared to using a CMS:
  Performed infrequently and for a relatively short period of time (hours)
  Often conducted when the source is operating under optimal conditions, which may not result in producing normal, day-to-day emission values

## Slide 9: CMS
CMS have become an important part of a facility’s compliance demonstration. The advantages of CMS are:

## Slide 10: CMS Are Used To…
Demonstrate compliance with regulations
Generate data that can be used to develop regulations
Improve emission databases
Monitor control equipment operation
Monitor process operating parameters
Identify periods of excess emissions
Assess control equipment efficiency
Validate emission credits
Provide public assurance

## Slide 11: Types of CMS
The four types of CMS:
  Continuous Opacity Monitoring Systems (COMS)
  Continuous Emission Monitoring Systems (CEMS)
  Predictive Emission Monitoring Systems (PEMS)
  Continuous Emission Rate Monitoring Systems (CERMS)

## Slide 12: Continuous Opacity Monitoring Systems (COMS)
12

## Slide 13: COMS
COMS consist of the total equipment used to sample, analyze, and provide a permanent record of opacity.
COMS use light to determine opacity levels.
Due to absorption and scattering of light by dust, smoke, and/or particulate present in the gas stream, there will be an attenuation of the transmitted light and a decrease in the light intensity that is measured.
COMS can be “single pass” or “double pass.”

## Slide 14: COMS (Cont’d)

## Slide 15: Typical Sources with COMS Requirements
COMS are typically used by facilities that rely on waste materials, oil, coal, wood, or other fossils fuels for combustion.
Examples of sources are:
  Utilities
  Boilers
  Flares

## Slide 16: Continuous Emission Monitoring Systems (CEMS)

## Slide 17: CEMS Definition
CEMS consists of the total equipment necessary to determine a gas or particulate matter emission concentration.
Image courtesy of Thermo Fisher Scientific™

## Slide 18: CEMS
CEMS:
  Continuously measures actual emissions from stationary sources by extracting a sample of gas from the emission source:
      Sample gas may be filtered, transported, conditioned, or diluted before being presented to the analysis system.
      Gas concentrations are measured, recorded, and stored as data.
  May also include components for measuring particulate matter, and stack gas flowrate

## Slide 19: CEMS: Illustrative Example

## Slide 20: Basic CEMS Components
CEMS consist of the following:
Sample Interface. The portion of the system that is used for one or more of the following:
  sample acquisition,
  sample transportation,
  sample conditioning, or
  protection of the analyzer from the effects of the stack effluent.
Analyzer/Measurement Method. The portion of the system that senses the gas or particulate and generates an output proportional to the gas or particulate concentration.
Data Acquisition System. The portion of the system that records a permanent record of the measurement values. The data acquisition system, or DAS, may include automatic data reduction capabilities.

## Slide 21: Major Components of CEMS
Sample Probe
Filter
Sample Line (umbilical)
Gas Conditioning System
Calibration Gas System
Gas Analyzers (may include more than one)
Data Acquisition Systems (DAS)
Data Acquisition System
Extractive Conditioning System
Gas Analyzers

## Slide 22: Cylinders of EPA Certified Gases and CEMS Cabinet
Cylinders of EPA Certified Gases
Inside a CEMS Shelter
Outside a CEMS Shelter

## Slide 23: CEMS Unit Shelter

## Slide 24: Typical Sources with CEMS Requirements
CEMS are generally required on larger emitting stationary sources. Below are a few examples:
  Utilities
  Cement Plants
  Municipal Waste Combustors
  Nitric and Sulfuric Acid Plants
  Petroleum Refineries
  Copper, Zinc, and Lead Smelters
  Steel and Ferroalloy Plants
  Kraft Pulp Mills
  Glass Manufacturing Plants
  Magnetic Tape Production
  Phosphate Plants

## Slide 25: Predictive Emission Monitoring Systems (PEMS)
25

## Slide 26: PEMS
The total equipment necessary to predict an emission concentration or emission rate.
The system may consist of any of the following major subsystems: sensors and sensor interfaces, emission model, algorithm, or equation that uses process data to generate an output that is proportional to the emission concentration or emission rate, diluent emission model, data recorder, and sensor evaluation system.

## Slide 27: PEMS (Cont’d)
Software-based system which uses process values as input variables to provide a real-time estimation of emissions by means of derived mathematical or statistical algorithm
PEMS are an acceptable regulatory alternative to CEMS for source emission compliance in some regulations.
Examples of Input Variables

## Slide 28: Continuous Emission Rate Monitoring Systems (CERMS)
28

## Slide 29: CERMS
  Is the total equipment required for determining and recording the pollutant mass emission rate (in terms of mass per unit of time)
  Includes the use of a flow rate monitor to measure the volumetric flow rate of the emission stream and generate an output proportional to that flow rate

## Slide 30: CMS in Federal Regulations

## Slide 31: 40 CFR, Part 60 - New Source Performance Standards (NSPS)
CAA, Section 111 establishes mechanisms for controlling emissions of air pollutants from stationary sources:
      Section 111(b) provides authority for EPA to promulgate new source performance standards (NSPS) which apply only to new and modified sources.
      Section 111(d) requires regulation of existing sources.
These standards limit the amount of air emissions (SO2, NOx, etc.) that may be emitted from stack sources.
The performance specifications and quality assurance procedures for CMS are found in Appendix B and F of 40 CFR, Part 60.

## Slide 32: 40 CFR Part 61 - National Emission Standards For Hazardous Air Pollutants (NESHAP)
Established under Section 112 of the CAA
Promulgated prior to November 15, 1990, the date of enactment of the CAA amendments of 1990
National emission standards for hazardous air pollutants (NESHAP) contained in this part remain in effect until they are amended, and if appropriate, added to Part 63.

## Slide 33: 40 CFR, Part 63 - National Emission Standards for Hazardous Air Pollutants (NESHAP) for Source Categories
Established under Section 112 of the 1990 amendments to the CAA
These standards regulate specific categories of stationary sources that emit (or have the potential to emit) one or more hazardous air pollutants listed in this part.
The standards in this part are independent of the NESHAP contained in 40 CFR Part 61.

## Slide 34: 40 CFR, Part 75 – Acid Rain Program
Established under Title IV of the CAA of 1990
First national cap and trade program in the country
Requires major emission reductions of SO2 and NOX from the power sector
SO2 and NOX are the primary precursors for acid rain.
Since Part 75 is handled by EPA’s Clean Air Markets Division (CAMD), the Part 75 monitoring requirements are not the focus of this training.

## Slide 35: Performance Specifications and Quality Assurance
Performance Specifications are used for evaluating the acceptability of the CMS at the time of, or soon after installation, or whenever specified in the regulations.
Quality Assurance (QA) procedures are used to evaluate the effectiveness of quality control (QC) and the quality of data produced by any CMS that is used for determining compliance with the emission standards as specified in the applicable regulation.
Performance specifications and QA procedures can be found in 40 CFR, Part 60 Appendices B and F, respectively.

## Slide 36: Use of CEMS Data for Enforcement
CEMS can provide accurate data regarding a source’s compliance with the emissions limits and standards.
  CEMS data can be more representative of a source’s ongoing compliance status when compared to infrequent performance testing, and
  CEMS data typically can cover a greater percentage of a source’s time in operation.

## Slide 37: Use of CEMS Data for Enforcement (Cont’d)
CEMS data is important to enforcement, irrespective of whether the legal requirement being enforced specifies CEMS as the compliance method.
  The CAA authorizes EPA to bring an administrative, civil, or criminal enforcement action “on the basis of any information available to the administrator.”
  The 1997 “Credible Evidence” revisions to 40 CFR Parts 51, 52, 60, and 61 clarified that non-reference test data, including CEMs, can be used for establishing whether or not the source has violated or is in violation of any standard of that part.

## Slide 38: Enforcement Applications of CEMS
The governing regulation* specifies CEMS as the compliance method.
The governing regulation* specifies some method other than CEMS as the compliance method, or the governing regulation doesn’t specify a compliance method.
* e.g., 40 CFR Part 60

## Slide 39: CEMS is the Compliance Method
Required by some NSPS, National Emission Standards for Hazardous Air Pollutants (NESHAPS) and State Implementation Plans (SIPs)
Includes data validation requirements
Requires monitoring against emission limits with long averaging time
Data documents compliance against the emissions standard

## Slide 40: CEMS is not the Compliance Method
CEMS data is “Credible Evidence:”
Data is used for initiating and supporting enforcement cases alleging emissions violations.
CEMs data may provide a basis to issue a Section 114 request for compliance method data.
CEMs data may be used to enforce operation and maintenance, monitoring and recordkeeping and reporting requirements, when the regulation does not specify a compliance method or an emissions standard (e.g. General Duty Clause).

## Slide 41: Let’s Test Your Knowledge!

## Slide 42: Types Of Continuous Monitoring Systems
1. CMS are used to identify periods of excess emissions, assess control equipment efficiency, and monitor control equipment operation.
True
False
True! In addition, CMS are also used to:
Demonstrate Compliance with Regulations
Generate Data that can be Used to Develop Regulations
Improve Emission Data Bases
Monitor Process Operating Parameters
Validate Emission Credits
Provide Public Assurance of Compliance

## Slide 43: Uses of CMS
1. CEMS are used for continuous compliance determinations or determination of exceedances of the standards.
True
False
True! CEMS are used for continuous compliance determinations or determination of exceedances of the standards.
2. COMS use light to determine percent opacity.
True
False
That true! COMS use light to determine percent opacity
3. PEMS use direct measurements of emissions to determine results.
True
False
This is false. PEMS use process or control device operating parameter measurements and a conversion equation, graph, or computer program to yield final results
4. CERMS determine and record the pollutant mass emission rate.
True
False
It’s true. CERMS are the total equipment required for determining and recording the pollutant mass emission rate (in terms of mass per unit of time).

## Slide 44: Regulations – Question 1
The regulations that detail the monitoring, recordkeeping, and reporting requirements of the first national cap and trade program in the US are found in 40 CFR, Part 75- Acid Rain Continuous Emission Monitoring.
True
False
This is true.

## Slide 45: Regulations – Question 2
Performance specifications and quality assurance procedures for CMS are contained in Appendices B and F of 40 CFR, Part 60 – New Source Performance Standards.
True
False
That’s true. Performance specifications and quality assurance procedures for CMS are contained in Appendices B and F of 40 CFR, Part 60 – New Source Performance Standards.

## Slide 46: Performance Specifications
1. Performance Specifications are used to evaluate the effectiveness of quality control and the quality of data produced by any CMS.
True
False
This is false. Performance specifications are used for evaluating the acceptability of the CMS at the time of, or soon after installation, or whenever specified in the regulations. The QA procedures are used to evaluate the effectiveness of quality control and the quality of data produced by any CMS.

## Slide 47: Activity
Title: Group Experts
Purpose: To become an “expert” on the knowledge learned from Module 1 for an assigned CMS. Share information and help your peers understand and retain this information.
Time: 40 minutes
            20 minutes in groups
            20 minutes group debrief

## Slide 48: Activity Debrief

## Slide 49: Module 1 Summary
Now that you have completed Module 1, you should be able to:
  Recognize the different types and uses of CMS
  Identify the regulations that contain CMS requirements
  Recognize, in general, what performance specifications are and how they are used
  Recall enforcement aspects of CMS