## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 8: Other Tools

## Slide 2: TOXC102+ Chapter 8: Other Tools What is HEM?
Human Exposure Model (HEM): Used to perform risk assessments for sources emitting air toxics to ambient air
Only addresses the inhalation pathway of exposure
Predicts risks associated with chemicals emitted into the ambient air (nearby but beyond facility's property boundary)
Output is ambient air concentrations (as lifetime exposure)
Combine with IUR and RfC to produce estimates of cancer risk (Risk) and noncancer hazard (HQ) for air toxics modeled
Use HEM instead of AERMOD for air toxics

## Slide 3: TOXC102+ Chapter 8: Other Tools HEM

## Slide 4: TOXC102+ Chapter 8: Other Tools HEM Data Requirements
Input
Facility List Options (Excel) File: List facilities to be modeled and specify model run parameters and options
HAP Emissions (Excel) File: Provide names and amounts of air toxics emitted from each emission source in facility list
Emissions Location (Excel) File: Provide emission source locations and configurations for facility list
HEM provides additional databases necessary for the run including meteorological, census (elevations, population, demographics), and HAP dose response toxicity

## Slide 5: TOXC102+ Chapter 8: Other Tools HEM Data Requirements
Advanced HEM
Additional Input Files for more Advanced HEM Runs:
Polygon Vertex (source)
Buoyant Line Parameter (source)
Building Dimensions (building downwash)
Emissions Variation (temporally-varying emissions)
Input Files for Particle and Gas Deposition
User-Defined Receptors

## Slide 6: TOXC102+ Chapter 8: Other Tools HEM Data Requirements
User inputs Facility’s Source & Emissions Information into HEM
HEM combines with Met & Census Databases
HEM applies Dose Response Data
Air Concentrations,
Cancer Risk and Incidence
Noncancer Health Impacts
HEM Strengths:
For each facility run, AERMOD is used for multiple pollutants (instead of 1 pollutant)
HEM applies dose-response relationships to the modeled air concentrations for cancer risk, population incidence, and noncancer health impacts (instead of only air concentrations)
HEM runs AERMOD for each facility to obtain air concentrations

## Slide 7: TOXC102+ Chapter 8: Other Tools HEM Process
HEM is Risk Assessment Simplified
HEM provides facility info, 1 year of meteorological data, and census data to AERMOD
AERMOD (within HEM) simulates hour-by-hour dispersions from emission sources into the atmosphere
AERMOD (within HEM) outputs annual average ambient air concentrations at receptor locations (including census block centroids)

## Slide 8: TOXC102+ Chapter 8: Other Tools HEM Data Output Selection
Results for all modeled facilities in the run group:
Cancer Drivers
Hazard Index (non-cancer) Drivers
Acute (short-term) impacts
Multipathway (non-inhalation)
Max Concentration
Max Risk & HI by Source and Pollutant
Risk & HI Histogram (# people)
Source Type Risk Histogram

## Slide 9: TOXC102+ Chapter 8: Other Tools HEM Data Output Selection

## Slide 10: TOXC102+ Chapter 8: Other Tools HEM Data Output Selection
Demographics
Demographics by radius (up to 50 km)
Provide demographics as percentage by:
  Race;
  Age;
  Poverty Status;
  High School Graduates;
  Limited English Speaking; and
  Disabilities.

## Slide 11: TOXC102+ Chapter 8: Other Tools HEM Data Output Selection
Results by Demographics
Demographics by cancer risk level
  Enter cancer risk levels of 1-, 5-, 10-, 20-, 30-, 40-, 50-, 100-, 200- or 300-in-1 million
  Population and demographics with cancer risk greater than or equal to level specified
Demographics by non-cancer HI level
  Enter non-cancer HI levels of 1 to 10
  Population and demographics with non-cancer HI greater than level specified
Total of 4 cancer / non-cancer risks can be run simultaneously

## Slide 12: TOXC102+ Chapter 8: Other Tools HEM Data Output Selection

## Slide 13: TOXC102+ Chapter 8: Other Tools HEM Data Output

## Slide 14: TOXC102+ Chapter 8: Other Tools HEM Data Output
HEM Output:
One HEM run produces over 30 tables of outputs
  Provides different ways of looking at the predicted and modeled cancer risk and non-cancer health impacts
Provides risk drivers, including the source type drivers (e.g., a specific process type) and the pollutant drivers
  Can be used for regulatory or permit development

## Slide 15: TOXC102+ Chapter 8: Other Tools HEM Data Output
HEM Outputs Formats:
Tabular: Individual modeled facility or a summary for entire run
Maps: Google Earth™ map showing cancer and non-cancer risk levels, by acute (short term) or (chronic/lifetime) impacts
Graphs: Pie charts and bar charts of cancer incidence by pollutant, risk drivers (cancer and non-cancer) and population at risk level
Risk Contours: Overlay of colored-coded risk levels on map
Demographic Assessment Results: Tables and bar charts of each demographic analyzed compared to nation, state, county

## Slide 16: TOXC102+ Chapter 8: Other Tools HEM Data Output
Example HEM Outputs

## Slide 17: TOXC102+ Chapter 8: Other Tools HEM Data Output
Google Earth™ Map
Point, area, and lines sources within red polygon
Receptors:
  Populated census blocks (squares)
  Polar grid receptors (circles)
  MIR receptor with red “X”
  Red: Total cancer risk >100 in a million
  Yellow: Total cancer risk level between 20 and 100 in a million
  Green indicates a risk <20 in 1 million
Example HEM Output

## Slide 18: TOXC102+ Chapter 8: Other Tools HEM Data Output
Risk Contour Maps
Colored contours represent different risk levels around a modeled facility
  Yellow is highest risk closest to the facility at >200-in-1 million
  Purple is areas with lowest modeled risk <3-in-1 million
Can overlay contours on street or satellite maps

## Slide 19: TOXC102+ Chapter 8: Other Tools ProxTool
ProxTool
Provides population and demographics for selected locations
  No emissions data
  Used when emissions data unavailable or a risk analysis not needed
ProxTool can be run much faster and include thousands of facility locations into each input
ProxTool outputs results useful for informing and supporting rulemaking decisions for all air pollutants (e.g., air toxics, HAPs, criteria), because it’s not risk based

## Slide 20: TOXC102+ Chapter 8: Other Tools ProxTool
ProxTool Inputs
Input file has 3 columns:
  Facility ID
  Longitude
  Latitude

## Slide 21: TOXC102+ Chapter 8: Other Tools ProxTool

## Slide 22: TOXC102+ Chapter 8: Other Tools Census Circular Area Profiles (CAPS)
Missouri Census Data Center CAPS
Aggregates 2019-2023 American Community Survey (ACS) data to approximate population and demographic data
Data Input:
  Single latitude / longitude or ZIP Code and up to 5 radius values (≥3 miles)
Data output:
  Demographic, Economic, Social, and Housing
  mcdc.missouri.edu/applications/capsACS.html

## Slide 23: TOXC102+ Chapter 8: Other Tools National Inventories
National Emission Inventory (NEI): Detailed estimate of criteria pollutants and HAP
Includes air emissions from point, nonpoint, onroad, and nonroad sources and air pollution events like wildfires
AirToxScreen 2020: Screening tool with data and risk analysis for air toxics
Replaced National-Scale Air Toxic Assessment (NATA) in 2017
Cancer risk and non-cancer hazard data available 2017-2020
www.epa.gov/AirToxScreen/airtoxscreen-mapping-tool

## Slide 24: TOXC102+ Chapter 8: Other Tools 2014 NATA Cancer Risk by County