## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 1: Air Toxics Background

## Slide 2: TOXC102+ Chapter 1: Air Toxics Background Epidemiology vs Toxicology
Amended on 09/16/2019 by Andrew D. Shroads, QEP on 09/16/2019 • ashroads@scainc.com • 614-887-7227
Epidemiology:
What is causing a person to experience this particular harmful effect?
  Known effect; determine the cause
Toxicology:
Seeks to discover the relationship between the amount taken in (dose) and the degree of effect (response)
  Known or suspected cause; determine the adverse health effects (by dose)
“All things are poison and nothing [is] without poison. Solely the dose determines that a thing is not a poison.” - Paracelsus (1493-1541)

## Slide 3: TOXC102+ Chapter 1: Air Toxics Background Dose
Dihydrogen Monoxide (H2O) Safety Data Sheet (SDS):
Eye: Irritant in sensitive persons
Skin Contact: May cause discomfort (temperature dependent)
Skin Absorption: May cause temporary wrinkling of skin
Inhalation: Inhalation of liquid can be fatal
Ingestion: Ingestion of large quantities may result in excessive micturition, intoxication, and death
Jennifer Strange, a 28-year-old mother of three, died from acute water intoxication in 2007 after participating in a radio station’s water drinking contest “Hold Your Wee for a Wii.”

## Slide 4: TOXC102+ Chapter 1: Air Toxics Background History of Epidemiology
BCE Greeks & Romans were aware of lead poisoning and noticed exposure to lead fumes impacted health
  Plumbism: Disease limited to miners and metallurgists
1775 Percival Pott observed scrotal cancer in chimney sweeps
  First observed cause-effect relation between an environmental agent and cancer
1854 Dr. John Snow traced London’s cholera outbreak to the use of a contaminated well
  Observed that lack of cholera in areas with cleaner water supply
  When variables were removed, the Broad Street Well was the single commonality among all cholera deaths in outbreak

## Slide 5: TOXC102+ Chapter 1: Air Toxics Background Toxicology
Toxicology began as the study of poisons
BCE Poisons were an early political weapon
  Very important to know how much of a substance can kill a person and what antidotes blocked poisons
1927 J.W. Trevan developed first test for toxicity
  Studied chemical warfare chemicals (poison gas)
  Tested impacts of chemicals on animals by injecting varying amounts of poison
  Determined amount that killed half the population (Lethal Dose 50 / LD50), to compare toxic potency (toxicity) of different compounds

## Slide 6: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1930 Meuse River Valley, Belgium, December 1-5: Doctors received frantic phone calls of a mysterious illness
Hoarseness
Irritation of the larynx
Chest pain and coughing
Nausea, vomiting, and foaming at the mouth
Within 24 hours:
60 people and dozens of cattle were dead

## Slide 7: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1931 Medical / Scientific Investigation
What caused these deaths?
  Mustard gas attack?
  Sahara desert sands?
  Something else?
Determined thermal inversion and topography trapped air pollution at ground level
Report given to Belgium Royal Academy of Medicine and medical journal The Lancet
  First scientific proof that atmospheric pollution (fluorine) caused death and disease
  “The same factors were likely to occur elsewhere”

## Slide 8: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1948 Donora, PA
20 miles south of Pittsburgh on Monongahela River
  American Smelting & Refining Company (ASARCO) Zinc Works and American Steel & Wire Company
October 27-28:
  Smog starts to build
  Respiratory distress blamed on asthma
October 29:
  Annual Halloween parade
  Roads impossible to traverse due to thick smog
  Firefighters with air tanks and doctors go door to door, being led by people with flashlights

## Slide 9: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1948 Donora, PA
October 30:
2:00 AM: first death occurs
Doctors warn people with chronic illness to evacuate
People turning blue from lack of oxygen
Donora Dragons high school football game played in extremely poor visibility (relied on the running game)
11:30 PM: 17 citizens dead
October 31:
Meeting convened with plant operators and officials
Plant superintendent said shutdown already in process, started at 6 AM
Afternoon: Rain showers dissipate the smog

## Slide 10: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1948 Donora, PA
20 people dead
  Autopsies on 3 revealed severe lung damage
1,440 people affected by serious illness
4,470 people with mild to moderate symptoms

## Slide 11: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
Video: Beware the Wind

## Slide 12: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1948 U.S. Public Health Service (PHS) Investigates
November 2:
  Phone call to PHS Division of Industrial Hygiene requesting assistance
November 3:
  PHS arrives onsite, to begin smog investigation
  First large-scale epidemiological study of an environmental health disaster in the US
  Investigation grows to include 25 government personnel
  Biological study of community impacted
  Atmospheric study of air pollutants and meteorological conditions

## Slide 13: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1949 PHS Preliminary Report
Air pollution emitted by American Steel & Wire Company and American Smelting & Refining Company (ASARCO) Zinc Works
  Sulfur dioxide (SO2) only atmospheric pollutant measured in significant amounts after event, but no single substance was responsible for smog
  Emphasized that information on toxicological effects of mixed gases is meager and limited
  Coal-fired residential furnaces and river traffic also contributed to smog
Meteorological inversion
  Cold front caused stagnant air, trapping air pollution within the valley
Geography
  Horseshoe bend in river surrounded by 400 foot-hills trapped air pollution within the valley

## Slide 14: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1950 Damage Control
PHS did not publish final Donora report
ASARCO funded Havard School of Public Health to show that SO2 and sulfuric acid (H2SO4) did not contribute to Donora smog
1952 Creating a Toxicologist
Dr. Mary Amdur developed a method for spraying mists of SO2 and H2SO4
Investigated damage to guinea pigs
  Inhalation of SO2 / H2SO4 dramatic affected breathing, weight loss, and lung disease
Presented paper at American Association for the Advancement of Science

## Slide 15: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1953 Dr. Amdur investigates chronic toxicity
Existing tests for only acute toxicity
  If animal remained alive, dose was “safe”
1954 ASARCO Damage Control
Dr. Amdur physically threatened at conference while presenting paper
ASARCO threatened to pull funding
  Havard withdrew paper and cancelled project
1961 Studies on Donora Long-Term Effects
Cancer and cardiovascular disease deaths consistently higher in Donora
  70 actual deaths vs 39 expected deaths

## Slide 16: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
Dr. Mary Amdur: “Mother of Modern Toxicology”
Developed a physiological model for particulate interaction in the respiratory tract of mammals
Combined engineering and toxicology to create aerosols for inhalation studies
Served on advisory committees
    National Instituted of Health (NIH)
    Occupational Safety and Health Administration (OSHA)
    Environmental Protection Agency’s Clean Air Act Scientific Advisory Committee (CASAC)
Editor of Toxicology: The Basic Science of Poisons

## Slide 17: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
Expanding Toxicology in a Chemical World
Scientists have created over 100,000 compounds that do not occur in nature
  After World War II, development of new chemicals accelerated
  Vast majority of chemicals even today have no toxicity information
1962 Rachel Carson publishes Silent Spring
Hazards of the environmental harms of a man-made chemical DDT

## Slide 18: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1984 Methyl Isocyanate Release at Union Carbide in Bhopal, India
  Killed 2,500-10,000 people
  Injured / permanently disabled 200,000
  15,000-20,000 premature deaths over the next 20 years
  $5 million spent upgrading safety and control measures at sister plant in Institute, WV

## Slide 19: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1985 Aldicarb Oxime Release at Union Carbide in Institute, WV
  135 residents treated for eye, throat, and lung irritation
  Closed all highways in the area
  3,100 residents ordered to shelter-in-place
  8 months after Bhopal, India
  Company delayed activating emergency siren until after affects observed by residents

## Slide 20: TOXC102+ Chapter 1: Air Toxics Background History of Air Toxics
1985 National Academy of Science published the report “Known Chemicals; Known Risks”
  Americans potentially exposed to about 70,000 different chemicals
  84% of these chemicals had minimal or no toxicity data available
  14% had sufficient data for a partial hazardous health assessment
  2% had sufficient data to complete a hazardous health assessment