## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 2: Laws & Regulations

## Slide 2: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
§108&109: National Ambient Air Quality Standards (NAAQS)
Criteria Pollutants: Chemicals that cause or contribute to air pollution which may reasonably be anticipated to endanger public health or welfare
  Carbon Monoxide (CO) • Nitrogen Oxides (NOX)
  Ozone • Particulate Matter (PM)
  Sulfur Dioxide (SO2) • Lead (added by regulation in 1978)

## Slide 3: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
§112: National Emission Standards for Hazardous Air Pollutants (NESHAP)
Hazardous Air Pollutants (HAPs): Chemicals that cause, or contribute to, air pollution which may reasonably be anticipated to result in an increase in mortality or an increase in serious irreversible, or incapacitating reversible, illness
All HAPs are air toxics, but not all air toxics are HAPs
!

## Slide 4: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
Differences Between NAAQS and HAP:
Criteria Pollutants:
  Ambient air monitoring to determine public exposure
  State implementation plan (SIP) / federal implementation plan (FIP) to reduce air pollutant concentrations below “safe dose” (NAAQS)
HAP / Air Toxics:
  Regulation (standard) establishes “safe dose”
    Risk exposure assessment to establish acceptable dose
    Source-specific standards to establish allowable emissions
  Ambient air monitoring not required to demonstrate public exposure
  Not required to be part of a SIP

## Slide 5: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
1970 Clean Air Act NESHAP Program (40 CFR, Part 61)
Exposure-based standard for HAP control
EPA had to identify and list HAP
  Only identified carcinogenic HAP, as most research at the time focused on cancer, rather than other health effects from air toxics
EPA must establish emissions limit within 1 year of listing HAP
  Conduct risk analyses to determine what emissions limits would protect public health
  NESHAP would be established with an “ample margin of safety”
  Determine what controls were necessary to achieve emissions limits, considering costs and technical feasibility

## Slide 6: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
1970 Clean Air Act NESHAP Program
From 1970 to 1990, EPA listed 8 HAP and issued 22 standards in 40 CFR, Part 61
  Arsenic • Coke oven emissions
  Asbestos • Mercury
  Benzene • Radionuclides
  Beryllium • Vinyl chloride
EPA investigated 25 additional HAP, but no standards issued

## Slide 7: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
NESHAP General Regulatory Structure:
Applicability: Sources applicable to NESHAP
  NESHAP issued to all sources emitting HAP (e.g., Asbestos) or specific industries (e.g. Beryllium from rocket motors and everything else)
Definitions: Terms used in NESHAP
Standards: Emissions limits and work practices
Testing: Test methods and procedures
Monitoring: Operation and control equipment parameters
Recordkeeping: Maintenance of records required by standard
Reporting: Frequency and reporting required by standard

## Slide 8: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1970 Clean Air Act
NESHAP Delegation of Authority:
Local, state, and tribal (LST) air agencies can request delegation from U.S. EPA to implement and enforce NESHAP
  Delegation is a political decision for EPA Region and LST air agency
Two options for delegation
  LST air agency issues State Implementation Plan (SIP) with NESHAP requirements or reference to NESHAP
  Memorandum between LST air agency and EPA Region allowing issuance of a permit containing NESHAP requirements

## Slide 9: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1986 Emergency Planning and Community Right-to-Know Act
1986 Emergency Planning and Community Right-to-Know Act (EPCRA)
Response to Bhopal, India & Institute, WV chemical releases
Help communities plan for chemical emergencies
  Local emergency planning committees (LEPC) at city/county level
  State emergency response commissions (SERC)
Industry must report to local, state, tribal, and federal agencies certain chemicals stored onsite and certain chemical releases
  Annual reports for chemical storage and releases
  Immediate report for accidental chemical release

## Slide 10: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1986 Emergency Planning and Community Right-to-Know Act
§304: Accidental Release Reporting
Facilities must immediately report accidental chemical releases
  EHS Reporting Quantity (RQ) Threshold: 1-10,000 pounds
  Hazardous Substance from Comprehensive Environmental Response, Compensation and Liability Act (CERCLA): 1-5,000 lbs.
Separate report from air pollutant malfunctions (to you)
May have to report accident to U.S. Chemical Safety and Hazard Investigation Board (CSB)
  Must report if release results in fatality, serious injury, and/or substantial property damage

## Slide 11: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1986 Emergency Planning and Community Right-to-Know Act
Releases of air toxics are regulated by multiple agencies
Develop Standards
Issue Permits
Conduct Inspections
Monitor Air Quality
Review Release Reports
Emergency Response
Emergency Planning
All Releases Emergency Releases

## Slide 12: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1986 Emergency Planning and Community Right-to-Know Act
§312: Annual Hazardous Chemical Inventory
Facilities must submit an Annual Hazardous Chemical Inventory (Tier II Report) of all EHS and hazardous substances
  Submitted to Fire Department, LEPC, and SERC on March 1 annually
  Includes chemical storage amounts, chemical hazards, emergency contacts, and map of the facility indicating chemical storage locations

## Slide 13: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1986 Emergency Planning and Community Right-to-Know Act
§313: Annual Toxic Release Inventory
Facilities must submit annual Toxic Release Inventory (TRI), a report of toxic chemical releases to the environment
  Air, land, and water releases, including shipments for recycling, energy recovery, on-site and off-site treatment, storage, and disposal
  Applicable to facilities in specific industrial sectors (by Standard Industrial Classification – SIC) with 10 or more full time employees and using or processing a listed toxic chemical
  Submitted annually on July 1 to U.S. EPA and state environmental protection agencies
  Information is publicly available: enviro.epa.gov/envirofacts/tri/search

## Slide 14: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1989 EPA Risk Policy
1987 Natural Resources Defense Council (NRDC) vs. EPA
EPA established a NESHAP for vinyl chloride based on available technology above the safe level (of zero)
Federal court ruling:
  EPA cannot consider costs for establishing safe levels of exposure (1st Step), but that safe did not mean “risk free” (i.e., zero risk)
  EPA can consider costs and technological feasibility when determining ample margin of safety (2nd Step)

## Slide 15: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1989 EPA Risk Policy
1989 EPA Revised NESHAP Risk Policy
Safe emissions limits: Maximum exposure to a HAP would not cause maximum individual risk (MIR) greater than 1 in 10,000
  Estimate risk to a person living near a source of HAP exposed to maximum annual pollutant concentration over their lifetime (70 years)
Ample margin of safety: Individual lifetime risk (ILR) should not be greater than 1 in 1,000,000, including costs, economic impacts, and technical feasibility
  Estimated risk to a person living near a source of HAP exposed to average annual pollutant concentration over their lifetime (70 years)
  Protect the greatest number of persons

## Slide 16: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1989 EPA Risk Policy
1×106 MIR 1×104.
< Decreasing Risk Increasing Risk >
Risk is acceptable with ample margin
No further action needed
Risk may be acceptable
Look at health impacts
Consider costs and technical feasibility for determining if emissions reductions are necessary
Risk is unacceptable
Only consider health impacts
Identify actions to reduce risks

## Slide 17: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1989 EPA Risk Policy
Stroke
Car Accident
Home Accident
Fire
Poisoning
Lightning
NESHAP Risk
EPA Risk Policy In Perspective
(Lifetime Risk of Death)
1:1,000,000 1:100,000 1:10,000 1:1,000 1:100 1:10

## Slide 18: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
1990 Amendments to the Clean Air Act
Due to EPA inaction, Congress reinvents air toxics standards
  §112: Hazardous Air Pollutants (HAP)
  (b) List of Pollutants – Regulated air toxics
  (c) List of Source Categories – Sources of air toxics to be regulated
  (d) Emissions Standards – How EPA develops standards
  (f) Standard to Protect Health and Environment – Residual risk
  (j) Equivalent Emission Limitation by Permit – MACT hammer
  (r) Prevention of Accidental Releases – Risk management
1970 NESHAP Program discontinued but standards retained in 40 CFR, Part 71
!

## Slide 19: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(b): List of Pollutants
Congress identified 189 HAP in Clean Air Act
  Compounds with any significant and widespread adverse environmental effect or carcinogenic effect
    Reasonably anticipated to impact wildlife, aquatic life, or other natural resources
    Adverse impacts to populations of endangered or threatened species
    Significant degradation of environmental quality over broad areas
  List included 8 HAP already identified in 1970 NESHAP program
EPA Administrator can add and remove HAP from list
  Methyl Ethyl Ketone (MEK) removed in 2005
  1-Bromopropane added in 2022

## Slide 20: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
Curious Case of Lead:
1973: EPA regulated lead concentration in gasoline
1975: Natural Resources Defense Council (NRDC) successfully sued EPA requiring a lead NAAQS
1978: EPA issues final lead NAAQS of 1.5 micrograms per cubic meter (µg/m3) as a calendar month average
1990: Lead compounds listed as a HAP in Clean Air Act
  Title V Applicability for HAP (lead compounds): 10 tons per year (tpy)
  Title V Applicability for criteria pollutant (lead): 100 tpy
2008: Lead NAAQS revised to 0.15 µg/m3 per 3-month period

## Slide 21: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(c): List of Source Categories
EPA published initial list of source categories on July 16, 1992
Major Sources: 166 sources with a potential-to-emit of:
  10 tons per year (tpy) or more of any individual HAP or
  25 tpy or more of all HAPs in total
Area Sources: 8 smaller, non-major sources with a potential-to-emit:
  Less than 10 tpy for any individual HAP and
  Less than 25 tpy for all HAPs in total

## Slide 22: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(c)(6): Seven Specific HAP
Congress identified 7 HAP and required EPA to identify sources to reduce HAP emissions by 90% due to persistence and tendency to bioaccumulate (bioaggregation)
Alkylated lead compounds • Mercury
Polycyclic organic matter (POM) • Hexachlorobenzene
Polychlorinated Biphenyls (PCB)
2,3,7,8 tetrachlorodibenzo-p-dioxin (Dioxins)
2,3,7,8 tetrachlorodibenzofurans (Furans)

## Slide 23: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
Potential to Emit
Maximum capacity of a source to emit HAP
Assumes full production and operation 24 hours per day, 365 days per year
Control devices and operating restrictions NOT included, unless in included in an applicable permit or regulation
Ensures similar sources are treated equally

## Slide 24: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d): Emissions Standards
Emissions standards shall require the maximum degree of reduction in HAP emissions determined to be achievable
  Maximum Achievable Control Technology (MACT)
  Consider cost of achieving reduction and non-air quality health / environmental impacts
  EPA can consider health thresholds when establishing emissions standards (using data from 1970 NESHAP program)
For area sources, EPA may define Generally Available Control Technologies (GACT)
1970 NESHAP Program: Exposure-based Standard
1990 NESHAP Program: Technology-based Standard
!

## Slide 25: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
Establishing MACT Standards for §112(d)
  Establish “MACT floor” – the minimum degree of emissions reductions that sources must achieve without consideration of cost
2
  Evaluate more stringent “beyond-the-floor" controls, considering costs, non-air quality health / environmental impacts, and energy requirements
3
  Establish the MACT standard at either the “MACT floor” or “beyond-the-floor”
1

## Slide 26: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d): Establishing MACT Floor
Existing Sources:
  If ≥30 sources, the average emissions limitation achieved by the best performing 12% of existing sources; or
  If <30 sources, the average emissions limitation achieved by the best performing 5 existing sources.
New Sources:
  The emissions control that is achieved in practice by the best controlled similar sources (i.e., best performing 1 existing source).

## Slide 27: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d): Beyond the MACT Floor
Identify all commercially available and demonstrated control technologies that are reasonably applicable to each source.
Create a list of control technologies that are reasonably applicable to each source.
Evaluate each control technology to consider:
  Costs;
  Non-air quality health / environmental impacts; and
  Energy requirements associated with using each control technology.

## Slide 28: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d): GACT
GACT only applies to some area sources
  EPA has discretion to identify control technologies or management practices used by similar sources
  EPA can include the cost of achieving the emission reductions
Area sources can be subject to MACT
  Required to achieve 75% reduction of 30 urban HAP in §112(k)
  Required to achieve 90% reduction from 7 HAP in §112(c)(6)
  EPA issues “Finding of Threat of Adverse Effects” to require MACT at area sources

## Slide 29: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d)(6): Review and Revision
Technology Review: Each standard will be reviewed and revised as necessary no more often than every 8 years to incorporate new developments in practices, processes, and control technologies
§112(f): Standard to Protect Health and Environment
Residual Risk Review: Each standard will be reviewed and revised as necessary no more often than every 8 years to provide an ample margin of safety to protect public health

## Slide 30: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d)(6)/(f): Residual Risk & Technology Review
EPA combines Risk and Technology Review (RTR) on an 8-year cycle for MACT
RTR includes both human health (toxicity) and ecological (environment) risk assessments using exposure-based standards (1970 NESHAP)
  Non-carcinogen: Review target organ hazard information
  Carcinogen: Reduce risk to 1989 EPA Risk Policy standards (range of 1:10,000 to 1:1,000,000)
RTR not required for GACT

## Slide 31: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(d)(6)/(f): Residual Risk & Technology Review
RTR determines if additional requirements are necessary to:
Reduce residual risks (protect public health with ample margin of safety);
Ensure that emissions do not result in adverse environmental effects, (considering cost, energy, safety, and other relevant factors); and
Incorporate new practices, processes, and/or control technologies

## Slide 32: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(j): Equivalent Emission Limitation by Permit
MACT Hammer: If EPA fails to promulgate a MACT standard by November 15, 2000, LST air agency shall issue a permit with emissions limits equivalent to what MACT was supposed to be
Limits included in Title V (Part 70) Federal Operating Permit
  Part 1 permit application (notification) to EPA and LST air agency by May 15, 2002
  Part 2 (updated Title V) permit application to LST air agency within 24 months of Part 1 deadline (revised to 12 months after lawsuit)

## Slide 33: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(j): Equivalent Emission Limitation by Permit
EPA estimated over 80,000 MACT sources impacted
EPA issued all MACT by MACT Hammer Part 2 deadline
  Numerous facilities submitted Part 1 applications
  No known Part 2 application due
  3 years was enough “breathing room” for EPA to issue all initial MACT standards
Resurfaced in 2010 to address court vacatur of an entire MACT standard (i.e., no promulgated standard)
  EPA issued revised MACT standards before MACT hammer deadline

## Slide 34: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(l) Delegation:
LST air agencies can request implementation and enforcement of NESHAP (both 40 CFR Part 61 and 63)
Regulatory Delegation: LST air agency administrative code incorporates NESHAP, making NESHAP a state requirement
  Administrative code can incorporate by reference or has to contain word for word the NESHAP
Permit Delegation: LST air agency includes requirements for NESHAP into issued permit
  Title V / Part 70 Federal Operating Permits must contain all applicable requirements

## Slide 35: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(r): Prevention of Accidental Releases
Risk Management: Program to prevent the accidental release of air toxics and minimize the consequences of a release
Separate list of air toxics created by EPA
  Divided into two categories: flammability and health risks
  258 compounds with many HAP included
Created Chemical Safety & Hazard Investigation Board (CSB)
  Investigates accidental releases that caused fatality, serious injury, or substantial property damage
  Separate release reporting requirement from EPA and LST air agencies

## Slide 36: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(r): Prevention of Accidental Releases
Risk Management: Program to prevent the accidental release of air toxics and minimize the consequences of a release
Separate list of air toxics created by EPA
  63 substances listed for flammability
  77 substances listed for toxicity (many HAP included)
Created Chemical Safety & Hazard Investigation Board (CSB)
  Investigates accidental releases that caused fatality, serious injury, or substantial property damage
  Separate release reporting requirement from EPA and LST air agencies

## Slide 37: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
§112(r): Prevention of Accidental Releases
Risk Management: Program to prevent the accidental release of air toxics and minimize the consequences of a release
Separate list of air toxics created by EPA
  63 substances listed for flammability
  77 substances listed for toxicity (many HAP included)
Created Chemical Safety & Hazard Investigation Board (CSB)
  Investigates accidental releases that caused fatality, serious injury, or substantial property damage
  Separate release reporting requirement from EPA and LST air agencies

## Slide 38: TOXC102+ Chapter 2: Air Toxics Laws & Regulations 1990 Clean Air Act
Multiple Programs for Prevention of Accidental Releases
Onsite: Occupational Safety and Health Administration (OSHA) Process Safety Management (PSM) Program
Offsite: Environmental Protection Agency (EPA) Risk Management Plan (RMP) Program

## Slide 39: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Local / State / Tribal Air Toxics Programs
Other Air Toxics Management Programs:
LST air agencies can develop their own air toxics management program
Identification of regulated air toxics
  Usually a more expansive list that includes all HAP
Determine impacts
  Conduct air dispersion modeling to determine highest ambient air concentration beyond fenceline
Establish emissions limits
  Acceptable concentration based on toxicological exposure data

## Slide 40: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Local / State / Tribal Air Toxics Programs
Air Toxic | HAP? | Ohio EPA† | Georgia EPD‡ | WA Ecology
Ammonia | No | 404 µg/m3 | 1.00×102 µg/m3 | 5.0×102 µg/m3
Benzene | Yes | 0.47 µg/m3 | 0.13 µg/m3 | 0.13 µg/m3
Carbon Monoxide | No | N/A | N/A | 2.3×104 µg/m3
Hydrogen Sulfide | No | 33 µg/m3 | 2.0 µg/m3 | 2.0 µg/m3
Methyl Ethyl Ketone (MEK) | No | N/A | 5.0×103 µg/m3 | 5.0×103 µg/m3
2,3,7,8-Tetra-chlorodibenzo-p-dioxin | Yes | Unknown | 1.50×10-3 µg/m3 | 2.6×10-8 µg/m3
† From American Conference of Governmental Industrial Hygienists (ACGIH) ‡ From EPA, National Institute of Occupational Safety and Health (NIOSH), and OSHA |  |  |  | 

## Slide 41: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Other Air Toxic Requirements
Toxic Torts: Judicial claim of physical or psychological harm caused by exposure
Difficult to identify & quantify source(s) causing plaintiff’s harm
  Air toxics from one or many sources
  Drinking water polluted with numerous contaminants from multiple sources
Uses complex litigation procedures
  Plaintiff may have to demonstrate evidence of exposure & causation
Reliance on scientific concepts to resolve causation issues
  Need for experts in meteorology, epidemiology, and toxicology

## Slide 42: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Plaintiff: Individual or group that suffered harm
Must prove a causal link between exposure and harm
  Serious injury with unverifiable level of exposure?
  Known exposure, but injury has not yet manifested?
  Did the exposure cause the harm?
  Was lawsuit brought within statute of limitations between date of exposure and date injury was caused by Defendant?
Defendant: Group that allegedly caused the harm
Argue against causation (did not cause exposure and/or harm)
  Who created the exposure?
  Are there multiple sources for exposure (multiple liabilities)?

## Slide 43: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Causation Components
Exposure & Dose:
  Prove that the defendant is the source of the exposure
General Causation:
  Show that exposure to a substance is capable of causing the observed condition
Specific Causation:
  Demonstrate the magnitude and duration of exposure
  Present the actual dose received by plaintiff

## Slide 44: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Special Causation Challenges
Long latency period from exposure to injury manifesting (disease or death)
Problems with exposure
  Plaintiff’s injury can be caused by other exposures from chemicals not used by defendant
Little hard data exists for linking toxic exposure to injury
  Animal studies have only limited use for causation
    Animal studies may be used as “speculative evidence” (e.g., saccharine, BPA) to remove products for safety concerns but not legal “preponderance of evidence”
  Court requires epidemiological studies or in vitro studies as evidence

## Slide 45: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Expert Opinions
Trial judge as “gatekeeper,” must assess reliability of expert testimony to determine admissibility
  Daubert v. Merrel Dow Pharmaceuticals, decided by U.S. Supreme Court in 1993
Factors considered:
  Theory or technique can be / has been tested
  Subjected to peer review and publication
  Known or potential error rate
  Existing and maintenance of standards
  Generally accepted in relevant scientific community

## Slide 46: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Asbestos
Asbestos is a naturally occurring silicate mineral widely used as a flame-retardant and insulation
Examples of products containing asbestos:
  Roofing shingles and tar,
  Ceiling and floor tiles,
  Paper and cement products, and
  Friction products such as automobile clutch, brake and transmission parts.
Asbestos fibers break off, forming smaller fibers
  Microscopic fibers cause inflammation and scarring of lung tissue

## Slide 47: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Asbestos
Asbestos exposure causes asbestosis (lung scarring), mesothelioma (cancer in lung lining), and other lung cancers
  Latency period between exposure and asbestos-type disease can be 10-40 years
  In many “smoking lung cancer” cases where Plaintiff did not have asbestosis, jury found cigarettes were the cause
  Between 1940-1979, >27.5 million Americans worked in occupations where substantial asbestos exposures common (shipyards, construction, industry)

## Slide 48: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Asbestos
Johns-Manville filed a petition in August 1982 for bankruptcy reorganization
  Not insolvent, but sought to limit future liabilities from asbestos litigation
U.S. Bankruptcy Court for Southern District of New York approved Bankruptcy Reorganization in December 1986
  Established Manville Trust – an independent organization for distributing funds for existing and future asbestos claims
  Trustees appointed by the Court
  Model for all subsequent companies filing bankruptcy for asbestos

## Slide 49: TOXC102+ Chapter 2: Air Toxics Laws & Regulations Toxics Torts
Asbestos
Asbestos litigation is the longest-running mass tort litigation in U.S. history
  >8,000 defendants
  >700,000 plaintiffs (as of 2017)
  60,000 jobs lost and $1.4-3.0 billion in bankruptcies
  90% of American industries are listed as defendants in asbestos suits
$36.8 billion in assets in asbestos trusts in 2011

## Slide 50: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
Once In/Always In:
In 1995, EPA released a memorandum stating that once a MACT compliance deadline had passed, a facility could no longer reclassify as an area source (once in, always in)
In 2018, EPA updated the memorandum to allow major facilities to reclassify as an area source
In 2024, EPA modified the MACT regulations to allow some major facilities to reclassify as an area source
  Applies to all sources that reclassify after September 10, 2024

## Slide 51: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
§112(c)(6): Seven Specific HAP
Congress identified 7 HAP and required EPA to identify sources to reduce HAP emissions by 90% due to persistence and tendency to bioaccumulate (bioaggregation)
Alkylated lead compounds • Mercury
Polycyclic organic matter (POM) • Hexachlorobenzene
Polychlorinated Biphenyls (PCB)
2,3,7,8 tetrachlorodibenzo-p-dioxin (Dioxins)
2,3,7,8 tetrachlorodibenzofurans (Furans)

## Slide 52: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
Reclassification
EPA determined that sources emitting any of the seven HAP in §112(c)(6) cannot reclassify, as Congress required EPA to reduce 90% of the HAP emissions from these sources
All other sources can reclassify after providing notification 15 calendar days prior to reclassifying as an area source

## Slide 53: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
Subparts Exempted from Reclassification (1 of 3)
F: Hazardous Organic NESHAP (Synthetic Organic Chemical Manufacturing Industry)
G: Hazardous Organic NESHAP (Synthetic Organic Chemical Manufacturing Industry)
H: Hazardous Organic NESHAP (Synthetic Organic Chemical Manufacturing Industry)
I: Hazardous Organic NESHAP (Synthetic Organic Chemical Manufacturing Industry)
L: Coke Ovens: Charging, Top Side, and Door Leaks
R: Gasoline Distribution (major sources)
X: Secondary Lead Smelters
CC: Petroleum Refineries (CC)
GG: Aerospace
II: Shipbuilding and Ship Repair Surface Coating
JJ: Wood Furniture Surface Coating

## Slide 54: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
Subparts Exempted from Reclassification (2 of 3)
KK: Printing and Publishing Surface Coating
LL: Primary Aluminum
MM: Combustion Sources at Kraft, Soda, and Sulfite Pulp & Paper Mills (Pulp and Paper MACT II)
EEE: Hazardous Waste Combustors
HHH: Natural Gas Transmission and Storage
JJJ: Polymers & Resins IV
LLL: Portland Cement Manufacturing
RRR: Secondary Aluminum
UUU: Petroleum Refineries (UUU)
FFFF: Misc. Organic Chemical Production and Processes (MON)
JJJJ: Paper and Other Web Surface Coating

## Slide 55: TOXC102+ Chapter 2: Air Toxics Laws & Regulations MACT: Reclassification of Major Sources to Area Sources
Subparts Exempted from Reclassification (3 of 3)
MMMM: Miscellaneous Metal Parts and Products Surface Coating
PPPP: Plastic Parts Surface Coating
ZZZZ: Reciprocating Internal Combustion Engines (RICE) includes area sources
CCCCC: Coke Ovens: Pushing, Quenching, and Battery Stacks
DDDDD: Industrial, Commercial and Institutional Boilers and Process Heaters (major sources)
FFFFF: Integrated Iron and Steel
IIIII: Mercury Cell Chlor-Alkali Plants
LLLLL: Asphalt Processing and Asphalt Roofing Manufacturing
YYYYY: Electric Arc Furnace Steelmaking Facilities (area sources)
JJJJJJ: Industrial, Commercial and Institutional Boilers (area sources)
EEEEEEE: Gold Mine Ore Processing and Production (area sources)