## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 3: Types of Air Toxics

## Slide 2: TOXC102+ Chapter 3: Types of Air Toxics Categories of Air Toxics
Organic compounds
  Chemicals that contain carbon, (except carbonic acid and ammonium carbonate)
  Includes volatile organic compounds (VOC) and semi-VOC (SVOC)
Inorganic compounds
  Chemicals that do not contain carbon
Organometallic compounds
  Chemicals that contain metals and organic compounds
Radionuclides
  Chemicals that are radioactive (can be organic or inorganic)

## Slide 3: TOXC102+ Chapter 3: Types of Air Toxics Categories of Air Toxics
Organic Compounds VOC vs SVOC
Volatile: relative evaporation rate (based on vapor pressure)
  VOC have higher vapor pressure and evaporate quickly at standard conditions
    VOC are used in paints, pharmaceuticals, and solvents
    VOC are usually aromatic (release a smell)
  SVOC have a lower vapor pressure and tend to remain as a solid or liquid at standard conditions
    SVOC are used in pesticides, plastics, and furniture
    SVOC are not aromatic (do not smell)

## Slide 4: TOXC102+ Chapter 3: Types of Air Toxics Categories of Air Toxics
Radionuclides
Any compound that spontaneously undergoes radioactive decay
  Uranium, radium, and radon are regulated in 40 CFR, Part 61 NESHAP
Emit only ionizing radiation
  Alpha Particle – two protons, two neutrons (He with no electrons)
    Stopped 1.2 inches of air or by a sheet of paper
  Beta Particle – one electron
    Stopped 10 feet of air or by a roll of aluminum foil
  Gamma Ray – photon (almost pure energy)
    Stopped by 1.3 feet of lead

## Slide 5: TOXC102+ Chapter 3: Types of Air Toxics Air Toxics Identification
Single Compound Identification
Chemical Name
  Standards use common name (e.g., xylene) rather than International Union of Pure and Applied Chemistry name (e.g., dimethylbenzene)
Chemical Abstracts Service (CAS) registry – a unique number assigned to every chemical substance in scientific literature
  As of the December 2024, 204 million unique organic and inorganic substances included in CAS registry
  CAS does not apply to groups of chemicals, as groupings that include multiple chemicals cannot be listed by a single CAS

## Slide 6: TOXC102+ Chapter 3: Types of Air Toxics Air Toxics Identification
Multiple Compound Identification
Common Hazard Identifier
  Common chemical that makes the compound an air toxic (e.g., arsenic compounds)
Process Identifier
  Process that generates the air toxic (e.g., coke oven emissions)

## Slide 7: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Isomers
Same chemical formula but different structure
  Can have different chemical / physical properties
Mixtures
Material made up of two or more different substances
  Mixtures with multiple air toxics can have multiple different impacts
  Easier to establish one “category” for mixture
Grouping
Different chemicals that share a similar feature

## Slide 8: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Isomers: Cresols / Cresylic Acid
Three different compounds with the same chemical formula C7H8O
  Listed as isomers and mixtures of cresol

## Slide 9: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Isomers: Xylenes
Three different compounds with same chemical formula (CH3)2C6H4
Commercial xylene usually contains 40-65% m-xylene, ~20% o-xylene, and ~20% p-xylene

## Slide 10: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Mixture: Coke Oven Emissions
Different organic compounds emitted from coke ovens
  Coal Tar (Benzene, Toluene, Xylene)
  Coal Tar Pitch
  VOC
  Creosote
  Polycyclic Organic Matter
  Metals

## Slide 11: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Mixture: Diesel Particulate Matter
Different organic compounds emitted from diesel combustion
  Acetaldehyde
  Benzene
  Bis(2-ethylhexyl)phthalate
  Furans and dioxins
  Formaldehyde
  Metals
  Polycyclic Organic Matter
  Styrene

## Slide 12: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Cyanide Compounds
Any compound containing cyanide
X–CN, where:
X = Hydrogen or any other group where formal dissociation occurs
  Hydrogen Cyanide – HCN
  Potassium Cyanide – KCN
  Zinc Cyanide – Zn(CN)2

## Slide 13: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Dioxins and Furans
Any organic compounds containing a dibenzo-p-dioxin nucleus or a dibenzofuran nucleus
Not intentionally produced
  No known technical use
  Unwanted byproduct in manufacture of chlorinated materials or other organic materials
  Emitted from fossil-fuel and waste combustion

## Slide 14: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Fine Mineral Fibers
Fibers with an average diameter of ≤1 micrometer
  Glasswool – glass fibers
  Rockwool – stone fibers
  Slagwool – slag fibers
  Glass filaments
  Refractory ceramic fibers
1/256 inch ½ inch
Human Hair
2.5µm 10 µm 30 µm 50 µm 100 µm 12700 µm
> <1 µm

## Slide 15: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Glycol Ethers
Mono- & di-ethers of ethylene, diethylene, and triethylene glycols
  Excludes polymers (endlessly repeating chains) as they are not volatile
Glycol Ether Chemical Formula R–(OCH2CH2)n–OR' where:
  n = 1, 2, or 3 (ethylene glycols) R = alkyl (alkane missing H1) or aryl (benzene missing H1) groups R' = R, H, or any R-(OCH2CH)n-OH (ethylene glycol) groups
Ethylene Glycol [OH–CH2–CH2–OH] + Ether [R–O–R’]
  2-methoxyethanol (methyl cellosolve) OH–CH2–CH2–O–CH3

## Slide 16: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Metal Compounds
Elemental metals react with other chemicals to form metal compounds
Metals form salts (beryllium nitrate) or oxides (cadmium oxide)
  Antimony • Arsenic
  Beryllium • Cadmium
  Chromium (trivalent & hexavalent) • Cobalt
  Lead (except elemental lead) • Manganese
  Mercury • Nickel
  Selenium

## Slide 17: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Grouping: Polycyclic Organic Matter (POM)
Organic compounds with more than one benzene ring and a boiling point ≥100º C
  Polycyclic aromatic hydrocarbons (PAHs)
  Chrysene
  Benzo(a)pyrene
  Naphthalene (also listed separately as a HAP)

## Slide 18: TOXC102+ Chapter 3: Types of Air Toxics Multiple Compounds of Air Toxics
Program Variations in Air Toxics
Chemicals are not always grouped or defined in the same manner, even within the same agency
  Glycol ethers defined differently in EPCRA and Clean Air Act (HAP)
  Differences among chemical listed are based mostly on legal and regulatory considerations, not necessarily on toxicological properties
Toxicity data may not be available all grouped chemicals
  Compounds that are not typically encountered may not have enough toxicological information to establish acceptable thresholds

## Slide 19: TOXC102+ Chapter 3: Types of Air Toxics Air Toxic Identification
Chemical Abstract Services (CAS) Registry Number
Unique number assigned to every chemical substance in scientific literature
  CAS does not apply to groups of chemicals (i.e., cyanide compounds), which include multiple chemicals and no single CAS
  As of February 2023, >200 million unique organic and inorganic substances in CAS Registry

## Slide 20: TOXC102+ Chapter 3: Types of Air Toxics Special Air Toxics
30 Urban HAP §112(k) |  | 
Acetaldehyde | Dioxin | Mercury compounds
Acrolein | Propylene dichloride | Methylene chloride (dichloromethane)
Acrylonitrile | 1,3-dichloropropene | Nickel compounds
Arsenic compounds | Ethylene dichloride (1,2-dichloroethane) | Polychlorinated biphenyls (PCBs)
Benzene | Ethylene oxide | Polycyclic organic matter (POM)
Beryllium compounds | Formaldehyde | Quinoline
1,3-butadiene | Hexachlorobenzene | 1,1,2,2-tetrachloroethane
Cadmium compounds | Hydrazine | Tetrachloroethylene (perchloroethylene)
Chloroform | Lead compounds | Trichloroethylene
Chromium compounds | Manganese compounds | Vinyl chloride

## Slide 21: TOXC102+ Chapter 3: Types of Air Toxics Special Air Toxics
§112(r): List of Regulated Substances
77 toxic chemicals
  Ammonia, chlorine, fluorine, formaldehyde, and hydrochloric, hydrofluoric, nitric, and sulfuric acids, etc.
63 flammable gases and liquids
  Acetylene, ethane, methane, butane, ethylene, hydrogen, propane, vinyl chloride, formic acid, etc.

## Slide 22: TOXC102+ Chapter 3: Types of Air Toxics Air Toxics
Air Toxics Listings
EPA List of HAPs
  30 Urban HAPs from §112(k)
  7 Persistent Bioaccumulative Toxic (PBT) HAPs from §112(c)(6)
EPA List of 112(r) Regulated Substances
EPCRA Toxic Release Inventory (TRI)
EPA List of Lists: CERCLA, EPCRA, and 112(r)
Local / State / Tribal Air Regulations