## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 6: Toxicity Assessment

## Slide 2: TOXC102+ Chapter 6: Toxicity Assessment EPA Risk Assessments
EPA Risk Assessment Framework
Planning and Scoping
Toxicity Assessment
Risk Characterization
Exposure Assessment
Quantitative and Qualitative Expressions of Risk/Uncertainty
POPULATION CHARACTERISTICS
Measures of Exposure
CHEMICAL
CONCENTRATIONS
Air, Soil, Water, Food
(monitor/model)
Dose/ Response Assessment
Y
X
Chemical
Release
SOURCES
FATE AND TRANSPORT ANALYSIS
SOURCE IDENTIFICATION
EXPOSURE information DOSE/RESPONSE information
Hazard Identification

## Slide 3: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Toxicity Assessment:
Hazard Identification: Determine whether exposure to a chemical can cause adverse health effect
  Review of strength of evidence of causation & circumstances that cause impacts
  Very often little new toxicological evaluation of primary data is required
Dose-Response Assessment: Establish quantitative relationship between the dose & the incidence of adverse health effects to the exposed populace
  Must understand how the dose-response data were analyzed & produced (especially for uncertainties & extrapolations)

## Slide 4: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Hazard Identification
Review & Analyze Toxicity Data: Determine if exposure to a chemical can cause particular health effects
Weigh Evidence: Assess the strength of the evidence that the chemical causes various toxic effects

## Slide 5: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Biological Effects,,,,,,,,,
Lethality (LD50, Lethal Concentration50)
Impairment of normal biological function (e.g., liver damage)
Inheritable genetic change
Increases/decreases in species population size or range
Health/productivity of ecosystems, etc.
Non-Biological Effects,,,,
Reduced visibility from airborne particulates (AQRV)
Damage to historic structures by air pollutants (Acid Rain)
Climate change from global warming

## Slide 6: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Non-Cancer Effects,,,,,,,
Multiple Adverse Endpoints
Reproductive, developmental, neurological disorders
Immunologic effects
Acute effects (edema, nervous system impacts)
Various other systemic effects (liver, kidney, lung damage)
Cancer Effects,,,,,,,,
Uncontrolled Growth of Cells
Mutations
DNA Damage

## Slide 7: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Step 1: Hazard Identification
Gather data on adverse biologic effects from studies
Epidemiological Studies: study distribution of disease in a specific population of humans
Animal Studies: Study impacts on animals (rats, mice, rabbits, guinea pigs, hamsters, dogs, or monkeys)
In-vitro Assays (Test Tube Studies): Study mutations in genetic material after cell division

## Slide 8: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Epidemiological Studies
Controlled exposure studies (usually occupational)
  Exposure concentrations (usually acute) & durations are known
Accidental exposure studies (Bhopal, India)
  Exposure concentrations usually high and chronic
Advantages:
  Animal to human extrapolation not necessary
  Real exposure concentrations
Disadvantages:
  No control over exposure amount, exposure to other toxins, or lifestyle differences; lengthy latency periods

## Slide 9: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Animal Studies
Acute: Tests short in duration, but high in concentration
  Study effects after exposure for less than 14 days
  Commonly use Lethal Dose 50 (LD50)
Sub-chronic: Tests in-between acute and chronic
  Exposure from about 7 days up to 10% of animal’s lifetime
  Commonly use Lowest Observed Adverse Effect Level (LOAEL), No Observed Adverse Effect Level (NOAEL), or other “critical factors”
Chronic: Tests long in duration, but low in concentration
  Study effects after exposure over at least 10% of the animal’s lifetime
  Commonly use LOAEL, NOAEL, or other “critical factors”

## Slide 10: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Animal Studies: Cancer Rodent Study
Two species (rats and mice) with both sexes & >50 animals per group
Exposed from ~6 weeks through full lifespan (~24 months)
  Maximum Tolerated Dose (MTD), MTD fractions, and control (no dose)
  Route of exposure similar to human exposure
Observe and report on outcomes (animals are sacrificed)

## Slide 11: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Weight of Evidence (WOE) Scheme†
Carcinogenic to Humans
Likely to be Carcinogenic to Humans
Suggestive Evidence of Carcinogenic Potential
Inadequate Information to Assess Carcinogenic Potential
Not Likely to be Carcinogenic to Humans
  † From EPA’s 2005 Guidelines for Carcinogen Risk Assessment

## Slide 12: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Step 2: Dose-Response Assessment
How much dose gives how much response?
How potent is the chemical?

## Slide 13: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Non-Cancer Effects,,,,,,,
Threshold: Body breaks down chemicals to less toxic substances
Reported in Reference Values:
Inhalation: Reference Concentration (Rfc)
Oral: Reference Dose (RfD)
Cancer Effects,,,,,,,,
Non-threshold: No exposure is without risk
Slope Factors:
Inhalation Unit Risk
Oral Potency Factor

## Slide 14: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment
Exposure: Concentration when it enters the body (inhalation, ingestion, dermal absorption)
Dose: Amount that actually enters the body
  Derived from exposure concentration, dose, and dosimetry (how the body handles a chemical once its inhaled)
Adjustments for “human equivalent concentration” (HEC)
  Duration Adjustment: Animal inhalation exposures about 6 hours/day, 5 days/week must be adjusted to continuous inhalation exposure
  Interspecies Adjustments: Compensate for differences between humans & lab animals

## Slide 15: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Interspecies Adjustments
Interspecies adjustments must account for:
Differences in exposure route (orally or inhaled)
Differences in size & life spans
Differences in pharmacokinetics (what the body does with the chemical once its inside the body):
  Metabolism (conversion to a less toxic substance)
  Excretion & distribution to storage sites (fat, bones etc.)
  Absorption rate (mainly in lungs & small intestines)

## Slide 16: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Pesticide | Rabbit | Monkey | Man
DDT | 46.30% | 1.50% | 10.40%
Lindane | 51.20% | 16.00% | 9.30%
Parathion | 97.50% | 30.30% | 9.70%
Examples of Interspecies Adjustments

## Slide 17: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment
Derive an Inhalation Unit Risk (IUR) & RfC from an Animal Study
Point of Departure (POD)
Estimated dose near the low end of the observed range without extrapolation to lower doses

## Slide 18: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment for Carcinogens
High-to-low dose linear extrapolation from POD to 0,0 (non-threshold)

## Slide 19: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment for Carcinogens
Unit Risk: Slope of the dose response line:
Lifetime cancer risk that results from continuous exposure to an agent over a lifetime (assume 70 years)
Also known as “potency”
Refer to EPA IRIS database

## Slide 20: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment for Non-Carcinogens
EPA assumes that there is a threshold concentration below which no observable adverse effect will occur
Reference dose / concentration (RfC) estimates daily exposure to human population (including sensitive subgroups) that is likely to have no risk of lifetime adverse effects
EPA includes with RfC a statement of confidence:
  High: RfC are less likely to change with new info
  Medium: RfC could change with new info
  Low: RfC most likely to change with new info

## Slide 21: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment for Non-Carcinogens
Part 1: Calculate human equivalent concentration (HEC)
  Lowest Observed Adverse Effect Level (LOAELHEC)
  No Observed Adverse Effect Level (NOAELHEC)
  Benchmark Concentration Level (BMCL) involves fitting various mathematical models for dose-response data to reported data
Part 2: Analyze a series of uncertainty factors to estimate a “safe” or “reference” exposure for humans
  RfC methodology from EPA 1994 Methods for Derivation of Inhalation Reference Concentrations and Application of Inhalation Dosimetry

## Slide 22: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Dose-Response Assessment for Non-Carcinogens
= Observed Animal Data
LOAEL
Human RfC
Apply Uncertainty Factors
% Animals Responding
Concentration
NOAEL
NOEL
Liver Toxicity
(Critical Effect)
Tremors
Enzyme Change
Weight Decrease

## Slide 23: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
Inhalation RfC Calculation
Uncertainty Factor (UF)† Criteria UF
Extrapolating animal data to human 10, 3, or 1
Sensitive human populations 10, 3, or 1
Sub-chronic NOAEL instead of chronic NOAEL 10, 3, or 1
LOAEL used instead of NOAEL 10, 3, or 1
Uncertainties in the database for the chemical 10, 3, or 1
  †UF is generally an order of 10, but can be reduced to 3 or 1 when considering dosimetry adjustments or other information

## Slide 24: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment

## Slide 25: TOXC102+ Chapter 6: Toxicity Assessment Toxicity Assessment
EPA Center for Public Health & Environmental Assessment (CPHEA)
CPHEA provides the science needed to understand the complex interrelationship between people and nature by conducting assessments protect human health and ecological integrity
Cancer
Chemical Mixtures
Developmental Toxicity
Ecological Assessment
Exposure Assessment
Mutagenicity
Neurotoxicity
Reproductive Toxicity