## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 7: Risk Characterization

## Slide 2: TOXC102+ Chapter 7: Risk Characterization EPA Risk Assessments
EPA Risk Assessment Framework
Planning and Scoping
Toxicity Assessment
Risk Characterization
Exposure Assessment
Quantitative and Qualitative Expressions of Risk/Uncertainty
POPULATION CHARACTERISTICS
Measures of Exposure
CHEMICAL
CONCENTRATIONS
Air, Soil, Water, Food
(monitor/model)
Dose/ Response Assessment
Y
X
Chemical
Release
SOURCES
FATE AND TRANSPORT ANALYSIS
SOURCE IDENTIFICATION
EXPOSURE information DOSE/RESPONSE information
Hazard Identification

## Slide 3: TOXC102+ Chapter 7: Risk Characterization Risk Characterization
Risk Characterization: Combines outputs from toxicity & exposure assessments
Quantify risks from individual chemicals for each pathway separately (e.g., inhalation, ingestion)
Combine risks from multiple chemicals for each pathway
Combine risks from all pathways to give total risk
Repeat the process for all non-cancer hazards
Assess and present uncertainty

## Slide 4: TOXC102+ Chapter 7: Risk Characterization Risk Characterization
Toxicity
Evaluation
Exposure
Assessment
Risk Management
Decision
Statutory and Legal
Considerations
Risk
Management
Options
Social
Factors
Economic
Factors
Political
Considerations
Risk Assessment
Risk Management
Public Health
Considerations
Risk
Characterization

## Slide 5: TOXC102+ Chapter 7: Risk Characterization Risk Characterization
Presenting Risks
Cancer risks presented separately from non-cancer hazards
  Calculate & present cancer risks
  Calculate & present non-cancer hazards
  Assess & present uncertainties & assumptions
Some chemicals are in both analyses because they cause both cancer & non-cancer effects
Air toxic risk characterization includes only inhalation pathway
  Other pathways may be considered only for persistent, bio-accumulative HAP (i.e. mercury, dioxin)

## Slide 6: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Basic Equation for Inhalation Risks from Cancer Hazards
Risk = EC×IUR
Where:
  EC = Exposure concentration for long term inhalation (lifetime 70 years) for a specific HAP (µg/m3)
  IUR = Inhalation Unit Risk (risk/µg/m3)

## Slide 7: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Inhalation Risk Characterization Examples
Class C – Possible Carcinogen
  EC = 1 µg/m3
  IUR = 2×10-3 per µg/m3
  RISK=(1 µg/m3)×(2×10-3/µg/m3) = 0.002 (2 in 1000)
Class A – Known Human Carcinogen
  EC = 5 µg/m3
  IUR = 2×10-5 per µg/m3
  RISK=(5 µg/m3)×(2×10-5/µg/m3) = 0.0001 (1 in 10,000)

## Slide 8: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Multiple Carcinogens
Sum all the individual cancer risks for each carcinogen present in the air:
RiskTotal = Risk1 + Risk2 + Riski
Unless there is contrary evidence, assume an additive effect from simultaneous exposures.
  No synergistic (greater than additive) or antagonistic (lesser than additive) effects

## Slide 9: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Example of Multi-Pollutant Cancer Risk Estimate |  |  |  | 
HAP | EC µg/m3 | IUR 1/(µg/m3) | Cancer Risk | Percent of Total Risk
Benzene | 0.3 | 7.8×10-6 | 2.3×10-6 | <1%
Dichloroethyl Ether | 2.5 | 3.3×10-4 | 8.3×10-4 | 88%
Formaldehyde | 0.2 | 1.3×10-4 | 2.6×10-5 | <1%
Cadmium compounds | 0.1 | 1.8×10-3 | 1.8×10-4 | 11%
Total Risk (TR) |  |  | 1×10-3 | 100%
Sum All Individual Risks: Unless there is contrary evidence, assume an additive effect from simultaneous exposures |  |  |  | 

## Slide 10: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Expressing Cancer Risk
Individual Lifetime Risk: Cancer risk estimated to be experienced by an individual from a lifetime of exposure at a specified level
  Use average or maximum risk for individuals within population of interest
Incidence: Number of expected cases of the disease over a lifetime (70 years)
  Population × unit risk = # of new cancer cases
Population Risk: Number of people at different risk and hazard levels
  Express population separately for each risk level

## Slide 11: TOXC102+ Chapter 7: Risk Characterization Carcinogens
Expressing Cancer Population Risk

## Slide 12: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Basic Equation for Inhalation Hazard Quotients from Non-Cancer Hazards
HQ = EC÷RfC
Where:
  HQ = Hazard Quotient
  EC = Exposure Concentration
    Acute Exposure: Hourly concentration
    Chronic Exposure: Annual concentration
  RfC = Reference Concentration

## Slide 13: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Definitions
Hazard Quotient: Unitless comparison of a chemical’s concentration in air to a level below which no adverse effect is likely to occur
  HQ is NOT a risk
Reference Concentration: Estimate of continuous lifetime inhalation exposure likely to be without deleterious effects
  RfC do not have equal accuracy due to uncertainty with each RfC
    An HQ of 100 does not mean that the hazard is 10 times > HQ of 10
    An HQ of 10 for two different substance are not the same hazard levels
Uncertainty Factor (UF): Recognized uncertainties in data

## Slide 14: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Inhalation Risk Characterization Examples
Reduced Kidney Function (UF = 30)
  EC = 2 mg/m3
  RfC = 1 mg/m3
  HQ=(2 mg/m3)÷(1 mg/m3) = 2
Reduced Liver Function (UF = 1,000)
  EC = 8 mg/m3
  RfC = 2 mg/m3
  HQ=(8 mg/m3)÷(2 mg/m3) = 4

## Slide 15: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Multiple Non-Carcinogens
Sum all the individual hazard quotients for each non-carcinogen present in the air:
Hazard Index (HI) = HQ1 + HQ2 + HQi
Unless there is contrary evidence, assume an additive effect simultaneous exposures for HQs impacting the same organ
  No synergistic (greater than additive) or antagonistic (lesser than additive) effects

## Slide 16: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Example of Multi-Pollutant Cancer Risk Estimate |  |  |  | 
HAP | EC mg/m3 | RFC mg/m3 | HQ-Hazard Quotient | Percent of Hazard Index
Benzene | 0.0006 | 0.06 | 0.01 | 1%
Dichloroethyl Ether | 0.005 | -- | -- | --
Formaldehyde | 0.0004 | 0.01 | 0.04 | 4%
Cadmium compounds | 0.00002 | 0.00002 | 1 | 95%
Hazard Index (HI) |  |  | 1 | 100%
Sum All Individual HQ: Unless there is contrary evidence, assume an additive effect from simultaneous exposures for same organ |  |  |  | 

## Slide 17: TOXC102+ Chapter 7: Risk Characterization Non-Carcinogens
Non-Carcinogen Mixtures
HI for a mixture of non-carcinogenic chemicals is a screening level study because different toxins target different organs
Target Organ Specific Hazard Index (TOSHI): HI for each organ subgroup
  Identify all major effects & target organs
  Classify each chemical according to target organ
Should be performed by an experienced toxicologist

## Slide 18: TOXC102+ Chapter 7: Risk Characterization Presenting Risk Characterization
Presenting Risk Results
Map average risk and hazards across modeling receptors
Include demographic data
Alternatively: Display risk from highest to lowest variation across modeling receptors

## Slide 19: TOXC102+ Chapter 7: Risk Characterization Presenting Risk Characterization
Presenting Risk Results
Map average risk and hazards by isopleth for multiple sources
Recommend including air toxics from mobile sources (roadways, trains, ports)

## Slide 20: TOXC102+ Chapter 7: Risk Characterization Presenting Risk Characterization
Comparing Risk Estimates
Estimated risk from specific sources evaluated in a modeling study are compared to the estimated risk from background sources from an upwind monitor

## Slide 21: TOXC102+ Chapter 7: Risk Characterization Presenting Risk Characterization
Uncertainty Analysis
Estimates of health risks and hazards are presented with their uncertainties and limitations in the data and methodology
  Exposure estimates & assumptions
  Toxicity estimates & assumptions
  Any other estimate of uncertainty
EPA Risk Characterization Handbook includes guidance for developing and presenting uncertainties
www.epa.gov/risk/risk-characterization-handbook

## Slide 22: TOXC102+ Chapter 7: Risk Characterization Example of Risk Characterization
BNSF Richmond Railyard
Estimated potential cancer risk (X in a million) associated with on-site diesel PM†
  50-100: 280 acres / 1,600 persons
  25-50: 580 acres / 1,900 persons
  10-25: 1,600 acres / 6,200 persons
† 80th percentile breathing rate for 70-year exposure
Source: California Air Resources Board “Health Risk Assessment for the BNSF Richmond Railyard,” 2007

## Slide 23: TOXC102+ Chapter 7: Risk Characterization Example of Risk Characterization
BNSF Richmond Railyard
Comparison of estimated potential cancer risk from Diesel PM emissions and background cancer risk level
Source: California Air Resources Board “Health Risk Assessment for the BNSF Richmond Railyard,” 2007

## Slide 24: TOXC102+ Chapter 7: Risk Characterization Example of Risk Characterization
BNSF Richmond Railyard
Estimated potential non-cancer Hazard Indices associated with on-site diesel PM
  0.05-0.1: 34 acres / <300 persons
  0.02-0.05: 525acres / 2,300 persons
  0.01-0.02: 1,107 acres / 3,500 persons
Source: California Air Resources Board “Health Risk Assessment for the BNSF Richmond Railyard,” 2007

## Slide 25: TOXC102+ Chapter 7: Risk Characterization Example of Risk Characterization
BNSF Richmond Railyard
Uncertainties with emissions inventory (locomotive idling)
Air dispersion modeling (meteorological limitations)
Population variability (metabolism, genetics, age, etc.)
Underlying assumptions regarding Risk and HI (EC)
  Range of inhalation cancer potency: 1.3×10-4 to 2.4×10-3 1/(µg/m3)
Lifetime 70-year (chronic) exposure
  80th percentile breathing rate for lifetime (70-year) exposure
Only used inhalation pathway