## Slide 1: Electrostatic Precipitators PERM 281

## Slide 2: Course Overview
Background/Applications
Theory of Operation
Major Types of ESPs
Design Considerations
ESP Components
Performance Monitoring
Inspecting ESPs

## Slide 3
U.S. Mortality Figures
~64,000 = Deaths from particulate air pollution (2021 report)
~42,500 = Traffic accident fatalities (2022)
~46,000 = Handgun fatalities (2023)
~480,000 = Deaths from smoking (2023)

## Slide 4
0
1000
2000
3000
4000
5000
6000
Los Angeles
New York
Chicago
Philadelphia
Detroit
Particulate Air Pollution-Related Deaths
Based On 1996 Report
Premature Deaths Per Year
5873
4024
3479
2599
2123

## Slide 5: PM10 Emissions by Source Category (1995)
Fugitive Dust
67.5%
Agriculture and Forestry
19.7%
Fuel Combustion, Industrial Processes, Transportation
6.0%
Wind Erosion
5.1%
Fires
1.7%
Source: EPA Trends Reports, Oct 1996

## Slide 7: PM 2.5 National Trend

## Slide 11: History
Single-Stage:
1913 Cottrell (US);
Lodge (UK)
Two-Stage:
1933 Penney

## Slide 12: Background
Advantages
Disadvantages
Applications

## Slide 13
Single -Stage
Two-Stage
Figure 301.2
Charging
Collection
Charging & Collection
Notes: TQ 2

## Slide 14: Single-Stage Industrial ESP

## Slide 18: Concentric Plate Wet ESP

## Slide 19: Tubular Condensing Wet ESP

## Slide 20: Hitachi Tubular Wet ESP

## Slide 22: Two-Stage Module
Charging Section
Collection Section

## Slide 23: Two Stage ESP

## Slide 26: Ionization Section
-
Plates
Wires

## Slide 27
Basic 2 Stage ESP

## Slide 29: ESP Processes
Charging
Migration
Collection
Removal
Notes: TQ 1

## Slide 30: Electric Field Generation
Collection Electrode
Collection Electrode
Collection Electrode
Discharge Electrode
Non-Uniform Electrical Field
Notes: TQ 3

## Slide 31
Corona
(voltage
negative)
Notes: TQ 3
TQ 4

## Slide 32: Avalanche Multiplication
)
Notes:         REF: Page 300-4, Figure 301.3

## Slide 33: Charging and Collection ….so far
"Corona" generated at discharge electrode = high-velocity electrons
Flue gas molecules ionized by high-velocity electrons = positive gas ions + free electrons
Free electrons migrate towards positive collection electrode
Free electrons captured by gas molecules = negative gas ions
Negative gas ions attach to particles which migrate to collection electrode

## Slide 34: Charging & Collection
Gas molecule
Inter-electrode region
Negative gas ion

## Slide 35
Field Charging Diffusion Charging
Negative Electrode
Positive Electrode
Negative Electrode
Positive Electrode
Air Flow
Air Flow

## Slide 36: Particle Size & Collection Efficiency
Notes: TQ 13
TQ 22

## Slide 37
Conduction Mechanisms
Surface
Bulk

## Slide 39: Design Considerations (garbage in/cleaner air out)
Dust Properties
Gas Flow Rate
Gas Temperature

## Slide 40: Migration Velocity
Characteristic of type and size of particles
Experimentally determined or calculated
Used with collection area and gas flow rate to calculate efficiency

## Slide 41: Resistivity
Tendency of a particles to retain a charge after collection
Resistance of collected dust layer to flow of electrical current
Affected By:
  Chemical make-up of dust
  Temperature
  Moisture
  Sulfur content of flue gas
Notes: TQ 10

## Slide 42: Resistivity of Dusts @ Various Temperatures

## Slide 43: Effect of Temperature & Moisture on Resistivity of Cement Dust
Temperature oF
0
100
300
500
700
108
109
1010
1011
1012
1013
Percent Moisture
1%
5%
10%
15%
20%

## Slide 44: Fly Ash Resistivity vs. Coal Sulfur Content
Coal sulfur, %
0.5
1.0
1.5
2.0
2.5
3.0
3.5
108
109
1010
1011
1012
330-350 oF
290-320 oF
250-270 oF

## Slide 45: Generalized Effect of Temperature on Resistivity of Fly Ash
Surface
conductivity
dominant
Bulk
conductivity
dominant
Carbon content 
Moisture 
SO3 
Carbon content 
Moisture 
SO3 
High
Moderate
Low
Average flue gas temperature, oF
107
108
109
1010
1011
1012
0
200
300
500
700
400
600
800
Resistivity, ohm-cm
Normal MWC operating range

## Slide 46: Problem Resistivity Conditions
High • Slower migration rate • Excessive rapping forces • "Back Corona"
Low • Reentrainment
Notes: TQ 21

## Slide 47: Where should ESP be put it?
BOILER
HOT- SIDE
COLD- SIDE
AIR
PRE-
HEATER
FAN
Notes: TQ 23

## Slide 48: Flue Gas Conditioning System

## Slide 49: Design Factors Affecting Performance
Specific Collection Area
Aspect Ratio
Collection Plate Spacing
Sectionalization
Power Requirements/Spark Rate
(Making Your ESP Work)
Notes: TQ 13

## Slide 50: Aspect Ratio
For efficiencies of 99% or higher, should be at least 1.0 to 1.5
Effective Length
Effective Height
=
Notes: TQ 8
TQ 9

## Slide 51: Collection Plate Spacing
Critical Performance Factor
Important Maintenance Point
Single-Stage Spacing: 9 - 20 inches
Wider Spacing = Higher Voltages

## Slide 52: Sectionalization
cell
cell
cell
cell
chamber
chamber
field
field
field
total treatment length
bus section
field
TR
TR
TR
TR
Notes: TQ 18
TQ 19
TQ 20

## Slide 53: Fields and Yields
Field 1
40 KVA
Field 2
50 KVA
Field 3
60 KVA
50 - 60 ft/sec
3 - 5 ft/sec
80%
eff.
80%
eff.
80%
eff.
100 lbs. IN
? lbs. OUT
?
?
?
Notes: TQ 7

## Slide 54: Power Requirements/Sparking
Corona Power = Voltage x Current
Most ESPs designed to produce maximum corona power with spark rate 30 - 150 per minute

## Slide 55: ESP COMPONENTS

## Slide 56: Inlet Duct

## Slide 57: Gas Flow Distribution
Not So Good
Better

## Slide 58: Inlet Diffuser

## Slide 59: Discharge Electrodes

## Slide 60
Notes: Insulator Photos

## Slide 61: Weighted-Wire Discharge Electrodes & Charging System
Tensioning Weight
Discharge Electrode
Discharge Electrode Support Frame
Transformer-Rectifier
High-Voltage Bus Duct
Support Insulator Housing
“Hot Roof”
Weight Guide Frame

## Slide 62: View into Penthouse
Rapper shaft
Discharge Electrode Insulator
Notes: Field Control Panels
Analog gauges
Computer screen with continuous readings of voltage, current, spark rate
Rapper control panel
CEM gauges
Hopper Heater Switch
Instrumentation Photo Series

## Slide 63
Water Tracks
Notes: Top Insulator - Photo
Tub and Insulator - Photo
Insulator Photos

## Slide 64
Weighted Wires
Notes: Top Insulator - Photo
Tub and Insulator - Photo
Floor of ESP

## Slide 65: Frame-Type Discharge Electrodes

## Slide 66
Collection
Plate

## Slide 67: Collection Plate Designs

## Slide 68
Notes: View of collection plates thru hatch - Photo
Top view plates and discharge electrodes - Photo
Top view plates and discharge electrodes - Photo
Hatch Entry - Photo Series
Hatch Entry - Photo
DEs have sawtooth pattern and rigid design.
Distance between DE and CP is critical for proper operation. Sometimes as little as 1/4 inch deviation from mfr specifications can affect performance.
While you will not look at this as a compliance inspector, plant maintenance records should show periodic inspection and adjustment of internal component spacing.

## Slide 69: View Into Side Port
Notes: Field Control Panels
Analog gauges
Computer screen with continuous readings of voltage, current, spark rate
Rapper control panel
CEM gauges
Hopper Heater Switch
Instrumentation Photo Series

## Slide 70
Discharge Electrode
Collection Electrode
Notes: View of collection plates thru hatch - Photo
Top view plates and discharge electrodes - Photo
Top view plates and discharge electrodes - Photo
Hatch Entry - Photo
DEs have sawtooth pattern and rigid design.
Distance between DE and CP is critical for proper operation. Sometimes as little as 1/4 inch deviation from mfr specifications can affect performance.
While you will not look at this as a compliance inspector, plant maintenance records should show periodic inspection and adjustment of internal component spacing.

## Slide 71
Particulate Removal
Notes: TQ 12

## Slide 72: Rapper Types
Pneumatic
Magnetic-Impulse, Gravity-Impact (MIGI)
Hammer and Anvil
Vibratory
Notes: TQ 5

## Slide 73
Pneumatic Rappers
Notes: Pneumatic Rapper Close-up
Pneumatic Rappers - Photo Series
Line of rappers on roof (cement plant, Helena, Montana)
Pneumatic Rappers
>
Failures may be caused by rust, sediment, corrosion in piston chamber.
Compressed air supplied must be clean and dry with dew point less than ambient to prevent moisture from getting inside control device.

## Slide 74
Notes: Pneumatic Rapper Close-up
Line of rappers on roof (cement plant, Helena, Montana)
>Describe operation
Provide most intense shock
Can be impact or vibrator type

## Slide 75
Magnetic Impulse Rappers
Notes: MIGI Rapper close-up - Photo
Note rubber boot cracking.
One of these also installed over gas inlet diffuser plate.

## Slide 76
Magnetic-Impulse
Gravity-Impact
(MIGI) Rapper
Notes: Pneumatic Rapper Close-up
Line of rappers on roof (cement plant, Helena, Montana)
Pneumatic Rappers
Failures may be caused by rust, sediment, corrosion in piston chamber.
Compressed air supplied must be clean and dry with dew point less than ambient to prevent moisture from getting inside control device.

## Slide 77: Penthouse Vent Blower
Notes: TQ 25

## Slide 78: Hammer-Anvil Rappers

## Slide 80: Rapper Control Panel

## Slide 81: Collection Hopper
Notes:   Center divider baffle unique to ESP hoppers to prevent gas from "sneaking" under one field to the next. Side baffles also perform same function. Baffles also prevent fast moving air from reentraining dust in hopper.

## Slide 82
Hopper with Strike Plate

## Slide 83
Hopper Level Indicator System
Notes: TQ 11

## Slide 84
Hopper Vibrator
Notes: Vibrator prevents buildup on sides of bin. Bottom valves must be designed to permit downward movement of dust with minimal air infiltration. Butterfly or rotary airlock valves common.
Dust must be removed quickly to prevent buildup and pluggage.
Vibrators compact dust in hoppers.
Airlock and Bin Screw- photo
Airlock prevents inleakage.
Q. Other places to look/listen for inleakage include ???
  Access doors, Ductwork, sample ports
Inleakage results in cooling and introduction of moisture. Can result in agglomeration of dust in hopper = pluggage; also corrosion.
Inleaking air can also reentrain dust.

## Slide 85: Hopper Heater Control
Notes: Computer screen with continuous readings of voltage, current, spark rate
Rapper control panel
CEM gauges
Hopper Heater Switch

## Slide 86: Airlock & Bin Screw
Notes: .

## Slide 87: Rotary Airlock Valve

## Slide 88: Pneumatic Dust Collection System
Notes: TQ 24

## Slide 89: Dust Discharge Problems
In leakage
Corrosion
Dust Buildup
Pluggage
Fugitive Emissions

## Slide 90: High Voltage Equipment
Transformer
Rectifier
Sensors
Control System

## Slide 91: Transformer-Rectifier (T-R Set)
Transformer - Increases voltage at discharge electrodes
Rectifier - Converts alternating current (AC) to direct current (DC)
Notes: TQ 14

## Slide 92: Transformer-Rectifier Set
Bus
Notes: s
GaugeTransformer Liquid Temperature
T-R Specification Panel
Each T-R set may supply power to one or more sections of an ESP.
Q. Each of these is called what? (Bus Section)

## Slide 93
Notes: T-R Photo Series

## Slide 94
Sensors/Gauges
Spark Rate Meter
Primary Ammeter
T-R Set
Primary Voltmeter
Secondary Voltmeter
Secondary Ammeter

## Slide 95: Control System
Power Control Circuits
Voltage-Limit Control
Current-Limit Control
Spark Control

## Slide 96: T-R Set Spec. Plate
Notes: Each T-R set may supply power to one or more sections of an ESP.
Q. Each of these is called what? (Bus Section)

## Slide 97: Analog Gauges

## Slide 98: Digital Readouts

## Slide 99: Performance Monitoring
Air Load Testing
Gas Load TestingOpacity
Corona Power
Spark Rate

## Slide 100: Voltage-Current (V-I) Curve
Secondary voltage, kV
10
20
30
40
50
0
300
400
600
700
0
100
200
500
800
Onset voltage
Sparkover

## Slide 101: Corona Power versus Collection Efficiency for Coal-Fired Utility Boiler
0
100
200
300
400
Corona Power, watts/1000 acfm
Collection Efficiency, %
0
90.0
99.0

## Slide 102: Baseline Conditions
Secondary current, mA
Sparks per minute
Secondary voltage, kV
4
30
40
0
10
20
50
0
1
2
3
Inlet Field
Outlet Field
Current
Voltage
Spark rate

## Slide 103: High Resistivity Shifts from Baseline
Secondary current, mA
Sparks per minute
Secondary voltage, kV
4
30
40
0
10
20
50
0
1
2
3
Inlet Field
Outlet Field
Current
Voltage
Spark rate

## Slide 104: Common Problems
Resistivity
Hopper Pluggage or Overflow
Misalignment or Warpage
Insulator Failure
Discharge Electrode Failure
Air Inleakage
Corrosion
Rapping System Problems
Control System Failures
Particle Size and Concentration

## Slide 105: Enhancing ESP Efficiency
Wide plate spacing
Pulse energization
Automatic voltage controls
Improved flow conditions
Optimal rapper timing
Flue gas conditioning
COHPAC

## Slide 106: COHPAC (Compact Hybrid Particulate Collector)
ESP
Pulse BH
Flue
Gas
30%
Opacity
2% Opacity

## Slide 107
INSPECTING
ESPs

## Slide 108: Typical Permit Conditions
Opacity limits
Grain loading limits
Ranges of ESP inlet & outlet temperatures
Minimum total corona power
Maximum process rate
Recordkeeping requirements
CEM requirements
Maximum allowable pressure drops
Limit on the number of fields offline

## Slide 109: Air Pollution Control System Points of Inspection
System Entrance/Exit
Transport
Air Mover
Control Device
Instrumentation
Subsystem
Records

## Slide 110: Observe Stack Effluent
Opacity vs. Mass Emissions
Plume Color
Vapor Plume
Puffing
Notes: TQ 12

## Slide 111
As particle size gets smaller, reflective surface area increases
Bouguer's Law

## Slide 113: Perform External Inspection
T-R Sets
Rappers & Vibrators
Insulators
Shell
Access Doors
Ductwork

## Slide 115: Note Exposed Insulation
Notes: TQ 24
Insulation helps to prevent heat loss from the
shell of an ESP.

## Slide 116
Notes: Accumulation of caked dust on exterior shell of ESP.
Caused by condensed liquid leaking from the shell of the ESP. Dust accumulates on the liquid and hardens. Something which should be looked for during a visual inspection of the ESP.

## Slide 117: Evaluate Ash Handling Procedures
Evacuation rate
Level alarms operating
Hopper temperature
Ash buildup

## Slide 120: Ash Storage Silo

## Slide 121: Instrumentation
Power Input: 1º/2º Voltage; 1º/2º Current; Spark Rate
Gas Flow & Temperature
Rapper Frequency/Intensity
Hopper Dust Level Indicator/Alarm
Opacity Monitor
Oxygen Monitor
Notes: TQ 23

## Slide 122: Check High Voltage System Operation
Observe control panels
Check log for drift in electrical data
Note inoperative meters
Note T-R sets on "manual” and "auto"

## Slide 123: Analog Gauges

## Slide 124: CEM System Readouts & Controls

## Slide 125: Review Recordkeeping
Design Specifications
Operating Data & Records
Inspection & Maintenance Records
Component Failure Records

## Slide 126: Safety
Notes: TQ 16

## Slide 129: THE
END