## Slide 1
Auto, Metal Parts and Products
TOXC 231
Notes: INTRODUCTORY REMARKS:
  Fill out name tents, tracking cards, sign-in sheet. "Please write legibly as you want your name to appear on your certificate. Include agency name and address."
  Agenda highlights - lecture, breaks, lunch, exam, field trip, safety gear requirements, certificate
  Student background, experience, expectations.
  Introduce yourself, background, and experience.
  Aims of 200-Series training program:
  • Inspector-oriented.
  • Details of process and practical inspection techniques.
  • Facilitate communication and share experiences.
COURSE OVERVIEW/PURPOSE:
  Goal: To familiarize you with coatings used in metal finishing, how they work, and how to evaluate compliance with air pollution regulations and permits. Some engineering considerations covered, but not an engineering course.
  Topics to be covered - refer to Agenda, Handout, or Overview Slide
  Course Manual (if applicable) - review contents, indicate how used
  Handouts - indicate how will you be using them.
  Additional information - instructor discretion

## Slide 2: Course Overview
Ozone and Human Health -- HAPS
General Overview of Coating Ops
Coating Composition & Emissions
Pollution Prevention and Control
Control Devices
Rules & Regulations
Inspections
Calculations
Notes: Course Overview
Ozone and Human Health -- HAPS
General Overview of Coating Ops
Coating Composition & Emissions
Pollution Prevention and Control
Control Devices
Rules & Regulations
Inspections
Calculations

## Slide 3: Why Are We Here?
Alveolar Injury Leading to Pulmonary Inflammation and Permanent Lung Damage
Respiratory Discomfort to Sensitive Populations
$330 Million in Crop Damage Each Year
Damage & Failure of Paints and Rubber Parts
Ozone Causes:
Notes: VOCs are precursors to the formation of OZONE
Oxidants (including ozone) are a hazard to organic tissues and the economy.
We all care because we are all directly affected.
TQ 14

## Slide 4
Notes: Note the role of VOC in diagram
Plays a role in preventing recombination of O3 & NO
Reduces Ozone scavenging
Ozone is a criteria pollutant. LD-50 of 50 ppm in 1 hour in mice. Public health emergency at 1 ppm.
NOx, the largest part of this equation, is already controlled to the maximum extent possible. So in the early 1970s regulatory agencies turned to VOC regulations. List sources of hydrocarbon emissions.

## Slide 5: Coating Market Segments
OEM Product Coatings
  Automotive
  Marine
  Aircraft
  Metal Containers
  Appliances
  Machinery and Equipment
  Wood Furniture
  Plastics
  Coil
  Overprint
Architectural Paints
  Interior
  Exterior
Special Purpose
  Industrial Maintenance
  Traffic Paint
  Auto Refinish
Miscellaneous
  Roof, Tank, Deck
  Concrete
Notes: Big Picture
Miscellaneous could be architectural under some rules.

## Slide 6: Comparison of Automotive vs. Metal Parts
Less Steps
Many Application Types
Booth
Corrosion Resistance
More Steps/Coats
Basically, One Type of Application
Booth or Outdoors
Looks Are Everything
Notes: Corrosion resistance is important in automotive as well.

## Slide 7: What Are Metal Parts?
Motor Vehicle Parts
and Accessories
Recreational Vehicles
Heavy Duty Trucks
Railroad Cars
Bicycles and Sporting
Goods
Extruded Aluminum
Structural Components
Medical Equipment
Lawn and Garden
Equipment
Electronic Equipment
Magnet Wire
Steel Drums
Industrial Machinery
Metal Pipes
Notes: What Are Automotive Parts?
Motor Vehicle Parts and Accessories
Recreational Vehicles
Heavy Duty Trucks
Railroad Cars
Bicycles and Sporting Goods
What Are Metal Parts?
Extruded Aluminum
Structural Components
Medical Equipment
Lawn and Garden Equipment
Electronic Equipment
Magnet Wire
Steel Drums
Industrial Machinery
Metal Pipes

## Slide 8: What is a Coating?
A thin film of organic material
adhering to a mechanical device to
protect it from corrosion or degradation
by its environment. Consequently
the color and texture of the
surface are also altered.
Notes: Coating
A thin film of organic material adhering to a mechanical device to protect it from corrosion or degradation by its environment.
Consequently, the color and texture of the surface are also altered.

## Slide 9: What Kinds of Coating?
Topcoat
Undercoat
Primer
Sealer
Surfacer
Notes: Topcoat -- final paint coat, what meets the eye.
Undercoat -- any coats underneath topcoat.
Primers -- increase topcoat adhesion
-- corrosion protection for SUBSTRATE or both.
-- filling and smoothing of surface irregularities.
MOST IMPORTANT COATING (arguably)
Sealer -- usually an undercoat which protects subsequent coatings from absorption or other harm.
Surfacer -- used to fill surface imperfections, designed for easy sanding.
SUBSTRATE – the surface being coated.
TQ 8

## Slide 10
New Car Coating Process
Phosphate Cleaner, Electro Deposition for Corrosion
Primer
White, Black, Silver and Red
Base Coat
Top Coat and Clear Coat
Sealer
Notes: At BMW the first step of the process is to degrease and wash the car. It is then given a layer of phosphate followed by the e-coat which is baked to cure. This is followed by a trip along the sealer line to seal the gaps, making the car water tight and guaranteeing proper acoustics. The car is then cured after which the spray painting process starts. The first step is the primer which comes in 4 different colors, namely white, black, silver and red. This is the first color layer and it is ‘color keyed’ to the final color, for example, a blue base coat has a black primer, and silver has silver. The primer layer is then cured in an oven. Base coat is applied in 2 steps for metallic finishes. The coat is applied electrostatically, which minimizes overspraying. You do however then get a situation where the aluminum flakes all point in the same direction and you negate the ‘flip flop’ effect.
Pneumatic application then follows over the first layer, which makes metallic align in a way which gives the metallic ‘flip flop’ effect. The car is then clear-coated and baked and then cavity waxed to protect vulnerable areas from corrosion. The thickness of the whole process is in the region of 100 microns.

## Slide 11: A Coating System
Compatibility Intercoat
Topcoat
Substrate: Metal, Plastic or other
Primer/Sealer/Surfacer
1 to 5 mils each
Powder
Notes: The coating system is inserted between the substrate and the environment as a permanent protective boundary. 1 mil equals 25.4 microns
In most cases, pretreatment is an acid etch that alters the chemistry of the substrate and may leave a residue of 0.005 to 0.5 mils thickness. Or 0.125 to 12.5 microns.
Primers : 1) fill and smooth the surface
2) provide for adhesion of top coat
3) protect substrate from corrosion

## Slide 12: REFINISHING
Refinishing is the coating of vehicles, their exterior parts or components, or mobile equipment, including partial body collision repairs for the purpose of protection or beautification and which is subsequent to the coating applied at the manufacturers’ assembly line.
Notes: REFINISHING
Refinishing is the coating of vehicles, their exterior parts or components, or mobile equipment, including partial body collision repairs for the purpose of protection or beautification and which is subsequent to the coating applied at the manufacturers’ assembly line.
--- EPA DEFINITION

## Slide 13: Refinish Coating Manufacturers
BASF InMont
DuPont
PPG/Ditzler
Sherwin Williams
Glasurit Sikkens
More than 65,000 Formulations for 13,000 Colors!!
Notes: OEM colors are chosen by the marketing team after five years of field testing. Once selected, refinish formulations to match these colors must be developed.
If we ask for a high solids formulation 65,000 new chemical formulas would have to be developed.
Note there is no Japanese entrant. The Germans had been making inroads in both the coatings market and the spray gun market. Today (2006) DuPont has 70% of the San Francisco market and PPG has 70% of the rest of northern CA. California is 18% of PPG’s business.

## Slide 14: Special Features of Auto Refinishing
Color Matching
Sun and Weather Exposure
Extreme Aesthetic Standards
No Oven Curing
Notes: This is what separates automotive from other MP&P.

## Slide 15
Metal
White Primer
Grey Intercoat
Topcoat
Bondo Plastic Putty (dent filler)
Plastic & Fiberglass Body Parts
Notes: Sanding reveals various layers of coating system.

## Slide 16: Color Matching
Little Full Color Changes
Notes: Masking is the majority of refinishing process.
Work is repairs with color matching.
Little is full color change. So the work area is isolated from the non-work area until the final steps.

## Slide 17: What’s in a Coating?
Four components of any coating:
Binder aka Resin
Pigment
Solvents
Additives
Notes: There are literally a limitless number of organic chemical solutions to every coating problem.
Binders or Resin
Pigments and Extenders
Additives
Solvents, Thinners and Diluents
All of these components are applied to a substrate to a mil thickness of from 1 to 10 mils (thousandths of an inch).
As inspectors, however, you are primarily concerned with VOC content.
TQ 18

## Slide 18: BINDER
Natural or Synthetic Resin
Will Harden on Cue (Evaporation)
Most Often a Plastic
Notes: The heart of the coating system.
This is the material that will spread as thin as a liquid and convert to a solid when we want it to -- on queue.
Most often a plastic, but fundamentally anything that we can dissolve, that will impart the right set of properties to a surface when it hardens. Gives the coating its physical properties such as hardness, flexibility, and chemical resistance.
Most often referred to as RESINS >>>>>>>

## Slide 19: Common Binders
Nitrocellulose
Acrylics
Alkyds
Polyurethanes
Epoxies
Notes: This is most often a plastic. It is a liquid material that we can convert to a solid on cue. That cue is normally the simple evaporation of the liquid it is dissolved in.
The binder is normally chosen for 1) the mechanical properties of the dry film and/or 2) its curing technology, how it behaves for the painter.
Usually a non-voc part of the coating.

## Slide 20: PIGMENTS
Small Hard Particles added for:
  Color
  Strength
  UV Protection
Notes: Pigments are “small particles added to a coating to influence properties such as color, corrosion resistance and mechanical strength.”
Like the gravel in concrete, pigment is the principal mechanical strength in the dry film. The binder is the cement that holds the strong particles together.
Solid pigments cast a shadow on the solid (uv sensitive plastic) binder below is the simplest surest way to extend the life of a binder film (coating).
“Finely ground insoluble particles dispersed in coatings to influence properties such as color, corrosion resistance, mechanical strength, hardness, and durability. Particles may be natural , synthetic, inorganic, or organic.”

## Slide 21: SOLVENTS, DILUENTS AND THINNERS
Liquids Added To:
“Dissolve” Binder
Adjust Viscosity
Promote Adherence
Promote Flow
Drying & Curing
Notes: The component we are most concerned about is added simply as a vehicle. Solvents are chosen for their ability to dissolve the binder chosen earlier and their speed of drying and curing once the mixture is spread.
Solvents gradually evaporate away until they are essentially purged from the coating. At or near this point the coating is said to be cured.
“Dry to the touch” is different from cured.
Over the last 20 years the amount of VOC solvent in most coating systems has been systematically reduced.
From a regulatory standpoint, this is the component we are most interested in. First because of the VOC (ROG) content and second because of the Hazardous Air Pollutants (HAPS) used and emitted.
TQ 19

## Slide 22
Reducer
Notes: To get any respect in this business of inspecting automotive ops,
you must remember this:
You thin a lacquer & You reduce an enamel.
Reducing alters the speed of the catalyst’s action.
Historically, painters thinned their lacquers with art and experience, adding as much as they thought necessary according to the weather. Today Lacquers are rare & enamel components are mixed as a precise science. The painter usually does not deviate from the recipe.
Here are Dupont reducers in an automotive paint shop.

## Slide 23
Thinner
Notes: What is the difference between a thinner and a reducer?
About $10 per gallon.
Thinners (like mineral spirits) are usually crude petroleum distillates.
Reducers are very specifically designed for the resin.

## Slide 24
Notes: Pure, highly volatile VOC.

## Slide 25
Notes: LOW VOC CLEANER -- Probably an aqueous glycol mixture.

## Slide 26: ADDITIVES
Material Introduced For:
Specific Effect on either
Wet or Dry Film
Less than 5% of total coating mass
May or May Not Evaporate
with solvent
Notes: Additives Types
Chemicals added for a specific effect on either the wet or dry film. examples: luster enhancer, drying speed, hardness, anti-fisheye
(Normally total less than 5% of liquid volume)
Additives may be solids or liquids and may or may not evaporate with the solvent. They may or may not be HAPS.
TQ 16

## Slide 27: Poll Questions 1 & 2
Notes: 1 What is a common range of thickness per coat on metal parts?
1-5 mils
10-20 mils
100-150 mils
0.1-0.8 mils
2 Which is NOT a component of a coating?
Binder
Pigment
Solvent
Aggregate

## Slide 28: VOC Control Strategies for Coatings
Use Reduction
• Use of Exempt Solvents
• Use of Water-Borne Products
• Increased Solids Contents
• Increased Transfer Efficiency
Retrofit Control Devices
• Capture and Reuse
• Capture and Destroy
Notes: VOC Control Strategies for Coatings:
Use Reduction
  Exempt Solvents (AZ = non-precursor)
  Water-Borne Products
  Increased Solids Content
  Increased Transfer Efficiency
Retrofit Control Devices
  Capture and Re-Use
  Capture and Destroy
TQ 24

## Slide 29: Rule Provisions: Automotive Refinishing and Metal Parts
Transfer Efficiency (T.E.) Provision
Spray Booth Requirement (PM)
VOC Coating Content Limits
Open Container Limits
Clean Up
Notes: EFFECTIVE VOC Coating Regulations
Transfer Efficiency (T.E.) Provision
Spray Booth Requirement (PM)
VOC Coating Content Limits
Open Container Limits
Clean Up
TQ 12

## Slide 30: Coating Type Formulations
Coating % Organic % Water %Solids*
Solvent
Solvent-Borne ~75 0 ~ 25
High-Solids < 40 0 60 - 80
Waterborne 0 - 20 < 80 50 - 100
Powder Coats 0 - 5 0 > 95
* Solids Include: Binders, Pigments & Additives
Notes: Coating % Organic % Water %Solids*
Solvent
Solvent-Borne ~75 0 ~ 25
High-Solids < 40 0 60 - 80
Waterborne 0 - 20 < 80 50 - 100
Powder Coats 0 - 5 0 > 95
* Solids Include: Binders, Pigments & Additives
Primary source: p2pays.org and EPA

## Slide 31: Exempt Solvents*
Vary by Agency Definition
Have a Variety of Human Health Effects
Including Anesthesia and Intoxication
Stratospheric Ozone Depletion
Sometimes Incompatible with Aluminum or Water
*Negligibly Photochemically Reactivity
Notes:   Exempt Solvents* (AZ = non-precursor)
Vary by Agency Definition
Have a Variety of Human Health Effects Including Anesthesia and Intoxication
Stratospheric Ozone Depletion
Sometimes Incompatible with Aluminum or Water

## Slide 32: Waterborne Coatings
Provide: Solvent Penetration Protection Low VOC Reduced Fire Insurance Easy Clean-up
Require: Careful Surface Prep Temp. & Humidity Control While Curing or Longer Drying Times Stainless Steel Equipment
Notes: Water is the volatile fraction.
Provides: Solvent Penetration Protection Low VOC Reduced Fire Insurance Easy Clean-up
Requires: Careful Surface Prep Temp. & Humidity Control While Curing or Longer Drying Times Stainless Steel Equipment

## Slide 33: Difficulties for Waterborne Metallic Topcoats
Hydrogen Evolution
Flake Orientation (Critical Dry Times)
Notes: Most Waterborne in Automotive is undercoat or primer coats, not top coats

## Slide 34: Water as a Diluent
x grams of solids
covers area y
x grams of solids
covers area y
Solids
Organic Solvents
Solids
WATER
Co-solvent
Solvents
Notes: The rules are written in terms of less water because the applicator will use as much as he needs to get the coverage.

## Slide 35: Co-Solvent (aka coupling agent)
Solvent that Causes Two Immiscible Liquids to Mix
May Comprise up to 30% of the Liquid in a Waterborne Coating
Notes: Examples: glycols, ketones, alcohols

## Slide 36: Powder Coatings
Thermoplastic or Thermoset
No on-site Color Mixing
Faraday Cage Effect
Baked to Cure
Electrostatic Application or
Fluidized Bed Required
Notes: Have especially low VOC content and especially high transfer efficiency (because of electrostatics)
May not reach internal corners due to Faraday cage effect
Possibly the solution to the VOC and TAC problem, if the user can deal with the limitations:
1) Must be baked to cure → no temp. sensitive parts
2) Color matching is much more difficult
3) No acute angles (faraday cage).
Most Common Resins: Polyurethanes
Epoxies
Polyesters
TQ 1
TQ 7

## Slide 37: Transfer Efficiency (T.E.)
Percentage ratio of the weight of solids
deposited on the substrate to the weight
of solids actually used
Notes: Definition Transfer Efficiency is
Mass of solid coating deposited
Mass of solid applied
TQ 2

## Slide 38: Transfer Efficiency Variables
Spray Equipment
Shape of Part
Ambient Temperature and Humidity
Air Flow Rate in Spray Booth
Notes: TE Variables
Spray Equipment
Shape of Part
Ambient Temperature and Humidity
Air Flow Rate in Spray Booth

## Slide 39: Transfer Efficiency Variables
Coating Chemistry
Painter Training and Experience
Paint Pressure and Air Pressure at Nozzle
Notes: TE Variables
Coating Chemistry
Painter Training and Experience
Paint Pressure and Air Pressure at Nozzle

## Slide 40
0 20% 30% 40% 50% 60% 70% 80% 90% 100%
HVLP
Airless Electrostatic
Air - Assisted Airless Electrostatic
Air Electrostatic
Air - Assisted Airless
Airless Spray
65%
Percent Transfer Efficiency
Air Spray
Notes: Air Spray – Conventional old way, needle sized holes in horn
Airless Spray – Pneumatic pump pushing the fluid, Wagner Sprayer
Assisted Airless – Compressor pushing paint.
Air Electrostatic, Air Assisted Airless Electrostatic
HVLP is air spray with HVLP cap Most districts require 75% TE

## Slide 41: HVLP Transfer Efficiency Saves $$
Notes: EXAMPLE illustrates saving from using HVLP --
but similar savings would occur using other high T.E. application methods.

## Slide 42: Air Spray Video

## Slide 43: HVLP? DeVilbiss Gun
Notes: Criteria
high volume of air
low pressure air at cap (0.1 - 10 psig)
generally has high transfer efficiency
SDAPCD Definition
"High-Volume Low-Pressure (HVLP) Spray" means a coating application method which uses pressurized air at a permanent pressure between 0.1 and 10.0 psig, not to exceed 10 psig, measured at the air cap of the coating application system.
TQ 11

## Slide 45: HVLP Caps
Air Horn or Wing Port
Hole Size
HVLP
Primer
Conventional Air
Notes: If not marked, you can recognize HVLP by inspecting the wing ports.
If the cumulative size of the wing ports will accommodate a new Crayola crayon this is HVLP.
If the wing port fits a sharpened No. 2 pencil, this is likely the primer gun. A high solids primer will require more air to shape the fan.
A conventional air gun has one to five needle sized ports in the air horn (aka wings).

## Slide 46
Spray Cap Pressure Gauge
Notes: Many facilities have HVLP equipment these days.
But our job isn’t done unless we know that the coating is being applied at or below 10 psi.
To confirm this we need a SCPG. This must be specifically for the make & model of gun in use.
So the operator will need to have his own @ about $50/unit.

## Slide 47
Digital
Air
Pressure
Readout

## Slide 48
Gun Air Pressure Gauge.
Can this Replace the Spray Cap Pressure Gauge?
Notes: It can if it reads at or below 10 psi.
If it reads above 10 we have to go to the spray cap press gauge to confirm that the gun is stepping down the pressure.

## Slide 49: HVLP Gun Manufacturers
SATA High end products with precision engineering and digitally controlled mechanisms.
DeVilbiss Age old industry standard spray gun. A wide range of models.
Sharpe American made, budget price.
Binks Another industry standard gun. Binks guns share a market niche with DeVilbiss.
Accuspray Only gun with a plastic body
Astro Pneumatic guns are modeled after higher priced models above .
Notes: Binks and DeVilbiss once owned this market.
Today there are many brands for operators to choose from.
Roughly in order of market share.

## Slide 50: Spray Gun Feed Options
Gravity Feed
Pressure Feed
Suction/Siphon Cup
Notes: All manufacturers make all styles. Painters tend to be dedicated to the tools they learned with. Gravity feeds, originally from Europe are rapidly gaining in popularity in the states.

## Slide 51
Electrostatic Spray Gun
Note: Charging Electrode
Notes: Both liquids & powders may be sprayed electrostatically.

## Slide 52: Electrostatic Spray Video
Notes: 3 minutes

## Slide 53: Powder Coating Gun
Notes: This is often referred to as WRAP-AROUND

## Slide 54: Powder Coatings Video

## Slide 55: Powder Coated Products

## Slide 56: Poll Questions 3 & 4
Notes: What does HVLP stand for?
  Hydro-Vacuum Liquid Pump
  High Volume Low Pressure
  High Viscosity Light Polarizing
  Half Volume Latent Pressure
How is Transfer Efficiency defined?
  Mass of solids deposited ÷ mass of solids used
  Volume of coating deposited ÷ volume of coating used
  Mass of solids used ÷ mass of solids deposited
  Mass of solids deposited ÷ volume of coating used

## Slide 57: Coating Steps and Points of Emission
Abrasive Sanding or Blasting
Surface Clean and Prep
Primer & Topcoat Application
Flash Off -- Drying
Curing
Touch Up
Equipment Clean Up
Notes: The briefest step here is coating application. When you visit they are likely to be doing anything BUT spraying.
Sanding or Abrasive Blasting
Surface Clean and Prep
Primer & Topcoat Application
Flash Off -- Drying
Curing
Touch Up
Equipment Clean Up

## Slide 58: Points of VOC Emission
Storage Application Cleanup
Mixing Drying & Prep.
90% of VOC Emissions
Notes: As can be seen on this pictorial:
MOST VOC EMISSIONS FROM SPRAY PAINTING OPERATIONS OCCUR DURING THE APPLICATION PROCESS.
TQ 4

## Slide 59: Surface Preparation
Abrasive Sandblasting
Body Filler (Auto)
Cleaning/Degreasing
Application Acid Etching
Notes: SURFACE PREPARATION
>> Abrasive Sandblasting
>> Body Filler (Auto)
>> Cleaning/Degreasing
>> Application Acid Etching

## Slide 60: Surface Preparation
Detergent Washing
Sandblasting
Filling and Sanding
Notes: Acetone is also used in prep.
Compatibility of various layers in a coating system are a consideration if all layers were not purchased as a single system. The solvents in slow drying enamels will destroy a lacquer below. A fast drying lacquer will release its solvents before they attack an enamel. A lacquer will be selected as a lower coat if it is known to be immune to the subsequent layer.
This intercoat is also a natural application for a waterborne product since it will be immune to the solvents in the topcoat.
The intercoat must also be able to adhere to bare metal, the existing primer and the existing topcoat.

## Slide 61: VOC Emissions Automotive

## Slide 62: Curing
The Process in which Paint is Converted from Liquid to Solid
Notes: CURING
The Process in which Paint is Converted from Liquid to Solid

## Slide 63: Curing and Coating Types
Air Drying
Lacquers
Enamels
Powder Coats
High Solids
Waterborne
Notes: “Dry to the Touch” is different than Cured.
Air Drying, does not need to be heated to cure.
Lacquers - Paints which dry by evaporative loss of a solvent.
Enamels - Chemical reaction between binder materials. Latex, drying is loss of water and merging of paint particles.
Powder Coats, finely ground paint, heated to melting point, and flows out and smoothes. Solidifies upon cooling.
High solids, greater than 50% solids, usually must be heated.
Waterborne, dissolved or suspended in water.
TQ 6

## Slide 64: More on Curing - Lacquer
Cures by the Evaporation of the Solvent
Notes: Evaporation IS the normal drying (to touch) agent for AR but not necessarily the curing (final hardness) agent.
These also come in reversible and nonreversible curing chemistries.
The history of AR begins with lacquers and ends with enamels.

## Slide 65: More on Curing - Enamel
Cures by an Irreversible Chemical Reaction Involving Various Components or Atmospheric Water or Oxygen
Notes: ENAMEL
Cures by an Irreversible Chemical Reaction Involving Various Components or Atmospheric Water or Oxygen
e.g. Polyurethanes, Alkyds, not as pretty.

## Slide 66: Curing Methods
Air dried
Thermoset or Thermocure
Baked Coating > 194oF
Thermoplastic
Radiation
Notes: 194oF is a regulatory number. In the real world air drying usually done below 140oF and baked begins at 250oF
Like frying an egg, the chemistry of thermoset and thermocure plastics is irreversibly changed by the heating. Further heating can only damage the coating.
Thermoplastics can be re-melted an indefinite number of times
Radiation polymerization by exposure to a high-energy radiation (ultraviolet or an electron beam)
In auto refinishing curing is always below 194oF (air dry)
Heat is never the principle curing agent.
The factory applied OEM is normally a thermoset. Any factory applied, heat cured coating is better protection than any air dried refinish.
Thermoplastics are a more exotic class of coatings where the curing is reversible, such as powder coatings (not used in AR).
TQ 5

## Slide 67: Curing Times
Air dried hours
Oven Baked minutes
Epoxy Systems minutes
Ultraviolets (UV) seconds
Electron Beam < 1 second
Notes: This slide is designed to give you an idea of the time requirements to cure using the major types of curing systems.

## Slide 68: Curing Types (cont.) Thermoset/Thermocure
Solid Resins
Heated - melt and flow
Cross-link to form Higher Molecular Weight Solid
Remains Stable After Heating
Notes: Thermoset/Thermocure Resins
Solid Resins
Heated - melt and flow
Cross-link to form Higher Molecular Weight Solid
Remains Stable After Heating

## Slide 69: Curing Types (cont.) Thermoplastic
A Polymer
Liquid when Heated
Freezes Glassy when Cooled
No Cross-linking
Re-melted, Re-molded, and Recycled
Notes: CURING OF THERMOPLASTICS
Liquid Polymer when heated
Freezes when cooled
No cross-linking
Can be re-melted, re-molded and re-cycled
TQ 21

## Slide 70: Oven Cured Temps
Notes: Normally 250-350 degrees F

## Slide 71: Automotive Ops Are Special
Notes: Automotive Operations Are Special.

## Slide 72
Forced Dry or
Accelerated Drying
with heat lamps
Is this a baked cure?
194° F
Regulatory Cutoff
Notes: Due to rubber tires, installed glass and plastic components (tail lights etc.) normal limit for an accelerated drying is 120o F.

## Slide 73: Poll Questions 5 & 6
Notes: How long does oven baked curing generally take?
  Hours
  Minutes
  Seconds
Most VOC emissions from a spray coating operation come from…
  Surface preparation
  Paint mixing
  Application
  Drying

## Slide 74: Control Alternative
Rather than Meet VOC Limits a Source May:
• Collect at Least a Required Percent by Weight of Emissions
And • Transport to a Central Device that Reduces Emissions at Least a Required Percent (Total Control = 85%)
Notes: Rather than Meet VOC Limits a Source May:
• Collect at Least a Required Percent by Weight of Emissions (usually 90%)
And
• Transport to a Central Device that Reduces Emissions at Least a Required Percent (Total Control = 85%)

## Slide 75
Capture System Schematic
Notes:   ENCLOSURES
    Permanent total (on left) – 100% capture efficiency
    HOOD (on right) -- partial capture efficiency
    which must be measured
    NDO = Natural Draft Opening
drawings are from Method 204

## Slide 76: Booth Design
Air Flow Particulate Collection
Downdraft Water Wash
Sidedraft Dry filter
Hood
Notes: BOOTH DESIGN
Air Flow
Downdraft
Sidedraft
Hood
PM Collection
Water Wash
Dry Filter

## Slide 77: Down Draft Spray Booth
Notes: DOWN DRAFT SPRAY BOOTHS ARE COMMONLY USED IN AUTOMOTIVE COATING OPERATIONS.

## Slide 78: Water Wash Spray Booth
Notes: Technology Fact Sheet: Water Wash Spray Booths [Technology Description | Internet Resources | Supplier Information | Broadcast E-mail]
Technology Type: Pollution Control | Classification: Commercialized Technology Description. The most important alternative to dry filter spray booths are water-wash booths. Instead of collecting overspray in the filter bank, a constant stream of water in an entrainment section scrubs overspray from the air that the booth exhausts. Some water-wash booths are designed with a water curtain, but this is not a prerequisite. Most commonly, cross-draft and semi-down draft booths have water curtains while down draft booths do not. Water flowing down the curtain collects much of the overspray, but the scrubbing action in the entrainment section is more important. In the entrainment section, fixed baffles force the exhaust air to constantly change direction and, as this occurs, the water scrubs the particulates from the air or they simply fall into the water trough.
Without benefit of pump or water-spraying manifold, Global Finishing Solutions' No Pump Spray Booth uses the highly effective scrubbing action of a water wash to separate paint particles from exhaust air. By ingenious channeling of the paint-laden exhaust air through a "water tunnel" the No Pump system eliminates pumps, piping, filters, manifolds, and nozzles.

## Slide 79
Performance indicators
  Enclosures (Spray Booths)
    Face velocity
    Differential pressure
    Average face velocity and daily inspections
VOC Control Techniques – Capture System
Notes: Performance Indicators for Enclosures
Face velocity – the velocity of air as measured across the open face of the enclosure
    Differential pressure – the pressure drop (delta p) of air as measured across a filter (particulate) used in the enclosure
    Average face velocity and daily inspections

## Slide 80: Baghouse for Powder Coater
Notes: Here are filter banks and cyclones for controlling emissions from a powder coating operation.
Baghouse in this case in really a misnomer.
Note the hoppers for recovering powder.

## Slide 81: REMEMBER Booth is for PM Only NOT VOC’s
Notes: Booths can be very effective at controlling PM overspray.
They have little or no affect on gaseous emissions.

## Slide 82: VOC Control Equipment
Incineration Direct Flame – Thermal Oxidizer Catalytic Oxidizer
Carbon Adsorption
Condensation
Absorption
Notes: BASIC TYPES OF ADD-ON CONTROLS
Incineration Thermal Oxidation -- Direct Flame Catalytic
Regenerative Thermal Oxidizer (RTO)
Carbon Adsorption
Condensation
Absorption
One of the main limitations of thermal oxidizers is the large amount of fuel required to heat the gas stream to the temperature necessary for high-efficiency VOC destruction. Heat exchangers are used to recover some of this heat. The heat exchanger shown in Figure 1 is sometimes called a recuperative heat exchanger. This type of heat exchanger has a heat recovery efficiency ranging from 30 to 60% depending on the size of the unit. Some types of thermal oxidizers use large regenerative beds for heat exchange. These beds have heat recovery efficiencies up to 95%. Due to the amount of heat that can be recovered and returned to the inlet gas stream, these units, termed regenerative thermal oxidizers (RTOs) require less fuel to maintain the combustion chamber at the necessary temperature.
TQ 22

## Slide 83: Catalytic Oxidizer
Notes: Here is a typical installation of a Catalytic Oxidizer.
One of the disadvantages of a catalytic oxidizer is its weight.
Because of its weight most have to be installed on the ground and not on the roof closer to the process line. This means much more duct work and bigger fans.

## Slide 84: Regenerative TO - RTO
Notes: Heat Exchange Media is usually a ceramic material
Ceramic Material absorbs heat from the exhaust gas
THEN Preheats the incoming process gas stream
Due to the amount of heat that can be recovered and returned to the inlet gas stream, these units, termed regenerative thermal oxidizers (RTOs) require less fuel to maintain the combustion chamber at the necessary temperature.
Process gas with VOC contaminants enters the Four Bed RTO through an inlet manifold. A flow control valve directs this gas into an energy recovery chamber which preheats the process stream. The process gas and contaminants are progressively heated in the stoneware bed as they move toward the combustion chamber.
The VOCs are then oxidized, releasing energy in the second stoneware bed, thereby reducing any auxiliary fuel requirement. The stoneware bed is heated and the gas is cooled so that the outlet gas temperature is only slightly higher than the inlet temperature. The flow control valve switches and alternates the stoneware beds so each is in inlet and outlet mode. If the process gas contains enough VOCs, the energy released from their combustion allows self-sustained operation. For example, at 95% thermal energy recovery, the outlet temperature may be only 77° (25°) higher than the inlet process gas temperature.
Cost effective on large scale, 24 hr. operations only. You buy 3 building sized control devices so one is always preheating the next while the 3rd is absorbing emissions. A computer is required to turn the valves in time to optimize the thermodynamics. There’s a car plant in Lansing Michigan that saves a lot of natural gas with one of these.
TQ 22

## Slide 85: Poll Questions 7 & 8
Notes: What is the assumed capture efficiency for a permanent total enclosure (PTE)?
  90%
  81%
  100%
  99%
Spray booths are effective at controlling VOC emissions?
  True
  False

## Slide 86: MACT Case Study Video
Notes: 9 minutes

## Slide 87: Applicable Rules
Nuisance
Visible Emissions
Prohibitory & NSR
HAPS
Permits
Fugitive Dust (PM)
Notes: Automotive & MP coating operations are regulated based on:
VOC emissions (precursor to Ozone)
HAP emissions
Permit could include, booths, ovens, voc limits, TE, VOC controls, record keeping requirements, coating usage, cleaning equip.
TQ 3

## Slide 88
Notes: Let’s Talk about Federal regulations.

## Slide 89: Why NESHAP’s
Hazardous Air Pollutants (HAPs)
Toxic Air Contaminants (TACs)
Chromium
Cadmium
Lead
Manganese
Notes: WHY NESHAPS?
CAA Amendments of 1970 required EPA to identify and list HAPS
> Original List of 118 HAPS
> Systematic development of NESHAPS
National Emission Standards for Hazardous Air Pollutants
(In California we had legal impetuous to identify and list TACs
such as >> Chromium
>> Cadmium
>> Lead
>> Manganese)

## Slide 90: NESHAPS Misc. Metal Parts
A Major Source If More than 10 tons per year of any ONE Hazardous Air Pollutant or 25 tpy or more of any COMBINED HAPs
The Operator Will be Subject to Maximum Achievable Control Technology (MACT)
40 CFR Part 63 MMMM for Misc. Metal Parts
Notes: Major Source
  > 10 tons per year of any HAP, or
    > 25 tpy combined HAPs
Owner/Operator subject to MACT requirements
40 CFR Part 63 Subpart MMMM
Surface Coating of Misc. Metal Parts & Products

## Slide 91: NESHAPS Misc. Metal Parts
General 1.9
High Performance 27.5
Magnet Wire 0.44
Rubber-to-Metal 6.8
Fluoropolymer 12.4
* also written in terms of kg HAP per liter of coating solids
This is for new sources, existing usually have higher allowances
lb. HAP / gal solids*
Coating
Notes: TQ 20
COATING EMISSION LIMITS
(lb organic HAP emitted / gal coating solids*)
Coating Subcategory Existing Sources New & Reconstructed
General Use 2.6 1.9
High Performance 27.5 27.5
Magnet Wire 1.0 0.44
Rubber-to-Metal 37.7 6.8
Extreme Performance 12.4 12.4
Fluoropolymer
(Teflon, etc.)
Manufacturers should be able to provide affected sources with this information. Or, this will need to be determined with Performance Testing.
NOTE: Emission Limits are in terms of weight of HAP per gal of solids.

## Slide 92: 6 HHHHHH Rule Video
Notes: 20 minutes

## Slide 93: NESHAPS: Paint Stripping and Misc. Surface Coating Ops at Area Sources
40 CFR 63 Subpart HHHHHH
Initial Notification by Jan. 10, 2010 for Existing Sources
Jan. 9, 2008 for New Sources
Exclusions (Military, labs, etc.)
Notes: 40 CFR 63 Subpart HHHHHH
Initial Notification by Jan. 10, 2010 for Existing Sources
Jan. 9, 2008 for New Sources
Exclusions (Military, labs, etc.)

## Slide 94: HAPS Affected
Chromium
Lead
Manganese
Nickel
Methylene Chloride
Notes: Chromium
Lead
Manganese
Nickel
Methylene Chloride (an organic compound)
Metals that must be reported for initial recordkeeping.
TQ 15

## Slide 95: HHHHHH Rule Provisions
Motor Vehicle and Misc. Surface Coatings
Train/Certify ALL Painters
Spray Booth Requirements
  98% Capture Efficiency
  Enclosures - Auto Complete
Notes: HHHHHH Rule Provisions
Train/Certify ALL Painters
Spray Booth Requirements
  98% Capture Efficiency
  Enclosures - Auto Complete
TQ 15

## Slide 96: More on Training
Painters must be certified as completing training in proper spray application of surface coatings, setup and maintenance of spray equipment
Except students of accredited surface coating training program who are under the direct supervision of an instructor who is certified
Notes: TRAINING
Painters must be certified as completing training in proper spray application of surface coatings, setup and maintenance of spray equipment
  Except students of accredited surface coating training program who are under the direct supervision of an instructor who is certified

## Slide 97
Training program must include:
  Spray gun equipment selection, set up, and operation
  Best spray technique for different types of coatings to improve transfer efficiency and minimize overspray
  Routine booth and filter maintenance, filter selection and installation
  Compliance with requirements of the NESHAP
More on Training
Notes: Training program must include:
  Spray gun equipment selection, set up, and operation
  (measuring viscosity; selecting proper tip or nozzle; proper spray pattern, air pressure and volume, and fluid delivery rate)
  Best spray technique for different types of coatings to improve transfer efficiency and minimize overspray
  (spray gun distance and angle to the part; proper banding and overlap; reducing lead and lag spraying)
  Routine booth and filter maintenance, filter selection and installation
  Compliance with requirements of the NESHAP

## Slide 98: More on Training
Owner or operator must certify training of each person was completed
Certification must include:
  List of personnel who are required to be trained, with name and job description
  Hands-on and classroom instruction, covering elements of training program at a minimum
  Description of methods used at completion of initial or refresher training to demonstrate successful completion
Notes: Owner or operator must certify training of each person was completed
Certification must include:
  List of personnel who are required to be trained, with name and job description
  Hands-on and classroom instruction, covering elements of training program at a minimum
  Description of methods used at completion of initial or refresher training to demonstrate successful completion

## Slide 99: More on Booths
Spray Booths and Prep Stations
  Booths and prep stations for complete motor vehicles or mobile equipment must
    Have full roof and four walls or side curtains, and operate at negative pressure;
    OR
    If sealed doors/openings + automatic pressure balancing system, booth operated at up to, but no more than, 0.05 inches w.c.g. positive pressure
Notes: Spray Booths and Prep Stations
  Booths and prep stations for complete motor vehicles or mobile equipment must:
    Have full roof and four walls or side curtains, and operate at negative pressure;
    OR
    If sealed doors/openings + automatic pressure balancing system, booth operated at up to, but no more than, 0.05 inches w.c.g. positive pressure

## Slide 100: More on Booths
Spray Booths or Prep Stations
  Booths or prep stations for miscellaneous coating or vehicle sub-assemblies
    Have full roof, at least 3 complete walls or side curtains, and ventilated so air is drawn into the booth
    Roof and walls may have openings for conveyors
Notes: Spray Booths or Prep Stations
  Booths or prep stations for miscellaneous coating or vehicle sub-assemblies
    Have full roof, at least 3 complete walls or side curtains, and ventilated so air is drawn into the booth
    Roof and walls may have openings for conveyors

## Slide 101: Recordkeeping
Surface Coating
  Painter training certification
  Documentation of filter efficiency
  Copies of all notifications and reports required
  Records of any deviations from requirements in the rule, including date and time period it occurred, a description of deviation, and corrective actions taken
  If spray gun does not meet definition of acceptable technologies and has cup capacity at least 3.0 oz., documentation from spray gun manufacturer that Administrator has determined equivalent transfer efficiency
Notes: Surface Coating
  Painter training certification
  Documentation of filter efficiency
  Copies of all notifications and reports required
  Records of any deviations from requirements in the rule, including date and time period it occurred, a description of deviation, and corrective actions taken
  If spray gun does not meet definition of acceptable technologies and has cup capacity at least 3.0 oz., documentation from spray gun manufacturer that Administrator has determined equivalent transfer efficiency

## Slide 102: Possible SIP Automotive Req’ts
Prohibition of Non-Compliant Coatings
Prohibition of Specification
Reactive Organic Compound (ROC) Content Must be Listed on Either the Container or Product Spec. Sheet
All ROC Stored in Sealed Containers
Operator Must Maintain all Records Necessary to Determine Compliance
Specialty Coatings May Not Exceed 840 gm/ltr or 5% of Monthly Usage
Notes: Prohibition of Non-Compliant Coatings
Prohibition of Specification
Reactive Organic Compound (ROC) Content Must be Listed on Either the Container or Product Spec. Sheet
All ROC Stored in Sealed Containers
Operator Must Maintain all Records Necessary to Determine Compliance
Specialty Coatings May Not Exceed 840 grams/liter
or 5% of Monthly Usage

## Slide 103: Possible SIP Automotive Requirements
        Coatings Must be Applied Using
        High-Volume Low-Pressure
        HVLP) Equipment
OR
Agency Prohibitory Rules May Require Best Available Control Technology
Notes: HVLP application equipment is required.
(Some Districts in California may have more stringent BACT requirements.)

## Slide 104: Possible SIP Automotive Req’ts
All Coating Application Usually in a Permitted Spray Booth
Notes: Primer due to high solids could be used outside a spray booth.
How does the HHHHHH actually address this?

## Slide 105: Poll Questions 9 & 10
Notes: What painters are exempt from the training certification requirement in Subpart HHHHHH?
  Painters with 20+ years experience
  Painters using HVLP spray guns
  Students of accredited surface coating training programs under the direct supervision of a certified instructor
  Painters using low-HAP coatings
40 CFR 63 Subpart MMMM applies to all of the following EXCEPT?
  Surface coating of miscellaneous metal parts and products
  Major sources of HAP
  Area sources of HAP
  Coating metal products with high performance fluoropolymers such as Teflon

## Slide 106: Inspections
Notes: Let’s talk about INSPECTIONS.

## Slide 107
Obtain Inspection Forms
Permit Review and Check
Safety Equipment Check
Regulation Review
File Review
Meeting at Facility with Representative
Pre-Inspection
Notes: 401.1.1 Review Source File
401.1.2 Review Applicable Rules
401.1.3 Inspection and Safety Equipment Check
respirator, vision protection, hearing protection, safety shoes, hard hat, gloves
401.1.6 Permit Check
Pre-Inspection Requirements
Obtain appropriate inspection forms
Permit review and check
Safety equipment check
Appendix E contains numerous well designed inspection forms.
TQ 25

## Slide 108: Inspection Video
Notes: 5 minutes

## Slide 109
Inspection
Look for
Open Containers
Notes: LOOK FOR OPEN CONTAINERS
Many agencies regulate OPEN CONTAINERS
Why is he saving every color he ever mixed?
(We’re seeing less of this as the color chemistry gets more technical.)

## Slide 110: Open Containers?
Notes: OPEN CONTAINERS
Most regulations require that all containers used for VOC-containing materials be covered when “not in use”.
Closed and/or covered containers should be “leak-free”.

## Slide 111: Good Housekeeping?
Notes: GOOD HOUSEKEEPING
Housekeeping is often an accurate indicator of a sources overall compliance.
Although this isn’t necessarily a violation of any regulation, it might indicate that other problems may exist.

## Slide 112: Speaking of Rags
Notes: Rags from this container were dumped into an outside dumpster that was open.
Inspector suggested they bag the rags before being thrown into the dumpster.

## Slide 113: Booth Inspection
Notes: Is the Permit Posted ??
Many agencies require the permit to be conspicuously placed on or near the permit unit.

## Slide 114: Booth Inspection
Check Filters Intake and Exhaust
Notes: Paint Spray Booths are simple collection devices.
Check filters for operation and maintenance.
Both INTAKE & EXHAUST.
Look at pressure differential, if equipped with magnahelic or manometer gauges.

## Slide 115: Violation?
Notes: Appears to be a Polyester Resin Operation.
Filters appear to be almost totally clogged.
Therefore, capture efficiency may be seriously limited resulting in fugitive emissions from elsewhere in the booth.
If the permit has a pressure drop specification, then that limit may have been exceeded.

## Slide 116: Inspection
Check Filters.
Dirty, Painted or Clogged?
Check Pressure Drop
(∆p) Across Filters
Notes: INSPECTION
Check and record pressure drop across filters
Compare with Permit Limits
Check Filters: Dirty
Painted
Clogged

## Slide 117: Inside the Mixing Room
Notes: Check for Compliant coatings

## Slide 118
Notes: Bypass valve at the top of the funnel allows direct emission while the control device is warming up.
A failure here could mean:
emissions are never ducted to the control device, or
oven is always exhausted to control device, ready or not.
These are no longer standard equipment but may be allowed by the permit engineer especially if there is a worker safety rational.

## Slide 119: Inspection
Automated VOC tracking system
Notes: Computer weighs each component as it is added and directs & corrects proper mixing.
The unused portion is weighed after the job and emissions are automatically calculated.

## Slide 120: Solvents
Used for Cleaning
  Tar
  Prep for Plastic
  Removing Adhesive
Notes: May not require recordkeeping, better TE and some districts may regulate and others don’t. SJVAPCD will be and Sacramento does not.

## Slide 121
Do we need a spray
cap pressure gauge?
Inspection
Notes: Do we need a spray cap pressure gauge here to determine whether this is HVLP?
Not if the inlet pressure is 10 psi or less. If inlet is above 10 psi, only a spray cap pressure gauge can tell us if we’re in compliance.

## Slide 122
Acetone
Reclaim
System
Notes: Acetone is not a VOC and an extremely good solvent.
So, it has seen broad use for cleaning and thinning.
Essentially a distillation system for reclaiming acetone used for cleaning of application equipment.

## Slide 123
SAFETY-KLEEN Spray
Gun Cleaner.
Is this a covered
or open container?
Inspection
Notes: While technically there is no lid here. By convention the three foot head space with the 1/4 inch diameter tubing is accepted as compliant.
One bucket holds clean solvent. Used solvent drains from the sink into the other.
Quick Overview
Model 1077 Paint Spray Gun and Equipment Parts Washer is an economical, safe, and innovative system designed to effectively clean paint spray guns and their related components and equipment. It consists of a cleaning bowl on a stand with two air-operated spigots to clean paint spray gun assemblies or other related equipment.

## Slide 124: How The Gun Cleaner Works
Notes: Quick Overview
Model 1077 Paint Spray Gun and Equipment Parts Washer is an economical, safe, and innovative system designed to effectively clean paint spray guns and their related components and equipment. It consists of a cleaning bowl on a stand with two air-operated spigots to clean paint spray gun assemblies or other related equipment.

## Slide 125: Alternative Cleaning Solutions
Notes: ACETONE – a negligibly photochemically reactive material, but extremely volatile and an fire hazard
UNI-RAM UM80W -- Wall-Mount (in booth) Spray Gun Cleaner
• Water under high pressure flows, at the press of a button, to thoroughly clean the paint passage in less than 30 seconds.
• Outside of the gun is cleaned with the Flow-through Brush and dried with the included Blow Gun.
• Locating the compact UM80WF inside the spray booth saves time because the gun can remain connected to the air line and the painter can remain in the booth; the paint channel is flushed while the paint is still "wet".
• After cleaning, treat dirty water by Flocculation and Filtering to recover clean water for reuse.
• For use with waterborne paints only.

## Slide 126: Recordkeeping Review
Longest Part of the Inspection
Do They Keep Records ?
Check Permit Requirements
Notes: Recordkeeping Review
Probably Most Time-Consuming Part of the Inspection
Do They Keep Records ?
What are Permit Recordkeeping Requirements ?
What are Rule Recordkeeping Requirements ?

## Slide 127: Time for Calculations
What is the VOC content of this coating?
Notes: Most of the VOC Coating Regs are written to prevent meeting VOC limits by just thinning materials and then using more coating to provide for the needed coating thickness.
WORKING INDIVIDUALLY
Given the information on this slide, what is the Rule VOC content of the coating?

## Slide 128
1.1 lbs VOC
= 2.1 lbs/gal
(1 Gal - .24 gal - .24 gal)
Notes: Subtracting the volumes of Exempt VOC and water
(as the Rules require), the Rule VOC content of this coating is
2.1 lbs/gallon.
ANY QUESTIONS?

## Slide 129: Time for Calculations
What is the HAP content of this coating?
Notes: The new HAP Coating Regs have limits written in terms of Weight of HAPS per volume of solids.
Assuming that all of the VOC in this coating is also HAP, and
WORKING INDIVIDUALLY
What is the HAP content in pounds per gallon solids?

## Slide 130
1.1 lbs + 2.9 lbs (voc + exempts)
= 11.1 lbs/gal
.36 gal
Notes: Note that the volume of solids is given.
Adding the weights of VOC and Exempt VOC solvents, and dividing the weight of HAPS by the volume of solids we have
11.1 lbs HAPS/gallon of solids.
In many cases the volume of ingredients is not given.
So >>>>>>>>>>> (go to next slide)

## Slide 131
1.1 lbs + 2.9 lbs (voc + exempts)
= 11.1 lbs/gal
1 – [2.9/(2.9/.24)] – [2.2/(2.2/.24)] – [1.1/(1.1/.16)]
Notes: In such cases only the densities of individual ingredients allows you to calculate the volumes.
Density are readily available in handbooks, etc.
So dividing the weight of an ingredient by its density gives its volume. And the equation reduces to the same one we used before yielding the same answer.
SO – Knowing the density of individual components is the only additional data needed to convert
lbs/gal liquid to lbs/gal of solids
TQ 23

## Slide 132: A Real World Application

## Slide 133: Time for Calculations
Coating VOC = 2.76 lbs/gal
Thinner VOC = 7.27 lbs/gal
Our Operator uses it at 1% Mixture Rate
Notes: SO – Knowing the density of VOC or HAP components is the only additional data needed to convert
lbs/gal liquid to lbs/gal of solids
TQ 23

## Slide 134: Time for Calculations
7.27 X .01 = .0727 lbs/gal VOC @ 1% Mixture Ratio
2.76 lbs/gal x .99 = 2.73 + .0727 = 2.80 lbs/gal

## Slide 135: Websites
nmfrc.org/
epa.gov/stationary-sources-air-pollution/national-emission-standards-hazardous-air-pollutants-neshap-9
epa.gov/collision-repair-campaign
ccar-greenlink.org
paintcenter.org/
Notes: January 2021 – Updated Links
https://www.epa.gov/stationary-sources-air-pollution/national-emission-standards-hazardous-air-pollutants-neshap-9
List of National Emission Standards for Hazardous Air Pollutants (NESHAP)
http://www.nmfrc.org/
National Metal Finishing Resource Center
ccar-greenlink.org -- Coordinating Committee For Automotive Repair is “A Partnership of Industry, Education & Government”.
paintcenter.org is the best all-round website I’ve found to deal with real world problems and questions.
jty/07-Oct-2011

## Slide 136: Questions?
Notes: ANY QUESTIONS BEFORE WE TAKE THE EXAM?