## Slide 1
Ambient Air Monitoring
(AMBM 102)

## Slide 2: Course Overview
Regulations and Standards
Monitoring Networks
Station Siting
Instrumentation
Documentation
Data Handling
Quality Assurance
References and Resources

## Slide 3
Standards and Regulations

## Slide 4: EPA Responsibilities Under CAA
National Ambient Air Quality Standards (NAAQS)
  Identification
  Attainment
Toxic air pollutants
  Identification
  Control
Acid Rain
Pollution Index
PSD

## Slide 5: Monitoring
Attainment
Progress Toward Attainment
Pollution Trends
Emergency Control Procedures
Database

## Slide 6: Regulations
U.S. EPA
  40 CFR 50 - NAAQS
  40 CFR 53 - Methods
  40 CFR 58 - Monitoring criteria
  40 CFR 52.21 – PSD
State and Local Regs
Notes: Test Question #1

## Slide 7: Monitoring Networks
SLAM: State and Local Air Monitoring Station
NAMS: National Air Monitoring Station
PAMS: Photochemical Assessment Monitoring Station
Ncore: National Core Multipollutant Network
Notes: Test Questions
#12-16

## Slide 8: Monitoring Networks
PSD: Prevention of Significant Deterioration
SPM: Special Purpose Monitoring
IMPROVE: Interagency Monitoring of Protected Visual Environments
Near Road NO2
Notes: Test Questions
#12-16

## Slide 9: State and Local Monitoring (SLAMS) Network

## Slide 10: National Air Monitoring (NAMS) Network

## Slide 11: Photochemical Assessment Monitoring (PAMS) Network
Updated 08/24

## Slide 13: NCore Network
Updated 08/24

## Slide 14: NCore Objectives
Timely reporting of air quality data to public
Support for development of emission strategies
Long-term tracking of emission strategies
Long-term health assessment for NAAQS reviews
Establish Attainment/Nonattainment areas
Support for scientific studies in technical, health & atmospheric disciplines
Support to ecosystem assessment

## Slide 15: NCore pollutants

## Slide 16
IMPROVE Sites

## Slide 17
Texas Commission on Environmental Quality 2023 Ambient Monitoring Network

## Slide 18
NATTS Monitors

## Slide 19
Criteria Pollutants

## Slide 20: Current NAAQS
9.0 µg/m3

## Slide 21: Carbon Monoxide(CO) Standards-Table of Historical CO NAAQS
Final Rule/Decision | Primary/ Secondary | Indicator | Averaging Time | Level (2) | Form
1971 36 FR 8186 Apr 30, 1971 | Primary and Secondary | CO (1) | 1-hour period | 35 ppm | Maximum, not to be exceeded more than once in a year
 |  |  | 8-hour period | 9 ppm | Maximum, not to be exceeded more than once in a year (3)
1985 50 FR 37484 Sept 13, 1985 | Primary standards retained, without revision; secondary standards revoked. |  |  |  | 
1994 59 FR 38906 Aug 1, 1994 | Primary standards retained, without revision. |  |  |  | 
2011 76 FR 54294 Aug 31, 2011 | Primary standards retained, without revision. |  |  |  | 

## Slide 22
CO
Current CO Monitoring

## Slide 23: Nitrogen Dioxide (NO2) Standards-Table of Historical NO2 NAAQS
Final Rule/Decision | Primary/ Secondary | Indicator (1) | Averaging Time | Level (2) | Form
1971 36 FR 8186 Apr 30, 1971 | Primary and Secondary | NO2 | Annual | 53 ppb (3) | Annual arithmetic average
1985 50 FR 25532 Jun 19, 1985 | Primary and secondary NO2 standards retained, without revision. |  |  |  | 
1996 61 FR 52852 Oct 8, 1996 | Primary and secondary NO2 standards retained, without revision. |  |  |  | 
2010 75 FR 6474 Feb 9, 2010 (4) | Primary | NO2 | 1-hour | 100 ppb | 98th percentile, averaged over 3 years (5)
 |  | Primary annual NO2 standard retained, without revision. |  |  | 
2018 83 FR 17226 April 8, 2018 | Primary | Primary annual NO2 standard retained, without revision. |  |  | 

## Slide 24
Current NO2 Monitors
Updated 08/24

## Slide 25: Oxides of Sulfur (SO2) Standards-Table of Historical SO2 NAAQS
Final Rule/Decision | Primary/ Secondary | Indicator (1) | Averaging Time | Level (2) | Form
1971 36 FR 8186 Apr 30, 1971 | Primary | SO2 | 24-Hour | 0.14 ppm | Not to be exceeded more than once per year
 |  |  | Annual | 0.03 ppm | Annual arithmetic average
 | Secondary |  | 3-Hour | 0.5 ppm | Not to be exceeded more than once per year
 |  |  | Annual (3) | 0.02 ppm | Annual arithmetic average
1973 38 FR 25678 Sept 14, 1973 | Secondary | Secondary 3-hour SO2 standard retained, without revision; secondary annual SO2 standard revoked. |  |  | 
1996 61 FR 25566 May 22, 1996 | Primary | Existing primary SO2 standards retained, without revision. |  |  | 
2010 75 FR 35520 Jun 22, 2010 (4) | Primary | SO2 | 1-hour | 75 ppb | 99th percentile, averaged over 3 years (5)
 |  | Primary annual and 24-hour SO2 standards revoked. |  |  | 
77 FR 20218 April 3, 2012 | Secondary | Existing secondary SO2 standard (3-hour average) retained, without revision. |  |  | 
84 FR 9866 March 18, 2019 | Primary | Existing primary SO2 standard retained, without revision. |  |  | 

## Slide 26
Current SO2 Monitors

## Slide 27
SO2 Nonattainment Areas

## Slide 28
SO2 Nonattainment Areas (1971 Std)

## Slide 29: Lead (Pb) Standards- Table of Historical Pb NAAQS
Final Rule/Decision | Primary/ Secondary | Indicator | Averaging Time | Level (1) | Form
1978 43 FR 46246 Oct 5, 1978 | Primary and Secondary | Pb-TSP (2) | Calendar Quarter | 1.5 µg/m3 | Not to be exceeded
Feb 21, 1991 – Agency released multimedia “Strategy for Reducing Lead Exposures” (3) |  |  |  |  | 
2008 73 FR 66964 Nov 12, 2008 | Primary and Secondary | Pb-TSP | 3-month period | 0.15 µg/m3 | Not to be exceeded
2016 81 FR 71906 Oct 18, 2016 | Primary and secondary standards retained, without revision. |  |  |  | 

## Slide 30
Pb
Current Lead Monitors
Updated 08/24

## Slide 31
Lead Nonattainment Areas

## Slide 33
Pb

## Slide 34: Ozone (O3) Standards-Table of Historic O3 NAAQS
Final Rule/Decision | Primary/ Secondary |  | Indicator (1) | Averaging Time | Level (2) | Form
1971 36 FR 8186 Apr 30, 1971 | Primary and Secondary |  | Total photochemical oxidants | 1-hour | 0.08 ppm | Not to be exceeded more than one hour per year
1979 44 FR 8202 Feb 8, 1979 | Primary and Secondary |  | O3 | 1-hour | 0.12 ppm | Attainment is defined when the expected number of days per calendar year, with maximum hourly average concentration greater than 0.12 ppm, is equal to or less than 1
1993 58 FR 13008 Mar 9, 1993 | EPA decided that revisions to the standards were not warranted at the time |  |  |  |  | 
1997 62 FR 38856 Jul 18, 1997 | Primary and Secondary | O3 | O3 | 8-hour | 0.08 ppm | Annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years
2008 73 FR 16483 Mar 27, 2008 | Primary and Secondary | O3 | O3 | 8-hour | 0.075 ppm | Annual fourth-highest daily maximum 8-hr concentration, averaged over 3 years

## Slide 36
OZONE Formation

## Slide 37: Ground-Level Ozone

## Slide 39
Current Ozone Monitors
Updated 08/24

## Slide 40
Ozone Nonattainment Areas (2008 Std)
(8 hour, average 4th maximum, 0.75 ppm)

## Slide 41
O3

## Slide 42: Particulate Matter (PM) Standards - Table of Historical PM NAAQS
Final Rule | Primary/ Secondary | Indicator | Averaging Time | Level (1) | Form
1971 36 FR 8186 Apr 30, 1971 | Primary | TSP (2) | 24-hour | 260 µg/m3 | Not to be exceeded more than once per year
 |  |  | Annual | 75 µg/m3 | Annual Average
 | Secondary | TSP | 24-hour | 150 µg/m3 | Not to be exceeded more than once per year
1987 52 FR 24634 Jul 1, 1987 | Primary and Secondary | PM10 | 24-hour | 150 µg/m3 | Not to be exceeded more than once per year on average over a 3-year period
 |  |  | Annual | 50 µg/m3 | Annual arithmetic mean, averaged over 3 years
1997 62 FR 38652 Jul 18, 1997 | Primary and Secondary | PM2.5 | 24-hour | 65 µg/m3 | 98th percentile, averaged over 3 years
 |  |  | Annual | 15.0 µg/m3 | Annual arithmetic mean, averaged over 3 years (3),(4)
 |  | PM10 | 24-hour | 150 µg/m3 | Initially promulgated 99th percentile, averaged over 3 years; when 1997 standards for PM10 were vacated, the form of 1987 standards remained in place (not to be exceeded more than once per year on average over a 3-year period) (5)
 |  |  | Annual | 50 µg/m3 | Annual arithmetic mean, averaged over 3 years
2006 71 FR 61144 Oct 17, 2006 | Primary and Secondary | PM2.5 | 24-hour | 35 µg/m3 | 98th percentile, averaged over 3 years (6)
 |  |  | Annual | 15.0 µg/m3 | Annual arithmetic mean, averaged over 3 years (2), (7)
 |  | PM10 | 24-hour | 150 µg/m3 | Not to be exceeded more than once per year on average over a 3-year period
2012 | Primary | PM2.5 | Annual | 12.0 µg/m3 | Annual arithmetic mean, averaged over 3 years
 |  |  | Annual | 15.0 µg/m3 | Annual arithmetic mean, averaged over 3 years
 | Secondary |  |  |  | 
 | Primary and Secondary |  | 24-hour | 35 µg/m3 | 98th percentile, averaged over 3 years
 | Primary and Secondary | PM10 | 24-hour | 150 µg/m3 | Not to be exceeded more than once per year on average over a 3-year period

## Slide 43: PM Standards Revision in 2024
Final Rule | Primary/ Secondary | Indicator | Averaging Time | Level (1) | Form
89 FR 16202 | Primary | PM2.5 | Annual | 9.0 µg/m3 | Annual arithmetic mean, averaged over 3 years 2, 7
2024 | Secondary PM2.5 standards, and primary and secondary PM10 standards, retained without revision. |  |  |  | 

## Slide 44
Current PM 10 and 2.5 Monitors
Updated 08/24

## Slide 46
PM-10 Nonattainment Areas

## Slide 47
PM-2.5 Nonattainment Areas

## Slide 48
PM-2.5 Nonattainment Areas
For Standards of Different Years

## Slide 51
Siting Criteria

## Slide 52: Network Design Considerations
Concentration Expected
Representative Concentrations
Significant Sources or Source Categories
Notes: 10:00am BREAK

## Slide 53: Network Design Considerations
Background Concentrations
Regional Transport
Welfare-Related Impacts for Rural Areas
Notes: 10:00am BREAK

## Slide 54: Scales of Monitoring
Micro
Middle
Neighborhood

## Slide 55: Micro Scale Site Up to 100 m

## Slide 56: Middle Scale Site 100 m to 0.5 km

## Slide 57: Neighborhood Scale Site 0.5 km to 4 km

## Slide 58: Additional Scales of Monitoring
Urban
Regional
National and Global

## Slide 59: Urban Scale Site 4 km to 50 km

## Slide 60: Regional Scale Site 10s km to 100s km

## Slide 61: National & Global Scale Site
100s to
1,000s km
(On the Scale
of a Nation
or the World as a Whole)

## Slide 62: Monitoring Objectives & Scale
Monitoring Objective
Appropriate Siting Scales
Highest concentration Source impact
Population
General / Background
Micro, middle, neighborhood (sometimes urban)
Micro, middle, neighborhood
Neighborhood, urban
Neighborhood, regional, global

## Slide 64: Network Design Considerations
Priority area (zone of highest pollution conc.)
Air Transport
Evaluation

## Slide 65: Network Design Considerations
Population Areas
Future development
Full Representation

## Slide 66: Number of Stations – PM10
1 Exceeding NAAQS by 20% or more, or 95% Probability of PM10 Nonattainment
2 Exceeding 80% of NAAQS, or 20% to 95% Probability of PM10 Nonattainment
3 Less than 80% NAAQS, or < 20% Probability of PM10 Nonattainment
Population
Expected Maximum Concentration
High1
Medium2
Low3
> 1,000,000
500,000 - 1,000,000
250,000 - 500,000
100,000 - 250,000
6 - 10 4 - 8 2 - 4
4 - 8 2 - 4 1 - 2
3 - 4 1 - 2 0 - 1
1 - 2 0 - 1 0

## Slide 67: Station Siting Considerations
Available sites
Start-up costs
  Equipment
  Facility improvements
Operation costs
  Equipment operation and maintenance
  Station costs (lease payments, heating, etc.)
  Expendables (calibration gases, chart paper, etc.)
  Personnel

## Slide 68: Station Siting Considerations
Types of Pollutants
Topography
Air flow

## Slide 69: Station Categories
A (Ground Level) | Heavy pollutant concentration, high potential for pollutant buildup
B (Ground Level) | Heavy pollutant concentration, minimal potential for buildup
C (Ground Level) | Moderate pollution concentration
D (Ground Level) | Low pollutant concentration
E (Air Mass) | Sampler probe that is between 6-45m (20-150 ft) above ground
F (Source-Oriented) | Sampler that is adjacent to a point source

## Slide 70: Site Information
Local Sources
  Flues & Vents by Inlet
  Non-Vehicular/Local Industry
  Traffic
Dominant Influence Category
  Industrial
  Residential
  Commercial
  Vehicular
  Urbanization
  Near Urban
  Agricultural
  Recreational Area

## Slide 71
Local Sources Near Monitoring Stations

## Slide 72: Site Information
Data Acquisition Objective
Station Type
Spatial Scale
Instrumentation
Sampling System
Influential Pollutant Sources
Topography
Atmospheric Exposure

## Slide 73: Site Information
Obstacles
  Description
  Distance
  Height above inlet
  Walls
  Air flow arc
Trees
  As obstacles
  As interferants

## Slide 74: Obstacle Effects

## Slide 75: Location of Monitors
C = Core site
S = SLAMS site
p = Special Purpose Monitor

## Slide 76
Measurement Process

## Slide 77: Air Pollutant Measurement Process
Separate pollutant from air
Determine pollutant quantity and air volume
Calculate pollution concentration by dividing pollutant quantity by air volume
Analyze data

## Slide 78: Types of Monitoring
Automated analytical methods
  Point analyzers
  Open path analyzers
Time averaged samplers
  Manual methods
  Filter (ex. PM10) samples

## Slide 79: Electromagnetic Spectrum
400 nm
700 nm
Visible Range
Notes: (T.Q. #6)

## Slide 80: Beer-Lambert Law
Absorption of light related to:
  Absorption coefficient dependencies
    Wavelength of light
    Properties of the pollutant molecule
  Number of molecules in light path
    Concentration
    Path length

## Slide 82: Analytical Techniques
Infrared Methods
  Differential Absorption
  Gas Filter Correlation
  Fourier Transform Infrared
Ultraviolet Methods
  Differential Absorption
  Second Derivative Spectroscopy
Visible Light - Opacity Measurement
  Scattering & Absorption
Notes: (T.Q. #7)

## Slide 83: Analytical Techniques
Luminescence Methods
  Fluorescence
  Chemiluminescence
  Flame Photometry
Electroanalytical Methods
  Polarography
  Electrocatalytic
  Paramagnetism
  Conductivity
Notes: T.Q. #7

## Slide 84: Site Information
Site Description
  Ground Cover
  Height of Inlet
  Type of Samplers
  Spacing Between Samplers
  Inlet Boom Description and Orientation
  Meteorological Instrument Tower Description
  Meteorological Instrument Radiation Shield

## Slide 85: Site Information
Probe Information
  Probe Material
  Probe Dimensions
  Manifold Description
  Manifold Dimensions
  Tubing Material
  Tubing Dimensions
  Residence Time
    Probe, Manifold, Tubing, Total

## Slide 86: LUNCH BREAK
Returning at 1pm

## Slide 87
Gas Inlet

## Slide 88
Instrument Manifold

## Slide 89
Instrument Manifold

## Slide 90: Non-Dispersive IR Analyzer

## Slide 91
NOx & CO Analyzer

## Slide 92
Let’s Discuss GFC CO Analyzer

## Slide 93: Gas Filter Correlation Analyzer
Notes: (T.Q. #14)

## Slide 94
Looking Inside a GFC CO Analyzer

## Slide 95: Chemiluminescence NOx Analyzer
Notes: (T.Q. #13)

## Slide 96
Thermo Environmental Chemiluminescence NOx Analyzer

## Slide 97
Typical NOx Analyzer

## Slide 98
Chemiluminescence NOx Analyzer

## Slide 99: Non-Dispersive UV Analyzer

## Slide 100: Fluorescence SO2 Analyzer

## Slide 101
Typical CO & O2 Analyzer

## Slide 102: Calibrations and Zero Air
Pure (zero) air generators
Certified cylinder gases
Dilution calibration systems
Calibration is the process of establishing the relationship between the output of a measurement process and a known input

## Slide 103
Calibration Gases

## Slide 104
Calibration Gases

## Slide 106: Particulate Properties
Collected Mass
Inertial Properties
Particle Size
Optical Density
  Haze and Opacity in the Air
  Density of Collected Deposit

## Slide 107: Measures of Particulate Matter in the Atmosphere
Total Suspended Particles
PM 10
PM 2.5
Aerosols

## Slide 108: Particulate
Total Suspended Particulate (TSP) Samplers
    Lead
PM10 and/or PM2.5 samplers
    Size Selective Inlet
    BAM
    TEOM
Visibility Samplers
    Nephelometer
    Optical Test Tape Sampler

## Slide 109
Size Selective Inlet (SSI) Sampler

## Slide 110: PM10 - Size Selective Inlet (SSI)
Buffer Chamber
Acceleration Nozzle
Impaction Chamber
Vent Tubes
Filter Cassette
Filter
Filter Support Screen
Air Flow
Acceleration Nozzle
Impaction Chamber
Motor Inlet

## Slide 111
Inside SSI Head

## Slide 112
SSI Filter Area

## Slide 113
PM2.5 Sampler

## Slide 115: PM10 Size Selective Inlet
Screen
Upper Plenum
Acceleration Jet
Deflector Cone
Flow to Virtual Impactor
Vent Jet
Ambient Air Flow
Middle Plenum Particles > 10 um
Lower Plenum Particles <10 um

## Slide 117: Virtual Impactor
From Inlet
To Control Module
Coarse Particles >2.5 um
Virtual Impactor Nozzle
Fine Filter Cassette
15.03 LPM
Coarse Filter Cassette
1.67 LPM
PM 10 to 2.5 Coarse Particle Filter
PM 2.5 to 0 Fine Particle Filter
Fine Particles <2.5 um
Virtual Impactor Receiver Tube
Inlet Drift Tube

## Slide 118: EPA-WINS PM2.5 Impactor
PM-10 Aerosol from Inlet
Collection Cup with Antispill Ring
Impaction Filter
Nozzle
T
PM-2.5 Aerosol to Filter
S
W

## Slide 119
Tapered Element Oscillating Microbalance (TEOM) Inlet

## Slide 120: PM10 - TEOM
Flow
To Flow Controller
Microprocessor
Electronic Feedback System
Tapered Element
Filter Cartridge
Flow
Sampling Head
Heated Air Inlet

## Slide 121: PM10-TEOM
PM10 Inlet
Auxiliary Flow Controller
Main Flow Controller
Mass Transducer
TEOM Sensor Unit
Sample Tube
Flow Splitter
Inline Filters
TEOM Filter
Bypass Flow Line
Air Tubes
Bypass Fine Particle Filter Assembly
TEOM Control Unit
Vacuum Pump

## Slide 123
BAM Sampler

## Slide 124
Meteorological Instruments

## Slide 125: Meteorological Instruments
Wind speed
Wind direction
Atmospheric pressure
Temperature
Relative humidity, dew pt
Solar radiation

## Slide 126
Meteorological Instruments

## Slide 127
3D Wind Sensor

## Slide 128
DATA

## Slide 129: Data Handling
Data loggers
  Strip charts
  Computers
  Temporary data storage
  On-line data retrieval

## Slide 130
Data Acquisition System

## Slide 131: Site Survey Data
Quality Assurance Procedures and Plans
Cleaning Schedule
Calibrations
Station Temperature Control
In-Line Filters

## Slide 132: Documentation
Instrument Log
  Stays with Instrument
  Documents Acceptance Tests
  Documents Routine Maintenance
  Documents Repairs
  Documents Calibrations
  Other Instrument Specific Information
    i.e. Location, History, etc.

## Slide 133: Documentation
Station Log
  Stays at Station
  Documents Conditions that may Influence Data
    Nearby Construction
    Changes in Traffic Patterns and Flow
  Documents Alterations of Sampling Train
    Probe and Equipment Changes
  Contains Completed Site Reports

## Slide 134
Typical Monitoring Station

## Slide 135
Quality Assurance

## Slide 136: Quality Assurance
Valid Data
Air Monitoring Network
Data
Quality Assurance Program

## Slide 137: Quality Assurance
Field QA
  Daily and Weekly Zero and Span Checks
  Semi-Annual Multipoint Calibrations
  External Audits
    Agency Audits
    EPA NPAP (National Pollutant
    Audit Program)

## Slide 138: Data Handling
Data review and editing
  Complete data set
  Reviewed for accuracy
  Reviewed for consistency

## Slide 139: Data Handling
Data Processing
  Upload to AQS (formerly AIRS)
  Air Quality Data Actions
    Data Deletion
    Data Correction
    Links Data to Field QA
AIRS

## Slide 140: Station Inspection
Review Siting
Examine Instruments
  Condition, Zero/Spans, Calibration, Audit Results
Examine Gases
  Certification
Review Logs
Evaluate Overall Station Cleanliness and Operation

## Slide 141: California ARB Audit Van

## Slide 142: ARB Audit Van Instrumentation

## Slide 143
Accuracy
&
Precision

## Slide 144: Safety
Compressed Gas Cylinders
Hazardous Gases
Electrical Hazards
Heights

## Slide 146: www.epa.gov/outdoor-air-quality-data

## Slide 147: www.epa.gov/outdoor-air-quality-data

## Slide 151: The future
Greenhouse Gases
Real time Particulate Speciation
Satellite Stations
???????

## Slide 152: The Web
https://www.epa.gov/outdoor-air-quality-data Monitoring data
http://www.airnow.gov
  AQI
https://www.epa.gov/technical-air-pollution-resources
  NAAQS
  Air monitoring regulations and information
https://www.epa.gov/green-book
  Non attainment Areas

## Slide 154
Questions???