## Slide 1
Auto, Metal Parts and Products
TOXC 231

## Slide 2: Course Overview
Ozone and Human Health -- HAPS
General Overview of Coating Ops
Coating Composition & Emissions
Pollution Prevention and Control
Control Devices
Rules & Regulations
Inspections
Calculations

## Slide 3: Why Are We Here?
Alveolar Injury Leading to Pulmonary Inflammation and Permanent Lung Damage
Respiratory Discomfort to Sensitive Populations
$330 Million in Crop Damage Each Year
Damage & Failure of Paints and Rubber Parts
Ozone Causes:
Notes: TQ 14

## Slide 5: Coating Market Segments
OEM Product Coatings
  Automotive
  Marine
  Aircraft
  Metal Containers
  Appliances
  Machinery and Equipment
  Wood Furniture
  Plastics
  Coil
  Overprint
Architectural Paints
  Interior
  Exterior
Special Purpose
  Industrial Maintenance
  Traffic Paint
  Auto Refinish
Miscellaneous
  Roof, Tank, Deck
  Concrete

## Slide 6: Comparison of Automotive vs. Metal Parts
Less Steps
Many Application Types
Booth
Corrosion Resistance
More Steps/Coats
Basically, One Type of Application
Booth or Outdoors
Looks Are Everything

## Slide 7: What Are Metal Parts?
Motor Vehicle Parts
and Accessories
Recreational Vehicles
Heavy Duty Trucks
Railroad Cars
Bicycles and Sporting
Goods
Extruded Aluminum
Structural Components
Medical Equipment
Lawn and Garden
Equipment
Electronic Equipment
Magnet Wire
Steel Drums
Industrial Machinery
Metal Pipes

## Slide 8: What is a Coating?
A thin film of organic material
adhering to a mechanical device to
protect it from corrosion or degradation
by its environment. Consequently
the color and texture of the
surface are also altered.

## Slide 9: What Kinds of Coating?
Topcoat
Undercoat
Primer
Sealer
Surfacer
Notes: TQ 8

## Slide 10
New Car Coating Process
Phosphate Cleaner, Electro Deposition for Corrosion
Primer
White, Black, Silver and Red
Base Coat
Top Coat and Clear Coat
Sealer

## Slide 11: A Coating System
Compatibility Intercoat
Topcoat
Substrate: Metal, Plastic or other
Primer/Sealer/Surfacer
1 to 5 mils each
Powder

## Slide 12: REFINISHING
Refinishing is the coating of vehicles, their exterior parts or components, or mobile equipment, including partial body collision repairs for the purpose of protection or beautification and which is subsequent to the coating applied at the manufacturers’ assembly line.

## Slide 13: Refinish Coating Manufacturers
BASF InMont
DuPont
PPG/Ditzler
Sherwin Williams
Glasurit Sikkens
More than 65,000 Formulations for 13,000 Colors!!

## Slide 14: Special Features of Auto Refinishing
Color Matching
Sun and Weather Exposure
Extreme Aesthetic Standards
No Oven Curing

## Slide 15
Metal
White Primer
Grey Intercoat
Topcoat
Bondo Plastic Putty (dent filler)
Plastic & Fiberglass Body Parts

## Slide 16: Color Matching
Little Full Color Changes

## Slide 17: What’s in a Coating?
Four components of any coating:
Binder aka Resin
Pigment
Solvents
Additives
Notes: TQ 18

## Slide 18: BINDER
Natural or Synthetic Resin
Will Harden on Cue (Evaporation)
Most Often a Plastic

## Slide 19: Common Binders
Nitrocellulose
Acrylics
Alkyds
Polyurethanes
Epoxies

## Slide 20: PIGMENTS
Small Hard Particles added for:
  Color
  Strength
  UV Protection

## Slide 21: SOLVENTS, DILUENTS AND THINNERS
Liquids Added To:
“Dissolve” Binder
Adjust Viscosity
Promote Adherence
Promote Flow
Drying & Curing
Notes: TQ 19

## Slide 22
Reducer

## Slide 23
Thinner

## Slide 26: ADDITIVES
Material Introduced For:
Specific Effect on either
Wet or Dry Film
Less than 5% of total coating mass
May or May Not Evaporate
with solvent
Notes: TQ 16

## Slide 27: Poll Questions 1 & 2

## Slide 28: VOC Control Strategies for Coatings
Use Reduction
• Use of Exempt Solvents
• Use of Water-Borne Products
• Increased Solids Contents
• Increased Transfer Efficiency
Retrofit Control Devices
• Capture and Reuse
• Capture and Destroy
Notes: TQ 24

## Slide 29: Rule Provisions: Automotive Refinishing and Metal Parts
Transfer Efficiency (T.E.) Provision
Spray Booth Requirement (PM)
VOC Coating Content Limits
Open Container Limits
Clean Up
Notes: TQ 12

## Slide 30: Coating Type Formulations
Coating % Organic % Water %Solids*
Solvent
Solvent-Borne ~75 0 ~ 25
High-Solids < 40 0 60 - 80
Waterborne 0 - 20 < 80 50 - 100
Powder Coats 0 - 5 0 > 95
* Solids Include: Binders, Pigments & Additives

## Slide 31: Exempt Solvents*
Vary by Agency Definition
Have a Variety of Human Health Effects
Including Anesthesia and Intoxication
Stratospheric Ozone Depletion
Sometimes Incompatible with Aluminum or Water
*Negligibly Photochemically Reactivity

## Slide 32: Waterborne Coatings
Provide: Solvent Penetration Protection Low VOC Reduced Fire Insurance Easy Clean-up
Require: Careful Surface Prep Temp. & Humidity Control While Curing or Longer Drying Times Stainless Steel Equipment

## Slide 33: Difficulties for Waterborne Metallic Topcoats
Hydrogen Evolution
Flake Orientation (Critical Dry Times)

## Slide 34: Water as a Diluent
x grams of solids
covers area y
x grams of solids
covers area y
Solids
Organic Solvents
Solids
WATER
Co-solvent
Solvents

## Slide 35: Co-Solvent (aka coupling agent)
Solvent that Causes Two Immiscible Liquids to Mix
May Comprise up to 30% of the Liquid in a Waterborne Coating

## Slide 36: Powder Coatings
Thermoplastic or Thermoset
No on-site Color Mixing
Faraday Cage Effect
Baked to Cure
Electrostatic Application or
Fluidized Bed Required
Notes: TQ 1
TQ 7

## Slide 37: Transfer Efficiency (T.E.)
Percentage ratio of the weight of solids
deposited on the substrate to the weight
of solids actually used
Notes: TQ 2

## Slide 38: Transfer Efficiency Variables
Spray Equipment
Shape of Part
Ambient Temperature and Humidity
Air Flow Rate in Spray Booth

## Slide 39: Transfer Efficiency Variables
Coating Chemistry
Painter Training and Experience
Paint Pressure and Air Pressure at Nozzle

## Slide 40
0 20% 30% 40% 50% 60% 70% 80% 90% 100%
HVLP
Airless Electrostatic
Air - Assisted Airless Electrostatic
Air Electrostatic
Air - Assisted Airless
Airless Spray
65%
Percent Transfer Efficiency
Air Spray

## Slide 41: HVLP Transfer Efficiency Saves $$

## Slide 42: Air Spray Video

## Slide 43: HVLP? DeVilbiss Gun
Notes: TQ 11

## Slide 45: HVLP Caps
Air Horn or Wing Port
Hole Size
HVLP
Primer
Conventional Air

## Slide 46
Spray Cap Pressure Gauge

## Slide 47
Digital
Air
Pressure
Readout

## Slide 48
Gun Air Pressure Gauge.
Can this Replace the Spray Cap Pressure Gauge?

## Slide 49: HVLP Gun Manufacturers
SATA High end products with precision engineering and digitally controlled mechanisms.
DeVilbiss Age old industry standard spray gun. A wide range of models.
Sharpe American made, budget price.
Binks Another industry standard gun. Binks guns share a market niche with DeVilbiss.
Accuspray Only gun with a plastic body
Astro Pneumatic guns are modeled after higher priced models above .

## Slide 50: Spray Gun Feed Options
Gravity Feed
Pressure Feed
Suction/Siphon Cup

## Slide 51
Electrostatic Spray Gun
Note: Charging Electrode

## Slide 52: Electrostatic Spray Video

## Slide 53: Powder Coating Gun

## Slide 54: Powder Coatings Video

## Slide 55: Powder Coated Products

## Slide 56: Poll Questions 3 & 4

## Slide 57: Coating Steps and Points of Emission
Abrasive Sanding or Blasting
Surface Clean and Prep
Primer & Topcoat Application
Flash Off -- Drying
Curing
Touch Up
Equipment Clean Up

## Slide 58: Points of VOC Emission
Storage Application Cleanup
Mixing Drying & Prep.
90% of VOC Emissions
Notes: TQ 4

## Slide 59: Surface Preparation
Abrasive Sandblasting
Body Filler (Auto)
Cleaning/Degreasing
Application Acid Etching

## Slide 60: Surface Preparation
Detergent Washing
Sandblasting
Filling and Sanding

## Slide 61: VOC Emissions Automotive

## Slide 62: Curing
The Process in which Paint is Converted from Liquid to Solid

## Slide 63: Curing and Coating Types
Air Drying
Lacquers
Enamels
Powder Coats
High Solids
Waterborne
Notes: TQ 6

## Slide 64: More on Curing - Lacquer
Cures by the Evaporation of the Solvent

## Slide 65: More on Curing - Enamel
Cures by an Irreversible Chemical Reaction Involving Various Components or Atmospheric Water or Oxygen

## Slide 66: Curing Methods
Air dried
Thermoset or Thermocure
Baked Coating > 194oF
Thermoplastic
Radiation
Notes: TQ 5

## Slide 67: Curing Times
Air dried hours
Oven Baked minutes
Epoxy Systems minutes
Ultraviolets (UV) seconds
Electron Beam < 1 second

## Slide 68: Curing Types (cont.) Thermoset/Thermocure
Solid Resins
Heated - melt and flow
Cross-link to form Higher Molecular Weight Solid
Remains Stable After Heating

## Slide 69: Curing Types (cont.) Thermoplastic
A Polymer
Liquid when Heated
Freezes Glassy when Cooled
No Cross-linking
Re-melted, Re-molded, and Recycled
Notes: TQ 21

## Slide 70: Oven Cured Temps

## Slide 71: Automotive Ops Are Special

## Slide 72
Forced Dry or
Accelerated Drying
with heat lamps
Is this a baked cure?
194° F
Regulatory Cutoff

## Slide 73: Poll Questions 5 & 6

## Slide 74: Control Alternative
Rather than Meet VOC Limits a Source May:
• Collect at Least a Required Percent by Weight of Emissions
And • Transport to a Central Device that Reduces Emissions at Least a Required Percent (Total Control = 85%)

## Slide 75
Capture System Schematic

## Slide 76: Booth Design
Air Flow Particulate Collection
Downdraft Water Wash
Sidedraft Dry filter
Hood

## Slide 77: Down Draft Spray Booth

## Slide 78: Water Wash Spray Booth

## Slide 79
Performance indicators
  Enclosures (Spray Booths)
    Face velocity
    Differential pressure
    Average face velocity and daily inspections
VOC Control Techniques – Capture System

## Slide 80: Baghouse for Powder Coater

## Slide 81: REMEMBER Booth is for PM Only NOT VOC’s

## Slide 82: VOC Control Equipment
Incineration Direct Flame – Thermal Oxidizer Catalytic Oxidizer
Carbon Adsorption
Condensation
Absorption
Notes: TQ 22

## Slide 83: Catalytic Oxidizer

## Slide 84: Regenerative TO - RTO
Notes: TQ 22

## Slide 85: Poll Questions 7 & 8

## Slide 86: MACT Case Study Video

## Slide 87: Applicable Rules
Nuisance
Visible Emissions
Prohibitory & NSR
HAPS
Permits
Fugitive Dust (PM)
Notes: TQ 3

## Slide 89: Why NESHAP’s
Hazardous Air Pollutants (HAPs)
Toxic Air Contaminants (TACs)
Chromium
Cadmium
Lead
Manganese

## Slide 90: NESHAPS Misc. Metal Parts
A Major Source If More than 10 tons per year of any ONE Hazardous Air Pollutant or 25 tpy or more of any COMBINED HAPs
The Operator Will be Subject to Maximum Achievable Control Technology (MACT)
40 CFR Part 63 MMMM for Misc. Metal Parts

## Slide 91: NESHAPS Misc. Metal Parts
General 1.9
High Performance 27.5
Magnet Wire 0.44
Rubber-to-Metal 6.8
Fluoropolymer 12.4
* also written in terms of kg HAP per liter of coating solids
This is for new sources, existing usually have higher allowances
lb. HAP / gal solids*
Coating
Notes: TQ 20

## Slide 92: 6 HHHHHH Rule Video

## Slide 93: NESHAPS: Paint Stripping and Misc. Surface Coating Ops at Area Sources
40 CFR 63 Subpart HHHHHH
Initial Notification by Jan. 10, 2010 for Existing Sources
Jan. 9, 2008 for New Sources
Exclusions (Military, labs, etc.)

## Slide 94: HAPS Affected
Chromium
Lead
Manganese
Nickel
Methylene Chloride
Notes: TQ 15

## Slide 95: HHHHHH Rule Provisions
Motor Vehicle and Misc. Surface Coatings
Train/Certify ALL Painters
Spray Booth Requirements
  98% Capture Efficiency
  Enclosures - Auto Complete
Notes: TQ 15

## Slide 96: More on Training
Painters must be certified as completing training in proper spray application of surface coatings, setup and maintenance of spray equipment
Except students of accredited surface coating training program who are under the direct supervision of an instructor who is certified

## Slide 97
Training program must include:
  Spray gun equipment selection, set up, and operation
  Best spray technique for different types of coatings to improve transfer efficiency and minimize overspray
  Routine booth and filter maintenance, filter selection and installation
  Compliance with requirements of the NESHAP
More on Training

## Slide 98: More on Training
Owner or operator must certify training of each person was completed
Certification must include:
  List of personnel who are required to be trained, with name and job description
  Hands-on and classroom instruction, covering elements of training program at a minimum
  Description of methods used at completion of initial or refresher training to demonstrate successful completion

## Slide 99: More on Booths
Spray Booths and Prep Stations
  Booths and prep stations for complete motor vehicles or mobile equipment must
    Have full roof and four walls or side curtains, and operate at negative pressure;
    OR
    If sealed doors/openings + automatic pressure balancing system, booth operated at up to, but no more than, 0.05 inches w.c.g. positive pressure

## Slide 100: More on Booths
Spray Booths or Prep Stations
  Booths or prep stations for miscellaneous coating or vehicle sub-assemblies
    Have full roof, at least 3 complete walls or side curtains, and ventilated so air is drawn into the booth
    Roof and walls may have openings for conveyors

## Slide 101: Recordkeeping
Surface Coating
  Painter training certification
  Documentation of filter efficiency
  Copies of all notifications and reports required
  Records of any deviations from requirements in the rule, including date and time period it occurred, a description of deviation, and corrective actions taken
  If spray gun does not meet definition of acceptable technologies and has cup capacity at least 3.0 oz., documentation from spray gun manufacturer that Administrator has determined equivalent transfer efficiency

## Slide 102: Possible SIP Automotive Req’ts
Prohibition of Non-Compliant Coatings
Prohibition of Specification
Reactive Organic Compound (ROC) Content Must be Listed on Either the Container or Product Spec. Sheet
All ROC Stored in Sealed Containers
Operator Must Maintain all Records Necessary to Determine Compliance
Specialty Coatings May Not Exceed 840 gm/ltr or 5% of Monthly Usage

## Slide 103: Possible SIP Automotive Requirements
        Coatings Must be Applied Using
        High-Volume Low-Pressure
        HVLP) Equipment
OR
Agency Prohibitory Rules May Require Best Available Control Technology

## Slide 104: Possible SIP Automotive Req’ts
All Coating Application Usually in a Permitted Spray Booth

## Slide 105: Poll Questions 9 & 10

## Slide 106: Inspections

## Slide 107
Obtain Inspection Forms
Permit Review and Check
Safety Equipment Check
Regulation Review
File Review
Meeting at Facility with Representative
Pre-Inspection
Notes: TQ 25

## Slide 108: Inspection Video

## Slide 109
Inspection
Look for
Open Containers

## Slide 110: Open Containers?

## Slide 111: Good Housekeeping?

## Slide 112: Speaking of Rags

## Slide 113: Booth Inspection

## Slide 114: Booth Inspection
Check Filters Intake and Exhaust

## Slide 115: Violation?

## Slide 116: Inspection
Check Filters.
Dirty, Painted or Clogged?
Check Pressure Drop
(∆p) Across Filters

## Slide 117: Inside the Mixing Room

## Slide 119: Inspection
Automated VOC tracking system

## Slide 120: Solvents
Used for Cleaning
  Tar
  Prep for Plastic
  Removing Adhesive

## Slide 121
Do we need a spray
cap pressure gauge?
Inspection

## Slide 122
Acetone
Reclaim
System

## Slide 123
SAFETY-KLEEN Spray
Gun Cleaner.
Is this a covered
or open container?
Inspection

## Slide 124: How The Gun Cleaner Works

## Slide 125: Alternative Cleaning Solutions

## Slide 126: Recordkeeping Review
Longest Part of the Inspection
Do They Keep Records ?
Check Permit Requirements

## Slide 127: Time for Calculations
What is the VOC content of this coating?

## Slide 128
1.1 lbs VOC
= 2.1 lbs/gal
(1 Gal - .24 gal - .24 gal)

## Slide 129: Time for Calculations
What is the HAP content of this coating?

## Slide 130
1.1 lbs + 2.9 lbs (voc + exempts)
= 11.1 lbs/gal
.36 gal

## Slide 131
1.1 lbs + 2.9 lbs (voc + exempts)
= 11.1 lbs/gal
1 – [2.9/(2.9/.24)] – [2.2/(2.2/.24)] – [1.1/(1.1/.16)]
Notes: TQ 23

## Slide 132: A Real World Application

## Slide 133: Time for Calculations
Coating VOC = 2.76 lbs/gal
Thinner VOC = 7.27 lbs/gal
Our Operator uses it at 1% Mixture Rate
Notes: TQ 23

## Slide 134: Time for Calculations
7.27 X .01 = .0727 lbs/gal VOC @ 1% Mixture Ratio
2.76 lbs/gal x .99 = 2.73 + .0727 = 2.80 lbs/gal

## Slide 135: Websites
nmfrc.org/
epa.gov/stationary-sources-air-pollution/national-emission-standards-hazardous-air-pollutants-neshap-9
epa.gov/collision-repair-campaign
ccar-greenlink.org
paintcenter.org/

## Slide 136: Questions?