## Slide 1: Health & Safety for the Agency Inspector
Chapter 1: Introduction
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 1: Introduction Housekeeping
Please Complete Pre-Test by Noon Today
https://forms.office.com/g/7Rz0kUn0ES
Schedule for 1/27 and 1/28:
  9:00 AM – 11:30 AM Session 1 (w/ 15-minute break)
  11:30 AM – 12:30 PM Lunch Break
  12:30 PM – 3:00 PM Session 1 (w/ 15-minute break)
  All times PST

## Slide 3: Chapter 1: Introduction Disclaimer
This course presents safety procedures for inspecting and evaluating sources of air pollution. While it is based on Air Knowledge NACT 446: Inspection Procedures & Safety, this course was not sanctioned, reviewed, or approved by U.S. Environmental Protection Agency (EPA).
It is much better.

## Slide 4: Chapter 1: Introduction Disclaimer
The information presented is only intended to provide a generic, non-exhaustive overview of OSHA requirements for specific standards-related topics.
This training does not include requirements for posting information, warning signs, and qualifications for people assigned to test workplace conditions or equipment.
States with their own OSHA-approved state plan may differ from Federal OSHA requirements; consult state regulations.
This training is for informational purposes only and should not be used to replace professional advice.
Your safety is your responsibility.

## Slide 5: Chapter 1: Introduction Topics
Course Topics
Introduction
Health & Safety Requirements
Climbing / Fall Hazards
Crushing / Striking Hazards
Electrical / Fire Hazards
Temperature Hazards
Toxic Chemical Hazards
Other Hazards
Inspection Preparation (Flowcharts)

## Slide 6: Chapter 1: Introduction Objective
To better develop the skills to recognize and avoid chemical, physical, and biological hazards
Hazard Identification
Common Health and Safety Programs
Personal Protective Equipment (PPE)
We will NOT be covering:
Toxicology
Office Safety (Ergonomics / Bloodborne Pathogens)
First Aid / Cardiopulmonary Resuscitation (CPR) / Automated External Defibrillator (AED)

## Slide 7: Chapter 1: Introduction Definitions
What is a hazard?
Any condition, activity, or source that could, if left uncontrolled, lead to an injury or illness
Hazard vs Danger vs Risk
Hazard: Underlying condition that can potentially cause harm
  Falling from a ladder will hurt / kill you
Danger: Exposure to a hazard causing damage or injury
  Using a ladder exposes you to falling
Risk: Likelihood of the hazard causing damage or injury
  Probability of falling from an unmaintained painted ladder in the rain

## Slide 8: Chapter 1: Introduction Definitions
What doesn’t kill you, makes you stronger.
Except workplace hazards: if they don’t kill you, they can leave you with a lifelong disability.

## Slide 9: Chapter 1: Introduction Hazard Categories
Occupational Hazard Categories | 
Chemical Hazards | Physical Hazards
Corrosives | Cold
Explosive | Confined Spaces
Flammable | Ergonomics
Toxins | Electricity
Biological Hazards | Heat
Allergic Reactions | Noise
Diseases | Radiation
Toxins | Slips / Trips / Falls

## Slide 10: Chapter 1: Introduction Hazard Categories
Common Occupational Hazard Categories | 
Confined Spaces | Inhalation (Toxins)
Electrical | Skin Absorption (Toxins)
Eye | Thermal / Chemical Burn
Fire / Explosion | Thermal Stress
Hearing | Walking / Climbing / Hoisting

## Slide 11: Chapter 1: Introduction Hazard Categories
Common Hazards in Air Pollution Control
Climbing / Falls Crushing / Physical Electrical / Fire
Temperature Toxic Chemicals Other

## Slide 12: Chapter 1: Introduction Accidents
Select accidents involving agency personnel onsite:
Severe chemical burns from a spill
Cornea scratches from high-velocity particles
Thermal burns from hot surfaces / stack testing probes
Slips on wet and oily surfaces
Near-miss from high voltage electrical equipment
Near-miss from internal inspections of control devices NO!
Near-miss from falls due to improper climbing technique
Near-miss from fall due to static electricity buildup on stack testing probe

## Slide 13: Chapter 1: Introduction Hazards
Inhalation:
High air pollutant concentrations can exist in localized areas
Inhalation problems can develop without warning
  Smell is not a good indicator of toxicity
  Oxygen poor environments can cause fainting
  Inhalation of exhaust gases usually involve multiple pollutants

## Slide 14: Chapter 1: Introduction Hazards
Odors
Sensitivity of human nose varies
  Human smell detection range varies from zero (no odor) to parts per trillion (ppt)
  Sensitivity decreases after prolonged exposure (fatigue)
Human nose very sensitive to compounds containing sulfur
  Hydrogen sulfide, SO2, Methyl Mercaptan (natural gas)
Odors are not a reliable indicator of health impacts
  Toxic compounds can exhibit no odor or an odor threshold lower or higher than its recommended exposure level

## Slide 15: Chapter 1: Introduction Hazards
Comparison of Odor Observation Thresholds & Recommended Exposure Limit (REL) |  |  | 
Pollutant | Odor Threshold† | Short-Term REL‡ | Odor indicative of health impacts?
Benzene | 4.68 ppm | 1 ppm | Yes
Chlorine | 0.314 ppm | 0.5 ppm | No
Hydrochloric Acid | 10 ppm | 5 ppm | Yes
Hydrogen Sulfide | 0.00047 ppm | 10 ppm | No
Methanol | 100 ppm | 250 ppm | No
Phosgene | 1.0 ppm | 0.2 ppm | Yes
Propane | Odorless | 1,000 ppm | No
SO2 | 0.47 ppm | 5 ppm | No
† Gregory Leonardos, David Kendall & Nancy Barnard (1969) Odor Threshold Determinations of 53 Odorant Chemicals, Journal of the Air Pollution Control Association
‡ The National Institute for Occupational Safety and Health (NIOSH) recommended exposure limits (RELs) for short-term exposure

## Slide 16: Chapter 1: Introduction Hazards
Burn / Frostbite Hazard:
Thermal burns are due to hot surfaces, hot materials, and hot test equipment
  Combustion exhaust gases make the flues, ducts, and stacks hot
Freezing is due to the presence of cold surfaces or materials
  Refrigerated condensers, cryogenically cooled processes, and chillers

## Slide 17: Chapter 1: Introduction Hazards
Explosion:
Sudden and rapid release of energy with expanding pressure (shock) wave
  50% chance of death at 62 pounds per square inch (PSI)
  Lung damage at 40 PSI
Improper testing procedures, improper use of equipment
  Pressure vessels, fuel storage, combustion sources

## Slide 18: Chapter 1: Introduction Hazards
Slip / Trip / Fall:
Elevated platforms and sampling locations may not have enough room and subject to inclement weather
Unfamiliarity with plant hazards
Processes may use / generate slippery materials
  Oils, tallow, lubricating agents, powdered solids are all slippy (slippery)

## Slide 19: Chapter 1: Introduction Hazards
Heat / Cold Stress:
Internal body temperature rises / falls more than the body can accommodate
  Body cannot lose (too hot) or retain (too cold) heat, causing stress
Proximity to hot / cold processes impacts local atmosphere
Lack of acclimation or protection for hot / cold environments
  Heat exhaustion, heat stroke, and hypothermia

## Slide 20: Chapter 1: Introduction Hazards
High Voltage:
Exposure to large voltages or amperages of electricity
  Releases large amount of energy at contact
Multiple hazards:
  Contact burns, damage to internal organs, and powerful, involuntary muscle contractions

## Slide 21: Chapter 1: Introduction Hazards
Select ISO Hazard Warnings
Biohazard Confined Space Cut Crush Entanglement
High Voltage Hot Surface Laser Radiation Slip

## Slide 22: Chapter 1: Introduction Hazards
Hazard Communication Standard Pictograms
Caution Compressed Gas Corrosive Environmental Explosive
Flammable Oxidizer Toxicity-Acute Toxicity-Chronic

## Slide 23: Chapter 1: Introduction Precautions
Symptoms of Exposure to Hazards:
Headaches Dizziness / Lightheadedness
Loss of Coordination / Confusion
Drowsiness
Difficulty Breathing / Slurred Speech
Heavy Sweating
Shivering
Seizures
Unconsciousness
Sudden Death

## Slide 24: Chapter 1: Introduction Precautions
General Precautions:
Conduct field work with appropriate clothing / PPE
Postpone / reschedule field work if it cannot be done safely
NEVER risk the health and safety of agency or facility personnel
Comply with ALL applicable health and safety requirements
  Agency
  Facility
  Occupational Safety and Health Administration (OSHA)
  Department of Transportation (DOT)

## Slide 25: Chapter 1: Introduction Review
What is a hazard?
  Any condition that could cause injury or illness if uncontrolled
What are common hazards in air pollution control?
  Climbing, falls, crushing, physical, electrical, fire
Why is smell a poor way to detect toxic chemicals?
  Some toxic chemicals have no odor or are toxic before you smell them
What does “danger” mean in safety terms?
  Exposure to a hazard causing damage
What is a symptom that may mean someone have been exposed to a hazard?
  Headache and dizziness

## Slide 26: Chapter 2
Health and Safety Requirements
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 27: Chapter 2: Requirements Safety and Health Agencies
Multiple agencies are responsible for health and safety standards
Federal
State
Municipal (City / County)
Voluntary

## Slide 28: Chapter 2: Requirements Safety and Health Agencies
If you think OSHA is a small town in Wisconsin, you’re in trouble.

## Slide 29: Chapter 2: Requirements Safety and Health Agencies
Occupational Safety and Health Administration (OSHA)
Federal agency ensuring safe and healthy working conditions for employees
  Within the Department of Labor
  Establishes federal safety and health standards in Title 29 of the Code of Federal Regulations
21 states +Puerto Rico are fully delegated by OSHA for workplace safety and health programs
  6 states +Virgin Islands are delegated for municipal / state employees
  In the remaining 23 states (Ohio), OSHA is the responsible agency

## Slide 30: Chapter 2: Requirements OSHA Map

## Slide 31: Chapter 2: Requirements Safety and Health Agencies
Other State Health & Safety Requirements
General Duty Clause: Requirements for safety in workplace
  Employer (facility) has a duty to furnish a safe workplace for employees and frequenters (visitors)
  Employer (facility) shall do everything reasonably necessary to protect the health, safety, and welfare of employees and frequenters (visitors)
Risk Reduction for Public Employees
  State workers’ compensation programs provide medical care and wage replacement for employees injured during work activities
  Programs may incorporate health and safety standards to reduce the number and severity of injuries (reducing program costs)

## Slide 32: Chapter 2: Requirements Safety and Health Agencies
Other State Health & Safety Requirements
State Workers’ Compensation may manage their own health and safety programs
  While not OSHA standards, they may have additional protections and requirements
Examples of additional standards for public employees
  Right of refusal to work if employee believes there is imminent danger
  Reporting of occupational injuries and illnesses
  Posted notices of protections and obligations
  State-specific standards for certain risks

## Slide 33: Chapter 2: Requirements OSHA Health & Safety Standards
Select OSHA Health & Safety Standards:
Walking-Working Surfaces (1910.21-1910.30)
  Ladders and scaffolds
Exit Routes & Emergency Planning (1910.33-1910.39)
Occupational Health & Environmental Control (1910.94-1910.98)
  Occupational Noise Exposure
Hazardous Materials (1910.101-1910.126)
  Hazardous Materials Storage
  Process Safety Management (Counterpart to Risk Management)
  Hazardous Waste Operations and Emergency Response (HAZWOPER)

## Slide 34: Chapter 2: Requirements OSHA Health & Safety Standards
Select OSHA Health & Safety Standards:
Personal Protective Equipment (1910.132-1910.140)
General Environmental Controls (1910.141-1910.147)
  Confined Spaces
  Lockout/Tagout
Electrical (1910.301-1910.399)
Toxic & Hazardous Substances (1910.1000-1910.1499)
  Bloodborne Pathogens
  Hazard Communication
  Laboratory Safety

## Slide 35: Chapter 2: Requirements OSHA Health & Safety Standards
Ladder & Scaffold Standards
Requirements for securing, stability, load bearing, placement and dimensions
  Must include a fall / falling object protection system if exposed to falling / falling object hazard
Applies to:
  Fixed and Portable Ladders
  Catwalks / Runways
  Scaffolds
  Stairs

## Slide 36: Chapter 2: Requirements OSHA Health & Safety Standards
Exit Route Standards
Requirements for designating and maintaining exit routes and assembly points in an emergency
  Part of a comprehensive emergency action plan
Exits routes must be:
  Clearly marked
  Unobstructed
  Well-Lit
Emergency assembly point must be away from potential hazards and clearly marked

## Slide 37: Chapter 2: Requirements OSHA Health & Safety Standards
Occupational Noise Exposure Standards
Permissible Exposure Limit (PEL) for noise
  Hearing conservation program required if exceeded
  85 decibels as an 8-hour time-weighted average (TWA)
Requires:
  Noise monitoring
  Annual audiogram (hearing test)
  Proper hearing protectors (PPE)
  Training and notification

## Slide 38: Chapter 2: Requirements OSHA Health & Safety Standards
Hazardous Materials
Conduct a hazardous chemical inventory and assessment to develop a Hazard Communication Program that includes:
  Labeling with hazard warnings
  Proper storage and handling
  PPE
  Training
  Emergency response and cleanup (HAZWOPER)
Specific requirements for compressed gases, flammable gases and liquids, explosives, and highly hazardous chemicals

## Slide 39: Chapter 2: Requirements OSHA Health & Safety Standards
Process Safety Management (PSM)
Comprehensive plan to prevent and minimize impacts from a catastrophic release of hazardous or flammable chemical(s)
  Process hazard analysis to identify and analyze potential hazards
  Process safety information and operating procedures
  Employee training
  Emergency planning and response
  Internal audits

## Slide 40: Chapter 2: Requirements OSHA Health & Safety Standards
OSHA PSM is counterpart to Environmental Protection Agency (EPA) Risk Management Plan (RMP) [Clean Air Act §112(r)]
OSHA PSM Program: Onsite program for worker safety
EPA RMP Program: Offsite program for public safety

## Slide 41: Chapter 2: Requirements OSHA Health & Safety Standards
HAZWOPER
Applicable to workers who handle hazardous waste and respond to emergencies involving hazardous substances
  PPE
  Procedures
  Training
    Awareness (Level I): 2- hour training to provide emergency notification for a release
    Operations (Level II): 8-hour training for workers with direct involvement
    Technician (Level III): 24-hour training for supporting responders to releases
    Specialist (Level IV): 40-hour training for workers with uncontrolled hazardous waste
    Incident Commander (Level V): Training on incident management

## Slide 42: Chapter 2: Requirements OSHA Health & Safety Standards
PPE
Equipment worn to minimize exposure to hazards
  Reduces risk from contact with biological, chemical, and physical hazards
Program to assess and identify what types of PPE are required
  Training (use, adjustment, donning, and doffing)
  Limitations
  Proper care and maintenance

## Slide 43: Chapter 2: Requirements OSHA Health & Safety Standards
Specialized PPE
Certain industries require additional PPE for specific hazards
  Hairnets / beard nets for food preparation
  Flame retardant clothing for welding / combustible materials
  Full safety goggles (no contact lenses)
  Full face shield for splashes
  Metatarsal protection (+steel tip safety shoes)
  Supplied air respirators
  Chemical resistant clothing / gloves
  High-visibility vests
  Ice traction cleats (Crampons)

## Slide 44: Chapter 2: Requirements OSHA Health & Safety Standards
General Environmental Controls
Confined Spaces: Area large enough for a worker to enter but not designed for continuous occupancy
  Limited or restricted means for entry or exit
  May contain hazardous atmosphere, electrical wires, hot / cold surfaces
  Can trap or asphyxiate personnel
  Tanks, vessels, silos, bins, pits, hoppers, control equipment, ducts, pipelines, etc.
Require specialized training and safety program to enter
Do NOT enter confined spaces!
!

## Slide 45: Chapter 2: Requirements OSHA Health & Safety Standards
General Environmental Controls
Control of Hazardous Energy (Lockout/Tagout): Program to safeguard workers from hazardous energy
  Lockout/Tagout is a device (lock or tag) applied to energy control (switch) to ensure energy cannot be activated (turned on) when employees are present (conducting service / maintenance)
  Hazardous energy includes physical energy (heavy objects), mechanical energy (moving objects), and electrical energy
Require specialized training and safety program to enter
Do NOT enter lockout/tagout areas
!

## Slide 46: Chapter 2: Requirements OSHA Health & Safety Standards
Electrical Systems
Includes design safety standards and safety work practices
  Applies to electrical systems, elevators, fire alarm systems, etc.
Protects workers from electrical hazards by requiring:
  Training
  Safe work practices (grounding)
  Separation distance between energized electrical lines and conducting metal objects

## Slide 47: Chapter 2: Requirements OSHA Health & Safety Standards
Toxic & Hazardous Substances
Bloodborne Pathogens: Standards for workers who may be exposed to blood or other potentially infectious materials
  Exposure Control Plan - Procedures to eliminate or minimize exposure
  Work Practice Controls – Isolate or remove hazards from workplace
  Training and recordkeeping
  Vaccinations and medical consultation for workers potentially exposed to bloodborne pathogens
Requires specialized PPE
Treat ALL bodily fluids as potentially infectious
!

## Slide 48: Chapter 2: Requirements OSHA Health & Safety Standards
Toxic & Hazardous Substances
Hazard Communication: Program for sharing information concerning hazardous chemicals
  Safety Data Sheets (SDS) must be readily available
  Containers must be properly labeled (in addition to solid waste / DOT)
  Training

## Slide 49: Chapter 2: Requirements OSHA Health & Safety Standards
Toxic & Hazardous Substances
Laboratory Safety: Program for reducing risks from exposure to chemicals in a laboratory
  Chemical Hygiene Plan (CHP) establishes safe work practices
  Designated Chemical Hygiene Officer (CHO)
  Medical consultation for employees potentially exposed to chemicals
  Training

## Slide 50: Chapter 2: Requirements Safety and Health Agencies
Department of Transportation (DOT)
Federal agency regulating all interstate transportation (rail, highway, air)
  Safety and environmental requirements apply to the transport of hazardous materials
  Establishes federal safety and health standards in Title 49 of the Code of Federal Regulations
State Public Utilities Commissions are the state agency counterpart to DOT with responsibility for transportation
  Public Utilities Commission of Ohio (PUCO) is responsible for intrastate transportation

## Slide 51: Chapter 2: Requirements DOT Health & Safety Standards
Select DOT Health & Safety Regulations:
Hazardous Materials Regulations (Part 172)
  Transporters must register with DOT
  Containers must be properly labeled and placarded
  Containers must meet standards for safety based on contents
  Shipping papers (bills of lading, manifests) and vehicle placards
  Training

## Slide 52: Chapter 2: Requirements Other Health & Safety Standards
Other Federal / state / municipal agencies may have health and safety requirements within their regulatory scope
Radiological: Nuclear Regulatory Commission (NRC) / International Atomic Energy Association (IAEA)
Environmental Cleanup: U.S. Environmental Protection Agency (EPA)
All Federal Agencies required to setup their own health and safety standards
  OSHA can conduct inspections but cannot issue fines
  U.S. Department of Defense (DoD) uses OSHA and its own Safety and Occupational Health (SOH) standards for military equipment

## Slide 53: Chapter 2: Requirements Other Health & Safety Standards
Other Federal / state / municipal agencies may have health and safety requirements within their regulatory scope
National Codes: States, counties, and municipalities may adopt standards for construction, utilities, and equipment
  Building: Number of egress points, fire sprinkler requirements, etc.
  Mechanical: Ventilation, plumbing, electrical, specific equipment
  Fire Code: Standards to safeguard from fire and explosions
Ohio Department of Commerce is state responsible agency
  Division of Industrial Compliance & State Fire Marshal
Counties / cities may have responsible agencies
  Fire departments and/or building and housing

## Slide 54: Chapter 2: Requirements Occupational Health and Safety Management Systems
Consensus Based Organizations (CBO) Standards
Voluntary initiative for Occupational Health and Safety Management Systems
  Structured approach to managing health and safety
  Identify, assess and control hazards and risks
  May require measurement of performance metrics
  May require continuous improvement
  May require third party audits of Health & Safety Management Systems

## Slide 55: Chapter 2: Requirements Occupational Health and Safety Management Systems
Organizations & Standards
OSHA Voluntary Protection Program (VPP)
International Standards Organization (ISO) 45001
  Replaced ISO 18001 in March 2018
American Chemistry Council (ACC) – Responsible Care®
American National Standards Institute (ANSI) / American Society of Safety Professionals (ASSP) Z10.0
United Nations International Labour Office (ILO)
  Conformance is self-declared (no third-party audits required)

## Slide 56: Chapter 2: Requirements Occupational Health and Safety Management Systems
National Institute for Occupational Safety & Health (NIOSH)
Federal agency within the Centers for Disease Control and Prevention (CDC)
  Evaluates workplace hazards
  Researches and makes recommendations
  Develops training programs
  Used by OSHA to develop new standards

## Slide 57: Chapter 2: Requirements Health and Safety Programs
Health & Safety Plan (HASP)
Written procedures to identify, control, and prevent workplace hazards
  Individual hazard class regulated by OSHA (i.e., lock-out, tag-out); or
  Single site-wide plan (not required by OSHA)
Hazard identification and assessment
Control measures to mitigate hazards
Training by role and/or job class
Emergency preparedness and response
Worker participation for improving plan

## Slide 58: Chapter 2: Requirements Health and Safety Programs
Site Health & Safety Coordinator
Responsible for developing and maintaining HASP
Responsible for training and emergency response
Investigates accidents and near-miss
Responsible for providing and maintaining control measures
Manages medical monitoring program
Inspects employee work areas
  Identify new hazards and improper use of control measures
Summarizes accident, illness, and near-miss information for reports to management and OSHA, DOT, etc.

## Slide 59: Chapter 2: Requirements Health and Safety Programs
Agency Health & Safety Coordinator
Develops health and safety procedures for agency staff
  Defers to site HASP, unless more restrictive (or not available)
  Develops procedures to be used by agency field staff (monitoring, stack testing, inspectors)
Investigates accidents and near-miss involving agency personnel
  May require coordination with onsite Health & Safety Coordinator
Manages staff medical monitoring program
Responsible for providing and maintaining control measures (personal protective equipment)

## Slide 60: Chapter 2: Requirements Health and Safety Programs
Agency HASP:
All agency health and safety program policies
Responsibilities for employees, supervisors, and Health and Safety Coordinator
Required PPE
Required training
Procedures for obtaining PPE, conducting medical monitoring, post-incident medical consultation, accident-illness forms, training, and special equipment / procedures
Disciplinary procedures for violating health and safety program

## Slide 61: Chapter 2: Requirements Health and Safety Programs
Agency HASP:
Hazard recognition and avoidance procedures
  Incorporate all applicable OSHA management programs
Hazard communication program
Procedures for shipping hazardous materials in private vehicles, agency vehicles and commercial carriers
Medical monitoring requirements and records

## Slide 62: Chapter 2: Requirements Health and Safety Programs
Required Training | Requirement | Annual Refresher?
Respirators | 1910.134 | No
Hearing Protectors | 1910.95 | No
Hazardous Waste Operations and Emergency Response | 1910.120 | Yes
Bloodborne Pathogens | 1910.1030 | Yes
Hazard Communication | 1910.1200 | Yes
Laboratory Safety | 1910.1450 | Yes
Confined Space Entry | 1910.146 | No
Electrical Work Practices | 1910.332 | No
Process safety Management | 1910.119 | Yes

## Slide 63: Chapter 2: Requirements Health and Safety Programs
Recommended Training | Annual Refresher?
First Aid | Yes
Cardio-Pulmonary Resuscitation (CPR) | Yes
Defensive Driving | No
Supervisor's Duties and Responsibilities | No
Climbing, Hoisting, Lifting and Roof Safety | No
Shipping of hazardous Materials | No
Use of Chemically Resistant Gloves | No
Fire Extinguisher Uses and Limitations | No
Conflict Management | No
Personal Safety | No

## Slide 64: Chapter 2: Requirements Health and Safety Programs
Agency Required PPE
Safety shoes (steel tip)
Helmet (hard hat)
Safety glasses (prescription)
Ear protection
High visibility vest
Respirator & carrying case
Leather gloves
Natural fiber coveralls
Rainwear
Agency Recommended PPE
Full-face respirator
Self-contained breathing apparatus (SCBA)
Dosimeter (Radiation)
Chemically resistant gloves and shoe coverings
High temperature gloves / shoes
Flame resistant clothing

## Slide 65: Chapter 2: Requirements Health and Safety Programs
Site Provided PPE (if required)
Multi-gas Meter (e.g., O2, toxins)
Powered air purifying respirator
Escape respirator
Fall arrest harnesses or lanyards
Third rail ladder shuttle
Climbing belt
Special clothing
Most sites can provide helmets, safety glasses, hearing protection, and high-visibility vests

## Slide 66: Chapter 2: Requirements Health and Safety Programs
Medical Monitoring Program
Program of medical examinations to detect and monitor potential health effects from exposure to chemical, physical, and biological hazards
  Annual surveillance to establish baseline and detect any changes
  Post-incident (post-exposure) evaluation
Medical examinations must be conducted by qualified healthcare professionals

## Slide 67: Chapter 2: Requirements Health and Safety Programs
Agency Medical Monitoring Program
Lung function test
Vision test
Hearing test
Blood test
Urine test
Electrocardiogram (ECG)
Reflex tests
Chest x-ray
Other requirements for specific chemical exposure

## Slide 68: Chapter 2: Requirements Review
Which federal agency ensures safe working conditions?
  Occupational Safety and Health Administration (OSHA)
Hearing protection is needed if sound is:
  85 decibels or more
What does lockout/tagout do?
  Stop energy sources from being activated
What does the acronym PPE mean?
  Personal Protective Equipment
What is a confined space?
  Area large enough to enter but not designed for continuous habitation

## Slide 69: Chapter 3
Climbing / Fall Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 70: Chapter 3: Climbing / Fall Hazards Overview
Climbing and falling are physical hazards
Climbing / falling from ladders, stairs, scaffolds, or elevated platforms
Slip, trip, and fall hazards
Safe use of harnesses and ropes

## Slide 71: Chapter 3: Climbing / Fall Hazards Overview
Ladder Safety:
A step in the right direction

## Slide 72: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Caged (Fixed)
Portable
Third (Safety) Rail

## Slide 73: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Fixed Ladder
Ladder permanently secured to a structure or equipment
Portable Ladder
Any ladder that is not fixed

## Slide 74: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – All Ladders
Must be of substantial construction and properly maintained
  Cannot support weight • Weak, broken, or bent parts

## Slide 75: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – All Ladders
Ladders must:
Extend 3 feet above landing
Fall protection barrier across opening
Do not incline backwards

## Slide 76: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – Fixed Ladders
Must be offset or have substantial landings ever 30 feet; OR
Must use back guard; OR
Must use safety lines + harness / belt

## Slide 77: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – Portable Ladders
Placed securely (at top and bottom); AND
Suitable base
  Portable ladders are most stable at a 4:1 rise-to-run ratio

## Slide 78: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – Wooden Ladders
Wooden ladders are not to be painted except with a transparent finish
  Allows ladder to be inspected for damage

## Slide 79: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – Weather
Ice and rain can make ladders unsafe
  Fixed Ladder: Iced over with slip and trip hazards
  Portable Ladder: Does not provide safe access (inserted through handrail)

## Slide 80: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Best Practices – Ladders
Personal fall arrest equipment
Not using the top 2 rungs on step ladder
Not using the top 4 rungs on an extension ladder
Keep ladders clean of slippery substances
Tying ladders at the top to equipment

## Slide 81: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Safe Access – Scaffolds
Ladders / stairs provided to access working level of scaffolds
Rungs on scaffolds are NOT ladders

## Slide 82: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Best Practices – Scaffolds
Avoid electrical lines and equipment
Avoid placement above / adjacent to hot or toxic gas vents (stacks)
Avoid placement in moving vehicle areas
Avoid placement below material handling equipment
Avoid severely sloped locations
Avoid spraying, splashing, or dripping chemicals

## Slide 83: Chapter 3: Climbing / Fall Hazards Ladders & Scaffolds
Fatal Accident
Person fell from stepladder, over handrail

## Slide 84: Chapter 3: Climbing / Fall Hazards Elevated Platforms
Elevated Platforms
Fall Prevention: Engineered controls to prevent falls (guardrails)
Fall Arrest: Safety nets or harnesses to stop injury after fall

## Slide 85: Chapter 3: Climbing / Fall Hazards Elevated Platforms
Best Practices – Roof Access
Beware of hidden skylights, holes, roof patches, corroded areas and supports, and slippery sloped surfaces
No person can be alone on a roof
No person can walk outside of the designated walkways (warning lines)
All personnel must leave the roof when weather conditions create potential hazards
Sites must have a rescue plan (site-wide) and may create a “Roof Permit” program

## Slide 86: Chapter 3: Climbing / Fall Hazards Elevated Platforms
Best Practices – Harness
Inspect harness for damage and fit
  Do not use if damaged or worn
  Must fit so all straps are snug
Position back D-ring between shoulder blades
Buckle up legs
Buckle up front of harness
Final adjustments for snug fit
  D-ring must remain in correct position
  No dangling arm or leg straps

## Slide 87: Chapter 3: Climbing / Fall Hazards Elevated Platforms
Best Practices – Ropes
Inspect ropes for burns, cuts, thinning, fraying, or deterioration
  Do not use rope that has been severely twisted or knotted (retains kink)
Only haul to rated capacity of rope
Only use double locking clamps
Tightly secure items
  Use slings for items that cannot be bound or secured
Avoid electrical lines and equipment

## Slide 88: Chapter 3: Climbing / Fall Hazards All Areas
Beware of Slips, Trips, and Falls
Use “three points of contact” when using stairs
Ice / black ice / spilled liquids
Wet and oily material underneath thin layers of dust and fibers
Storage piles
Clothing and items can be caught on protruding equipment
  Watch, clipboard, helmet, hair, necklace, bracelet, glasses, harness

## Slide 89: Chapter 3: Climbing / Fall Hazards All Areas
Slips, Trips, and Falls
While doing facility walk-throughs, is the path clear?
Walking on the snow:
  No ice from compressed snow
  Cannot see obstructions / holes
Walking on the path:
  Ice from compressed snow
  Can see obstructions / holes

## Slide 90: Chapter 3: Climbing / Fall Hazards Slips, Trips, and Falls
Video
Stop the Fall
5 Ways to Prevent Falls
Belt Buckle Rule

## Slide 91: Chapter 3: Climbing / Fall Hazards Review
What is a fixed ladder?
  A ladder permanently secured to a structure
How far must a ladder extend above a landing?
  Minimum of 3 feet
What ratio makes portable ladders most stable?
  4 to 1 (4:1)
Where should you never step on a step ladder?
  Top two rungs
What is required when working on a roof?
  Stay inside designated walkways

## Slide 92: Chapter 4
Crushing / Striking Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 93: Chapter 4: Crushing / Striking Hazards Overview
Crushing (caught-in / caught-between) and striking (struck-by) are physical hazards
Equipment that crushes (presses)
Heavy materials that crush (steel coil)
Trenches can collapse, crushing personnel
Mobile equipment can strike personnel (vehicles, conveyors)
Rotating equipment pull in personnel and crush them (rollers)

## Slide 94: Chapter 4: Crushing / Striking Hazards Overview
No Safety: Know Pain
Know Safety: No Pain

## Slide 95: Chapter 4: Crushing / Striking Hazards Crushing / Caught Between
Body part is caught-between two objects (crushed)
  Machinery with moving parts next to a stationary object
  Mobile sources (vehicles, tow motors, forklifts, conveyors)
  Equipment that moves side-to-side

## Slide 96: Chapter 4: Crushing / Striking Hazards Crushing / Caught Between
Paper Roll: 1-2 tons
Forklift: 4-7 tons
Steel Coil: 5-30 tons

## Slide 97: Chapter 4: Crushing / Striking Hazards Rotating / Caught-In
Body part gets caught-in or entangled by machinery (crushed)
  Machinery with moving parts, rollers, and rotating shafts
  NEVER reach into a moving machine
  NEVER reach around a machine guard or barrier

## Slide 98: Chapter 4: Crushing / Striking Hazards Rotating / Caught-In
Personal Items That Can Become Entangled (Partial List)
Jewelry:
  Watches, rings, necklaces, bracelets
Clothing:
  Neckties, loose clothing, high-visibility vests, gloves
Hair:
  Braids, long hair

## Slide 99: Chapter 4: Crushing / Striking Hazards Trenches / Caught-In
Trench collapse or cave-in will crush personnel in trench
  Trenches <20 feet deep should be constructed with a slope of 0:1 through 1½:1, depending on soil type and length of trench open time; or
  Use of a trench box or shield (if ≥5 feet depth) to prevent trench sides from collapsing

## Slide 100: Chapter 4: Crushing / Striking Hazards All Areas
Beware of Being “Caught”
Wear high-visibility PPE
Hearing protection dampers awareness
  Trains, conveyors, and other equipment can move silently
Make eye contact with equipment operators; ensure they see you!
  Robot transfer systems do NOT recognize human obstacles
  Lock-out/Tag-out used to secure areas

## Slide 101: Chapter 4: Crushing / Striking Hazards All Areas
Lockout/Tagout
A lock or tag is secured to control hazardous energy, ensuring that it cannot be activated when employees present
  Each person entering lockout/tagout area applies their own lock/tag, to ensure hazardous energy cannot be activated if they are present
Require specialized training
  Sequential steps for controlling hazards
  Relieve any stored / residual energy
  Verify isolation of equipment

## Slide 102: Chapter 4: Crushing / Striking Hazards All Areas
Good Lockout/Tagout
Clasp prevents lowering derailer
Locks for everyone in affected area
Bad Lockout/Tagout
Clasp does not prevent use

## Slide 103: Chapter 4: Crushing / Striking Hazards Review
What does “caught-between” mean?
  Body or body part crushed between objects
What are some items that can entangle workers?
  Jewelry, clothing, and hair
Why should a worker wear high visibility PPE?
  Increase visibility to equipment operators
What should you never do with a moving machine?
  Reach into the machine
What is lockout/tagout?
  The use of a lock or tag to secure the control of hazardous energy

## Slide 104: Chapter 5
Electrical / Fire Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 105: Chapter 5: Electrical / Fire Hazards Overview
Electricity
Causes shocks, burns, and electrocution (death)
Flammable
Materials that can ignite easily, creating fires and causing burns
Explosive
Materials that can cause explosions and generate toxic gases

## Slide 106: Chapter 5: Electrical / Fire Hazards Overview
Do Not Set Yourself on Fire

## Slide 107: Chapter 5: Electrical / Fire Hazards Electricity
Electricity: movement of electrons through a conductive media
Voltage: Difference in electrical potential difference in a circuit
  “Pressure” moving electrons through circuit
Amperage: Rate of electrical flow through a current (amps)
  Conductor: material that easily moves electricity
  Resistor: material that limits electricity movement
  Insulator: material that is insulated from electricity (high resistance)
Wattage: Measure of electrical power (amps × volts)

## Slide 108: Chapter 5: Electrical / Fire Hazards Electricity
Electrical Terms as Water
Voltage = Water Pressure
  Higher voltage, more pushing
Current = Hose Diameter
  Higher current, more room
Resistance = Blockage
  Higher resistance, less flow
Voltage=Pressure
Current=Diameter
Resistance=Blockage

## Slide 109: Chapter 5: Electrical / Fire Hazards Electricity
Electric Circuit: movement of electrons from negative to positive terminals
Closed circuit: continuous path
  Subject to electrical grounding if there is less resistance (amps) through new path (you)
Open circuit: break in path
  Subject to electrical grounding through you if wire is “live” (charged with electrons)

## Slide 110: Chapter 5: Electrical / Fire Hazards Electricity
Ground means a direct connection to Earth (ground)
If you are on the ground and touch a live electrical wire, electricity flows through you (close circuit)
Similar concept to a lightning rod
  Lightning travels through wire and does not damage house

## Slide 111: Chapter 5: Electrical / Fire Hazards Electricity
Grounding Safety
Extra “safety” ground wire: Lower resistance than human body (easier for electrons to travel to ground)
Rubberized mats / gloves: Increase resistance between human body and ground

## Slide 112: Chapter 5: Electrical / Fire Hazards Electricity
Electrical Safety
Grounded outlets / wires
  Additional “safety” grounding wire prevents grounding through you
  Only works if all wires are properly grounded
Circuit Breaker / GFCI
  Opens circuit at a set amperage
    Circuit Breaker 15-60 amps (home) to >2000 amps
    GFCI ~5 milliamps
Safety Mats / PPE
  Increases resistance between wire and ground

## Slide 113: Chapter 5: Electrical / Fire Hazards Electricity
© 2013 Dennis van Zuijlekom

## Slide 114: Chapter 5: Electrical / Fire Hazards Electricity
Common Electric Voltages:
120-volt – Household current (wall plug)
  Computers, printers, lights, household objects
240-volt - Highest household current (special devices)
  Air Conditioner / Heater / Oven & Range / Dryer
277-volt – Industrial / office lighting
  Highway, car dealership, hospital lighting (replaced by LED)
≥480-volt – Large equipment
  Specialty equipment (electrostatic precipitators, ionizing scrubbers) can use between 4,000 and 69,000 volts
  Electrical power lines can range from 115,000 to 765,000 volts

## Slide 115: Chapter 5: Electrical / Fire Hazards Electricity
“Shocking” Awareness
Improperly wired outlets / ungrounded electrical equipment
  Lack of Ground-Fault Circuit Interruption (GFCI)
  Missing path to ground
Contact with power lines
Damaged / improper extension cord

## Slide 116: Chapter 5: Electrical / Fire Hazards Electricity
Beware of Damaged Extension Cords
Abrasion of insulation by sharp edges and corners
Melting of insulation due to contact with hot surfaces
Corrosion of insulation due to contact with corrosive liquids
Frayed connections due to stretching
  Do not use cords to lift small equipment
Melting / heat when using an extension cord below equipment rating (current / amperage too high for cord)

## Slide 117: Chapter 5: Electrical / Fire Hazards Electricity
Beware of Metal and Electricity
Improperly grounded equipment and damaged extension cords can discharge through metal platforms, ladders, or handrails
  Increased risk using metal stairwell / walkway with electrical cords on it
Mobile equipment and ladders can contact power lines
Inspecting electrostatic precipitators (ESP) and ionizing scrubbers requires proximity to electrical equipment
  Transformer-Rectifier sets and rappers are usually located on ESP roof

## Slide 118: Chapter 5: Electrical / Fire Hazards Electricity
Static Electricity: Buildup of electrons on one surface that can discharge into another, grounded surface
Static electricity can occur where any two surfaces touch
  Rubbing a balloon on carpet: balloon pickups extra electrons
  Air or fluid movement through a metal duct or pipe
  Paper or rubber conveyor moving across metal rollers and spools
  Sand or grit blasting metal objects
  Person in rubberized boots walking on a metal floor / platform

## Slide 119: Chapter 5: Electrical / Fire Hazards Electricity
Static Electricity Discharge: Static electricity can form a spark
Spark equalizes electrons between charged object and grounded object, forming electrical circuit
Spark occurs when electrical discharge overcomes the insulating properties of air
  Lightning is an extreme version of a static electricity discharge
Spark can ignite flammable materials
  Combustible dust
  Flammable liquids
Spark can damage electrical equipment

## Slide 120: Chapter 5: Electrical / Fire Hazards Electricity
Beware Static Electricity
Limit charge generation
  Limit flow rate of air or liquid through metal pipe or duct
  Grounding pipes or ducts to charge is dissipated
  Allow relaxation time for filling containers, trucks, railcars, and tanks
Eliminate spark gaps
  Properly use bonding / grounding cables
  Use anti-static materials (wrist-straps, clothing, mats)

## Slide 121: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Fire: Rapid chemical reaction between a fuel and oxidizer
Explosion: Rapid, expansive release of energy that produces damaging pressure waves
  Fire is not required to have an explosion
  Lethal pressure wave: 60 pounds per square inch (psi)

## Slide 122: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Upper Explosive Limit (UEL): Maximum concentration for a flame to propagate (too rich, not enough air)
  Although ignition may not occur if UEL is exceeded, there may not be enough oxygen in an UEL atmosphere to support life
  Leaving UEL atmosphere reduces concentration into flammable range
Lower Explosive Limit (LEL): Minimum concentration for a flame to propagate (too lean, not enough fuel)
  The lower the LEL, the more dangerous the material
  If LEL is exceeded, leave area immediately
Flammable Range:
  Range of flammable gas or vapor in which ignition can occur

## Slide 123: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Lean Fuel
/ Rich Air
Rich Fuel
/ Lean Air

## Slide 124: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Division | Type | Description of Hazardous Location
I | 1 | Flammable gases or vapors may be present during routine operation or maintenance work
 | 2 | Flammable gases or vapors may be present during unusual conditions
II | 1 | Explosive dusts may be present during routine operation or maintenance work
 | 2 | Explosive dusts may be present during unusual conditions
III | 1 | Ignitable fibers may be present during routine operation or maintenance work
 | 2 | Ignitable fibers may be present during unusual conditions

## Slide 125: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Division | Type | Description of Hazardous Location
I | 1 | Flammable gases or vapors: Volatile Organic Compound (VOC) or methane ductwork and control equipment
 | 2 | Flammable gases or vapors: VOC / Methane storage tank or system pressure relief valves
II | 1 | Combustible dusts: Dry particulate matter (PM) control systems (cyclones, baghouses, filters, ESP)
 | 2 | Combustible dusts: Unloading dry materials from storage area
III | 1 | Ignitable fibers (cotton, cloth, synthetic fibers): Dry PM control systems (cyclones, baghouses, filter, ESP)
 | 2 | Ignitable fibers: Unloading or settling

## Slide 126: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Liquid Type | NFPA Class | Flash Point | Boiling Point | OSHA Class
Flammable Liquid | IA | <73°F | <100°F | 1 - 2
 | IB | <73°F | ≥100°F | 2 - 3
 | IC | ≥73°F and <100°F | ≥100°F | 3 - 4
Combustible Liquid | II | ≥100°F and <140°F | ≥100°F | 3 – 4
 | IIIA | ≥140°F and <200°F | ≥100°F | 4
 | IIIB | ≥200°F | ≥100°F | N/A
Liquid Type | OSHA Class | Flash Point | Boiling Point | NFPA Class
Flammable Liquid | 1 | <73.4°F | <95°F | IA
 | 2 | <73.4°F | ≥95°F | IA - IB - IC
 | 3 | ≥73.4°F and <140°F | N/A | IC - II
 | 4 | ≥140°F and <200°F | N/A | IIIA

## Slide 127: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Sampling Flammable Liquids
Use metal sample containers
  Sample container size limits specified by OSHA in 29 CFR 1910.106
Grounding-bonding cables must be attached to the sampling container and source of the flammable liquid
Liquid source (storage vessel or drum) also must be grounded
Site may require specialized (non-conductive) shoes / clothing
Multi-gas Meter for LEL / UEL / O2
Site must provide instructions on emergency and evacuation procedures

## Slide 128: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Baghouses (fabric filters) contain combustible dust
Particle movement creates static electricity
High operating temperatures

## Slide 129: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Storage Tanks may contain flammable and/or compressed materials (liquids / gases)
May be equipped with pressure relief valves (PRV)
Highly toxic / flammable material storage subject may be subject to OSHA PSM and EPA RMP programs

## Slide 130: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Video
Combustible Dust
Safety Pays Off - The Value of Vigilance

## Slide 131: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Fire Safety Storage:
Intrinsically Safe: Components do not generate sufficient energies to cause ignition
  Areas where flammable materials are stored must have an intrinsically safe fan to exhaust vapors
Explosion Safety Storage:
Explosion Proof: Will not rupture due to ignition of gases, vapors, or dusts (exploded materials will not puncture unit)
  Areas where flammable materials are stored must be explosion proof, venting any explosions safely by absorbing debris and dissipating pressure wave (blowout panels)

## Slide 132: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Physical Explosion Hazard

## Slide 133: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Physical Explosion Hazard

## Slide 134: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Fan Disintegration
Fan wheel corrosion
Fan wheel erosion
Fan wheel solids accumulation
Bearing failure (squeal)
Operation in aerodynamically unstable range
Operation at excessive tip speeds

## Slide 135: Chapter 5: Electrical / Fire Hazards Fires & Explosions
Extinguisher Type | For Use On | Extinguishing Material | Interference
A | Rubbish, Paper or Wood | Water | Removes Heat
B | Organic Liquids | Carbon Dioxide | Removes Oxygen
C | Electrical Equipment | Halon | Removes Oxygen
D | Metal Powders | Inert Powders | Removes Oxygen

## Slide 136: Chapter 5: Electrical / Fire Hazards Fires & Explosions
How to use a fire extinguisher:
  Sound the fire alarm or call fire department
  Identify safe evacuation path before approaching fire. Do not allow fire, heat, or smoke to come between you & evacuation path
  Select appropriate type of fire extinguisher
  Discharge the extinguisher within its effective range using the pull, aim, squeeze, sweep (P.A.S.S.) technique
  Back away from an extinguished fire in case it flames up again
  Evacuate immediately if extinguisher is empty and fire is not out
  Evacuate immediately if fire progresses beyond incipient (initial) stage (you need more than one fire extinguisher)

## Slide 137: Chapter 5: Electrical / Fire Hazards Fires & Explosions
In the event of a fire and/or explosion:
Immediately terminate inspection and/or testing activities
Deenergize any electrical equipment (testing)
Follow plant evacuation procedures
Meet at designated assembly point

## Slide 138: Chapter 5: Electrical / Fire Hazards Review
What is voltage?
  Difference in electrical potential (i.e., electrical pressure)
What does a GFCI do?
  Opens unsafe circuits
What is the problem with static electricity?
  Sparks can ignite flammable materials
What is the flammable range?
  Range of gas concentration where fire can occur between LEL and UEL
What does PASS mean in using a fire extinguisher?
  Pull, Aim, Squeeze, Sweep

## Slide 139: Chapter 6
Temperature Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 140: Chapter 6: Temperature Hazards Overview
Variations in temperature can cause injuries
Heat:
  Burns (including sunburn)
  Heat Exhaustion
  Heat Stroke
Cold:
  Frostnip
  Frostbite
  Hypothermia

## Slide 141: Chapter 6: Temperature Hazards Overview
Temperature Safety:
Hot enough to fry an egg
-or-
Penguins wearing parkas

## Slide 142: Chapter 6: Temperature Hazards Heat vs Burn
Heat (Exhaustion/Stroke)
Body temperature becomes higher than normal (>100ºF)
  Symptoms can develop ≥80ºF depending on humidity and temperature (heat index)
Sweat is body’s natural way of cooling itself
  Hydration replaces water
  Electrolytes need replaced, too!
Burn
Skin is exposed to temperature ≥111ºF
  Higher temperatures and longer contact increases burn severity
  Sunburn: low temperature for long time
Inhaling hot gases (smoke, fumes) can burn lung tissue

## Slide 143: Chapter 6: Temperature Hazards Heat Exhaustion / Heat Stroke

## Slide 144: Chapter 6: Temperature Hazards Burns
Burn is a heat injury to the skin or underlying tissue
Heat (Thermal) • Electricity
Radiation (including sun) • Chemicals
Burn Medical Issues:
  Burns that cover >20% of the body may require intravenous fluids
  Burns that cover >30% of the body may be fatal without treatment
  Deeper burns are more severe (destroying more layers of skin)
  Inhaling smoke (or hot gases) burns lung tissue and may contain carbon monoxide (CO)

## Slide 145: Chapter 6: Temperature Hazards Burns
1st Degree Burn
  Burned first (top) layer of skin
  Red and painful
2nd Degree Burn
  Burned first & second layer of skin
  Wet skin / blisters
3rd Degree Burn
  All layers of skin
  Skin is black, white, or red and leathery
4th Degree Burn: Burns into muscle, tendon, and bone
Warning:
Graphic Content of Burns

## Slide 146: Chapter 6: Temperature Hazards Burns
Common Sources of Thermal Burns
Steam and steam lines
Ductwork or metal surfaces of air pollution control equipment (thermal oxidizer, flare)
Furnace or boiler
Hot probes or test port caps during emissions testing
Hot gases from process equipment
Hot solids exiting hoppers
Lasers / infrared lights

## Slide 147: Chapter 6: Temperature Hazards Burns

## Slide 148: Chapter 6: Temperature Hazards Burns

## Slide 149: Chapter 6: Temperature Hazards Burns

## Slide 150: Chapter 6: Temperature Hazards Chemical Burns
Chemical Exposure
Surface Contact: Burns (damage to skin tissue) from exposure to a chemical
  Acids (low pH)
  Bases (high pH) – causes deeper burns
Skin Absorption: Chemical absorbed into the skin, then bloodstream, then circulated through body into target organs
  Chemicals can penetrate skin or enter through wounds
  Phenols and cresols (VOC / HAP) are absorbed into skin
  Hydrofluoric acid both burns and is absorbed into the body

## Slide 151: Chapter 6: Temperature Hazards Heat Prevention
Preventing Heat Exhaustion
Stay hydrated with water and electrolyte solutions
Avoid heat
Light colored, loose-fitting clothing (wicking clothing)
Take frequent breaks in the shade
Preventing Burns
Avoid contact with steam, flames, hot liquids, hot surfaces, and chemicals
Wear flame-resistant clothing (may be required site PPE)
Avoid reaching over or through hot surfaces, pipes, or chemicals

## Slide 152: Chapter 6: Temperature Hazards Cold vs Frostbite
Cold (Hypothermia)
Body temperature becomes lower than normal (<95ºF)
  Symptoms can develop <50ºF especially if windy or wet
  Most likely to develop <32ºF
Frostnip / Frostbite
Skin is exposed to temperature <32ºF
  Lower temperatures and longer contact increases frostbite severity
  Water in skin cells is freezing, rupturing skin cells
Frostbite numbs skin, so you may not know you have it

## Slide 153: Chapter 6: Temperature Hazards Frostbite / Hypothermia

## Slide 154: Chapter 6: Temperature Hazards Frostnip/Frostbite
Frostbite is a cold injury to the skin or underlying tissue
Frostbite Medical Issues:
  Frostnip: redness or pain in skin
  Frostbite affects extremities first: nose, ears, cheeks, chin, fingers, toes
  Frostbite numbs skin, masking symptoms
  Once you have had frostbite, you are more likely to develop it again
  Frostbite can develop into blisters, gangrene (dead tissue), and damage to tendons, muscles, nerves, and bone
  If frostbite affects blood vessels, permanent damage has occurred and amputation may be required

## Slide 155: Chapter 6: Temperature Hazards Frostnip/Frostbite
Frostnip
  Red, purple, or lighter than natural skin tone
  Painful and tingly
Surface Frostbite
  Requires medical treatment
  Pins and needles
  Swelling
  Blisters and peeling
Severe Frostbite
  Requires immediate medical treatment
  Skin turns black (cells died)
  Blood vessels affected
Winky
Warning:
Graphic Content of Frostbite

## Slide 156: Chapter 6: Temperature Hazards Frostnip/Frostbite
Common Sources of Frostnip/Frostbite
Cryogenic lines and equipment
Refrigerated lines and equipment
Windchill below freezing (32ºF)
Wet parts of the body below 50ºF
Medications like beta-blockers can increase risk of frostbite
Poor circulation increases risk of frostbite
Sweat inside gloves / clothing can freeze, causing frostbite
Metal jewelry / watches constrict blood vessels and attract cold

## Slide 157: Chapter 6: Temperature Hazards Frostbite
Frostbite Leads to Amputations
January 13, 2024, Arrowhead Stadium, Kansas City, MO
  Playoff game between the Kansas City Chiefs and Miami Dolphins
  4th coldest game in NFL history (-4ºF temperature; -27ºF windchill)
  Dozens treated at local hospitals for hypothermia and frostbite
  30 patients treated at a burn clinic with ~12 amputations (fingers / toes)
  ESPN.com - https://www.espn.com/nfl/story/_/id/43346375/nfl-chiefs-dolphins-frostbite-amputation-playoffs-wild-card

## Slide 158: Chapter 6: Temperature Hazards Cold Prevention
Preventing Hypothermia
Multiple loose-fitting layers of wool, polyester, or down (avoid cotton)
Inner layer wicking
Outer layer wind- and waterproof
Stay dry
Take frequent breaks
Stay hydrated
Preventing Frostbite
Multiple loose-fitting layers of wool, polyester, or down (avoid cotton)
Inner layer wicking
Outer layer wind- and waterproof
Protect extremities
Use hand / foot warmers
Take frequent breaks

## Slide 159: Chapter 6: Temperature Hazards Cold Prevention
Balaclava
Fits under helmet
Lined Gloves
Moisture wicking
Other
Crampons (ice)
Hand/foot warmer
Wool socks (2)
Outer layer wind/waterproof

## Slide 160: Chapter 6: Temperature Hazards Review
What is a heat-related illness?
  Heat exhaustion and heat stroke
At what internal body temperature does hypothermia begin?
  95ºF and below
Which type of burn goes through all skin layers?
  Third degree burn (and fourth degree burn)
What clothing should be worn in hot conditions?
  Light-colored and loose-fitting
What is a cold injury to skin called?
  Frostnip or frostbite

## Slide 161: Chapter 7
Toxic Chemical Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 162: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Acute Exposure,,,,,,,,,,
Short term exposure (minutes, hours, days) to relatively high levels of contaminant
Acute exposure may result in acute effects, from relatively mild (eye irritation), to extreme (an asthma attack), to fatal
Chronic Exposure,,,,,,,,
Long term (years to lifetime) exposure to relatively low levels of contaminant
Chronic exposure may result in chronic effects (cancer, chronic obstructive pulmonary disease, neurological problems, etc.)

## Slide 163: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Chemicals can enter the body via three major routes:
Absorption (Dermal)
Inhalation
Ingestion

## Slide 164: Chapter 6: Temperature Hazards Overview
Toxic Waste Does Not Give You Superpowers

## Slide 165: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Chemical Exposure
Effects:
  Impacts at initial point of entry in the body (burn, rash)
  Blood circulates toxics throughout body (target organ)
Toxic response to chemical exposure includes:
  Absorption: how much chemical exposed to
  Distribution: how chemical is distributed throughout body
  Metabolism: how quickly your body processes chemical
  Storage: how your body stores chemical
  Elimination: how your body gets rid of chemical

## Slide 166: Chapter 7: Toxic Chemical Hazards Exposure Limits
Occupational Exposure Limit (OEL): Exposure to highest concentration without adverse effect (skin / inhalation)
Different organizations have established exposure limits
  OSHA
    Permissible Exposure Limit (PEL) – approved by Congress
  California Division of Occupational Safety and Health (Cal/OSHA)
    Permissible Exposure Limit (PEL) – approved by State of California
  National Institutes of Occupational Safety and Health (NIOSH)
    Recommended Exposure Limit (REL) – non-enforceable consensus standard
  American Conference of Governmental Industrial Hygienists® (ACGIH®)
    Threshold Limit Value® (TLV®) – non-enforceable consensus standard

## Slide 167: Chapter 7: Toxic Chemical Hazards Comparison of Occupational Exposure Limits
Substance | OSHA PEL 1 | Cal/OSHA PEL 2 | NIOSH REL 3 | ACGIH® TLV® 4
Acetone | 1,000 ppm | 500 ppm | 250 ppm | 250 ppm
Acrolein | 0.1 ppm | 0.1 ppm | 0.1 ppm | 0.05 ppm
Carbon Tetrachloride | 10 ppm | 2 ppm | 2 ppm | 5 ppm
Chlorine | 1 ppm | 0.5 ppm | 0.5 ppm | 0.1 ppm
Hexane | 500 ppm | 50 ppm | 50 ppm | 50 ppm
Mercury | 0.1 mg/m3 | 0.025 mg/m3 | 0.05 mg/m3 | 0.025 mg/m3
Methyl Chloride | 100 ppm | 50 ppm | NDEL5 | 50 ppm
Nitric Acid | 2 ppm | 2 ppm | 2 ppm | 2 ppm
Sulfuric Acid | 1 mg/m3 | 0.1 mg/m3 | 1 mg/m3 | 0.2 mg/m3
1 OSHA PEL from 29 CFR §1910, Subpart Z 2 Cal/OSHA PEL from Title 8, California Code of Regulations (CCR) §5155 3 NIOSH REL from NIOSH Pocket Guide to Chemical Hazards (NPG) 4 ACGIH® TLV® from ACGIH® website / TLVs and BEIs 5 No detectable exposure level |  |  |  | 

## Slide 168: Chapter 7: Toxic Chemical Hazards Exposure Limits
Immediately Dangerous To Life or Health (IDLH) Values: Exposure to concentration that can cause undesirable health outcomes
  Irritation of the eyes / respiratory tract
  Severe irreversible health effects
  Impairment of the ability to escape from exposure environment
  Death
Established by NIOSH
  Ensure worker can escape in the event of respiratory equipment failure
  Maximum level for a highly reliable breathing apparatus
  Still using 1994 values

## Slide 169: Chapter 7: Toxic Chemical Hazards Comparison of Occupational Exposure Limits and ILDH
Substance | OSHA PEL 1 | NIOSH REL 2 | NIOSH ILDH 3
Acetone | 1,000 ppm | 250 ppm | 2,500 ppm
Acrolein | 0.1 ppm | 0.1 ppm | 2 ppm
Carbon Tetrachloride | 10 ppm | 2 ppm | 200 ppm
Chlorine | 1 ppm | 0.5 ppm | 10 ppm
Hexane | 500 ppm | 50 ppm | 1,100 ppm
Mercury | 0.1 mg/m3 | 0.05 mg/m3 | 10 mg/m3
Methyl Chloride | 100 ppm | NDEL4 | 2,000 ppm
Nitric Acid | 2 ppm | 2 ppm | 25 ppm
Sulfuric Acid | 1 mg/m3 | 1 mg/m3 | 15 mg/m3
1 OSHA PEL from 29 CFR §1910, Subpart Z 2 NIOSH REL from NIOSH Pocket Guide to Chemical Hazards (NPG) 3 NIOSH ILDH from Documentation for Immediately Dangerous to Life or Health Concentrations 4 No detectable exposure level |  |  | 

## Slide 170: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Dermal Chemical Exposure
Surface Contact: Burns (damage to skin tissue) from exposure to a chemical
  Acids (low pH)
  Bases (high pH) – causes deeper burns
Skin Absorption: Chemical absorbed into the skin, then bloodstream, then circulated through body into target organs
  Chemicals can penetrate skin or enter through wounds
  Phenols and cresols (VOC / HAP) are absorbed into skin
  Hydrofluoric acid both burns and is absorbed into the body

## Slide 171: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Dermal Chemical Exposure Can Kill
Karen Wetterhahn, Professor of Chemistry, Dartmouth College
  August 14, 1996, spilled several drops of dimethylmecury onto latex-gloved hand
  Latex gloves were recommended precaution at the time
    Subsequent analysis demonstrated that dimethylmercury can permeate latex gloves
  3 months post incident, experienced significant weight loss
  5 months post incident, mercury poisoning including slurred speech and loss of balance
  10 months post incident, descended into vegetative state and removed from life support; pronounced dead June 8, 1997

## Slide 172: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Video
Fatal Exposure

## Slide 173: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Avoiding Dermal Chemical Exposure
Avoid dripping chemicals from overhead pipe bridges, valves, and other sources
Avoid "splatter" areas while walking through industrial facilities

## Slide 174: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Avoiding Dermal Chemical Exposure via Incidental Contact
Chemicals contaminated onto clipboards, notebooks, pens, or pencils
Absorption of chemicals into respirators, gloves, ropes, and other equipment
Rubbing of eyes with contaminated hands
Touching contaminated gloves / clothing when removing
Using the bathroom without washing your hands first

## Slide 175: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Dermal Chemical Exposure while Sampling
Plant personnel should obtain samples under agency direction using established plant safety procedures
  Appropriately sized sample bottle should be used
  Sample bottle mouth should be pointed away from people
  Liquid stream pressure should be minimized
Wear appropriate PPE even if not sampling to minimize injuries due to spray
  Chemically resistant gloves
  Splash goggles and face shield
  Apron / smock / Tyvek®

## Slide 176: Chapter 7: Toxic Chemical Hazards Chemical Exposure

## Slide 177: Chapter 7: Toxic Chemical Hazards Chemical Exposure

## Slide 178: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Inhalation Chemical Exposure
Chemicals in the air are carried into our lungs, where they are distributed via the bloodstream throughout the body
  Carbon Monoxide (CO): Colorless, odorless gas that reduces amount of oxygen that can be transported in blood
  Particulate Matter (PM): Enters blood via lungs, potentially causing:
    Nonfatal heart attacks • Irregular heartbeat • Aggravates asthma
    Decrease in lung function • Premature death for people with heart or lung disease
  Sulfur Dioxide / Nitrogen Oxides: Cause lung irritation (coughing)
  Volatile Organic Compounds (VOC): Hydrocarbons evaporating ≤230ºF
  Hazardous Air Pollutants: VOC / PM that causes serious health effects

## Slide 179: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Preventing Inhalation Chemical Exposure
Respirator: Device designed to protect wearer from breathing harmful substances (PPE)
  AIR PURIFYING
  Half face with cartridges
  Full face with cartridges / canisters
  Powered air purifying
  ATMOSPHERE SUPPLYING
  Cylinder type escape respirator
  Positive pressure, pressure demand
  Self-contained breathing apparatus

## Slide 180: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Oxygen Deficiency: Exposure to atmosphere without enough oxygen (19.5% minimum | 20.9% normal)
  Impaired cognition / coordination
  Increased respiration rate
  Loss of consciousness
  Death
Only atmosphere supplying respirators ensure oxygen
  Purifying respirators do not provide oxygen

## Slide 181: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Respirator Requirements
The need for respiratory protection is determined based on the types of hazards present (chemical concentrations, O2 level)
Site-specific determination if a respirator is required
  “Gut” determination if respirator is required (if you think you need one, wear one)
If wearing a respirator, also equip a multi-gas meter to ensure sufficient oxygen and appropriate chemical levels
  Oxygen level
  LEL / UEL
  Other pollutant(s) (CO, H2S, Methane, SO2, etc.)

## Slide 182: Chapter 7: Toxic Chemical Hazards Respirator Decision Tree
Are there potentially explosive gases, vapors, or aerosols?
Is Lower Explosive Limit (LEL) <10%?
Leave the Area
Immediately
Is there sufficient Oxygen (>19.5%)?
Atmosphere Supplying Respirator
Yes
No
SAR: Supplied-Air Respirator
SCBA: Self-Contained Breathing Apparatus
Is concentration ≥ IDLH: Immediately Dangerous to Life & Health?
Is concentration ≥ 50 × Limit?
Is concentration ≥ 10 × Limit?
Full-Face Air Purifying Respirator
Half-Face Air Purifying Respirator
Is concentration ≥ Limit?
Respirator Optional
Yes
No
No
Yes
Yes
Yes
Yes
Yes
No
No
No
No
Or
Explosive / Flammable Atmosphere Exists

## Slide 183: Chapter 7: Toxic Chemical Hazards Respirator Cartridges
Type of Cartridge | Categories | Color
Acid Gases |  | White
Acid Gases + Organic Vapors |  | Yellow
Acid Gases, Ammonia, and Organic Vapors |  | Brown
Acid Gases, Ammonia, Carbon Monoxide, and Organic Vapors |  | Red
Ammonia + Compounds |  | Green
Cabron Monoxide |  | Blue
Non-Oil Particulates (See Efficiency) | N95, N99, N100 | Teal
Oil Particulates (See Efficiency) | P/R95, P/R99, R100 | Orange
All Particulates (HEPA) | P100 | Purple
Particulates, Oils, and Solid Radioactive Materials (HEPA) | P100 | Magenta
Organic Vapors |  | Black
Chemical, Biological, Radiological, or Nuclear |  | Olive

## Slide 184: Chapter 7: Toxic Chemical Hazards Respirator Cartridges
Respirator Cartridge Notes
Multi-chemical Resistance:
  Both colors as stripes on cartridge
Oil Resistance:
  N - Not resistant to oil (do not use if oil is present)
  R - Resistant to oil (one-time use)
  P - Oil Proof (multiple use)
Particulate Removal Efficiency:
  95% - N95, R95, and P95
  99% - N99, R99, and P99
  99.97% (HEPA) - N100, R100, and P100

## Slide 185: Chapter 7: Toxic Chemical Hazards Respirator Cartridges
Respirator Cartridge Problems
Cartridges must include the following on the label:
  NIOSH Approval Holder (Manufacturer)
  Product part/model number
  Protections/filter series
  NIOSH stamp
  Lot number
Search for approved respirators on Certified Equipment List (CEL): https://wwwn.cdc.gov/niosh-cel/
  NIOSH Approval: TC-84A-???? for respirators

## Slide 186: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Protection Factor = In-Mask Chemical Concentration
Assigned Protection Factors (APF) for Respirators (Fit Test)
  Half-face – 10
  Full-face – 50
  Continuous Supplied Air – 50 (half) and 1,000 (full)
  Self-Contained Breathing Apparatus (SCBA) – 10,000 (full only)
Maximum Use Concentration (MUC)
  Upper limit at which each respirator can provide protection
  APF × OSHA Permissible Exposure Limit (PEL)
  Cannot be used for IDLH conditions

## Slide 187: Chapter 7: Toxic Chemical Hazards Respirator Protection
What value do your use for exposure limit?
  ACGIH TLV / NIOSH REL – consensus standards, more protective
  Cal/OSHA – regulatory standards for California only
  OSHA – national regulatory standards, least protective
Acetone Exposure Limit Example
  OSHA PEL – 1,000 ppm | 10,000 ppm upper limit for half-face
  Cal/OSHA PEL – 500 ppm | 5,000 ppm upper limit for half-face
  NIOSH REL / ACGIH® TLV®– 250 ppm | 2,500 upper limit for half-face
Respirators MUST be accompanied by multi-gas meter to ensure MUC is not exceeded
!

## Slide 188: Chapter 7: Toxic Chemical Hazards Respirator Protection
Symptoms of Chemical Inhalation Exposure
Headache
Dizziness / Lightheadedness
Irritability
Loss of coordination
Drowsiness
Difficult breathing
Presence of chemical odor or taste
Symptoms CAN occur during respirator use
!

## Slide 189: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Requirements
The need for respiratory protection is determined based on the types of hazards present (chemical concentrations, O2 level)
There must be written AGENCY program for using respirators
  Training must be provided by the AGENCY concerning respirator selection, use, and limitations
  The respirators must be routinely cleaned, inspected and disinfected by AGENCY personnel (you)
  Respirators must be properly stored by AGENCY personnel (you)
Agency personnel must comply with site-specific respirator requirements as PPE

## Slide 190: Chapter 7: Toxic Chemical Hazards Respirator Protection
All respirator users must pass a fit test
Each respirator user must have medical screening to determine if he/she is physically able to wear a respirator
The effectiveness of the respirator use program must be evaluated frequently
Only use NIOSH approved respirators and cartridges that are not expired

## Slide 191: Chapter 7: Toxic Chemical Hazards Respirator Protection
Special Requirements for IDLH Conditions
Written safety plan required
Attendant(s) with rescue equipment required while personnel are within IDLH environment
Visual and audible contact must be maintained between attendant(s) and personnel within IDLH environment
Positive pressure, pressure-demand SCBA, or equivalent required for respiratory protection
Do you really need to be in this environment for your job?
NIOSH IDLH Table: https://www.cdc.gov/niosh/idlh/intridl4.html

## Slide 192: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Video
Donning / Doffing a Respirator

## Slide 193: Chapter 7: Toxic Chemical Hazards Respirator Protection
High Temperature Respirator Problems
Heat stress
Increased cardio-pulmonary stress
Sweat-related sealing problems (decrease APF)
Increased demand on portable air (SCBA)
Cold Temperature Respirator Problems
Fogging of face pieces
Low temperature-related sealing problems (decrease APF)
Increased slip hazards due to restricted vision

## Slide 194: Chapter 7: Toxic Chemical Hazards Respirator Protection
Cartridge Breakthrough Time – Select Organic Vapors
  Bromobenzene – 142 minutes
  Butanol – 115 minutes
  m-Xylene – 99 minutes
  Toluene – 94 minutes
  Carbon Tetrachloride – 77 minutes
  Benzene – 73 minutes
  Ethanol – 28 minutes
  Ethyl Chloride – 6 minutes
  Vinyl Chloride – 4 minutes
  Methanol – 0.2 minutes (12 seconds)
  Methyl Chloride – 0.05 minutes (3 seconds)

## Slide 195: Chapter 7: Toxic Chemical Hazards Respirator Protection
Cartridge Breakthrough

## Slide 196: Chapter 7: Toxic Chemical Hazards Respirator Protection
Cartridge Service Life
Change cartridges whenever there is a noticeable odor or taste
Do not use cartridges for more than one day (8 hours)
  Do not reuse cartridges
Use an analyzer to recognize and avoid localized areas of high concentration
Avoid areas with potentially high concentrations

## Slide 197: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Fit Problems
Beards and sideburns
Scars, special dentures
Glasses
Contact lenses

## Slide 198: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Care
Clean in accordance with manufacturer's instructions
  Clean with mild soap in water at <120ºF
  Rinse thoroughly
  Disinfect for at least two minutes
  Rinse thoroughly
  Air Dry

## Slide 199: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Care
Store respirator within conditions prescribed by manufacturer
  Cleaned and dried respirators should be stored in respirator cabinets
  Respirators should be protected during storage in vehicles and during movement through industrial facilities
  Storage in a vehicle can result in very high and very low temperatures
Maintenance
  Routine Inspection
  Component Replacement

## Slide 200: Chapter 7: Toxic Chemical Hazards Respirator Protection
Respirator Fit Testing
Qualitative Fit Testing
  Use isoamyl acetate (banana oil), sodium saccharin, or irritating smoke to ensure fit
Quantitative Fit Testing
  Condensation nuclei
Training on respirator use
Respirator care and maintenance

## Slide 201: Chapter 7: Toxic Chemical Hazards Respirator Protection
Videos
Respirator Maintenance
Respirator Fit Testing

## Slide 202: Chapter 7: Toxic Chemical Hazards Respirator Protection
Example 1: Stack Testing
Leave roof if plume shifts towards you
Measure ZnO and O2 concentration before re-entering roof
Put on half-respirator with P100 cartridge before re-entering roof
Put on emergency respirator when needed

## Slide 203: Chapter 7: Toxic Chemical Hazards Respirator Protection
Example 2: Rapper Check
Wear a positive pressure, pressure demand SCBA
Measure SO2 concentration
Leave the roof if alarm sounds

## Slide 204: Chapter 7: Toxic Chemical Hazards Respirator Protection
Question:
What do you do when there is a toxic gas cloud release?
Go upwind
Go cross-wind
Go downwind
Stand still
Run
Try to stay cross-wind or upwind and follow evacuation plan for facility
Go to muster location and check-in with emergency coordinator

## Slide 205: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Ingestion
Do NOT eat food / drink water in locations where it can become contaminated
  Particulate deposition
  Acid gases
  Solvents
  Toxic chemicals

## Slide 206: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Beware Cross-Contamination
Contamination of PPE (especially respirator cartridges)
Incidental contact (rubbing eyes, touching contaminated surfaces)
Contamination of objects (clipboard, clothing, pen)
Contamination during PPE removal (gloves, Tyvek®)
  Do not wash contaminated materials with other household materials
  What are your agency decontamination procedures?

## Slide 207: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Heaters / Incinerators / Boilers
Thermal burns from hot surfaces and flames
Solid waste incinerator: explosions
  Aerosol cans, gas cylinders
Inhalation hazards from dioxins, furans, & acid gases
Biological hazards from pathogens (medical waste)

## Slide 208: Chapter 7: Toxic Chemical Hazards Chemical Exposure
Over-Reliance on Senses to Detect Dangers
We use our senses to detect dangers, but they do not always include the full risk picture
Natural gas / methane has no smell until mercaptans added
Hydrogen, methanol, and ethanol burn with an invisible flame
Cold desensitizes your nerves, so you may not feel its effects
Decreased oxygen concentration is not detectable by senses
Hot surfaces usually do not look any different
Do NOT just trust only your senses to identify chemical dangers
!

## Slide 209: Chapter 7: Toxic Chemical Hazards Pathogen Exposure
Pathogens: Infectious microorganisms that can cause disease
Engineering and work practice controls used to prevent exposure to pathogens (airborne and bloodborne)
  Protective clothing, including gloves, face shield, and eye protection
  Potential use of masks or supplied-air respirators
  Vaccinations (Hepatitis B)
  Needle-less or shielded needles
  Plastic instead of glass equipment
Pathogen exposure can happen at many facilities
  Crematoriums, laboratories, hospitals, waste incinerators, landfills

## Slide 210: Chapter 7: Toxic Chemical Hazards Review
What is acute exposure?
  Short-term exposure to high levels of a chemical
What are routes of chemical entry into the body?
  Inhalation, ingestion, and skin absorption
What does the acronym IDLH mean?
  Immediately Dangerous to Life or Health
What type of respirator provides air (oxygen)?
  Supplied-air respirator
What are some hazards from incinerators?
  Inhalation, burns, explosions, pathogens

## Slide 211: Chapter 8
Other Hazards
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 212: Chapter 8: Other Hazards Other Hazards
Other Hazards:
Eye and Face Protection
Hearing protection
Driving
Situational Awareness
Exits and Evacuation
Confined Spaces

## Slide 213: Chapter 8: Other Hazards Other Hazards
If PPE does not fit
It’s not PPE

## Slide 214: Chapter 8: Other Hazards Eye and Face Protection
Injury from exposure to flying particles, molten metal, chemicals, potentially infected material (biohazards), or radiation (light)
Workers suffered 18,510 eye injuries in 2020 (~51 per day)
Injuries can result in blindness or decreased vision

## Slide 215: Chapter 8: Other Hazards Eye and Face Protection
Eye and face protection are required when exposed to potential eye hazards
  It is a best practice to just always wear eye protection
Safety glasses must be certified
  American National Standards Institute (ANSI) Z87.1-2020
Certified safety glasses can have several components
  Prescription, welding, ultraviolet (UV) filter, infrared (IR) filter (lasers), visible light filter, splash/droplet use, dust/fine dusts use
All safety glasses must have side shields
  Newer safety glasses have foam to seal with face

## Slide 216: Chapter 8: Other Hazards Eye and Face Protection
Normal Tinted Bifocals Heavy Tint
(Sunglasses)
Prescription Goggles
Face Shield

## Slide 217: Chapter 8: Other Hazards Eye and Face Protection
Contact Lenses
Guidance pre-2005 to not wear contacts near chemicals
  Concern with contact lens trapping chemicals and damaging eye tissue
Some of these restrictions have been mediated
  Do not wear contacts with potential exposure to specific chemicals: isopropyl alcohol, ethyl alcohol, acrylonitrile, methylene chloride, 1,2 dibromo-3-chloropropane, ethylene oxide, and methylene dianiline
Always follow site requirements regarding contact lenses
Always wear recommended eye protection
If any concerns, take out the contacts before entering site
https://www.cdc.gov/niosh/docs/2005-139/pdfs/2005-139.pdf

## Slide 218: Chapter 8: Other Hazards Eye and Face Protection
Eye & Face Hazards from Particulates
Particulate deposits on adjacent surfaces (columns, guide wires, buildings)
Deposits on ground or roof in an area near discharge
Slight visible emissions
Temperature / breeze
Being pelted with particulate

## Slide 219: Chapter 8: Other Hazards Eye and Face Protection
Eye & Face Hazards from Chemical Splashes / Drips
Centrifugal pump seals
Wet scrubber recirculation liquid
Lime slakers and slurry mixing tanks at dry scrubbers and flue gas desulfurization systems
Droplet re-entrainment from wet scrubber stacks
Wet scrubber recirculation liquid sampling taps
Steam, process water, wastewater, chemical transport pipes
Sampling liquid systems

## Slide 220: Chapter 8: Other Hazards Eye and Face Protection
Eye & Face Protection from Chemical Splashes / Drips
Avoid areas with severe droplet spray, drips, or re-entrainment
Wear goggles or safety glasses + full face shield in areas with potential splash hazards
  Wearing a face shield still requires safety glasses underneath
Carry a sterile eye wash bottle to begin irrigation of the eye as soon as possible
  Flush eyes for a minimum of 15 minutes for all chemicals and 30 minutes of alkalis
  Obtain medical assistance for all eye injuries

## Slide 221: Chapter 8: Other Hazards Eye and Face Protection
Chemical Exposure while Sampling
Plant personnel should obtain samples under agency direction using established plant safety procedures
  Appropriately sized sample bottle should be used
  Sample bottle mouth should be pointed away from people
  Liquid stream pressure should be minimized
Wear appropriate PPE even if not sampling to minimize injuries due to spray
  Chemically resistant gloves
  Splash goggles and face shield
  Apron / smock / Tyvek®

## Slide 222: Chapter 8: Other Hazards Radiation Protection
Radiation
Radiation is energy traveling via electromagnetic waves
  Ionizing: particles (alpha & beta) and high frequency electromagnetic radiation (gamma rays & x-rays)
  Non-ionizing: low- to mid-frequency electromagnetic radiation (extremely low frequency to ultraviolet)

## Slide 223: Chapter 8: Other Hazards Radiation Protection
Ionizing Radiation
Ionizing radiation can alter atoms, including in human cells
  Particulate: Alpha (a – Helium nucleus) and Beta (b – electron/positron)
  Electromagnetic: X-rays and Gamma (g) rays
Decay is radioactive materials (radioisotopes) spontaneously releasing ionizing particles (a & b) and gamma (g) rays
  Decay into stable isotopes through “daughter” particles
  Radon222 (gas) → Polonium218 (solid) + a (alpha particle)
Half-life is when half of the radioisotopes have decayed
  Daughter particles may also be radioactive

## Slide 224: Chapter 8: Other Hazards Radiation Protection
Ionizing Radiation Protection
Alpha (a): Easily shielded (skin); extremely dangerous inhaled (respirator)
Beta (b): Easily shielded (Tyvek® suit); extremely dangerous inhaled (respirator)
Gamma (g): Hard to shield (inches of lead); can pass through human body
X-ray: Difficult to shield (lead lined clothing); less penetrating than gamma rays

## Slide 225: Chapter 8: Other Hazards Radiation Protection
Non-ionizing Radiation
Not strong enough to remove an electron from an atom
  Not a significant health risk unless prolonged exposure or high power
  Radio broadcasting, medical imaging, heat therapy
  Causes premature aging (ultraviolet exposure = sunburn), skin cancer, eye damage (cataracts), and burns

## Slide 226: Chapter 8: Other Hazards Radiation Protection
Eye & Face Hazards from Radiation & Lasers
Light Amplification by Stimulated Emission of Radiation (LASER) is an intense and very focused beam of light
Bar code scanners, laser pointers, industrial lasers, measurement equipment, safety equipment
Visible Light
Laser
Infrared

## Slide 227: Chapter 8: Other Hazards Radiation Protection

## Slide 228: Chapter 8: Other Hazards Radiation Protection
Laser Safety – First Line of Defense
Interlocks, enclosures, and keeping out of identified laser area are primary safety measures
Laser Goggles – Last Line of Defense for Eyes
Must be coordinated to specific laser wavelength
  Using the wrong goggle wavelength = no eye protection
Must be displayed with Optical Density and laser wavelength
  Optical Density: amount of light attenuated by the lens
  Match to laser wavelength and power
  Laser beam power can still melt laser goggles

## Slide 229: Chapter 8: Other Hazards Other Hazards

## Slide 230: Chapter 8: Other Hazards Ear Protection
Noise Exposure
Decibel: intensity of sound
  140 dB threshold of pain
  85 dB long term – hearing loss
Loudness: power of sound
  Weighted decibel: dBA
Excessive noise damages cilia lining cochlea part of ear
  Irreversible damage to hearing

## Slide 231: Chapter 8: Other Hazards Ear Protection
Malleable Earplugs
20-33 dB reduction
Fixed Size Earplugs
15-31 dB reduction
Ear Muffs
20-30 dB reduction
Ear protection is ONLY effective if ambient noise is reduced below 85 dB
!

## Slide 232: Chapter 8: Other Hazards Ear Protection
Noise Hazards
Emission test observations on platforms close to steam discharge points
Cutting, milling, and grinding equipment
Sonic horns on fabric filters and electrostatic precipitators
Explosives testing
Presses and stamping
Generators, pumps, motors, and fans

## Slide 233: Chapter 8: Other Hazards Ear Protection
Audiometric Testing
Baseline to establish initial hearing thresholds
Annual re-test to determine if there is hearing loss
  Standard Threshold Shift (STS) is a significant change in hearing

## Slide 234: Chapter 8: Other Hazards Driving
Driving
6.14 million motor vehicle accidents in 2023 (U.S.)
  40,901 people died in motor vehicle accidents in 2023 (U.S.)
In 1891, the Buckeye Gasoline Buggy was involved in the first documented automobile accident in Ohio City – now Cleveland – Ohio

## Slide 235: Chapter 8: Other Hazards Driving
Defensive Driving
Always wear a safety (seat) belt correctly
Maintain safe distance (3-seconds behind front vehicle)
Maintain safe speed (adjust to weather conditions)
Be aware of surroundings (location for sudden stop)
Avoid distractions (cell phone)
Anticipate other drivers’ actions

## Slide 236: Chapter 8: Other Hazards Situational Awareness
Situational Awareness: Knowing what is going on all around to identify critical elements of information and respond
  Identify (Perceive)
  Process (Understand)
  Respond (React)

## Slide 237: Chapter 8: Other Hazards Situational Awareness
1. Identify (Perceive)
Where is your attention focused?
Are you actively identifying overlooked areas?
  Horses wear blinders to limit their field of vision to focus on what is in front of them and reduce peripheral distractions
  What are your blinders during an inspection?

## Slide 238: Chapter 8: Other Hazards Situational Awareness
Video
Attention Test
Used with permission

## Slide 239: Chapter 8: Other Hazards Situational Awareness
2. Process (Understand)
Is the situation identified a hazard?
What are the impacts of the identified hazard?
  Experience is forecasting future actions from present events
Do you need additional information to understand or identify a hazard?

## Slide 240: Chapter 8: Other Hazards Situational Awareness
2. Process (Understand)
Information is ordered into your brain via a schema
You automatically filter out “unnecessary” information
  Judgements are made based on filtered information
Could an accident happen?
How likely is an accident?
Comprehension Errors
Faulty information
New situation
Excessive motivation
Complacency
Overload
Fatigue
Poor communication

## Slide 241: Chapter 8: Other Hazards Situational Awareness
Video
Illusion Test
Used with permission

## Slide 242: Chapter 8: Other Hazards Situational Awareness
3. Respond (React)
How are you going to react?
How are other people reacting to the hazard?
Responses
Communicate the hazard
Try to stay calm in stressful environments
Mitigate the hazard
Leave the hazardous environment

## Slide 243: Chapter 8: Other Hazards Situational Awareness
Repeat
Continue assessing hazards and practicing situational awareness
Situational awareness does not end when you leave site

## Slide 244: Chapter 8: Other Hazards Situational Awareness
Location
Don’t assume continuous cell phone reception
  Cell towers are (still) concentrated in urban areas and near highways
  Download (or print) offline maps
  Let your supervisor/coworker know where you will be and check-in when leaving the facility
  Contact the facility if you are running late (if they know you are coming)
  Ensure you are going to the correct location (use latitude/longitude instead of an address)
Let someone know where you are going!
!

## Slide 245: Chapter 8: Other Hazards Exits & Evacuation
Exit Routes
Every workplace must have a minimum of two (2) separate and unobstructed exits for evacuation
  Small structures can have only one (1) exit but everyone must be able to evacuate safely through that exit
  Not all doors are exits!
Exits must be clearly marked, adequately lit, and free from clutter and flammable furnishings
Emergency Action Plan (EAP): procedures emergency reporting, building evacuation, and accounting for personnel

## Slide 246: Chapter 8: Other Hazards Exits & Evacuation
Evacuation Plan
Exit Signage

## Slide 247: Chapter 8: Other Hazards Exits & Evacuation
Exits – Situational Awareness
As you travel through the facility, identify marked exits to ensure you know the most direct path in case of evacuation
Remember the path you took to get to where you are, so that you can follow that path back out
Request a map or site plan of the facility for walkthrough

## Slide 248: Chapter 8: Other Hazards Exits & Evacuation
Shelter-in-Place
For certain emergencies, it is better to remain indoors
  Severe weather (tornados)
  Release of biological, chemical, or radiological contaminants
May require taping of doors / windows and covering vents

## Slide 249: Chapter 8: Other Hazards Exits & Evacuation
Accounting for Personnel: Sign-in Sheet
Sites should employ a sign-in / sign-out sheet to account for non-site personnel for emergency evacuations
  Make sure you sign-out when you leave!
Do not sign anything that requires you to maintain information as confidential
Do not sign any liability waiver
  If necessary, write “Agency Inspector” on the line

## Slide 250: Chapter 8: Other Hazards Confined Spaces
Confined Spaces:
  Large enough that an employee can enter to perform work;
  Limited / restricted means for entry / exit; and
  Not designed for continuous occupancy.
Must be identified and labelled
Must have a written permit program
Must train workers on hazards and safety procedures
Must have a trained attendant monitoring entrants
Must have rescue provisions and hazard monitors

## Slide 251: Chapter 8: Other Hazards Confined Spaces

## Slide 252: Chapter 8: Other Hazards Confined Spaces
Do NOT Enter Confined Spaces
Not required for onsite inspection
  Agency inspector has not been trained on entering confined spaces
  Agency inspector does not have appropriate PPE
  Agency inspector has not been advised about specific hazards present
  Agency inspector may block egress for workers in an emergency
  Agency inspector may distract the attendant monitoring confined space
  Plant personnel working inside confined space may not be aware of the agency inspector
Do NOT enter confined spaces!
!

## Slide 253: Chapter 8: Other Hazards Confined Spaces
" … the one thing that most frequently turns a single confined space accident into a multiple death catastrophe is an unsuccessful rescue attempt."
Do NOT enter confined spaces!
!
 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Fatalities | 120 | 88 | 112 | 116 | 136 | 144 | 166 | 148

## Slide 254: Chapter 8: Other Hazards Confined Spaces
Internal Floating Roof Tanks
Visually inspect through holes / roof hatches without breaking plane of entry
What if it’s empty and degassed?
  No: Still a confined space
  Limited / restricted means for entry / exit; and
  Not designed for continuous occupancy.

## Slide 255: Chapter 8: Other Hazards Air Pollution Control Devices
Common Hazards with Air Pollution Controls:
Asphyxiants • Toxic gases
High temperature gases • High voltage surfaces
High static charges • Hot, free flowing solids
Hot ash deposits • Hot metal surfaces
Corroded walking surfaces • Restricted Visibility
High dust levels • Explosive dusts
Eye hazards • Chemical splash hazards
Rotating equipment • High noise levels
Restricted walking spaces • Slippery walking surfaces

## Slide 256: Chapter 8: Other Hazards Suggested PPE
Safety glasses with side shields (ANSI Z87.1)
Earplugs and earmuffs
Steel toe safety shoes (ASTM F2412, F2413)
Hard Hat (ANSI Z89.1)
Cellphone
Flashlight (intrinsically safe)
High visibility vest
Gloves (chemically resistant, leather, and disposable)
Eye wash bottle (agency vehicle)
First aid kit (agency vehicle)

## Slide 257: Chapter 8: Other Hazards Optional PPE
Flame retardant clothing (foundry greens)
Tyvek® Suit
Metatarsals (steel toe + top of foot)
Ice traction cleats (crampons)
Respirators, replacement cartridges or canisters
Portable Organic Vapor Analyzers / Multi-gas Meter
Hairnet / Beardnet
Full safety goggles
Laser / welding goggles
Full face shield

## Slide 258: Chapter 8: Other Hazards Review
What are the three types of ionizing radiation?
  Alpha, beta, and gamma
How many exits must a workplace have?
  At least two (except very small structures)
True or False: safety glasses protect the user on all sides
  Generally false; safety goggles are used for protection on all sides
What is situational awareness?
  Knowing what is going on around you
How much distance should be left for the vehicle ahead?
  3 seconds

## Slide 259: Chapter 9
Site Inspections
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 260: Chapter 9: Inspection Preparation Site Safety Requirements
Site Safety
The site representative escorting you through the facility should know health and safety hazards at the site
  Health and Safety Manager
  Environmental Manager
  Maintenance or Engineering
  Plant Manager
  Other
Level of Knowledge
As a visitor, the site is legally responsible for your safety
!

## Slide 261: Chapter 9: Inspection Preparation Site Safety Requirements
Site Safety
Review any special site safety concerns and site-specific PPE
  Site access can be legally denied if you do not conform to reasonable site safety requirements (PPE, training)
  Ask specifically if your PPE is sufficient
  You can always wear more (upgraded) PPE than required
  If wearing contacts, ask if there are any special concerns
  Include list of PPE in inspection report
Do not sign any liability waivers
    Do write your name for evacuation accounting purposes (sign-in)
    Do not forget to sign-out when leaving the facility!

## Slide 262: Chapter 9: Inspection Preparation Site Safety Requirements
Site Safety
Onsite health and safety training
  Company can require attendance at a mandatory health and safety training before allowing access (if reasonable)
  If you need immediate access to the site, consider attending health and safety training annually
PPE
  Sites generally have extra PPE for visitors
  There may be areas excluded if you do not have appropriate PPE
    Metatarsals may be required to approach equipment
    SCBAs or respirators may be required for entry to certain areas

## Slide 263: Chapter 9: Inspection Preparation Site Safety Requirements
Site Safety
Situational Awareness
  Always assess and reassess your situational awareness
  Always know where you are within the facility and the closest exit(s)
  Always stay with site representative (do not go off alone)
  Do not enter confined spaces
  Do not enter any areas that you do not judge as safe

## Slide 264: Inspection Procedures & Safety Conclusion
Andrew D. Shroads, QEP
Director of Special Projects
ashroads@scainc.com
614.887.7227
Any questions?
Comments to improve the course?
Thank you!