## Slide 1: Effect of Title V
Required “continuous” monitoring of many sources
Standard CEM is impractical for most small sources.
No CEM exists for some pollutants
This forced a new approach to monitoring

## Slide 2
Compliance Assurance Monitoring (CAM)
NACT 220

## Slide 3
Pre-CAM MONITORING ALTERNATIVES
Emissions data for some smaller sources limited to occasional "stack tests".
Instrumental CEMs are expensive ==> limited to big sources
Indirect monitoring holds promise, but was unproven.
AQMD/APCD permits required various data recorded that define or imply compliance for non Title V sources.

## Slide 4
CONCEPTS BEHIND CAM
If the emissions control system is working properly, there is "reasonable assurance of compliance".
Monitoring the control system is more practical than monitoring emissions - e.g. instruments for temperature, flow, volts, etc. are much cheaper and more reliable than CEM systems.  FLEXIBILITY
So - relate control system indicators to compliance.
Many sources with no active emission controls can be monitored in other ways.

## Slide 5: CAM Background
CAA Origins: Titles V & VII
Promulgated 10/22/97
Codified in CFR, Part 64
Regulation implementing the Title V monitoring principle:
  Implement monitoring for a reasonable assurance of compliance

## Slide 6: CAM Presentation Overview
Background
Some New Concepts
Part 64 (CAM) applicability
Exemptions
CAM Monitoring Design Criteria
Source, District, and EPA Roles
Quality Improvement Plan

## Slide 7: CAM Background
CAA Origins: Titles V & VII
Promulgated 10/22/97
Codified in CFR, Part 64
Regulation implementing the Title V monitoring principle:
  Implement monitoring for a reasonable assurance of compliance

## Slide 8: Enhanced Monitoring Rule History
1990 - CAAA requires EPA to publish monitoring rules for major sources
1992 - EPA proposes Enhanced Monitoring rules
  CEMS based
  All major sources subject
1995 - EPA changes direction
  Reasonable assurance of compliance
  Focus on add-on control devices

## Slide 9
Part 64 (CAM) design principles…
Requires source owners to design monitoring to fit site and incorporate into permits

## Slide 10: CAM Background
Targets facilities with add-on control devices
"assure that control measures...are properly operated and maintained so that they do not deteriorate to the point where the owner/operator fails to remain in compliance...“
"long-term, significant loss of control efficiency that can occur without complete failure of a control device"

## Slide 11: Purpose of CAM
Intended to provide a “reasonable assurance of compliance" with applicable requirements for large emission units with add-on controls
Monitoring is conducted to determine that control measures are properly operated & maintained

## Slide 12
Part 64 (CAM) design principles
Monitoring sufficient to also ensure operators pay the same level of attention to pollution control measures as to production activities.

## Slide 13
What are CAM design criteria?
Build on current requirements and practices:
Select representative control device operational parameters (e.g., temperature, flow, pressure drop, electrical voltages, component concentration);

## Slide 14: What are CAM design criteria?
Establish indicator ranges for reasonable assurance of compliance
  Accounting for site-specific factors such as margin of compliance, emissions control variability, correlation with emissions,
  Relying on design information, historical data, similar sources, test data; and
Establish data collection method and averaging time.

## Slide 15: CAM Monitoring
Documenting continued operation of add-on controls within ranges of specified indicators of performance
Indicating excursions from ranges
Correcting of excursions

## Slide 16: Who will be affected by CAM (§64.2)
An emission unit (except some backup utility power emission units) &
With an emission limit or standard
With a control device &
With pre-control emissions greater than major source thresholds &
At a major source subject to title V permitting

## Slide 17
Part 64 applicability examples Major source threshold = 100 t/y

## Slide 18
YES
YES
NO
NO
Part 64 applicability examples Major source threshold = 100 t/y

## Slide 19
Pollutant Specific Emissions Unit (PSEU)
Pre-control Potential to Emit
Excursion
Exceedances
Some New Concepts

## Slide 20
Pollutant Specific Emissions Unit (PSEU)
Pre-control Potential to Emit
Excursion
Exceedances
Some New Concepts
Handout #2

## Slide 21: Defining Excursions & Exceedances
Exceedance – condition detected by monitoring (in units of pollutant emissions) that emissions are beyond permit limit
Excursion – departure from indicator range established in accordance with part 64

## Slide 22
PSEU
Control
Device
Pre-controlled
Emissions
Annual emissions = Control Device X Emission Rate
Post-control
Emissions
Pre-Control Emissions

## Slide 23: Determining Emissions Rates
Emissions testing
  EPA test methods
  Control device inlet and outlet
Mass balance measurements
  e.g., VOC from solvents
  Chemical reactions
Emissions factors X throughput
Industry standards

## Slide 24
Let’s discuss Mass
Balance Calculations

## Slide 25: Mass balance example: coal-fired boiler
Coal-fired boiler
  9% ash
  12,000 Btu/lb coal
Calculate precontrol
emissions:
0.09 lb ash/lb coal = 7.5 lb/mmBtu 0.012mmBtu/lb coal

## Slide 26: Mass balance example: wood-working facility
source
source
dust collector
Eo
Ei
Eo = 8 T/Y (measured via source test)
Control Eff = 90%
Ei (T/Y) x (1 - 90/100) = 8 T/Y
Ei = 80 T/Y

## Slide 27
Note: CAM applicability is made on a
pollutant-by-pollutant basis for each unit
Exercise: Handout #3

## Slide 28: Definition of Control Device

## Slide 29: Definition of Control Device
Equipment used to destroy or remove pollutants
  End of pipe controls
  Scrubber
  ESP
  Baghouse
  Incinerator

## Slide 30
Definition of Control Device
Equipment used to destroy or remove pollutants
  In-process controls where treatment can be adjusted to control emissions
  Steam/water injection on turbines
  FGR for boiler

## Slide 31
Steam/Water Injection
Definition of Control Device

## Slide 32
Control Devices Do NOT Include:
Combustion or other
process design features
Low NOx Burners
Passive control measures
Seals & lids
Low sulfur fuel

## Slide 33: Who is exempt from CAM?
Post-1990 NSPS and NESHAP emission limits (does not include rules amended after Nov 15, 1990)(example)
CFC rules
Acid Rain requirements
Emissions trading programs
Emission caps
Title V permit requiring continuous compliance determination method (CEM)

## Slide 34
Who is exempt from CAM?
Exemptions are by rule type, not facility type:
  Acid rain rules, Post-1990 EPA rules,
  Rules requiring CEMs

## Slide 35
CEM & PEMS
Monitors
CEMS is a subset
Also includes PEMS
CEMS not required if not already present
PSEU with CEMS not automatically exempt
  only if Title V permit specifies as compliance determination method
  if not exempt, CEMS is CAM monitoring

## Slide 36: Exemption for Backup Utility Power Plants
Municipally owned &
Exempt from Part 75 monitoring &
Peaking unit throughout Title V permit term &
Actual emissions over last 3 years < 50% of major source threshold

## Slide 37
CAM Process + RECAP
CAM applicability determination
CAM submittal
Review & approval of CAM submittal
CAM implementation

## Slide 38
CAM Process + RECAP
CAM applicability determination
CAM submittal
Review & approach of CAM submittal
CAM implementation

## Slide 39: CAM Timing (§64.5)
"Other" units: post-control PTE LESS than major source thresholds
  CAM must be addressed at permit renewal
"Large" units: post-control PTE GREATER than major source threshold
  CAM addressed at initial permit issuance if source had not submitted application (or if PA did not determine application complete) by 4/20/98 (Rule effective date of Nov 21, 1997)
  When the unit becomes subject to a significant modification
  Otherwise, at permit renewal

## Slide 40: Source's Role
Develop and propose monitoring in permit application (CAM Plan)
Monitoring in CAM Plan must "provide a reasonable assurance of compliance" to provide a basis for certifying compliance with applicable requirements for PSEUs with add-on control devices

## Slide 41
Monitoring Approach (CAM) Objectives
Identify the indicators of performance of the control device
Identify the ranges to be maintained
Rationale for selecting the indicators & ranges

## Slide 42
Monitoring Approach (CAM) Objectives
Identify the indicators of performance of the control device
Identify the ranges to be maintained
Rationale for selecting the indicators & ranges

## Slide 43
Monitoring
Approach
SOx Control -
Wet Scrubber:
Case Study

## Slide 44: Monitoring Approach – SO2
Indicator | Slurry pH | Slurry flow rate gpm
Indicator range | <9.0 - corrective action, reporting | <175 – corrective action, reporting
Measurement location | Recirculation line | Recirculation line
QA/QC | Annual cal. | Annual cal.
Frequency | Once /15 minutes | Once /15 minutes
Data Collection | pH monitor | Flow rate monitor
Averaging time | hourly | hourly
QIP Threshold | < 10 excursions | < 6 excursions

## Slide 45: Examples of Indicators of Performance of Control Device
Measured Indicators
  NOx conc., Opacity or VEE
  Total HC conc.
Control Device Operating Indicators
  Temp., P, pH, gallons/min
Process Operating Indicators
  Temperature or Flow
Record Keeping
  Lbs VOC/gal of coating
  Maintenance Activity @ fabric filter baghouse inspection

## Slide 46
CAM Monitoring Design Criteria (§64.3)
Select representative control device operational parameters
Establish indicator ranges for reasonable assurance of compliance
Single maximum or minimum value or multiple values
Ranges based on source testing ((§64.4(c)(1)))

## Slide 47
CAM Monitoring Design Criteria
Specify how data to be obtained:
e.g. location of pressure drop gauge
Verification procedures for new
or modified equipment
Quality assurance and control practices to ensure validity of data
Frequency of monitoring

## Slide 48
Frequency of Monitoring (§64.3)
"Large" PSEUs
  for each parameter, collect 4 or more data values equally spaced over each hour
"Other" PSEUs
  some data collection at least once per 24-hour period

## Slide 49: Design Evaluation Factors
Averaging periods:
Sufficient to detect control device or other potential compliance problems
Not so short as to flag minor perturbations as excursions

## Slide 50: Design Evaluation Factors
Level of confidence issues:
Subjective - provides reasonable assurance of proper operation and compliance
Permit application must include justification
for selection

## Slide 51: Example: Indicator Level of Confidence
Indicator Level of confidence
1. VEE 1. Low
2. Aux. burner flame 2. Low inspection
3. Combustion temp. 3. Low
daily monitoring
4. Combustion temp. 4. Moderate
hourly monitoring
5. Combustion temp. 5. Very high
hourly monitoring
+ CO monitoring

## Slide 52
Design Evaluation Factors
Equipment needs - factors to consider
Location and installation logistics
Maintenance and training needs
Cost factors – inherent in source owner’s planning and design

## Slide 53
Design Evaluation Factors
Equipment needs - factors to consider
Location and installation logistics
Maintenance and training needs
Cost factors – inherent in source owner’s planning and design

## Slide 54
Design Evaluation Factors
Selecting and justifying indicator ranges - define a basis:
Parameter data collected during testing
Historical data Baseline Data (months/yrs)
Design or engineering data
From similar operations

## Slide 55
Design Evaluation Factors
Selecting and justifying indicator ranges - define a basis:
Parameter data collected during testing
Historical data Baseline Data (months/yrs)
Design or engineering data
From similar operations

## Slide 56
Design Evaluation Factors
Selecting & justifying indicator ranges:
Type of data (e.g., instrumental or manual)
Frequency (temp. @ 1/min vs. temp. @ 1/day)
Quantity of data for analysis (temp. @ 1/min during 3 hour source test vs. temp. @ 1/min over 3 months)
Data variability (example: pH between 9 & 11)

## Slide 57
Design Evaluation Factors
Selecting & justifying indicator ranges:
Type of data (e.g., instrumental or manual)
Frequency (temp. @ 1/min vs. temp. @ 1/day)
Quantity of data for analysis (temp. @ 1/min during 3 hour source test vs. temp. @ 1/min over 3 months)
Data variability (example: pH between 9 & 11)

## Slide 58: Design Evaluation Factors
Selecting and justifying indicator ranges (continued) - performance criteria:
Data measured during compliance test must fall within range
Range must be indicative of good operations and compliance performance
Range must be sensitive to control device changes
Range should account for normal operational variability (pulsejet cleaning cycle spike @ baghouse; wet ESP flushing causes drop in KV)

## Slide 59: Design Evaluation Factors
Indicator range formats:
Mean value + set value (e.g., 1650 F + 50 F)
Mean value + percent of mean
Max/min value(s) observed
Max/min + set value
Max/min values + percent of mean (e.g. 11-15% O2)
Combination of more than one of above (e.g., if "x" and "y", then excursion) (e.g. P : 3-5 in w.c.)

## Slide 60
Let’s Discuss Submittal
Requirements for CAM

## Slide 62
Let’s Discuss Required
Permit Conditions for CAM

## Slide 64
Let’s Discuss Monitoring
Report Requirements for CAM

## Slide 66
Let’s Discuss Recordkeeping
Requirements for CAM

## Slide 68: What does source do with monitoring results?
Report deviations, excursions & exceedances in semi-annual monitoring reports
  date & duration
  nature of corrective action
Certify compliance status for each applicable requirement
  Operating control device(s) within designated CAM or other indicator ranges

## Slide 69
Let’s Discuss Quality Improvement Plan

## Slide 70: Quality Improvement Plan (§64.8)
District or EPA can require
Permit may specify appropriate threshold, such as an accumulation of exceedances or excursions exceeding 5% of PSEUs operating time
Implementation of QIP does not shield source from noncompliance with emission limit

## Slide 71: Quality Improvement Plan (§64.8)
Written QIP available for inspection
Evaluate performance problems
Modify QIP to include
  improved preventive maintenance practice
  process operation changes
  improvements to control methods
  more frequent or improved monitoring

## Slide 72
Status of Compliance for
Exceedances & Excursions

## Slide 73: Defining Excursions & Exceedances
Exceedance – condition detected by monitoring in units of pollutant emissions) that emissions are beyond limit
Excursion – departure from indicator range established in accordance with part 64

## Slide 74: Status of Compliance: Excursions
Potential problem in the operation & maintenance of the control device,
Possible exception to compliance with applicable requirements,
Owner or operator to take appropriate corrective action, but
Not necessarily a failure to comply with the underlying emissions limitation or standard.

## Slide 75: Status of Compliance: Excursions
Reporting requirements already established in existing requirements,
May have to specify an appropriate time period for averaging data to report exceedances,
Exceptions to compliance.

## Slide 76: Status of Exception to Compliance
Certification of intermittent compliance is not necessarily a certification of noncompliance
  Periods for which one does not really know (e.g., excursions from operating conditions),
  Excused periods (e.g., SS&M),
  Monitoring errors offset by other information indicating compliance.

## Slide 77: What is required for compliance certification?
40 CFR 70.6(c)(5) - annual or more frequent certification requires the source owner (responsible official) to:
Certify as to status of compliance for each permit term or condition, &
Indicate whether compliance is continuous or intermittent.

## Slide 78: What constitutes continuous or intermittent compliance?
From preamble to part 70 revisions (06/27/03):
  Any failure to meet permit terms or conditions (e.g., deviations or possible exceptions to compliance as per part 64 excursions) will result in intermittent compliance certification;
From other EPA documents : Certification of intermittent compliance is not necessarily a certification of noncompliance:
  Periods for which one does not really know (e.g., excursions from CAM indicator ranges),
  Monitoring errors offset by other information indicating compliance.

## Slide 79
Agency Role Evaluate source's CAM plan
Disapprove submitted plan
  draft or final permit must include periodic monitoring
  compliance schedule in permit

## Slide 80: Agency Role Evaluate source's CAM plan
Approve submitted plan
  Approve proposed monitoring and include in permit
  Confer with source if monitoring is inadequate
  Agency may condition approval on source gathering more data on indicators
  If testing or equipment installation required, permit must include enforceable schedule with milestones

## Slide 81
Agency Role: Issue final permit
Indicators to be monitored
Means or device used to measure indicators (e.g. temperature measurement device, VE, CEMS)
Performance requirements
Definitions of exceedance or excursion
Obligation to conduct monitoring,reporting & recordkeeping, implement QIP

## Slide 82: Compliance Certification Condition
Part 70 (§70.6(c)(5)(iii)) revised when Part 64 promulgated
Certification conditions must “identify as possible exceptions to compliance any periods during which compliance is required and in which an excursion or exceedance as defined under part 64 of this chapter occurred.”

## Slide 83
EPA Role
Same as with periodic monitoring or other title V monitoring
Review permits to determine if monitoring is sufficient to assure compliance

## Slide 84
CAM Technical Guidance Document
epa.gov/air-emissions-monitoring-knowledge-base/compliance-assurance-monitoring
epa.gov/sites/production/files/2016-05/documents/cam-tgd.pdf

## Slide 85: Monitoring Approach – SO2
Indicator | Slurry pH | Slurry flow rate gpm
Indicator range | <9.0 - corrective action, reporting | <175 – corrective action, reporting
Measurement location | Recirculation line | Recirculation line
QA/QC | Annual cal. | Annual cal.
Frequency | Once /15 minutes | Once /15 minutes
Data Collection | pH monitor | Flow rate monitor
Averaging time | hourly | hourly
QIP Threshold | < 10 excursions | < 6 excursions

## Slide 86
Let’s Discuss Oxidizers

## Slide 87
Thermal Oxidizer

## Slide 88
Performance indicators
  Outlet VOC concentration
  Outlet combustion temperature
  Outlet CO concentration
  Exhaust gas flow rate
  Outlet O2 concentration
  Inspections
Thermal Oxidizer

## Slide 89
Heat Exchangers

## Slide 90
1,000 PPM
VOC
Burner
1,000 PPM
VOC
10 PPM
VOC
10 PPM
VOC
Primary Heat Exchanger
DRE =
1,000 - 10
1,000
= 99%
Thermal & Catalytic Oxidizer Heat Exchangers

## Slide 91
1,000 PPM
VOC
Burner
1,000 PPM
VOC
10 PPM
VOC
10 + 20 =30 PPM VOC
Primary Heat Exchanger
(with 2% leakage)
2% of 1000 ppm = 20 ppm
DRE =
1,000 - 30
1,000
= 97%
99%
Thermal & Catalytic Oxidizer Heat Exchangers

## Slide 92
Thermal & Catalytic Oxidizer Heat Exchangers
There are two basic types of heat exchangers used for thermal or catalytic oxidizers
Metal Heat Exchangers or “recuperative heat exchangers”
Ceramic Bed Heat Exchangers or “regenerative heat exchangers”

## Slide 93
Thermal efficiency range of 30% to 70%
Shell & tube or plate-type
Usually constructed of alloy steel
Welded systems have very low leakage rates when new
Susceptible to cross-leakage as heat exchanger ages
Not typically used with acid gases
Susceptible to thermal shock on startup and shutdown
Recuperative Heat
Exchangers

## Slide 94
100 oF
Solvent
Laden
Air (SLA)
1,400 oF
Clean, hot air
300 oF
“Clean” hot air
to atmosphere
1,300 oF
SLA
Recuperative Heat
Exchangers

## Slide 95
Key Factors to Consider When Monitoring a Recuperative HX:
  Annual inspection and/or testing of heat exchanger to assess leakage per manufacturer’s recommendations.
Recuperative HX –
Monitoring Approach

## Slide 96
Thermal efficiency range of 80% to 95%
Can be random packing or structured
Extremely tolerant of very high temperatures
Highly resistant to thermal shock
Can resist corrosion by many acid gases
May be susceptible to fouling or plugging
Subject to cross-leakage because of geometry
It is a non-continuous process
Regenerative Heat
Exchangers

## Slide 97
100 oF
1300 oF
HOT CERAMIC BED
BED COOLS AFTER A FEW MINUTES
Regenerative Heat
Exchangers

## Slide 98
COOL CERAMIC BED
BED HEATS UP AFTER A FEW MINUTES
Regenerative Heat
Exchangers
1500 oF
200 oF

## Slide 99
Regenerative Heat
Exchangers
HOT
COLD
FIRST HALF OF VALVE CYCLE
200 oF
100 oF
1300 oF
1500 oF

## Slide 100
Regenerative Heat
Exchangers
SECOND HALF OF VALVE CYCLE
HOT
COLD
100 oF
200 oF
1500 oF
1300 oF

## Slide 101
FIRST HALF OF VALVE CYCLE
Regenerative Heat
Exchangers

## Slide 102
SECOND HALF OF VALVE CYCLE
Regenerative Heat
Exchangers

## Slide 103
VALVE CLOSED
VALVE OPEN
Regenerative Heat
Exchangers
Add Thermocouple to Monitor
Add Thermocouple to Monitor

## Slide 104
Key Factors to Consider When Monitoring a Regenerative HX:
  Assessment of proper closure of valves: Annual inspection/testing
  Annual documentation of valve timing control system parameters
Regenerative HX –
Monitoring Approach

## Slide 105: Heat Exchange Problems
Any cracks or leaks in a recuperative HX will bleed emissions into the clean side
Uncoordinated valves in a regenerative HX will transfer emissions into the clean air.
A regenerative HX usually burps some emissions into the clean air each time the valves switch the flow.

## Slide 106: Monitoring Approach– Example: VOC CONTROL: Thermal Incinerator

## Slide 108
Monitoring
Approach
PM Control -
Venturi Scrubber:

## Slide 109
Venturi
Scrubber

## Slide 111: Test Results
 | Nominal steam generation rate (lb/hr) | Venturi P (in. H2O) | Boiler O2 (%) | Measured particulate emissions (lb/MMBtu) | Allowable particulate emissions (lb/MMBtu)
Boiler Results | 33,000 | 12.0 | 15.0 | 0.081 | 0.25
 | 33,000 | 12.0 | 15.23 | 0.062 | 0.25
 | 33,000 | 12.0 | 16.17 | 0.077 | 0.25
 | 52,000 | 12.1 | 13.87 | 0.067 | 0.21
 | 52,000 | 12.1 | 13.37 | 0.056 | 0.21
 | 52,000 | 12.1 | 14.43 | 0.057 | 0.21
 | 77,000 | 12.0 | 11.77 | 0.045 | 0.17
 | 77,000 | 12.0 | 13.33 | 0.053 | 0.17
 | 77,000 | 12.0 | 13.87 | 0.057 | 0.17

## Slide 112: Particulate Emissions vs. Steam Flow Rate

## Slide 113: Particulate Emissions vs. Exhaust Oxygen Level

## Slide 116
Exhaust O2 conc.
Excursion <11% or >16%
O2 trim system
Daily zero/span Adjust drift >0.5%
15 second compute 1min avg
1-min avg. by DAS
One hour
<6 excursions Semi annual
P transducer
Excursion <10 Inch w.c.
Inlet & outlet of venturi
Calibrate to manometer
At least 1 point 15 minutes
1-hr avg. by DAS
One hour
<10 excursions Semi annual
Flow monitor
Excursion: <175 reporting
Inlet throat to venturi
Calibrate to primary
At least 1 point 15 minutes
1-hr avg. by DAS
One hour
<10 excursions Semi annual

## Slide 117: Monitoring Approach– Exercise: PM10 CONTROL: Baghouse

## Slide 120: Enforcement Authority §64.7(d)
"Upon detecting an excursion or exceedance, the owner or operator shall restore operation of the pollutant-specific emissions unit (including the control device and associated capture system) to its normal or usual manner of operation as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions."

## Slide 121: Relationship of CAM to Other Title V Monitoring
PSEUs not subject to CAM are subject to periodic monitoring
Periodic monitoring similar but less detailed approach than CAM
Periodic monitoring could be used to develop data to support proposed CAM plan

## Slide 122
Review of Key Concepts
CAM applies if PSEU has control device
New concepts in CAM
  Pre-control PTE
  PSEU
  Excursion and exceedance
Data collection to ensure control device operating properly
  sources that don't address problems subject to enforcement

## Slide 123
Thank You
Photo Credits: www.jasonbranz.com

## Slide 124
Recap: Elements of CAM