## Slide 1
National Training Program
NACT 282
Baghouses

## Slide 2: Course Overview
What are we looking at?
Why do we care?
How does fabric filtration work?
Types of baghouses
Design and operation of baghouses
Operation and maintenance problems
Baghouse inspection
Notes: AGENDA/ APPROXIMATE TIMELINE:
8:30 Class begins
9:30 Break
9:45 Methods of Cleaning through Filter Media
10:45 Break
11:00 “What’s Going Into Your Baghouse” through Instrumentation
12:00 Lunch
1:00 Performance Monitoring thru Maintenance
1:30 Inspections
2:00 Test and Review
3:00 Field Visit
4:30 Adjourn

## Slide 3
What Do They Look Like?

## Slide 4: Generic Baghouse (reverse air)
4
Notes: Baghouses can be compartmentalized, sized, and customized for any application.
Review main components of typical baghouse:
Shell
Inlet
Hopper with baffles = One “outlet”
Outlet to stack = 2nd outlet
Bags and support
Dust release mechanism
etc....
Introduce terminology:
Pressure drop
Air-to-Cloth ratio
Cleaning methods

## Slide 5
5
Notes: A baghouse is a glorified vacuum cleaner. It simply uses fabric or a similar medium as a sieve. Invented in U.S., it is most common PM control for both low emission processes like woodshops and high emission processes like electric power plants. In Europe, ESPs more commonly used for PM control.
Photo: Baghouses on top of cement silo
Smaller box to the side is commonly called Bin Vent Filter or Envelope Filter. BVFs are used for gas displacement as in filtering air that is displaced from this silo as silo filled with cement.
Larger box is baghouse for overall process associated with cement silos.

## Slide 6
6
Notes: Pulse-jet baghouse at cogen facility.
This BH had some 400 plus bags used to collect fly ash from boiler (very common use).

## Slide 7
7
Notes: Collecting dust generated from handling of rice.
Principle use of BH as AP control equipment, but in this case, rice dust sold to feed mill where it is mixed with wheat dust, soybean dust, and whatever else is available along with some kind of nutritious binder such as molasses --- for animal feed pellets.

## Slide 8
8
Notes: BH to control dust from coal used as fuel supply at previous cogen facility.

## Slide 9
Notes: BH at lumber processing plant, Arcata. Note single, bottom inlet.

## Slide 10
Notes: 16-compartment BH used at tail end of Portland Cement processing plant in So. Calif.
Additional applications: Table 300-60.

## Slide 11
Why do
we care?

## Slide 16
12,000

## Slide 17
Smoke
Soot
Aerosols
Dust
Nitrates
Carbon
Sulfates
Soil
Salts
Heavy Metals
Organic
Complex Mixture
Particulate Matter: Composition
Notes: First, I’ll go over particulate matter.
Particulate matter, or PM, is a very complex mixture of chemical species. Particles range in size from sub-micron to visible. The sources of PM are complex, and the PM mixture can vary widely from area to area. Sources of PM include both natural and combustion products.

## Slide 18: How Small is PM?
Human Hair
(60 m diameter)
PM10
(10 m)
PM2.5
(2.5 m)
Hair cross section (60 m)
Notes: To give you a perspective on how small these particles are, the left side of this slide shows an electron micrograph of a human hair.
On the right is a representation of the cross-section of the hair compared with two particles, one a 10-micron particle, and the other a 2.5-micron particle.
The majority of ultrafine particles are many times smaller than the PM2.5 particle shown in the picture.
Individually, these particles (coarse, fine, and ultrafine) are not visible to the naked eye. Together, however, fine particles can cause reduced visibility which we associate with “haze.”

## Slide 19
11 Microns and larger
7 to 11 Microns
4.7 to 7 Microns
3.3 to 4.7 Microns
2.1 to 3.3 Microns
1.1 to 2.1 Microns
0.65 to 1.1 Microns
0.43 to 0.65 Microns
Alveoli
Skin
Hair
Primary bronchus
Secondary bronchi
Pharynx
Trachea
Bronchioles
19
Notes: Discuss various PM sizes:
Particles come in all shapes and sizes. Aerodynamic diameter (PM#) depends on size and density.
1 inch = 25,400 microns
Raindrop = 1000 microns
Head of pin = 100 microns
Human hair = 50 microns
Limit of visible particles = 10 microns
Explain diagram:
Emphasize that >10 micron can be expelled by healthy body, <10 cannot and lodge at various levels as shown.
Studies showing that PM 2.5 probably the most problematic component affecting human health.
EPA as promulgated new standards fo r PM10 and PM2.5

## Slide 20
12,000

## Slide 21
U.S. Mortality Figures
In 2005
64,000 = Deaths from particulate air pollution
45,520 = Traffic accident fatalities
32,179 = AIDS deaths
30,694 = Firearm fatalities
Notes: NRDC report “Breath-Taking” cites particle pollution as cause or contributor to some 64,000 excess deaths each year. Based on mortality statistics for 1990-1994.
REF: NRDC

## Slide 22: Los Angeles - Clear Day

## Slide 23: Los Angeles - Smoggy Day

## Slide 24: Most Polluted Regions In the U. S.*
*American Lung Association “State of the Air” Report 5/08
Particulates
Pittsburg
Los Angeles Metro
Fresno
Bakersfield/Kern Co.
Birmingham, AL
Logan, UT
Salt Lake City
Sacramento
Detroit
Washington, D.C. Metro
Ozone (SMOG)
Los Angeles Region
Bakersfield
Visalia/Tulare Co.
Houston
Fresno/Madera
Sacramento
Dallas/Fort Worth
New York Metro
Washington, D.C. Metro
Baton Rogue, LA

## Slide 25: Most Polluted Regions In the U. S.*
*American Lung Association “State of the Air” Report 2021
Particulates
Bakersfield, CA
Fresno-Madera-Hanford, CA
Visalia, CA
Los Angeles-Long Beach, CA
Medford-Grants Pass, OR
Fairbanks, AK
San Jose-SF-Oakland, CA
Phoenix-Mesa, AZ
Pittsburgh-New Castle-Weirton, PA-OH-WV
El Centro, CA
Ozone (SMOG)
Los Angeles-Long Beach, CA
Bakersfield, CA
Visalia, CA
Fresno-Madera-Hanford, CA
Phoenix-Mesa, AZ
Sacramento-Roseville, CA
SD-Chula Vista-Carlsbad, CA
Denver-Aurora, CO
Salt Lake City-Provo-Orem, UT
San Jose-SF-Oakland, CA

## Slide 26
How do
They Work?

## Slide 27: Baghouses may be classified in several ways ....
Method of dust collection
Bag design
Fan location
Method of cleaning
Notes: This will serve as framework for subsequent discussion....

## Slide 28: Interior Filtration
Exterior Filtration
tube sheet (cell plate)
end cap
cell plate
(tube sheet)
28
Notes: Explain diagram
Drawings show gas entering from bottom. This is not always the case. Gas inlet position taken into account in design. Typically, gas inlet at bottom, just about hopper. This is easiest to design and manufacture, but reentrainment can be problem (more later). BHs can also be designed with gas entry at middle or top....
Q. What would be advantages/disadvantages of these?
Both tube sheet and cell plates are walkways for maintenance. These can deteriorate and present hazard for maintenance personnel.

## Slide 29: Particle Collection Mechanisms
Direct interception
Impaction
Diffusion
Gravitational settling
Agglomeration
Electrostatic attraction

## Slide 30
Gas Streamlines
Fiber
Particle
Direct Interception
30
Notes: On fabric itself

## Slide 31
Gas Streamlines
Fiber
Particle
Impaction
31
Notes: Direct interception and impaction account for 99% of particle collection for 1 micron and larger on clean fabric.

## Slide 32
Gas Streamlines
Fiber
Particle
Diffusion
32
Notes: Random motion a.k.a. Brownian motion significant for collection of very fine particles that are less inclined to travel in streamlines.

## Slide 33: Sieving on Woven Fabric
Sieving on Felted Fabric
33
Notes: Actual filtering surface is not the bag itself, but the dust cake as it builds up on woven or felted surface. Collection of particles by impaction and interception called “sieving”. Particles close many of the pores in the fabric and dust cake builds up. Eventually, too many pores blocked and pressure drop exceeds specs. Bags should be cleaned before this.
Filtering time can be 15 minutes to several hours, depending on particle type, concentration, operating conditions. (Remember 10:1 rule)
Dustcake characteristics critical for collection and cleaning. Needs to be cohesive, yet release easily, i.e., should fall off in sheets, chunks, clumps rather than as individual particles which could be reentrained. Sometimes conditioners (NH3, SO3, H2O) are added to enhance dust collectability.

## Slide 34: Other Mechanisms
Gravitational settling
Agglomeration
Electrostatic attraction
Notes: Gravitational Settling:
Very important when gas enters at bottom of unit.
Agglomeration = Dust cake formation and release:
Captured PM should come off in chunks, sheets, clumps, wads. Material that doesn’t agglomerate well can create emissions problems upon release from filtering surface...Why? (reentrainment).
In some cases, agglomerating agents are added to gas stream.
Electrostatic attraction:
Some materials acquire charge readily, e.g., metals, grain dust. Some specialized applications of BHs designed with small electrodes to impart charge and enhance collection.
[Check AP Consultant]

## Slide 35
Settling Chamber
Notes: Designed to take out “rocks”-- 60 micron and above.

## Slide 36
Bag Design

## Slide 37
Metal Cap
Anti-collapse
Ring
Clasp
End Cap
Internal Support
Cage
Venturi
Bags and Support
37

## Slide 38: Cartridge Filter Dust Collector
38

## Slide 39: Filter Cartidges
39

## Slide 40: Cartridge Filter Baghouse
40

## Slide 41: Envelope Filter Baghouse
41

## Slide 42
Fan Location

## Slide 43: Positive Pressure Baghouse
43

## Slide 44: Negative Pressure Baghouse
7/15/2026
44

## Slide 45
Cleaning Mechanism

## Slide 46: Methods of Cleaning
Shaking
Reverse Air
Pulse Jet
Sonic
Notes: To be covered in detail.
Rule of thumb: Cleaning time to Filtering time should be ~ 10:1

## Slide 47
Shaker Mechanism
47

## Slide 48: Shaker Bag with Torsion Spring
Courtesy BHA
48

## Slide 49: Shaker Motor and Hangers
49

## Slide 50: Shaker Cleaning System Problems (Section 503.9)
Improper operation or failure of motors
Inadequate maintenance of linkages
Improper bag tension
Hanging mechanism problems

## Slide 51
Reverse Air Baghouse
51

## Slide 52
52

## Slide 53: Reverse Air Bag
metal cap
anti-collapse ring
bag clamp
thimble
tube sheet
53
Notes: Note parts, especially anti-collapse ring which prevents bag from sticking to itself when cleaned.
Q. Interior or exterior filtration

## Slide 54: Thimble Design
OK
Better
54

## Slide 55
55

## Slide 56: Reverse Air Baghouse
Notes: Old standard for BHs.
Bottom inlet actually a type of cyclone to drop out larger particles. Air with particulate flows upward and out (though reentrainment can occur). Several manifolds introduce reverse air to collapse groups of bags.
System remains on-line.
E.g., lumber processing

## Slide 57
Reverse air baghouse at lumber mill
57

## Slide 58
58

## Slide 59: Reverse Air Cleaning System
59

## Slide 60: Reverse Air Cleaning System Problems (Section 503.10)
Inadequate reverse air flow
Leakage through poorly sealed dampers
Improper bag tension
Corrosion
60

## Slide 61: Pulse Jet Cleaning
61

## Slide 62: Pulse Jet Baghouse
Clean Air
Clean Air Plenum
Pulse Pipe
Bag
Cage
Venturi
Solenoids
Dust-Laden Air
Inlet Baffle
62

## Slide 63: Pulse Jet Baghouse
Clean Air
Clean Air Plenum
Pulse Pipe
Bag
Cage
Venturi
Solenoids
Dust-Laden Air
Inlet Baffle
63

## Slide 64
64

## Slide 65
Pulse Jet Baghouse

## Slide 66
Inside a Pulse Jet Baghouse

## Slide 67
Pulse Jet
Bag

## Slide 68
Pulse Air Distribution System
68

## Slide 69
Snap Ring
69

## Slide 70: Pulse Jet Cleaning System Problems (Section 503.11)
Cage/bag misalignment
Low compressed air pressure
Contaminated compressed air
Diaphragm valve leakage or freezing
Loose, misaligned pulse pipe
Timer or differential pressure sensor failure
Excessive cleaning frequency
Notes: Misalignment can result in bags touching, usually at bottom, leading to bag-to-bag-abrasion.
Diaphragm valve part of compressed air system.

## Slide 71: Sonic Cleaning

## Slide 72: Acoustic Horn
72
Notes: Side-mounted acoustic horn.
Can be louder than siren @ 140-150 dB.
Lower frequencies especially effective in cleaning and can reduce pressure drop by 40-50% in situations where physical cleaning not very effective.

## Slide 73: Filter Media
Woven
Felted
Membrane
Sintered metal
Ceramic

## Slide 74: Fabric Weaves
Plain
Twill
Sateen
74
Notes: Most fabric filter media employ some kind of woven fabric either as direct filter medium or as backing.
Plain weave is tightest, :. best for smallest particles. Tends to “blind” easily, i.e., particles become impregnated in fabric and decrease air flow, increase pressure drop.
Twill weave: Easier release of dust cake. Lower abrasion.
Sateen: Easiest cake release but “bleedthrough” more likely.
Type of fabric depends on type of dust, operating conditions, cost

## Slide 75: Sieving on Woven Fabric
Sieving on Felted Fabric
75
Notes: Felted fabric: Made by needle punching fibers unto woven backing called “scrim.” Felts attached by chemical, heat, resin, or stitch bonding. Felting may increase thickness 2-3X.
Bags durable, good for pulse cleaning.

## Slide 76: Fabric Selection Factors
Maximum Operating Temperature
Melting Temperature
Resistance to Corrosive Chemicals
Flex and Abrasion Resistance
Permeability (vs. blinding)
Type of dust
Notes: Selecting the right fabric for the job..... Need to know about the process.
Most bag failures caused by high temperatures, abrasion, or chemical attack.
Temperature-related:
Fabric breakdown or melting
Breakdown of coating, lubricant, etc.
Cumulative effects of temperature excursions in operating range.
Condensation problems, e.g. cement dust
Abrasion:
Bag attachment points, rings, cleaning mechanism.
Bag-to-bag from misalignment, swaying, improper installation
Abrasive particles
Abrasion from high speed ejection from holes in bags
25% per year replacement not unususal. Inspectors: Check purchase records, stocks of spare parts.
Chemical Attack:
Acid dewpoint (related to temperature). Following proper startup/shutdown protocols minimizes dewpoint concerns.
Resistance to particular chemicals in process,e.g., Fiberglass won’t stand up to sulfuric acid compounds.
Flex resistance:
Cleaning process, Air-to-cloth ratio, overall strength (Mullen Burst test)
Ease of handling: Installation and maintenance; e.g., cotton vs. fiberglass
REF: Pp. 300-25, 26: Tables 303.1, 2, 3

## Slide 77: Fabric Treatment Processes
Calendaring
Napping
Singeing
Glazing
Coating
Precoating
Notes: Calendaring: Pressing down of fibers under pressure to achieve more uniform surface.
Napping: Scrapping to create “fuzz” and increase collection by interception and diffusion. Good for sticky, oily dusts.
Singeing: Over open flame; increases uniformity.
Glazing: Pressing of fibers under high pressure and elevated temperatures. Increases mechanical stability and decrease bag shrinkage.
Coating: With natural resin or lubricant to ease movement of fibers and cleaning flexibility; e.g., glass bags with Teflon.
Pre-coating: Not really a fabric treatment, but a pretreatment. When new bags put into service, some bleedthrough can occur until dust cake builds = opacity. Some bags pretreated at factory with dry inert material or material injected into gas stream to coat bags with dust cake and prevent bleedthrough. Materials include limestone, fly ash, diatomaceous earth, proprietary materials of various kinds. Limestone good for SO2 control, but can “set” if temperature falls below moisture dewpoint.

## Slide 78: Applications for Different Types of Fabrics
Cotton - Simple applications
Nylon - Abrasive dusts
Polyester - Metal industries
Nomex - Asphalt batch plants
Teflon - Coal-fired boilers
Notes: Refer to Tables 303.1, 2
Nomex common for many high-temp (300-400F) applications.
Gore-Tex: Semipermeable membrane cloth. Surface filtering; no penetration into fabric to create dust layer; therefore, no dust buildup and minimal dP. Membrane is hydrophobic; therefore, moisture differentially excluded from filtered dust.
Ceramic: 3M-Nextel is one brand. Used in:
- catalyst recovery
- solid fuel gasification
- acid gas treatment
- pyroprocessing separation of ores (metal processed as fumes)
- production of high-grade products

## Slide 79: Fabric Blinding
Moisture in dust cake
Lubricating oil (pulse jet)
Submicron particles
Notes: Moisture an obvious potential problem, although in some situations, moisture might be added to enhance cleaning. Extreme version called “mudding” which occurs when dust cake absorbs water and builds layer of mud on bag, blocking air flow and impairing mechanical cleaning motion.
Submicron particles can be driven into fabric weave, essentially blocking air flow. What you want is dust cake to do the collection, but leave some pore space for air flow. Can be particular problem if bags overcleaned and placed online where there is very fine particulate and high air flow.

## Slide 80
80
Notes: Agglomeration from excess moisture

## Slide 81
81
Notes: Spark carryover damage. Can be prevented by pretreatment with spark retardant material and/or spark arrestors on gas inlet.

## Slide 82: What Is Going Into Your Baghouse?
Dust Properties
Gas Flow Rate
Gas Temperature
Chemical Composition
Notes: Starting point for design.
Discussed in Sections 304 and 308 of manual.

## Slide 83: Dust Properties
Mass Loading
Abrasive Particles
Size Distribution
83
Notes: Various techniques for determining mass loading and size distribution (see Section 304.6). Will not cover in this course.
Mass loading and size distribution can vary up to 20% without affecting original design, but may necessitate changes in operation. Increase in concentration of dust may require more frequent cleaning.
Too load dust load can result in excessive emissions after each cleaning cycle -- Why?
Abrasive particles - use precleaner
Fine particles - Blinding possible REF: Section 304.6

## Slide 84: Design Considerations
Pressure Drop
Air-To-Cloth Ratio
Collection Efficiency
Fabric Type
Cleaning
Temperature Control
Bag Spacing
Compartment Design
Space and Cost
Notes: Based on what’s going in and what you want out, namely, emissions in compliance with regulations.
We’ll discuss the first 2 in some detail. These are fundamental to all baghouses.
Collection Efficiency not really an issue. Baghouses operate at 99+% efficency in most applications if functioning properly.
Temperature Control will be discussed later. Not used in all BHs.
Last 3 are important, but not for this course.

## Slide 85: Pressure Drop (dp)
Resistance To Airflow
Inlet Pressure - Outlet Pressure
Size of Fan
Filter & Dust Cake
Notes: Fundamental variable
Normal operating BH pressure drop is between 3" to 10" H2O.
Demo magnehelic gauge.
Affects size of fan and initiation of cleaning cycle.
Practically speaking, pressure drop comprised of dp across filter and across dust cake that builds up on filter media.
REF: Section 304.1

## Slide 86
86

## Slide 87
87
Notes: Photohelic gauge not only measures but allows for setpoints. When gauge reads outside of setpoint limits, cleaning may be initiated or stopped.

## Slide 88
88
Notes: Magnehelic gauge typically use to determine pressure drop as shown. Pressure drop is difference between clean side and dirty side.
Number should rise slowly until cleaning cycle initiated. Sudden decrease or very slow rise may indicate leak. Sudden increase or increase beyond design value indicates possible blinding of bags.

## Slide 89: Pressure Drop Across Filter
dpf = dp across clean fabric
      k1 = fabric resistance
      vf = filtration velocity
dpf = k1vf
Notes: Equation also known as Darcy’s Law. Describes flow of fluids through porous materials.
k1 is function of filtering medium (porosity) and viscosity of gas.
vf is velocity of gas in ft/min or cm/sec.

## Slide 90: Pressure Drop Across Dust Cake
dpc = dp across dust cake
      k2 = resistance of dust cake
      vf = filtration velocity
      ci = dust concentration loading
      t = filtration time
dpc = k2 ci vf2 t
Notes: More important is pressure drop across dust cake:
k2 is experimentally determined. Depends on gas and particle density and dust porosity in dust cake. This is indicated by permeability which is measureable by ASTM Method D737-69. Dust cake made up of very small particles will have high k2 and bags will have to be cleaned often.
Also note that filtration velocity, vf, figures in prominently as a squared value. Changing the gas flow velocity will :. have big affect on dpc.
Total pressure drop is dpf + dpc.
Bags designed to withstand certain maximum pressure.
Process designed to operate at certain maximum pressure.
Fan designed to operate effectively up to certain maximum pressure.

## Slide 91: Static Pressure Drop vs. Gas Flow Rate
Gas flow rate, % of maximum
20
40
60
80
100
0
1
2
3
4
p,
inches of water
Notes: Gas flow rate has direct effect on pressure drop and thus is major factor to consider in design.
Trend, not precise numerical relationship. Must be considered in light of other factors if used as performance evaluation tool.

## Slide 92: Pressure Drop Profile
Time
p
Notes: Sawtooth pattern typical of BH cleaned on-line.

## Slide 93: Problems Related to Pressure Drop
Pressure Drop Too High =
  bag blinding, blockage
  increase in gas flow rate
  fugitive emissions
Pressure Drop Too Low =
  bag failure
  inleakage

## Slide 94: Fugitive emissions due to excessive pressure drop
94
Notes: What can happen to Capture when something else is amiss.

## Slide 95: Air-to-Cloth Ratio
vf = filtration velocity
Q = volumetric air flow rate
A = area of cloth filter
vf = Q/A
p 300-32
Notes: AKA “Filtration Velocity.”
We already saw that vf is the rate of gas flow. Vf can be expressed as ratio of volume of gas filtered, Q in ft3/min, in to total area of filtering medium, A in ft2; usually expressed in units of (ft3/min)/ft2, but units can be reduced to ft/min. Given gas velocity and volumetric flow rate, amount of cloth area needed to filter particulate can be determined.

## Slide 96
Air-To-Cloth Ratio
Shaker < 3:1 < 6:1
Reverse Air < 2:1 < 4:1
Pulse Jet 2.5:1 to 7.5:1 <15:1
(cm3/sec)/cm2 (ft3/min)/ft2
Cleaning
Method
p 300-33
Notes: These are some general air-to-cloth (A/C) ratios for each of the various cleaning mechanisms. Note that pulse-jet has an A/C ratio over twice that of a shaker and over three times that of a reverse-air. This allows a pulse-jet collector to be smaller than a shaker or reverse-air.

## Slide 97: Importance of A/C Ratio
A/C Too High:
  fan works harder
  increased abrasion
  blinding
  breakdown of dust cake
A/C Too Low:
  smaller BH required
Notes: Reducing A/C can enhance performance. This can be done by reducing gas flow rate (relatively easy) or increasing fabric area (not very easy after baghouse built).

## Slide 98: Controlling Gas Entry
Precleaner
Baffle Plate
Inlet Diffuser
Inlet Location
Thimble Design
Bypass
Notes: Let’s look at some other components of BH control device as entire system, that is, entry and exit points, instrumentation.

## Slide 99: Effects of Primary Collection
Size in microns
.00
.02
.05
1.00
5.00
20.00
Relative distribution of
particles
99
Notes: Utilizing primary collection systems enhances control of fine particles by BH. BH shd be designed with this in mind, since gas stream will carry more fines when primary collectors used.

## Slide 100
Cyclones
100
Notes: Individual cyclones very common for controlling particulate down to 5 microns.
Can develop pinhole leaks and subject to corrosion.

## Slide 101
Baghouse with Cyclonic Inlet
101
Notes: Individual cyclones very common for controlling particulate down to 5 microns.
Can develop pinhole leaks and subject to corrosion.

## Slide 102: Industry Description Bin Vent Filter

## Slide 103: Industry Description Bin Vent Filter
Notes: During the filtering cycle, dust laden air is drawn into the bin vent filter by a positive air source such as a pneumatic conveying system. Air enters the bin vent filter through the hopper or storage bin and passes up through the filter cartridge. The clean air then passes through the plenum into the atmosphere. During the cleaning cycle, compressed air is injected through the cleaning nozzle to clean the cartridge. This energy charged air is directed downward against the interior of the filter cartridge, creating a positive back pressure and a shock wave. This action is immediately followed by an inrush of secondary atmospheric air that helps create a compression zone, causing the accumulated dust to be quickly released from the cartridge.

## Slide 104: Bin Vent Filter
Notes: Principles of Operation — Previous Page
Particles collect on the outside surface of the bags as the air stream passes through the filter media and up to the clean air plenum.
At timed intervals a selected solenoid valve actuates a diaphragm valve, releasing a predetermined volume or pulse of compressed air into distribution pipe, producing a shock wave along the length of the bag, flexing the fabric and dislodging dust particles from the surface.
The cleaning cycle can also be initiated by monitoring the differential pressure across the filter media as a result of dust build-up. Referred to as "cleaning on demand," this pulsing system only operates when bags require cleaning, minimizing compressed air consumption and lengthening bag life. Optional Smart Timer™ also available for these units. Top Access Units: Bags and cages are removed and installed from Flex-Kleen patented Trap 10 above the tube sheet. Our Trap 10 design provides the most effective tube sheet/bag seal available anywhere.
Bottom Access Units: Bags are removed from beneath the tube sheet. Broad range of filter media and surface finishes are available to handle high temperatures, smaller particle sizes, corrosive environments, sticky materials, etc. Venturis have multiple functions: 1) aspirate filtered air into the bag to create the cleaning pulse, and 2) retard the escape of the pressure wave from the top of the bag, causing multiple and repetitive pulses.
— Previous Page Flex-Kleen Division 955 Hawthorn Drive Itasca, Illinois 60143-2641 E-mail: info@flex-kleen.com

## Slide 105
Baffle Plate
105
Notes: Baffle plate will diffuse gas and cause dropout of larger particles.

## Slide 106: Inlet Diffuser
106
Notes: Designed to create more uniform gas flow.
62

## Slide 107: Inlet Air Dispersion
Dust
re-entrainment
Ladder vane baffle
Wear points
107
Notes: Simpler installation has problem. Since 90% of bag failures occur near inlet, bag replacement chart would probably show pattern here.
Adding baffle or blast plate minimizes this problem.

## Slide 108: Thimble Design
OK
Better
108
Notes: This is primary wear point in reverse and shaker BHs (manual says 90% of all bag failures occur at thimble). Not difference between OK and Better.

## Slide 109
Dampers
109
Notes: Dampers can be used to control influent.

## Slide 110: Lunch Break
Return at 1:05 pm CST

## Slide 111: Gas Temperature Effects
High Operating Temp. =
  fabric breakdown
Low Operating Temp. =
  condensation
  blinding, chemical attack
Inlet - Outlet Temp. Too High =
  inleakage
Notes: Temperature drop of 2 - 25 degrees inevitable when hot process gas enters BH. Minimum and maximum temperature should be set and monitored as should temperature drop which can indicate air inleakage. Some systems have alarms.
Air Inleakage (-P, min T):
Reduces efficiency; can cause dewpoint / condensation; corrosion / blinding.
Problem with operating near maximum temperature limit of medium:
GRAPH
Nomex will withstand 400 degrees for a long time, but if temp spikes, only thing protecting bag is dust cake. Better to operate 25-50 degrees below limit to prolong bag life.

## Slide 112: Temperature Control
Gas Cooling
  Dilution
  Radiation
  Evaporative Cooling
Preheating
Insulation
Minimize Inleakage
Notes: Gas cooling sometime employed. Expensive.
Preheating especially before startup where high moisture expected. May involve process gas or in some cases electrically heated shell.
Insulation another option (next slide).
Minimizing inleakage, especially through hoppers, ducting, shell is important maintenance concern. Inleakage can have drastic effect on operating temperature.

## Slide 113: Insulated Baghouses
113

## Slide 114: Radiation Cooling
114
Notes: Far-away view of baghouse at cement plant near Tucson, AZ.

## Slide 115: Radiation Cooling
115
Notes: Radiation cooling of high temp kiln flow before entering same baghouse.
[Need particulars from RC or Al}

## Slide 116
Courtesy BHA
Notes: Startup/shutdown procedures affect temperature which in turn affects condensation. Chart is for BH controlling PM from combustion process
Review chart:
Startup: Preheat BH to temperature above acid dewpoint. Objective is to minimize potential condensation period inside unit by preheating quickly. Moisture-laden gases should be kept out until operating temperature reached. Bypass may be permitted in some areas so baghouse can warm up to operating temperature.
Shutdown: At some point, temperature will pass through acid and water dewpoints. Purge dirty gas before allowing temperature to descend and introduce clean, dry (hot) air where possible. Dust should be removed from hopper so it won’t set up due to condensation.
REF: BHA

## Slide 117
Hoppers and Dust Handling Equipment
(Section 303.5)
Notes: Integral part of particulate control system.
Exposed to ambient air more than rest of control system, so site of inleakage, temperature drop.

## Slide 118
Hoppers and Dust Handling Equipment
(Section 303.5)
Notes: Integral part of particulate control system.
Exposed to ambient air more than rest of control system, so site of inleakage, temperature drop.

## Slide 119
Hopper with Strike Plate
119
Notes: Hoppers designed with steep sides to prevent clogging.
This photo show hopper with strike plate to jar dust loose. Many hoppers are insulated to minimize temperature drop.
Hoppers may also be heated depending on dust and ambient conditions. Look for temperature gauge.

## Slide 120
Hopper with Compressed
Air Cleaner
120
Notes: Another cleaning method.

## Slide 121
Hopper Level Indicator System
121
Notes: Large hoppers may have level indicators. Capacitance probe commonly used. Probe inserted into hopper; as dust builds up around probe, change in capacitance (stored electrical energy) occurs and triggers alarm.
Photo shows an indicator using a cesium radioisotope to generate radioactive beam that is received by detector on opposity side of hopper.
Advantage--no probe subject to dust buildup and more than one hopper can be monitored.
Alarms also used.
General rule: Hoppers shd not be used for long-term storage of captured dust.

## Slide 122
122
Notes: Tried and true method for transporting collected dust.
Airlock desirable.
Gas inlet shd be on side opposite conveyer discharge.

## Slide 123
Pneumatic Dust Transport System
123
Notes: Pneumatic conveyer uses differential pressure to facilitate movement of particulate from hoppers. Partial vacuum in pneumatic transport system relative to hopper supplements gravity feed to move dust away from control system for disposal or reuse.
[Followup with Stockton Cogen]

## Slide 124
Pneumatic Hopper Valve System
124

## Slide 125
Trickle Valve System
125
Notes: Weight of particulate on top flap pushes down on counterweight to release small batch of dust; top flap closes. Lower flap opens when weight of dust tips counterweight. Whole system isolated from outside. Motorized versions also used.
Used in smaller scale baghouses.

## Slide 126
Trickle Valve System
126

## Slide 127: Rotary Airlock Valve
127
Notes: Rotary airlock used in medium or large-sized BHs. Often used in conjunction with pneumatic conveyer to maintain even flow of material.
Airlock maintains more or less airtight seal to prevent inleakage. In addition, airlock allows for a constant removal of material from hopper, preventing buildup. Can also be used for precise volumetric feeding if required.
Note that one operator (ESP, Constellation in Rockin), mentioned that inleakage common with these valves. Result is ambient air at higher pressure than inside hopper supports a small head of dust above valve until weight of dust overcomes pressure.

## Slide 128
Slide Gates
128
Notes: Can be used for intermittant cleaning or to isolate hopper if conveyer below needs to be serviced.

## Slide 129: Dust Discharge Problems
Inleakage
Corrosion
Change Process Temp.
Dust Buildup
Pluggage
Fugitive Emissions
Notes: Inleakage previously discussed
Corrosion can cause malfunctioning of dust discharge system; can result from malfunction, poor sealing.
Dust buildup and Pluggage may result in reentrainment of particles from system with gas inlets just above hopper. In extreme cases, may block gas flow by blocking bags at bottom.
Fugitive emissions from hoppers, discharge areas, cleaning of hoppers can negate collection efforts. Control of fugitive emissions shd be part of permit and inspection.

## Slide 130: Types of Hopper Blockage
Arching
Bridging
Ratholing
Buildup
Notes: Any of these will require more aggressive cleaning.

## Slide 131: How Do We Monitor Compliance

## Slide 132: Performance Monitoring (Section 501, 502)
Opacity
Triboelectric & Tribokinetic Devices
Light Modulation
Pressure Drop
Temperature
Bag Failure Patterns
Clean-side deposits
Notes: Performance monitoring is daily job of operators. As inspectors, you would expect to note: 1) that such monitoring is being done; 2) results that indicate non-compliance with permit/rule conditions.
Baseline Conditions shd be established for initial PTO and subsequent source tests. Baseline conditions include process parameters and BH operating parameters (see list p 400-6.) Inspectors may find this helpful to determine changes in process or BH that could affect compliance.
Opacity and Pressure Drop are key indicators of performance. Opacity is not good indicator of certain problems, like hopper bridging or pluggage :. don’t rely on opacity exclusively.
Pressure Drop shd remain in operating range as determined by baseline testing. Gradual increase in dp after cleaning may indicate oil deposits, blinding.
Temperature can have profound effects on performance. Effects fabric life, collection, and integrity of shell.
Bag Failure Patterns: Bag Replacement Chart is another indicator of performance problems (p. 500-7). Often, localized abrasion is a problem revealed by these records. Overall replacement frequency can indicate need for overhaul of entire system.

## Slide 133: Double-Pass Transmissometer
Stack
Flow
Mirror
Adjustable Focussing Lens
Tungsten Light Source (10 W)
Photocells
Reference Beam
Measurement Beam

## Slide 134: Pressure Drop Profile
Time
p
Notes: Sawtooth pattern typical of BH cleaned on-line.

## Slide 135: Static Pressure Drop Profiles - Reverse Air Baghouse
Time
p
-2
-1
0
+1
+2
+3
+4
Normal Profile
Filtering Cycle
Cleaning Cycle
Abnormal Profile
Null Period
Notes: Indicates Normal and Abnormal operation for reverse air system.
Explain graph
Problems that could create this pattern include:
1. Inadequate reverse air flow by reverse air fan
2. Leakage of reverse air through reverse air dampers and relief dampers
3. Leakage of reverse air through poorly-sealed compartment outlet dampers.
Leaking poppet valves (dampers) may show starburst air sweep pattern.
REF: APTI, p 5-42,43.

## Slide 136
136
Notes: Bag leaks can be detected long before opacity exceeds permitted limit using a system like this. Operates by “triboelectric effect”. When one material rubs or impacts another, a transfer of charge takes place. This “triboelectric effect” or frictional electrification creates small electrical signal (4-20mA) which can be measured to generate an analog readout.

## Slide 137: Triboelectric Monitoring
Notes: Analog signal graph shows bag status and allows for early detection and replacement.
A similar but newer technology uses the small charges generated by particles passing close to a probe to indicate particulate concentration. This is called the tribokinetic effect. Advantages are the tribokinetic probes are not sigificantly affected by buildup of dust on the probe and do not need calibration as often as triboelectric probes.
Both of these technologies are non-optically based.

## Slide 138: CPM™ Technology
138
Notes: These detectors are optically-based units. CPM technology uses a variation on standard light extinction method (opacity). When dust passes between the transmitter and receiver, the momentary absorption of light by particles causes the receiver to see a modulating signal from the transmitter. This signal modulation increases with and relates to increasing dust concentrations. Instrument calibrated with known dust sample or used as relative monitoring signal.
Advantages (over transmissometer): No clogging and less blocking of optical windows. Only responds to moving dust so buildup and misalignment will not affect output.

## Slide 139: Clean-Side Deposits
139
Notes: Clean-side deposits on shaker or reverse air system

## Slide 140
Clean-Side Deposits
140
Notes: Clean-side deposits on pulse-jet system
Show Video: Troubleshooting using fluorescent dye injection.

## Slide 141: Fluorescent Dye Leak Detection
141
Notes: Clean-side deposits on pulse-jet system
Show Video: Troubleshooting using fluorescent dye injection.

## Slide 142: Maintenance
142
Daily
Weekly
Monthly

## Slide 143
143

## Slide 144: Inversion Bag Cleaning Device
144
Notes: Invert bag cleaner

## Slide 145: Spare Cages
145
Notes: Spare parts should be on hand!

## Slide 146: Inspection Elements
Pre-Inspection
On-Site Inspection
Post-Inspection
Notes: Review elements with student input
Pre-Inspection:
Note that in reviewing regulations, you probably won’t find something specifically addressing baghouses.
Particulate matter emissions limits will apply (APPENDIX B)
On-Site: Refer to list of questions, p 400-5,6

## Slide 147: Permit Conditions
Opacity Limits
Process Weight Limits
Ranges of Inlet and Outlet Temps.
Process Rate
Recordkeeping Requirements
CEMS Requirements
Minimum / Maximum Pressure Drop
Notes: Standard approach--observe compliance with permit conditions.
Recordkeeping (Section 502)
Periodic I & M shd also be required.

## Slide 148: Air Pollution Control System Points of Inspection
Capture (System Entrance/Exit)
Transport
Air Mover
Control Device
Instrumentation
Subsystem(s)
Records
Notes: AP inspections shd be done methodically. This general scheme used by our division can be applied to nearly all inspections
Let’s look at each of these segments as they apply to baghouses....
(Alternately, 9-Step approach starting p 400-7. This is useful for troubleshooting in non-compliance situations.)

## Slide 149
149

## Slide 150: Fugitive emissions due to excessive pressure drop
150
Notes: What can happen to Capture when something else is amiss.

## Slide 151
As particle size gets smaller, reflective surface area increases
Beer’s Law
151

## Slide 152
152
Notes: Ductwork from metal-working machines to baghouses at a foundary near Fresno, CA

## Slide 153
153

## Slide 154
154

## Slide 155
155

## Slide 156
156

## Slide 157
157

## Slide 158
158

## Slide 159
159

## Slide 160: Instrumentation
Flow Meters
Thermocouples
Pressure Gauges
Transmissometers / CEMs
Hopper Level Indicators
Compressed Air Pressure Gauges
Notes: Inspection of instrumentation may be most telling aspect of BH inspection. Rarely will inspector have a chance to...or need to .... inspect interior of BH. Instruments indicate day-to-day operation/compliance of BH with permit conditions.
Flow meter not often present. Indirect msmts include fan operating parameters, production rate, etc.
Thermocouples or other temperature monitoring instruments: There are several temperature-related concerns ... Which are?..... (High temperature damage to fabric. Dewpoint problems.). Alarms.
Pressure gauges: Differential best to measure pressure drop.
Hopper level indicators: Covered
Compressed air gauges: To indicate psi for pulse-cleaning systems.
Transmissometers/CEMS: Opacity. Increase normal when bags changed. Opacity increases after cleaning in pulse system can indicate pinhole leak. Puffs can indicate bag damage. One special kind of CEM is broken bag indicator.......

## Slide 161
161

## Slide 162
162
Notes: These gauges on shaker system at almond processing plant. Can be monitored periodically to ascertain whether system performing properly.
Clearly marked permit requirements.
Facility has applied for permit change because they have found that dp won’t go to 2” until many months after cleaning... but no opacity or operational problems.

## Slide 163
163

## Slide 164: Computer Monitors slides
164
Notes: Example of a multi-baghouse monitoring system at a power plant. A variety of parameters can be measured and reported in real-time with this kind of system.

## Slide 165
165
Notes: The Good

## Slide 166
166
Notes: The Bad

## Slide 167
167
Notes: The Ugly

## Slide 168: General Safety Policies
Anticipate hazards before leaving for inspection site
Have all necessary personal protective equipment
Be aware of and conform to all applicable plant and agency safety policies
Do one thing at a time
Don't work alone
Notes: 90
These are standard for nearly all industrial site inspections.

## Slide 169
169
Notes: Hoppers have a number of safety concerns, included rotating screw, hot solids, blowing dust.

## Slide 170
170
Notes: Sign, sign everywhere a sign.... Discuss briefly

## Slide 171
171
Notes: Yes, these happen

## Slide 172
172

## Slide 174: Air Inleakage Sites
Top/Side access hatches
Hopper discharge valves and poke holes
Inlet duct and outlet duct expansion joints
Improperly welded shell
Corroded shell

## Slide 175: Instrumentation

## Slide 176
176

## Slide 177
0
1000
2000
3000
4000
5000
6000
Los Angeles
New York
Chicago
Philadelphia
Detroit
Particulate Air Pollution-Related Deaths
Based On 1996 Report
Premature Deaths Per Year
5873
4024
3479
2599
2123
Notes: AIRS = Aerometric Information Retrieval System
MSA = Metropolitan Statistical Area

## Slide 178: COHPAC (Compact Hybrid Particulate Collector)
ESP
Pulse BH
Flue
Gas
30% Opacity
2% Opacity

## Slide 179
SOx-NOx-Rox Box
Graphic Courtesy of B&W
179
Notes: The SNRB process includes operation of a pulse-jet baghouse at high temperatures which require the filter bags to withstand exposure as high as 900 degrees F while maintaining high particle collection efficiency. Still somewhat experimental. Used in a few power plants in Ohio.
Initial SO2 capture takes place as the injected sorbent (calcium or sodium based) is transported through the system to the filter bag, and the final absorption occurs as the flue gas passes through the sorbent/ash/spent-sorbent filter cake on the bag surface.
NOx removal occurs by injection of NH3 into the hot flue gas upstream of the baghouse and reaction of the ammonia with the NOx in the presence of a zeolite catalyst inside the bags (and away from the SO2 and particulate).