## Slide 1: TOXC 240 Fugitive VOC Emissions

## Slide 2: Course Overview
Regulated Facilities
Components
Estimating Emissions
Regulations and Standards
Method 21
Field Inspections
Notes: COURSE OVERVIEW/PURPOSE:
Purpose: Overview of Fug VOC inspections, with emphasis on local rules, portable monitoring equipment, and inspection procedures. Not a permitting or engineering course. Course based on an EPA APTI course.
Topics to be covered - animated bullets

## Slide 3: Definition of LDAR
LDAR is a work practice designed to identify leaking equipment so that emissions can be reduced through repairs.
A component that is subject to LDAR requirements must be monitored at specified, regular intervals to determine whether or not it is leaking. Any leaking component must then be repaired or replaced within a specified time frame.

## Slide 4: Elements of an LDAR Program
LDAR programs. Identifying Components
Leak Definition
Monitoring Components
Repairing Components
Recordkeeping
Notes: The requirements among the regulations vary, For each element, this section outlines the typical but all LDAR programs consist of five basic ele-LDAR program requirements, common compliance ments, which are discussed in detail in Sections 5.1 problems found through field inspections, and a through 5.5. set of best practices used by facilities with effective

## Slide 5: Why Check for Leaks?
Public Health
Safety
Reliability
Economic
Notes: EPA has determined that leaking equipment, such as valves, pumps, and connectors, are the largest source of emissions of volatile organic compounds (VOCs) and volatile hazardous air pollutants (VHAPs) from petroleum refineries and chemical manufacturing facilities. The Agency has estimated that approximately 70,367 tons per year of VOCs and 9,357 tons per year of HAPs have been emitted from equipment leaks. Emissions from equipment leaks exceed emissions from storage vessels, wastewater, transfer operations, or process vents.
VOCs contribute to the formation of ground-level ozone. Ozone is a major component of smog, and causes or aggravates respiratory disease, particularly in children, asthmatics, and healthy adults who participate in moderate exercise. Many areas of the United States, particularly those areas where refineries and chemical facilities are located, do not meet the National Ambient Air Quality Standard (NAAQS) for ozone. Ozone can be transported in the atmosphere and contribute to nonattainment in downwind areas.
Some species of VOCs are also classified as VHAPs. Some known or suspected effects of exposure to VHAPs include cancer, reproductive eff ects, and birth defects. The highest concentrations of VHAPs tend to be closest to the emission source, where the highest public exposure levels are also often detected. Some common VHAPs emitted from refineries and chemical plants include acetaldehyde, benzene, formaldehyde, methylene chloride, naphthalene, toluene, and xylene

## Slide 6: The Bad Guys
Total Hydrocarbons
Reactive Organic Compounds
(ROCs,ROGs,VOCs)
Non-Reactive Organic Compounds
Hazardous Air Pollutants
(HAPs)
Notes: EPA has determined that leaking equipment, such as valves, pumps, and connectors, are the largest source of emissions of volatile organic compounds (VOCs) and volatile hazardous air pollutants (VHAPs) from petroleum refineries and chemical manufacturing facilities. The Agency has estimated that approximately 70,367 tons per year of VOCs and 9,357 tons per year of HAPs have been emitted from equipment leaks. Emissions from equipment leaks exceed emissions from storage vessels, wastewater, transfer operations, or process vents.
VOCs contribute to the formation of ground-level ozone. Ozone is a major component of smog, and causes or aggravates respiratory disease, particularly in children, asthmatics, and healthy adults who participate in moderate exercise. Many areas of the United States, particularly those areas where refineries and chemical facilities are located, do not meet the National Ambient Air Quality Standard (NAAQS) for ozone. Ozone can be transported in the atmosphere and contribute to nonattainment in downwind areas.
Some species of VOCs are also classified as VHAPs. Some known or suspected effects of exposure to VHAPs include cancer, reproductive effects, and birth defects. The highest concentrations of VHAPs tend to be closest to the emission source, where the highest public exposure levels are also often detected. Some common VHAPs emitted from refineries and chemical plants include acetaldehyde, benzene, formaldehyde, methylene chloride, naphthalene, toluene, and xylene

## Slide 7: Hazardous Air Pollutants (HAPs)
Pb
Asbestos
Ni
O
O
DIOXIN
BENZENE
Benzo[a]pyrene
1,3-Butadiene
CHCl3
Notes: Some species of VOCs are also classified as VHAPs. Some known or suspected effects of exposure to VHAPs include cancer, reproductive effects, and birth defects. The highest concentrations of VHAPs tend to be closest to the emission source, where the highest public exposure levels are also often detected. Some common VHAPs emitted from refineries and chemical plants include acetaldehyde, benzene, formaldehyde, methylene chloride, naphthalene, toluene, and xylene

## Slide 8: Industrial Source Categories
8
Notes: Where do leaks come from well anywhere there is piping such as

## Slide 9
Notes: Oilfields (based on 1996 database for California.)
The biggest source in California.

## Slide 10
Notes: Refineries (based on 1996 database for California.)

## Slide 11
Notes: Petroleum marketing facilities (based on 1996 database for California.)

## Slide 12
Notes: Chemical Plants (based on 1996 database for California.)

## Slide 13
Notes: Various Fugitive Components

## Slide 14: EPA Source Categories
NSPS (40 CFR 60)
  SOCMIs (Subpart VV)
  Petroleum Refineries (Subpart GGG)
  Natural Gas Processing Plants (Subpart KKK)
  Polymer Manufacturing Plants (Subpart DDD)
  Oil & Natural Gas (Proposed Subpart OOOOb, c & Appendix K)
NESHAP (40 CFR 61)
  Benzene (Subparts J & V)
  Vinyl Chloride (Subpart F)
HON (40 CFR 63, Subpart H)
RCRA (40 CFR 264, 265, Subparts AA, BB)
  Hazardous Waste TSDFs
Notes: NESHAP (National Emissions Standards for Hazardous Air Pollutants): 40 CFR Part 61 Subpart V. Aimed at specific hazardous air pollutants.
  -Benzene ----- 40 CFR 61 Subpart J (incorporates V)
  -Vinyl Chloride -- " " F
HON (Hazardous Organic NESHAP): 40 CFR 63 Subpart H. Covers emission point at organic chemical plants and several other chemical mfr. processes. Does NOT apply to Petroleum Refining.
Hazardous WasteTransfer, Storage, Disposal Facilities:
Fugitive emissions from these are covered under RCRA - the federal Resource Conservation and Recovery Act. Not subject of this course.
Within source categories, these regulations further apply to specific equipment/hardware as we will see shortly....
REF: Handbook, p.6
Additional Information: Handbook, Ch. 2
Q. What are sources of most concern locally?
This is the tip of the iceberg for a more complete list
NSPS – New Source Performance Standards
Oil & Natural Gas Source Categories
  Proposed Subpart OOOOb applies to new (or modified or reconstructed after 11/15/2021)
  Proposed Subpart OOOOc applies to existing crude oil & natural gas facilities
  Proposed Appendix K is for determination of VOCs and GHG leaks using Optical Gas Imaging (OGI)
NESHAP – National Emission Standards for Hazardous Air Pollutants
HON – Hazardous Organic NESHAP
RCRA – Resource Conservation & Recovery Act

## Slide 15
Appendix A
Federal Regulations That Require a Formal LDAR Program With Method 21
40 CFR
Part Subpart Regulation Title
60 VV SOCMI VOC Equipment Leaks NSPS
60 DDD Volatile Organic Compound (VOC) Emissions from the Polymer Manufacturing
Industry
60 GGG Petroleum Refinery VOC Equipment Leaks NSPS
60 KKK Onshore Natural Gas Processing Plant VOC Equipment Leaks NSPS
61 J National Emission Standard for Equipment Leaks (Fugitive Emission Sources) of
Benzene
61 V Equipment Leaks NESHAP
63 H Organic HAP Equipment Leak NESHAP (HON)
63 I Organic HAP Equipment Leak NESHAP for Certain Processes
63 J Polyvinyl Chloride and Copolymers Production NESHAP
63 R Gasoline Distribution Facilities (Bulk Gasoline Terminals and Pipeline Breakout
Stations)
63 CC Hazardous Air Pollutants from Petroleum Refi neries
63 DD Hazardous Air Pollutants from Off-Site Waste and Recovery Operations
63 SS Closed Vent Systems, Control Devices, Recovery Devices and Routing to a Fuel
Gas System or a Process
63 TT Equipment Leaks – Control Level 1
63 UU Equipment Leaks – Control Level 2
63 YY Hazardous Air Pollutants for Source Categories: Generic Maximum Achievable
Control Technology Standards
63 GGG Pharmaceuticals Production
63 III Hazardous Air Pollutants from Flexible Polyurethane Foam Production
63 MMM Hazardous Air Pollutants for Pesticide Active Ingredient Production
63 FFFF Hazardous Air Pollutants: Miscellaneous Organic Chemical Manufacturing
63 GGGGG Hazardous Air Pollutants: Site Remediation
63 HHHHH Hazardous Air Pollutants: Miscellaneous Coating Manufacturing
65 F Consolidated Federal Air Rule – Equipment Leaks
264 BB Equipment Leaks for Hazardous Waste TSDFs
265 BB Equipment Leaks for Interim Status Hazardous Waste TSDFs
Note: Many of these regulations have identical requirements, but some have different applicability
and control requirements.
Notes: There are many types of sources that require LDAR programs with Method 21
There are additions since this was compiled most notibly VVa the SOCMI reg and GGGa the new refinery reg
The point of this list is not to be all inclusive but to show the numbers of times that LDAR Is used..

## Slide 16
Appendix B
Federal Regulations That Require the Use of Method 21 But Do Not Require a Formal LDAR Program
40 CFR
Part Subpart Regulation Title
60 XX Bulk Gasoline Terminals
60 QQQ VOC Emissions from Petroleum Refinery Wastewater Systems
60 WWW Municipal Solid Waste Landfills
61 F Vinyl Chloride
61 L Benzene from Coke By-Products
61 BB Benzene Transfer
61 FF Benzene Waste Operations
63 G Organic Hazardous Air Pollutants from SOCMI for Process Vents, Storage
Vessels, Transfer Operations, and Wastewater
63 M Perchloroethylene Standards for Dry Cleaning
63 S Hazardous Air Pollutants from the Pulp and Paper Industry
63 Y Marine Unloading Operations
63 EE Magnetic Tape Manufacturing Operations
63 GG Aerospace Manufacturing and Rework Facilities
63 HH Hazardous Air Pollutants from Oil and Gas Production Facilities
63 OO Tanks – Level 1
63 PP Containers
63 QQ Surface Impoundments
63 VV Oil/Water, Organic/Water Separators
63 HHH Hazardous Air Pollutants from Natural Gas Transmission and Storage
63 JJJ Hazardous Air Pollutant Emissions: Group IV Polymers and Resins
63 VVV Hazardous Air Pollutants: Publicly Owned Treatment Works
65 G CFAR – Closed Vent Systems
264 AA Owners and Operators of Hazardous Waste Treatment, Storage, and Disposal
Facilities - Process Vents
264 CC Owners and Operators of Hazardous Waste Treatment, Storage and Disposal
Facilities - Tanks, Surface Impoundments, Containers
265 AA Interim Standards for Owners and Operators of Hazardous Waste Treatment,
Storage, and Disposal Facilities – Process Vents
265 CC Interim Standards for Owners and Operators of Hazardous Waste Treatment,
Storage, and Disposal Facilities - Tanks, Surface Impoundments, Containers
270 B Hazardous Waste Permit Program – Permit Application
270 J Hazardous Waste Permit Program – RCRA Standardized Permits for Storage
Tanks and Treatment Units
Notes: And just as many types of sources that use Method 21 but do not require an LDAR program

## Slide 17: Sources of equipment leaks
Pumps
Valves
Connectors
Sampling connections
Compressors
Pressure relief devices
Open-ended lines
Notes: More specifically within those plants

## Slide 18: Equipment component counts at a typical refinery or chemical plant(1995)
Component Range Average
Pumps 10 – 360 100
Valves 150 – 46,000 7,400
Connectors 600 – 60,000 12,000
Open-ended lines 1 – 1,600 560
Samp connections 20 – 200 80
Pressure relief valv 5 – 360 90
Notes: This is 1995 information the use of unwelded connections has been reduced welded connections eliminates the possibility of leaks as well as open ended lines are now either eliminated or are double valved or capped/plugged

## Slide 19: Uncontrolled VOC emissions at a typical facility (1995)
Component Percent of Total Emissions Pumps 3
Valves 62
Connectors 31
Open-ended lines 1
Sampling connections 2
Pressure relief valves 1
Total uncontrolled emissions 653 T/y
Notes: Again this is 1995 data and it has shifted some however valves and connectors are still the largest contributors

## Slide 20: Component Population and Fugitive Emissions Profiles
Notes: Another way of looking at this This is only one refinery the numbers are not there as absolutes but graphically you can see the mix
This is an average of data for a particular refinery. Different process units in a facility will have different profiles.
Discuss
REF: Pollution Prevention for Chemical Processes, David Allen and Kirsten Rosselot, Wiley-Interscience, [Date?]

## Slide 21: Leaks happen
Where
Why
How

## Slide 22
Valves
Notes: Show Photo Slide -- Typical Valve
3 categories of valves:
  Block for on/off control
  Control for flow rate control
  Check for directional control. Check valves don't have stems (potential leak area), so not discussed here.
  Flow control valves have highest leak potential because process material can erode seal.
REF: Benzene Equipment Manual, p.3-2

## Slide 23
Manual Globe Valve
Handwheel
Stem
Packing Nut
Packing
Bonnet
Disk
Seat

## Slide 24
Control Valve

## Slide 25
Ball Valve
Potential Leak
Areas
Notes: REF: p. 33
Used for open-ended lines where samples might be drawn.
Not good for high pressure applications.
Q. Why do valves leak?
Refer to Handout: "Reasons for Valve Leaks"
There are other types of valves such as? .....student responses
We have covered main types here.
  Note that Check Valve, Butterfly Valvemay not actuated externally; therefore, not as likely to have fugitive leaks. Still need to be inspected.

## Slide 26
Gate Valve
Notes: Good view of valve stems (use of saps map warp stems and increase the potential for leaks.

## Slide 27: Types of Valve Seals
Packing Gland
O-Rings
Bellows Seal
Diaphragm
p. 33, 34
Notes: Most leaks are from around the valve stem. There are a number of strategies to minimize these leaks.
(Display hardware if available)
  Packing Gland:
  Standard method of minimizing leaks. Shown in previous slides. Packing materials include braided asbestos, graphite, graphite-impregnated fibers, Teflon. Progressive tightening until seal fails.
  O-Rings:
  not suitable where there is sliding motion in valves. Used in pressure relief valves or PRVs.
  REF: Handbook, pp. 33-34.
  Additional Information: Manufactures Literature-Components section

## Slide 28: Bellows Valve/Seal
Metal
Bellows
Notes: REF: Cutaway drawing, Handbook p.34
Bellows Seal very effective. Stem isolated from process fluid by pleated metal case. However, it is weak point in system because of fatigue of metal pleats. Often have conventional gland seal backup.
Considered "best available control technology" (BACT), or "no detectable emissions" valve. From regulatory inspection standpoint, this means emissions readings must less than 500 ppm above background concentration and that less frequent inspections required of operator (generally annual only).
High-tech alternative is "Live-Loading" technology, where a set of springs is placed between the outside tightening bolts to place a sustained load on the packing. Used in nuclear industry where leaks cannot be tolerated.
Cost differential e.g.: Gate Valve may cost $250; Bellows upwards of $1200.
Addtional Information: Manf Literature-Chesterton Live Loading

## Slide 29
Diaphragm Valves
Weir Diaphragm Seal
Bonnet Diaphragm Seal
Notes:   Diaphragm completely isolated process fluid from stem. Recommend for abrasive fluids and operate under medium pressure.
  Also BACT.
  REF: Handbook p.34

## Slide 30: First Attempt at Repair for Valves
Tightening bonnet bolts
Replacing bonnet bolts
Tightening packing gland nuts
Injecting lubricant into lubricated packing
Notes: EPA regulations identify the "first attempt" at repair; Most valve leaks can be repaired using these procedures:
...Read list from slide
Other procedures? [eg, retrofit with injected sealant]
For flanges and other connectors, first attempt would involve tightening bolts and replacing gaskets.
If these standard approaches are not successful, component may have to be replaced. Some regulations specify upgrading replaced components with BACT or MACT components.
REF:
Additional Information:

## Slide 31: Types of Pumps
Centifugal
Rotary
Reciprocating
Canned
Diaphragm
Magnet Drive
Notes: Although there are six types of pumps the industry uses mainly the first three predominantly and then mostly the centrifugal
There are fewer pumps and compressors at most operations, but these components likely to have higher leak rates than valves.
Types of Pumps include: Read Slide
Centrifugal Pump far and away most common type used.
Canned, Diaphragm, Magnet Drive are "leakless" types that will be described in section on pump seals.
REF: Handbook pp.27-29

## Slide 32: Centrifugal Pump
Potential Leak
Flow Line
Impeller
Notes: REF: EPA Seminar Publication, Organic Air Emissions from Waste Management Facilities, EPA/625/R-92/003, August 1992.
Impeller moves liquid through pump using principle of centrifugal force. Shaft that powers impeller penetrates housing--> potential leak site.

## Slide 33
Notes: Pump seal location.

## Slide 34: Centrifugal Pump
Notes: And in real life from the outside it looks like this

## Slide 35: Rotary Pump
Notes: Describe Operation::
Mechanical displacement of liquid produced by rotation of gear or gears within stationary housing. As spaces between teeth of impeller gears pass the suction opening, liquid is trapped between them carried around casing to discharge opening, and forced through opening as indicated by arrows.
Close tolerances, so cannot handle abrasive materials.
REF: EPA Course #380, Reference Volume 3- Inspection Manuals, Benzene Equipment Leak Manual, pp. 3-14 to 3-17.
Reciprocating ---> NEED INFO

## Slide 36: Types of Pump Seals
Simple Packed Seal
Basic Single Mechanical Seal
Dual Mechanical Seal
Seal-Less
Diaphragm Pump
Magnet Drive Pump
Notes: These are major and not-so-major types of pump seals. Packed and Single Mechanical most commonly used.
First 3 listed pump seals will leak somewhat; i.e., most pump will have some leaks. Mechanical can leak at rate of 0.1 -0.4 cu. in. per hour.
REF: Handbook p. 27-29.

## Slide 37
xxxxx
Simple Packed Seal
23
Notes: REF: p. 27.
Packed Seal must be cooled by fluid or other lubricating fluid. Used for reciprocating or rotary shafts. Easy to replace but need frequent adjustment.

## Slide 38
Basic Single Mechanical Seal
Spring
Shaft Packing
Rotating Seal Ring
Seal Face

## Slide 39
Rotating Face
Stationary Face
Quench Port
Flange Bushing
Flush Port
Seal Flange
Shaft Sleeve
Low Emission Mechanical Seal
Courtesy BW/IP International, Inc.
Notes: Describe Operation:
  Stationary element and rotating ring held together tightly to form lapped seal face. Surfaces pushed together by combination of spring pressure and fluid pressure from liquid being pumped. Rotating element attached to shaft with an elastomer or gasket; stationary ring sealed to stuffing box with elastomer or gasket. Other areas also sealed. Any place where rotating and stationary surfaces meet must be lubricated, but much less than packed seal.
  Some mechanical seals fits with ports for sealing fluid/heat dissipation Fluid may be vented to control device which may be independently regulated.
Limited to rotary shafts.
Additional Info:
- EPA Course #380 Student Manual p. 2-6, 2-9.
- BW/IP International literature.

## Slide 40
xxxxx
26
Double Mechanical Seal
Seal Face
Seal Face
Inner Seal Assembly
Outer Seal Assembly
Notes: REF: Handbook, p 28.
Double or Dual Mechanical Seal:
  Function in same way as Single Mechanical Seal. In back-to-back arrangement shown, cavity between seals filled with barrier fluid (sealing liquid) under pressure for seal and lubrication. More durable than single mechanical seal.
Dual Mechanical Seals are BACT according to EPA.
  Terminology used is "no detectable emissions" type of seal. Regulations stipulate less frequent monitoring compared with packed or single mechanical seals, but failure sensor and alarm required.
Seals can also be arranged in tandem, where one seal is a backup, or face-to-face. Sealing or barrier fluid usually at lower pressure than fluid being pumped, so potential for leakage of process fluid into barrier fluid chamber and into atmosphere. Barrier fluid reservoir may be vented to VOC control device.

## Slide 41: Centrifugal Pump with Double Mechanical Seal
Notes: This one has a double mechanical seal (I think), so emissions should be low or none. If this is a BACT component, inspection frequency may be less per district rules.

## Slide 42
xxxxx
Seal-Less Canned Motor Pump
27
Notes: REF: p. 29.
Describe diagram:
Single moving part, a combined rotor-impeller assembly driven by the magnetic field of an induction motor. Stator windings prevented from contacting process fluid by corrosion-resistant liner. Process fluid is sealing fluid.
Organic solvents, light oils, toxics. Abrasives cannot be tolerated. Tend to raise temperature of process fluid, so not good for flammables.
(REF: "Eliminate Pump Seals with Magnet Drives", Plant Engineering, Jan 24, 1991, pp. 36-41)
Used when leakage would result in loss of valuable product or when toxic air emissions are a concern; e.g. facilities handling RCRA hazardous waste.

## Slide 43
xxxxx
29
Diaphragm Pump
Piston
Diaphragm
Notes: REF: Handbook, p. 29. Describe Operation:
  Shaft seals not exposed to process liquid.
  Typically air powered, so inherently explosion proof.
  Used for hazardous or toxic materials.
  BACT (REF: "Eliminate Pump Seals with Magnet Drives", Plant Engineering, Jan 24, 1991, pp. 36-41)

## Slide 44
xxxxx
30
Magnet Drive Pump
Notes: REF: EPA Course #380, Instructor Manual, p. 2-71.
Describe Operation:
Do not have shaft seal. Pump rotor (torque ring) magnetically coupled to motor. Magnetic flux passes through containment shell via outer magnetic ring to turn impeller shaft.
(REF: "Eliminate Pump Seals with Magnet Drives", Plant Engineering, Jan 24, 1991, pp. 36-41)
Considered "No Detectable Emission" technology by USEPA.
Used when leakage would result in loss of valuable product or when toxic air emissions are a concern; e.g. facilities handling RCRA hazardous waste.

## Slide 45
Magnet Drive Pump
Notes: REF: EPA Course #380, Instructor Manual, p. 2-71.
Describe Operation:
Do not have shaft seal. Pump rotor (torque ring) magnetically coupled to motor. Magnetic flux passes through containment shell via outer magnetic ring to turn impeller shaft.
(REF: "Eliminate Pump Seals with Magnet Drives", Plant Engineering, Jan 24, 1991, pp. 36-41)
Considered "No Detectable Emission" technology by USEPA.
Used when leakage would result in loss of valuable product or when toxic air emissions are a concern; e.g. facilities handling RCRA hazardous waste.

## Slide 46: Types of Compressors
Centrifugal
Reciprocating
Rotary
Notes: Compressors are really pumps for gasses so they work pretty much the same
Read list, adding details:
Centrifugal most common. Rotating element/blades increase pressure of gas by centrifugal force.
Reciprocating increase pressure by confining gas in cavity and progressively decreasing volume.
REF: Handbook, p 29.

## Slide 47: Types of Compressor Seals
Labyrinth
Restrictive Ring
Mechanical
Packed
Liquid-Film
Notes: There are several types of seals and since they are meant to keep gases in they have to be tighter than pump seals
Types of Compressor Seals: Read list from slide
These are pictured on p. 30, Fig 3-6. "Typical designs of mechanical compressor seals. Brief discussion of each type to follow (next slides).

## Slide 48
Port for scavenging or inert gas sealing
Internal
gas pressure
Atmosphere
Atmosphere
Internal gas pressure
Port for sealing
Scavenging port for vacuum application
Labyrinth Seal Restrictive Ring Seal
Notes: REF: Handbook p. 31.
Labyrinth Seal: Series of close-tolerance, interlocking teeth. Fairly high leak potential.
Restrictive Ring: Series of stationary carbon rings with close shaft tolerance. Lower leak rates than labyrinth.

## Slide 49
Liquid Film Compressor Seal
Notes: REF: Handbook p.30.
Review slide:
Seal is film of oil that flows between rotating shaft and stationary gland. Oil leaves system contaminated with process gas. Oil returned to reservoir and VOCs/VHAPs released to atmosphere or vented to control device. (REF: Handbook p.31.)
No slides of following:
Mechanical Seals: Rotary compressors. Similar to pump mechancal seals. Lowest leak rates for compressor seals. (REF: Handbook p.31.)
Packed seals: Reciprocating compressors (REF: Handbook p.31.)
All compressor seals leak somewhat. Many are equipped with closed vent systems to duct emissions to control device. If so equipped, compressor may have to be monitored more frequently than if not equipped with CVS. The venting systems and control devices are also regulated as discussed earlier.

## Slide 50: Screening a Compressor
Notes: These are more prone to leak than many other components., except maybe PRVs.

## Slide 51: Closed Vent Systems
Designed and operated for no detectable emissions
Monitored at startup, annually, and as required by agency
Facility owner/operator must verify operating parameters

## Slide 52: Control Devices
Vapor Recovery Systems - 95% efficient
Incinerators/Oxidizers - 95% efficient or minimum residence time and temperature
Flares - Several conditions

## Slide 53: Pressure Relief Devices

## Slide 54
Pressure Relief Valve
Notes: (REF: p. 31.)
Review Diagram--Spring-Loaded PRV:
Set at certain pressure, e.g., 1 lb. Must be checked after release for proper reseating. Simmering or popping noise indicates improper seating. Some have cables that indicate PRV has blown.
Show Photo Series:
    Spring-Loaded PRV
    Disassembled PRD- Photo

## Slide 55
Spring-Loaded Pressure Relief Valve
Seat
Disk
Nozzle
Spring
Notes: (REF: p. 31.)
Review Diagram--Spring-Loaded PRV:
Set at certain pressure, e.g., 1 lb. Must be checked after release for proper reseating. Simmering or popping noise indicates improper seating. Some have cables that indicate PRV has blown.
Show Photo Series:
    Spring-Loaded PRV
    Disassembled PRD- Photo

## Slide 57
PRV with Rupture Disk
Notes: Describe Diagram -- Rupture Disk Upstream of a Relief Valve:
  Provides backup if disk ruptures. Used where atmospheric venting undesirable.
  REF: Handbook p. 32.

## Slide 58
Screening Non-Vented PRVs

## Slide 59
Open-Ended Line

## Slide 60
Sight Glass

## Slide 61: Connectors
Flanges
Threaded
Welded

## Slide 62: Flanges
Notes: In the past bolted joints leaks have been a problem and little was done to eliminate the problem
Recently new gasket materials and new bolting techniques have made improvements

## Slide 63: Threaded
Notes: Threaded joints can still leak if there is insufficient tightening or thread length for the pressure contained in the stream

## Slide 64: Welded
Notes: Once a joint is welded it is no longer considered a joint and is therefore no longer in the system.
As a method of reducing components and hence leaks many new installations ore using welded joints rather than flanges or threaded joints
They can come in almost any size from 1 inch to greater than 48 inches

## Slide 65: AND NOW TO PUT IT ALL TOGETHER

## Slide 66
Counting Components
Valve
Flange
Flange
Screen here
Screen here
Screen here
Notes: Counting the components is not necessary but to look at the individual components in the picture shows that in a short time the number of components can climb It is on EPAs hit list of common errors in LDAR

## Slide 67
Counting Components
Valve
Connection
Screen here
Open-End Line
Screen here
Screen here
Notes: Open-Ended Lines (aka open-ended valves): If a short piece of pipe is attached to the end of a valve, but no pressure buildup, system is an open-ended line. This setup may be considered a violation It requires a second valve a cap or a plug

## Slide 68
Open-Ended Line?
Notes: Two valves in series, both closed (double block and bleed?), the open end of the second valve is not considered an open-ended line. However in this case the second valve has been left open and it is a violation System is 2 valves. Plugs or caps at the end of a line are connectors or flanges. NOTE: Should be plug in end of pipe.

## Slide 69
How many components do you count?
Notes: Work in groups

## Slide 70: Estimating Component Emissions
Average Emission Factors
Screening Value Ranges
Correlation Equations
Unit-Specific Correlation Equations
Notes: Why quantify Fugitive emission EPA and agencies need them for permit and Title V fees
TRI requires it
Corperate many times wants to know
Having an idea of how much components leak affects overall facility inventory and (increasing) regulatory strategies. To generate emission factors, some kind of sampling of actual emissions from each component is required. This involves bagging components, measuring mass emissions collected in the bag, and correlating with portable instrument readings for each component. Then the following data manipulation procedures can be applied:
Average Emission Factors:
- Apply one generic factor for a component to all such components
- Least accurate, but quickest.
- AP-42 has factors for petroleum refinery components; these have been used to estimate SOCMI emissions.
- Newer, generally lower EFs available from CAPCOA, EPA.
Illustrate with next slide now, then back to this one.
Screening Value Ranges:
- Use OVA to scan background concentration.
- Greater than 10,000 ppm ="leaking" --> Determine % of components leaking --> Apply "leaking EF" --> Total Emissions from "Leaking" Components.
- "Non-leaking" components --> apply "non-leaking" EF = 2% of leaking
Illustrate with 2nd next slide now, then back to this one.
Correlation Equations:
-OVA-measured concentrations for each component areentered into an equation that correlates screening values within a certain rangewith emissions generated from bag sampling. Components with screening values above or below this range are still counted as either default zeros or pegged, each of which have an emission factor assigned.
Unit-Specific Correlation Equations:
I.e., facility does its own bagging study or equivalent to come up with unique correlation equations for particular components.

## Slide 71: Types of service
Gas/vapor service
Liquid service
  light liquid service
  heavy liquid service

## Slide 72: In VOC or HAP service
  VOC -- 10% by weight VOC
    NSPS
    HAP– 5% by weight total HAPs
    MACT/NESHAPs

## Slide 73: Gas/Vapor service
The equipment is in gas or vapor phase at the operating conditions
Temperature / Pressure

## Slide 74: Liquid service
The equipment is not is gas or vapor service

## Slide 75: Light liquid service
The total concentration of the organic compounds having a vapor pressure > 0.3 kPa at 20o C and
=>20% by weight of the total process stream and Is a liquid
Notes: A kilo pascal one newton per sq meter and about 1% of 1 atmosphere so we are not talking a lot of vapor pressure

## Slide 76: Heavy liquid service
Means a piece of equipment is not in gas/vapor or in light liquid service
Notes: It is the catch all for the rest of the liquid

## Slide 77
1995 EPA Protocol Refinery
Average Emission Factors
Component
Service
Emission Factor (kg/hr)
Valves
Pump Seals
Compressor Seals
Pressure Relief Valve
Connectors
Open-Ended Lines
Sampling Connections
Gas/Vapor 0.0268
Light Liquid 0.0109
Heavy Liquid 0.00023
Light Liquid 0.114
Heavy Liquid 0.0210
Gas/Vapor 0.160
0.636
0. 00025
0.00230
0. 0150
Gas/Vapor
All
All
All
Notes: These are most recent factors featured in California Implementation for Estimating Mass Emissions of Fugitive Hydrocarbon Leaks at Petroleum Facilities, February 1999, CAPCOA and ARB/SSD. (http://www.arb.ca.gov/fugitive/fugitive.htm)
Note which component has highest Emission Factor (Compressor) and which constitute the highest percent of total (Valves). Even though most emissions from valves, only a small percentage of the hundreds or thousands of valves in a facility actually have significant leaks. (TQ# )
Old REF: Handbook, p. 65, Table 7-1.

## Slide 78
1995 EPA Protocol Refinery
Screening Value Range Emission Factors
Component
Service
< 10,000 ppm Factor (kg/hr)
Valves
Pump Seals
Compressor Seals
Pressure Relief Valves
Connectors
Open-Ended Lines
Gas/Vapor 0.00060
Light Liquid 0.0017
Heavy Liquid 0.00023
Light Liquid 0.0120
Heavy Liquid 0.0135
Gas 0.0447
0.0894
0.000060
0.01195
All
All
All
0.2626
0.0.0852
0.00023
1.608
1.691
0.00150
0.437
0.3885
0.0375
> 10,000 ppm
Factor(kg/hr)
Notes: Based on assumption of only 2 emission rates and 2 populations of components: Leaking and Non-Leaking. Requires field screening to get percentages of leaking and non-leaking.
Q. Now which type of component has highest leak rate?
There are at least 7 other inventory methods used by districts and industry groups. In determining which emission factors to use, must refer to local authority.
CAPCOA Guidelines provide some statewide standardization. Some emission factors are different from EPA, notably: SV Ranges for Oil and Gas Production and Correlation Equation for Refineries and Marketing Terminals.
These values might be multiplied by ROG/TOG to get more accurate estimate of reactive hydrocarbons for inventory purposes. Usually, this means factoring out methane, so operator must know proportion of methane in process stream.
Old REF: Control Techniques Handbook, p. 67, Table 7-2.

## Slide 79
REGULATIONS
& STANDARDS
Notes: In this section we will look at the format and discuss the content language of typical fugitive VOC rules.

## Slide 80: Generic Fugitive VOC Emissions Regulations
Applicability
Exemptions
Definitions
Equipment Leak Standards/ LDAR Standards
Identification Requirements
Recordkeeping Requirements
Test Methods
Compliance Schedule
Notes: This would include repair timing
Generic Fugitive VOC Emissions Rule might contain these sections:
Read list from slide
Definitions usually near the beginning. Include levels of VOC emissions that constitute a "leak"
Glossary for this course starts on p. 134 in Portable Instrument User Manual.
Let's look at most of these sections in more detail.....

## Slide 81: Applicability
Source Category
Process Unit
Equipment in process unit
Process gas/fluid
Notes: How do you determine if a regulation applies? For federal regs, you have to look at the following: Read Slide
Source Category: Refineries, SOCMIs, etc.
Process Unit: Equipment assembled to produce a chemical as an intermediate
Or final product, which can operate independently if supplied with sufficient
storage facilities for the product. E.g., fluid catalytic cracking unit.
Handbook p. 130 gives list of process units. In practice, helps delineate
equipment actually regulated in a larger facility.
Equipment: = valves, pumps, compressors, etc.
Process gas/fluid: = What's in the process stream.
Rules generally apply to equipment "in VOC service;" EPA defines this as at
least 10% VOC by weight. Presumption that ALL equipment is in VOC service
unless shown otherwise by source. NSPS regulations further broken down into
Gas/Vapor, Light Liquid, Heavy Liquid, Liquid Service. ASTM methods may
be used to confirm type of organic fluid in process.
REF: Handbook pp. 13-15

## Slide 82: Types of Standards
Performance Standards
Equipment Standards
Work Practice Standards (LDAR)
Notes: These are the types of enforceable standards that apply to regulated equipment. Essentially translate into regulatory strategies.
Performance Standards - Allowable emission limits over time or a % reduction.
For most components, this is impractical because bagging of each component would be required to determine compliance. Certain components may be designated as "no detectable emissions" for purposes of compliance. A reading of less than 500 ppm above background indicates such components are in compliance with "no detectable emissions" designation. This is BACT that allows source to inspect components less frequently. Equipment Standards - Use, design, or operation of a particular piece of equipment.
E.g., an open-ended line equipped with cap, blind flange, plug, or 2nd valve. Design would involve specifying operational parameters. Operational standards would say that equipment is in compliance if operated in specified manner. Work Practice - Monitoring of components at regular intervals and repair, aka, "Leak Detection and Repair/LDAR." This is by far the most widely applied standard.
Another type of work practice standard is "evidence of a leak" for pumps and valves carrying heavy liquid, PRDs, flanges, and connectors; e.g., discoloration. This goes back to the MACT as layed out in the CCA 90
As we get better at LDAR we have found that the leaking rate can go down to almost nothing with the use of better packing and maintenance practices

## Slide 83: Leak Detection and Repair Standards
Inspection Frequency
Definition of Leak
Repair Interval
Percentage Leaking
Notes: Focus on Work Practice Standards = LDAR. 2 phases of LDAR program - Detection and Repair or Replacement of leaking components.
Sections of a regulation that establish compliance points for an LDAR program are: Read Slide ; elaborate from notes
We will discuss the standards later but remember the use of more frequency, a lower leak definition , faster repair leads to less emissions
Repair Interval: For valves, CFR also specifies "first attempt" repair methods. EPA regs may also have standards for equipment to be used, its design, and its operation; e.g. "no detectable emissions" (BACT), though this is usually optional. Some California districts (e.g. SCAQMD) require that problem components be replaced with BACT components.
Percentage Leaking: EPA has limit for different components. For VHAP, limited to 2% (or less in some districts, e.g. BAAQMD). Percentage of those listed as "delayed repair" or "non-repairable" also limited (????%)

## Slide 84
Inspection Frequency
Regular Compliance Inspection (monthly, quarterly, annually, etc.)
Daily or Weekly Visual Inspections
Inspection Interval After Repair
Inspection Interval After Turnaround
Notes: Refer to local regulations if possible
Inspection Frequency; How often does the operator need to inspect components?
1. Components typically are monitored monthly or quarterly. Components that are consistently in compliance my be put on a semi-annual or annual schedule.
Inaccessible components or Difficult-to-Monitor --> annual inspections. Under EPA regs., components declared "no detectable emissions" type (i.e., BACT) can skip monitoring periods if successive inspections reveal <2% leakers. This can significantly reduce costs of LDAR for 100's or 1000's of valves.
[OPTIONAL: Look at Skip Period table, page 51 of Handbook. Under "Skip Period" approach, penalty for not achieving performance levels is return to quarterly monitoring]
2. Daily or Weekly Inspections typically required for Pumps and Compressors. SCAQMD require every 8 hours; BAAQMD requires every 24 hours. Pumps and Compressors using "no detectable emissions" seals still must be inspected visually. (REF: SCAQMD Rule 1173 Operators Handbook p.7, BAAQMD Regulation 8)
3. Inspection Interval After Repair typically 15 days, but depends on rule and component. PRVs may have to be monitored no later than 5 days after pressure release per EPA (ARB RACT recommends 3 days). Pump or valve in heavy liquid service and flange or other connector suspected of leaking must be monitored within 5 days.
4. Inspection After Turnaround allowed if component is "essential". In this case, inspection must take place during some definite period after process shutdown and component repaired or (more likely) replaced.
REF: Handbook Ch 2. Additional Information: - CAP Petroleum Refineries manual

## Slide 85: Definition of Leak
Basic standard: 10,000 ppm
Range: 50,000 ppm - 100 ppm
Liquid leaks : 3 (or more) drops per minute
Other definitions
Notes: 10,000 ppm is NSPS and most local regs. Trend is toward lower.
  NSPS: "No detectable emissions" components must register < 500 ppm above background or increased frequency of inspection required.
  HON: Valves phase-in standard of 500 ppm. Pumps phase-in standard of 1000-5000 ppm (depends on application).
  EPA is using a lower def of leak as negotiated during enforcement as low as 100 ppmv
Liquid leaks very straightforward. Count drops.
Other definitions: Visual, audible, or olfactory
  Under EPA regs - discolored flange must be monitored within 5 days;
  compressors - sensors for seal system or barrier fluid system indicate failure.

## Slide 86: HON LDAR Standards for Valves
500 ppm
Quarterly LDAR
Monthly LDAR
Semi-annual
LDAR
Annual
LDAR
QIP
< 1%
500 ppm
< 0.5%
500 ppm
> 0.5%
500 ppm
>1%
500 ppm
< 2%
500 ppm
> 2%
500 ppm
or
86
Notes: Standards for valves and also for pumps were phased in starting in 19???. (REF: APTI Course 050-94, Final HON Rule, July 1994, p.28.)
QIP=Quality Improvement Program:
Consists of information gathering, determining superior performing technologies, and replacing poor performers with superior technologies until target performance level met. Recognition that low leak definitions may not be easily achievable for each component. Provisions allow plants to develop process-specific and cost-effective methods for improving emissions performance without violation "hammer" looming.
(REF: EPA Course #380, Reference Volume 1: Equipment Leak Regulations, Section 1-3, "HON")
Pumps:
Similar phase-in periods. MONTHLY monitoring in all cases. Phase II is 5000 ppm. Phase III is 1000-5000 ppm depending on application. Provision for QIP, but not for reduced LDAR.
Other alternative approaches available for other components; e.g, flanges can be stretched to 6 mos and then to 1 year.

## Slide 87: Repair Interval
Basic standard: 15 days
First attempt: 5 days
Range: 1-15 days
Repeat leakers: Possible replacement
Delay of Repair: Until next shutdown (DOR) 6-month to 5-year limit
Percentage awaiting repair
Notes: Basic standard (NSPS, many locals): Most leaking components must be repaired within 15 days.
First attempt at repair must be made within 5 days and record kept. For valves, types of repair specified in regs.
Range varies from 1 - 15 days:
SCAQMD has 1-day deadline for leaks >50,000 ppm and liquid leaks. BAAQMD has 7-day deadline for leaks discovered by operator; 24 hrs for leaks discovered by district inspector. (REF: SCAQMD Rule 1173 Operators Handbook p.11, BAAQMD Regulation 8)
Repeat Leakers: Replacement optional under NSPS.
Some California districts mandate BACT after valve leaks certain number of times during over a period. ARB RACT recommends BACT after 5 repeat leaks over one year, or one leak for inaccessible component. (REF: ARB RACT/BARCT SSD-93-002)
Delay of Repair: Usually allowed until next shutdown of process, with time limits from 6 months to 5 years.
Other stipulations: Allowed if repair technically infeasible without process unit shutdown. Allowed if equipment isolated from process and does not remain in VOC or VHAP service. Allowed if emissions from purging material from system for immediate repair are likely to be greater than fugitive emissions from delay. Delay for valves may be allowed if spare parts not available, but source should have had enough on hand prior to repair. (REF: Handbook p.18) DOR except for pumps which if parts are not available can go beyond the first shut down
IT IS IMPORTANT TO NOTE THAT OTHER THAN FOR PUMPS IN THE DOR THERE IS NO DOR JUSTIFCATION FOR LACK OF PARTS
Percentage awaiting repair becoming more stringent:
E.g., BAAQMD will allow only 0.5% valves to be designated as "awaiting repair" starting 1997. (REF: BAAQMD Regulation 8)

## Slide 88: Component Identification
Tags
  Inaccessible components tagged
  Leaking components: brightly-colored, waterproof tag with date leak detected, other info
P & IDs
Notes: What types of identification do you use/encounter? E.g., SCAQMD has Identification Plan.
What are the pros and cons of different types?
What do you do if you don’t know whether or not to monitor?
Identification code tag:
EPA has recommendations about Identification code numbers. ID code may be designed to show type of component, location or process unit, composition of stream, etc. Any logical system that works for facility and for leak contractor (if there is one) is sufficient. EPA only requires tagging for leakers.
Inaccessible components:
Access refers to whether or not components are "unsafe" or "difficult to monitor". Unsafe to monitor components cannot be reached without reaching up or out from ground or platform a certain distance (EPA - no more than 2 meters above platfom; BAAQMD policy - 6 feet out, 14 feet up.) Important in determining frequency of monitoring.

## Slide 89: Recordkeeping Requirements
1. Component ID code, description, process unit, service, material transported, concentration, compliance method
2. Dates of inspection
3. Emission levels (compliance or leak) and method of detection
4. Dates of repair (or attempt) and reinspection
5. Emission levels after repair or replacement
6. Repair delayed, reason, expected date of repair
7. List and number of components awaiting repair
8. Portable monitoring instrument records
Notes: 1. These records should be kept for all components.
NSPS and NESHAPS explicitly requires records for equipment designated "no detectable emissions", PRVs in gas/vapor service, equip't in vacuum service. Also list inaccessible/unsafe, difficult-to-monitor. Closed-vent systems and control devices require special records (REF: Handbook p. 49). Process stream determination needed for NESHAP.
2. Dates: Should include monitoring dates for no detectable emissions components and for alternative standards.
3. Emission levels: Should include background level
6. If repair delayed till shutdown, signature of operator required. If process unit shutdowns occur while leak remains unrepaired, dates must be recorded.
8. Obtain monitoring instrument records from facility or contractor.

## Slide 90: Reporting Requirements (NSPS, NESHAP)
Notification of Construction or Reconstruction
Initial Semiannual Reports
Semiannual Reports
Percentage of Valves Leaking
Notes: Under NSPS and NESHAP, the main reports that must be filed are:
  Notification of Construction or Reconstruction
  Initial Semiannual Reports (Appendix F, p.123)
  Semiannual Reports (Appendices E, G, H, I, J)
Percentage of Valves Leaking necessary for NSPS sources using one of two alternative standards:
  Maximum 2% leakage determined by annual performance test,
  2) Skip-period LDAR, an alternative work practice standard
  Skip Period approach gives plant flexibility to implement its own LDAR program or to install valves with lower probabilities of leaking.
  Penalty structure: Under option 1), >2% leaking components would result in violation and penalties. Under option 2) the only penalty would be to return to routine quarterly monitoring.

## Slide 91: Test Methods
EPA Method 21
EPA Method 25
ASTM Methods
Alternative methods
Notes: EPA Method 21 used for fugitive leak monitoring and quantification for compliance. See p 94 of Handbook.
For flares from associated control equipment, use Method 22 for VEE.
EPA Method 25 for efficiency of control devices.
ASTM Methods pertinent to fugitive VOC inspections:
  D-86: Initial boiling point; i.e., evaporation at 150ºC.
  E-260, E-168, E-169: Weight % VOCs .
  D-2267: Weight % VHAPs .
  D-287: API gravity crude oil.
  D-4457: Exempt compounds
Alternative Methods: the main alternative method is the infrared imaging
e.g., engineering judgement. Source must prove validity of alternative.
Ring Sensors
HVCS

## Slide 92: Portable Hydrocarbon Analyzers
Types of VOC Analyzers
Response Factors
Method 21
Factors in Selection and Use
Safety Concerns
Notes: Topics to be covered in this section: Read Slide
Refer to Chapter 4 in Handbook. Additional details can be found in Portable Instrument User's Manual.

## Slide 93: Types of Analyzers Used for Fugitive Inspections
Flame Ionization Detector (FID, OVA)
Catalytic Combustion Analyzer (CCA, TLV)
Photo Ionization Detector
(PID)
Notes: Types of VOC Analyzers include: Read Slide
Infrared Analyzer is another type, but not often used for fugitive VOC inspections. IR good for specific, known compounds; ones shown here better for general VOC emissions inspections.

## Slide 94: LDAR Equipment/Methods
Organic Vapor Analyzer (OVA)
Threshold Limit Value Meter (TLV)
Flame Ionization Detector (FID)
Photoionization Detector (PID)
Infrared Detector (FLIR)
Look and Listen
  Soap Solution
  Visual Distortion
  Odor

## Slide 95
Century
OVA 108

## Slide 96
OVA 108
Readout

## Slide 97
VOC Analyzer Using PID
Dilution Air Intake
Notes: Photoionization Analyzer Operating Principles
  1. Sample gas drawn in continuously
  2. Organic vapor ionized by absorption of UV radiation
  3. Positive ions collected on negative electrode
  4. Current is amplified and measured
Instrument Characteristics: PIDs equipped with UV lamp of specific eV energy. Generally all compounds with ionization potention less than the ionization energy of the lamp are detected. Because the ionization potential of major components of air (O2, N2, CO, CO2, H2O) greater than ionization energy of lamp, no interference problems.
Only small fraction of organic vapor ionized; therefore, response of PID instruments insensitive to sample gas flow rate. Also sensitive to air infiltration prior to detector. Most effective for low concentrations of aromatics. Not effective for low molecular weight aliphatics such as methane and ethane.

## Slide 98: Analyzer with PID and FID
Notes: TVA will allow reading of carbon ions per unit time, but same conversion to volume/volume (ppm) is the normal approach.

## Slide 99
FOXBORO TVA – 1000 (Toxic Vapor Analyzer)
Notes: TVA will allow reading of carbon ions per unit time, but same conversion to volume/volume (ppm) is the normal approach.

## Slide 100
Catalytic Combustion Analyzer (TLV)
Sample Inlet
Sample Outlet
Sample Outlet
Catalyst-Coated Filament
Reference Cell
To Wheatstone Bridge
Notes: AKA: "TLV"= Threshold Limit Value meter. Used to determine exposure levels for health and safety purposes; i.e., whether health-based threshold limit value for particular chemical has been exceeded.
Catalytic Combustion Analyzer Operating Principles
  1. Sample gas is drawn in continuously.
  2. Sample burned in sintered metal reaction chamber with 2 wires.
  3. Organic vapor is oxidized as it passes over a catalyst-coated wire (usually platinum). The change in electrical resistance of the coated wire relative to the uncoated wire is sensed and a current signal is generated.
Instrument Characteristics:
  As with FID, sensitive to sample gas flow rate and to air infiltration prior to detector.

## Slide 101: IR Camera Development
Is there a better way?
Hydrocarbon energy absorb and emit infrared at specific wavelengths within the IR spectrum
Camera sees IR energy, but has a filter to allow only IR energy in the 3.3 – 3.5 µm wavelength band to be detected
Hydrocarbons that absorb IR energy in that range will be detected and imaged as a visible plume
Benzene
Butane
Ethane
Ethanol
Ethylbenzene
Heptane
Hexane
  Methane
Methanol
Octane
Pentane
Propane
Propylene
Toluene
Xylene
Common
chemicals detectable by
the camera

## Slide 102: IR Camera Used for LDAR
New “alternative work practice” promulgated to allow the use of Optical Gas Imaging (OGI) as a replacement for method 21
40 CFR §63.11 (c), (d), and (e) and
40 CFR §60.18 (g), (h), and (i)

## Slide 103: IR Camera Used for LDAR
Expected Benefits
In theory – ability to survey equipment faster
Cheaper/less labor intensive
Actual Implementation
Camera is not as sensitive
The image can be manipulated – leaks can disappear or be seen more easily with certain camera settings
Image affected by background, environmental conditions
Daily calibration and recordkeeping of everything monitored
Camera is not intrinsically safe
Camera is very expensive
Alternative work practice requires annual Method 21 monitoring

## Slide 104: Examples From Real Inspections
Compressor distance piece oil sump at a natural gas compressor station
Distance piece is designed to prevent lubricating oil from leaking into the compressor cylinder
Distance piece also acts as a process gas leakage control device
In this case, compressed gas was leaking passed the packing rings and carried over into the oil sump

## Slide 105: Examples From Real Inspections
Storage vessel bleeder vents must be closed at all times unless the tank roof is being landed or floated off the leg supports

## Slide 106: Examples From Real Inspections
Refinery Flare
  Excess steam = incomplete combustion of hydrocarbons

## Slide 107: Temperature Readings
Fruit processing plant waste dumped in a pit
Exposure to air and decomposition caused it to heat up
IR camera used to see elevated temperatures
Notes: And here is the problem with the wrong IR filters the
Camera will not read VOC’s that you need to look at
EPA method then requires that each day that the camera is used it must be checked to determine that the camera can “see” the compound that you need it to see

## Slide 108
Fugitive Leak Screening
- FLIR
FLIR stands for forward looking infrared camera – it reads the thermal infrared signature of a plume. Although not a Method 21 device it can be used to screen for leaks quickly.

## Slide 109: FLIR Video of Vent from Centrifugal Pump
Notes: FLIR stands for forward looking infrared camera – it reads the thermal infrared signature of a plume

## Slide 110: US EPA Method 21 (40 CFR 60 Appendix A)
1. Applicability/Principle
2. Definitions
3. Instrument/Calibration Gases
4. Procedures
Notes: Method 21 also includes soapy water for checking leaks and now we have infared imaging to check for leaks
Both soapy and infrared require a quantitative measure with as instrument within 5 days of observation much the same as visual, ofactory and audio

## Slide 111: Performance Specifications (Method 21 - 3.1.1)
Must respond to organic compounds being processed
Must be intrinsically safe for operation in explosive atmospheres
Must measure concentration specified in the regulation
Scale must be readable to +/- 2.5 percent of defined leak concentration
Must have nominal flow rate of 0.1-3.0 liter/min
Probe must be < ¼ inch OD with 1 opening
Notes: Please revise section 3.1.c. 1990 revisions to Method 21: Scale readable to +/-2.5% of defined leak conc., not +/-5%.
I would call your attention to the last 2 bullets. What are the flow rate specs listed in M21 (0.1-3.0 lpm). In the Guidelines the flow rate range is quite narrow, 0.7 - 1.2 lpm. The flow rate used during the emission factor development studies was typically 1 liter/min, so the technical folks who published the Guidelines felt that this narrower range would be most consistent with the earlier protocols use in the studies. Flow rate is set at the factory. Since adjustment of pump is difficult, the only thing you can do with flow rate is to check it and make reasonably sure the instrument maintains it.
Probe diameter in M21, is “not to exceed 1/4-inch in outside diameter.” The inside diameter is the important thing; the Guidelines specify 3/16-inch.

## Slide 112: Performance Specs (continued)
Criteria | Requirement | Time Interval
Response factor | Must be <10 unless correction curve is used | One time before detector is put in service
Response time | Must be <= 30 seconds | One time before detector is put in service If modification to sample pumping or flow conf is made a new test is req
Calibration precision | Must be <= 10 percent of calibration gas value | Before detector is put in service and 3-month intervals or next use, whichever is later
Notes: Let’s talk about these for a minute
Instruments to be used must meet the following criteria before being place into service:
Response Factor: What is it? Cannot be greater than 10 (but practically, 3 is maximum)
Response Time: Interval from change in VOC concentration at the sample probe to the time at which 90% of the corresponding final value is reached as displayed on analyzer readout meter.
Note M21 states that response time must be less than 30 seconds, while Guidelines require 5 seconds or less. OVA-108 and TVA should respond to changes in VOC concentration within 5 seconds.
Calibration Precision: Degree of agreement between reading of known concentration and actual concentration, expressed as relative percentage of average differences.
All Performance Evaluations should be logged. District inspector authorized to check these records

## Slide 113: Response Factor
The ratio of the known concentration of a VOC to the observed meter reading when measured by the instrument with a reference compound
Notes: What this is saying is that the instruments count Carbon atoms by flame or photo the number of carbon atoms in the VOC we are measuring is different from the number of Carbon atoms in say propane which is the calibration gas therefore we have to have a way of converting the number we get to the compound that we are interested in

## Slide 114
Response
Factor
Actual
Concentration
Instrument Indicated
Concentration
=
Notes: An important criteria in the selection VOC detectors is response of the instrument to the specific chemical or chemicals in the sample gas stream. This response is quantified as shown.
As Response Factor increases, the instrument readout is proportionally less than the actual concentration.
Q. A HIGH response factor indicates that the instrument does/does not detect a compound well?

## Slide 115
Actual Concentration = 1,000 ppm
Instrument Gauge Reading = 3,000 ppm
Response Factor = ??
Actual Concentration = 100,000 ppm
Instrument Gauge Reading = 10,000 ppm
Response Factor = ??
Response Factor Examples

## Slide 116: Response time
The time interval from a step change in the VOC concentration at the input on the sampling system to the time at which 90 percent of the value is reached on the readout meter

## Slide 117: Calibration precision
The degree of agreement between measurements of the same known value, expressed as the relative percentage of the average differrence between the meter readings and the known concentration

## Slide 118: Calibration

## Slide 119: Calibration Gases (Method 21 - 3.2)
Zero air (< 10 ppm VOC)
Span gas
Cylinder cal gas mixtures
  certified to + 2 % accuracy
  shelf life specified
Prepared gases
  accurate to + 2 %
  replaced each day
Notes: Zero is actually <10 ppm in this case

## Slide 120: Preparing FIDs for Field Use
Check hydrogen supply; refill if necessary
Confirm presence of exhaust port flame arrestor
Check battery status
Warm-up instrument electronics
Check amplifier settings ("span check")
Check pre-filter and probe conditions
Leak check probe
Measure sample gas flow rate at probe inlet
Calibrate
Notes: REF: EPA Course #380, Ch ; Portable Instrument User's Manual...
Demo OVA; Follow steps in slide, referring to OVA Diagram Handout . Add additional information as follows:
Approx 1hour field time per 150 psi. Over 8 hrs on full tank.
Flame arrestor occasionally removed for cleaning and not replaced. Required for instrument to be intrinsically safe.
Some useres have report battery life problems.
Warm-up 10 minutes.
Remember, FIDs sensitive to air infiltration. Example: Flow rate into probe is 3.0 L/min; Meter Reading = 500 ppm. Change flow rate to 0.1 L/min (minimum for Method 21); meter reading = 15,000 ppm
Demo calibration; use calibration gases if available.
According to Method 21, should be done each time instrument is used. Methane is preferred calibration gas. Concentration of calibration gas should be close to leak standard (10,000, 1000, 500 ppm) Hexane sometimes used, but 10,000 ppm hexane is close to LEL. Also, hexane can condense on calibration bag surfaces.
  Carbon filters remove all VOCs except methane and can be used to determine ROGs by difference between filtered and non-filtered readings. (Problem with carbon filters is that they saturate very quickly, so breakthrough time not precise.) EPA does not require leak determination based on ROGs. ARB RACT discusses reason for basing leaks on methane rather than ROG. Leaks detected on basis of methane indicate the component has some kind of leak problem, whatever the process gas. (REF: ARB RACT/BARCT, SSD-93-002)
  PIDs and IRs do not respond to methane. If using one of these instruments, calibrate with gas that is of concern for particular inspection.

## Slide 121: Preparing PIDs for Field Use
1. Check battery status
2. Check probe condition
3. Check for obvious deposits on optical window
4. Confirm detector response
5. Measure sample gas flow rate at probe inlet
6. Calibrate
Notes: Deposits on optical window unique to PIDs.
Other procedures as with FIDs, CCAs.

## Slide 122: Performance Criteria (Method 21 - 3.1.2)
Response Factor less than 10
Response time of 30 seconds or less
Calibration precision less than or equal to 10% of calibration gas value
Notes: Again Instruments to be used must meet the following criteria before being place into service:
Response Factor: What is it?
Response Time: Interval from change in VOC concentration at the sample probe to the time at which 90% of the corresponding final value is reached as displayed on analyzer readout meter.
Note M21 states that response time must be less than 30 seconds, while Guidelines require 5 seconds or less. OVA-108 and TVA should respond to changes in VOC concentration within 5 seconds.
Calibration Precision

## Slide 123: Determining Flow Rate
Highly recommended
No official protocol
Flow rate may be affected by contamination, battery life, etc.
Notes: Currently, there is no official protocol to evaluate flow rate. Several experts have suggested that this should be checked because changes in flow rate can have profound impact on readings.
Can be affected by ….student input. (Contamination of probe, dirty filter, water, battery life, tiny particles in pump, etc.)
Demonstrate protocol in class.

## Slide 124: Effect of Flow Rate
Pump Flow Rate =
1.0 liters/min
Leak Rate = 10 milliliters/min
Meter Reading =
10,000 ppm
0.010 liters = 0.010000
1.0 liters
Notes: Changes in flow rate could significantly affect the accuracy of your readings. As a hypothetical example, let’s take a look at the following slides:
Let’s say when you calibrate the instrument at the start of the day, the flow rate is 1.0 liters/min. In the field, a leak of 10 milliliters/min will register on the meter as 10,000 ppm (see the equation below the Meter Reading).

## Slide 125: Effect of Flow Rate
Pump Flow Rate =
0.5 liters/min
Leak Rate = 10 milliliters/min
0.010 liters = 0.020000
0.5 liters
Meter Reading =
20,000 ppm
Notes: Later in the day, let’s say the pump flow rate has decreased because of debris in the pump diaphragm, a weak battery, or some other problem. While this is not a common occurrence, it can happen.
For purposes of this illustration, the decrease in pump flow rate has decreased by 50% -- admittedly a dramatic drop – to 0.5 liters/min. All other environmental and operational factors being equal, now the instrument will read 20,000 ppm for the same 10 milliliters/minute leak. This because the instrument was calibrated at a pump flow rate of 1.0 liters/min. Had the instrument been calibrated with the pump flow rate at 0.5 liters/min, this would not be a problem.
For these numbers to be exactly as shown here, there are several important assumptions. One is that the probe captures ALL the leak. For a small pinhole leak, this might be a realistic assumption, but in many cases, the probe will not capture all of the leaking gas. A second assumption is that there is no cross-wind or other interferences.
Generally, the pump flow rate does not change significantly during the course of the day. The take home lesson here is that you should do a precise check of the flow rate periodically (every few weeks or months) to make sure the pump has not started failing or is contaminated.

## Slide 126: Conducting an Inspection

## Slide 127: Leak Detection Monitoring
1000’s to 100s of 1000’s of valves and connections that must be monitored for leaks
90 to 99% of valves and connections are not leaking
Costly, monotonous, time consuming
Work is contracted out to lowest bidder, technicians often uneducated and complacent

## Slide 128: EPA list of common problems leading to enforcement
Failure to Identify process units and components
Failure to follow prescribed procedures
Incorrect or expired calibration gases
Failure to repair and retest leakers on time
Failure to submit quarterly records
Failure to maintain calibration and monitoring records
Notes: Since EPA has reviewed many refineries and chemical plants they have come up with what amounts to a hit list of things to look for in an inspection
Additionally industry audits recommend to auditors that they look at screening record to determine if the screening was even possible
A rule of thumb is that it is possible to do only about 400 components in a day with a one man team maybe 600 with a two man team
Also look at the order on inspection does it go from one side of the plant to the other or is it orderly would take use time than scattered

## Slide 129: Oil & Natural Gas Source Category
40 CFR 60 Subparts OOOOb and OOOOc
  Promulgated March 8, 2024, Effective May 7, 2024
40 CFR part 60 Appendix K, Protocol for Use of Optical Gas Imaging (OGI) in leak detection
  OGI surveys must be conducted by Appendix K for Oil and Gas Industry. Appendix K is written for broader applicability.
  Equipment Specs, Calibration & Maintenance, Init. Perf. Verification/Operating Envelope, Conducting Surveys, Camera Operator Training
Notes: The oil and natural gas industry is the nation’s largest industrial source of methane, a highly potent climate pollutant that is responsible for approximately one-third of current global warming from human activities.
This sector is also a leading source of other harmful air pollutants, including VOCs that contribute to ground-level ozone (“Smog”) and air toxics such as benzene that ar emitted along with methane and that effect the human health.
On November 2, 2021, EPA proposed NSPS and Emission Guidelines for existing sources that requires states to reduce methane emissions from hundreds of thousands of existing sources nationwide. Promulgated in 2024.
The Key Components of the rules include finding and repairing methane leaks from well sites and compressor stations..
OGI uses a field portable infrared camera to image emissions that are otherwise invisible.
The OGI survey must be conducted according to Appendix K for Subparts OOOOb & OOOOc. Appendix K is written for broader applicability than the oil and natural gas sector.

## Slide 130: Protocol for Use of OGI (40 CFR Part 60 - Appendix K)
Scope & Applicability
Summary
Definitions
Interferences
Safety
Equipment & Supplies
Camera Calibration & Maintenance
Initial Performance Verification & Operating Envelope
Monitoring Survey
Camera Operating Training
QA/QC
Recordkeeping
Sections 13 & 14 References and Tables, Diagrams & Flow Charts
Notes: 40 CFR Part 60 Appendix K includes proposed Protocol for Use of Optical Gas Imaging (OGI) Cameras.
Appendix K consists of 14 sections, as shown above. We will discuss Sections 1 & 6-10.

## Slide 131: Protocol for Use of OGI (40 CFR Part 60 - Appendix K - Section 1)
Scope
Oil and gas upstream and downstream sectors, including well heads, compressor stations, boosting stations, petroleum refineries, gas processing plants, and gasoline distribution facilities
Not applicable to chemical plants at this time
Specific component focus for surveys determined by the applicable subpart
Applicability
Analytes: VOC (including hazardous air pollutants), methane, ethane
Must be referenced by an applicable subpart
Not currently applicable for use in direct emission rate measurements from sources

## Slide 132: Protocol for Use of OGI (40 CFR Part 60 - Appendix K - Section 6)
Equipment & Supplies
OGI cameras must meet two specifications:
Camera Spectral Range overlap with a major absorption peak for chemicals of interest
Camera must produce a detectable image of 17 g/hr for methane & 18.5 g/hr for butane emissions at viewing distance of 2 meters, delta-T of 5o C and calm wind conditions (<1 meter/sec)

## Slide 133: Protocol for Use of OGI (40 CFR Part 60 - Appendix K - Section 7)
Camera Calibration and Maintenance
The Camera does not require routine calibration for purposes of gas leak detection, but may require calibration is used for thermography (such as delta-T determination)

## Slide 134: Protocol for Use of OGI (40 CFR Part 60 - Appendix K - Section 8)
Initial Performance Verification & Operating Envelope
The initial performance verification is to meet Section 6
Operating Envelope must be established for all potential configurations (operating modes of standard vs. high sensitivity or enhanced; lens; hand held vs. tripod; the viewer in OGI camera screen vs an external device; etc.)
Use Section 6 performance specifications for gas composition, flow rate, etc. for both methane & butane
Notes: Section 8 covers initial performance verification and development of the operating envelope.
The initial performance verification must demonstrate that the camera meets Section 6.0.
Camera configuration means different ways of setting up an OGI camera that affect the detection capability.
Can include the operating mode (e.g. standard vs. high sensitivity or enhanced), the lens, the portability (e.g., handled vs. tripod), and the viewer (e.g., OGI camera screen vs. an external device like a tablet).

## Slide 135: Protocol for Use of OGI (40 CFR Part 60 - Appendix K - Section 9)
Conducting the Monitoring Survey per Monitoring Plan
Daily Verification Check
Route Map with GPS
View from >2 Different Angels & Minimum of 5 Seconds or 10 Seconds if a Leak Detected & Tag for Repair
Avoid Camera Fatigue (Break every 20 Minutes)
A 5 Minutes Video of Survey Techniques/Procedures Daily
Notes: The procedures for conducting the monitoring must be described in a monitoring plan.
Daily verification check is required to confirm that the camera is operating properly.
Also must ensure that the conditions in the field are within the operating envelope as shown above..
The approach used to monitor all regulated components must use a route map or map with designated observation locations, use visual cues (tags, streamers, color-coded pipes) and use global positioning system route tracing.
View components from at least 2 different angles, divide complex scenes into manageable subsections and dwell on each angle for a min. of 5 seconds per component and document each leak with a 10-second video clip and tag for repairs.
Avoid camera fatigues by breaking up surveys every 20 minutes.
At least each monitoring day each operator must record a 5-minute video that documents the survey technique and procedure.

## Slide 136: Protocol for Use of OGI (40CFR Part 60 - Appendix K- Section 10)
Camera Operator Training
Initial Classroom (Fundamentals of OGI, Component Survey, Calibration, Camera O&M, Common Mistakes, Best Practices, Regulatory Requirements & Record Keeping)
Initial Field (Observe 10 Surveys by a Senior OGI Camera Operator; Conduct 40 Practice Surveys Side by Side with a Senior OGI Operator; Conduct 50 Independent Surveys with Senior OGI Operator Oversight; Final Site Survey Followed by a Senior OGI Operator to Confirm Zero Mistakes)
Annual Classroom Refresher
Quarterly Performance Audits (Comparative Monitoring or Video Review)
Repeat the Initial Training If No Monitoring Survey Conducted in 12 Months
Notes: Provide Operator Training.
Initial classroom to include fundamental concepts of OGI camera technology, description of the components to be surveyed and examples of leaks that can be expected, calibration, operation, and maintenance for the camera, parameters that can affect image detection and procedures for performing the monitoring survey, common mistakes and best practices and regulatory requirements, including recordkeeping.
Initial field training to include 10 surveys where trainee is observing a senior OGI camera operator, 40 surveys where the trainee performs the survey with a senior operator verifying side-by-side, 50 surveys where the trainee performs the survey independently with the senior operator providing oversight and instruction/correction, and final site survey test where the trainee conducts the survey and a senior operator follows behind with a second camera to confirm the results with zero missed persistent leaks.
Annual classroom refresher can be shorter in duration than the initial classroom training but must cover procedures for conducting surveys.
Quarterly performance audits has two options. Option 1 , comparative monitoring is when a senior operator performs an independent monitoring survey of at least 4-hours to ensure no persistent leaks were missed. Option 2 video review is to use an unedited and uncut video footage of OGI survey technique is reviewed by senior operator for missed leaks and survey techniques. Retraining is required if senior operator finds any leaks missed by the camera operator being audited or finds that the survey techniques during the video review do not match the monitoring plan.
If an OGI operator has not conducted a monitoring survey in over 12 months, they must repeat the initial training requirements

## Slide 137: Pre-Inspection
Regulation Review
File Review
Permit Check
Equipment Check
Notes: Handout: Permit or List of Components for field visit; Host Agency Checklist
Regulation Review: Depending on type of source and way your rules are written, this may involve reviewing multiple rules. (TQ# )
Q. What types of rules can apply to fugitive VOC emissions?
(Can be based on Source Category, eg. Refineries; Component, eg. valves and flanges; or Compound, eg. benzene; Control Device, eg. adsorber, incinerator)
File Review -- What do you look for?
Example: See p. 140 for semi-annual NESHAP Report showing Skip-Period approach. Note # of valves leaking = 0.4%.
Permit Check: Ideally, copy permit. For long ones, make list of major compliance points.
Equipment would include: Safety equipment and Portable VOC monitoring instruments. Calibration critical (next slide)
[Optional classwork: ----> Obtain real source files to review]

## Slide 138: On-Site Inspection
Initial Interview
Records Review
Plant LDAR Program Evaluation
Component Screening Strategies
Leak Monitoring
Notes: On-Site or Facility Inspection topics to be covered: Read Slide
Contact Source to schedule regular inspection -- Your policy?
REF and Addtional Information: EPA Course #380, Reference Vol 3, Benzene Equipment Leak Inspection Manual, pp. 6-4 through 6-23.

## Slide 139: Records Review
Are records complete per regulations?
Verify unsafe and difficult-to-monitor determinations listed
Check process unit determinations
Notes: Read Slide
The emphasis here is on completeness.
Q. Complete records would include what kinds of information?
(Location, type, description, date leak detected, date of/to be repaired, date of recheck after repair, type of repair, percentage of components leaking, dates of process unit turnaround for components awaiting repair). Refer to your regs for details.
Handbook, pp. 162-163 has checklists

## Slide 140: Plant LDAR Program Evaluation
Evaluate tracking system for scheduling monitoring and repairing
Interview plant personnel
Observe calibration of leak detection equipment
Observe leak detection monitoring
Notes: Evaluation of source's LDAR program recommended. EPA estimates that an effective LDAR program can reduce fugitive VOC emissions by 60-70 percent.
(REF:
Read Slide with following notes:
Facilities, independent monitoring companies generally develop or use computer-based tracking systems.
Inspectors--you may not be able to "evaluate" such programs critically, but at least make sure facility can track LDAR for compliance purposes.
Also look at components designated for repair. Are reasons given for repair justified? Are components being repaired within time frame specified in regs?
Observe, interview to see if field monitoring conducted properly; i.e., according to Method 21.

## Slide 141: Focusing on the Inspection
Most important components for monitoring:
  components/process units with history of high leak rates
  valves in gas and light-liquid service
  pumps in light liquid service
  compressors
Review component identification system
Notes: REF: Portable Instrument Users Manual, p. 62
Priority should be given to the categories shown.
Q. What are some factors that may affect the leak potential of a component? Get student responses
(Type of component; type of service; pressure; temperature; design of component; type of seal; age; specific chemical in process; etc.)
(REF: Portable Instrument Users Manual, p. 61-62.)
In general, highest percentage of leaking components are compressor seals. Highest number will probably be......? (valves). Though valves represent the greatest number of leaking components, only a small percentage of total number of valves at a facility usually leak (< 5%). Analogous to "gross emitter" situation for mobile sources.
(REF: Portable Instrument Users Manual, p. 62-63.)
Need to be aware of component identification system to link written records to components in field.

## Slide 142: Locating Potential Leaks
Individual Component Survey
  visual, auditory, olfactory
  soap solution screening
  portable VOC analyzer
Area Survey ("Walk-Through")
Fixed Point Monitors
Infrared imaging
Notes: Individual Component Survey:
How are sight, smell, and hearing useful in detection of leaks?
Has anyone used soap solution? Doesn't really save time compared with using instrument. Also won't work on hot components or rotating shafts.
Portable VOC analyzer pretty much mandatory to determine gaseous leak violations.
Area Survey might be useful where there is obvious leaker. Also important to gauge background levels. VCAPCD Enforcement Guidance states that 50% of all significant leaks in a unit are detected by walk-through survey, if only a few pieces of equipment leaking. Not reliable under windy conditions or where there are many components in an area.
Fixed Point: For worker exposure; detect emissions of hazardous substances.
(REF: VCAPCD Enforcement Guidance)

## Slide 143: Monitoring Individual Components (Method 21 - 4.3.1)
Measure background levels
Probe at surface of component
Move along interface periphery while observing readout
If increase occurs, sample until
maximum reading;
leave probe tip at this location for approx. 2 times response time
Record results
Notes: There is always some background concentration. Usually this is quite low (10 or less ppm). TVA can be set to automatically factor this out. With OVA, you would measure background upwind of site.
Q. How do you deal with background concentration in the field?
"Surface" stated in Method 21 for most components, except for Pumps and Compressors, where "within 1 cm" is specified.
Because capture distance is limited, sampling probe distance can affect readings. EPA studies have shown that a significant number of leaks can be missed even at 1 cm. Therefore, stay as close as you can.
Almost impossible to go around entire periphery for most components. Especially important to check undersides of sealed areas since more leaks tend to occur there. A common error is to do “tenderizer-style” screening (poking around components). While large leaks may be revealed this way, many smaller leaks will not. Q. Your experience with this?
Flexible tubing can be used to get to difficult-to-reach parts of a component. May change flow rate and response time slightly. Continued next page ---->

## Slide 144
Screening Valves
Screen here
Screen here
Screen
here
Notes: Screening areas shown. Where have I missed?

## Slide 145: Limitations and Problems Using Portable Instruments
Poor capture capability & pinpoint nature of most leaks --> probe should be oriented directly into plume
Negative pressure sampling --> limited capture distance
Air drawn into probe from all directions --> dilution
All instruments sensitive to gas flow rates
Cross-wind reduces capture efficiency
Notes: Most leaks are pinpoint. Many are transient or sporadic. Flow rate of leak may vary, so: 1. you may not be monitoring component at precise time leak is occurring, 2. leak rate may not be representative of typical conditions.
Undersides of components tend to leak more than other areas.
Because monitors draw in air through small opening under low negative pressure --> limited capture distance
Affect of cross-wind in next slide

## Slide 146
10000
10
seconds
ppm
0
650
Still Air
Still Air
1 mph
Effect of Wind Velocity on PPM Reading (probe tip 1/4" from leak source)
Notes: This is for Propane measured with OVA 108. Ramifications clear--wind has big affect!

## Slide 147: Effects of Excessive VOC Intake
Flame Ionization Detectors
  Flame-out at sample concentrations above 70,000 to 100,000 ppm
  Blinding of flame arrestor
  Sustained high observed readings due to condensation & revolatilization in sample lines
Photo Ionization Detectors
  Condensation of organic materials on the optical surface
  Condensation and revolatilization
Catalytic Combustion Analyzers
  Volatilization of catalyst on detector wire
  Condensation and revolatilization
Notes: Read Slide with notes:
FIDs:
  Flameout very common. Generally, waiting for HCs to volatilize will work.
  Condensation is particular problem for heavier hydrocarbon streams. Response time of meter will be slower than for lighter HCs, and time to return to zero may also be longer. Allow enough time for meter to return to zero after such a reading, but be aware that adjustment and cleaning may be necessary.
PIDs: One of biggest problems with PIDs is keeping optical surface clean.
Q. How can you minimize the effects of excessive VOC intake on instruments? (Withdraw probe immediately when gauge spikes to maximum reading).
CCAs: High levels of hydrocarbon can result in excessive temperature within instrument and degradation of catalyst.

## Slide 148: Post-Inspection
Compare field inspection observations with plant records
Review findings with plant representative(s)
List items to be checked during follow-up inspection(s)
Notes: This gets back to evaluating recordkeeping system and LDAR program. You would be looking for discrepancies between what were listed as leakers and what you found in your monitoring.
NOVs may be issued... Your policy?
Because of way fugitive emissions regulations are written, followup inspections are inevitable.
Q. What might you inspect during subsequent inspections?

## Slide 149
Inspection Safety
Notes: What are some of the health and safety concerns you would have when conducting fugitive VOC inspections?

## Slide 150: Pre-Field Safety
Calibrate in well-ventilated space
Make sure all intrinsically-safe features are intact
Review possible on-site hazards
Wear long-sleeved, fire protective clothing
Be trained in use of specialized equipment
Notes: Q. What are the main hazards associated with instrument preparation?
Q. What on-site hazards do you need to prepare for? Learn warning signals.
Long, sleeved, fire protective clothing (Nomex) is addendum to standard PPE.
Specialized equipment may include: SCBA, H2S monitor

## Slide 151: FIELD Safety
Stay alert
Move at a reasonable pace
Be extremely cautious around hot (or cold) surfaces
Be extremely cautious monitoring components with rotating shafts
Stay upwind of components being screened
Keep both hands free when climbing ladders
Don’t make “heroic” physical efforts
to reach components
Notes: Always be aware of hazardous situations and locations. Be alert for locations of SCBA equipment.
Watch out for moving vehicles, forklifts, etc.
NOTE: Tarzan sound linked to jumping inspector and should be surprise to students.