## Slide 1: PERM 202 (NACT 334)
Permitting Practices and Principles

## Slide 2: Online Housekeeping
Instructor & Student Introductions
Online Agenda
Breaks
Caveats
Notes: Today thru Thursday – end about three

## Slide 3: Introductions - Instructors
Mohsen Nazemi
Carl Daly
NACT 334

## Slide 4: NACT 334 Online Student Introductions Survey
Air Quality Experience
Job Responsibility with the Agency
Permitting Experience
NACT 334
Notes: Now we want to know who you are and what you do. In addition we would like you to pose one question probably on the back of the test that tells us what you expect from this class. We will make sure that we answer all of the questions.
Also and very important: this course can be fun and interesting or very boring. This depends on you. We will be making what seem to silly and strange statements. If you don’t ask questions and challenge us the course will be very boring. Please interrupt, ask questions, bring what we are saying into a Maryland context.
One area to really call us on is acronyms. We are gong to use lots of them and they may or may not be obvious especially if you are relatively new to this game. If we don’t explain what the acronym means do not let us get away with it.

## Slide 5: Course Objectives
Overview of air pollution permitting
Permitting agencies
Permitting process
Applicable regulations
Related programs
Notes: Stress overview
Cover a lot of material
Won’t go into great detail on most topics
The material we intend to cover in 3.0 days is actually more than we covered in my first graduate course.
All of the course is generally aimed in a federal perspective. Most of what you do on a day by day basis have little to do with complex federal requirements but the definitions and techniques we talk about here will be useful.
CT and New York regulations:
The Abatement of Air Pollution Regulations are available on the Connecticut eRegulation System under Title 22a-174.
CT PSD = Section 22a-174-3a

## Slide 6: Lessons
Lesson 1 – Introduction - Who, What, Why & When
Lesson 2 – Attainment of NAAQS
Lesson 3 – Source Types
Lesson 4 – Permitting Basics
Lesson 5 – Potential to Emit
Lesson 6 – Non-attainment NSR Pre-construction Permits
Lesson 7 – PSD Pre-construction Permits
Lesson 8 – PSD Netting
Lesson 9 – Emission Limitations
Lesson 10 – Averaging Time
Notes: Just like a reporter we are organized into who what where why and when

## Slide 7: Lessons (Cont’d)
Lesson 11 – Best Available Control Technology (BACT)
Lesson 12 – Offsets/Banking/Trading
Lesson 13 – Modeling & Inventories
Lesson 14 – Title V Operating Permits
Lesson 15 – Monitoring, Reporting & Recordkeeping
Lesson 16 – Compliance Assurance Monitoring (CAM)
Lesson 17 – Permit Conditions
Lesson 18 – NSPS & Toxics
Lesson 19 – Compliance & Enforcement
Notes: Just like a reporter we are organized into who what where why and when

## Slide 8: LESSON 1
Introduction
Who, What, Why and When
Notes: 8

## Slide 9: Lesson Objectives
Who needs a permit?
What requires a permit? (covered in Lesson 3)
Why is a permit necessary?
When is a permit required?
Notes: Just like a reporter we are organized into who what where why and when

## Slide 10: Who Needs a Permit? Pre-construction Review
Stationary sources of air pollutants
  Criteria pollutants
    Pollutants for which there
    is a National Ambient Air
    Quality Standard (NAAQS)
  Regulated pollutants
    Criteria pollutants
    Hazardous air pollutants
Notes: Stationary sources are defined differently for different programs
I will go into more detail in Lesson #3. and by the time we are finished you will be overwhelmed with how a source is defined.

## Slide 11: Who Needs a Permit? Pre-construction Review (Cont’d)
Permitting agencies provide specifics
  Applicability thresholds
    Horsepower
    Heat input
    Throughput
  Exempted equipment/activities
    Storage/Transfer of diesel fuel
    Residential Equipment
Notes: Applicability thresholds will vary:
from agency to agency
from area to area
May be based on:
SIP considerations
Attainment status
Local issues
Any thoughts on why equipment may be exempt?
Could it be things like resources; – mention Colorado and NSPS i.e. cover all NSPS until impossible

## Slide 12
I think it’s over the applicability threshold
Who Needs a Permit?
Notes: Sure looks like a slam dunk but looks can be deceiving. Talk about gold mine

## Slide 13: Who needs a permit? Operating Permit
Major Sources – Criteria pollutants
  Applicability based on quantity of emissions
  Definition depends upon where the source is located
  Attainment status
Notes: In the 1990 act the Feds got into the operating permit program via “Title V”
The Title V permit requirement applies to any source that meets one of the following criteria:
Any "major source". A "major source" is any stationary source, or a group of stationary sources, that are located on one property or two or more contiguous or adjacent properties under common control of the same person or persons belonging to a single major industrial grouping and is described in one of the following:
Potential to emit 100 tons per year or more of any regulated air pollutant, e.g., particulate matter, sulfur dioxide, lead, nitrogen oxides, carbon monoxide, or volatile organic compounds.
Potential to emit 10 tons per year or more of any one of the 188 Hazardous Air Pollutants (HAP) listed in section 112(b) of the CAAA of 1990.
Potential to emit 25 tons per year or more of any combination of HAPs.
Sources subject to the requirements under New Source Performance Standards or National Emission Standards for Hazardous Air Pollutants, if specifically required by EPA.
Coal-fired electric utilities subject to the acid rain program.
50/25/10 tpy in bumped O3 NA areas
CO and PM areas
Handout 1A

## Slide 14: Who needs a permit? Operating Permit (Cont’d)
Hazardous Air Pollutants (HAPs)
  10 tpy of a single HAP
  25 tpy of combination of HAPs
Notes: HAPs are Hazardous Air Pollutants . They are defined in the CAA. We will talk about them in more detail later on.

## Slide 15: Legal Basis (Federal)
Clean Air Act (CAA)
  NAAQS – Public health concerns
  Title V Operating Permit
  State Implementation Plan (SIP)
Notes: Other federal requirements addressed in permitting
  NSPS 111
  NESHAPS 112
  Toxics 112
  SIPs/NAAQS 110

## Slide 16: Legal Basis (State/Local)
State and/or local environmental protection rules, regulations or legislation
  Preconstruction Review
  Operation of non-Title V sources
Notes: Agencies may require permits (both pre-construction and operating) of sources below federal permit applicability thresholds

## Slide 17: Why is a permit necessary?
Notes: Interesting picture and shows the public perception of massive air pollution. Most of what you see is steam.

## Slide 18: Why is a Permit Needed?
To protect air quality
To legally limit the amount of air pollutants released into the atmosphere
To exercise control over air emissions by implementing statutory and regulatory requirements

## Slide 19: Protection of Air Quality

## Slide 20: Protection of Air Quality – Pre-construction Review
Attainment Areas – Prevention of Significant deterioration - PSD
  Best Available Control Technology (BACT)
  Increment protection
  Modeling
Non-attainment Areas – New Source Review (NSR)
  Lowest Achievable Emission Rate (LAER)
  Offset requirement
  Trading (offset) ratios
  Modeling
Notes: Pre-construction review includes two phases:
  Authority to Construct/Permit to Construct
  Permit to Operate
The state/local NSR/PSD program commonly applies to sources even if they are too small to be subject to Title V
PSD is the pre-construction review program in effect in attainment areas
Although it is a federal program – delineated in the Clean Air Act - it has been delegated to most states
The standards for control technology and air quality protection are less stringent than the NSR program applicable to nonattainment areas
State and local programs incorporated in SIPs in nonattainment areas
Applicability thresholds vary from state to state, depending on
  Attainment status
  Category of nonattainment

## Slide 21: When is a Permit Required?
Construct a New Source
Modify an Existing Source
Operate a Source
Renew an Existing Permit
Change an Existing Permit
Others?
Notes: Pre-construction permits are – necessarily – required prior to the construction, or modification, that triggers the permit requirement.
The permitting agency should be contacted early in the process to discuss application requirements and timelines.

## Slide 22: Questions?
Notes: 22

## Slide 23: LESSON 2
National Ambient Air Quality Standards:
Attainment Issues
Notes: Carl
Background on CAA standards to set stage for CAA permitting
What is the permit trying to protect?
23

## Slide 24: Lesson Objectives
Understand Criteria Pollutants
  Criteria Pollutants have NAAQS
Define Attainment
Define Non-attainment
Discuss why the difference matters
Notes: Criteria Poll = SO2/Nox PM10/2.5 O3 CO Pb [have NAAQS]
24

## Slide 25: NAAQS/Attainment Issues
Many definitions, rules, applicability issues, etc. are dependent upon the concept of attainment/non-attainment
Attainment designation is based upon an area’s air quality as compared to prescribed levels of air quality
Prescribed levels are referred to as National Ambient Air Quality Standards (NAAQS)
Notes: This topic will be discussed in more detail later in this class.
NACT 334 - INTRODUCTION
3/2/2014
25

## Slide 26: NAAQS
National Ambient Air Quality Standards
  Required by CAA § 109
Primary Standards
  Protect public health
  Including at-risk population
Secondary Standards
  Protect public welfare
Notes: Primary = public health of sensitive populations
Secondary = protect vegetation and env
Found in the 40 CFR Part 50
26

## Slide 27: State Implementation Plans
CAA requires SIP (§110)
  States prepare and submit to EPA
  Roadmap to attainment
  Attainment dates
  Program issues
    Permit program
    Regulatory requirements
    Enforcement program
Notes: Not just a roadmap to attainment, also the plan to maintain AQ and incorp fed regs
Sec 110 plans to protect and attain the NAAQS = SIP
As specified in Part 51 [SIP planning group]
27

## Slide 28: Criteria Pollutants
Carbon Monoxide (CO)
Lead
Nitrogen Dioxide (NO2)
Ozone (Secondary Pollutant)
  Volatile Organic Compounds (VOC)
  Nitrogen Oxides (NOx)
Particulate Matter (PM, PM10, PM2.5)
Sulfur Dioxide (SO2)
Notes: Again Criteria pollutants = have NAAQS associated with them
NOx = generally means NO + NO2[form of the NAAQS]
Ozone is not emitted directly. Most common NA area across the country
It is formed by a complex photochemical reaction involving nitrogen oxides, volatile organic compounds, and sunlight.
PM2.5 (fine) also has precursors as well as direct emissions = Nox and SO2, maybe others
May still have PM maintenance areas ,but pretty much PM1 and PM2.5 NA areas now
28

## Slide 30
What is PM?

## Slide 31: NAAQS
Pollutant | Averaging Time | Level | Form
Ozone | 8 hr. | 0.070 ppm | 4th highest daily max (3 yr. ave.)
PM2.5 | Annual 24 hr. | 12 9 μg/m3 35 μg/m3 | Annual mean (3 yr. ave.) 98th %ile (3 yr. ave.)
PM10 | 24 hr. | 150 μg/m3 | Not to be exceeded
Notes: This is a simplified statement of the NAAQS. A more detailed treatment may be found by “googling” NAAQS or reading Part 50.
Annual PM2,5 revised in ‘24 [for now]
Explain form of standard – exceedance vs design value (DV)
98% = 8th max
31

## Slide 32: NAAQS (Cont’d)
CO | 8 hr. 1 hr. | 9 ppm 35 ppm | Not to be exceeded >1x/yr.
NO2 | 1 hr. Annual | 100 ppb 53 ppb | 98th %ile 3 yr. ave. Annual Mean
SO2 | 1 hr. | 75 ppb | 99th %ile of 1 hr. daily max (3 yr. ave.)
Lead | Rolling 3 mo. ave. | 0.15 μg/m3 | Not to be exceeded
Notes: 99% = 4th max
Most areas are attainment for lead since it was phased out of gasoline. However, local exceedances may occur near busy private airports (small piston air craft still use leaded fuel) and near manufacturing facilities that use lead i.e. lead acid battery manufacturing/recycling
Can be found in 40 CFR Part 50 [show part 50 TOC]

## Slide 33: What is Attainment?
U.S. is divided into Air Quality Control Regions (AQCRs)
Ambient air quality is monitored
If ambient air is “cleaner” than the standards, the AQCR is designated as attainment
Notes: An area can be attainment for one or more pollutants, non-attainment for other pollutants.
Show 81.301: NA (serious) for 2015 O3,
Severe for 2008 O3 in some parts of CT
Attain for all others
CFR Part 81.13 CT, NJ, NY AQ region, 81.183 east CT, 81.184 NW CT, 81.301 Attainment status designations
33

## Slide 34: What is Non-attainment?
If ambient air quality is “dirtier” than the standards, the area is designated as non-attainment
Degrees of non-attainment
Designation is pollutant-specific
Notes: Degrees of non-attainment
more details 3 slides from now
34

## Slide 35: Insufficient Monitoring Data?
Area is called “unclassified”
Treated as attainment
Notes: Show CFR Part 81 TOC and then EPA AQ DV interactive map
Refer to acronyms list
35

## Slide 36
Notes: The degree of non-attainment determines how long an area has to come into attainment.
If area not attaining gets bumped up by EPA

## Slide 37
Notes: The lowering of Major source thresholds in NA areas will impact if source needs a NA NSR/PSD and TV permit

## Slide 38
8 – Hour Ozone Nonattainment Areas in the Country
Notes: 2015 standard also 2008 standard O3

## Slide 39
New PM2.5 NAAQS
Based on 2020-2022 air monitoring data, the dark green areas on the map indicate counties that do not meet the annual PM2.5 standard of 9 ug/m3
Notes: Annual PM2.5

## Slide 40: Why does it matter?
Attainment/non-attainment status impacts many issues
  Definition of Major Source
  Pre-construction review
  Offset ratios
Notes: If NA, people are breathing unhealthy air
But specifically for permit writers Again, if Major Source NA NSR/PSD and TV permitting may be required
40

## Slide 41: Major Source Definition
Ozone non-attainment: NOx, VOC (CAA § 182)
  100 TPY – marginal and moderate
  50 TPY – serious
  25 TPY – severe
  10 TPY – extreme
PM10/2.5 (§ 189(c))
  70 TPY - serious non-attainment
CO (§ 187(c))
  50 TPY – serious non-attainment if stationary source contribution to CO levels is significant
Notes: This is also covered this in Lesson 3
In O3 NA areas can also lower TV permitting threshold for VOC and Nox sources [and PM NA areas too]
41

## Slide 42: Federal Offset Ratios
Area Classification Ratio
Ozone Marginal 1.1:1
Ozone Moderate 1.15:1
Ozone Serious 1.2:1
Ozone Severe 1.3:1*
Ozone Extreme 1.5:1*
*1.2:1 if SIP requires all existing major sources in Non-attainment Area to
use BACT
CAA § 182
Notes: LESSON 2 - NSR
12/06
CARB 334
42
Lesson on offsets later
Emit 100tpy Nox/VOC need 110tpy offsets [reductions] from somewhere else in the NA area

## Slide 43: Federal Offset Ratios (Cont’d)
Area Classification Offset Ratio
CO Moderate 1:1
CO Serious 1:1
PM10 Moderate 1:1
PM10 Serious 1:1
NO2, SO2 All 1:1
Notes: LESSON 2 - NSR
12/06
CARB 334
43
And PM2.5

## Slide 44: QUESTIONS?
Notes: CARL

## Slide 45: LESSON 3
Sources, Major Sources, and Modifications
Notes: Ted

## Slide 46: Lesson Objectives
Understand the different types of sources
Understand what are the elements of a major source
Understand what constitutes a modification
Understand activities which are not modifications
Notes: 46
The concept and definition of a source is one of both the simplest and most complex definitions in this entire area. The complexity can be seen from the amount of litigation that has resulted from this area. Today we will discuss what is a major source (almost all of the 62 different definitions a lawyer told me were in the act) and we will try to discuss what is and what is not a modification. Modification arguments have been to the supreme court several times and have cost industry billions of dollars,
Classifying major/minor modifications at existing major sources is a complicated, long standing issue with lots of debate about whether PSD/NA NSR triggered.

## Slide 47: What is a Stationary Source
Stationary source is defined in two ways:
“building, structure, or facility” = “the plant”
  Includes all of the pollutant-emitting activities which belong to
    the same industrial grouping, are located on one or more
    adjacent properties, and are under the control of the same
  owner or operator.
Source “installation” = “the emissions unit”
  An identifiable piece of process equipment.
Notes: 47
Use flip chart diagram to show the “source” or “facility” vs “emissions unit” Add coal mine and landfill
Here the definition of a stationary source. Basically if it does not move (for over a year/12 months so not a non-road engine) and it emits something it is a stationary source. A few state still use a dual source definition under which the source can either be the entire source or a individual emitter. EPA dropped this definition in the 2002 NSR reform. In this lesson we will deconstruct the definition of a source and look in detail at each part of the definition.
More detail on stationary source in a couple of slides
52.21 b 5 = stationary source = b 6 and 70.2
B 6 = building, structure facility or installation
B 7 = emission unit < 2 yrs = new
[SEE also 51.166 and 51.165 and state SIP approved NSR regs – Can’t find defn of B,S, or F in NY regs]

## Slide 48: Major Source
From EPA perspective only concerned with major sources*
States may control sources smaller than major (Non-major Sources)
* Some EPA regulations apply to Non-major (Area) Sources
Notes: Although EPA’s main focus for permitting program is on Major Sources, some EPA regulations also apply to Non-major sources, such as Area Source MACTs. Almost all of our focus for the next three days will be on major sources. From EPA’s perspective these are the primary source they are concerned with under PSD, NA NSR, or Title V. The next couple of slides will describe what a major source is under various programs. This does not mean to minimize the importance of state regulation but this course has a fed/EPA perspective. Also we will try and point out that state definitions do not necessarily match the federal definition and this can lead to interesting issues – mention STATE and up to permit.
EPA can occasionally be interested in minor source permitting particularly syn minor sources that have high interest.

## Slide 49: What is a Major Source?
Depends on location and regulation type
Non-attainment NSR: Potential to Emit (PTE) of 100 tpy or less
PSD: PTE of 250 tpy unless listed
Notes: 49
There are a large number of different definitions of a major source in NA NSR and PSD (and also a TV definition). In simplest terms NA NSR will apply to any source with a PTE of 100 tpy and PSD will apply to any source with a PTE pf 250 tpy but as the next slide shows it really does get more complicated. TV defn is generally 100tpy for criteria pollutants (w/NAAQS) and 10/25tpy for HAPs.
Talk a lot more about how to calculate “PTE” in a future lessons.
NA NSR major source threshold is 100 tpy (or lower in some NA areas) for ALL sources. It is irrelevant what category the source belongs to because listed source categories do not exist for nonattainment NSR.
At a new major source, NA NSR applies only to the NA pollutants with PTE above the major source threshold.
This is unlike PSD, which applies to all attainment pollutants plus GHG (for part) and some HAPs with significant emissions at a major source. In other words, the “Major for one, major for all” concept does not apply for NA NSR. Or more simply if you trigger PSD for one pollutant you may trigger it for others even if they are less than major source thresholds.
Note: a source can be major for PSD and NA NSR at the same time and can even be PSD and NSR for the same pollutant. Can someone explain that?

## Slide 50: NSR “Major Source” Thresholds for NSR for Ozone, CO and PM Depend on Non-attainment Classification
Area Classification Major Source PTE (tpy)
Ozone Marginal 100 (precursors i.e. NOx and VOC)
Ozone Moderate 100
Ozone Serious 50
Ozone Severe 25
Ozone Extreme 10
CO Moderate 100
CO Serious 50
PM10/2.5 Moderate 100
PM10/2.5 Serious 70
Notes: 50
For NSR the definition of a major source varies by location and degree of non attainment. This slide shows the major source PTE for types of non attainment. Since NOx and VOC are precursors for ozone the major source tonnage for ozone applies to them.
CT O3 classifications: severe, serious, moderate [see 81.307]
a major source is 25 tpy.
Green book and DC map
50

## Slide 51: Greenhouse Gases
After July 2014, the Supreme Court decision Greenhouse Gases alone will not cause a source to be major.
Notes: 51
After the court decision greenhouse gases will be subject to BACT but will not by themselves cause a source to be major. However GHG can be considered if the source is already subject to PSD
Significant is 52.21 b 49 iv a = 75,000 tpy CO2e
Now EPA undertaking a regulatory action to reverse the GHG endangerment finding.

## Slide 52: PSD Source Categories with 100 tpy Major Source thresholds
1. Coal cleaning plants (with thermal dryers) | 15. Coke oven batteries
2. Kraft pulp mills | 16. Sulfur recovery plants
3. Portland cement plants | 17. Carbon black plants (furnace process)
4. Primary zinc smelters | 18. Primary lead smelters
5. Iron and steel mills | 19. Fuel conversion plants
6. Primary aluminum ore reduction plants | 20. Sintering plants
7. Primary copper smelters | 21. Secondary metal production plants
8. Municipal incinerators capable of charging more than 50 tons of refuse per day | 22. Chemical process plants (does not include ethanol production facilities that produce ethanol by natural fermentation)
9. Hydrofluoric acid plants | 23. Petroleum storage and transfer units with a total storage capacity exceeding 300,000 barrels
10. Sulfuric acid plants | 24. Taconite ore processing plants
11. Nitric acid plants | 25. Glass fiber processing plants
12. Petroleum refineries | 26. Charcoal production plants
13. Lime plants | 27. Fossil fuel-fired steam electric plants of more than 250 million British thermal units (BTU) per hour heat input
14. Phosphate rock processing plants | 28. Fossil-fuel boilers (or combination thereof) totaling more than 250 million BTU/ hour heat input
Notes: 52
For these sources the Major Source Threshold PTE is 100 tpy.
Fugitive emissions count for this list of sources.
52.21 b 1 i a - will be duplicated in your state PSD regs -

## Slide 53: Major Source (Cont’d)
  Major for One, Major for All: If a source emits even one pollutant (attainment or non-attainment) in major amounts, the source will be considered major. Then all attainment pollutants, even those emitted in non-major amounts, will be reviewed for PSD applicability by using their respective Significant Emissions Rate (SER).
  Emissions equal to or higher than the SER make the pollutant subject to PSD
Notes: It only takes one pollutant to make a source major. In the case of PSD if one pollutant is major then other pollutants which exceed a significant emission rate are also major.
SER will be discussed on the next slide.

## Slide 54: Significant Emission Rates PSD (tpy)
Carbon monoxide 100
Nitrogen oxides 40
Sulfur dioxide 40
Particulate matter (PM/PM-10) 25/15
Particulate matter (PM2.5) 10 of direct PM2.5 emissions; 40 of sulfur dioxide emissions; 40 of nitrogen oxide emissions unless demonstrated not to be a PM2.5 precursor
Ozone (VOC) 40 (of VOCs or NOx)
Lead .6
Fluorides 3
Sulfuric acid mist 7
Hydrogen sulfide (H2S) 10
Total Reduced sulfur compounds (including H2S) 10
Notes: These are the significant emission rates, These constitute a major modification or trigger PSD for a pollutant if the source is already a major source. At the present time GHGe are 75,000 tpy (+0 tpy GHG mass basis)
Pb is still a criteria pollutants. PM2.5 = 10ug/m3, BE and Hg are not [b23]

## Slide 55
Let’s Look Closely at the Definition of a Stationary Source
Notes: Remember a stationary source has a number of parts including:
Plant sketch

## Slide 56: Same Industrial Classification
Means part of the same two digit North American Industry Classification System (NAICS) or Standard Industrial Classification (SIC)
Support facilities are also considered regardless of SIC – EPA policy evolving
Notes: 56
The two digit SIC tells us what industry we are dealing with and being in the same industry makes it more likely that emissions and controls are similar. Note: Support facilities are typically those which convey, store, or otherwise assist in the production of the principal product." Where more than 50% of the output or services provided by one facility is dedicated to another facility that it supports, then a support facility relationship is presumed to exist. Use Travers example
Coal mine to power plant, coal washing facility, steam plant to provide steam to process
Check EPA’s NSR Policy and Guidance Database for current policy
11/26/2019 - Interpreting "Adjacent" for New Source Review and Title V Source Determinations in All Industries Other Than Oil and Gas

## Slide 57: Common Control
Case-by-case determinations based on several factors:
Common ownership
Located on the same property
EPA guidance and memos can be used
Determinations should be reasonable and adequately explained in the record
Notes: 57
Common control is where things can get a bit complicated. If the two operations have the same owner (defined as >50% control) they are considered to be under common control. For example if a landfill supplies landfill gas to a power plant then the two operations would be under common control. Or company A takes sour gas from a refinery and treats the gas to produce H2SO4 and sends the clean gas back. The two operations would count as one for source definition but if company A took sour gas from several refineries common control would not matter.

## Slide 58: Adjacent or Contiguous
According to Merriam Webster:
  Contiguous means being in actual contact touching along a boundary or at a point and
  Adjacent means close or near : sharing a border, wall, or point
Changed Sept 4, 2018 - EPA no longer considers the functional interrelationships between activities to determine if they are adjacent
Notes: 58
Adjacent or contiguous has been a controversial issue. EPA has taken the position that distance is not the main factor in determining adjacent. Rather if the sources are connected in a supply or other relationship EPA believes them to be adjacent. EPA as we will discuss lost.
In addition adjacent also has a temporal sense. If two projects are built within a short time period they may well be considered part of the same project. It is generally up to the owner to prove that the projects are different. The owner can do this by proving that the two projects were separate business decision. One of our netting exercises covers this.
Case by case evaluation
9/4/2018 was a draft memo for comment, then
11/26/2019 EPA memo “interpreting adjacent” issued.
So miles long pipeline between to sources does not establish adjacent.

## Slide 59
Let’s try an
Applicability example
Taken from an EPA power point presentation
First a simple example
Notes: 59

## Slide 60: Example: Which pollutants are subject to PSD, NA NSR, and minor NSR permitting?
Facts:
Kraft pulp mills produce the dark-colored wood pulp used in the manufacture of a variety of paper products
The tons per year (tpy) in the plume are the mill’s potential to emit these pollutants
  10 tpy PM10
  80 tpy VOC
185 tpy SO2
New Kraft Pulp Mill
Area in
attainment
for PM10 and O3
Area in attainment
for SO2
Notes: 60
The objective here is to determine what rules the new plant is subject to.
New so using PTE (not actuals).
This example came from a 2013 briefing by EPA.

## Slide 61: Example Solution
Mill’s PTE:
  SO2=185 tpy
  VOC=80 tpy
  PM10=10 tpy
Area is in:
  Attainment for SO2
  Attainment for Ozone and PM10
Evaluate for PSD
  Determine what the applicable threshold is
    Since kraft pulp mills are one of the 28 listed source categories, the major source threshold is 100 tpy, not 250 tpy
  Determine if the source is major based on the threshold
    In this case, the SO2 emissions are 185 tpy, which is greater than 100 tpy. This makes the mill a major source for PSD. Now we have to review all attainment pollutants for PSD applicability.
Notes: 61
Since we have 185 tpy SO2 and kraft pulp mills are on the list of 28 sources (#2 on list) we are subject to PSD

## Slide 62: Example solution (Cont’d)
Mill’s PTE:
  SO2=185 tpy
  VOC=80 tpy
  PM10=10 tpy
Area is in:
  Attainment for SO2
  Attainment for Ozone and PM10
  Review the two attainment pollutants based on their SER to see if they fall into PSD
    The mill’s VOC PTE is 80 tpy, but VOC is not on the SER list. However, it is a precursor for ozone, and ozone is on the list with a SER of 40 tpy. VOC is subject to PSD because PTE is higher than 40 tpy.
    PM10 is on the SER list with a SER of 15tpy. The mill’s PM10 PTE is 10tpy, which is less than the SER. PM10, not subject to PSD.
Notes: 62
Even though VOC does not exceed the 100 tpy threshold it is subject to PSD (analysis and BACT) just like SO2.
PM10 would go thru state’s minor NSR permitting not PSD if above minor permit thresholds.

## Slide 63: “Significant Net Emission Increase” for NSR
Area Designation Modification Trigger (tpy)
Ozone Attainment 40 (NOx and VOC precursors)
Ozone Marginal 40
Ozone Moderate 40
Ozone Serious 25 (count all increases in 5 years)
Ozone Severe 25 (count all increases in 5 years)
Ozone Extreme 0
CO Attainment 100
CO Moderate 100
CO Serious 100 (if mobile sources significant)
CO Serious 50
PM2.5 All 10 [40 SO2 and NOx precursors]
PM10 All 15
PM All 25
NO2 All 40
SO2 All 40
Any other pollutant All any amount for those not listed
subject to regulation in the rule*
*More pollutants are listed in the rule than are in this table.
Notes: These are the net emission rates for NSR.
From 52.21 b 23 i

## Slide 64: Modified Sources
Major Modification (for both PSD and NA NSR) as defined, means any physical change in or change in the method of operation of a major stationary source that would result in: a significant emissions increase of a regulated NSR pollutant and a significant net emissions increase of that pollutant from the major stationary source.
64
Notes: 64
Now that we have finished with what new sources are covered by NSR and PSD it is time to see which modified sources are affected.
Note under modification you have to have an increase in emissions. Emission increases can eliminated by netting which will be discussed later. However there is something very important that is missing from this definition. Can anyone spot it. There is no discussion of permit limits Modifications can occur well under permit limits – allowable vs actuals.
Note: Two step process for modifications – first: physical change or change in operation that results in a significant emission increase, then second: a net emission increase looking facility wide

## Slide 65: Is It a Modification?
Physical changes or changes in the Method of Operation Include:
New Production Lines
Increased capacity of existing equipment
Process reconfiguration
Change in fuels not otherwise exempt
Non-routine replacement
Notes: 65
There are a number of different ways a source can be modified. Some of the more common are shown here.

## Slide 66: Exemptions
The following are not, by themselves, physical changes or a changes in method of operation:
Routine maintenance, repair, or replacement
Alternative fuel or raw material that the source was capable of accommodating before 1975
Increase in operating rate or hours of operation that does not exceed a permit limit
Change in ownership, with no other changes
Certain 1970’s energy crisis driven conversions
Notes: 66
RMRR
Even if you do have an increase in emissions there are a number of things that are not modifications. The most difficult of these to see and enforce is the routine maintenance exemption. We will spend several slides on this topic.

## Slide 67: Routine Maintenance, Repair and Replacement (RMRR)
You should consider:
  Nature and Extent of the change
  Frequency the change is performed
  Purpose of the change
  Cost of the change
  Other relevant factors
Notes: 67
One of the more complicated areas that are not modifications are “routine maintenances repair and replacement. This is a very complex issue. The famous WEPCO case where an electric utility conducted a “life extension” project. This was determined not to be Routine. A number of electric utilities in the late 1990s were issued NOVs for projects that EPA considered non routine but did not increase capacity. As a result of the NOVs the plants were subject to PSD or NSR. Gas transmission stations were also affected. EPA tool the position that turbines which were taken out of service for repair were considered non routine unless they were replaced back in exactly the same location.
EPA proposed a regulation in 2003 to better define what is routine repair. This rule included a cost test i.e.. 20% of the original equipment cost as well a reasonable test. However a court stayed the rules so we are left with logic and the reasonableness test.

## Slide 68: RMRR Exemption to Major Modification
Major Modification means:
(1) any physical change or change in the method of operation of a major stationary source that
(2) would result in a significant emissions increase of a regulated pollutant and a significant net emissions increase of that pollutant from the stationary source
See e.g., 40 CFR 52.21(b)(2)(i)
Notes: The next few slides are somewhat lawyerly so please put up with it. The topic is important.
Text from the reg, again two step definition
68

## Slide 69: RMRR Exemption to Major Mod. (Cont’d)
  A physical change or change in the method of operation shall not include . . . routine maintenance, repair and replacement.
See e.g., 40 C.F.R. §52.21(b)(2)(iii)
Notes: 69
Background: NSR rules exempt certain categories of activities from modifications
No activity is categorically exempt,
The RMRR was subsequently promulgated by EPA after the Seventh Circuit decision in WEPCO. [WI electric power company] which I’ll talk more about.

## Slide 70: RMRR Exemption to Major Mod. (Cont’d)
RMRR Case Law Principles:
  Definition of “physical change” is broad; the exemption applies to a narrow range of activities
  Applies to a narrow range of activities in keeping with EPA’s limited authority to exempt activities from the CAA
  No activity is categorically exempt
  Applies WEPCO multi-factor test on a case-by-case basis evaluation
Notes: WEPCO = consideration crtieria mentioned a couple of slides back.
70

## Slide 71: RMRR Exemption Wisconsin Electric Power Company (WEPCO)
WEPCO Multi-factor Test
  Nature and Extent
  Frequency
  Purpose
  Cost
Notes: These are the factors EPA considers based on the WEPCO case. Most of the discussion is based on power plants However all of these principles apply to any source.
1990 court decisions regarding RMRR
1992 EPA rulemaking 7/21/92
(21) * * *
. (iv) For any emissions unit (other than
an electric utility steam generating unit
specified in paragraph (b)(21)(v) of this
section) which has not begun normal
operations on the particular date, actual
emissions shall equal the potential to
emit of the unit on that date.
(v) For an electric utility steam
generating unit (other than a new unit or
the replacement of an existing unit)
actual emissions of the unit following
the physical or operational change shall
equal the representative actual annual
emissions of the unit, provided the
source owner or operator maintains and
submits to the Administrator on an
annual basis for a period of 5 years from
the date the
(33) Representative actual annual
emissions means the average rate, in
tons per year, at which the source is
projected to emit a pollutant for the two year
period after a physical change or
change in the method of operation of a
unit,
(ii) Exclude, in calculating any
increase in emissions that results from
the particular physical change or change
in the method of operation at an electric
utility steam generating unit, that
portion of the unit’s emissions following
the change that could have been
accommodated during the
representative baseline period and is
attributable to an increase in projected
capacity utilization at the unit that is
unrelated to the particular change,
including any increased utilization due
to the rate of electricity demand growth
for the utility system as a whole.

## Slide 72: RMRR Exemption WEPCO (Cont’d)
Nature and Extent
  Indications of Non-Routine Changes (from Cinergy)
    Use of “several outside contractors”
    “Several multi-volume planning studies”
    Time to complete the project: 13 weeks; 15 weeks
    “A majority of the parts of the unit, and in some cases every part of the unit, was modified or replaced, redesigned or upgraded”
    “Permanent improvements”
    Not like-kind replacements
Notes: 72
The Cinergy decision offers the most recent detailed analysis of the RMRR case-by-case factors.
Outside Contractors:
    “several outside contractors [performing] detailed inspections and assessments” See e.g., Cinergy, 495 F. Supp. at ___.
Extensive studies for the project
  “several multi-volume planning studies” See e.g., Cinergy, 495 F. Supp. at ___.
Time to complete the projects
  13 weeks for one unit’s project. See e.g., Cinergy, 495 F. Supp. at ___.
  15 weeks for one unit’s project. See e.g., Cinergy, 495 F. Supp. at ___.

## Slide 73: RMRR Exemption WEPCO (Cont’d)
Frequency
  Indications of Non-Routine Changes
    Occurs once or twice in the life of a unit
    Replacement of original components that have never been replaced
    Projects of this type occur infrequently in the industry
  Courts tend to scrutinize this factor more than the others
Notes: 73
Frequency of the project at the unit
  The frequency factor underscores the uniqueness of the project.
  Has the owner/operator ever conducted the project during the life of the unit? See e.g., Cinergy, 495 F. Supp. at ___.
Replacement of original components near the expected life. See e.g., Cinergy, 495 F. Supp. at ___.

## Slide 74: RMRR Exemption WEPCO (Cont’d)
Purpose
  Indications of Non-Routine Changes
    Restoring the unit to an original capacity or efficiency
    Less outages or downtime
    Extending the life of a unit beyond its expected retirement date
      E.g., unit is expected to last 35 years, but project designed to add additional 30 years of service for a total of 65 years - almost 2 times the expected life
Notes: Basic goal of NSR: improve AQ incrementally as old sources retire and new sources are subject to NSR/PSD (as is being done with the motor vehicle fleet)
74

## Slide 75: RMRR Exemption WEPCO (Cont’d)
Cost
  Indications of Non-Routine Changes
    Capitalization of costs
    Expenditures approved by high level management approval - e.g., company president
    Comparison of project costs to average annual maintenance costs at the facility - not across the company
Notes: 75

## Slide 76: “Routine Maintenance, Repair and Replacement” Policy
EPA policy is that the routine activity exception has a narrow scope and should generally be applied only to actions that are regular, customary, repetitious, and undertaken as standard practice to maintain a facility in its present condition
Notes: 76
Currently EPA takes a relatively conservative definition of RMRR. If you do it all the time it is RMRR but if you do it once every 15 years it is not.

## Slide 77: Debottlenecking
Significant Net Emissions Increase must include emissions increases from all emissions units affected by the change, both upstream and downstream
Removal of any limitation (physical or permitted) in a process line that enables the source to increase throughput can potentially increase emissions at other emissions units upstream or downstream in the process line
Notes: 77
Debottlenecking means a change to some part of the process which removes a restriction on the capacity of the source by modifying part of the process and thereby increasing the capacity and emissions. However, since there has been no physical change in the source which may have been the benefit of debottlenecking no additional action may be required such as use of BACT. But the increase in emissions should be used to determine if major mod or not.
Couple of examples

## Slide 78: Example 1 - Debottlenecking
Example from July 28, 1983 PSD Determination in Region 10
  A digester system in a Kraft pulp mill produces black liquor which is sent through a multiple effect evaporator system where it is concentrated and is then burned in a recovery boiler
  When the digester is expanded, in a way that additional black liquor will be produced, emissions from the recovery boiler must be counted in determining the net emissions increase
  Since the recovery boiler itself will not be undergoing a physical change or change in the method of operation, it will not have to apply BACT
Notes: 78

## Slide 79: Example 2 - Debottlenecking
Utility Example
  A coal prep plant is expanded to provide more coal to a coal fired utility boiler. The boiler is not modified but operates at a higher rate because of the additional coal provided by the coal prep plant.
  The increase in emissions from the boiler must be counted in determining the net emissions increase caused by the expansion of the coal prep plant.
  Since the boiler itself will not be undergoing a physical change or change in the method of operation, it will not have to apply BACT, but BACT must be applied at the coal prep plant for each pollutant for which NSR is triggered.

## Slide 80: Summary
Concept of Source been Subject of Litigation
Major source definition same for PSD, NSR, and Title V
Definition depends on location and source type
Same Source must be under Common Control, Same SIC Code, and on Adjacent Property – In flux
Notes: Same definition but thresholds can vary: 250/100 PSD 100 or less for NA NSR, 100/25/10 for TV
Single source is case by case. Company could avoid major source permitting by breaking up the facility into smaller sources.

## Slide 81: Summary (Cont’d)
Modification is physical change or change in the method of operation which results in a significant change in emissions
Significant net change varies by pollutant and location and program
Notes: Talk a lot more about net emission increases later.
SER, PSD/NA NSR

## Slide 82: Summary (Cont’d)
Modification does not include Routine Maintenance, Repair and Replacement (RMRR); emission increases up to permit levels; and/or change of fuel (if originally designed and permitted for the fuel)
Notes: Emission increases absent a physical or operational change

## Slide 83: Questions?
Notes: 83

## Slide 84: LESSON 4
Permitting Basics
Notes: Carl
E CFR: Show permit regs in CFR Part 52.21, 51.165 and 166 and Part 70
Federal version that states and local PAs use to develop their own regs that EPA approves into the SIP.
Learn your own agency’s regs as it can be slightly different than the federal regs:
The Abatement of Air Pollution Regulations are available on the Connecticut eRegulation System under Title 22a-174.

## Slide 85: LESSON OBJECTIVES
Understand what a permit is
Discuss who issues permits
Notes: Contract to emit pollutants
Permitting authority

## Slide 86: PERMIT DEFINITIONS
Permission given by an authorized government agency to construct, and/or to operate a source of air pollutants
A contract between source of regulated air emissions and public (as represented by authorized agency)
A document to translate broad regulatory requirements into specific requirements for facility
Notes: Regs vs permit conditions. Regs are broad
Don't want permits to just repeat or incorp by ref (IBR) regs
Also need to set source specific limits such as BACT and put in a permit

## Slide 87: “TYPES” OF PERMITS
Two “types” of permits
  Construction (or Pre-construction)
  Operating
These may be combined
  Depending on agency
Notes: As mentioned earlier Pre Construction = NSR/NA NSR/PSD Operating = title V or Part 70
Talk about merged program in TV lesson

## Slide 88: TYPE 1: PRE-CONSTRUCTION PERMITS
Notes: 88

## Slide 89: PRE-CONSTRUCTION PERMITS
Program often referred to as “pre-construction” permitting
Also called “New Source Review” (NSR)
AKA
Notes: Use context of “NSR = major PSD, NA NSR, minor NSR, state only (not in SIP)

## Slide 90: PRE-CONSTRUCTION PERMITS
Authorize the applicant to
  Construct or build, a new source of air pollutants
  Modify an existing source

## Slide 91: PRE-CONSTRUCTION PERMITTING PROGRAMS
Included in State Implementation Plan (SIP) for significant (major) sources
  SIPs are subject to EPA approval
For non-major sources, permitting agency rules apply
  These may - or may not - be in the SIP
Notes: Major defined in previous lesson
Some type of regulatory program should be in the SIP for minor sources per 40 CFR 51.160, with state by state permit thresholds.

## Slide 92
PRE-CONSTRUCTION PERMITS
Major Sources
NSR
New Source Review
Agency’s construction permit program
NA-NSR
Non-attainment New Source Review
Applicable in non-attainment areas
PSD
Prevention of Significant Deterioration
Applicable in attainment & unclassifiable areas
Notes: NA NSR and PSD is for Major sources
92

## Slide 93: PRE-CONSTRUCTION PERMITTING Major sources
Non-attainment
LAER
Offsets & Modeling
Attainment/Unclassified
BACT
Increment
Air Quality Analysis
Modeling
Notes: If an area is already Non-attainment for certain Criteria Pollutant, the State/Local Non-attainment NSR Rules (i.e. South Coast Air Quality Management District in Los Angeles, California) may also require Modeling to ensure that the new or modified source will not make an existing NAAQS or SAAQS (State Ambient Air Quality Standard) significantly worse.
LAER = from lesson 1
BACT mentioned earlier but will have a lesson on BACT later
At/un = psd
Show EPA’s AQ design value web page?? Or wait to NA NSR lesson

## Slide 94: STATE ONLY PERMITS
Most state and local agencies have permitting rules based on state statutes
These rules have various names such as State Air Code, etc.
They typically cover small sources
Notes: NA NSR and PSD is for Major sources
CT minor construction permitting = Sec. 22a-174-3a. Permit to construct and operate stationary sources >15 tpy criteria pollutants unless exempted [or 10/25 tpy HAPs and incins, but not in CT’s SIP, so not fed enf]

## Slide 95: STATE ONLY (Cont’d)
Examples – sources below major source thresholds
  Small boilers
  Small engines
  Small incinerators
  Area sources
    Gasoline transfer
    Coating operations
Chart: Emissions PTE
| Small boiler | Small engine | Small incinerator | Gasoline transfer | Coating Operation
PTE | 4.3 | 2.5 | 3.5 | 4.5 | 3.2
Column1
Column2
Notes: See PTE < 5 or 15 tpy if higher generally subject to SIP approved permit program

## Slide 96: “TRUE MINOR” PERMITS
Permits that are required for True Minor sources due to the requirements of the SIP
Examples:
  Emission levels above a certain threshold for a criteria pollutant
  Equipment may be subject to requirements such as NSPS
Notes: EXAMPLE: Source consisting solely of an Internal Combustion Engine that when operated 24/7/365 is below the major source threshold
NA NSR and PSD is for Major sources
> 15tpy but < major source thresholds (100/250tpy) in CT need minor permits [mostly what permit writers will work on!]
96

## Slide 97: “TRUE MINOR” PERMIT DEFINED (Cont’d)
A source of regulated emissions that when operated at maximum capacity continuously for 8760 hrs. per year, emits less than the major source threshold for each regulated pollutant, i.e., its PTE is less than the threshold
Notes: But is above the permitting threshold set in the state’s SIP: Varies by state 5-10 tpy up to the NSR SERs.
< 15tpy criteria poll or 10/25tpy HAP actuals per EU?.

## Slide 98: “TRUE MINOR” PERMITS (Cont’d)
TRUE MINOR exercise:
  A Waukesha lean burn internal combustion, spark ignited engine is to be installed at a natural gas gathering station. Its NOx emissions are 2.3 lbs. per hour at maximum rpm and load.
  Calculate the yearly emissions of this engine and make a determination if it is a “True Minor”
Notes: Next slide

## Slide 99: “TRUE MINOR” PERMITS (Cont’d)
TRUE MINOR exercise calculation
  8,760 hrs. per year
  2.3 lbs. of NOx per hr.
  8,760 x 2.3 / 2,000 = 10.1 tpy
  No Title V permit required
  If SIP has a permitting threshold of 10 tpy of a criteria pollutant before permitting is required, a “True Minor” permit would be required
  What if the source reduced its hours of operation?
Notes: Because the “PTE” is above the applicable threshold a permit would be required. to ensure the source is a true minor i.e. does not exceed the 10 ton/year threshold and would contain the necessary recordkeeping and reporting.
??? a FESOP permit would be required to make the reduction enforceable.
Talk about PTE in next lesson
Not a great example w/10.1 pte

## Slide 100: SMALL SOURCE PERMITTING
State/local agencies may have less formal permitting procedures for smaller sources (perhaps called “area sources”)
Some examples:
  Dry-cleaning
  Auto refinishing
  Gasoline dispensing
  Solvent cleaning/degreasing
  Rock crushing
Notes: I’m going to focus on SIP approved minor source permit program – needs to protect the NAAQS, should have some type of notice and comment, min thresholds vary by agency 5, 10, 15, 40 tpy up to the major source thresholds.
Sec. 22a-174-3b. Exemptions from permitting for construction and operation of external combustion units, automotive refinishing operations, emergency engines, nonmetallic mineral processing equipment and surface coating operations

## Slide 101: SMALL SOURCE PERMIT TYPES
Permitting authority issues source-specific permits
Permitting authority issues one permit that as long as procedures are followed, allows many individual sources to construct
  General permits
  Permit-by-rule
  Registration
Notes: For minor sources only: not for major sources subject to PSD or NA NSR
CT Sec. 22a-174-3d. Permit-by-Rule for Combined Heat-and-Power Systems.

## Slide 102: GENERAL PERMITS
Application process for sources under these programs is simplified, with quicker turn-around
In general, fees are still required
Notes: EPA does general permits for tribal lands
Show EPA general permit web pages for 5 and 6 sources categories
Concrete batch plants
Boilers and emergency engines
SI RICE
CI RICE
Printing ops
sawmill
Hot mix asphalt plants
Stone crushing
Gas dispensing
Auto body repoar
Petroleum dry cleaning

## Slide 103: ADVANTAGES OF GENERAL PERMITS
Extensive work done to develop “template” for source category
Permits for source category are standardized
Various levels of emissions may be covered by establishing categories by equipment type and emissions thresholds
Requirements may be more extensive for source categories with greater emissions

## Slide 104: ADVANTAGES OF GENERAL PERMITS (Cont’d)
Recordkeeping requirements are often reduced significantly
  Example for Cotton Gins
    Compliance is determined by number of bales of cotton produced
    Other conditions are usually included to ensure equipment is operated & maintained properly:
      No visible emissions from process equipment and control equipment.
      Fugitive emissions may not leave property boundaries
Notes: Show EPA’s concrete batch plant GP [define batch plant vs Portland cement kiln]
Source-wide production of concrete shall not exceed 2,000,000 cubic yards per year based on a 12-month rolling total.

## Slide 105: PRE- CONSTRUCTION PERMITS
REVIEW
Notes: NSR can be NA NSR and PSD for major and minor NSR (and syn minors that will talk about later) = pre construction permits (vs operating permits)
Key point: Applicant must have final permit in hand before commencing construction of a major source (and syn minor). Generally true for minor sources as well [not as stringent]

## Slide 106: OPERATING PERMITS
Notes: Later lesson
106

## Slide 107
  Authorize the permit holder to operate a source of air emissions
OPERATING PERMITS
Notes: CT TV regs = Sec. 22a-174-33. Title V sources
107

## Slide 108: OPERATING PERMITS (Cont’d)
Federal operating permits (Title V/Part 70/71)
Synthetic Minor permits
FESOPs (Federally Enforceable State Operating Permits)
State-only operating permits
Notes: 40 CFR part 70 for state regs 71 EPA’s regs = needed for “major sources” 100tpy criteria in attainment area, 100/50/25 tpy in O3 NA area, 10/25tpy HAPs, subject to a NSPS or MACT [unless exempted]
Syn minor and FESOP set fed enforceable limits to get source out of TV major [on criteria pollutants and HAPs]. Must go thru SIP approved permit issuance process [notice and comment]
State only can incorp limits from state construction permits that keep source below major [100 25/10]

## Slide 109: State-Only Operating Permit Applicability
Depends on
  Program
  Quantity and type of emissions
  Current and historical state requirements
Notes: CT has state operating permit regs, FESOP, and HAP 112.g pre construction permit regs???

## Slide 110: TITLE V PERMITS
Often referred to as “Title V”, “Part 70”, or “Federal” Operating Permits
Operating Permits detail the requirements that major sources, and other specified sources, must meet in order to operate in compliance with the CAA
A detailed discussion of Title V operating permits will be presented later in the course
Notes: More on TV in lesson 14
110

## Slide 111: SYNTHETIC MINOR PERMITS
An operator may avoid some of the requirements of the Title V program through the “synthetic minor” permit process
An otherwise major source can limit its emissions to below major source thresholds
These limits must be federally enforceable
Notes: Need to be issued under a SIP approved NSR permit program or an EPA approved FESOP.

## Slide 112: SYNTHETIC MINOR PERMITS (Cont’d)
Examples of emission limitations
  Reducing the hours of operation
  Limiting throughput
  Limiting the composition of
    Fuel
    Coatings
  Installing control equipment
Notes: Once in permit can take “credit” for these limits and controls. More in PTE lesson

## Slide 113: SYNTHETIC MINOR PERMITS (Cont’d)
If a source’s emissions are reduced to less than major source thresholds, and
If those limitations are federally enforceable as reflected in a permit, then
The source is eligible for a synthetic minor permit
Notes: Other options to take limits: SIP rule, compliance order

## Slide 114: FESOPs
FESOP Federally Enforceable State Operating Permit
A FESOP is the vehicle by which a synthetic minor source’s emission limitations are rendered federally enforceable
Purpose
  Reduce the PTE of a source below the Title V major source threshold, or otherwise place a limit on a source which would exempt it from Title V requirements
Notes: Many states have some form of FESOP
<100tpy Criteria or 10/25tpy HAPs
114

## Slide 115: SYNTHETIC MINOR PERMITS (Cont’d)
How does it work?
  PTE = A x EF x (1-ER/100) x (8760 hrs./yr.)/(2000 lbs./T)
    PTE = Potential to Emit
    A = Activity Rate
    EF = Emission factor for worst case operating alternatives
    ER = Overall Emissions Reduction Efficiency
      Collection efficiency
      Control efficiency
  Reducing anything on the right side of the equation will reduce the PTE
  In order for a limit restricting PTE to be effective, A, EF and ER must be clearly defined
Notes: A, EF and ER may also need to be in a fed enf permit
A = MMBTU/hr, ton clinker/hr EF= lbs/MMBTU, lbs/ton clinker produced
NB: ER has to be fed enf, more in lesson 5

## Slide 116: SYNTHETIC MINOR PERMITS (Cont’d)
Remember:
  All the components in the PTE equation must not only be defined, but must be documented
  All reductions in those components must be documented and federally enforceable
  Must be reflected in permit conditions
Notes: Afterburners, flares, baghouses all must be required by rule , order or permit to be fed enforceable, unless thry are “inherent” to the system [LNBs, feedstock recycling]

## Slide 117: SYNTHETIC MINOR PERMITS (Cont’d)
To develop effective synthetic minor permits, the permit writer must understand the following concepts:
  Major source
  Potential to emit (PTE)
  Developing enforceable permit conditions
These concepts will all be covered in detail in this course
Notes: What are you trying get source out of? PSD, TV, MACT/NSPS etc.

## Slide 118: CAUTION
Permit application for Synthetic Minor Permit asks for 9.9 tpy of HAP emissions
MSDS for solvents and compounds used indicates that accuracy of proposed solvents and compounds is ± 5%
Should this application be accepted as adequate for a synthetic minor?
Notes: 9.9 + 5% = 10.4tpy HAP so still subject to TV
HAPs = benzene, formaldehyde, Hg, Cr

## Slide 119
  States may or may not have a state only operating permit
  Many states view the state only construction permit as the vehicle, along with state regulations, that determine how a small source must be operated
  Must look to the individual state programs
STATE ONLY PERMITS
Notes: Such as CT/ NY ??
119

## Slide 120: STATE ONLY PERMITS (Cont’d)
As in construction permits, applicability is to smaller sources, with emissions below major source thresholds
The types of sources eligible for State Only permits varies with the permitting agency, but the typical sources are the same as those discussed in construction permits

## Slide 121: OPERATING PERMITS
REVIEW
Notes: A lot more detail in lesson 14: lots of details around TV that differ from NSR e.g., EPA’s role
Major sources need Title V operating permits issued in accordance with Part 70 or 71 regs. OP incorporate all applicable requirements into one permit – PSD, minor NSR, NSPS, MACT, SIP limits/requirements, along with appropriate monitoring, recordkeeping and reporting. Also FESOP and state only OP, can limit PTE to keep source out of major category.

## Slide 122: COMBINATION PERMITS
Notes: For complex sources such as refineries
122

## Slide 123: COMBINATION PERMITS
Combine the construction and operating permits into a single document
Permitting authority processes requirements at the same time
Doesn’t reduce the requirements for each type of permit
Can reduce paperwork and duplication
  Process and review only one permit application, rather than separate construction permit and operating permit applications
Notes: One notice and comment period
123

## Slide 124: WHO ISSUES PERMITS?
Permitting Agencies

## Slide 125: PERMITTING AUTHORIZATION
The EPA Administrator
Any state or local agency authorized by the Administrator
The state/local agency must also be authorized by state law
Notes: EPA = IC (part 49), outer continental shelf (part 55), and non approved states
Most State NSR SIPs and TV programs approved in the 90s or 00s

## Slide 126: PERMITTING AUTHORIZATION (Cont’d)
Any State or local entity authorized “under state law” to issue permits and implement various federal, state, and/or local air quality regulations
The agency must be authorized by EPA administrator to implement federal programs, including federal permitting programs
Notes: Thru the SIP state regs get made fed enf
TV programs not in the SIP but approved by EPA

## Slide 127: PERMITTING AGENCIES
Air quality permits for stationary sources are generally issued by state or local agencies
These agencies generally have responsibilities other than permitting
Notes: Such as Enf of permits, NSPS, MACTs, SIP development, NA area planning, AQ monitoring/modeling, voluntary programs (Clean School Bus – DERA)

## Slide 128: PERMITTING AGENCIES (Cont’d)
In some states, stationary source permitting is done by the state agency
In some states, stationary source permitting is done by local agencies
  Counties
  Cities
  Special purpose Districts
In some states, a hybrid situation exists

## Slide 129: PERMIT CUSTOMERS
Applicant
Public
Courts
Enforcement branch of agency
Other Sources
EPA and other governmental agencies
Others?
Notes: Source dependent e.g., refinery in city vs rock crusher in rural area
National NGOs
NPS, USFS
Other permit authorities, Academics for research, Local elected officials
Sierra Club, EDF

## Slide 130: PERMIT CUSTOMERS (Cont’d)
Class Discussion
  For what purpose(s) did each “customer” use the permit?
  What kinds of permit terms were important to each?
  Are there other people who might use the permit?
Notes: 130

## Slide 131: PERMITTING AGENCIES Other Roles
In addition to permitting, state statutes authorize state and local agencies to administer certain parts of federal programs
  State Implementation Plan (SIP) development
    A Plan developed by the state to attain and maintain compliance with federal air quality standards
  NSPS
  Hazardous air pollutants: NESHAP, MACT
Notes: CAA 110 = SIP to protect the NAAQS. States develop and revise the SIP and EPA reviews/approves
CAA 111 and 112 = delegation to states (to stand in EPA’s shoes) otherwise EPA implements

## Slide 132: PERMITTING BASICS Review
Pre-construction permits
  Non-attainment NSR
  PSD
Operating permits
  Title V
  State only
Permit Issuance
  State/local agencies (may require EPA authorization)
Notes: PSD/NA NSR for major sources, minor NSR, syn minor NSR

## Slide 133: QUESTIONS?

## Slide 134: LESSON 5
Potential to Emit (PTE)
Notes: Ted
This lesson is about the concept called potential to emit. In the permitting world potential to emit or PTE is the concept that determines what permitting scheme applies to a particular source i.e. PSD,NSR, minor NSR and title V.

## Slide 135: POTENTIAL TO EMIT
Why discuss Potential to Emit (PTE)?
  Applicability is often based on PTE
    Permit (PSD/NSR, Title V, etc.)
    Regulatory (MACT/NESHAP standards)
  Applicability can also be based on the date of construction, modification or reconstruction of specified source categories (e.g., NSPS)
PTE is pollutant specific
    The exception is total HAPs
Notes: PTE generally determines applicability esp for new sources that don’t have actual emissions baseline
MACT/NSPS not so much PTE
Mention NSR 250/100, TV 100, HAPs 10/25tpy
Not so much for NSPS/MACT (more based on size of EU)
135

## Slide 136: Lesson Objectives
Determine how PTE affects permit requirements
Learn how to calculate PTE
How to limit PTE
Notes: We will learn how to calculate PTE and how PTE affects the type of permit a source needs and how we can use PTE to avoid certain major source regulations.

## Slide 137: Potential to Emit (PTE)
So what is “Potential to Emit” ?
The maximum capacity of a stationary source to emit a pollutant under its physical and operational design.
Any physical or operational limitation on the capacity of the source to emit a pollutant, including air pollution control equipment and restrictions on hours of operation or on the type or amount of fuel combusted, stored or processed, shall be treated as part of its design if the limitation or the effect it would have on emissions is federally enforceable.
Notes: From 40 CFR 52.21(b)(4). Also in your agency’s SIP approved regs
The key terms here are the “maximum capacity of the source” and the “physical and operational restrictions”. We will discuss both of these later.
Any physical limit on capacity has to be federally enforceable. Now while the regulation and definition says federally enforceable case law now says that it has to be enforceable as a practical manner.
137

## Slide 138: PTE (Cont’d)
In simple terms PTE is the maximum emissions that the source can produce or is allowed to produce
For many sources PTE can be challenging to calculate
Notes: The concept of PTE is relatively simple but the application and calculation of PTE is not.

## Slide 139: PTE Example Calculations
Fuel Burning sources like boilers and process heaters are frequently assumed to run at nameplate capacity for up to 8760 hours per year.
Non-emergency generators are generally assumed to run 100% of the time or 8760 hours
Emergency generators are limited (by NSPS) to 100 hours of non-emergency operation per year (EPA policy recommends assuming 500 hours per year of emergency operation).
Batch operations like auto refinishing take into account startup clean up and actual paint time.
Notes: PTE is not always a very logical number. To calculate the PTE you need to know the type of source. You will end up with situations like a space heating boiler in Arizona operating a full capacity in the summer months. Obviously this will not happen. In other cases a multi-station printing press will have it assumed that it covers a paper stock 10 times over. However in some cases EPA has recognized that continuous operation will not be possible. The vehicle refinishing operations take into account the time it takes to prep the vehicle and allow the car to dry. Many sources will take limits on operation and this will be discussed in detail later.
September 6, 1995
MEMORANDUM
SUBJECT: Calculating Potential to Emit (PTE) for Emergency Generators
The EPA believes that 500 hours is an appropriate default
assumption for estimating the number of hours that an emergency
generator could be expected to operate under worst-case
conditions.
139

## Slide 140: PTE (Cont’d)
Where does the data to calculate PTE come from?
First we calculate emissions, then ramp them up to annual rates
Ideally, source specific data
Notes: Source specific = stack test or CEMs (gold standard), if not EF (AP42)
140

## Slide 141: PTE (Cont’d)
Emission Factors
  Stack test data
  AP-42
  WebFIRE
Material Balance
EPA software
  Tanks
  LandGEM
  WATER9
  SPECIATE
Engineering Judgment
EPA’s Air Emissions Factors and Quantification website is a good source of info
  www.epa.gov/air-emissions-factors-and-quantification
Notes: The data shown on these page are the more generic data sources, i.e., not specific to a particular source. Generally you and the source are better off with source specific data but if you can’t do that these sources are defensible. For example AP-42 says large generators emit 0.031 lb/hp-hr. but new and even 10 year old engines actually emit less than half this amount.
Of course EPA and states have found the opposite to be true as well after testing sources – oil production engines emitting more Nox than the AP42 EF
Show Air Emissions Factors and Quantification web page and link on handout
141

## Slide 142: PTE (Cont’d)
Emission Factor method
  E = A x EF x (1-ER/100)
    E = Emissions
    A = Activity Rate
    EF = Emission factor for worst case operating alternatives
    ER = Overall Emissions Reduction Efficiency
      Collection efficiency
      Control efficiency
    [A and EF are often stated in pounds and at hourly rates, so E must be converted to tons annually to determine the PTE]
    Activity rate is the maximum capacity of the source
Notes: Emission factors are the simple to use. In AP42 most of the emission factors are in pounds per unit of production and need to translated into pounds per hour. Most of the time this translation is done on the basis of 8760 hours but this is not always the case. Time for maintenance and other mandated shut downs can be considered and taken into account. i.e. boilers must be shut down for inspection and maintenance.
MMBTU/hr * lbs/MMBTU * 8760hrs/yr / 2000lbs/ton = tpy
NB: ER only if enforceable or inherent
142

## Slide 143: PTE (Cont’d)
Material balance method
  Emissions = Input – consumed – recovered – destroyed
    Input is the total amount of the pollutant that can enter the process
    Consumed is the total amount that becomes an integral part of the product or process
    Recovered for recycling or reuse
    Destroyed using a control device
Notes: Material balance is a good way and for some sources the only way to calculate emissions (esp for VOCs). The term recovered includes both recovered and generated as waste. This is used for VOC sources where solvent is evaporated like paint booths. Destroyed (in add on control device) only counts if required by regulation or other enforceable conditions.
143

## Slide 144: PTE EXERCISE 1
Evaluate the following:
  A facility can use a maximum 100 lbs/hr of ink that has a VOC content of 35% by weight.
  20% of the ink is retained on the substrate.
  The incinerator has a 95% control efficiency.
What are the lbs/hr of VOC emitted?
VOC Mass Emissions = (100 lbs/hr * .35) (1 - .20) (1 - .95) = 1.4 lbs/hr
6.13 tons/year
Notes: Simple mass balance exercise. In simplest terms the lbs/hr would be multiplied by 8760 hrs/yr to produce PTE or 6.13 tpy. Note: we can only count the incinerator if it is part of an enforceable condition or required by the permit. The PTE would be 120 tpy without the incinerator.
144

## Slide 145: PTE EXERCISE 2
A 300 MMBtu/hr. boiler that can burn either natural gas or distillate oil, is limited to NOx emissions of 0.10 lbs/MMBtu by an NSPS.
NOx EF for natural gas is 190 lb/106 scf
NOx EF for distillate oil is 20 lb/103 gal
Convert to MMBtu
  Natural Gas: divide by 1,020 MMBtu/106 scf
  Distillate Oil: divide by 140 MMBtu/103 gal
The NSPS limit is met with low-NOx burners and FGR realizing 50% NOx reduction for fuel oil and 85% NOx reduction for natural gas
2011 fuel usage
  Natural Gas - 1,200 x 106 scf
  Distillate Oil – 100,000 gals
Notes: A bit more complicated spend some time playing with the numbers. EF = emission factor which are from AP-42.
NSPS can be considered an fed enf limit.
Another not so great example: Why can’t the LNB and FGR controls be taken into account as the are inherent to the boiler system (can’t run w/o LNB or FGR). If so, EF woulndn’t be .1 lbs/MMBTU it would be lower accounting for the LNB and FGR.
145

## Slide 146: PTE EXERCISE 2 (cont’d)
What is the PTE of the boiler for NOx?
What are the actual annual NOx emissions from the boiler for 2011?
Notes: The obvious questions
146

## Slide 147: PTE EXERCISE 2 CALCULATIONS
Boiler PTE for NOx:
  EF * Max Hourly Capacity * 8760 hr/yr /2000 lbs/T
  0.10 lbs/MMBtu * 300 MMBtu/hr * 8760 hrs/yr / 2000 lbs/T
  262,800 lbs/yr of NOx or 131.4 T/yr of NOx
Actual NOx emissions:
  EF * annual usage * (1-control efficiency)
  Nat Gas = 190 lb/106 scf * 1,200 x 106 scf * (1 - .85) = 34,200 lbs
  Dist. Oil = 20 lb/1000 gal * 100,000 gal * (1 - .5) = 1,000 lbs
  Total = 34,200 lbs + 1,000 lbs = 35,200 lbs = 17.6 T/yr
Notes: These calculations show that the PTE bears little relationship to actual emissions i.e. it is almost an order of magnitude higher.
But can’t use actual for PTE applicability determination unless source takes fed enf limits in a permit or reg.
[Why not use the LNB and FGR controls be taken into account as the are inherent to the boiler system]
Boiler over 250mmbtu/hr is subject to 100tpy threshold for major NSR
147

## Slide 148: LIMITING PTE
Why
How
Legal Requirements
Notes: Now that we can calculate PTE let’s look at how to limit it so the very high number in the last example does not cause unnecessary permitting. We have a lesson on emissions limits that covers this in more detail in a couple of days.

## Slide 149: LIMITING PTE (Cont’d)
Why place an operation or physical limitation on the capacity of a source?
  Actual emissions may be much lower than the potential to emit, or
  To clearly demonstrate that only non-regulated materials are used.
  Source can avoid some regulatory requirements
    NSR/PSD, MACT, Title V
    Still subject to NSPS, NESHAPS and SIP requirements not triggered by PTE or raw material usage
  Sources with similar actual emissions will be regulated similarly.
  Regulators can concentrate resources on large sources.
Notes: Bottom line if the PTE is far from actuals both you and source are better off. Less enforcement for both of you.
NSPS = Part 60 regs for new sources of criteria poll
NESHAPS = Part 61 and 63 regs for HAPs
149

## Slide 150: LIMITING PTE (Cont’d)
Where do you find physical or operational limitations?
  Regulations
  Permits
  Consent decrees
  Other enforceable documents
Notes: There are lots of ways to find physical and operational limits. The ones shown here are the conventional and normal ways to make limits but there can be more imaginative ones that should not be neglected. EPA limits emergency generators to 500 hours. If there is a downstream system that limits operations of your source it may be an operational limit on emissions.

## Slide 151: LIMITING PTE (Cont’d)
…physical or operational limitation to be effective, it must be [federally] enforceable:
  Federal regulations (NSPS, NESHAPs, Acid Rain)
  State Implementation Plan rules (SIP)
  Legally enforceable documents (Consent decrees, binding agreements)
  Permits
How do we write a permit that is federally enforceable?
Notes: You generally find PTE limits in permits but there can be circumstances that don’t fit the normal mold.

## Slide 152: LIMITING PTE (Cont’d)
What does “enforceable” require?
  The permit limitation must be:
    Permanent
    Quantifiable
    Practically Enforceable
Notes: Define in next 3 slides
Permanent means it will not change. Quantifiable means it must be able to be measured and practically enforceable is averaging time etc. In addition any enforceable condition must have monitoring and data collection built in.

## Slide 153: LIMITING PTE (Cont’d)
Limit must be Permanent
  In general, limit must not expire on its own accord
Notes: To revoke would need notice/comment process
TV permits typically only last 5 years

## Slide 154: LIMITING PTE (Cont’d)
Limit must be Quantifiable
  The limit can be measured or determined reliably and replicably
  Limits must be either
    Physical limits or operational limits
    Blanket emission limits (i.e., less than 249 t/yr, etc.) must be accompanied by
      Corresponding physical or operational limits or
      Some method to demonstrate calculation methodology
PTE = A x EF x (1-ER/100) x (8760 hrs/yr) / (2000 lbs/T)
Notes: You must have a number that can be calculated

## Slide 155: LIMITING PTE (Cont’d)
Limit must be practically enforceable
  Limit must be clearly stated and defined
  Specify averaging times
    Should be monthly or less
      Annual limits must be on a rolling basis
    At a minimum, should reflect the emission limit’s purpose
A later session will focus on averaging times
Notes: Averaging time is very important to EPA. 12 month rolling is the minimum. Reflecting the limits purpose can mean that the averaging time should reflect the way the control equipment operates for example
<100/250 tpy = 12 month rolling
Avg time lesson 10

## Slide 156: LIMITING PTE (Cont’d)
Practical enforceability (cont’d)
  Method for determining compliance
    Initial compliance
      Reference Test Methods usually
    Operational compliance
      CEMs, parametric monitoring, PEMs, periodic testing
  Recordkeeping
  Reporting
Notes: PEMs = predicative emiss monitoring
Versus parametric emissions monitoring

## Slide 157: LIMITING PTE (Cont’d)
The limit must be properly issued
  Permit issued pursuant to an approved SIP, or sec. 112(l) submittal
    Processed and issued in compliance with the approved SIP or sec. 112(l) procedure
  Reflect an NSPS, NESHAP, SIP, Acid Rain or other federal regulation
Notes: CAA112(l) approval for state to issue permits to HAP source to limit PTE below major.

## Slide 158: LIMITING PTE (Cont’d)
Procedural requirements
    The procedural requirements set out in SIP or other approved permitting program must be followed
    Example: EPA Environmental Appeals Board In re Prairie State Generation Station, PSD Appeal No. 05-02 (March 25, 2005)

## Slide 159: Quick Review
Potential to Emit (PTE)
  Why it is important
  How it is calculated
    Methods
    Reference material
  Why limit PTE
Notes: Starting point for applicability of permit programs
Emissions test, EF, mass balance
Get out of unnecessary permit req
159

## Slide 160: Questions?
Notes: 160

## Slide 161: LESSON 6
Nonattainment (NA)
New Source Review (NSR) Permits
Notes: Carl
This lesson is first of two lessons on permitting in non attainment (NA NSR) and attainment areas (PSD – tomorrow).
CT PSD = Section 22a-174-3a

## Slide 162: Lesson Objectives
Explain legal basis for NA- NSR
Review applicability
Discuss state and local permits for nonattainment areas
Define technology requirements
Examine procedures for air quality protection
Notes: Here are the lesson objectives. One area we discuss is the state federal relationship

## Slide 163: Pre-construction Permits NA-NSR
Purpose:
  Allow economic expansion in Non attainment areas without air quality degradation
  Assure emissions from new and modified major sources are reduced to the maximum extent feasible
  Implemented through a preconstruction permit requirement
Notes: This preconstruction program is defined in the CAA 1990 and was designed to allow economic growth and minimize emissions in the nonattainment areas. In fact the program was supposed to eliminate emission increases from large sources. Overall the system is supposed to ensure that new construction actually leads to an emission decrease in NA areas.
163

## Slide 164: Pre-construction Permits NA-NSR (Cont’d)
Similar to PSD in many respects, but with the following significant differences:
  Major source thresholds
  Pollutants evaluated
  VOC & NOx significance levels
  Control technology requirement is LAER rather than BACT
  Offsets
  Certification that other facilities under the same ownership within the state are in compliance
Notes: We will talk about PSD tomorrow in lesson 7, but this will give you a taste of what is to come. Two ways it is different are the requirement for offsets i.e. reduce more then you add. And the certification that all other sources are in compliance.
164

## Slide 165: NSR Permitting Process
Major Source?
Yes
No
Attainment
Area?
PSD
NA- NSR
Yes
No
Offsets
Modeling
Modeling
LAER
LAER
BACT
minor source
review or
other programs
Notes: Simple flow chart showing how the two programs are related. If an area is already Non-attainment for certain Criteria Pollutant, the State/Local Non-attainment NSR Rules (i.e. South Coast Air Quality Management District in Los Angeles, California) may also require Modeling to ensure that the new or modified source will not make an existing NAAQS or SAAQS (State Ambient Air Quality Standard) significantly worse.
LAER = lowest achievable lesson 1
Remember SER from lesson 3, so if NA NSR applies likely PSD does as well for pollutants that the area is in attainment for.
Show EPA’s AQ DV maps website, map doesn’t show classifications but areas get “bumped up” if they don’t attain by the attainment date. NY/NJ/CT is severe for ‘08 O3 and serious for ‘15 O3, rest is marginal or moderate.
Your agency’s planning (SIP) group will know and NA areas are also listed in the CFR at Part 81
https://epa.maps.arcgis.com/apps/MapSeries/index.html?appid=bc6f3a961ea14013afb2e0d0e450b0d1

## Slide 166: Clean Air Act – Title I
Part A: Air Quality and Emissions Limitations
Part B: Ozone Protection (replaced by Title VI)
Part C: Prevention of Significant Deterioration
Part D: Plan Requirements for Nonattainment Areas
Notes: The program is found in title I (stationary sources) subpart D [aka as 40 CFR 51.165 and in CT’s regs]

## Slide 167: “Major Source” Thresholds for NSR for Ozone, PM, and CO Depend on Non-Attainment Status
Area Classification Major Source PTE (tpy)
Ozone Marginal 100
(precursors i.e. NOx and VOC)
Ozone Moderate 100
Ozone Serious 50
Ozone Severe 25
Ozone Extreme 10
CO Moderate 100
CO Serious 50
PM10/2.5 Moderate 100
PM10/2.5 Serious 70
Notes: Recall from lesson 2 the NA NSR major source thresholds.
NA NSR major source threshold is 100 tpy (or lower in some NA areas) for ALL sources. It is irrelevant what category the source belongs to because listed source categories do not exist for nonattainment NSR.
At a new major source, NA NSR applies only to the NA pollutants with PTE above the major source threshold (other that are not NA related get treated as attainment PSD). You will hear that this different in PSD
167

## Slide 168: Pre-construction Permits NA-NSR
Pollutants evaluated:
  Criteria pollutant(s), precursors or constituents, for which the area is nonattainment
    VOC and/or NOx for Ozone NA, depending on attainment plan
    NOx and SOx are PM2.5 precursors
    Remember, PSD evaluation includes all NSR pollutants
Notes: NA-NSR applies only to criteria pollutants and their precursors for which the area is NA. Precursors of ozone are NOx and VOC. Precursors of PM2.5 are NOx and SO2
PSD/NA NSR eval triggered if exceeds SER
168

## Slide 169: Pre-construction Permits NA-NSR
Control technology requirement is LAER (Lowest Achievable Emissions Rate) rather than BACT
  Emissions rate that does not exceed the amount allowable under applicable new source performance standards promulgated by the United States Environmental Protection Agency under 42 United States Code, §7411, and that reflects the following:
    (A) the most stringent emission limitation that is contained in the rules and regulations of any approved state implementation plan for a specific class or category of facility, unless the owner or operator of the proposed facility demonstrates that such limitations are not achievable; or
    (B) the most stringent emission limitation that is achieved in practice by a specific class or category of facilities, whichever is more stringent.
Notes: Lowest Achievable Emission rate (LAER) is effectively the best that has been done in practice. For example the last 5 LAER results for combined cycle gas turbines came up with an emission limit of 2 ppm for NOx using combustion control and SCR. Going back about 8 years the LAER decision was a bit higher at 5-9 ppm.
NSPS limits set the LAER floor (same as for BACT under PSD)
From 40 CFR Part 51.165 (a) (1) (xiii) same in your agency’s SIP approved NA NSR regs
169

## Slide 170: BACT vs. LAER
Primary difference
  BACT review considers economic and other factors
  LAER does not
Notes: Since LAER does not consider cost (at least overtly) and site specific factors, LAER tends to be more consistent that BACT (talk more about BACT in lesson 11)

## Slide 171: Pre-construction Permits NA-NSR
Certification that other major facilities owned or operated within the state are in compliance or on a schedule of compliance (Title I certification)
Notes: This merely means that the permit application has to have a certification that the company has no NOVs outstanding and is in compliance with all rules in the state. One interesting side to this is that it means that if the company has any facility out of compliance that the state does not know about it must report it or come into compliance before the permit application is filed. Also the company must make a good faith effort to determine if they are in compliance.
171

## Slide 172: Pre-construction Permits NA-NSR
Offsets:
  Emission reductions that:
    Offset the emissions increases resulting from the new source or modification, and
    Provide a net air quality benefit
  Offset ratio can be from 1:1 up to 1.5:1, depending on:
    the criteria pollutant of concern; and
    the nonattainment classification
Notes: In addition to LAER emissions from the new source must be offset with emission reductions at other sources. All offsets are more than 1 to 1 and may go as high as 1.5 to 1. The intent is to provide a net air quality benefit.
Offsets in lesson 12

## Slide 173: Quick Review NA-NSR Pre-construction Permits
Nonattainment NSR
  Major source thresholds
  Pollutants evaluated
  VOC & NOx significance levels
  Control technology requirement is LAER rather than BACT
  Offsets
  Certification that other facilities within the state are in compliance
Notes: VOC and Nox SER can’t be 40tpy in a serious or severe area as the major threshold is 50 or 25tpy. So regs specify 25tpy.
173

## Slide 174: Questions?
Notes: 174

## Slide 175: LESSON 7
Prevention of Significant Deterioration (PSD)
Notes: Carl
Intro to PSD: PSD is one of the most important and complicated of all of the air regulations. It was born in litigation (in a supreme court non decision). Prior to being put into the CAA as subpart C PSD was found in the preamble to the act where it says that the purpose of the act is “to protect and enhance the quality of the nation’s air resources so as to protect public health and the productive capacity of its people.” The complications of PSD can be seen from the fact that it has been to the supreme court five times and will probably be back again.
At end of lesson can go thru PSD SOB [Deseret pdf] as an overview of what a permit writer would have to prepare.
CT PSD = Section 22a-174-3a

## Slide 176: Lesson Objectives
What we’re going to cover:
  Purpose
  Applicability
  BACT
  Increment
  Ambient Air Impact
  Pre- and Post-Construction Monitoring
  Additional Impact Analysis
Notes: Today we are somewhat briefly go over all sections of the regulations from its purpose to the various parts of the rules.

## Slide 177: Regulations
40 CFR 52.21 - EPA PSD regulation
40 CFR 51.166 - A state or local approved program requirements
Notes: As with most federal air regulations part 51 tells the states what they should have in their regulations and part 52 has the rules that will be imposed if the states do not act.
NY DEC’s Chapter III Subpart 231-7 and 231-8 = PSD regs

## Slide 178: PSD Purpose
Purpose:
  Ensure air quality in attainment and unclassifiable areas does not deteriorate due to construction or modification of major stationary sources
  Ensure emissions from new and modified major sources are well controlled
Implemented through a pre-construction permit requirement (NSR for attainment and unclassifiable areas)
Notes: From CAA Title I Part C: The intent of PSD is to keep changes in air quality within what are considered acceptable levels. It is implemented through a complicated pre-construction review process. It is equivalent to NSR for attainment area. Both programs are pollutant by pollutant.
178

## Slide 179: PSD Applicability
Construction of a new major stationary source
A Major Modification to a non-major source, if the physical change by itself constitutes a major stationary source
Major Modification to a major stationary source resulting in a significant emissions increase and a significant net emissions increase
Notes: PSD affects only major sources of criteria pollutants. These are generally large sources or modification of large sources. These are also the types of sources that top officials like to announce and frequently take interest in the rapid construction of. In other words the governor announces a source with 5 thousand jobs and wants it started tomorrow and you have to tell him that it will take a long to process the information when you finally get it.
179

## Slide 180: PSD Applicability Major Source
“Major stationary source” was the common term in all three scenarios
What is a Major Source?
  Depends on location and regulation type
  PSD: PTE of 250 tpy unless listed source
Notes: We did this yesterday by repeating is always a good idea. There are a number of different definitions of a major source in PSD. In simplest terms PSD will apply to any source with a PTE pf 250 tpy but as the next slide shows it really does get more complicated.
PSD, which applies to all attainment pollutants with significant emissions at a major source. The “Major for one, major for all” concept does not apply for NA NSR.
180

## Slide 181: PSD Source Categories with 100 tpy Major Source thresholds
1. Coal cleaning plants (with thermal dryers) | 15. Coke oven batteries
2. Kraft pulp mills | 16. Sulfur recovery plants
3. Portland cement plants | 17. Carbon black plants (furnace process)
4. Primary zinc smelters | 18. Primary lead smelters
5. Iron and steel mills | 19. Fuel conversion plants
6. Primary aluminum ore reduction plants | 20. Sintering plants
7. Primary copper smelters | 21. Secondary metal production plants
8. Municipal incinerators capable of charging more than 50 tons of refuse per day | 22. Chemical process plants (does not include ethanol production facilities that produce ethanol by natural fermentation)
9. Hydrofluoric acid plants | 23. Petroleum storage and transfer units with a total storage capacity exceeding 300,000 barrels
10. Sulfuric acid plants | 24. Taconite ore processing plants
11. Nitric acid plants | 25. Glass fiber processing plants
12. Petroleum refineries | 26. Charcoal production plants
13. Lime plants | 27. Fossil fuel-fired steam electric plants of more than 250 million British thermal units (BTU) per hour heat input
14. Phosphate rock processing plants | 28. Fossil-fuel boilers (or combination thereof) totaling more than 250 million BTU/ hour heat input
Notes: 181
Again from yesterday, For these sources the PTE for PSD is 100 tpy. As we talked earlier The list seems somewhat random and in fact it may be. The only rationale for the list was that there was data on large sources available in 1973.
Fugitive emission count for this list of sources. BTW: Same applies for NA NSR and TV

## Slide 182: Pollutant Added to PSD
  PM 2.5
    PM2.5 final NSR rule published May 16, 2008
    See table on page 5 of the rule
    Major source baseline date – October 20, 2010
Notes: Another pollutant was added to PSD in 2008. PM 2.5 is treated just like any other criteria pollutant.

## Slide 183: Major Modification PSD
Subjects Source to PSD
See Lesson 3 for discussion
Notes: We discussed major mods yesterday, so we are going to talk about them again!
183

## Slide 184: Modification PSD
Two preliminary concepts to discuss
  Project vs. Emissions Unit
    Emissions from a project determine whether a significant emissions increase occurs
    A project is made up of modifications to one or more emissions units
  Aggregation
    Activities at a source should be aggregated when they are substantially related.
      EPA codified a proposed new aggregation rule
      Note that on March 29, 2010, EPA proposed to revoke the new rule
Notes: Emissions are counted on a project and emission unit basis.
Aggregation means that sources that are substantially related either in time or type should be counted together. For example if a project can be considered to be built in stages over time all stages should be counted together to determine if PSD applies. Note add discussion of court and other.
. We have already talked about aggregation in our discussion of what is a source. Lesson 3 [Slide 56]
Interpreting "Adjacent" for New Source Review and Title V Source Determinations in All Industries Other Than Oil and Gas – 11/26/19
Source can’t break up related projects (dis aggregate) to avoid PSD permitting.
Exercise on improper dis-aggregation a bit later.
Use flip chart diagram to show the “source” or “facility” vs “emissions unit” Add coal mine and landfill
In notebook from Raleigh – 1. common control or ownership, 2. same SIC code [or support facility, 3. contiguous and adjacent

## Slide 185: Major Modification PSD
Significant Emissions Increase
    New Emission Unit [52.21(b)(7)(i)]
      Is, or will be newly constructed and
      Has existed for less than 2 years since it first operated
    Existing Emission Unit [52.21(b)(7)(ii)]
      Any emission unit that isn’t a new emission unit
      A replacement unit is an existing unit
Notes: If < 2 years can’t calculate a 2 year actual emission value
Here we define a new versus an existing unit. Important since we have different emission rates that trigger PSD. Also important since PSD is in for one and in for all.
Replacement = exact same as existing unit [like replacing car engine with exact same engine as original, can’t add a turbo or V8 to replace a I4]
185

## Slide 186: Significant Emission Rates [52.21(b)(23)]
Pollutant | SER
Carbon Monoxide | 100 tpy
Nitrogen Oxide | 40 tpy
Sulfur Dioxide | 40 tpy
Particulate Matter (PM/PM10) | 25/15 tpy
PM2.5 | 10 tpy of direct PM2.5 emissions; 40 tpy of sulfur dioxide emissions; 40 tpy of nitrogen oxide emissions unless demonstrated not to be a PM2.5 precursor 52.21(b)(5)
Ozone | 40 tpy VOCs or nitrogen oxides
Lead | .6 tpy
Fluorides | 3 tpy
Sulfuric acid mist | 7 tpy
Total reduced sulfur (including H2S): | 10 tpy
Reduced sulfur compounds (including H2S) | 10 tpy
Notes: Main concept to remember
- If new source emissions > SERs trigger PSD permitting for other pollutants less than the major source threshold
– if Mod at existing major source net emissions increase would exceed these SERs then project is subject to PSD permitting

## Slide 187: Significant Emission Rates [52.21(b)(23)]
Pollutant | SER
Municipal waste combustor organics (measured as total tetra-through octa-chlorinated dibenzo-p-dioxins and dibenzofurans) | 3.2 x 10–6 megagrams per year (3.5 x 10–6 tons per year)
Municipal waste combustor metals (measured as particulate matter) | 14 megagrams per year (15 tons per year)
Municipal waste combustor acid gases (measured as sulfur dioxide and hydrogen chloride) | 36 megagrams per year (40 tons per year)
Municipal solid waste landfills emissions (measured as nonmethane organic compounds) | 45 megagrams per year (50 tons per year)

## Slide 188: Major Modification PSD
Significant Emissions Increase – New Units
    Actual to Potential
      Emissions Increase = PTE – BAE
    Calculating Baseline Actual Emissions (BAE)
      Equals zero for initial construction and operation purposes
      Thereafter, and for all other purposes, equals PTE
    Calculating PTE
      Can be limited by enforceable restrictions
Notes: If you are adding a new unit to an existing source the test is base line emission to PTE. So, if entire source is new then BAE = 0 and PTE
Since NSR “reform” in 2002 the test [for existing units] was modified to be base line emissions to projected actuals, but still PTE for new EUs.
188

## Slide 189: Major Modification PSD (Cont’d)
Significant Emissions Increase – Existing Units
      Actual to Projected Actual
        Emissions Increase = PAE – BAE
        BAE = Baseline Actual Emissions
        PAE = Projected Actual Emissions
Notes: 189
Much more common than new source is mods at existing major sources. On the surface sound fairly straightforward, but determining BAE and PAE is quite complex at existing major sources such as EGUs.
Next slide will discuss

## Slide 190: Major Modification PSD (Cont’d)
  Significant Emissions Increase – Existing Units
    Calculating Baseline Actual Emissions (BAE)
      Highest of two years in past five
      With approval non electric utility may use 10 years
    Calculating Projected Actual Emissions (PAE)
      Consider all relevant information, including but not limited to, historical operational data, the company's own representations, the company's expected business activity and the company's highest projections of business activity, the company's filings with the State or Federal regulatory authorities.
Notes: 190
As is the case with most things in PSD the baseline to projected actual test is not set in stone. The source can use most anything logical and defensible to go with. In general projected business activity is the best way to go.
Reg defn: Baseline actual emissions means the average rate, in tons per year, at which the emissions unit actually emitted the pollutant during any consecutive 24-month period selected by the owner or operator within the 10-year period immediately preceding either the date the owner or operator begins actual construction of the project, or the date a complete permit application is received by the Administrator for a permit required under this section or by the reviewing authority for a permit required by a plan, whichever is earlier,
For electric utilities only a 5 year window is allowed.
or a regulated NSR pollutant, when a project involves multiple emissions units, only one consecutive 24-month period must be used to determine the baseline actual emissions for all the emissions units being changed. A different consecutive 24-month period can be used For each regulated NSR pollutant.
Reg defn: projected actual emissions means the maximum annual rate, in tons per year, at which an existing emissions unit is projected to emit a regulated NSR pollutant in any one of the 5 years (12-month period) following the date the unit resumes regular operation after the project, or in any one of the 10 years following that date, if the project involves increasing the emissions unit's design capacity or its potential to emit that regulated NSR pollutant and full utilization of the unit would result in a significant emissions increase or a significant net emissions increase at the major stationary source.
For both fugitive emissions count if on list of 28

## Slide 191: Pre-construction Permits PSD
Major Modification (cont):
  Significant Emissions Increase (cont)
    Actual to Potential
      Emissions Increase = PTE – BAE
    Hybrid
      Calculate Actual to Projected Actual or Actual to Potential, depending on whether an emissions unit is new or existing
      Sum the increases only
191
Notes: The key to the hybrid is that number of different types of emission units
Sum increases only - has been superseded by 2020 project accounting rule
191

## Slide 192: Modification PSD
EXERCISE
Major Modification
Let’s do some calculations
192
Notes: 192

## Slide 193: PSD Source Categories with 100 tpy Major Source thresholds
1. Coal cleaning plants (with thermal dryers) | 15. Coke oven batteries
2. Kraft pulp mills | 16. Sulfur recovery plants
3. Portland cement plants | 17. Carbon black plants (furnace process)
4. Primary zinc smelters | 18. Primary lead smelters
5. Iron and steel mills | 19. Fuel conversion plants
6. Primary aluminum ore reduction plants | 20. Sintering plants
7. Primary copper smelters | 21. Secondary metal production plants
8. Municipal incinerators capable of charging more than 50 tons of refuse per day | 22. Chemical process plants (does not include ethanol production facilities that produce ethanol by natural fermentation)
9. Hydrofluoric acid plants | 23. Petroleum storage and transfer units with a total storage capacity exceeding 300,000 barrels
10. Sulfuric acid plants | 24. Taconite ore processing plants
11. Nitric acid plants | 25. Glass fiber processing plants
12. Petroleum refineries | 26. Charcoal production plants
13. Lime plants | 27. Fossil fuel-fired steam electric plants of more than 250 million British thermal units (BTU) per hour heat input
14. Phosphate rock processing plants | 28. Fossil-fuel boilers (or combination thereof) totaling more than 250 million BTU/ hour heat input
Notes: 193
For these sources the threshold for PSD is 100 tpy. As we talked earlier The list seems somewhat random and in fact it may be. The only rationale for the list was that there was data on large sources available in 1973.
Fugitive emission count for this list of sources.

## Slide 194: Significant Emission Rates (tpy) PSD
Carbon monoxide 100
Nitrogen oxides 40
Sulfur dioxide 40
Particulate matter (PM/PM10/PM2.5) 25/15 /10
Ozone (VOC) 40 (of VOCs or NOx)
Lead .6
xFluorides 3
xSulfuric acid mist 7
xHydrogen sulfide (H2S) 10
xTotal Reduced sulfur compounds (including H2S) 10
Notes: These are the significant emission rates, These may constitute a major modification that trigger PSD for a pollutant if the source is already a major source.

## Slide 195: EXERCISE
Scenario 1:
  New Chemical Process Plant
  Non-fugitive NOx emissions – 75 T/yr PTE
  Non-fugitive VOC emissions – 30 T/yr PTE
  Fugitive VOC emissions – 75 T/yr PTE
PSD review required?
Scenario 2:
  New Source which is not a listed source
  Non-fugitive NOx emissions – 75 T/yr PTE
  Non-fugitive VOC emissions – 210 T/yr PTE
  Fugitive VOC emissions – 75 T/yr PTE
PSD review required?
195
Notes: Start with new
Scenario 1 Chemical plants are a listed category therefore, the plant would be a PSD major source for VOC. Remind the class fugitives count toward the major source determination because it is a listed source. It would also be subject to PSD for NOx because of it’s significant emissions increase (greater than 40 tpy).
Note if new source then PSD applies, if existing major source would need to determine if the new EU is a significant net emissions increase.
Scenario 2 Even though the emissions for this source a more than double the first source Under scenario 2 no PSD review is needed. Fugitive emissions do not count for non-listed sources therefore, it is not a major source for any pollutant. Because it is not a major source PSD does not apply. Minor NSR permitting would apply, e.g., in NY > that 50%
210 +210 tpy would even not be PSD but now a major source as over 250 tpy so next mod would use SER (e.g., 40 tpy as threshold.

## Slide 196: EXERCISE
Scenario 3:
  Adding a new < 250 MMBtu/hr boiler at a hospital
  Hospital existing maximum PTE: 240 T/yr NOx
  (assume any existing boilers total < 250 MMbtu/hr)
  New boiler PTE: 200 T/yr NOx
PSD review required?
Scenario 4:
  Same scenario except the existing boiler > 250 MMBtu/hr
Scenario 5:
  Same as 3, except new boiler PTE is 270 T/yr
Scenario 6:
  Same scenario as 3, except the source is a refinery rather than a hospital
Notes: These scenarios are different from our first one in that these are new units added at an existing source. Assume increases are “net significant emission increases” which will talk about more soon. Adding new unit a lot more straightforward than mods at existing units.
Scenario 3 Because this is not a listed source so the 250 tpy thresholds applies therefore, the hospital is an existing non-major source. The new boiler does not constitute a major mod to a major source (the boiler itself is not a listed category and is less than 250 tpy). Final PTE = 440tpy so hospital is now a major source for NOx so next mod will use SER of 40tpy
Scenario 4 the existing boiler has made our list of 28 (boilers > 250 MMBtu/hr) and therefore PSD is triggered since the new boiler has a significant emission rate (> 40 tpy).
Scenario 5 the boiler is itself a major source (> 250 tpy) and is subject to PSD as the mod would add 270tpy (>250tpy)
Scenario 6 is a PSD case since a refinery is a listed source and existing PTE is above 100 tpy and the boiler has a significant emission increase (> 40 tpy)

## Slide 197: Example
Lets look at a couple of baseline examples
Notes: Modified existing unit
In order to calculate significant emission increase and then a net significant emission increase, the sources needs to go through an analysis of annual actual emissions to determine their BAE.

## Slide 198
Baseline Actual Emissions |  |  |  |  |  | 
EUSGU (for each existing emissions unit) |  |  |  |  |  | 
Actual TPY |  |  |  |  |  | 
900 | 2002 |  |  |  |  | 
870 | 2003 |  |  |  |  | 
970 | 2004 |  |  |  |  | 
850 | 2005 |  |  |  |  | 
900 | 2006 |  | Date actual construction begins |  |  | 
870 + 970 = 1840/2 = 920 |  |  |  |  |  | 
Notes: Since it is a electric utility only 5 years count. You pick the highest emissions for 24 consecutive months
198

## Slide 199
Baseline Actual Emissions |  |  |  |  |  | 
Non- EUSGU (for each existing emissions unit) |  |  |  |  |  | 
Actual TPY |  |  |  |  |  | 
840 | 1997 |  |  |  |  | 
910 | 1998 |  |  |  |  | 
870 | 1999 |  |  |  |  | 
970 | 2000 |  |  |  |  | 
850 | 2001 |  |  |  |  | 
830 | 2002 |  |  |  |  | 
170 | 2003 |  | 0.85 emission reduction limit commences |  |  | 
130 | 2004 |  |  |  |  | 
120 | 2005 |  |  |  |  | 
150 | 2006 |  | Date actual construction begins |  |  | 
870 + 970 = 1840/2 = 920 * (1 - 0.85) = 138 |  |  |  |  |  | 
170 + 130 = 300/2 = 150 |  |  |  |  |  | 
Notes: For a non utility you use 10 years – highest is 2003 and 2004
This slide also has the complication of control. You have the ten years but must include the control. You must adjust for required controls so 1999 and 2000 adjusted is less than 2003 and 2004
You cant get credit for what you have to do!
199

## Slide 200
Baseline Average Emissions Same Pollutant |  |  |  |  | 
EU1-NOx |  |  |  | EU2-NOx | 
840 | 1997 |  |  | 100 | 1997
910 | 1998 |  |  | 120 | 1998
870 | 1999 |  |  | 110 | 1999
970 | 2000 |  |  | 140 | 2000
850 | 2001 |  |  | 100 | 2001
900 | 2002 |  |  | 150 | 2002
960 | 2003 |  |  | 120 | 2003
910 | 2004 |  |  | 90 | 2004
970 | 2005 |  |  | 110 | 2005
930 | 2006 |  |  | 100 | 2006
What is the NOx BAE for the project? |  |  |  |  | 
200
Notes: Since we have multiple emission units must use same two years. Looks like (2002 and 2003) 930 and 135 or 1065.
‘02 – ’03: 960+900/2= 930, 150+120/2 = 135
Disregard the white color
Same baseline period for all units in project CFR 40 51.21 (a)(28)(c)
SEE next slide
200

## Slide 201
Baseline Average Emissions Same Pollutant |  |  |  |  | 
EU1-NOx |  |  |  | EU2-NOx | 2year average
840 | 1997 |  |  | 100 | 
910 | 1998 |  |  | 120 | 985
870 | 1999 |  |  | 110 | 1005
970 | 2000 |  |  | 140 | 1045
850 | 2001 |  |  | 100 | 1030
900 | 2002 |  |  | 150 | 1000
960 | 2003 |  |  | 120 | 1065
910 | 2004 |  |  | 90 | 1040
970 | 2005 |  |  | 110 | 1040
930 | 2006 |  |  | 100 | 1055
Looks like 2002 and 2003 |  |  |  |  | 
Notes: Since we have multiple emission units must use same two years. Looks like (2002 and 2003) 930 and 135 or 1065.
Same baseline period for all units in project CFR 40 51.21 (a)(28)(c)
Can't cherry pick higher 2 year period for unit one in ‘05/’06
201

## Slide 202
Baseline Average Emissions Different Pollutants |  |  |  |  | 
EU1-NOx |  |  |  | EU1-VOC | 
840 | 1997 |  |  | 100 | 1997
910 | 1998 |  |  | 120 | 1998
870 | 1999 |  |  | 110 | 1999
970 | 2000 |  |  | 140 | 2000
850 | 2001 |  |  | 100 | 2001
900 | 2002 |  |  | 150 | 2002
960 | 2003 |  |  | 120 | 2003
910 | 2004 |  |  | 90 | 2004
970 | 2005 |  |  | 110 | 2005
930 | 2006 |  |  | 100 | 2006
What are the NOx & VOC BAE for the project? |  |  |  |  | 
Notes: Only one unit so we get whatever years work best for each pollutant 950 for NOx (2005-2006) and 135 for VOC (2002-2003)
Different baseline period for each pollutant CFR 40 51.21 (a)(28)(c)
950 and 135
202

## Slide 203
Projected Actual Emissions |  |  |  |  |  |  | 
(for each emissions unit) |  |  |  |  |  |  | 
Actual TPY |  |  |  |  |  |  | 
960 | 2009 |  | Unit resumes normal operation |  |  |  | 
960 | 2010 |  |  |  |  |  | 
960 | 2011 |  |  |  |  |  | 
1020 | 2012 |  |  |  |  |  | 
950 | 2013 |  | Year 5 (no increase in design cap. or PTE) |  |  |  | 
1020 | 2014 |  |  |  |  |  | 
1300 | 2015 |  |  |  |  |  | 
1300 | 2016 |  |  |  |  |  | 
1300 | 2017 |  |  |  |  |  | 
1100 | 2018 |  | Year 10 (inc. design cap. or PTE) |  |  |  | 
Notes: Here the projected actuals are set in 2 ways. If the project does not involve a physical change in unit or an increase in PTE you use 5 years, if it does use 10 years.
Unlike BAE there is not averaging years (or months) for PAE – just pick one year (consecutive 12 months) out into the future 5 years or 10 years.
203

## Slide 204: Major Modification PSD (Cont’d)
Significant Emissions Increase
    If the emissions increase for the project is below the significance rate for each pollutant, PSD does not apply
    If the emissions increase for the project exceeds the significance rate for a pollutant, the next step is to determine whether there is a significant net emissions increase
Notes: Okay, back to major mods at an existing major source: Once we go through this exercise we compare the emissions increase for the project with the list shown earlier. We have also to look at whether or not we have a net increase.
Remember 2 step process. So next we need to talk about PSD netting

## Slide 205: Major Modification PSD (Cont’d)
Significant Emissions Increase (cont)
    Provisions relating to recordkeeping and reporting requirements when electing to use “projected actual emissions” are found at 52.21(r)(6)
      Recordkeeping and reporting required if there is a “reasonable possibility” that significance level will be exceeded
Notes: Recordkeeping is set up in normal fashion and is designed to make sure that the source does not exceed significance level. The obligation is on the source to show that their modification hasn’t exceeded the SER for future years.
There is a lesson later on recordkeeping.
Remember slide 189? PAE – BAE = SER? For existing EUs

## Slide 206: Major Modification PSD (Cont’d)
Netting (Significant Net Emission Increase)
  Only applies to significant emissions increase
    Considers “contemporaneous” emission increases and decreases
    5 years prior to commencing construction through date the subject increase occurs
Notes: Now we have to look at net increases and consider contemporaneous increases and decreases. We use a five year period for this.
First have to have a sig emission increase for the project – step 1
206

## Slide 207
Contemporaneous Emissions Increases and Decreases
Application
Filed
Permit
Issued
Construction
Commenced
Operation
Begins
5 years
Contemporaneous Period
Notes: Diagram shows what the five year period. Source looks at facility wide increases and decreases for the period five years back from the date construction commenced.
Estimate permit issued construction commenced and operation begins

## Slide 208: Major Modification PSD (Cont’d)
Netting (Significant Net Emission Increase)
  Emission increases and decreases must be “otherwise creditable”
    Not relied upon previously in issuing a PSD permit (i.e., not used in air quality analysis)
    There are special provisions relating to NOx, PM or SOx reductions prior to minor source baseline
    Other restrictions to consider, including decreases must approximate the same qualitative significance for public health and welfare as the increase from the change
Notes:     Creditable Increases
      Previous change in, or change in the method of operation
      Actual emissions after the change minus actual emissions before the change
      Actual emissions before the change
        BAE calculation (w/o same 24 month period for same pollutant limitation)
      Actual emissions after the change
      Normally, previous 2 years
    Creditable Decrease
      Same pollutant
      Actual decreases occurring prior to the current modification beginning operation. Decreases have to be real and enforceable. Can’t count PTE.
      Enforceable prior to modification beginning construction

## Slide 209: Exercise Netting
For each of the following, determine whether there is
  A significant emissions increase, and
  A significant net emissions increase.
  (For each example, assume the emissions increases and reductions are all NOx)
Notes: 209

## Slide 210: Exercise Netting (Cont’d)
Example 1:
  7/1/06: Complete permit application submitted
  10/1/07: Permit issued (Estimated)
  10/30/07: Construction commenced (Estimated)
  12/1/08: New unit commences operation (Estimated)
  PTE related to new construction is 28 T/yr
  5/1/02: 50 T/yr decrease
  6/1/04: 10 T/yr increase
  8/1/06: 45 T/yr increase
  3/1/07: 65 T/yr decrease
  1/1/09: 25 T/yr increase
Example 2: Same as Example 1 except new construction PTE is 55 T/yr
Example 3: Same as Example 2 except pre 8/1/06 were used to net out 8/1/06 increase
Notes: Step 1 - If the increase is only 28 tons then not significant for NOx (<40tpy NOx) so netting not required and PSD does not apply [just minor source permitting if applicable]
So lets continue assuming PM10
In example 1 the 5/1/02 decrease lies outside the five year period and the 1/1/09 25 tpy increase occurs after the unit begins operation and both do not does not count. Net increase is 10 + 45 – 65[-10tpy] + 28 = 18 tpy and so a significant net increase has occurred (18 > 15tpy).
In example 2 the 55 tpy is a significant emission increase of Nox (55>40tpy) and the net increase is 45 tpy (55 – 10tpy) and a significant net increase happened.
Example 3 - If you drop the 8/1/06 and earlier because they have already been used. The 55 tpy is a significant emission NOx increase, but the 65 tpy decrease offsets the increase and a significant net increase has not occurred.
210

## Slide 211
Exercise Discussion
Application
Filed
Permit
Issued
Construction
Commenced
Operation
Begins
5 years
Contemporaneous Period
7/1/06
10/1/07
10/30/07
12/1/08
10/30/02
50 T
10 T
45 T
65 T
25 T
5/1/02
6/1/04
8/1/06
3/1/07
1/1/09
55 T
Notes: This diagram illustrates what we have been talking about. It shows that the 5/1/02 decrease falls outside and the 1/1/09 25 tpy increase occurs after operation begins

## Slide 212: Netting PSD
We will have an in depth discussion and exercise addressing netting later in the course
Notes: Lesson 8
212

## Slide 213: PSD
Quick Review – Applicability
  New Major Source
    100/250 TPY
    Source categories
  Modification to a non-major source, if modification by itself would be major
  Modification to a major source if results in:
    A significant emissions increase,
        Project vs. Emissions unit
        Aggregation
        New EU vs. Existing EU
      AND
    A significant net emissions increase
        Contemporaneous period
        Creditable emissions
Notes: All we have talked about is how to determine if PSD permitting applies. Now we have to consider what you have to do.
213

## Slide 214: Best Available Control Technology (BACT) PSD
Emission limitation required of a source subject to PSD
New major stationary source
    BACT for each regulated NSR pollutant with PTE > significant levels
Major modification
    BACT for each regulated NSR pollutant emitted resulting in a significant net emissions increase
    This requirement applies to each emission unit at which a net emissions increase would occur as a result of a physical change or change in method of operation of the unit
Notes: All PSD sources must apply BACT and determine a BACT limit (with your help) that will go into the PSD permit. BACT is equivalent to NSPS but for a particular source not for the source category. We will spend a goodly amount of time on BACT in Lesson 11
214

## Slide 215: BACT PSD (Cont’d)
  Top Down evaluation (EPA guidance) or equivalent (see Puzzle Book)
  Determine all emission reduction technologies in use by similar processes (world wide) (BACT/LAER Clearinghouse)
  Defined at 52.21(b)(12)
    consideration given to the energy, environmental, and economic impacts and other costs
    See “Guidance for Determining BACT Under PSD”
Notes: Top down is a 5 step process that
STEP 1--Identify All Control Technologies . . . . . .STEP 2--Eliminate Technically Infeasible Options. . . STEP 3--Rank Remaining Control Technologies by Control Effectiveness. . . . STEP 4--Evaluate Most Effective Controls and Document
Results . . . STEP 5--Select BACT . .
Cost effective varies from state to state and by pollutants. For some states it may be as low as $4000 per ton and in other states it may be as high as $15,000 per ton removed.
Guidance is from 1979 so there are better guidance available: https://www.epa.gov/sites/default/files/2015-07/documents/bactupsd.pdf
Show NSR workbook manual aka puzzle book cover jpg - Chapter B is about BACT

## Slide 216: BACT PSD (Cont’d)
Cannot be less stringent than NSPS or NESHAP
BACT is not set until final permit issued
BACT at Phased Construction Projects requires special considerations 52.21(j)(4)
We will have an in depth exercise addressing BACT later in the course
Notes: i.e., BACT must be the same or more stringent than NSPS limits.
The remainder of BACT will discussed a bit later as a separate lesson [11]
216

## Slide 217: Ambient Impact Analysis PSD
Owner/Operator required to demonstrate allowable increases will not cause or contribute to:
    An increment exceedance
    A NAAQS violation
Modeling exercises
Notes: After BACT, sources must demonstrate that they will not allow an increment to be exceeded or a standard to be violated. This is done through specific modeling exercises for most NSR pollutants. Modeling will be discussed later lesson 13.
So what is increment?

## Slide 218: Increment PSD
Increment is the extent by which the ambient concentration of a pollutant is allowed to exceed a specified baseline
Limits increases in ambient concentrations of PM 2.5, PM10, SOx and NOx from new or modified emission sources
Increment consumption includes emissions from major, minor, area and secondary sources.
3 area classifications [52.21(e) & (g)]
    Class I – primarily nat’l parks, preserves, etc. and international parks
    Class II – most other areas
    Class III – must be specifically designated
Notes: One way to look at the increment is that it is the maximum amount of degradation (or deterioration) that is allowed in an area.
Increment consumption is more than just this one source. It includes all the other sources in the area including minor sources and secondary emissions associated with the source being reviewed. Secondary emissions means emissions which would occur as a result of the construction or operation of a major stationary source or major modification, but do not come from the major stationary source or major modification itself. Secondary emissions include emissions from any offsite support facility which would not be constructed or increase its emissions except as a result of the construction or operation of the major stationary source or major modification.
Show increments in CFR 52.21(c) [also specified in the CAA at 163 for SO2 and PM]
Closest to NY Class I in VT – Lye Brook Wilderness area
Not all park and wilderness areas are Class 1
218

## Slide 219: Increment Terms PSD
  Baseline area [52.21(b)(15)] [40CFR Part 81]
Area for which the minor source baseline date is established
  Baseline concentration [52.21(b)(13)]
    Concentration against which the increment change is evaluated
  Minor Source Baseline Date [52.21(b)(14)(ii)]
    Defines the date for calculating the baseline concentration
    Date after which all increases and decreases affect increment
    Date of which first PSD application is submitted
  Major Source Baseline Date [52.21(b)(14)(i)]
    Date after which Major Source increases and decreases affect increment
Notes: Several terms that are important for the increment.
Baseline area means any intrastate area (and every part thereof) designated as attainment or unclassifiable under section 107(d)(1)(A)(ii) or (iii) of the Act in which the major source or major modification establishing the minor source baseline date would construct or would have an air quality impact for the pollutant for which the baseline date is established, as follows: equal to or greater than 1 µg/m3 (annual average) for SO2, NO2, or PM10; or equal or greater than 0.3 µg/m3 (annual average) for PM2.5.
Minor Source Baseline date is the first PSD application for permit submitted.
Assume all triggered now?? – or maybe not per NC
219

## Slide 220: Increment Terms PSD (Cont’d)
Trigger Date – Date, set by regulation, before which, the Minor Source Baseline Date cannot be triggered
Baseline concentration and minor source baseline date established by area classifications
    In any case, emissions impact shall not cause or contribute to a NAAQS exceedance [52.21(d)]
Notes: Major Source baseline date then Trigger date then Minor Source baseline date.
Check with your planning group or POC on Increment
220

## Slide 221
Increment
Increment
NAAQS
Baseline Concentration
Baseline Concentration + Increment
Minor Source Baseline Date
Trigger
Date
Major Source
Baseline Date
Application
(PM10 - 24 hr)
Issued
Operated
PM
1/6/75
8/7/77
30 ug/m3
150 ug/m3
0
+
-
Emissions
Notes: Examples of various dates
PM10 24hr Increment is 30ug/m3 for a class 2 area, so baseline conc + 30 is limit for new source [plus what other sources have consumed]. Even though below the NAAQs of 150ug/m3.
221

## Slide 222: Pre-construction Permits PSD
Increment
  Increment Analysis is a modeling exercise
  Generally, if project emissions are below the Significant Impact Limits (SIL), increment evaluation not required
  If project emissions impact is above the SIL, evaluate all associated emissions, including secondary emission, for increment consumption
Notes: SILs are low levels where it is unlikely that the increment or any standard will be exceeded from the project only. If above the SIL then complete analysis needs to be done.
SILs are not the same as SERs, conc ug/m3 vs tpy
Defined in 51.165(b) or recent ‘18 and ‘24 EPA guidance for PM2.5 and O3
Range 1 to 5 ug/m3 24 hour to annual

## Slide 223: Secondary Emissions
Emissions which would occur as a result of the construction or operation of a major stationary source or major modification, but do not come from the major stationary source or major modification itself. Secondary emissions include emissions from any offsite support facility which would not be constructed or increase its emissions except as a result of the construction or operation of the major stationary source or major modification.
Notes: The definition of secondary emissions
Need to be included in AQ impact analysis and increment analysis [not included in the screening SIL modeling]

## Slide 224: EXERCISE
Scenario 1:
  SO2 24-hour standard (revoked in 2010) – 365 ug/m3 (140 ppb)
  SO2 24 hour increment – 91 ug/m3
  SO2 Baseline Concentration – 200 ug/m3
  SO2 increment consumed – 61 ug/m3
  Construction emissions impact – 10 ug/m3
Scenario 2:
  Same as 1 except
    SO2 increment consumed is 81 ug/m3
    construction emissions impact is 15 ug/m3?
Scenario 3:
  Same as 1 except Baseline concentration was 300 ug/m3
Notes: In scenario 1 the source is okay since the total impact is 61+10 or 71 and all is well [Note: assume project only is over the SO2 SIL of 5ug/m3 for 24hr, so an increment analysis is needed
Increment of 91ug/m3 means project is in a class II area [if the source was near a class I area the allowed SO2 24hr increment would only be 5ug/3]
In scenario 2 the consumption is 96 ug/m and all is not well.
In scenario 3 the available increment is only 65ug/m (not 91) and all is not well
NB: The current SO2 NAAQS (as of 2010) is a 1 hour standard – 196.5 ug/m3 (75 ppb), the 24-hour standard was revoked in 2010, however the SO2 increment remains in regulation based on a 24-hour averaging period.
224

## Slide 225: NAAQS analysis PSD
If project increase is below the SIL, no further review necessary
If project increase is above the SIL, then evaluate all emissions for NAAQS impact
Impact on Nonattainment Area
    If project increase is above the SIL, must reduce impacts of its emissions by obtaining emission reductions to compensate for its adverse impact.
Notes: There is no reg SIL for PM 2.5 since it was found arbitrary by a court.
Note: there are no reg SILs for ozone or for short term (1 hour) SO2 and Nox
PM2.5 and O3 addressed in EPA ’18/’24 guidance
It is also the case that short term NOx and SOx standards have much more impact on stationary sources then longer term standards.
Can also change the project to reduce the ambient impacts on a NA area

## Slide 226: Pre-construction Monitoring PSD
Minimum of 1 year preconstruction ambient monitoring data
May use approved state monitors
Pollutants to monitor
    New construction – pollutants PTE > significance amount
    Modifications – pollutants resulting in significant net emissions increase
    Non-criteria pollutants – as determined necessary
Post-construction Monitoring
    As determined necessary
Notes: Monitoring can be required if the baseline cannot be determined and the new source’s impact exceeds the SIL. Can require monitoring for any pollutant. Post construction can be required if necessary to evaluate impact. Generally not done
Significant Monitoring Concentration (SMCs) exception ??????
226

## Slide 227: Permit Conditions PSD
Obligation of source to provide information
  Mandatory
    information necessary to evaluate proposed source, construction schedule, emissions, controls and emissions impacts
  Upon request
    air quality impact evaluation of proposal, including met and topo data
    Air quality impacts, and nature and extent of commercial, residential, industrial and other growth since 8/7/77, in the area the source would affect
Notes: Sources have the requirement to provide data to access source impact
227

## Slide 228: Other analysis PSD
Additional Impact Analysis
  Impairment to visibility, soils & vegetation
    As a result of the source or modification
    Must include general commercial, residential, industrial and other associated growth
    No analysis required of impact on vegetation with no significant commercial or recreational value
  Air quality impact analysis as a result of general commercial, residential, industrial and other associated growth
  Visibility monitoring in any Federal Class I area near the source or modification may be required
Notes: In addition to direct air quality impact the permit application must address other impacts. The most important and potentially delaying is the impact on federal land
This additional impact analysis is required even if the proposed projects emission are modeled below the SILs, but the analysis can be a “screening” Below SIL just gets applicant out of more comprehensive NAAQs and increment modeling
228

## Slide 229: Sources impacting Federal Class I areas PSD
Federal Land Managers (FLMs) must be notified if emissions impact a Class I area
FLM may conduct or request a visibility analysis
Permit can be denied based upon FLM analysis, even if increment requirements satisfied
FLM role
    Can be a point of contention
Other special provisions relating to Class I areas
Regional Haze requirements
    Improve worst days
    No degradation on best days
Notes: If preliminary analysis shows over the SIL at the class I area
Lye Brook Wilderness area VT
New Jersey National Wilderness Areas Brigantine
New Hampshire National Wilderness Areas Great Gulf, Presidential Range-Dry
229

## Slide 230: PSD
Plantwide Applicability Limits (PALs) [52.21(aa)]
52.21(v) addresses procedures if a source proposes innovative control technologies
Notes: PAL is a multi unit emission limit where the source has the flexibility to transfer emissions among unit. – AKA facility wide cap or bubble permit
PAL permit is set at BAE plus the SER for that pollutant across the entire facility
230

## Slide 231: PSD
Permit issuance procedures
  Public notice with opportunity for public hearing
  Check state regulations for individual notice requirements
  Taking, and responding to, comments
    Source
    Public
    Sister state, local and tribal air agencies
    Other federal, tribal, state and local units of government
    EPA
    FLMs
Notes: How the permit is issued generally conforms to state procedures with the need to send it to EPA and maybe FLM
At least 30 day comment period
231

## Slide 232: PSD - Review
PSD Permits
  Attainment or Unclassifiable areas
Applicability
  Major source
  Modification at non-major source
  (if the modification itself exceed the major source level)
  Major modification at major source
    Significant emissions increase
    Netting
    Routine Maintenance
BACT
NAAQS & Increment analysis
Air Quality and Adverse Impact Analysis
Preconstruction Monitoring
FLM involvement
  Also, Regional Haze requirements
PALs
Notes: This is what we have talked about for the morning. Looking at this slide PSD looks very complex and it is. In fact one of the best features of PSD and the NSR we talked about yesterday is that they are so complicated that sources will go to great lengths to avoid coming under the regulations. This means that sources will control more and take other restrictions to avoid these regs. This is not a bad thing.
Deseret Waste Coal Fired Unit SOB overview – [will revisit SOB for the BACT and modeling sections in those lessons.]??
232

## Slide 233: QUESTIONS?

## Slide 234: LESSON 8
PSD Netting
Notes: Carl

## Slide 235: Major Modification
NSR Applicability to a Proposed Modification
To determine whether or not a proposed modification at an existing major stationary source is a Major Modification, we use a two-step test:
    Step one is to determine if there is a “significant emission increase” of a regulated NSR pollutant from the proposed modification “project”
    Step two is to determine whether or not the “project” results in a “significant net emissions increase” of that pollutant
Notes: To determine whether or not a physical change or change in the method of operation for a proposed modification at an existing major stationary source is a Major Modification subject to NSR Pre-Construction permitting review one has to use a two step test.

## Slide 236: PSD & NNSR Project Emissions Accounting
EPA Revises the NSR Applicability for Modifications
On 10/22/2020 EPA finalized a rule to clarify the process for evaluating whether NSR applies to a proposed modification at a major stationary source.
The final rule clarifies that both emission increases and decreases from a major modification are to be considered during “Step One” of the two-step NSR applicability test.
This process is called “Project Emissions Accounting” and applies to projects that include a combination of new and existing units
Notes: In March 2018, EPA Administrator issued a memo titled “Project Emissions Accounting Under the NSR Preconstruction Permitting Program.”
On August 1, 2019, EPA proposed for a 60 days comment period after publication in Federal Register to clarify the process for evaluating whether the NSR permitting program would apply to a proposed modified source of air emissions. This proposal would make it clear that both emission increases and decreases from a major modification are to be considered during Step 1 of the two-step NSR applicability test. This process is known as “Project Emissions Accounting” or previously as “Project Netting.”
On October 22, 2020, the EPA finalized a rule to clarify the process for evaluating whether the NSR (both PSD and Non-attainment NSR) permitting program would apply to a proposed modification of a source of air emissions. This final rule clarifies that both emission increases and decreases from a major modification are to be considered during Step 1 of the two-step NSR applicability test. This process is known as “Project Emissions Accounting.”
The final rule revises the NSR applicability regulations that apply to projects that include a combination of new and existing units and makes it clear that project emissions accounting is allowed as part of Step 1 of the two-step NSR major applicability test.
Added paragraph (G): The “sum of the difference” as used in paragraphs (c), (d) and (f) of this section shall include both increases and decreases in emissions calculated in accordance with those paragraphs.
ATPA can be used for step 1, Actual to PTE used for step 2 for non project EU – see R5 memo from 2011.

## Slide 237: Project Emissions Accounting (Cont’d)
EPA Revises the NSR Applicability for Modifications
This final rule applies to EPA and permitting authorities that have been delegated federal authority from EPA to issue NSR permits on behalf of EPA
State and Local Agencies that implement NSR program through an EPA-approved SIP, are not required to modify their program to account for this final rule and may continue to implement their current program without change.
Notes: This final rule applies to EPA and permitting authorities that have been delegated federal authority from EPA to issue NSR (both PSD and NNSR) permits on behalf of EPA.
State and Local Air Agencies that implement the NSR program through EPA-approved State Implementation Plan (SIP), are NOT required to modify their programs to account for this final rule and may continue to implement their current program without change.
EPA has concluded that permitting authorities that do not allow for project emission accounting have at least as stringent applicability requirements as those required by the Act or EPA’s implementing regulations and, therefore, are not required to submit SIP revisions or stringency determinations to EPA as a result of this action.
Proposed Rule: Revisions to Regulations Related to Project Emissions Accounting - February 22, 2024. Apply “guard rails”

## Slide 238: Netting
Netting is a process of looking back over a specified period and summing all the applicable increases and decreases in emissions of a pollutant and comparing that to the major modification threshold
Netting concept applies only to existing major sources
Minor sources not eligible to “net” emissions changes

## Slide 239: Determination of Significant Emissions Increase - Netting
Determine if a "net emissions increase" will result
Considers previous and prospective emissions changes
If so, PSD applies to each pollutant's emissions for which the net increase is "significant
Notes: We go through this exercise to demonstrate how you can use the ‘02 “reforms” to get out of things.

## Slide 240: Netting
  Required only if proposed project - by itself, or with “related projects” – has significant emissions, or a significant emissions increase
Process also used in NA- NSR
  Affects amount of offsets required
Notes: i.e., the project’s emissions would exceed the SER for that pollutant
Netting is also used in NA NSR

## Slide 241: Netting (Cont’d)
Net Emissions Change
EQUALS
Emissions increases associated with the proposed modification
MINUS
Source-wide creditable contemporaneous emissions decreases
PLUS
Source-wide creditable contemporaneous emissions increases
Notes: Here is what netting is. Netting is nothing more then all of the increases associated with the mod minus the decreases plus other increases. Note there is a time component in the whole process.

## Slide 242: Creditable Contemporaneous Emissions
Emission increases and decreases are creditable if:
  They have occurred within 5 years of modification
  Have not been relied upon for permits
Notes: The time period affects the creditable increases and decreases.
< 5 years from construction commenced + time to start operation
Refer to slides in PSD lesson #205

## Slide 243: Netting (Cont’d)
Netting analysis uses projected new emissions rather than potential
Projected actual emissions means the maximum annual rate, in tons per year, at which an existing emissions unit is projected to emit a regulated NSR pollutant in any one of the 5 years (12-month period) following the date the unit resumes regular operation after the project, or in any one of the 10 years following that date, if the project involves increasing the emissions unit's design capacity or its potential to emit that regulated NSR pollutant and full utilization of the unit would result in a significant emissions increase or a significant net emissions increase at the major stationary source.
Notes: As we have discussed we use projected actual emissions for existing units [new units use PTE]
PAE defn from PSD regs

## Slide 244: PSD NETTING EXERCISES (Optional)
Use handouts
Perform the netting calculations for each of the three exercises
A class discussion will follow
Notes: Let’s look at the three netting exercises in your handout. All of these came from the puzzle book. We would like you to divide into 6 groups and discuss among yourselves and then we will go through it all together.

## Slide 245: PRACTICAL EXERCISES – NETTING
EXERCISE 1
An existing minor source (subject to the 100 ton per year threshold for the list of 28) proposes a modification. The modification involves the shutdown and removal of an old emissions unit (providing an actual contemporaneous reduction in NOx emissions of 75 tpy) and the construction of two new units with a total projected actual NOx emissions of 110 tpy.
Does PSD apply to the new units?
Why or Why not?
Notes: Lets go through some simple math Please read and feel free to ask questions. The example came from the “puzzle book” EPA’s draft manual on PSD.
Okay somewhat of a trick question since netting does not apply since the source is not major and PSD does apply
BTW, if source was major then could net out of PSD [-75 tpy +110 tpy = 35 < 40 tpy]
Also, shouldn’t new unit use PTE ((not projected actual) unless it is a replacement unit

## Slide 246: PRACTICAL EXERCISES – NETTING
EXERCISE 2
An existing major source is located in an area which is attainment for all criteria pollutants. The source had less-than-significant increases of NOx (30 tpy) and SO2 (15 tpy) two years ago, and a 50 tpy decrease of SO2 three years ago. The source now proposes to add a new process unit with an associated projected increase in emissions of NOx (35 tpy) and SO2 (80 tpy). The 80 tpy increase in SO2 is significant before netting. The 35 tpy increase in NOx is not significant.
Would either the NOx or SO2 emission increase trigger PSD after netting?
Why or why not?
Notes: Recall we have a two step process. For NOx we stop since the increase in NOx is not significant. For SO2 when netting is examined increases and decreases are counted:
+15 t/y – 50 t/y + 80 t/y = +45 t/y PSD applies.

## Slide 247: PRACTICAL EXERCISES – NETTING
EXERCISE 3
A plant which manufactures automobile and truck tires – an existing major source – proposes to increase its production of both types of tires. For its automobile tire line, the source applies for – and is granted – a minor modification permit for a new extruder that will increase projected VOC emissions by 39 tons per year. A few months later, the source applies for another minor modification permit to construct a new tread end cementer on the same line. This will increase projected actual VOC emissions by 12 tons per year.
Should the extruder modification have been subject to PSD?
Why or why not?
Should the tread-end cementer modification cause the plant to be subject to PSD?
Why or why not?
Notes: Somewhat hard to read but here we have a case that looks like someone is in trouble. The extruder
39+12=51
The EPA would likely consider these proposals as
an attempt to circumvent the regulations because the two proposals are
related in terms of an
overall project to increase source-wide production capacity. The
important point in this example is that the two proposals are sufficiently
related that the PSD regulations would consider them a single project.

## Slide 248: QUESTIONS?

## Slide 249: LESSON 9
Emission Limitations
Notes: Ted

## Slide 250: Lesson Objectives
Understand types and pros/cons of emission limitations
Understand basics of converting technical/legal emission limit language of regulations into understandable language in permit

## Slide 251: Emission Limits
Performance-based
  Most common
  Requires meeting an emission standard
Technology-based
  Requires using a specified technology
Other
  Work Practices
Notes: Heart of permit
Three broad groupings
  Performance-based limits
  Technology-based limits
  Other limits
    Applicability thresholds
    Surrogate
Listed in regulations
Established through NSR permits
  BACT determinations
  LAER determinations
Netting/offsets/emission trades

## Slide 252: Performance-based Limits
Numerical limit is directly stated
Averaging times specified
Flexibility in how to meet limit
May be based on statute or rule
Notes: Emission rate
  Mass per unit of time
  Mass per throughput unit
Averaging time
  Hour, 24 hour, 30 days, etc.
  Shorter is more restrictive
Flexibility
  If one emission unit difficult to control, permittee can over control another emission unit (facility-wide bubble)
Authorized by statute or rule
  NAAQS
  SIP emission limits
  PSD impact analyses
  SO2 and NOx caps for emissions from utilities
More in Lesson 8

## Slide 253: Establishing a Performance-based limit
Can be established using dispersion modeling level set safely below an emissions rate at which adverse impact will occur
May reflect Best Available Control Technology (BACT) or Lowest Achievable Emission Rate (LAER) determinations

## Slide 254: Performance-based Limits Issues
Pro
  Flexibility
  Expectations clear
  Encourages advanced technology
Con
  Compliance may be difficult or expensive to determine
  Selection of averaging times is crucial

## Slide 255: Technology-based Limits
Require specified technology
  Actual control device specified
  Fuel throughput/composition
  Raw materials throughput/composition
  Must at a minimum reflect applicable
    BACT/LAER determinations
    NSPS/NESHAP
    MACT

## Slide 256: Technology-based Limits Issues
Pro
  Compliance may be easy to determine
  Precedents exist
  Expectations clear
Con
  Minimizes flexibility
  May inhibit technical innovation
Notes: Compliance determination
  Is it in place?

## Slide 257: Emission Limits – Other
Neither technology nor performance-based
Parametric/surrogate measures
Design parameters that limit uncontrolled emissions
Caps on production or operating hours
Applicability limits
Notes: These emission limits are indirect
  Parametric
  Temperature
  Pressure-drop
Design parameters
  Heat-input
  Minimum control efficiencies
  Minimum reagent feed-rates
Applicability thresholds
  Major source definition
  Prohibitory rules

## Slide 258: Should emission limits be included in permit?
Required for “Title V Operating Permits”
Other permits?
Notes: Yes, and NSR

## Slide 259: How should emission limits be included in permit?
Copy verbatim?
By reference?*
Redundant requirements?
Paraphrase?*
  *Use with caution!
Notes: Redundant okay just cant be inconsistent or conflicting.

## Slide 260: Documentation
The basis for the emission limitation must be specified
Determine applicable requirements
Explain determination in support document
Notes: Need to establish basis for limitation. It may seem obvious now, but questions/issues may arise later after staff turnover, etc.
  If basis not specified in the permit, then in the support document
Documentation helps inspectors understand why limitations are imposed – may help with inspections.

## Slide 261: Emission limitations vs. Permit conditions
Line may be blurry
Some permit conditions are surrogate for emission limitations
Emission limitations a subset of permit conditions

## Slide 262: Discussion Question
Why is it important to specify the effective date of any regulations on which emission limits in a permit are based?

## Slide 263: QUESTIONS?

## Slide 264
LESSON 10
Averaging Time
Notes: Carl

## Slide 265: Lesson Objectives
Understand the reason for averaging times
Review the connection between emission limits and averaging times
Examine the effects of shorter vs. longer averaging times
Notes: E.g., Nox lbs/MMBTU [emission limit] 30 day rolling [avg time]
Averaging time can have a significant impact on the severity of the permit. The appropriate averaging time is vital to protect the NAAQS and for permit enforcement.

## Slide 266: Averaging Time - Purpose
Establishes compliance parameter for emission limit
Allows emission limitation to match effect needed to be protected against
Notes: Emission limits meaningless without averaging time
  Particularly performance-based
  May be applicable to technology-based
    Solvent content of coating
Short averaging time for 24-hour standard PM2.5, PM10, O3, Nox, SO2
Longer for annual std., i.e. PM2.5
Monthly or annual averaging time would not be protective of an 8 hour or 24 hour ambient standard, such as ozone/PM2.5

## Slide 267: Averaging Times (Cont’d)
Instantaneous
Short-term (24 hours or less)
Long-term (more than 24 hours, i.e. monthly, annually, or May 1 through September 30)
Notes: Seasonal averages may be appropriate for some source types
  Agricultural operations
  Concrete manufacturing
If not specified, danger for agency to assume it is instantaneous
  lb/MM Btu implies instantaneous
  lb/hr is not necessarily an hourly limit but could be
    An instantaneous rate
    An hourly total
    An average over some period of time (3 hours, 24 hours, week, month, year)

## Slide 268: Averaging Times (Cont’d)
Must be specified for performance-based limits
May appear:
  In or near same condition as the limit
  In general section of permit on monitoring or testing
  In test method
Notes: Performance based = lbs/MMBtu or lbs/ton clinker
May be confusing if not spelled out clearly
Terminology must be unambiguous

## Slide 269: Averaging Time – Stringency
Affects stringency of limit
For a given level of emissions, a longer averaging time is less stringent than a shorter averaging time
Too long an averaging time would not protect against adverse effects of short term exposure
Notes: Example - Automobile Lease Agreement
  Long term
    24000 miles per year
    2000 miles per month
  Short term
    66.7 miles per day
The daily limit is more restrictive, even though they are the same - mathematically

## Slide 270: Short Averaging Times
If not explicitly stated, source will argue for longest reasonable time
If explicitly stated, but very short term, source may resist
Agency needs to impose averaging times commensurate with effect
Notes: Obviously sources like the longest averaging time. Can’t do very short unless you have source buy in. Watch for hidden strictness in apparently long term averaging time. One thing that happens is something like 5 tons per month or 60 tons per year. These are not the same and the 60 tons is not relevant.

## Slide 271: Averaging Times Technology-based Emission Limits
Irrelevant for some limits
  Work practices
  Solvent content, etc.
Others do need averaging time
  Specific control equipment
Notes: Averaging times, if needed must be determined by permit writer
Ease of inspection should be considered
Borrow from comparable guidance, regulations, or other comparable permits
Work practice permit conditions:
Operational limits: Restricting the hours of operation or the amount of raw materials processed.
Maintenance requirements: Specifying procedures and frequencies for equipment inspection and maintenance to minimize leaks and inefficiencies.
Fuel restrictions: Mandating the use of a specific type or grade of fuel to reduce emissions.
Equipment specifications: Requiring certain equipment, such as low-leak valves, to be installed and used.
Storage and handling procedures: Mandating specific techniques for storing and handling materials to minimize fugitive emissions.
Record-keeping requirements: Documenting and tracking specific operational practices to demonstrate compliance

## Slide 272: Sample Permit Condition Rolling 12-month Average
To comply with this Permit and to avoid applicability of 15A NCAC 2D .0530, "Prevention of Significant Deterioration”, as requested by the permittee, volatile organic compound (VOC) emissions from the modified nylon 6,6 manufacturing process (ID No. SRC-BCI) must be less than 40 tons in any consecutive twelve (12) month period. [15A NCAC 2D .0530]
Notes: The language could also address a calendar year, or could be 20 tons per six month period
Remember – there is not a single “right way” to do most things
12 month rolling is generally the best avg time to ensure emissions stay below an annual limit for syn minor – 100/250 tpy

## Slide 273: Class Discussion
Results for three 2-hour tests conducted over 3 consecutive days are 3.1, 2.6, and 4.9 lbs/hour. The average is 3.5 lbs/hour. Assuming the results are representative, what limits do the data support?
(3.1 + 2.6 +4.9) / 3 = 3.5
Notes: Next slide: Assuming that production levels and everything else is the same it seems that 4.9 is the number for a 2 hour or 3.5 + for a three day [or just 3.5 lbs per hr???, but source could exceed that 50% of time if operating at the same level as during the tests]

## Slide 274: Response to Class Discussion
Assuming the results are representative, the data support:
  A limit near 3.5 lbs/hour with a 72 hour averaging time
  A limit somewhere around 5 lbs/hour with a 2-hour averaging time or 6-hour averaging time
The data does not support an averaging time of less than 2 hours
Notes: Hidden slide
One hour avg would leave no margin of compliance – source emitted above the avg of 3.5 lbs/hr 50% of the time.

## Slide 275: Class Exercise
An applicant requests that an emissions unit be limited to 6,000 hours per year of operation to keep emissions below the major source threshold of 100 tons per year. Operation for 6,000 hours at the estimated emissions rate and maximum capacity would result in emissions of 99 tons per year.
Can this be done? If so, how? If so, what conditions should be imposed?
Notes: Next slide

## Slide 276: Class Exercise (Cont’d)
Yes, it can be done
However must ensure accuracy of ±1%
May be less costly for source to reduce it’s request to 95 tpy
Agree on an emission factor
Permit condition limiting hours
Select appropriate averaging time
Notes: May want to consider a rolling 12 month average
Desired permit conditions
  Records of operating hours essential
  Consider elapsed-time meter on key equipment
  Testing to verify continued correctness of emission factor
  Subject to revision if process/raw material changes

## Slide 277: Class Exercise (Cont’d)
An agreed upon factor (such as 0.1 lb emissions per unit produced) is consistent and can represent average emissions. It provides the most certainty to the source, which only has to stay below 6,000 hours per year to comply with that limit
Notes: This scenario assumes steady state operating conditions
If production changes temporally, or if raw materials, or other parameters are altered, more testing may be required
Emission factors would be changed as indicated
This approach avoids a “sudden jeopardy” situation for a source.

## Slide 278: Class Discussion
What are the three classifications used to describe averaging times?

## Slide 279: Averaging Times
Instantaneous
Short-term (24 hours or less)
Long-term (more than 24 hours, i.e. monthly, annually, or May 1 through September 30)
Notes: Seasonal averages may be appropriate for some source types
  Agricultural operations
  Concrete manufacturing
If not specified, danger for agency to assume it is instantaneous
  lb/MM Btu implies instantaneous
  lb/hr is not necessarily an hourly limit but could be
    An instantaneous rate
    An hourly total
    An average over some period of time (3 hours, 24 hours, week, month, year)

## Slide 280: Group Exercise Averaging Time (1 of 2)
5 new 4,000 HP EGU peaking engines at an existing major source in an attainment area:
    NSPS PM limit – 0.40 g/HP-hr
    PTE of each engine is 15 T/yr PM10
    24 hr PM10 SIL is 5 ug/m3
    24 hr PM10 impact on PM10 NA area is 7 ug/m3
Notes: Emissions at NSPS limit = 15tpy PM10 per engine
To not trigger PSD PM10 < 15tpy per 52.21
[Also not a great example – each engine has a PTE of 15tpy PM10 and the SER (existing major source) for PM10 is 15tpy. Maybe primary benefit of this slide is using the terminology!]
Since the NSPS has a PM limit must be compression ignition (Diesel) RICE under 60 IIII [60.4213]

## Slide 281: Group Exercise Averaging Time (2 of 2)
  What is the averaging time for the NSPS PM limit?
  Write an “hours of operation” limit that makes the project a PM10 synthetic minor (<15 T/yr).
  What is the maximum averaging time a PM10 limit could be given to assure PM10 emissions do not cause or contribute to a PM10 NAAQS violation?
Notes: How is the limit written in the NSPS rule?? 60 subpart IIII for compression RICE has a PM limit determined with three one hour compliance tests [Show IIII table
8760 / 5 = 1,752 hrs per engine 12 month rolling [e.g., only one of the 5 engines can run at any time?]
Rolling 24hr PM10 NAAQS in syn minor permit or PSD permit
To determine compliance with the PM mass per unit output emission limitation, convert the concentration of PM in the engine exhaust using Equation 8 of this section:
Where: ER = Emission rate in grams per KW-hour. Cadj = Calculated PM concentration in grams per standard cubic meter. Q = Stack gas volumetric flow rate, in standard cubic meter per hour. T = Time of test run, in hours. KW-hour = Energy output of the engine, in KW

## Slide 282: Discussion of Exercise
  Points to discuss
    “Speed limits” vs. average limits
    Referencing test methods
    Using CEMS for compliance monitoring
    Block average vs. rolling average (or sums)
    Operational flexibility vs. regulatory conditions
Notes: Miles per hour but actually instantaneous limit
Avg CEMs data into hourly averages

## Slide 283: Questions?

## Slide 284
LESSON 11
Best Available Control Technology (BACT)
Notes: Ted
Tip sheet on BACT on LMS and Air Knowledge for review
Also a handout on a Top Down BACT Exercise that I will go thru in a bit.
Deseret SOB BACT section overview – focus on CFB Nox starting on page 50. Costs of SCR on page 51.
But note also SO2 and PM10 and other EUs.

## Slide 285: Best Available Control Technology (BACT)
Best Available Control Technology (BACT) means an emission limitation (including opacity limits) based on the maximum degree of reduction which is achievable for each pollutant, taking into account energy, environmental, and economic impacts, and other costs.
Notes: Defn of BACT 40 CFR 52.21 b 12
51.166 b 12
Will be in your agency’s PSD regs as well
CT/NY/MA may have minor source BACT???
Emission limits determined through the BACT process will be included in the draft PSD permit for comment. And then final permit subject to appeal/court challenge
BACT is in effect very similar to how new source performance standards (NSPS) limits are established except it considers the best a particular new source can do rather than what a typical new source can do.
Not on slide: In no event shall application of best available control technology result in emissions of any pollutant which would exceed the emissions allowed by any applicable standard under 40 CFR Parts 60 NSPS, 61 and 63 NESHAP/MACT. NSPS limit sets the upper for a BACT permit limit.

## Slide 286: PSD Top Down BACT
Step 1 – Identify all control technologies
Step 2 – Eliminate technically infeasible options
Step 3 – Rank remaining control technologies by control effectiveness
Step 4 – Evaluate cost effectiveness of controls and document results
Step 5 – Select BACT
Notes: BACT is determined via a 5 step top down approach.
Source will propose BACT in their permit application. Your role is to review, potentially request revision, propose in PSD permit, approve
First you consider all control technologies that could be applied to a particular source regardless of what they cost or if any one has ever really put a piece of control equipment on a particular source. Any technically feasible control technologies are costed out and the cost effectiveness (in terms of annual dollars per ton removed) is determined. The technology that has the greatest degree of emission reduction at a cost effectiveness' the state or local agencies determine is cost effective is selected. Acceptable cost effectiveness will vary widely. What South Coast Air Quality Management Distinct considers acceptable would be much to high for a state will very clean air.

## Slide 287: BACT Limitations
BACT Determination is site specific
BACT does not redefine project
  BACT does not mandate changes in process or fuel (i.e. a coal fired power plant does not have to be gas fired)
BACT for GHG for “Anyway PSD Sources” will be addressed separately
Notes: Won’t discuss GHG BACT. Leave that to EPA.

## Slide 288: BACT TYPES
Inherently Lower-Emitting Processes/Practices, including the use of materials and production processes and work practices that prevent emissions and result in lower "production-specific" emissions; and
Add-on Controls, such as scrubbers, fabric filters, thermal oxidizers and other devices that control and reduce emissions after they are produced.
Combinations of Inherently Lower Emitting Processes and Add-on Controls. For example, the application of combustion and post-combustion controls to reduce NOx emissions at a gas-fired Combined Cycle Gas Turbine
Notes: e.g., use of VOC free solvent, LNB/OFA for Nox emission, work practices that reduce PM emission
In practice combination of inherent and add-on is used frequently esp if add on specified – LNB and SCR

## Slide 289: BACT Sources
Data sources for Determining Feasible control technology include:
    EPA's BACT/LAER Clearinghouse and Control Technology Center;
    Best Available Control Technology Guideline - South Coast Air Quality Management District;
    Control technology vendors;
    Federal/State/Local new source review permits and associated inspection/performance test reports;
    Environmental consultants;
    Technical journals, reports and newsletters air pollution control seminars
Notes: Link in 2 slides, Show EPA’s RBLC website – should have recent BACT determinations listed in it
https://www.epa.gov/catc/ractbactlaer-clearinghouse-rblc-basic-information
RBLC = explain RACT

## Slide 290: BACT/LAER Clearinghouse
Data on:
  Source Type (i.e. boiler, turbine etc)
  Type of Permit (NSR or PSD)
  Allowed Emission Rate in various units
  Basis for emission rate
Notes: AKA RBLC

## Slide 291: BACT/LAER Clearinghouse (Cont’d)
Control Levels will vary by Locality
Control Levels will vary by process and manufacturer
https://cfpub.epa.gov/RBLC/
Other agencies have clearinghouse documents
CARB, SCAQMD, BAAQMD, SJVAPCD

## Slide 292: BACT Determination
Example:
  Simple cycle gas turbine for peaking power Added to existing major source
  Existing plant has potential to emit (PTE) more than 250 tpy of NOx
  New peaking gas turbine has NOx PTE > 40 tpy, but < 100 tpy CO
  New turbine is subject to PSD BACT for NOx
Notes: We are going to try to look at
Nox SER = 40tpy
CO SER = 100tpy
Assuming PTE after netting etc

## Slide 293
Notes: Here is a cross section of a simple cycle gas turbine. These machines are used for peaking power for utility systems.
Rawhide example: coal boiler, CC turbine and SC turbines

## Slide 294
Notes: This is a picture of an installation of a plant near Colton California.

## Slide 295: BACT Determination For Simple Cycle Gas Turbine
Step 1 Identify All control technologies
  Water or Steam Injection
  Combustion control i.e. low NOx Combustor
  Combination of above
  Add on controls like Selective Catalytic Reduction (SCR)
Step 2 Eliminate Infeasible technologies
  Steam Injection not feasible
Notes: LNB, (OFA) – all lower flame temp to reduce Nox formation
SCR, SNCR, NSCR
Step 2 – watch out for source being overly conservative in eliminating tech as infeasible. Verify justification.
e.g., no steam plant available

## Slide 296: BACT Determination For Simple Cycle Gas Turbine (Cont’d)
Step 3 - Rank Remaining Controls
  SCR add on controls most effective
  Combustion Controls are higher emitting than SCR
  Water Injection least effective in controlling emissions
Notes: SCR gold standard for Nox removal, but quite expensive
All info gathered from source and from independent info – RBLC, other permits for similar source (your job verify)

## Slide 297: BACT Determination For Simple Cycle Gas Turbine (Cont’d)
According to BACT/LAER Clearinghouse;
  7 Installations built simple cycle gas turbines between 2001 and 2014
  BACT determinations ranged from 9ppm (3 cases) to 42 ppm (1 case)
  42 ppm was special case where limited water was available
  Range in BACT results shows that BACT is case by case

## Slide 298: BACT Determination For Simple Cycle Gas Turbine (Cont’d)
Best Available Control Technology Guidelines - South Coast Air Quality Management District
Gas Turbines, Simple Cycle
Gas Turbine, A/N 406065, El Colton, LLC 2/17/04
Gas Turbine, A/N 383044, Indigo 9/18/01
Gas Turbine, A/N 374502, LADWP Valley 9/18/01
Notes: SCAQMD Determinations are usually equivalent to LAER – although often referred to as CA BACT. EPA Region 9 considers them LAER equivalent
298

## Slide 299: BACT Determination For Simple Cycle Gas Turbine (Cont’d)
Step 4 - Evaluate Cost/Rank Controls
Cost of SCR for Peaking Turbine ~$18K/t of NOx removed
Cost of Combustion modification ~ $1K/t of NOx removed
Cost of water injection ~ $1.5K/t of NOx removed
Step 5 – Select BACT
  Water injection and combustion control
Notes: Can be differences between most effective and what is selected as BACT. SC has the worst air pollution problem in the country for O3 and PM 2.5. NOx is a precursor for these 2 criteria pollutants
Annualized costs = operating and capital over life of project (e.g., 20 years) – lot of emphasis and scrutiny on this step
More detail annualized cost when we do the BACT exercise
299

## Slide 300: Another Example
Combined Cycle Power Plant with heat recovery steam generator

## Slide 301
Notes: Nox removal add ons:
NSCR = 3 way cat like in a in car (large oil field engines
SNCR = NH3 with no cat (cement kiln)
SCR = NH3 and cat (power plants)

## Slide 302: BACT Options
Step 1 - Options Similar to Simple Cycle Gas Turbine
  Add on control i.e. SCR, SNCR, and NSCR
  Water injection
  Steam Injection
  Dry NOx Control
Step 2 - Eliminate Infeasible Options
  All options are technically feasible
Notes: A DLE combustor uses the principle of lean premixed combustion, and is similar to the SAC combustor (Single Annular Combustor) with some exceptions.[1][2] A DLE combustor takes up more space than a SAC turbine and if the turbine is changed it can not be connected directly to existing equipment without considerable changes in the positioning of the equipment.[1] The SAC turbine has one single concentric ring where the DLE turbine has two or three rings with premixers depending on gas turbine type.[2] DLE technology demands an advanced control system with a large number of burners.[1][2][5] DLE results in lower NOx emissions because the process is run with less fuel and air, the temperature is lower and combustion takes place at a lower temperature.

## Slide 303: BACT Determination
Step 3 – Rank Controls
  Combined (dry + Add on) highest control
  Add on controls
  Dry NOx Control
  Steam injection next
  Water Injection the Next
Step 4 – Evaluate Cost/Rank Controls
  Add on $30,000 per ton of NOx
  Others less than $4,000 per ton of NOx
Notes: Combined usually done anyway with add on SCR or SNCR e.g., LNB CCs + SCR

## Slide 304: BACT Determination (Cont’d)
Step 5 – Select BACT ????
Review of BACT Documents
According to BACT/LAER Clearinghouse
  36 sources since 2000
  Since 2010 all less than 5 ppm with add on control (SCR)
  2000-2010 most = dry control from 15-25 ppm

## Slide 305: BACT Determination (Cont’d)
Differences based on:
  technology demonstration – use of technology leads to more use
  Definitions of cost effectiveness vary from state to state
Notes: Cost effectiveness $s/ton will vary with assumptions made. Source will tend to assume higher costs for controls, other interested parties can assume lower costs. Permit writers job is to conduct an evaluation of estimated reasonable best case cost.

## Slide 306: Examples of Cost Effectiveness
What is your agency’s threshold?
Examples
Summary of BACT Cost Effectiveness Thresholds ($/ton) |  |  |  |  | 
 | SCAQMD | BAAQMD | SJVAPCD | YSAQMD | SDAPCD
NOx | 19,100 | 17,500 | 24,500 | 24,500 | 18,000
CO | 400 |  | 300 | 300 | 
VOC | 20,000 | 17,500 | 17,500 | 3,900 | 
SOx | 10,100 | 18,300 | 18,300 | 3,900 | 
PM10 | 4,500 | 5,300 | 11,400 | 5,700 | 
Notes: San Joaquin Valley Air Pollution Control District
Yolo Solano Air Quality Management District

## Slide 307: Summary Top Down BACT Review
Step 1 – Identify all control technologies
Step 2 – Eliminate technically infeasible options
Step 3 – Rank remaining control technologies by control effectiveness
Step 4 – Evaluate most effective controls and document results
Step 5 – Select BACT
Notes: BACT is determined via a top down approach. First you consider all control technologies that could be applied to a particular source regardless of what they cost or if any one has ever really put a piece of control equipment on a particular source. Any technically feasible control technologies are costed out and the cost effectiveness (in terms of annual dollars per ton removed). The technology that has the greatest degree of emission reduction at a cost effectiveness' the state or local agencies feels is cost effect is selected. Acceptable cost effectiveness will vary widely. What South Coast Air Quality Management Distinct considers acceptable would be much to high for a state will very clean air.
52.21 b 12
In no event shall application of best available control technology result in emissions of any pollutant which would exceed the emissions allowed by any applicable standard under 40 CFR Parts 60, 61 and 63.
Detailed in EPA’s 1990 draft NSR workbook, AKA puzzle book – walk though

## Slide 308: QUESTIONS?
Notes: Review BACT top down exercise handout
Assume Annualized Cost = 20% of Capital Cost.
Capital cost factoring life of control (e.g., 20 yrs) with depreciation and interest + annual O&M
EPA control cost manual has more detailed info on how to calc costs such as annualized cost.
Deseret SOB BACT section overview – focus on CFB Nox starting on page 50, costs of SCR on page 51 and setting BACT limit fo SNCR page 51 But note also SO2 and PM10 and other Eus.

## Slide 309: LESSON 12
Emission Offsets Banking and Trading
Notes: Carl
The requirement for offsets is specified in 40 CFR 51.165 Appx S Section IV [Appx S is the federal regs that apply in a NA area until the states attainment plan is approved into their SIP.
BTW this is also the section that requires an applicant to certify compliance state wide
NYDEC = Subpart 231-5 New Major Facilities and Modifications to Existing Non-Major Facilities in Nonattainment Areas, and Attainment Areas of the State Within the Ozone Transport Region

## Slide 310: Lesson Objectives
Explain the emission offset requirements
Define the offset ratios
Discuss criteria for emission offsets
Examine emissions trading vs emissions banking
Notes: Here are the lesson objectives.

## Slide 311: Emission Offsets Pre-Construction Permits NA-NSR
Offsets:
  Emission reductions that:
    Offset the emissions increases resulting from the new source or modification, and
    Provide a net air quality benefit
  Offset ratio can be from 1:1 up to 1.5:1, depending on:
    the criteria pollutant of concern; and
    the nonattainment classification
Notes: In addition to LAER emissions from the new source in a NA area, must be offset with emission reductions at other sources. All offsets are at least 1 to 1 and may go as high as 1.5 to 1. The intent is to provide a net air quality benefit.

## Slide 312: Federal Offset ratios
Area Classification Ratio
Ozone Marginal 1.1:1
Ozone Moderate 1.15:1
Ozone Serious 1.2:1
Ozone Severe 1.3:1*
Ozone Extreme 1.5:1*
*1.2:1 if SIP requires all existing major sources in Non-attainment Area to
use BACT
CAA § 182
Notes: LESSON 2 - NSR
12/06
CARB 334
312

## Slide 313: Federal Offset Ratios
Area Classification Offset Ratio
CO Moderate 1:1
CO Serious 1:1
PM10/2.5 Moderate 1:1
PM10/2.5 Serious 1:1
NO2, SO2 All 1:1
Notes: LESSON 2 - NSR
12/06
CARB 334
313

## Slide 314: Offsets Exercise
Maximum emission rate of new source is 100 pounds per hour
LAER reduces emissions 80%
Offset required is 1.2:1
What is the uncontrolled PTE of the source in tons per year?
What are the offsets required in pounds per hour?
From what geographical area are the offsets required?
How is the source going to obtain the offsets?
Notes: In this case the uncontrolled PTE = 438 tpy
After control (since the control is required by NA NSR permit) is 87.6 tons per year
And the offsets are 105.12 tpy or 24 lbs per hour.
The geographical area for the offsets depends on the pollutant. For PM10 and SO2 the geographic area can be limited to the area near the source (aka hot spot pollutants). The area for pollutants like ozone or PM2.5 is generally the entire aqcr (aka regional).
Since 1.2:1 must be O3 serious
Sources of offsets will be discussed next. NOTE: ALL EMISSION REDUCTIONS USED FOR OFFSETS MUST BE ACTUAL EMSSIONS
314

## Slide 315: Offsets Exercise (Cont’d)
Offsets:
  Calculating offsets is more involved than the example
    The example looked only at offsetting direct emissions from the project
    In practice, offsets must assure “reasonable further progress”
      Reasonable further progress is a planning term
Notes: In addition to just offsetting the source the area must make reasonable further progress so the offsets can be more than 1 to 1

## Slide 316: Emission Offsets
  How are offsets obtained?
    Enforceable emission reductions in the non-attainment area
    Banking
    Other?
Notes: Offsets can come from a variety of area. The new source can put controls on other sources that they own or can persuade other people to put on. As an alternative offsets can be obtained from an emission bank maintained by the state or private banker. Other offset sources can be made by the state or local government. In the past governments have done things like switch to a water based asphalt or add additional bus lines

## Slide 317: Emission Allowances & Emission Offsets
Emissions trading
versus
Emissions banking
Notes: 317

## Slide 318: Emissions Trading
Emissions Trading (Market Based program):
  Also called a “cap and trade” program
  Emissions are limited on a geographic basis
  Emissions are tracked through allowances
  Sources must hold enough allowances to cover actual emissions (usually on an annual basis)
  Sources can buy or sell allowances
    Sources that can economically reduce emissions can sell excess allowances to sources that cannot economically reduce emissions
  Title IV Acid rain SOx trading program is an example of an emissions trading program
  Requires comprehensive and transparent method of tracking emissions
Notes: Emission trading is used in both attainment and non attainment areas. SO2 trading for acid rain is a good example of a market based program for emission reductions. Also can be used under umbrella programs like RECLAIM in south coast or ERMS in Chicago. Also this is the type of program talked about for GHG emissions REGI
318

## Slide 319: Emissions Banking
Emissions Banking:
  Primarily a nonattainment area program
  Allows sources who have gone out of business or reduced nonattainment pollutants to below regulatory requirements to “bank” those emissions
  New or modified sources may purchase banked emissions when needed for offsets
  Requires comprehensive and transparent method of tracking emissions
Notes: Generally run by a state or local agency. Takes actual emissions from shut down sources or sources that over controlled and sells the emissions to new sources.
However banking can be less rigorous program that a trading program (e.g., just a spreadsheet the state maintains)
319

## Slide 320: Emissions Banking (Cont’d)
Emissions Banking:
  For purposes of banking, trading, or immediate use, emissions reductions must be:
      Real
      Surplus
      Permanent
      Quantifiable
      Enforceable
Notes: Here are the criteria you have to meet for the emissions to be banked.
Real means actual emissions [not PTE or allowables];
surplus means emissions reductions are not needed to show compliance;
permanent means that the emissions cannot be taken back due to things like growth etc.,
quantifiable means that the emissions can be measured and
enforceable means you can take administrative or court action on a source if the reductions don’t meet the 4 other criteria.

## Slide 321: Emissions Banking (Cont’d)
Emissions Banking:
  A state or local agency operating a registration program must ensure that the banked emissions meet these five criteria

## Slide 322: Emissions Banking (Cont’d)
Emissions Banking:
  Offsets must generally be of same pollutant
    Some consideration of inter-pollutant offsetting between PM2.5 precursors (SOx/NOx/PM2.5)
    Inter-pollutant offsetting for ozone precursors (VOC/NOx) not allowed (D.C. Circuit Court, Sierra Club v. EPA, January 29, 2021)
  The use of emission reduction credits to offset other criteria pollutants may be restricted geographically
Notes:   In a case of PM2.5 nonattainment, emission reductions of SOx or NOx for PM2.5 are used to offset a prescribed ratio. For ozone nonattainment, emission reduction credits of VOCs and/or NOx are not allowed based on the D.C. Circuit Court decision in the case of Sierra Club vs. EPA, January 29, 2021.
    These emission reduction credits have to come from the same nonattainment area or a contiguous nonattainment area of more severe nonattainment.

## Slide 323: Questions?

## Slide 324
LESSON 13
Role of Modeling
& Inventories in Permitting
Notes: Ted
Discussed increment and ambient air impact analysis in the PSD lesson. This is done through use of EPA approved computer modeling.
Deseret SOB TOC Re Modeling

## Slide 325: AIR SHED MODELING EXAMPLE
Air Quality Modeling to Support the Georgia SIPs for O3
Courtesy of Georgia Department of Natural Resources
Special thanks to Jim Boylan of the Protection Branch
Notes: This example shows how Photochemical models are used to evaluate Ozone SIPs. It is unrelated to the type of modeling that is done for permits.

## Slide 326: Lesson Objectives
Learn how permits fit within the SIP planning process
Provide an overview of Modeling & Inventories
  Uses and Reasons
  Benefits
  Limitations
  Factors Affecting Models
  Types of Models

## Slide 327
Non-Attainment in Georgia

## Slide 328
Future year emissions (e.g., 2009)
Air Quality Goals (i.e., attainment status)
Emissions control strategy
Clean Air
Pollutant distributions and sensitivities
Future year (e.g., 2009) emissions with controls
Area not in attainment
Area in attainment
Attainment demonstration and future year modeling
Air Quality Model
Both modeling runs use the same meteorological & air quality inputs
Note:
Air Quality Model
Pollutant distribution
Model Performance Evaluation
Base year emissions (e.g., 2002)
Base case modeling
Demonstrating Attainment using AQ models

## Slide 329: 2002 Atlanta VOCs (tons)
Notes: Again FYI on air planning activities

## Slide 330: 2002 Atlanta NOx (tons)

## Slide 331
Future Emissions in Georgia
Reductions in NOx and SO2  reductions in ozone and sulfate PM2.5

## Slide 332: CMAQ is a Grid-Based Model
Si
Si
Ri
ui
ui
ui
Ki
Ki
Ki
Model Outputs: Hourly pollutant concentrations for every grid cell in the domain
Gases (ppm) and PM (mg/m3)
Notes: The concentration in each grid cell (cube) is uniform. Since ozone presents very broad spatial concentration gradients the spatial resolution provided by a grid model is adequate. However, for pollutants such as SO2 where the spatial gradients are high grid models are inadequate for finding the design concentration.
In contrast to the model used for single sources and permitting - AERMOD

## Slide 333
Max 8-hour O3 on June 12 2002 Emissions
Air Quality Modeling (CMAQ)
Max 8-hour O3 on June 12 2009 Emissions

## Slide 334: Projected Ozone Attainment Status for 2009

## Slide 335
2002

## Slide 336
2009

## Slide 337: Future Ozone Concentrations
(BaseG2 emissions)
Notes: Did not make attainment in 2009 but did in 2012

## Slide 338: Discussion
How were permit terms and conditions helpful to development of the State’s SIP?

## Slide 339: QUESTIONS

## Slide 340: Lesson Objectives
Provide an overview of Modeling & Inventories
  Uses and Reasons
  Benefits
  Limitations
  Factors Affecting Models
  Types of Models

## Slide 341: Overview
Models use mathematical and numerical techniques to :
  Simulate physical and chemical processes that affect air pollutants
  Predict concentrations of pollutants of interest
Based on input related to
  Meteorological data
  Source information
  Type of pollutant
Notes: The type of pollutant determines whether you need to consider a chemical transformation in the atmosphere, depletion of plume mass due to settling or deposition due to diffusion near the ground, etc.

## Slide 342: Uses and Reasons
Used by agencies tasked with controlling air quality
Identify source contributions to air pollution problems
Verify that emissions from a new or modified source will not cause or contribute to a violation of air quality standards or PSD increment and/or adversely affect human health and the environment
Assist in the design of control strategies
Determine emission limits from stacks that are greater than GEP
Notes: * The only way to determine the appropriate emission limit for a PSD source is through modeling since the source does not exist.
* GEP (Good Engineering Practice) stack height, is the min height needed to avoid the problem of downwash. If a company builds a stack that's > GEP it can not get credit for the reduction in ground level concentration that the excess stack height provides. Therefore, to set an emission limit for stacks > GEP height the actual stack height is used in the model. Of course, this means that the actual "measured" concentrations should be lower than the model predicts. As a result in areas where there are a number of stacks above GEP monitoring is not useful since it can not account for the discredited dispersion that the excess stack height has produced.

## Slide 343: Benefits
Predict future concentrations from multiple sources
Capture peak concentrations (design values)
Determine contribution from proposed or existing sources
Only modeling can determine the emission limit for a proposed source
Faster turn-around than monitoring
Monitoring tools may be unavailable
  methodology
  instruments
Notes: The point of modeling for new source review or SIP demonstrations is to find the single concentration within the entire ambient air that should be compared to the standard or PSD increment. This one value is known as the design value. In areas that have a high concentration gradient only models are capable of determining the design value.

## Slide 344: Most Common Types of Models
Screen​ing
Dispersion ​
  Near Field - Gaussian​, steady state
  High resolution​
  Single or multiple sources
Photochemical ​
  Long Range Grid Models​
  Primarily for O​3 Secondary PM2.5
Puff
  Long-Range Transport
  Time dependent​
  E.g. used to predict the impact from a new source on a Class I area that is > 50 km away
Notes: EPA’s Guideline on AQ Models is found at Part 51 Appx W. This guideline is basically considered a reg by EPA regarding modeling for permits and SIPs.
Dispersion models are designed to simulate the near-field turbulent structure of the atmosphere since sources who's important impacts are within a few kms of the modeling area. The turbulent structure of the atmosphere plays that greatest role. This type is used for modeling single sources seeking PSD permits.
*Photochemical grid models (also known as Eulerian models) do not effectively deal with the near-field turbulent structure of the atmosphere. Rather, they are designed as atmospheric chemistry models where each grid cell acts as a reaction vessel that for each hour has pollutants (reactants) injected into it via emissions, diffusion from a adjacent cell, advection from an adjacent cell (I.e. wind blowing mass into the cell. Then a series of Photochemical reactions take place and the concentrations of pollutants and other chemical in the cell change and their distribution in the cell is considered to be uniform. This is done for each cell in the grid. The size of these cells are on the order of kms. Therefore, the ground level concentrations for any pollutant will be averaged over the size of the grid cell. This resolution is fine for pollutants like ozone and secondary PM2.5, since their spatial concentration gradients are very broad. But for other pollutants such as SO2, primary PM2.5, lead, many air toxics, etc. A grid model will be inadequate in finding the design concentration.
*Puff Models (also known as Lagrangian models). Like dispersion models the use a Gaussian approach to turbulent diffusion. However, these models can predict concentrations out to 100 km or more since pollutants are modeled as a series of puffs (not a plume). These puffs can then be move around, disperse, interact with other puffs within the modeling domain hour after hour as the meteorological data changes (puff models are time dependent). They contain minimal chemistry. Their main purpose is to make predictions for primary inert pollutants beyond a distance where the assumption of steady-state (I.e. dispersion models) fails.

## Slide 345: Screening Models
Usually applied to determine the need for more refined models
Common Screening models
  AERSCREEN – for flat and complex terrain
  CTS SCREEN – a more refined complex terrain
  VISCREEN – for visibility source impacts
Notes: CT Screen is the screening version of the CTDM+ model which an applicant can use to further refine an AERMOD analysis that predicts the design concentration to be on an isolated hill.

## Slide 346: AERSCREEN
Inputs
  Emission rate
  Source type (i.e., point, area, volume)
  Hs, Ds, Vs, & Ts
  Distance out to which receptors are placed
  Urban or Rural
  Building dimensions – if downwash is being considered
Limitations
  Can model a single source only
  Does not predict best case estimates of concentration. It uses conservative assumptions so it overpredicts
Notes:   Additional Input Info needed if NO2 is being modeled

## Slide 347: SCREEN Model Limitations
Cannot handle multiple sources
Only predicts hourly concentrations – 3hr., 24hr. & annual are scaled based on research studies
Does not use actual meteorology representative of the site
Impacts are generally overestimated
Notes: Although screening models only predict hourly concentrations, 3hr., 24hr and annual concentrations can be estimated from the hourly concentration through the use of simple scaling factors. Scaling factors are simply values that are less than one that get the one hour concentration gets multiplied by. These scaling factors are based on computational studies that suggest that their use is conservative, I.e. they should overestimate the various averaging times.

## Slide 348: SCREEN Model Attributes
Easy to use
Conservative downwind concentration
Minimal input requirements
Can simulate point, area, and volume type sources
AERSCREEN can simulate both inversion break-up as well as coastal fumigation.
Notes: * Inversion breakup fumigation occurs in the morning. It is due to pollutants that are trapped aloft once the boundary layer collapsed the day before and the atmosphere becomes very stable preventing the vertical dispersion of the pollutants aloft. The next morning when the sun starts to heat the surface the convective boundary layer begins to grow. Once the convective mixing height grows to the layer that contains the pollutants from the day before (an possibly additional elevated emissions during the night) the convective eddies, caused by surface heat flux, rapidly dispersions the pollutants to the ground. This causes a short lived but high concentration at ground level.
*Coastal fumigation can occur during the day. It is caused by the release of an elevated source that is located on the coast with the wind blowing on shore. When the wind blows on shore where the ground has a positive heat flux a thermally induced boundary layer is formed. That is, the air coming in off the water is generally stable. As it moves over the warm ground convective eddies eat away at the stable air creating a mixing depth the grows as one moves inland. The emissions from the source, located on the coast line, will initially be transported through a stable layer with very little vertical dispersion. However, as soon as the plume reaches the point inland where the mixing layer has grown to the height of the plume fumigation occurs where the highly concentrated plume is rapidly dispersed to the ground.

## Slide 349: Dispersion Models
Typically used in the permitting process
  Predicts ground-level concentrations at specified receptor locations no > than 50 km from the source
Commonly used for “inert” pollutants, although AERSCREEN can consider NOx chemistry
Notes: Although this is not scientifically correct, the agencies policy is that dispersion models can be use out to 50 km. The issue is their assumption steady-state. The accuracy of this assumption depends on how far the pollutants can travel in an hour (a function of wind speed) before the meteorology changes. Obviously a simple calculation shows that a wind speed of approx.13 m/s is needed for pollutants to travel 50 km in an hour. Typically, wind speeds that produce the highest concentrations range from 1 to 5 m/s.

## Slide 350: Modeling Assumptions
Concentrations at the receptor are directly proportional to emissions
Dispersion models are steady-state
Dispersion models assume Gaussian and bi-Gaussian distributions of concentration.
Grid model resolution is only as fine as the size of the grid cell, which is on the order of Kms.
The greater the down wind distance the greater the dispersion, but not necessarily the lower the concentration
Notes: On of the major improvements that AERMOD has over ISCST3 is that it more accurately models the Convective Boundary Layer (CBL – I.e., during the day when there is surface heating from the sun. For the concentration distribution to be Gaussian (bell curve) in the vertical the plume would have to be affected by as many updrafts as downdrafts. However, research during the 1980's demonstrated that 60% of the time the plume is impacted by a downdraft and 40% of the time by an updraft. To handle this AERMOD assumes that in the CBL the vertical concentration is better simulated by assuming two Gaussian plumes, an updraft and a downdraft plume. When combined the mathematical result is bi-Gaussian distribution.
For ground level sources the concentrations will always be lower the farther downwind the receptor is. However for elevated sources the pollutants need to diffuse to the ground before any concentration appears at a receptor. Therefore the distance downwind to the highest concentration depends on plume rise, mixing height and the strength of the vertical turbulence.

## Slide 351
He = Hs + h
Effective Stack Height = Physical Stack Height + Plume Rise
Sensitivity of GLC
to Release Height
Notes: GLC = ground level concentration
Concentrations from ground level sources are highest at the closest receptor downwind of the source and decrease farther downwind (see blue curve)
Elevated sources do not have the largest impact next to the source. The max impact is some distance downwind depending on the sources effective plume height, the mixing height and the magnitude of the vertical turbulence (see the red curve)

## Slide 352: Atmospheric Influences
Dilution
Dispersion
Transport
Chemistry
Removal
  Settling
  Deposition
  Transformation
Notes: Dispersion: Scattering of a substance away from its sources (fertilizing the lawn scatter particles)
Dilution: reduces the concentration of a pollutant by mixing the pollutant with air or water. One drop of bleach in water.

## Slide 353: Dispersion - A Function of
STACK CHACTERISTICS
  Stack height & diameter
  Exit gas temperature and velocity
  Emission rate
METEROLOGY
  Atmospheric turbulence
  Stability & Mixing height
  Wind direction & speed
  Distance down wind to point on ground
Notes: In dispersion models prior to AERMOD stability was effectively equated to turbulence. This misnomer has been corrected in AERMOD. By stability here I'm referring to whether our predictions are being made in the unstable Convective Boundary Layer (CBL) or the Stable Boundary Layer (SBL). The actual measure of stability, in AERMOD, is used primarily as a scaling length parameter for estimating meteorological profiles and other more esoteric effects (this is clearly.
Air quality dispersion modeling is a computer simulation that predicts air quality concentrations from various types of emission sources.
It considers the effect of nearby buildings and terrain. Other emission sources like vehicle traffic or wind erosion from storage piles are represented as 2-dimensional area sources or 3-dimensional volume sources.
AERMOD is current EPA approved dispersion model

## Slide 354: The Results
Ground level concentrations at all selected receptors
  Results can be the incremental impact from one or more sources. E.g. when estimating impact on PSD increment.
  By modeling all appropriate sources and adding background to account for distance sources, total concentrations can be estimated
Notes: Dispersion models provider the user to define thousand of receptors where calculations can be made. In general, there are 3 ways to define receptors: 1) defining one or more rectangular grids, which can vary in resolution; 2) defining one or more polar grids, which can vary in resolution (useful for a single elevated source, where the concentration gradient drops off with distance); and 3) defining individual single receptors (discrete receptors).

## Slide 355
U.S. EPA and American Meteorological Society (AMS) initiated a formal working group – AMS/EPA Regulatory Improvement Committee (AERIC)
AERMOD has replaced ISCST3 and Complex I as the approved Regulatory Guideline Model for both flat and complex terrain
  (Guideline on Air Quality Models, 40 CFR 51 Appendix W)
AERMOD
Notes: Before AERMOD different models had to be use depending on whether the source was in flat or complex terrain. With AERMOD the user does not have to distinguish between complex and flat terrain, AERMOD seamlessly considers both.

## Slide 356: AERMOD
AERMOD stands for American Meteorological Society/ Environmental Protection Agency Regulatory Model
Formally Proposed as replacement for ISCST3 in 2000
Adopted as Preferred Model November 9, 2005

## Slide 357: AERMOD GOALS
Replace ISCST3 by:
  Updating ISCST3’s algorithms based on the significant degree of research performed in the 1980’s
  Improve handling of source and atmospheric processes
  Produce a concentration that applies in both flat and complex terrain.
Notes:   AERMOD separates daytime (Convective BL) from nighttime (Stable BL). It also introduced explicit planetary boundary layer physics that had been highly parameterized in ISC3. These boundary layer states are very different in their physical properties and thus how pollutants are dispersed. In AERMOD the CBL and the (SBL) are mathematically simulated very differently, whereas prior models did not make this distinction they simple parameterized the entire turbulent structure of the PBL by using the PGT stability curves which depended on which stability class was estimated for the hour of your calculation; AERMOD never references stability class or PGT stability curves.

## Slide 358: AERMOD GOALS (Cont’d)
Replace ISC3 by:
  Capturing our present understanding of atmospheric processes
  Providing reasonable concentration estimates under a wide variety of conditions
  Accommodating modifications easily as technology advances
Notes:   AERMOD was designed to have its input framework mimic ISCST3, in order to at least have the part of the model that users interact with be as familiar as possible. It allows capturing our present understanding of atmospheric processes while remaining relatively simple in terms of input requirements. Providing reasonable concentration estimates under a wide variety of conditions (complex & simple terrain, downwash conditions, both urban and rural environments, etc.)

## Slide 359: AERMOD
3 COMPONENTS
  AERMET – THE METEOROLOGICAL PREPROCESOR
  AERMAP – THE TERRAIN DATA PREPROCESSOR
  AERMOD – THE DISPERSION MODEL
2 SUPPORT TOOLS
  AERSURFACE – PROCESSES SURFACE CHARACTERISTICS DATA for input to AERMET
  AERMINUTE – Processes 1 min. data for input to AERMET
  AERSCREEN – PROVIDES A SCREENING TOOL
Notes: Relative to surface characteristics AERMOD needs the albedo (% reflectivity of solar radiation by the earth), Zo (roughness height – essentially magnitude of the friction that the earth's surface presents to the flow of air), Bo (The Bowan ratio which is the ratio of sensible heat – the heat you feel to laten heat the heat used to evaporate moisture). These surface parameters are found in tables for each surface classification as defined by the USGS. AERSURFACE processes land use data from USGS and produces these parameters for AERMOD
AERMINUTE processes 1 min meteorological data where available (speed and direction) into true hourly averages. Most NWS data are not true hourly averages, they are simply an observation of speed and direction at the top of the hour that is used to represent that hour.

## Slide 360: AERMOD (Cont’d)
Requires extensive data input
  Meteorological
  Terrain
Steady state plume model, with concentration assumed to be
  Bi-Gaussian in the Vertically
  Gaussian in the Horizontal
Applicable to
  Rural & urban areas
  Flat & complex terrain
  Point, area, line & volume sources
Notes: A discussion of bi-Gaussian was provided in a previous note.

## Slide 361: AERMOD (Cont’d)
Removes need to distinguish between simple, intermediate, and complex terrain
Important because?
Includes two preprocessors and the dispersion model
  AERMET is the preprocessor which provides meteorological info to AERMOD
  AERMAP is the preprocessor which provides terrain and spatial info to AERMOD
Calculates concentrations, deposition and depletion
Notes: It’s important because prior to AERMOD different models had to be used for Complex and Flat terrain, i.e. Complex I and ISCST3, respectively
AERMOD can calculate either air concentrations or the amount or ground deposition resulting from a sources emissions. It also calculates depletion is the user so chooses. Depletion is the amount of pollutant that has deposited on the ground and is no longer available for calculating air concentrations beyond the point of its deposition. By selecting the depletion option the calculation of air concentrations will be the same of smaller depending on how much mass has been depleted by deposition.

## Slide 362: AERMOD (Cont’d)
Requires local information
  Wind speed, direction
  Surface Characteristics – Land use, impervious surface and tree Canopy
  Mixing height
  Topographical data
  Population – urban mode
Requires detailed source information
  Emissions
  Stack parameters
  Operation conditions
  Building dimensions – downwash
Tends to overestimate impacts for some situations but in general its predictions are unbiased
Notes: Permit application will need to include this information so air modeling expert and permit writer can review.
Land use data was discussed in a previous note

## Slide 363: Photochemical Models
Used Primarily for O3 attainment demonstrations, and the long-range transported PM2.5 aerosols component of the total PM2.5 concentration
Simulates impacts from all sources, anthropogenic and biogenic
Predict deposition of pollutants over wide areas
  Generally not useful for NSR/PSD permit modeling – lack of needed spatial resolution
Requires considerable computational resources
Notes: EPA has SIL guidance for O3 and PM2.5 so that generally (in the large majority of cases) PC models don’t need to be run for a PSD AQ impact analysis

## Slide 364: Common Photochemical Models
Community Multi-scale Air Quality (CMAQ)
Comprehensive Air Quality Model with extensions(CAMx)
Regional Modeling System for Aerosols and Deposition (REMSAD)
Urban Airshed Model Variable Grid (UAM V)

## Slide 365: Mobile Source Models
Mobile sources contribute significantly to:
  Criteria pollutant concentrations
  Air toxics effects
  Greenhouse gases emissions
EPA uses mobile models to estimate emissions from on-road vehicles, nonroad sources, and fuels, not ambient concentrations
Results of the mobile models are used for input to air quality simulation models
Notes: Need mobile emissions to calculate background (baseline) concs

## Slide 366: Mobile Source Models (Cont’d)
These models calculate amount of
  Carbon Monoxide
  Hydrocarbons
  Nitrogen Oxides
  Particulate Matter
  Sulfur Dioxide
  Air Toxics

## Slide 367: Mobile Source Models (Cont’d)
EPA’s MOtor Vehicle Emission Simulator (MOVES)
  Emission modeling system that estimates emissions for mobile sources at the national, county, and project level for criteria air pollutants, greenhouse gases, and air toxics.
Predicts on-road and non-road source emissions
https://www.epa.gov/moves

## Slide 368: Mobile Source Models (Cont’d)
Predict and assess, in conjunction with an air dispersion model, the effectiveness of mobile source and fuel control strategies
  Sulfur reduction in diesel fuels for PM 2.5
  Catalytic converter effectiveness
  Particulate traps for reduction of PM 2.5
  Future attainment strategies
Notes: State planning team need to look at these as part of non attainment plans

## Slide 369: A WORD ABOUT MONITORING
Useful tool
Advantages:
  Accurate data
  Needed to develop background levels
Disadvantages:
  Limited locations
  Ability to capture maximum concentrations are highly uncertain
  Time consuming & Expensive
Notes: Monitoring is the foundation of understanding AQ and AQ planning, However…

## Slide 370: EMISSIONS AS RELATED TO INVENTORIES
Emissions: Gases and particles which are put into the air or emitted by various sources

## Slide 371: EMISSION DATA REQUIREMENTS
EPA’s Emissions Measurement Center develops standards and evaluates testing methods
Example: Emission factors
This results in consistent emissions data for various uses

## Slide 372: EMISSION INVENTORIES
Quantity of pollutants are measured over time using standardized methods
Once measurements are made the data is stored for various uses
Rule development
Modeling use

## Slide 373: CHIEF
Clearinghouse for Inventories and Emission Factors
Centralized resource for emissions data
https://www.epa.gov/chief

## Slide 374: Questions?

## Slide 375: LESSON 14
Title V
Operating Permits
Notes: Carl
We have been talking about construction and pre construction permits. Now we switch to operating permits
Mentioned OP earlier in Permits lesson
Open PDFs for Colstrip TV permit, Rawhide TRD, Fidlar SOB
375

## Slide 376: Lesson Objectives
What is Title V
The purpose of Title V
Title V Applicability
What is included in a Title V permit
What is an “applicable requirement”
What is the “application shield”
Title V permit amendments/modifications
Notes: This is what we are going to do today. We will cover from what Title V is to how to amend the permit.
And “permit shield”
376

## Slide 377: What Is Title V
6 Titles in the 1990 Clean Air Act Amendments
  Programs and Activities
  Emission Standards for Moving Sources
  General Provisions
  Acid Deposition
  Permits
  Stratospheric Ozone Protection
Notes: It is called Title V since that is what it is in the Clean Air Act (CAA). In 1990, Title I of the CAA was amended by adding Air Toxics provisions into Title I. Also there are more titles in the CAA, such as Title VII (the Enforcement program), but those titles were not amended in 1990.

## Slide 378: How Title V Permits Differ from Pre-Construction Permits
Pre-Construction Permits are required for most new facilities or new/modified units at existing facilities
Title V is an “Operating Permit” program
Title V does not generally create any new federal requirements for a source
Title V permits contain most Pre-Construction Permit conditions
Notes: Title V (major sources) does not give permission for a source to construct but rather to operate in accordance with the permit to construct.
Title V does not provide any additional substantive requirements.
But a Title V can add monitoring and/or recordkeeping provisions if the applicable requirement doesn’t specify any.
All pre-constr permits – minor, syn minor, PSD

## Slide 379: Title V Permits – AKA Part 70
Statutory basis for federal operating permit program
  CAA Title V
Regulations implementing program
  40 CFR Parts 70 & 71
  Part 70: State-issued permits
    Therefore often referred to as Part 70 Operating permits
  Part 71: EPA-issued permits
Notes: Title V is also known a Part 70 from the CFR. Part 70 refers to state issued permit and part 71 is either federal issued or federal delegated permits

## Slide 380: Part 70 Programs
Most states (and some tribes) have a Title V operating permit program approved by EPA
The programs may be carried out by
  The state/tribal agency
  A local agency
These state/tribal/local programs must meet the requirements of 40 CFR Part 70
Notes: Title V has one rather unusual feature – in order to approved for a Title v the states have to get HAP [MACT] authority.
TV program approval is not part of the SIP but EPA did approve state Part 70 plans.

## Slide 381: Part 71 Programs
EPA will administer an operating permits program (full or partial program)
  If a Part 70 program has not been granted full approval
    In a state
    In Indian country
  As needed, for a specific permit/source

## Slide 382: Title V Permits
PURPOSE & BENEFITS

## Slide 383: Purpose of Title V
A comprehensive permit system that identifies, aggregates, and implements Clean Air Act requirements for sources of air pollution
Enable the source, states/locals/tribes, EPA, and the public to better understand the requirements to which the source is subject to
Combines existing applicable requirements into one permit
Notes: This is what the Title V program is supposed to do. Collect all permit conditions and applicable requirements into one permit doc.

## Slide 384: Benefits of Title V
Provide an opportunity for citizens to be involved in the permit review process
Aid in determining whether the source is meeting those requirements
Increase source accountability resulting in better compliance
Notes: One way to increase information as to what the source has to do is to put all the requirements from many construction permits issued over many years into one consistent and understandable permit, along with applicable NSPS and MACT standards, SIP rules, acid rain rules

## Slide 385: Benefits of Title V (Cont’d)
Provide the basis for better emission inventories
Provide a vehicle for the states to administer parts of the Federal Air Toxics program
Play a significant role in ensuring compliance with the acid rain regulations based on Title IV of the Clean Air Act
Notes: More good things a Title V program is supposed to do. Note the second bullet – actually the state has not choice in this if they want a title v program.

## Slide 386: Benefits of Title V (Cont’d)
Fee-for-service program
  Ensure that States have resources necessary to develop and administer the program effectively
  Create an incentive for sources to reduce emissions
Notes: Title V is also a way to get money. The fees are supposed to provide an incentive to reduce emissions – the fees are relatively low.
TV is to be self funded, other CAA grant money can’t be used for the program and TV funds cant be used elsewhere
EPA default fee is about $65/ton

## Slide 387: Title V Public Participation Opportunities
Comment on and request a public hearing on draft permits
Appeal Part 70 permits in state court
Petition the EPA to object to a permit
Appeal EPA-issued permits to the Environmental Appeals Board and federal courts
Track compliance by reviewing reports/certifications submitted by sources
Bring citizen suit in civil court for permit noncompliance
Notes: Min 30 day comment period

## Slide 388: Title V Permits
APPLICABILITY
Notes: 388

## Slide 389: Applicability
Title V Operating Permits are required for: (40 CFR 70.3)
  Major Sources
  Affected Sources (under CAA Title IV)
  Sources subject to section 111 (NSPS) or 112 (NESHAP) of the CAA
  Sources required to have a permit under Part C (attainment areas) or Part D (nonattainment areas) of CAA Title I
Notes: These are the sources subject to Title V. We talked earlier about what was a major source and how that was not so simple a situation.
Next slide: Major source generally > 100tpy or 10/25tpy HAPs, but can be less – in O3 NA area, certain incinerators
Note that many sources subject to 111 and 112 are specifically exempted from title V. EPA decided to do this to since many of the newer NSPS and MACT standards are for small sources like emergency generators (IIII, JJJJ and 63 zzzz) or gas stations 6c
CAA T IV = acid rain program
389

## Slide 390: Applicability (Cont’d)
  Regulated pollutant thresholds:
    Criteria pollutants: > 100 tpy PTE
    HAPs: > 10tpy (1 HAP) or > 25 tpy of HAPs
  Solid Waste incinerators required to obtain a permit under CAA section 129(e)
  Non-major sources when required by the applicable standard
Notes: The Major Source Thresholds for Title V sources will also depend on the attainment status of the source, as determined under Title I of the CAA. For example in an Extreme Ozone Non-attainment area, the Title V Major Source Threshold for VOCs and NOx would be 10 tpy PTE, instead of 100 tpy PTE. Also as I am sure you remember GHG cannot be the only reason that a source is subject to regulation but can be included if the source is otherwise affected. These are the “anyway” source. UARG is the Utility Air regulatory group.
390

## Slide 391: Greenhouse Gas “Anyway Sources”
In 2014, the Supreme Court found EPA could no longer regulate sources under the PSD and Title V permit programs based solely on their emissions of GHGs.
However, if a source triggers the PSD program for other pollutants, it can be required to comply with BACT for GHGs. Utility Air Regulatory Group v. EPA, 134 S. Ct. 2427 (2014).
These are often referred to as “anyway sources”.
Notes: GHGs need to be accounted for (PTE) in TV application

## Slide 392: Applicability (Cont’d)
Exempt source categories
40 CFR 60 subpart AAA, NSPS for New Residential Wood Heaters
40 CFR 61.145, Asbestos Reno/Demo NESHAP
Subsequently added exemptions:
  Non-major sources not otherwise required to obtain a Part 70 permit (state discretion)
Notes: 392

## Slide 393: Major Source
A more thorough discussion about the definition of “major source” is presented in Lesson 3

## Slide 394: Fugitive Emissions
To be included in PTE calculation when base program (i.e., MACT, certain PSD & NSR) so require inclusion
Definition of fugitive seems straightforward
Interpretation and application of definition may be challenging
Notes: Fugitive emissions can be an issue. If they are part of the construction they count in the title V. If not they don’t. for PSD this means that fugitive emissions do count for the listed sources but not for the non listed aka the 250 tpy

## Slide 395: Synthetic Minor
Source can avoid Title V requirements under certain conditions
Maintain an emission level below applicability thresholds
Notes: Next slide: Synthetic Minor permit may also be a FESOP (Federally Enforceable State Operating Permit)
FESOP conditions must be reflected in SIP
This makes them “Federally Enforceable”
If not in SIP, limiting conditions cam be in a “state-only” permit
Can be called SOP or state operating permits
395

## Slide 396: Synthetic Minor (Cont’d)
Emission levels must be
  Reflected in a formal permit issued by the agency
  Enforceable (federally and practically enforceable)
  Federally Enforceable State Operating Permit (FESOP) and Minor NSR Permit
Notes: We talked earlier how to limit PTE These are the same techniques in the synthetic minor

## Slide 397: Title V Permits
PERMIT APPLICATION
Notes: Now we will talk about what it is in the permit application.
397

## Slide 398: Permit Application
40 CFR 70.5 specifies the minimum requirements for Part 70 applications
  Timely submittal
  Completeness determination
  Application “Shield”
    Protects source from action while application is being processed, if application is timely and complete
Notes:   Timely submitted means
  For new sources - Within 12 months of commencing operation
  For permit renewal, a timely application is one that is submitted at least 6 months prior to the date of permit expiration
  Application deemed complete if Permitting Agency has not determined the application incomplete within 60 days of receipt
  Permitting agency can still request additional information even though deemed complete
  Source must respond to the request within the time frame specified in the request
  An application being deemed complete triggers the “Application Shield”
  A person operating a source that is required to have a Part 70 permit can operate without a Part 70 permit as long as the source timely submitted a Part 70 permit application that is deemed complete
  Application shield: protects the source from enforcement action while the application is being processed.
  While source can’t be sued if they have an application shield in place, the permitting authority can as the statute states permits must be issued in 18 months
  Minimum requirements. From the source’s perspective getting the application shield can be important and therefore the source has a real incentive to submit a complete and timely submittal.
398

## Slide 399: Permit Application (Cont’d)
Identifying Information (address, contact information, information about emitting equipment)
Emissions Reports (Potential, Actual)
Listing of Significant & Insignificant Activities
Compliance Plan
Compliance Schedule
Compliance Certification
Notes: The application has to contain a lot of information most of it logical.
Insignificant activities per 71.5 c 11 [not in part 70 regs for states]
Insignificant emission levels defined as < 2 tpy criteria < 1000 lbs/yr HAPs
399

## Slide 400: Class Discussion
Is this application complete?
  Certification has been reworded
  NSPS emission unit does not include compliance demonstration method
  Fails to include compliance status of the source with respect to all applicable requirements
  Certification signed by plant manager (definition of responsible official next page)
Notes: No? But if you wait 60 days after receipt it will default to complete
400

## Slide 401: Responsible Official
For a corporation
  Official in charge of a principal business function, e.g., president, vice president, secretary, or treasurer
  Delegation may be allowed if the chosen person oversees
    More than 250 employees; or
    Gross sales or expenditures > $25x106
    and if the permitting agency agrees
Notes: Must be signed, and certified to, by a responsible official
Responsible official means one of the following: (1) For a corporation: a president, secretary, treasurer, or vice-president of the corporation in charge of a principal business function, or any other person who performs similar policy or decision-making functions for the corporation, or a duly authorized representative of such person if the representative is responsible for the overall operation of one or more manufacturing, production, or operating facilities applying for or subject to a permit and either: (i) The facilities employ more than 250 persons or have gross annual sales or expenditures exceeding $25 million (in second quarter 1980 dollars); or (ii) The delegation of authority to such representatives is approved in advance by the permitting authority;
401

## Slide 402: Responsible Official (Cont’d)
For a government agency
  A principal executive officer, or
  A ranking elected official
  For a federal agency, the chief executive officer over a region
For a partnership or sole proprietorship
  One of the general partners, or the owner
Notes: Notice that the definition of a responsible official is very different for government agencies – the big difference is that there is no delegation. Only the top dog can sign.
The same thing is true for partnerships.
For example, an EPA Regional Administrator
In summary, any person that can make business decisions that would affect the entire facility or source.
402

## Slide 403: Title V Permits
PERMIT CONTENT
Notes: 403

## Slide 404: Permit Content Requirements
40 CFR 70.6
Emission limitations and standards
  All applicable requirements
  Origin & authority for each term or condition
Permit duration (usually 5 years)
Monitoring, and related recordkeeping and reporting
  Submittal of required monitoring reports every 6 months
  Include identification of deviations
  Certified by responsible official
  Compliance Assurance Monitoring (CAM) and addressed in a separate lesson
Notes: Deviations e.g., excursions and exceedances
404

## Slide 405: Permit Content (Cont’d)
Prohibition of exceedances of Title IV limits
Severability clause
Permittee must comply with provisions of permit
Need to halt or reduce activity not a defense
Permit may be reopened…for cause
Permit does not convey property rights
Permittee must provide requested information
Notes: Reopen can be by PA or EPA
405

## Slide 406: Permit Content (Cont’d)
Requirement to pay Title V fees
Emissions trading language
Alternative operating scenarios
All documents be signed by a responsible official
Periodic compliance certifications (at least annually)
Various general provisions
Anything else the permitting authority might require
Notes: 406

## Slide 407: Permit Content: Additional Discussion
Credible Evidence rule
  Any credible evidence can be used to show compliance or noncompliance with applicable requirements
  Disallows using only reference test method results to determine compliance or non-compliance
State rule amendments or modifications not yet approved into the SIP
  The applicable requirement is the SIP rule
  The amended or modified state rule is the applicable requirement once the SIP has been revised
Notes: Credible Evidence Rule: Feb ‘97 [e.g., 51.212 (c) and in part 60, 61 and 63
Enforceable test methods for each emission limit specified in the plan. For the purpose of submitting compliance certifications or establishing whether or
not a person has violated or is in violation of any standard in this part, the plan must not preclude the use, including the exclusive use, of any credible evidence
or information, relevant to whether a source would have been in compliance with applicable requirements if the appropriate performance or compliance
test or procedure had been performed.
EPA’s white paper #2 from late 90s talks about state rules not yet in the SIP – state only until added to the SIP
.
407

## Slide 408: Permit Content (Cont’d)
Compliance requirements
  Monitoring, Reporting & Recordkeeping (MRR)
  Right of Entry
  Right to Records
  Right to monitor and/or sample
  Compliance Schedule
  Compliance Assurance Monitoring (CAM)
Notes: Talk about CAM in next lesson
408

## Slide 409: Class Discussion
What is an applicable requirement?
Notes: Applicable Requirement:
All of the CAA requirements applicable to a Title V Source
Common Sources of applicable requirements are:
  SIP
  SIP approved permits previously issued to the source
  Standards promulgated by EPA, e.g.
    NSPS
    NESHAPS
    MACT Standards
    Title IV (Acid rain) provisions
    Title VI (Stratospheric Ozone) provisions
CLEAN AIR ACT SECTION 112(r): ACCIDENTAL RELEASE PREVENTION /RISK MANAGEMENT PLAN RULE
409

## Slide 410: Class Discussion (Cont’d)
Why is the concept of “applicable requirements” important to the Title V Operating permit program?
Notes: A major benefit of a Title V permit is that it combines in a single document all of a source’s CAA requirements in order to eliminate confusion for the source, the public, the permitting authority, and EPA as to what requirements apply.
This benefit is best achieved if:
  The permit does not incorrectly exclude any CAA requirements.
  The permit correctly and completely captures all applicable requirements.
410

## Slide 411: Class Discussion (Cont’d)
Which of the following are applicable requirements?
  A BACT requirement?
  A LAER requirement?
  Terms and conditions of a minor NSR permit?
  A BART requirement?
  A requirement that office air conditioning units be maintained by a licensed technician?
  A state rule?
  A requirement that an affected source operate its CEMs according to the requirements of 40 CFR Part 72?
  A requirement that all asbestos abatement projects meet the requirements of 40 CFR Part 61?
  A severability clause required by Title V of the CAA?
  An NSPS or NESHAP requirement?
  A consent decree order entered into between the state and the source?
Notes: AC units per 71.5 c 11
Asbestos reno exempted
NSPS/MACT unless the reg excludes TV
Typo fix it to its
411

## Slide 412: Class Discussion (Cont’d)
You are drafting a Title V permit for XYZ Corporation. XYZ Corporation timely submitted the application and your agency determined the application was administratively complete.
During your review of the application in preparing to draft the permit, you find that the application states that XYZ Corporation has a boiler that is subject to the Subpart Dc NSPS. However, you find no reference to emission limits or monitoring, record keeping and reporting requirements for the boiler.
What can you legally do?
Notes: Send a request for additional info with a reasonable deadline for response
NB: application defaults to admin complete after 60 days unless the PA notifies the source that it isn’t complete.
412

## Slide 413: Permit Shield
  Permit may include a “permit shield”
    A provision stating that compliance with the conditions of the permit shall be deemed compliance with any applicable requirements as of the date of permit issuance, with certain caveats
    Not mandatory – an option left to permitting authority
    If permit does not expressly state that a permit shield exists, it is presumed not to exist
Notes: What the permit shield does is allow the source to be treated as being in compliance with all applicable requirements
Mag Corp TV example on Cl reduction burner and CL limit, EPA needed to reopen for cause (even thou UT didn’t want to reopen).
413

## Slide 414: Title V Permits
PERMIT ISSUANCE
Notes: 414

## Slide 415: Permit Issuance
40 CFR 70.7
Before a permitting authority can issue a permit, it must have:
    Received a complete application
    Complied with public participation requirements
    Notified, and responded to, affected states
    Included in the permit a requirement that source comply with all applicable requirements and Part 70 requirements
    Prepared a statement of the legal and factual basis for issuing the permit (Statement of Basis or SOB); and
    Provided a copy of the permit application, permit, & SOB to EPA and received no objection to its issuance from EPA
Notes: Reference to Permit Issuance
  40 CFR 70.7
Affected States : State within 50 miles of the source
  State that is contiguous to the state issuing the Part 70 permit whose air quality may be affected by the source
415

## Slide 416: Permit Issuance (Cont’d)
Public Participation requirements
  Notice (Contents specified at 70.7(h)(2))
    Newspaper of general circulation where source is located or in state publication designed to give general public notice, or posted on a public website identified by the permitting agency
    To persons on the Title V mailing list
    To affected states
    Other means necessary to notify affected public
    Other state requirements
Notes: 416

## Slide 417: Permit Issuance (Cont’d)
Public Participation requirements (cont’d):
  Must provide at least 30 days to submit comments
  Must provide at least 30 days notice prior to public hearing
  Must keep record of commenters, and issues raised
  Response to comments
Notes: 417

## Slide 418: Response to Comments
The permitting authority must respond in writing to all significant comments raised during the public participation process, including any such written comments submitted during the public comment period and any such comments raised during any public hearing on the permit.

## Slide 419: Permit Issuance (Cont’d)
40 CFR 70.7(a)(5)
Statement of Basis (SOB)
  Sets forth the legal and factual basis for the draft permit conditions
  Include references to applicable statutory or regulatory provisions
  Send to EPA and anyone requesting it
  Follow your agency policy in regard to Statement of Basis
Notes: Gives justification to all permit conditions and applicable requirements
Show an example TV SOB – Rawhide TRD? Fidlar Comp Station SOB? Call attention to section 4 [regulatory analysis]
Onyx Order
A listing of any Title V permits issued to the same applicant at the plant site
Attainment status
Construction and permitting history of the source
Compliance history
419

## Slide 420: Permit Issuance (Cont’d)
More on Statement of Basis
Should discuss decision-making that went into the development of the permit
  Rationale for selected monitoring methods
  Basis for applying permit shield
  Compliance history of the source
Notes: Again – show example SOBs and Colstrip TV permit

## Slide 421: Permit Issuance (Cont’d)
EPA review of permit (40 CFR 70.8)*
  EPA must be provided a copy of the
    Permit application
    Proposed permit
    Statement of Basis
    See your agency procedure for specific requirements
Notes: Statement of Basis
See handouts in binder
421

## Slide 422: Permit Issuance (Cont’d)
EPA objection
  If EPA objects to the permit within 45 days of receiving all required information, permit cannot be issued
  Permitting authority has 90 days to revise and submit proposed permit, or EPA will issue or deny a permit under Part 71
Notes: 422

## Slide 423: Petitions Requesting EPA Object
If EPA’s Administrator does not object, any person may petition the Administrator within 60 days after the expiration of the Administrator's 45-day review period to make such objection.
The petitioner shall provide a copy of the petition to the permitting authority and the applicant.
A petition shall be based only on objections to the permit that were raised with reasonable specificity during the public comment period, unless the petitioner demonstrates that it was impracticable to raise such objections within such period, or unless the grounds for such objection arose after such period.

## Slide 424: Petitions Requesting EPA Object
If the Administrator objects to the permit as a result of a petition, the permitting authority shall not issue the permit until EPA's objection has been resolved,
  Except that a petition for review does not stay the effectiveness of a permit or its requirements if the permit was issued after the end of the 45-day review period and prior to an EPA objection.
If the permitting authority issued a permit prior to receipt of an EPA objection, the Administrator will modify, terminate, or revoke such permit, except in unusual circumstances. The permitting authority may thereafter issue only a revised permit that satisfies EPA's objection.
Notes: EPA tracks all TV petitions received. If EPA doesn’t act on a petition it can get sued
https://www.epa.gov/title-v-operating-permits/title-v-petition-database
None for CT, NY none currently but has had quite a few in the past (2019); CO has a bunch active right now for NGOs

## Slide 425: Title V Permits
PERMIT
MODIFICATION
Notes: E.g., TN fact sheet on TV mods with examples?
425

## Slide 426: Permit Modification
Three types
  Administrative amendments (AAs)
  Minor Modifications (MMs)
  Significant Modifications (SMs)
Notes: 426

## Slide 427: Permit Modification (Cont’d)
Administrative amendments
  Typos
  Change in name or phone number
  Require more frequent monitoring
  Change of ownership if no other changes
  Other changes approved by EPA as AA
    Case-by-case determination
  No Public notice or EPA review
Notes: 70.7 (d) Administrative amendments
More frequent monitoring? At request of source
60 days for PA to finalize
427

## Slide 428: Permit Modification (Cont’d)
Minor Modifications
  Would not violate any applicable requirement
  No significant changes to MRR conditions
  No impact on MACT, NSPS, AAQS, or PSD increments requirements
  No change to permit term for which source has assumed responsibility to avoid other requirements
  Not a modification as Per Title I
  Not deemed significant by Permitting Agency
Notes: 90 days for PA final action including EPA 45 day review
Needs Cert by Responsible official
“Significant” definition not entirely clear
40CFR 70.7(e)(vi)(4)(i) is ambiguous
Ultimately, and practically, determined by permitting agency
3. Does not require a case-by case determination for an emissions limitation, source-specific temporary ambient impact, or a visibility or increment analysis
4. Limiting landfill gas emissions to less than 50 megagrams per year to avoid PSD, for example.
Generally means no mods under NSPS, NESHAPs, or PSD
Title V sources typically monitor control device operating parameters such as baghouse pressure drop or scrubber flow rate. Minor permit modifications can be used to change the value or range of the monitored parameter (for example, a baghouse can use a minor modification to change the minimum pressure drop).
428

## Slide 429: Permit Modification (Cont’d)
Significant Modification
  Anything that cannot be classified as an Administrative Amendment or a Minor Modification is a Significant Modification
Notes: 70.7 e 4 – public participation, review by EPA etc.
Complete review on the majority of significant permit mods within 9 months after receipt of a (admin) complete application

## Slide 430: Reopening for Cause
  Originated by Permitting Agency or EPA
    Additional applicable requirements
    Material mistakes
    To assure compliance
  Affect only flawed parts of permit
  Procedurally similar to initial issuance
  As expeditiously as possible
CFR 70.7
Notes: 70.7 f
US Mag

## Slide 431: Title V Permits
PERMIT RENEWAL

## Slide 432: Permit Renewal
Generally required every 5 years
Permittee must submit application for renewal at least six months prior to expiration
Renewal process is nearly as extensive as initial issuance
Notes: A state in their Title V Program that is approved by EPA could require the renewal to be done sooner than every 5 years, but in general can’t be more than 5 years.

## Slide 433: QUICK REVIEW TITLE V OPERATING PERMITS
Purpose
Applicability
Permit Application
  Application Shield
Permit Content
  Applicable Requirements
  Permit Shield
Notes: Compile all Applicable requirement: Constriction permits (minor and major) SIP rules, NSPS and MACT, title IV, CDs
Generally Major source >100tpy 10/25tpy HAPs
Application Shield: protects source from enf action while application is being processed. If application is timely and complete.
Permit Shield: What the permit shield does is allow the source to be treated as being in compliance with all applicable requirements
433

## Slide 434: QUICK REVIEW (Cont’d) TITLE V OPERATING PERMITS
Permit Issuance
  EPA Review
  Public participation
  Statement of Basis
Permit revision
Permit Renewal
CAM*
Compliance/Enforcement issues*
* These two topics are covered in other lessons
Notes: EPA 45 day review required for initials, renewals, minor, major mods [not for admin changes]
Both CAM and Compliance/Enforcement topics are covered in more details in other lessons

## Slide 435: QUESTIONS?

## Slide 436: LESSON 15
Monitoring, Reporting and Recordkeeping
Notes: Ted

## Slide 437: Lesson Objectives
Understand reasons for monitoring, reporting and recordkeeping
Determine what types of monitoring, recordkeeping, and reporting are required
Identify who is responsible for monitoring, recordkeeping, and reporting

## Slide 438: Monitoring, Reporting and Recordkeeping
Required for Title V sources
  40 CFR 70.6 (a) (3)
Advisable for all sources

## Slide 439: Why Required?
To ensure continuous compliance with regulations and permit conditions
To ensure proper operation of equipment
  Prime equipment
  Control equipment

## Slide 440: Monitoring Requirements
Based on underlying regulation
Permit should identify techniques to measure emissions from unit
  By source operator
  By inspector
Permit should specify that penalties would apply for failure to monitor

## Slide 441: Emissions Monitoring
Performance testing
  Stack tests
  Extraction tests
  Fuel analysis
Continuous Emission Monitoring
Opacity monitoring

## Slide 442: Parametric Monitoring
Track some surrogate for emissions
  Combustion temperatures
  Boiler exhaust O2 content
  Gas inlet and outlet temperatures
Opacity monitoring
Throughput

## Slide 443: Calculations
Fuel usage
Mass balance
  Coatings utilized
  Raw material

## Slide 444: Monitoring to Ensure Effective Operation of Control Equipment
Bag leak detector on baghouse
Pressure drop for baghouse
Breakthrough detector on carbon bed
Water flow to dust suppression system
Electrical parameters (ESP)

## Slide 445: If No Monitoring Requirements Prescribed in Regulation
Prescribe monitoring based on:
  Previous permit
  Similar facilities
  EPA guidance
  Manufacturer’s recommendation
  Proposal presented by applicant

## Slide 446: Reporting Requirements
Permit should identify specific information that permittee is required to submit
Permit should define schedule for submittals
Permit should specify that penalties would apply for failure to submit reports as prescribed

## Slide 447: What Shall Be Reported?
Reports of any required monitoring at least every 6 months
All instances of deviations from permit requirements must be clearly identified
All reports required by Title V must be certified by a responsible official
Notes: 40 CFR 70.6(a)(3)(iii)(B)
Prompt reporting of deviations from permit requirements, including those attributable to upset conditions as defined in the permit, the probable cause of such deviations, and any corrective actions or preventive measures taken. The permitting authority shall define "prompt" in relation to the degree and type of deviation likely to occur and the applicable requirements.

## Slide 448: Record Keeping Requirements
Identify data and records to be maintained (electronic or paper)
Indicate how records are to be accessible to agency
Indicate how long records are to be maintained
Permit should specify that penalties would apply for failure to maintain records

## Slide 449: What records must be kept?
Title V requires records of required monitoring (advisable for all permits)
    Date, place & time of sampling or measurements
    Date of analyses
    Who performed the analyses
    Identification of analytical methods
    Analytical results
    Source operating conditions during sampling or measurements

## Slide 450: How long must records be kept?
Title V requires:
  Records of all required monitoring data and support information shall be maintained for a period of at least 5 years from the date of the monitoring sample, measurement, report, or application.
Notes: This is what the permit should require the permittee to do
It is advisable that the agency retain certain records indefinitely, as mentioned in lesson 10 - Documentation

## Slide 451: Class Discussion
Are there circumstances where no monitoring, recordkeeping or reporting are required?
Notes: If there is no monitoring included in the permit for a particular emission limit, or the monitoring
appears to be inadequate,
Check the Statement of Basis and review the permitting authority’s documentation of
their periodic monitoring evaluation. The Statement of Basis may show that the source
is able to assure compliance with the emission limit without monitoring:
An engineering evaluation may show that the source would not exceed the
emission limit under its anticipated range of operations.
If this demonstration is made, any assumptions included in the demonstration (for example, type of fuel
that will be combusted) must be enforceable permit terms.

## Slide 452: QUESTIONS?
Notes: 452

## Slide 453: LESSON 16
453
Compliance Assurance Monitoring
(CAM)
Notes: Carl
CAM mentioned in the TV permit lesson
Goal is to get source to closely observe subject control devices and make sure they are operating properly.
This lesson is an overview of CAM, LMS has a one day course on CAM (PERM204) which goes into a bit more detail on CAM
Colstrip TV with CAM plan Appx I

## Slide 454: Lesson Objectives
Explain legal basis for CAM
Review CAM applicability
Define CAM requirements
Discuss source, agency and EPA roles
Discuss Quality Improvement Plans
454
Notes: Part 64 , not too long for a CFR Part
NY DEC 201-6
QIP = quality improve plan
This lesson is just an overview of CAM as many TV permits don’t need CAM, but just an explanation in the SOB on why CAM doesn’t apply

## Slide 455: CAM Background
CAA Origins: Titles V & VII
Promulgated 10/22/97; codified in 40 CFR Part 64
Regulation implementing the Title V monitoring principle:
  “…monitoring sufficient to assure compliance”
455
Notes: - origins in Title V and VII of CAA
- Title V: directs EPA to implement monitoring and compliance certs through T5 program
- Title VII: 114(a)(3) requires EPA to promulgate rules on EM and compliance certs
- long rulemaking process began in 1991 ruled issued in 1997
- T5 principle: monitoring sufficient to assure compliance
Show EPA web site: https://www.epa.gov/air-emissions-monitoring-knowledge-base/compliance-assurance-monitoring

## Slide 456: CAM Background (Cont’d)
Targets facilities with add-on control devices
"assure that control measures...are properly operated and maintained so that they do not deteriorate to the point where the owner/operator fails to remain in compliance...“
"long-term, significant loss of control efficiency that can occur without complete failure of a control device"
Notes: - more on control devices shortly
- 27,000 CAM EUs nationwide
- preamble quotes 1997:
CAM seeks to "assure..."
Part 64 addresses the "long-term...“
To prevent sources from shutting down control devices

## Slide 457: Some New Concepts
Pollutant Specific Emissions Unit (PSEU)
Pre-control Potential to Emit
Exceedance
Excursion
Notes: - PSEU: EU considered separately with respect to each regulated pollutant (vs. PTE of source; e.g. boiler = several PSEUs NOx, SOx, CO, PM)
- pre-control: same as PTE except emission reductions achieved by control device not taken into account, even though source allowed to under regulatory definition of PTE.
We CAN take into account other emission reduction methods: e.g. operating hour and throughput limits
Excluding control device efficiency allows us to distinguish between units based on true size and degree of control required to achieve compliance, i.e. environmental significance

## Slide 458: Exceedance vs. Excursion
Exceedance
  A condition whereby emissions (or opacity) are greater than the applicable emission limitation or standard (or less than the applicable standard in the case of a percent reduction requirement)
Excursion
  A departure from an indicator range established for monitoring
Notes: Exceedance: More significant than Excursion, where monitoring (e.g., using CEMs) show permit emission limit exceeded
- Excursion: departure from indicator range established by CAM (consistent with averaging time specified for averaging the results of the monitoring), i.e. recording temperature outside range allowed by permit
- Excursion: although staying within appropriately established indicator ranges gives a reasonable assurance of compliance, excursions from indicator ranges do not necessarily indicate noncompliance with an emission limit

## Slide 459
PSEU
Control
Device
Pre-controlled
Emissions
Annual emissions = Control Device X Emission Rate
Post-control
Emissions
Pre-Control Emissions

## Slide 460: CAM Applicability (§64.2)
an emission unit (except some backup utility power emission units) AND
with a control device AND
with pre-control emissions greater than major source thresholds AND
with an emission limit (see exceptions) AND
at a major source subject to title V permitting
Notes: Boiler at a major TV source – with baghouse – and has pre-control PTE > 100tpy [or 10/25tpy HAP] – and the pollutant (PM) has an emissions limit
Applies to individual emission units, not facilities

## Slide 461
Notes: - Aid for sources: Do they need to include a CAM plan in their TV application and when, not something the permit authority prepares but does review and approve. good visual aid
- briefly review applicability
- careful with exemption part in lower left...exempt limit does not mean PSEU automatically exempt from CAM
Handout

## Slide 462: Fugitives Counted as in Title V Applicability
Not counted in pre-control PTE unless source belongs to one of 28 listed source categories in definition of "major source" in Part 70 (§70.2)
Fugitives are included when calculating HAP PTE
If counted in title V applicability determination, counted towards PSEU PTE.
Notes: Usually fugitives VOCs from valves, flanges etc on their way to a incin or combustion control device. Could also be PM on way to a baghouse or ESP
For criteria pollutant major source determination, fugitive criteria pollutant emissions are not counted towards the applicability for Title V, unless the source is one of the 28 listed sources. However, for HAP major source applicability determination, fugitive HAP emissions are counted. Once a source has been determined to be a major source subject to Title V, then all fugitive emissions are to be included in the permit and counted towards each PSEU which emits the fugitive emissions.

## Slide 463: Definition of Control Device
Equipment used to destroy or remove pollutants
  end of pipe controls: scrubber, ESP, baghouse, catalyst, incinerator
  in-process controls where treatment can be adjusted to control emissions: steam/water injection on turbines, FGR for boiler
Notes: Add on controls: Baghouse, SCR, Thermal oxidizer
LNBs, Fluidized bed would not be in process controls

## Slide 464
Steam/Water Injection
Example of Control Device
Notes: Not as obvious as an end of pipe APCE

## Slide 465: Control Devices (Cont’d)
Control Devices Do NOT Include:
  Combustion or other process design features, e.g. low NOx burner (LNB)
  Passive control measures, e.g. seals, lids, low-polluting fuel

## Slide 466: CAM Exemptions
CAM NOT triggered by:
  Post-1990 NSPS and NESHAP emission limits
  CFC rules
  Acid Rain requirements
  Emissions trading programs
  Emission caps
  Title V permit requires continuous compliance determination method
Notes: This is why many TV sources are now not subject to CAM - post 1990: EPA is committed to developing new emission standards in NSPS and MACTs that specify continuous compliance determination methods whenever possible. EPA has encouraged states to follow this same approach, and therefore does not believe that CAM will have a significant impact on requirements imposed subsequent to the 1990 Amendments.
Last bullet: if permit requires a CEM for some other reg or requirement that would get the PSEU out of CAM (for that pollutant only).

## Slide 467: Exempt Limit, not PSEU
Exemption does not apply to other limits on same PSEU
No additional monitoring for exempt limit
But monitoring for exempt limit may satisfy CAM for non-exempt limit
Example: Using installed “CEMS” to satisfy monitoring requirement
Note: Must be stated in CAM plan!
Notes: - acid rain: requirements pursuant to title IV of CAA. So AR emission limits can't trigger CAM. However, this does not mean that AR units automatically exempt. PSEU could be subject to CAM as a result of another emission limit, e.g. BACT or LAER for NOx.
- satisfies CAM: e.g., MACT can’t trigger CAM. When MACT requires VOC or particulate control and criteria pollutant is a VOC or particulate. Source must indicate in app whether MACT monitoring satisfies CAM for non-exempt limit , or propose additional monitoring
E.g., refinery with CEMs on PSEUs stacks/vents for some reason then that can cover CAM for all limits that PSEU is subject to.

## Slide 468: Continuous Compliance Determination Methods
CEMS is subset - could also include PEM*
PSEU with CEMS not automatically exempt
  only if Title V permit specifies as compliance determination method
  if not exempt, CEMS is CAM monitoring
CEMS not required if not already present
* Predictive Emissions Monitoring
Notes: PEMS: software analyzers able to provide a reliable real-time estimation of emission properties by means of a model, which uses process values (e.g. temperature, flow, pressure) as input variables.
- PEMS must be used to determine compliance, not assure compliance
- PEMS must be correlated to the standard
Just like CEMS, PEMS have a Performance Specification in Part 60 Appx B: 16—Specifications and Test Procedures for Predictive Emission Monitoring Systems in Stationary Sources
- example of EUs with CEMS that are subject: most NSPS require CEMS, but not for compliance determination
- comparison to illustrate the difference: big cogens where NSR permit, and therefore the T5 permit, require CEMS as compliance determination method, so exempt. BUT: PSD synthetic minors, for example IC engines emitting 150 tpy NOx,, that have SCR and need a CEMS to operate properly, CEMS may not be required as compliance determination method, so PSEU is subject to CAM.

## Slide 469: Exemption for Backup Utility Power EUs
Municipally owned AND
Exempt from Part 75 monitoring requirements AND
Peaking unit throughout Title V permit term AND
Actual emissions over last three years are <50% of major source threshold
Notes: - peaker and actuals: and expected to remain so
- EPA estimates that majority of backup utility power units under 25 MW will qualify
Part 75 acid rain CEMs regs

## Slide 470: Source's Role
Develop and propose monitoring in permit application (CAM Plan)
Monitoring in CAM Plan must "provide a reasonable assurance of compliance" to provide a basis for certifying compliance with applicable requirements for PSEUs with add-on control devices
Notes: Show CAM plan [Colstrip Appx I] in a bit along with CAM PCs in the TV permit
EPA has issued CAM guidance that has a template for sources to follow, the example I’ll show follows that template

## Slide 471: CAM Monitoring Design Criteria (§64.3)
Select representative control device operational parameters
Establish indicator ranges for reasonable assurance of compliance - a single maximum or minimum value or multiple values
Ranges based on source testing ((§64.4(c)(1)))
Notes: - CAM says that monitoring must meet certain design criteria
- parameter examples: temperature for afterburner for RTO, flow and pressure drop for PM scrubber, electrical voltages in ESP
- more than one parameter may be required for monitoring sufficient to assure compliance (depends on margin of compliance, pollutant, and type of control device ). e.g.: for VOC capture and destruction system, need to monitor temperature and an indicator for the quantity of gas collected such as fan amps or rpm.
- ranges: can supplement source test data with engineering assessments and manufacturer’s recommendations to justify the indicator ranges (or, if applicable, the procedures for establishing such indicator ranges) (§64.4(c)(1))

## Slide 472: CAM Monitoring Design Criteria (§64.3) (Cont’d)
Specify how data to be obtained, e.g. location of pressure drop gauge
Verification procedures for new or modified equipment
Quality assurance and control practices to ensure validity of data
Frequency of monitoring
Notes: - verification: procedures to confirm the operational status of the monitoring prior to date source must conduct monitoring, e.g. how to verify that a new pressure drop gauge is working properly - use mfg. recommendation
- QA/QC: all about monitoring devices, e.g. source could demonstrate that control device OK if COMS says 10% opacity, even if limit is higher

## Slide 473: Frequency of Monitoring (§64.3)
Sources should account for typical variability of the PSEU (including the control device and associated capture system)
"Such intervals shall be commensurate with the time period over which a change in control device performance that would require actions by owner or operator to return operations within normal ranges or designated conditions is likely to be observed."
Notes: 64.3 monitoring design criteria
- In designing period over which data is obtained...
- on the issue of frequency, the rule states:

## Slide 474: Frequency of Monitoring (§64.3) (Cont’d)
"Large" PSEUs
  for each parameter, collect four or more data values equally spaced over each hour
"Other" PSEUs
  some data collection at least once per 24-hour period
Notes: Large PSEU Controlled PTE > major threshold (100tpy)
b 4 ii and iii
In reality with today’s digital data collection will likely collect data much more frequently

## Slide 475: Evaluation Factors for CAM Account for site-specific factors
Applicability of existing monitoring equipment and procedures
Ability of the monitoring to account for process and control device operational variability
Reliability and latitude built into control technology
Level of actual emissions relative to emission limits
Notes: - variability, e.g., baghouses deteriorate slowly, so source can detect failure with less frequent monitoring [using Triboelectric detectors]
- variability, e.g. source initially wants to use manufacturer's specs but knows that they weren't appropriate for EU for some reason (e.g., the control device was overbuilt for the unit)
- reliability/latitude, e.g. ESP overbuilt for EU, so more latitude in parameters that would assure compliance. Conversely, less latitude if underbuilt
- margin of compliance: if high variability in emissions and close to the standard, we must factor this information into monitoring decision and not just rely on the parameter ranges measured during a single best-case source test. In this scenario, more frequent monitoring or more things to monitor if close to limit. Conversely, if actuals are 1/4 or 1/2 of limit, wider parameter range or less frequent monitoring assures compliance. Nothing new in CAM about this concept.

## Slide 476: What does a source do with monitoring results?
Report deviations, excursions, and exceedances in semi-annual monitoring reports
  date and duration
  nature of corrective action
Certify compliance status for each applicable requirement
  can cross-reference to semi-annual monitoring reports and other reports (e.g. to identify excursions)
Notes: As part of TV semi-annual reporting – CAM plan will be included
Defined Excur and exceed earlier: excursion is beyond the performance indicator range (but may not be violation of an emission limit), exceedance could be a violation of an emission limit

## Slide 477: Agency Role Evaluate source's CAM plan
If submitted plan is INADEQUATE
  Confer with source regarding needed changes
  Disapprove submitted plan
    Formal notice of disapproval
    Request revised plan by date certain
    Draft or Final permit must include periodic monitoring
    Compliance schedule in permit
Notes: - compliance schedule must require source to submit revised monitoring to PA within 180 days from date of issuance of draft or final permit
- SOB/TSD:: Need not be lengthy. If CAM doesn't apply, state why. If it does, specify units and describe what PA determined, e.g. negotiated with source, or incorporated as is
the periodic monitoring requirements are contained in 40 CFR, sections 70.6(a)(3) and 71.6(a)(3)
EPA issued guidance on PM in 1998 but because of a 2002 court case it can no longer be used (but it is available to review)

## Slide 478: Agency Role Evaluate source's CAM plan (Cont’d)
If submitted plan is ADEQUATE
  Approve Plan
    Agency may condition approval on source gathering more data on indicators
  Include provisions of CAM in permit and in Statement of Basis
  If testing or equipment installation required, permit must include enforceable schedule with milestones
Notes: - confer: such gap-filling not in rule, but discussed in preamble
- If testing or equipment installation required, permit must include enforceable schedule with milestones. Monitoring must implemented as expeditiously as practicable but no more than 180 days after PA issues permit
- PA does NOT have to revise permit to put in newly established or reestablished indicator range IF the permit has a replicable procedure used to establish or reestablish range. Good approach, but puts a lot of burden on the permit writer (lot of work). If permit does not have replicable procedure, mod required
- for MY info only: example of NESHAP-like replicable procedure: NESHAP directs source to do a source test under certain operating conditions. The parameter range to be monitored to assure compliance is that range which is monitored during the source test (usually with +/- some value like 10%). The source has to document that the test was conducted in accordance with the requirements spelled out in the rule and they have to document the ranges monitored during the test.

## Slide 479: Agency Role Issue final permit that includes
Indicators to be monitored
Means or device(s) used to measure indicators (e.g. temperature measurement device, VE, CEMS)
Performance requirements
Definitions of exceedance or excursion
Obligation to conduct monitoring, reporting and recordkeeping, Implement QIP if required
Notes: - Performance Criteria, i.e. what we discussed earlier: how data to be obtained, verification for new/mod sources, qa/qc, frequency
- permit should specify level at which excursion or exceedance deemed to occur
- repeat definitions: excursion is departure from indicator range, exceedance is potential violation
- for excursion from range, permit may include either specific value(s) or condition(s) at which an excursion shall occur, or the procedures used to establish that value or condition
- recordkeeping: comply with requirements of 70.6; alternative media (scanned docs, microfiche) may be used in lieu of paper records
QIP = 64.8 Quality improvement plan (QIP) requirements.
Will talk about QIPs in a moment

## Slide 480: Agency Role Compliance Certification Condition
Part 70 (§70.6(c)(5)(iii)) revised when Part 64 promulgated
Certification conditions must “…identify as possible exceptions to compliance any periods during which compliance is required and in which an excursion or exceedance as defined under part 64 of this chapter occurred.”
Notes: Added CAM obligation to certification

## Slide 481: EPA Role
Same as with periodic monitoring or other title V monitoring
Review permits to determine if monitoring is sufficient to assure compliance
Notes: If asked: guidance on TTN
EPA can object or respond to a petition on the TV permit based on CAM plan
So robust SOB is important

## Slide 482: Quality Improvement Plan (§64.8)
Agency or EPA can require
Permit may specify appropriate threshold, such as an accumulation of exceedances or excursions exceeding 5% of PSEUs operating time
Implementation of QIP does not shield source from noncompliance with emission limit
Notes: - PA/EPA can require QIP if it believes source's response to pattern of exceedances or excursions inadequate
- R9 generally expects sources to be able to demonstrate compliance more than 95% of the time.
- Numerous NSPS cases have been filed and settled for sources at better than 95%
- Example: Public Service Co. of CO sued by Sierra Club, went to court and lost summary judgement even though source was out of compliance for opacity only 2.1% of time
- QIP: optional tool, not required in CAM plan

## Slide 483: Quality Improvement Plan (§64.8) (Cont’d)
Written QIP available for inspection
Evaluate performance problems, and then
Modify QIP to include
  improved preventive maintenance practice
  process operation changes
  improvements to control methods
  more frequent or improved monitoring

## Slide 484: PM Control - Facility X
Baghouse
PM emission limit: 0.1 gr/dscf, 3-hr average
See Table – Next slide
Notes: Example: PM from some old NSR permit of old SIP rule that doesn’t have adequate monitoring and reporting [such as a one time stack test]
Grains per dscf

## Slide 485: Facility X
Indicator | Measurement Approach | Indicator Range | QIP Threshold
VE | Daily VE Survey | Presence of VE | 5 excursions in 6 months
Pressure Drop | Differential Pressure Gauge | Pressure drop >5 in. H2O | None selected
Notes: Could also have a min delta P on the range

## Slide 486: VOC Control - Facility Y
Thermal Oxidizer (incinerator)
VOC emission limit: 95% control
See Table – Next slide
Notes: Again from some ancient permit or rule

## Slide 487: Facility Y
Indicator | Measurement Approach | Indicator Range | QIP Threshold
Chamber Temperature | Thermocouple | ≥1500 degrees F | 7 excursions in 6 months
Work Practice | Burner Inspection and Maintenance | Failure to do annual maintenance or daily flame observation | None selected
Notes: Failure to due daily flame obs is an excursion not an exceedance but an exceedance could occur

## Slide 488: Enforcement Authority §64.7(d)
"Upon detecting an excursion or exceedance, the owner or operator shall restore operation of the pollutant-specific emissions unit (including the control device and associated capture system) to its normal or usual manner of operation as expeditiously as practicable in accordance with good air pollution control practices for minimizing emissions."
Notes: - enforcers in audience?!
- This is the additional layer of enforcement authority CAM gives EPA and PAs (in addition to what we already have, i.e. enforcing the underlying limit).
- Means you can go after source for not operating control device properly, even if there isn't evidence to prove a violation

## Slide 489: Relationship of CAM to Other Title V Monitoring
PSEUs not subject to CAM are subject to periodic monitoring
Periodic monitoring similar but less detailed approach than CAM
Periodic monitoring could be used to develop data to support proposed CAM plan
Notes: - PM applies to greater universe of sources since CAM can only apply if control device: e.g. VE on EU without control or not subject to CAM
- so can have CAM and PM for different pollutants on same EU. Example: kiln at cement plant, CAM for PM-10, PM/other T5 monitoring for NOx & SO2
- PM less fleshed out in a regulatory way than CAM
Periodic monitoring requirements contained in 40 CFR, sections 70.6(a)(3) and 71.6(a)(3)

## Slide 490: Review of Key Concepts
CAM can only apply if PSEU has control device
New concepts in CAM
  pre-control PTE
  PSEU
  excursion and exceedance
Data collection to ensure control device operating properly
  sources that don't address problems subject to enforcement
Notes: - end of pipe or in-process, not combustion or other process design features
- pre-control: emission reductions achieved by control device not taken into account. We're not used to looking at uncontrolled emissions.
- PSEU: EU considered separately with respect to each regulated pollutant (vs. PTE of source)
- Excursion: departure from indicator range established by CAM (consistent with averaging time specified for averaging the results of the monitoring), i.e. recording temperature outside range allowed by permit
- Excursion: excursions from indicator ranges do not necessarily indicate noncompliance
- Exceedance: condition detected by monitoring that provides data in terms of an emission limit that indicates that emissions (or opacity) are greater than the limit (or less in case of percent destruction requirement, i.e. a potential violation

## Slide 491: QUESTIONS?
Notes: Show Colstrip TV permit (page 20 and CAM plan (page 95)
CAM TGD page 254 is for PM control with venturi scrubber
Chipita SOB page 8 more likely for most permit writers

## Slide 492: LESSON 17
Permit Conditions
Notes: Ted
Discuss the different types of PC and what constitutes necessary and appropriate PCs
Since text on a slide isn’t the necessarily the most clear way to show that I will show some example permits I have worked on – true minor NSR, syn minor and TV.
And then we have a sample PC handout to go through to decide whether or not a PC is well written

## Slide 493: Lesson Objectives
Understand the need for permit conditions
Examine the various types of permit conditions
Learn how to prepare effective permit conditions
Notes: 493
Here are our objectives. Very obvious and straight forward.
This applies for both construction and operating permits major and minor

## Slide 494: Permit Conditions
Crucial component of permit
Define terms of permit “contract”
Tell permittee:
  What is allowed
  What is prohibited
  What is required
  When it is required
Notes: 494
Must be in understandable, unambiguous language
Intent needs to be stated – at least in support document
Basis or reason for condition m
Permit writers must collaborate with inspectors on expectation. This is very important and often not done. Here I don’t think you have this problems since the permit writer and compliance inspector are the same.

## Slide 495: Permit Conditions (Cont’d)
Necessary to:
  Ensure compliance of all emission units
  Provide operating requirements, information and limits to
    site personnel
    agency inspectors
Notes: 495
Here is why we need conditions. Conditions also provide the legal basis for any enforcement that may be needed.

## Slide 496: Basis for Permit Conditions
Applicable regulations
Compliance demonstration
Threshold management
Record keeping & reporting
Others?
Notes: 496
We have to have a basis for conditions. Here are some – applicable regs are clear we have to specify conditions needed to meet regs – conditions will be formed by the regulations. We need a permit condition to tell us how the source will demonstrate compliance and how to keep below thresholds what kinds of record keeping is needed. Can anyone come with other reasons for conditions?
Threshold management = syn minor
Consent Decree, settlement decree, court order

## Slide 497: Basis for Permit Conditions (Cont’d)
Basis for each condition should be stated in:
  Permit
  Review document
  Engineering analysis
  Statement of basis
Notes: 497
We need to spell out each permit condition and why we have it
SOB = TSD = TRD = Engr Review

## Slide 498: Permit Conditions (Cont’d)
Must be enforceable
  For Title V permits, conditions must be “federally enforceable”
  All conditions must be practically enforceable
Notes: 498
Permit conditions must be practically enforceable, that is, they must make it possible to determine whether a plant is complying with the rules. The permit must clearly explain how the requirements apply to the facility. If you cannot tell what the facility is required to do to comply with permit limits, it is not practically enforceable. With limited exceptions, a facility must comply with regulations at all times. The public may use any credible evidence to show a facility is violating its permit. Evidence may include air sampling tests taken at the property line of the facility.
BLUE RIDGE ENVIRONMENTAL DEFENSE LEAGUE Clean Air Campaign
Clean Air Act Title V Permits BREDL Fact Sheet

## Slide 499: Permit Conditions Enforceable / Credible Evidence
Practical Enforceability
  No calendar year limits
  Long-term limits based on 12 month rolling sum
  Operation of required control equipment
Credible evidence
  Permit conditions cannot limit information
  Nothing in permit precludes use of any credible evidence
Notes: Avg time lesson: no calendar yr limit, use 12-month rolling
Credible evidence rule: can be used by the public/env groups

## Slide 500: How many conditions?
No single “right” answer
No more than are necessary
Need to examine need for each condition
Better to divide complex conditions
Omit conditions that are redundant, unauthorized, or unnecessary
Notes: 500
Conditions should be grouped in a logical manner
There may be lots or only a few

## Slide 501: Categories of Permit Conditions
Standard conditions
Emission limits
Compliance demonstration
Other conditions
Notes: 501
These are some of the categories of conditions. Generally conditions are organized into these groups or similar groups

## Slide 502: Standard Conditions (Boilerplate)
Conditions in every permit
Language reviewed many times
Generally not revised by permit writers
May differ by type of permit
May differ by type of emission unit
Notes: 502
Standard conditions could be placed in the same place in each permit
These may be lengthy
Vary from authority to authority

## Slide 503: Standard Conditions (Cont’d) (Boilerplate)
What boilerplate does your agency use?
Notes: 503
Ask for examples from class

## Slide 504: Standard Conditions - Examples
Effective and expiration dates
Operator Training
Excess emission reporting
Transfer of permit
Severability
Right of entry
Notes: 504
More examples
  Availability of permit
  Notification requirements
  Upset/Breakdown provisions

## Slide 505: Emission limitations
Related requirements must also be specified as conditions
  Averaging time
  Testing requirements
Notes: 505
Basis for permit conditions which limit emissions need to be documented
  Regulatory requirements (cite reg.) NSPS MACT SIP
  BACT/LAER issues
  Offsets
  Netting
Interaction with
  Compliance demonstration
  Monitoring, Reporting, Record-keeping

## Slide 506: Compliance Demonstration
What must the permittee do to demonstrate continuing compliance?
  Inspect
  Maintain
  Test
  Monitor
  Keep records
  Report
Notes: 506
These can include lots of different approaches. Be consistent and make sure all are needed. More and more going to electronic records so specific if paper if needed

## Slide 507: Compliance Demonstration (Cont’d)
Periodic Visible Emission Evaluations (VEE)
Certified VEE observer on staff
Stack tests
Operation and Maintenance (O & M) logs
Notes: 507
If you put opacity into permit you (along with the source) will decide how often and whether the source needs to have a certified observer on site. I always tried to avoid this.
Also consider the need for method 9 vs 22 and if VE makes sense i.e. Florida presses

## Slide 508: Miscellaneous Statements
Generally advisory conditions
Examples
  Steps to revise emission limits
  Notice to permittee that regulation revisions may result in reopening of permit
  Definitions and abbreviations
Notes: 508
Although these may be advisory they can be important

## Slide 509: Problem Conditions
Redundant
Conflicting
Vague or ambiguous
Unenforceable
Notes: 509
Emission limits without averaging times
No milestones for future compliance requirements
Require source to do something they can’t do – fix a malfunction immediately
Testing requirements without methods specified
Unenforceable conditions include test at capacity
Examples to follow

## Slide 510
Sample Permit Conditions – ​
Well Written or Not? ​
​
See Handout​
Notes: First show EPA web page with permit links – true minor NSR, syn minor, TV
Note statement about protecting NAAQS
Note explanatory statements
Am Gilsonite true minor
Salvador Central Syn Minor – establish syn minor limits 1.5tpy CH2O, 38tpy CO,
Chapita Compressr Station TV – note explanatory statements

## Slide 511: QUESTIONS?
Notes: 511

## Slide 512: LESSON 18
Permitting Aspects: New Source Performance Standards (NSPS) & Hazardous Air Pollutants (HAPs)
Notes: Carl
Like several of the other lessons NSPS and Toxics may not seem to have much to do with permitting [as they are self implementing] but they are necessary to understand what they are and are not since they form the basis for many of the emission limit you will set.
NSPS and MACT will show up as applicable requirements. Also, sources may want syn minor permits or FESOP permits to get out of TV permits for HAPs.

## Slide 513: Lesson Objectives
Review basics of New Source Performance Standards and MACT programs
Review basics of toxics issues associated with permitting
Notes: We will look at where NSPS and HAP standards come from and how they influence permitting – syn minor and TV
Show 40 CFR 60, 61 and 63 – naming convention A AA, triple A, quad A , 5 As, 6 As and on

## Slide 514: Why Discuss Emission Standards in Permitting Course
NSPS, NESHAP, and MACT standards form a baseline for many emission limits
Also gives minimum recordkeeping and reporting requirements
Being subject to a standard can bring in permit requirements
Notes: Since NSPS and NESHAP/MACT regs are self implementing, seems like a good question but since many permits nowadays will contain some version of an NSPS etc. it makes sense to understand where they come from.
NSPS/MACT can trigger TV
Sources may want syn minor permits for HAPs to get out of TV

## Slide 515: Acronyms
New Source Performance Standards (NSPS)
National Emission Standards for Hazardous Air Pollutants (NESHAP)
Maximum Achievable Control Technology (MACT)

## Slide 516: New Source Performance Standards
CAA Section 111 and 129
Requires EPA to establish federal emission standards
Intended to promote use of best technologies
Since 12/71 – ~105 NSPS adopted
Codified in 40 CFR Part 60
516
Notes: Standards of performance for new stationary sources reflect the best level of control technology for a source category. Supposed to be reviewed every 5 years but generally are not or at least not modified. For example it took gas turbines were not changed for 27 years [‘79 – ’06] even though due to MACT etc. made the NSPS reasonably irrelevant
BSER vs BACT
Sector wide vs specific unit
Show CFR Part 60 – from Subpart A [general provisions] to UUUU [GHGs for EGUs]
Common examples: D(abcd) [steam generating boilers, F [cement plants], J/Ja [refineries], GG [older turbines] IIII, JJJJ

## Slide 517: NSPS (Cont’d)
Part 60 also contains “guidelines” for some existing sources – mainly waste incineration
Notes: Sec 129 covers solid waste and includes some existing sources. Sec 111d covers existing sources emitting pollutants that are not covered by ambient standards. The first of these was for fluorides from aluminum plants. EPA has proposed the utility ghg standard under this rule.
Also OOOOc (oil and gas production CH4) and (UUUUb EGU GHGs) has guidelines for existing sources – under 111d

## Slide 518: NSPS Format
Applicability
  Typically apply to larger equipment
Emission Standards
  May be less stringent than your agency’s
  May not include standards for all pollutants
Testing and monitoring provisions
Special provisions or requirements may be different than your agency’s
Some NSPS standards are “ancient”
518
Notes: Standards can be old, focus in general on larger sources. Contain record keeping and emission limits. May be less stringent or different than state standards for same sources. Sources have to meet both sets of standards.
For example CA have ACT standard for IC engines greater than 50 hp. Emissions limits are equal to or greater then NSPS IIII but NSPS starts at 25 hp and has different maintenance requirements.
By ancient we mean that some NSPS like the one discussed next go back over 40 years.
MRR >1990 means exempt from CAM

## Slide 519: National Emission Standards for Hazardous Air Pollutants
Originally required by 1970 Clean Air Act Amendments
  Section 112
Hazardous Air Pollutant:
  “…reasonably anticipated to increase mortality or cause a serious illness.”
Codified in 40 CFR Part 61
Notes: 1
1
1
The health effect mandate is the most complicated part of this requirement.
Show CFR Part 61
A to FF [benzene waster ops]

## Slide 520: NESHAPS (Cont’d)
1973
  Asbestos
  Beryllium
  Mercury
1984
  Vinyl chloride
  Benzene
  Radionuclides
  Arsenic
  Coke oven emissions
Notes: Obviously not very much done but not really EPA’s fault. The fact EPA had to prove health effects was a problem. Many of the pollutants of concern had health effects that were similar to other pollutants and EPA could not prove each pollutant as required.

## Slide 521: METHODOLOGY WAS SLOW AND CONTROVERSIAL
Toxic list contains “approximately” 186 to 190 compounds
A better way to address toxic air emissions needed to be developed
EPA decided to move to a “control based method”
Hence the MACT program was developed
EPA did not have the “statutory ability” to implement the MACT program under the 1970 CAA
CAA was “opened” by Congress to make additional authority to implement this program.
Notes: Slow to develop to fill the gap “MACT floor was established” should be about here for sources subject to MACT during the GAP MACT could not be less stringent than the MACT floor
MACTs are control based the become NESHAPS so NESHAS may be performance based or control based

## Slide 522: Maximum Achievable Control Technology
1990 Clean Air Act Amendments
Emission limits based on the best demonstrated technology or practices in similar sources
Codified in 40 CFR Part 63
Notes: MACT applies to new and existing sources.
Show CFR Part 63 – A to HHHHHHH [7 Hs] PVC production
Examples: CC/UUU [refineries, O [EtO sterilization facilities], YYYY [combustion turbines], ZZZZ RICE, UUUUU [MATS for power plants]
NB: Term NESHAP can refer to regs in part 61 or 63, but MACT means regs in part 63

## Slide 523: MACT For New Sources
The emission limit which:
  is not less stringent than that achieved in practice by the best similar source
  reflects the maximum degree of reduction, taking into consideration
    the cost of achieving such emission reduction
    any non-air quality health and environmental impacts and energy requirements
Notes: 41
This is where the MACT comes from. EPA has little discretion in how to set the standard. The degree of specification has allowed EPA to set a very large number of standards in a relatively short period of time.

## Slide 524: MACT for Existing Sources
The emission limitation reflecting the maximum degree of reduction in emissions considering
  the cost of achieving such emission reduction,
  any non-air quality health and environmental impacts, and
  energy requirements.
The limit must be
  achievable by sources in the category of stationary sources, and
  not be less stringent than the MACT floor.
Notes: 41
Whats the MACT floor? Next slide

## Slide 525: MACT Floor
For new sources
  The emission limitation achieved in practice by the best controlled similar source.
For existing sources
  For source categories with > 30 sources: MACT is the average achieved by the best 12% of the sources, excluding those recently equipped with MACT.
  For source categories with < 30 sources: MACT is the average achieved by the best performing five sources.
525
Notes: 41
US Mag universe of one source

## Slide 526: Example MACT Standards
Ferroalloy Production
Flexible Polyurethane Foam
Oil & Natural Gas Production
Portland Cement
Cellulose Production
Large Appliance Coating
Lead Acid Battery Mfg
Petroleum Refineries

## Slide 527: Example MACT Standards (Cont’d)
Primary Aluminum Production
Pulp and Paper Production
Wool Fiberglass Manufacturing
Sewage Sludge Incinerators
Tire Manufacturing
Metal Coil Coating
Natural Gas Transmission
RICE
Notes: MATS is the MACT for EGUs

## Slide 528: A WORD ABOUT “RESIDUAL MACT”
A “control based” technology has it’s advantages but it also has some inherent disadvantages
Advantage: A relatively fast way to reduce the amount of toxic emissions being emitted by regulated sources
Disadvantage: A threat to human health and the environment may still remain
Notes: Risk and Tech Review RTR: every eight years after setting the MACT standards, the Clean Air Act requires that EPA review and revise the standards, if necessary, to account for improvements in air pollution controls and/or prevention.
Just like EPA is supposed to review and revise NAAQS every 5 years

## Slide 529: “HYPOTHETICAL EXAMPLE”
Example I: A source that emitted 100 tpy of a regulated HAP implements the MACT for its source category resulting in a 90% reduction of the HAP and reducing its HAP emissions to 10 tpy
Example II: A facility in the same source category has pre MACT emissions of 1000 tpy of the same HAP, therefore reducing its emission levels to 100 tpy

## Slide 530: “RESIDUAL MACT” (Cont’d)
At a level of 100 tpy a real threat to human health and the environment may remain
Hence “Residual MACT”
Refinery – fence line monitoring
Stay tuned for others
Notes: Residual risk is just getting started. EPA has begun to propose residual risk for some source categories. There are 5 or 6 out for proposal now
MACT CC/UUU [for refineries]

## Slide 531: Reclassification of Major Sources as Area Sources
May 1995 EPA Memo (John Seitz), “PTE for MACT Standards – Guidance on Timing Issues”, AKA Once In Always In (OIAI)
Major sources of HAPs on first significant compliance date of a major source NESHAP, must “permanently” comply with the standard, and thus be also subject to Title V.
Notes: 1
1
1
In May 1995, EPA produced the “Potential to Emit for MACT Standards – Guidance on Timing Issues” memorandum, which is commonly known as OIAI Policy (1995 John Seitz Memorandum.” At the time, EPA took the position that facilities that are Major Sources of HAPs on the first significant compliance date of an applicable Major Source NESHAP must comply “permanently” with that standard and, thus, be subject to Title V permitting, even if the sources were to later become Area Sources by limiting their emissions.
This position was Transitional Policy Guidance, intended to remain in effect only until EPA proposed and promulgated amendments to the 40 CFR Part 63 General Provisions.

## Slide 532: Reclassification of Major Sources as Area Sources (Cont’d)
On January 25, 2018, EPA issued a guidance memo “Reclassification of Major Sources as Area Sources Under Sect. 112 of the CAA” and withdrew OIAI since EPA has determined that it is “contrary to the clear language of the CAA”
On October 1, 2020, EPA took final action amending NESHAP General Provisions to allow sources that reduce PTE below 10 & 25 tpy of HAPs to reclassify as Area Sources
Notes: 1
1
1
New MM2A policy
On 9/26/23 EPA proposed Review of Final Rule Reclassification of Major Sources as Area Sources under the Clean Air Act
Posted by the Environmental Protection Agency on Sep 26, 2023
Offers “safeguards”
EPA expects that three general types of sources may seek to reclassify as Area Sources:
Sources previously classified as Major that are no longer physically or operationally capable of emitting HAP in amounts that exceed 10 & 25 tpy of HAPs
Sources previously classified as Major that obtain enforceable PTE limits or that already have existing enforceable PTE limits that keep HAP emissions below 10 & 25 tpy of HAPs
Sources with actual emission above 10 & 25 tpy of HAPs that (a) reduce emission to below 10 & 25 tpy of HAPs, and (b) obtain enforceable PTE limits that keep HAPs emissions below 10 & 25 tpy

## Slide 533: Questions
Notes: 533

## Slide 534: LESSON 19
Compliance & Enforcement Considerations
Notes: Ted
Our final lesson is about compliance and enforcement.

## Slide 535: Lesson Objectives
Answer question “What is compliance?”
Explain how to define compliance in permit
Examine what is required to demonstrate compliance
Examine the importance of enforcement
What should the permittee do?
What can the agency do?
535
Notes: We will define compliance and how to put it into the permit. Look at what is needed to demonstrate compliance and why this is important. Finally the responsibility of both the permittee and the agency.

## Slide 536: Basis for Compliance
Basic purpose of a permit term or condition is to tell permit holder
  What is allowed
  What is prohibited
  What is required
  When it is required
  How to comply
Notes: These are what the permit should do. All of these items must be clear, concise and enforceable.
Owners and operators have to comply.

## Slide 537: Compliance vs. Enforcement
Compliance: The full implementation of requirements
Enforcement: The set of actions taken by the government to achieve compliance
  Inspections
  Negotiations
  Legal action
NACT 335
  Principles of Compliance and Enforcement

## Slide 538: What Constitutes Compliance?
Examples:
Emission limits being met
Work practices being observed
Maintenance being performed
Hours of operation within limits
Fuel meeting specifications
Notes: Depends on the requirement
The above are examples – are there other examples?
Don’t forget records – without records the source can’t prove any of the above

## Slide 539: Compliance Defined in Permit
Describe what constitutes compliance and how compliance will be determined
State who is responsible for demonstrating compliance (or noncompliance)
What does the permittee need to do to demonstrate to the agency that all the terms of the permit are being fulfilled
What actions does the permittee need to take if noncompliance is documented or observed
Notes: From Tom Maslany “Principles” workbook Table 3-5, pg. 3-17; and 3-7, pg. 3-26.
Handout 9-A

## Slide 540: Compliance Defined in Permit (Cont’d)
Specify those actions in permit conditions
Define time limits by which compliance must be attained
Describe evidence required to prove a violation

## Slide 541: Compliance Provisions
Permittee shall not knowingly falsify or render inaccurate any monitoring device or method required by the permit
The information obtained from the required monitoring can be used directly for enforcement.
Any credible evidence

## Slide 542: Compliance Demonstration
Surrogate measurements may be useful in demonstrating compliance
  Temperature
  Pressure drop
If relationship can be established, these may be easier, less costly
Must be reflected in permit

## Slide 543: Compliance Demonstration (Cont’d)
Permittee activities
  Source tests
  Continuous emission monitors (CEMs)
  Logs
    Fuel/raw material usage
    Parametric data (temp., pressure drop, VE)
    Maintenance/repair
Agency activities
  Inspections

## Slide 544: Compliance Demonstration (Cont’d)
Compliance demonstration hierarchy
    Reference method stack tests
    Calibrated (with reference method) CEMS
    Calibrated tests on similar units
    Non-reference method tests on unit
    Non-reference method tests on similar units
    Literature data for similar units
    AP-42 factors
Follow Agency Guidelines
Notes: Similarity of other unit must be verified

## Slide 545: Noncompliance
Noncompliance with any permit condition constitutes a violation of the Clean Air Act and/or State rules and is grounds for
  Enforcement action
  Permit termination, revocation and reissuance, or modification
  Denial of a permit renewal application
Notes: These provisions must be spelled out in the permit

## Slide 546: Class Discussion - Compliance
What is meant by the term “compliance”?
Why must the term “compliance” be defined in a permit for each emission unit and for each emission limitation?
Is the definition for the term “compliance” negotiable?

## Slide 547: Enforcement
After the permit is issued
Different than compliance schedule
Notes: Enforcement refers to the actions taken by the permitting agency to ensure that the requirements of the permit are being met

## Slide 548: Importance of Enforcement
Permitting process meaningless if not appropriately enforced
Levels “playing field”
Provides disincentive
Affords credibility to agency

## Slide 549: Enforcement (Cont’d)
Agency must communicate
Complex permits may warrant:
  In house meeting with appropriate enforcement personnel before draft permit is issued
  A meeting with permittee upon completion of the draft permit
  A walk-through existing facility with permit writer, enforcement personnel, and facility representatives
Notes: The permitting agency must be sure that the permittee knows what is expected

## Slide 550: Enforcement (Cont’d)
Permittee responsibilities:
  Understand the permit
  If questions, ask the agency
  Request a meeting if necessary
If permittee doesn’t understand the permit, compliance will be difficult and enforcement action is likely
Notes: The permittee must understand the consequences of the agency’s enforcement actions

## Slide 551: Enforcement (Cont’d)
Agency responsibilities
  Diligence
  Periodic inspections
  Thorough review of records
  Formal enforcement action if warranted
    Depends on agency’s enforcement policy
    Warning
    Notice of Violation (NOV)
Notes: It is crucial that inspection/enforcement staff be integrated into the enforcement process
If there is communication between permit writers and inspectors early in the process, it will make the enforcement program much more effective
Sources should be inspected:
  For new construction, before the initial permit is issued
  For existing sources
    Annual is desirable, though not always practical
    Upon permit renewal
    Upon modification

## Slide 552: Commencement of Construction
Important in two different contexts in Pre-Construction PSD Permit
  Before a Pre-Construction Permit is Issued
  After a Pre-Construction Perm it is issued
Notes: "Commencement of Construction" is a concept that arises in two different contexts in the PSD realm.
While the words used are very similar, the implications are very different.
It is important to understand both.

## Slide 553: Commencement of Construction Building a New Plant
Application Preparation
Agency Review
Final Permit Issuance
Land Will Be Laying Idle
Plant Construction Period
Notes: Constructing a new plant will take a long time. What May the Source Do Before a PSD Permit Is Issued?
Preparing the permit application can take a long time, even years.
Once the application has been submitted to the permitting authority, issuance can take a long time, many months or more.
At the site for construction of the subject equipment, the land is likely to be lying idle, especially if this is a totally new source.

## Slide 554
Activities Allowed Before Permit Is Issued
Sept 2, 2025 EPA Letter updated the Agency's position on construction prior to a PSD/NA NSR permit being issued.
https://www.epa.gov/nsr/construction-activities-allowed-obtaining-preconstruction-air-permit
Notes: https://www.epa.gov/nsr/construction-activities-allowed-obtaining-preconstruction-air-permit

## Slide 555: Activities Allowed Before Permit Is Issued
12/18/1978 EPA Memo from Ed Reich interprets 40 CFR 52.21(i) as follows:
Planning / Preparation
Ordering of Equipment
Clearing the Site
Grading Activities
On-Site Storage of Equipment and Material
Notes: What is allowed before permit issuance is very limited.
December 18, 1978 memorandum from Ed Reich spells it out, interpreting 40 CFR section 52.21(i). Allowed: Planning, ordering of equipment and material, site-clearing, grading, and on-site storage of equipment and materials.
Done at the risk of the owner or operator.

## Slide 556: Activities Not Allowed Before Permit Is Issued
Pouring Foundation
Installing Building Support
Paving
Laying Underground Pipework and Utilities
Avoiding “Equity In the Ground” argument
Notes: Activities Not Allowed Before Pre-Construction Permit is issued consists of: All on-site activities of a permanent nature aimed at completing a PSD source Examples: Installation of building supports and foundations, Paving, Laying of underground pipe work.
The applicant may want to begin construction early in the process, so that operation can begin as quickly as possible.
But if there are disagreements along the way, we don't want the company to be able to argue that, since they have spent so much money already, they should be able to continue with the project as they planned it.
That would be even a greater problem if construction of the source is not allowed at all, such as if the modeling shows that no increment is available.

## Slide 557: Activities Required After Permit Is Issued
Source is required to “Commence Construction” within 18 months after Permit is issued (40 CFR 52.21(r)(2))
Avoiding “Yesterday’s BACT”
Notes: What MUST the Source Do Within 18 months of Receiving a PSD Permit?
18-month window and "yesterday's BACT" Under 40 CFR 52.21(r)(2), companies are required to begin construction within 18 months after obtaining a PSD permit.
The main reason for the deadline is the PSD requirement to install BACT. Specifically, the EPA was concerned that after 18 months, BACT for a project may change, and the Agency does not believe a project should be allowed to proceed if the permit holder is installing yesterday’s BACT.

## Slide 558: Commencement of Construction?
What Qualifies as Commencement of Construction after permit is issued?
Placement, assembly, installation of materials, equipment or facilities as part of ultimate structure of source
Activities must take place at proposed site and be site-specific
Notes: What Qualifies as Beginning Construction?
Placement, assembly, or installation of materials, equipment, or facilities which will make up part of the ultimate structure of the source.
Activities must take place at the proposed site and be site-specific.
Contracts for work on footings, pilings, etc. are considered site specific, whereas contracts for site clearing or excavation work are not.
Contracts for non-site specific equipment, such as boilers will not suffice. A contractual obligation should be one which cannot be canceled or modified without substantial loss. Substantial loss being an exceedance of 10 percent of the total project cost.

## Slide 559: Commencement of Construction Extensions
Extension beyond 18 months is allowed “upon a satisfactory showing that an extension is justified”
Jan. 31, 2014 EPA may no longer require a new application, if applicant shows extensive analysis is not needed, on a case-by-case basis
2014 EPA Policy in SIP or Agency Policy for state/local/tribal agency issued permit
Notes: Extensions beyond the 18-month period are allowed “upon a satisfactory showing that an extension is justified.”
Section 52.21(r)(2) does not indicate any particular procedure or criteria the Agency should use to assess the validity of a request to commence construction beyond the 18-month period.
On January 31, 2014, the EPA departed from previous guidance that usually required new permit applications if, after 18 months, construction does not commence.
The Agency now allows a case-by-case approach that lets the applicant show that the extensive analysis required in a new application is not needed for the extension.
States are encouraged to include the 2014 policy in their SIPs.
Applicants seeking extensions of PSD permits issued by state, tribal, or local authorities with approved PSD programs should contact their permitting authority for information on the applicable requirements.

## Slide 560: Penalties
Should result in behavior change
Not just cost of doing business
Should recognize certain factors
Notes: Some of the other factors that should be considered include degree of willfulness, degree of cooperation, environmental damage, history of non compliance. Additional factors include importance to regulatory scheme (talk re targets etc.)

## Slide 561: Penalty Factors
Agency should formalize penalty factors
Economic factors
  Cost avoided
  Cost postponed
Deviation from standard
Potential for harm
Length of violation
Notes: These are the factors that should be taken into account when Penalties are assessed. Unfortunately this is not always practical or politically acceptable. In cases like the utilities the cost avoided is in the hundreds of millions and the fine would and should not be as high.

## Slide 562: QUESTIONS?
Notes: 562

## Slide 563: SUMMARY

## Slide 564: Permits
Permits
  Permission to Pollute
  Preconstruction
  Operating permit
Who needs permit varies
Sources can reduce emissions to avoid stringent permit requirements
Notes: NSR = PSD, NANSR, minor NSR, syn minor
OP = TV/Part 70, FESOP, SOP

## Slide 565: Federal Permits
PSD
  Only major sources
    Major source is >250 tpy or 100 tpy on list
    Major modification means a physical change with emissions greater than SER (note source is major if the modification is major on own)
  Applies in attainment or unclassified areas
  Requires BACT
    BACT considers cost
    Uses Top down approach that identifies all possible options
Notes: 5 steps top down

## Slide 566: Federal Permits (Cont’d)
PSD (Cont’d)
  PSD applies to criteria pollutants
  PSD does not require offsets or banking

## Slide 567: NA NSR
Applies in non-attainment area
Applies only to Criteria Pollutants
Requires LAER
  No consideration of cost
Offsets Required
  Are equal to or greater than 1 to 1
Offsets come from shutdowns or over control
Offsets may be obtained from banks

## Slide 568: Title V
Operating Permit Program
Covers major sources – generally greater than 100 tpy (10/25 tpy HAPs)
Consolidates all other permit conditions
May add recordkeeping provisions
If control equipment may have CAM plan (CAM plan will include CEM)
CAM plans use reference methods

## Slide 569: Title V (Cont’d)
All permits reviewed by EPA
Notes: Initial, renewals, minor mods, major mods

## Slide 570: Tools
Inventory
  Used in PSD in increment analysis
  Mobile sources very large part of inventory
Dispersion Models
  Only EPA approved models
  Estimate air quality impact of sources
  Can estimate point of maximum concentration more easily than monitoring
  Uses local met data for input
  Stack height influences results
Notes: Part 51 Appx W Guideline on AQ Models

## Slide 571: EPA Emission Standards
Provide basis for permit conditions
NSPS
  Emission or performance standards
  Best demonstrated technology considering cost
  Local standards can be more stringent
NESHAP
  In 1970 act
  Health based approach
  Not successful

## Slide 572: EPA Emission Standards (Cont’d)
MACT
  Technology based does consider cost
  New – based on best demonstrated
  Existing average of top sources but above MACT floor

## Slide 573: Contacts
Carl Daly carlsdaly@outlook.com