## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 1: Basic Concepts
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 1: Basic Concepts Objective
To better understand the scientific and mathematic principles associated with different types of air pollution controls
Gas Temperature
Gas Pressure
Molecular Weight
Ideal Gas Law
Dry Standard Conditions
Types of Air Pollution Control Technologies
Control vs Capture

## Slide 3: Chapter 1: Basic Concepts Temperature
Temperature is a measure of heat
Heat is generated by molecular motion (energy)
  More molecular motion, more heat
  Less molecular motion, less heat
  Absolute Zero:
  No heat = No molecular motion
Temperature is the scale that measures heat

## Slide 4: Chapter 1: Basic Concepts Temperature Scales
 | Fahrenheit (ºF) | Celsius (ºC) | Rankine (ºR) | Kelvin (K)
Steel Melts | 2,597ºF | 1,425ºC | 3,057ºR | 1,698K
Water Boils (at sea level) | 212ºF | 100ºC | 672ºR | 373K
EPA “Standard” Temperature | 68ºF | 20ºC | 528ºR | 293K
Water Freezes (at sea level) | 32ºF | 0ºC | 492ºR | 273K
Absolute Zero | -460ºF | -273ºC | 0ºR | 0K
Fahrenheit (ºF)
= 1.8×(ºC)+32
= (ºR)-460
= 1.8×(K-273)+32
180º between water freeze / boil
Celsius (ºC)
= (ºF-32)÷1.8
= (ºR-492)÷1.8
= K-273
100º between water freeze / boil
Kelvin
= (ºF+460)÷1.8
= (ºC)+273
= (ºR)÷1.8
Celsius begins at absolute zero
Rankine (ºR)
= (ºF)+460
= (ºC+273)×1.8
= (K)×1.8
Fahrenheit begins at absolute zero

## Slide 5: Chapter 1: Basic Concepts Pressure
Pressure is force (weight) applied over surface (area)
The same weight applied over a smaller area “feels” heavier
  6,600 lb. elephant: 35 psi
  100 lb. woman in high heels: 1,600 psi
6 lbs. ÷ 6 square inches = 1 lbs./square inches (psi)
6 lbs. ÷ 1 square inches = 6 lbs./square inches (psi)
1 square inch
6 square inches

## Slide 6: Chapter 1: Basic Concepts Atmospheric Pressure
Our atmosphere has weight
1 square foot 7.4 miles high
= 39,000 cubic feet of air
= ½ Olympic swimming pool
= ~2,100 pounds of air
2,100 pounds ÷ 144 sq. in.
= 14.7 psi
= 1 atmosphere (atm)
1 sq. ft.
39,000 ft.

## Slide 7: Chapter 1: Basic Concepts​ Pressure Scales
 | Atmosphere (atm) | Pounds / Square Inch (psi) | Pascal (Pa) | Inches of Water Column (”W.C.)
Lethal Pressure Wave | 4.0 atm | 60 psi | 414,000 Pa | 1,662” W.C.
Tire Pressure | 2.4 atm | 35 psi | 241,316 Pa | 970” W.C.
Atmosphere at Mean Sea Level | 1.0 atm | 14.7 psi | 101,325 Pa | 407” W.C.
Baghouse Upper | 0.025 atm | 0.36 psi | 2,488 Pa | 10” W.C.
Baghouse Lower | 0.012 atm | 0.18 psi | 1,244 Pa | 5” W.C.
Atmosphere (atm)
= (psi)÷14.696
= (Pa)÷101,300
= (”W.C.)÷407.2
Pounds/sq in (psi)
= (atm)×14.696
= (Pa)÷6895
= (”W.C.)÷27.708
Inches W.C.
= (atm)×407.2
= (psi)×27.708
= (Pa)÷248.8
Pascal (Pa)
= (atm)×101,300
= (psi)×6895
= (”W.C.)×248.8

## Slide 8: Chapter 1: Basic Concepts Types of Pressure
Barometric Pressure: Atmospheric pressure at elevation.
  Measured in millimeters of mercury (mmHg; 760 mmHg = 1 atm)
  Decreases at higher altitudes
  Record ranges from 1.07 atm to 0.858 atm
Gauge Pressure: Pressure of container
  Ignores atmospheric pressure, gauge is at atmospheric pressure
  Measured in psig, kilopascal (kPa or 1000 Pa), or inches water column ("W.C.)
Absolute Pressure: Barometric + Gauge Pressure
  The actual pressure on the container
  0 psig = 14.7 psia

## Slide 9: Chapter 1: Basic Concepts Pressure Differential
Pressure Differential: Change in relative pressure
Measured difference between high-pressure and low-pressure
Pressure Vessel:
Vessel pressure higher than atmosphere
Vacuum Vessel:
Vessel pressure lower than atmosphere

## Slide 10: Chapter 1: Basic Concepts Pressure Differential
Tank Pressure Differential
Used to establish ratings for tanks
  Tanks rated at pressures above atmosphere (high pressure / explosion) or pressures below atmosphere (vacuum / implosion)
Railroad Tank Car
Implosion
Storage Tank
Explosion

## Slide 11: Chapter 1: Basic Concepts Pressure Differential
Control Device Pressure Differential
Commonly used to monitor particulate control devices
  The more particulate trapped in a filter, the harder for air to pass
  Filter under negative pressure (fan is located after filter)
-5” W.C.
-12” W.C.
7” W.C.

## Slide 12: Chapter 1: Basic Concepts Gas Pressure / Temperature / Volume Relationship
Pressure, temperature, and volume all influence each other
  At constant pressure, temperature / volume are proportional
  At constant temperature, pressure / volume are inversely proportional
  At constant volume, temperature / pressure are proportional
Pressure Temperature Volume
PTV
“PTV is a Gas”

## Slide 13: Chapter 1: Basic Concepts​ Gas Pressure / Temperature Relationship
Constant Pressure – Charles’ Law
V∝T
Jacques Alexandre César Charles

## Slide 14: Chapter 1: Basic Concepts Gas Pressure / Volume Relationship
P T V
Constant Pressure
T V

## Slide 15: Chapter 1: Basic Concepts Gas Pressure / Temperature Relationship
Constant Temperature – Boyle’s Law
1
T P
V∝ .
Robert Boyle

## Slide 16: Chapter 1: Basic Concepts Gas Temperature / Volume Relationship
P T V
V
Constant Temperature
P

## Slide 17: Chapter 1: Basic Concepts Gas Pressure / Temperature Relationship
Constant Volume – Guy-Lussac’s Law
P∝T
Joseph Louis
Gay-Lussac

## Slide 18: Chapter 1: Basic Concepts Gas Pressure / Temperature Relationship
P T V
Constant Volume
P T

## Slide 19: Chapter 1: Basic Concepts Combined Gas Law
The Combined Gas Law combines the three gas laws and approximates gas properties at different conditions
P1V1 P2V2
T1 T2
∝

## Slide 20: Chapter 1: Basic Concepts Combined Gas Law
Compare exhaust gas volume at actual (measured) versus standard conditions (1 atm / 68ºF), but not dry standard conditions (removing water in air)

## Slide 21: Chapter 1: Basic Concepts Barometric Pressure
Winter Conditions
Colder air is denser
  Nov-Feb generally has higher barometric pressure
Clear Conditions
High barometric pressure indicates clear skies
  Can cause headaches and sinus pain
Summer Conditions
Warmer air is lighter
  May-Aug generally has lower barometric pressure
Stormy Conditions
Low barometric pressure indicates storms
  The lower the pressure, the stronger the storm

## Slide 22: Chapter 1: Basic Concepts Combined Gas Law Purpose
Do we really need to know this?
Air pollution is a gas
  The exhaust properties of the gas determine emission concentrations
  Actual cubic feet varies vs standard cubic feet
Factory in Toledo, OH - January
Temperature: 35ºF / 495ºR
Barometric Pressure: 30.42 in Hg / 14.94 psia
Airflow: 1,000 acfm
Equivalent to 878 acfm
in Summer (12% lower)
Factory in Toledo, OH - June
Temperature: 91ºF / 551ºR
Barometric Pressure: 29.74 in Hg / 14.60 psia
Airflow: 1,000 acfm
Equivalent to 1,138 acfm
in Winter (12% higher)

## Slide 23: Chapter 1: Basic Concepts Combined Gas Law Purpose
Test in January
Air Temperature: 45ºF / 505ºR
Barometric Pressure:
30.42 in Hg / 14.94 psia
1,790 gr ÷ 60,000 acf = 0.0298 gr/acf (Pass)
60,000 acf = 65,045 scf
1,790 gr ÷ 65,045 scf =
0.027 gr/scf (Pass)
Test in June
Air Temperature: 91ºF / 551ºR
Barometric Pressure:
29.86 in Hg / 14.67 psia
1,790 gr ÷ 60,000 acf = 0.0298 gr/acf (Pass)
60,000 acf = 57,380 scf
1,790 gr ÷ 57,380 scf =
0.031 gr/scf (Fail)
P1V1 P2V2
T1 T2
=
Stack Test (1-hour)
Airflow: 60,000 acf
Collected PM: 1,790 grains
Limit: 0.030 gr/cf
Operates at Ambient Conditions
Standard Conditions
Temperature: 68ºF / 528ºR
Pressure: 14.70 psia

## Slide 24: Chapter 1: Basic Concepts Molecular Weight
Atoms all have different masses (weight)
  Atomic weights are specified in the periodic table
  Oxygen has an atomic weight of 15.999
  Carbon has an atomic weight of 12.011
Molecules have the combined weights of their component atoms
  Atmospheric oxygen (O2) has a molecular weight of (15.999 × 2) = 31.998 (32)
  Carbon dioxide (CO2) has a molecular weight of 12.011 + (15.999 × 2) = 44.009 (44)
15.999 8
O
Oxygen
12.011 6
C
Carbon

## Slide 25: Chapter 1: Basic Concepts Periodic Table

## Slide 26: Chapter 1: Basic Concepts Molecular Weight of Mixtures
Mixtures have a representative fraction of the weight of their component molecules
  Sum of the weighted average for each individual gas
Molecular Weight of Dry Air
Compound | Atomic Weight | Molecular Weight | % Weight | Total Weight
N2 | 14.01 | 28.02 | 78.1% | 21.88
O2 | 16.00 | 32.00 | 21.0% | 6.72
Ar | 39.95 | 39.95 | 0.9% | 0.36
Dry Air |  |  | 100% | 28.96

## Slide 27: Chapter 1: Basic Concepts Chemical Mole
A chemical mole (n) is the number of molecules that make the molecular weight equal to weight units we use (gram / pound)
  Because atoms are so small, you need 6.022×1023 of them to measure them in grams
  There are almost a million times more carbon atoms in a gram of carbon than there are grains of sand on Earth
1 mole molecular mass = 1 mass unit
  32.0 g of atmospheric oxygen contain 1 g-mol of O2
  32.0 lbs. of atmospheric oxygen contain 1 lb-mol of O2
  Gram-mole (g-mol) can be converted to pound-mole (lb-mol) by converting grams to pounds (dividing by 453.592 grams/pound)

## Slide 28: Chapter 1: Basic Concepts Gas Pressure / Temperature Relationship
Constant Temperature & Pressure – Avogrado’s Law
V∝n
Lorenzo Romano Amedeo Carlo Avogadro

## Slide 29: Chapter 1: Basic Concepts Ideal Gas Law
The Ideal Gas Law (or equation of state) combines all four gas laws and approximates gas properties at different conditions
pV = nRT
  p = pressure (psia)
  V = volume (cubic feet)
  n = moles of the gas
  T = temperature (ºR)
  R = constant (10.73 psia-ft3/lb-mole-ºR)

## Slide 30: Chapter 1: Basic Concepts Ideal Gas Law
 | Pascal (Pa) | Atmosphere (atm) | Pounds / Square Inch (psi) | Millimeter Mercury (mmHg)
Ideal Gas Law Constant (r) | 8.314 Pa•m3/(g-mol•K) or Joule/(g-mol•K) | 0.73024 atm•ft3/(lb-mol•ºR) | 10.73 psi•ft3/(lb-mol•ºR) | 62.36 mmHg•l/(g-mol•K)
The ideal gas law works at high temperatures (≥ ambient) and low pressures (≤ ambient)
Considered accurate for air pollution
Less accurate for cryogenic conditions / compressed gases

## Slide 31: Chapter 1: Basic Concepts EPA Dry Standard
EPA Dry Standard
Emissions (stack) testing establishes gas flowrate and weight of pollutant collected
  Used to establish concentration (grains/cubic foot) and rate (lbs./hour)
  Dry standard cubic foot ≤ actual cubic foot
Testing firm corrects stack parameters to U.S. Environmental Protection Agency (EPA) dry standards
  1 atmosphere / 14.7 psia / 29.92 inches of mercury (Hg)
  68ºF / 528ºR
  Dry air molecular weight (O2 & N2 concentration of 29.00 lbs./lb-mole)
  0% moisture content in exhaust gases

## Slide 32: Chapter 1: Basic Concepts Calculating Emissions in EPA Dry Standard
Stack Test Calculations:
Molecular Weight of Stack Gas (dry basis) in lb/lb-mol (Md)
  44 CO2 × % CO2 + 32 O2 × % O2 + 28 N2 × % (100-CO2-O2)
Water Content of Stack Gas % by volume (Bws)
  Water Collected (cf) ÷ Total Airflow (cf)

## Slide 33: Chapter 1: Basic Concepts EPA Dry Standard
Normal Air (acf)
Air 5 acf
Water 1.5 acf
Air 3.5 acf
143ºF
14.40 psi
EPA Dry Standard (dscf)
Air 3.0 dscf
68ºF
14.70 psi

## Slide 34: Chapter 1: Basic Concepts​ Gas Law Purpose
Do we really need to know this?
Air pollution is a gas
  The exhaust properties of the gas determine emission concentrations
  Actual cubic feet vs standard cubic feet changes exhaust volume
Factory in Denver, CO
Temperature: 70ºF / 530ºR
Pressure: 14.72 psia
0.58 grains/actual cubic foot
0.58 grains/std cubic foot
Factory in Houston, TX
Temperature: 90ºF / 550ºR
Air Pressure: 14.61 psia
0.58 grains/actual cubic foot
0.61 grains/std cubic foot

## Slide 35: Chapter 1: Basic Concepts​ Review Question
Emission Limit: 0.1 grains/cubic foot (gr/cf)
Stack test report states the following:
  PM Weight: 8.2 lbs. (in 1 hour)
  Flowrate: 10,000 actual cubic feet per minute (acfm)
  Temperature: 150ºF
  Barometric Pressure: 14.49 psia
What is the emissions rate in grains per actual cubic feet and grains per standard cubic feet?
Is this emissions limit ambiguous?

## Slide 36: Chapter 1: Basic Concepts​ Review Question
Emissions rate in actual cubic feet:
  Weight: 8.2 lbs./hr × 7,000 grains = 57,400 gr/hr
  Flowrate: 10,000 acfm × 60 m/hr = 600,000 acf/hr
  PM Emissions Rate: 57,400 gr/hr ÷ 600,000 acf/hr = 0.096 gr/acf
Conclusion: PASS (0.096 gr/acf < 0.1 gr/cf)

## Slide 37: Chapter 1: Basic Concepts​ Review Question
Emissions rate in standard cubic feet (scf) - combined gas law:
  Weight: 8.2 lbs./hr × 7,000 grains = 57,400 gr/hr
  Flowrate: 10,000 acfm × 60 m/hr = 600,000 acf/hr
  Temperature: 150ºF / 609.7ºR
  Standard Temperature: 68.0ºF / 527.7ºR
  Barometric Pressure: 14.49 psia
  Standard Pressure: 14.70 psia
Standard Flowrate:
600,000 acf/hr×(14.49 psia÷14.70 psia)×(527.7ºR÷609.7ºR)=511,882 scf/hr
PM Emissions Rate: 57,400 gr/hr ÷ 511,882 scf/hr = 0.11 gr/scf
Conclusion: FAIL (0.11 gr/scf > 0.1 gr/cf)

## Slide 38: Chapter 1: Basic Concepts​ Discussion Questions
What is the relationship between pressure and temperature at a constant volume? [Hint: PTV]
Can a pressure vessel be used as a vacuum vessel?
For which control device would the difference between acfm and dscfm be expected to be the highest?
  Wet scrubber
  Baghouse
Should acfm or dscfm be used as a limit in permits and regulations?

## Slide 39: Chapter 1: Basic Concepts Controlling Air Pollution
Air pollution controls include any equipment or method of operation to reduce emissions of air pollutants
Prevention: Decreasing the amount of air pollutants formed
Collection: Removing air pollutants from exhaust air
Conversion: Changing an air pollutant to another, less harmful (inert) chemical
Reducing air pollution improves air quality and lowers impacts to human health and environment
!

## Slide 40: Chapter 1: Basic Concepts Controlling Air Pollution
Dust / Particulates
  Particulate Matter (PM, PM10, PM2.5)
  Lead (Pb)
  Metal Hazardous Air Pollutants (HAP)
Organic Gases & CO
  Volatile Organic Compounds (VOC)
  Volatile Organic HAP (VOHAP)
  Carbon Monoxide (CO)
Acid Gases
  Nitrogen Oxides (NOX)
  Sulfur Dioxide (SO2)

## Slide 41: Chapter 1: Basic Concepts Controlling Air Pollution
Three Concepts of Air Pollution Controls |  | 
1. Prevention | 2. Collection | 3. Conversion
Process Formulation | Separation / Filtration / Aggregation | Combustion / Oxidation / Incineration
Process Optimization | Absorption / Scrubbers | Reduction / Scrubbers
Alternative Processes | Adsorption | Bioreactors / Biofiltration
 | Condenser | 
 | Sequestration | 

## Slide 42: Chapter 1: Basic Concepts Air Pollution Controls - Prevention
Prevention: Equipment or operational restrictions reducing air pollutant formation directly from the source
Increasing raw material purity and/or incorporating additives can reduce air pollutant formation
Optimizing process parameters can reduce air pollutant formation
Alternative materials may generate less air pollution
Prevention controls are most effective for control of CO, CO2, NOX, SO2, and Lead
!

## Slide 43: Chapter 1: Basic Concepts Air Pollution Controls - Prevention
Prevention Controls: Purity / Additives
Fuel formulation reduces air pollution
Low-carbon feedstocks reduce CO2 emissions
Hydrogen-enriched compressed natural gas (HCNG) contains hydrogen and methane, reducing CO2 formation
HCNG Blend

## Slide 44: Chapter 1: Basic Concepts Air Pollution Controls - Prevention
Prevention Controls: Alternative Materials
Alternative materials may emit lower air pollution
  Dry powder coating lowers VOC & HAP emissions over spray coating
  Different fuels have different air pollutant emissions profiles
Pollutant | Wood | Coal | Fuel Oil | Natural Gas
CO | 0.60 lbs./mmBtu1 | 0.03 lbs./mmBtu | 0.03 lbs./mmBtu | 0.078 lbs./mmBtu
NOX | 0.49 lbs./mmBtu | 0.42 lbs./mmBtu | 0.16 lbs./mmBtu | 0.259 lbs./mmBtu
PM | 0.40 lbs./mmBtu | 4.64 lbs./mmBtu | 0.01 lbs./mmBtu | 0.007 lbs./mmBtu
SO2 | 0.03 lbs./mmBtu | 2.43 lbs./mmBtu | 0.95 lbs./mmBtu | 0.001 lbs./mmBtu
CO2 | 206 lbs./mmBtu | 214 lbs./mmBtu | 163 lbs./mmBtu | 117 lbs./mmBtu
1 mmBtu – Million (106) British Thermal Units, a measure of heat

## Slide 45: Chapter 1: Basic Concepts Air Pollution Controls - Collection Controls
Collection: Equipment reducing air pollution in exhaust
Separation: Removing air pollutants by changing air flow
Filtration: Capturing air pollutants too large to pass through a porous membrane or filter
Aggregation: Clustering air pollutants together
Absorption: Liquid material that absorbs air pollutants
Condensation: Physical change of air pollutant from gas to liquid by decreasing temperature and/or increasing pressure
Adsorption: Adhesion of air pollutants to a solid
Sequestration: Capturing and storing air pollutants

## Slide 46: Chapter 1: Basic Concepts Air Pollution Controls – Conversion Controls
Conversion: Equipment that chemically converts air pollutants into other, less toxic materials
Combustion / Oxidation / Incineration: Rapid chemical reaction where combustible air pollutants (VOC) are oxidized to form CO2, water, and heat
Reduction: Chemical reaction between liquid or solid material and air pollutant, converting it into a less toxic material
Bioreactors / Biofiltration: Microorganisms that consume VOC or PM that are soluble in water and biodegradable

## Slide 47: Chapter 1: Basic Concepts Air Pollution Control Methods by Pollutant
Control Methods by Air Pollutant |  |  |  |  | 
CO / CH4​ | Combustion​ | ​ | ​ | ​ | 
CO2​ | Prevention​ | Sequestration​ | ​ | ​ | 
Lead​ | Prevention​ | Separation | Aggregation​ | Filtration​ | 
NOX​ | Prevention​ | Absorption​ | Adsorption​ | ​ | 
PM10 / PM2.5​ Metal HAP​ | Separation | Aggregation​ | Filtration​ | Absorption | Bioreactor / Biofiltration​
SO2​ | Prevention​ | Absorption​ | Adsorption​ | ​ | 
VOC​ Organic HAP​ | Combustion​ | Absorption​ | Adsorption​ | Condenser​ | Bioreactor / Biofiltration​

## Slide 48: Chapter 1: Basic Concepts Emissions Egress
Stack (Point) Emissions
One identifiable emissions point (stack, duct, flue)
Fugitive Emissions
Emissions generated over an area (roadways, valves)

## Slide 49: Chapter 1: Basic Concepts Capture vs Control
Capture Efficiency: Measure of how much air pollution generated by the source is exhausted to control device
Assume 100% efficiency for closed systems (e.g., gas boiler)
Difficult to measure for open systems (e.g., painting operations)
Control Efficiency: Measured ability for equipment or operational restriction to reduce air pollution
Determined by comparing air pollutant concentration before and after control (e.g., stack / performance test)
Overall Control Efficiency = Capture Efficiency × Control Efficiency
!

## Slide 50: Chapter 1: Basic Concepts Capture Efficiency
Capturing Emissions
Most processes generate fugitive emissions
  Collection equipment can be used to capture fugitive particulate emissions and transfer it to control equipment
  Fugitive source becomes a stack source
Hoods / hoses capture fugitive emissions
Fans are used to transfer fugitive emissions via flues / ducts

## Slide 51: Chapter 1: Basic Concepts Capturing Air Pollutants
Capture System

## Slide 52: Chapter 1: Basic Concepts Capturing Air Pollutants
Capture Efficiency
Capture Efficiency: amount of air pollutants transferred from generating area to control device or stack
Captured = Control Device Inlet
How do you determine total air pollutants generated?
How do you determine total air pollutants captured?

## Slide 53: Chapter 1: Basic Concepts Controlling Air Pollutants
Control Efficiency
Control Efficiency: how well the control device collects PM

## Slide 54: Chapter 1: Basic Concepts Capturing Air Pollutants
Capture Principles
Total enclosure: Entire fugitive emissions area is enclosed
  Device enclosure – Device is completely enclosed (blast cabinet)
  Room enclosure – Room is completely enclosed (paint booth)
  Building enclosure – Hoods or pickup points are placed in ceiling (foundry floor)
Partial enclosure: Fugitive emissions generation relies on vacuum and placement of pickup points for enclosure
  Flexible hoses for grinding / machining equipment
  Halogenated solvent degreaser under a hood

## Slide 55: Chapter 1: Basic Concepts Capturing Air Pollutants
Total Enclosure
Partial Enclosure

## Slide 56: Chapter 1: Basic Concepts Capturing Air Pollutants
Capture Velocity
Hood needs sufficient draw (vacuum) to overcome opposing air currents and capture particulates
  Air currents within room
  Toxicity of the pollutant
  Amount of particulate produced
  Available area
Capture velocity decreases exponentially with distance

## Slide 57: Chapter 1: Basic Concepts Capturing Air Pollutants
Fans
Fans pull a different amount of air (flow rate) at different differential pressures
  Higher pressure drop increases air flow rate
  Fan curves are available from manufacturer
Fans are generally located after control device

## Slide 58: Chapter 1: Basic Concepts Collecting Air Pollutants
What do with collected air pollutants?
Landfill: PM from filtration / separation; Liquid VOC; spent catalysts; some wet scrubbers; adsorbers
Incineration: Liquid VOC, CO
Product / Reuse: PM from filtration / separation; Liquid VOC from refrigerated condenser; some wet scrubbers; some spent catalysts; adsorbers
Wastewater Treatment: Wet scrubbers (PM, Liquid VOC)
Deep Well Injection: CO2; liquid HAP

## Slide 59: Chapter 1 Video Towards Cleaner Air
Towards Cleaner Air
  https://catalog.archives.gov/id/73305 - Publicly Available