## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 2: Control of Particulate Emissions
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 2: Control of Particulate Emissions Objective
To improve understanding of particulate matter (PM) control
  What is PM?
  What are the four types of PM controls?
  How do PM controls operate?
  How are PM controls designed?
  What is the expected control efficiency for a PM control?
  What are common problems with a PM control?
  How are PM controls monitored?

## Slide 3: Chapter 2: Control of Particulate Emissions Introduction to Particulate Matter
Particulate Matter (PM)
Microscopic solid & liquid droplets that can be inhaled
  Filterable PM: collects on a Method 5 filter
  Condensable PM: condenses in Method 202 dry impinger
Wide variety of many different materials
  Airborne solids / liquids: aerosols, dust, dirt, pollen, smoke, and soot
  Hazardous air pollutants (HAP): asbestos and metals
  Sulfates / nitrates from sulfur dioxide (SO2) and nitrogen oxides (NOX)
  Carbon compounds from combustion of organic materials

## Slide 4: Chapter 2: Control of Particulate Emissions Particulate Sizes
PM Categories
Categorized by particle size (in micrometers - µm)
  PM12700 = Theoretical largest particle measured by Method 5 (½ inch)
  PM100 = Largest particle to suspend in air; 1971 National Ambient Air Quality Standard (NAAQS) for Total Suspended Particulate (TSP)
  PM30 = Largest U.S. Environmental Protection Agency (EPA) emissions factor for TSP
  PM10 = 1987 NAAQS for Coarse PM
  PM2.5 = 1997 NAAQS for Fine PM (revised 2012)
1/256 inch ½ inch
Human Hair
2.5 10 30 50 100 12700

## Slide 5: Chapter 2: Control of Particulate Emissions Particulate Sizes
Fine Beach Sand (90µm Diameter)
Human Hair
(50-70µm Diameter)
PM2.5 – 2.5µm Diameter
PM10 – 10µm Diameter
PM10 / PM2.5 Comparison

## Slide 6: Chapter 2: Control of Particulate Emissions Particulate Sizes

## Slide 7: Chapter 2: Control of Particulate Emissions Particulate Shapes

## Slide 8: Chapter 2: Control of Particulate Emissions Particulate Impacts
Coarse Particulate Matter – PM10
Solid or liquid particles commonly emitted by multiple Formation
  Includes dust, pollen, dirt, cooling towers emissions, soot, and smoke
PM10 enters blood via lungs; adverse health impacts include:
  Nonfatal heart attacks • Irregular heartbeat
  Aggravates asthma • Decrease in lung function
  Premature death for people with heart or lung disease
Settles on ground, water, vegetation, and structures
  Stains or damages stone and other materials

## Slide 9: Chapter 2: Control of Particulate Emissions Particulate Impacts
Fine Particulate Matter – PM2.5
Condensed compounds that react in the atmosphere
Irritates the respiratory system
  Lung, eye, nose, and throat irritation, coughing, and sneezing
  Aggravates heart and respiratory diseases, like asthma
PM2.5 forms atmospheric haze, reducing visibility
  Formed from atmospheric reactions of acid gases (sulfur dioxide – SO2 & nitrogen oxides – NOX)
  Impacts scenic views in national parks and wildernesses

## Slide 10: Chapter 2: Control of Particulate Emissions Particulate Types
Filterable PM
Captured on filter media in EPA Methods 5, 17, or 201a
PM are solids or liquids at stack temperature
PM2.5, PM10, and PM (TSP)
Condensable PM
Captured in ice bath or in silica gel in EPA Method 202
PM is a gas (vapor) at stack temperature
<PM2.5 (PM1.0)

## Slide 11: Chapter 2: Control of Particulate Emissions Particulate Types
Filterable PM
Well captured by PM air pollution control devices
Vendors will guarantee control efficiency
Condensable PM
Slight capture by some PM air pollution control devices
  Wet scrubber (decrease in exhaust temperature)
  Electrostatic precipitator (ESP)
Vendors will not guarantee control efficiency

## Slide 12: Chapter 2: Control of Particulate Emissions Particulate Control – Prevention
Prevention Controls: Process Optimization
Methods to reduce production of fugitive dust:
  Cover / enclose
  Apply water / surface protectant
  Debris removal

## Slide 13: Chapter 2: Control of Particulate Emissions Particulate Control Types
Four Types of Particulate Control
Mechanical Separation
Filtration
Wet Scrubber (Absorption)
Electrostatic Precipitator

## Slide 14: Chapter 2: Control of Particulate Emissions Mechanical Separation – Overview
PM Control: Mechanical Separation
Mechanical separators remove particulate matter (PM) via gravity (settling), momentum, or inertia
  Gravity: Reduce gas stream velocity and PM settles out
  Momentum / Inertia: Change gas stream direction and PM settles out
Modifications to the airflow within the collector separate PM from gas stream
  The fan is the only moving part
Cyclones are the most common mechanical separator

## Slide 15: Chapter 2: Control of Particulate Emissions Mechanical Separation – Principles of Operation
Settling: Reduced gas stream velocity separate particles from gas stream

## Slide 16: Chapter 2: Control of Particulate Emissions Mechanical Separation – Settling Chamber Example
Settling Chamber

## Slide 17: Chapter 2: Control of Particulate Emissions Settling Chamber – Operation
Larger volume chamber slows down gas stream
Larger particles settle and drop out of gas stream

## Slide 18: Chapter 2: Control of Particulate Emissions Settling Chamber – Operation
Settling Chamber
Particulate settles into hoppers
5% Control of PM10 (10µm)
13% Control of PM30 (30µm)
25% Control of PM52 (52µm)
14% Control of PM10-PM52
>99% Control at PM150 (150µm)
Adapted from Naseer, M. A., Maqsood, M. S., & Al-Zahrani, S. S. (2016). Numerical investigation of a horizontal gravity settling chamber with different baffle configurations. Journal of Applied Fluid Mechanics, 9(5), 2576–2585

## Slide 19: Chapter 2: Control of Particulate Emissions​ Types of Settling Chambers
Single Chamber
Multiple Tray
(Howard)

## Slide 20: Chapter 2: Control of Particulate Emissions​ Howard (Multiple) Tray Settling Chamber
Dirty Air
Particles
Clean Air
Vertical Baffle

## Slide 21: Chapter 2: Control of Particulate Emissions​ Settling Chamber – Design Considerations
Particle size and mass
  Effective only for heavier / larger particles (≥50µm)
  Unsuitable for sticky particulate
Decrease gas stream velocity
  Gas residence time ≥ particle settling time
  Increased chamber width slows airflow, allowing PM to settle
Increasing control efficiency
  Increasing chamber length increases residence time
  Multiple trays shorten settling distance for particles (usually vertical trays are used so that gravity attracts PM and cleans the trays)

## Slide 22: Chapter 2: Control of Particulate Emissions Settling Chamber – Design Considerations
Gravity does all the work
Only needs a fan for airflow
Control efficiency factors:
  Chamber volume
  Airflow (velocity): 15-30 scfm per cubic foot chamber volume
  Particulate size: 15µm - 50µm
  Particulate settling velocity: >25 feet/minute

## Slide 23: Chapter 2: Control of Particulate Emissions​ Settling Chamber – Design Considerations
Longer settling chambers, collect more and smaller PM
  PM1.0 3.44×10-5 m/s 8 hours to fall 1 meter @ 0 acfm
  PM2.5 1.96×10-4 m/s 85 minutes to fall 1 meter @ 0 acfm
  PM10 3.00×10-3 m/s 5½ minutes to fall 1 meter @ 0 acfm
  PM20 1.19×10-2 m/s 1½ minutes to fall 1 meter @ 0 acfm
  PM50 7.50×10-2 m/s 13 seconds to fall 1 meter @ 0 acfm
  PM100 3.12×10-1 m/s 3 seconds to fall 1 meter @ 0 acfm
Settling Chambers are incorporated into other PM control technologies (e.g., filtration, aggregation)
  Aggregating PM into larger particle sizes requires less time in settling chamber (collection hoppers in other PM control technologies)

## Slide 24: Chapter 2: Control of Particulate Emissions​ Settling Chamber – Design Considerations
Chart: Settling Time for PM by Size
| 0 | 15 | 30
PM1.0 | 0 | 2215.1162 | 4430.2324
PM2.5 | 0 | 388.7755 | 777.551
PM5.0 | 0 | 100.1314 | 200.2628
PM10 | 0 | 25.4 | 50.8
PM20 | 0 | 6.4034 | 12.8067

## Slide 25: Chapter 2: Control of Particulate Emissions​ Settling Chamber – Operating Problems
Settling Chamber
High particulate concentration can plug collection hoppers
Not effective for particulate collection <70µm
Re-entrainment (pickup) of collected PM due to airflow across settling chamber
Not suitable for sticky PM

## Slide 26: Chapter 2: Control of Particulate Emissions​ Pickup (Re-entrainment) Velocities
Material | Density (gram/cm3) | Median Size (cm) | Pickup Velocity (feet/second)
Aluminum chips | 2.72 | 33.5 | 14.2
Asbestos | 2.2 | 26.1 | 17
Nonferrous | 3.02 | 11.7 | 18.8
Lead oxide | 8.26 | 1.5 | 25
Limestone | 2.78 | 7.1 | 21
Starch | 1.27 | 6.4 | 5.8
Steel shot | 6.85 | 9.6 | 15.2
Wood chips | 1.18 | 137 | 13
Sawdust | <0.9 | 140 | 22.3

## Slide 27: Chapter 2: Control of Particulate Emissions Video
2.1 - Settling Chamber & Cyclone.mp4

## Slide 28: Chapter 2: Control of Particulate Emissions Settling Chamber – Control Efficiencies
Settling Chamber
<1% PM2.5
1% PM10
10% PM30
30% PM
Source: Control Techniques
for Particulate Emissions from
Stationary Sources – Vol. 1
EPA-450/3-81-005a
0%
20%
40%
60%
80%
100%
0
10
20
30
40
50
60
70
80
90
Control Efficiencies by Particle Size (µm)

## Slide 29: Chapter 2: Control of Particulate Emissions Mechanical Separation – Principles of Operation
Momentum / Inertia: Changing gas stream direction separates particles from gas stream.

## Slide 30: Chapter 2: Control of Particulate Emissions Mechanical Separation – Principles of Operation
Momentum:
Particles keep going the same direction when the exhaust air changes direction.

## Slide 31: Chapter 2: Control of Particulate Emissions Momentum Separator – Operation
Gas changes direction, particulate does not
Gravity settling chamber (dust hopper) used to collect particulate

## Slide 32: Chapter 2: Control of Particulate Emissions Baffled Settling Chamber – Operation
Baffled Settling Chamber
Particulate settles into hoppers and has momentum impacted
7% Control of PM10 (10µm)
18% Control of PM30 (30µm)
43% Control of PM52 (52µm)
23% Control PM10-PM52
>99% Control at PM100 (100µm)
Adapted from Naseer, M. A., Maqsood, M. S., & Al-Zahrani, S. S. (2016). Numerical investigation of a horizontal gravity settling chamber with different baffle configurations. Journal of Applied Fluid Mechanics, 9(5), 2576–2585

## Slide 33: Chapter 2: Control of Particulate Emissions Momentum Separator – Design Considerations
Momentum does the work
Only needs a fan for airflow
Control efficiency factors:
  Airflow (velocity): 1,000-21,000 scfm per cubic foot
  Particulate size: 15µm - 90µm
  Particulate loading (density): 9-1,970 gr/dscf
Cyclones are more efficient with same volume (space)

## Slide 34: Chapter 2: Control of Particulate Emissions​ Momentum Separator Operating Problems
Momentum Separators
High particulate concentration can plug collection hoppers
Erosion of baffle plates / collector shells
Take up a large amount of space
Particle size and mass
  Effective only for heavier / larger particles (≥90µm)
  Unsuitable for sticky particulate
Limited use in food / metallurgical industries (where particle size important)

## Slide 35: Chapter 2: Control of Particulate Emissions Momentum Separator – Control Efficiencies
0%
20%
40%
60%
80%
100%
0
10
20
30
40
50
60
70
80
90
Control Efficiencies by Particle Size (µm)
Momentum Separator
<1% PM2.5
1% PM10
10% PM30
30% PM
Source: Control Techniques
for Particulate Emissions from
Stationary Sources – Vol. 1
EPA-450/3-81-005a

## Slide 36: Chapter 2: Control of Particulate Emissions Settling Chamber / Momentum Separator – Compliance Inspection
Inspection Parameters
Visible emissions
Static pressure drop
Solids discharge
Internal inspection
□ Visible Emissions
□ Visible Inspection
□ Pressure Drop
□ Gas Monitoring
□ Emissions Testing
□ Internal Inspections

## Slide 37: Chapter 2: Control of Particulate Emissions Mechanical Separation – Principles of Operation
Cyclone (Inertia):
Like children on a fast merry-go-round or wet clothes on the spin cycle in a washing machine, centrifugal force directs particles outwards.

## Slide 38: Chapter 2: Control of Particulate Emissions Cyclone – Operation
Particulate laden gas enters the cyclone.
As the gas changes direction, inertia pushes particulates to the sides.
Clean gas exits the top and particulates exit the bottom.

## Slide 39: Chapter 2: Control of Particulate Emissions Mechanical Separation – Cyclone Examples
Cyclones

## Slide 40: Chapter 2: Control of Particulate Emissions Video
PM 1.0 - Cyclone Intro.mp4

## Slide 41: Chapter 2: Control of Particulate Emissions​ Design Considerations
Particle size and mass
  Heavier / larger particles are more easily separated from gas stream
Gas stream velocity
  Faster airflow increases centrifugal force from spinning gas stream
  Centrifugal force increases as diameter of cyclone decreases
Ratio of cyclone diameter to exhaust diameter
  Increases residence time
Cyclone height
  Increases the number of revolutions
  Increases residence time

## Slide 42: Chapter 2: Control of Particulate Emissions Cyclone – Design Considerations
Increased PM collection:
Smaller diameter bodies / cones = increased centrifugal force
Longer bodies / cones = longer residence times
Operate cyclones in series or parallel

## Slide 43: Chapter 2: Control of Particulate Emissions​ Types of Cyclones
Cyclones in Series
Cyclones in Parallel

## Slide 44: Chapter 2: Control of Particulate Emissions​ Parallel Cyclones Examples
Parallel Parallel & Series

## Slide 45: Chapter 2: Control of Particulate Emissions​ Inlet Types
All Types of Cyclones
Large Diameter Cyclones

## Slide 46: Chapter 2: Control of Particulate Emissions Cyclone – Types
Large Diameter Cyclone
Small Diameter Multiclone

## Slide 47: Chapter 2: Control of Particulate Emissions​ Types of Cyclones
Large Diameter Cyclone
Inlet gas stream enters tangentially to impart spin
½ to 2 rotations within cyclone body
Can be used in series or parallel to increase PM collection efficiency
Small Diameter Multi-cyclone
Inlet gas enters from the top, passing over stationary inlet vanes to impart spin
½ to 3 rotations within each cyclone body
Parallel multi-cyclones (multiclone) resting on a tube sheet to separate clean and dirty gases

## Slide 48: Chapter 2: Control of Particulate Emissions Multiclone
Particulate laden gas enters the tube from plenum.
Inlet vane imparts spin, rotating gas within tube.
As gas spins, inertia pushes particulates to the sides.
Clean gas exits the top and particulates exit the bottom.
Multiclone Tube
Plenum

## Slide 49: Chapter 2: Control of Particulate Emissions​ Multiclone Example
Multiclone

## Slide 50: Chapter 2: Control of Particulate Emissions​ Video
PM 1.1 - Cyclone Large Diameter.mp4
PM 1.2 - Cyclone Multiclone.mp4

## Slide 51: Chapter 2: Control of Particulate Emissions​ Separation – Control Efficiencies
Conventional Cyclone
0-40% PM2.5
30-90% PM10
70-90% PM30
65-85% PM
Source: Control Techniques
for Particulate Emissions from
Stationary Sources – Vol. 1
EPA-450/3-81-005a

## Slide 52: Chapter 2: Control of Particulate Emissions​ Separation – Control Efficiencies
High Efficiency Cyclone
20-70% PM2.5
60-95% PM10
99% PM30
80-95% PM
Source: Control Techniques
for Particulate Emissions from
Stationary Sources – Vol. 1
EPA-450/3-81-005a

## Slide 53: Chapter 2: Control of Particulate Emissions​ Separation – Control Efficiencies
Multiclone Cyclone
40-60% PM2.5
85-95% PM10
99% PM30
85-95% PM
Source: Control Techniques
for Particulate Emissions from
Stationary Sources – Vol. 1
EPA-450/3-81-005a

## Slide 54: Chapter 2: Control of Particulate Emissions​ Separation – Parametric Monitoring
Parametric Monitoring
On/Off Indicator
  Fan is only moving part
Pressure Differential (ΔP)
  Multiclone buildup on inlet vanes
  Tube / vane / chamber erosion
Visible Emissions (VE)
  Opacity caused by small particulates, so presence of VE indicates mechanical separator not an effective control

## Slide 55: Chapter 2: Control of Particulate Emissions​ Operating Problems
Cyclone
Vortex Disruption
  Air infiltration
Particulate Re-entrainment
  Particle bounce
  Wall accumulations
Multi-cyclone
Vortex Disruptions
  Air infiltration
  Inlet vane plug / erosion
Particulate Re-entrainment
  Hopper overflow
  Cross hopper recirculation
Cyclone Bypass
  Outlet pipe erosion
  Tube sheet erosion

## Slide 56: Chapter 2: Control of Particulate Emissions​ Examples
Operating Problems: Plugged Vanes

## Slide 57: Chapter 2: Control of Particulate Emissions Cyclone – Compliance Inspection
Inspection Parameters
Visible emissions
Static pressure drop
Air infiltration
  Inlet / outlet temperature or oxygen content
  Holes, dents or weld failures
Solids discharge
Internal inspection
□ Visible Emissions
□ Visible Inspection
□ Pressure Drop
□ Gas Monitoring
□ Emissions Testing
□ Internal Inspections

## Slide 58: Chapter 2: Control of Particulate Emissions​ Compliance Inspection
Visible Emissions (VE) - Example

## Slide 59: Chapter 2: Control of Particulate Emissions Filtration – Overview
PM Control: Filtration
Multiple forces aid particulate collection on filters
  Strain / Sieve
  Inertia Impaction
  Interception
  Diffusion
Filters become infused with collected particulate
  Particulates can be removed, and the filter reused
During particulate collection, the fan is the only moving part
  Other mechanical actions required for filter cleaning

## Slide 60: Chapter 2: Control of Particulate Emissions Filtration – Principle of Operation
Some filters can be cleaned periodically to capture more particulate.

## Slide 61: Chapter 2: Control of Particulate Emissions Filtration – Principle of Operation
Filtration
As the particles pass through the filter, they become stuck to the fibers, infusing the fiber with particulate.

## Slide 62: Chapter 2: Control of Particulate Emissions Filtration – Principle of Operation
Dust (Filter) Cake
As more particles stick to the filter surface, more particles are captured by the filter. A dirty filter is better than a clean filter.

## Slide 63: Chapter 2: Control of Particulate Emissions Filtration – Fabric Filter (Baghouse) Examples

## Slide 64: Chapter 2: Control of Particulate Emissions Video
PM 2.0 - Baghouses
PM 2.0a - Design.mp4
4.0 – Baghouse Design

## Slide 65: Chapter 2: Control of Particulate Emissions Filtration – Design Considerations
Draft (Air Movement) Options
Fan Type | Pros | Cons
Forced (Push) | Smaller Motor Less Expensive Easy to Identify Leaks | Erosion of Fan Blades
Induced (Pull) | No Erosion of Fan Blades | Larger Motor More Expensive Harder to Identify Leaks

## Slide 66: Chapter 2: Control of Particulate Emissions Filtration – Design Considerations
Air-to-cloth ratio
  Higher ratio (due to higher gas velocities) cause particles to migrate through the filter, reducing control efficiency
Exhaust gas characteristics
  Filters are flammable
  Filters are degraded by acids
  Filters are damaged by abrasive particles
  Filters ineffective when full of particulate (filter blinding)
Filter type
  Disposable
  Reusable: Type of filter cleaning mechanism

## Slide 67: Chapter 2: Control of Particulate Emissions Filtration – Design Considerations
Air-to-Cloth Ratio

## Slide 68: Chapter 2: Control of Particulate Emissions Filter – Certification
Mat / Panel / Cartridge Filter Certification
Filters are certified by independent, third-party laboratories using different national and international standards
American Society of Heating, Refrigerating and Air-Conditioning Engineers (ASHRAE) Procedure 52.2-2017
  Minimum Efficiency Reporting Value (MERV) with 16 categories
International Organization for Standardization (ISO) 16890-1:2016
  Removal efficiency established for four particle classes: ePM1, ePM2.5, ePM10, and Coarse (PM10+)

## Slide 69: Chapter 2: Control of Particulate Emissions ASHRAE MERV Filter Certification
MERV | PM10.0 – PM3.0 | PM3.0 – PM1.0 | PM1.0 – PM0.3
1-4 | <20% | 0% | 0%
5 | 20% | 0% | 0%
6 | 35% | 0% | 0%
7 | 50% | 0% | 0%
8 | 70% | 20% | 0%
9 | 75% | 35% | 0%
10 | 80% | 50% | 0%
11 | 85% | 65% | 20%
12 | 90% | 80% | 35%
13 | 90% | 85% | 50%
14 | 95% | 90% | 75%
15 | 95% | 90% | 85%
16 | 95% | 95% | 95%
ASHRAE MERV reflects the minimum removal efficiency (usually clean filter)

## Slide 70: Chapter 2: Control of Particulate Emissions ISO 16890 Filter Certification
Coarse | ePM10 | ePM2.5 | ePM1
95% | 95% | 95% | 95%
50% | 90% | 90% | 90%
 | 85% | 85% | 85%
 | 80% | 80% | 80%
 | 75% | 75% | 75%
 | 70% | 70% | 70%
 | 65% | 65% | 65%
 | 60% | 60% | 60%
 | 55% | 55% | 55%
5% | 50% | 50% | 50%
ePM: Average efficiency between a clean filter and a seasoned filter

## Slide 71: Chapter 2: Control of Particulate Emissions Filter – Certification
Filter Certification
High Efficiency Particulate Air (HEPA) Filters exceed MERV 16
  MERV 17 / HEPA – 99.97%
  MERV 18 / HEPA– 99.997%
Ultra-Low Particulate Air (ULPA) Filters exceed MERV 18 / HEPA
  MERV 19 / ULPA – 99.9997% (reduced airflow)
  MERV 20 / ULPA – 99.99997%

## Slide 72: Chapter 2: Control of Particulate Emissions Filter – Certification
Filter Certification
Complete filter report details removal (capture) efficiency at different loads, relative humidity, and pressure differentials
Control device manufacturers match filters to exhaust:
  Particle size / loading
  Flowrate
  Pressure differential
  Relative humidity
Request filter certification information from manufacturer
  Ensure filters are being used within established parameters

## Slide 73: Chapter 2: Control of Particulate Emissions Video
4.1 – ASHRAE Filter Testing

## Slide 74: Chapter 2: Control of Particulate Emissions Filter – Design Considerations
Disposable Filter
One-time use filter
Replaced when blinded (full)
No separate dust collection
Reusable Filter
Multiple-use filter
Cleaning mode to remove particulate buildup
Replace when degraded
Separate dust collection required

## Slide 75: Chapter 2: Control of Particulate Emissions Disposable Filters – Overview
Disposable Cartridge (Pleated) Filters
Pleated to increase surface area
Mounted inside frame for support
Frame may include a sealing gasket

## Slide 76: Chapter 2: Control of Particulate Emissions Cartridge Filters – Overview
Pleated Cartridges
Increase cloth surface area, decreasing air-to-cloth ratio
Air passes through entire filter
Harder to clean deep folds
8 inches
56 inches

## Slide 77: Chapter 2: Control of Particulate Emissions Disposable Filter – Operation
Disposable Filters
Exhaust air flows into filter
Particulates trapped in filter
Clean air flows from filter
As filter collects particulate, airflow is restricted
  Saturated filters disposed of as solid waste
Clean Gas
Dirty Gas

## Slide 78: Chapter 2: Control of Particulate Emissions Disposable Filter – Types
Disposable Coarse Filters
Used for large particulate with large airflows
  Lower pressure drop

## Slide 79: Chapter 2: Control of Particulate Emissions Disposable Filter – Types
Other Disposable Cartridge Filters
HEPA / ULPA Filters
  Higher particulate collection efficiency
  Unable to be cleaned (disposable)
  Airflow decreases as filter becomes clogged

## Slide 80: Chapter 2: Control of Particulate Emissions Reusable Filter – Types
Reusable Filter Types
Fabrics: Traditional fibers formed into bags or socks
  Woven: Interlaced yarns, like clothing
    Membrane: Plastic with small pores laminated onto woven fabric
  Felted: Randomly oriented fibers pressed together
    Metal Fiber: Felted metal fibers
Cartridges: Fabrics wrapped around a cylinder
  Pleated: Folded fabrics
  Ceramic: Cast ceramic

## Slide 81: Chapter 2: Control of Particulate Emissions Reusable Filter – Cleaning Mechanisms
Reverse Air
Pulse Jet
Shaker

## Slide 82: Chapter 2: Control of Particulate Emissions Filtration – Design Considerations
Fabric Filter Cleaning Mechanisms
Mechanical Shaker
  Baghouse offline during cleaning (2× baghouses)
Reverse Air
  Long time to clean
  Baghouse offline during cleaning (2× baghouses)
Pulse Jet
  Need high air pressure source (air compressor)
  Baghouse cleaning online

## Slide 83: Chapter 2: Control of Particulate Emissions Mechanical Shaker
Shaker Baghouse
Exhaust air flows inside of bags
Clean air flows outside of bags
Mechanical shaking cleans bags
  Electric motor provide shaking via rocker arms
Dampers
Dust to
Hopper

## Slide 84: Chapter 2: Control of Particulate Emissions Mechanical Shaker – Example
Shaker
Mechanism

## Slide 85: Chapter 2: Control of Particulate Emissions Mechanical Shaker – Example
Shaker
Mechanism
Shaker
Mechanism

## Slide 86: Chapter 2: Control of Particulate Emissions Video
PM 2.1 - Baghouse Shaker.mp4
4.2 – Manual Shaker Baghouse
4.3 – Shaker Baghouse

## Slide 87: Chapter 2: Control of Particulate Emissions Reverse Air
Reverse Air Baghouse
Exhaust air flows inside of bags
Cleaned air flows outside of bags
  Most cleaned air exits stack
  Some air provides counterflow
Counterflow air cleans bags
Counterflow air exhaust mixes with exhaust air to be cleaned
Dampers
Dust to
Hopper
Dirty Gas
Clean Gas

## Slide 88: Chapter 2: Control of Particulate Emissions Reverse Air – Example
Plenum
Plenum
Bag Level

## Slide 89: Chapter 2: Control of Particulate Emissions Video
PM 2.2 - Baghouse Reverse Air.mp4

## Slide 90: Chapter 2: Control of Particulate Emissions Reverse Air – Example
Reverse Air Baghouse (Interior)

## Slide 91: Chapter 2: Control of Particulate Emissions Reverse Air / Shaker Baghouse – Sonic Horn
Sonic Horn
Uses acoustics to vibrate bags, assist in removing dust layer
Used on Shaker and Reverse Air Baghouses
Sonic
Horns

## Slide 92: Chapter 2: Control of Particulate Emissions Pulse Jet Baghouse
Pulse Jet Baghouse
Exhaust air flows outside of bags
Clean air flows inside of bags
Short burst of compressed air into bags cleans outside of bags
  Continuous: Airflow does not have to be stopped during cleaning
Compressed
Air
Dust to
Hopper
Dirty Gas
Clean Gas

## Slide 93: Chapter 2: Control of Particulate Emissions Pulse Jet Baghouse – Example
High-Pressure Manifold

## Slide 94: Chapter 2: Control of Particulate Emissions Pulse Jet Baghouse – Example
Pulse Jet Baghouse (Interior)

## Slide 95: Chapter 2: Control of Particulate Emissions Cartridge Filter Example

## Slide 96: Chapter 2: Control of Particulate Emissions Cartridge Filter Example
Cartridge Baghouse Interior

## Slide 97: Chapter 2: Control of Particulate Emissions Video
PM 2.3 - Baghouse Pulse Jet.mp4
4.4 – Pulse Jet Baghouse
4.5 – Pulse Jet Cleaning
4.6 – Cartridge Filter
PM 2.4 - Alternatives.mp4

## Slide 98: Chapter 2: Control of Particulate Emissions Filtration – Control Efficiency
Control Efficiency
95-99.9% for PM10
95-99% for PM2.5
Lowest for just after filter replacement
  New filters have to buildup dust cake to reach design control efficiency

## Slide 99: Chapter 2: Control of Particulate Emissions Filtration – Parametric Monitoring
Parametric Monitoring
Continuous Emissions Monitoring System (CEMS)
Leak Detection System
Pressure Differential (ΔP)
Visible Emissions (VE) Checks

## Slide 100: Chapter 2: Control of Particulate Emissions Filtration – Operating Problems: All Filters
Fabric Holes, Tears, and Gaps
  Particles bypass filter and exit directly through stack
  Particle abrasion, heat, and acid gases wear down filters faster
  Pulse Jet: filter pores expand during cleaning, allowing particulate through the filter
  Pulse Jet: cleaning process increases filter deterioration rate
High Air-to-cloth Ratio
  Higher ratio (due to higher gas velocities) cause particles to migrate through the filter, reducing control efficiency
  Pore collapse where large particles push through fabric, expanding pore

## Slide 101: Chapter 2: Control of Particulate Emissions Filtration – Operating Problems: All Filters
Fires / Explosions
  Small particulate is highly flammable
  Particle movement creates static electricity
  High operating temperatures

## Slide 102: Chapter 2: Control of Particulate Emissions Filtration – Operating Problems: Reusable Filters Only
Blinding (Blockage)
  Filter cleaning ineffective if wet materials, oil, or water accumulates on filter
  Pulse Jet: compressed air usually has oil droplets in it
Particle Re-entrainment
  Particles released during cleaning process remain in air
    Do not settle into dust collection system (hopper)
    Smaller particles that do not collect into cake take longer to settle
  Corrective measures
    Reverse Air / Shaker – Longer delay after cleaning but before use
    Pulse Jet – Compartmentalize bags and switch compartments to allow material to settle after cleaning

## Slide 103: Chapter 2: Control of Particulate Emissions Filtration – Operating Problems: Pulse Jet Only
Compressed Air (Pulse Jet Only)
Compressed Air Supply Problems
  Air hoses all connected?
  Signs of wear or rust on air hoses and connections
  Pressure gauge during cleaning (need 60-120 PSIG)

## Slide 104: Chapter 2: Control of Particulate Emissions Video
4.7 – Combustible Dust

## Slide 105: Chapter 2: Control of Particulate Emissions Filtration – Inspection Parameters
Inspection Parameters
Visible emissions
Static pressure drop
Gas Temperatures
Evidence of Air infiltration
  Inlet / outlet temperature or oxygen content
  Holes, dents, or weld failures
  Corrosion
Cleaning Devices
Compressed Air (Pulse Jet)
□ Visible Emissions
□ Visible Inspection
□ Pressure Drop
□ Gas Monitoring
□ Emissions Testing
□ Internal Inspections

## Slide 106: Chapter 2: Control of Particulate Emissions Filtration – Overview
Filtration: Diesel Particulate Filter (DPF)
Honeycomb of ceramic or metal fibers collecting carbon deposits from engine (soot)
  Carbon collection increases back pressure on DPF (air is restricted)

## Slide 107: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter –Examples

## Slide 108: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Types
DPF Types:
Single Use: Replaced after a set number of operating hours
Regeneration: Soot is burned off with hot air (480ºF-1,200ºF)
  Active Regeneration
  Passive Regeneration
  Hybrid Regeneration

## Slide 109: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Types
Active Regeneration: Heater provides 1,200º hot air to clean soot from filter when engine is offline
Electricity Fuel Dosing
Externally powered Separate burner
using vehicle fuel

## Slide 110: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Types
Passive Regeneration: NO2 used as a catalyst to oxidize soot
NO2 oxidation occurs at 480ºF
NO2 can be generated by Diesel Oxidation Catalyst (DOC) during sustained engine use (>15 minutes at highway speeds)

## Slide 111: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Types
Hybrid Regeneration: Both options used to regenerate DPF
Passive regeneration while using engine
Active regeneration when engine is not being used

## Slide 112: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Control Efficiencies
DPF
80-97% Control Efficiency

## Slide 113: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Operating Problems
Operating Problems:
Filter regeneration requires power / fuel
Filter regeneration does not fully clean filter
Engine operation is changed during regeneration cycle (passive / hybrid)
Regeneration more often for engines idling often

## Slide 114: Chapter 2: Control of Particulate Emissions Diesel Particulate Filter – Compliance Inspection
Inspection Parameters
Visible emissions
Static pressure drop / backpressure
Oxygen content / gas monitoring
Regeneration cycle
  Hours of operation
□ Visible Emissions
□ Pressure Drop
□ Gas Monitoring
□ Regeneration Cycle
□ Emissions Testing
□ Internal Inspections

## Slide 115: Chapter 2: Control of Particulate Emissions​ Overview
Wet Scrubbers transfer particles from a gas stream to a liquid stream. For PM control, water is the most common scrubber liquid.

## Slide 116: Chapter 2: Control of Particulate Emissions​ Principle of Operation
Multiple forces trap particulates in liquid
Impaction
Diffusion
Electrostatic Attraction

## Slide 117: Chapter 2: Control of Particulate Emissions​ Principle of Operation
Wet Scrubbers: 2-Part Process
Contact: Wet scrubber mixes water with exhaust gases
  Clean (or recycled wastewater) is mixed with exhaust gases
Separation: Mist eliminator separates dirty water from clean gas
  Dirty water removed from exhaust gases for wastewater treatment (discharge / recycle)

## Slide 118: Chapter 2: Control of Particulate Emissions​ Video
PM 3.0 - Wet Scrubbers Intro.mp4

## Slide 119: Chapter 2: Control of Particulate Emissions Wet Scrubber – Design Considerations
Chevron
Mesh / Woven Pad
Radial Vane
Cyclone

## Slide 120: Chapter 2: Control of Particulate Emissions​ Mist Eliminators
Mist Eliminator | Orientation | Maximum Velocity (feet/second)
Chevron (Zigzag) | Horizontal | 15 – 20
Chevron (Zigzag) | Vertical | 12 – 15
Mesh Pad | Horizontal | 15 – 23
Mesh Pad | Vertical | 10 – 12
Woven Pad | Vertical | 8 – 15
Multiclone (Tube Bank) | Horizontal | 18 – 23
Multiclone (Tube Bank) | Vertical | 12 – 16

## Slide 121: Chapter 2: Control of Particulate Emissions Video
PM 3.6 - Wet Scrubbers Mist Eliminators.mp4

## Slide 122: Chapter 2: Control of Particulate Emissions​ Design Considerations
Water Supply
  Need a large supply of water to operate
  Water is the most common scrubbing liquid (scrubbing liquor)
  To minimize the amount of wastewater generated, scrubber liquid can be filtered, and the pH adjusted for reuse (alkali addition)
Alkali addition
  Alkali materials (lime, soda ash, sodium hydroxide) can be added to scrubber liquid to neutralize acidic PM and acid gases (NOX & SO2)
Liquid-to-Gas Ratio
  Gallons of liquid per 1,000 actual cubic feet (acf) of gas flow
  PM collection requires between 4-20 gallons / 1,000 acf

## Slide 123: Chapter 2: Control of Particulate Emissions​ Design Considerations
Exhaust gas characteristics
  Pre-coolers required to reduce high exhaust gas temperatures (if >212ºF, water may boil and reduce collection efficiency)
Gas Velocity
  Gas velocity cannot exceed the ability for liquid to drain by gravity (tower scrubbers) or liquids will collect (flood)
Wastewater treatment
  PM in scrubber liquid is a water pollutant
    Total suspended solids (TSS) / total dissolved solids (TDS)
    Must be removed before discharge to waterways
  PM in scrubber liquid erode pipes, valves, and nozzles faster

## Slide 124: Chapter 2: Control of Particulate Emissions​ Example Process Flow Diagram
Simple

## Slide 125: Chapter 2: Control of Particulate Emissions​ Example Process Flow Diagram
Recycled Water

## Slide 126: Chapter 2: Control of Particulate Emissions​ Example Process Flow Diagram
Alkali Addition

## Slide 127: Chapter 2: Control of Particulate Emissions​ Scrubber Examples

## Slide 128: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers

## Slide 129: Chapter 2: Control of Particulate Emissions​ Classifying Wet Scrubbers
Magnehelic Gauge
Measures differential pressure (drop) across scrubber
Higher pressure, better liquor / air contact

## Slide 130: Chapter 2: Control of Particulate Emissions​ Classifying Wet Scrubbers
Generally, wet scrubbers are classified by the pressure differential (drop) across the scrubber
  Pressure differential is a measure of the energy being used by the scrubber
  Often, higher pressure differential removes smaller PM
  Exceptions are for ionized scrubbers, fiber bed scrubbers, and condensation scrubbers (scrubbers used to cool a gas stream)

## Slide 131: Chapter 2: Control of Particulate Emissions​ Classifying Wet Scrubbers
Wet Scrubber | Classification | Pressure Differential | Particle Range
Spray tower | Low energy | <5 in. W.C.† | ≥PM5.0
Fiber bed | Low energy | <5 in. W.C. | ≥PM1.0
Corolis | Low energy | 0.5 – 6 in. W.C. | ≥PM5.0
Wet Fan | Medium Energy | 4 – 10 in. W.C. | ≥PM5.0
Packed bed | Medium energy | 5 – 25 in. W.C. | ≥PM1.0
Impingement | Medium energy | 5 – 25 in. W.C. | ≥PM1.0
Catenary | Medium energy | 4 – 40 in. W.C. | ≥PM1.0
Venturi | Medium energy | 5 – 25 in. W.C. | ≥PM1.0
Venturi | High energy | 25 – 100+ in. W.C. | ≥PM0.1
† Inches of Water Column |  |  | 

## Slide 132: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Spray Tower Scrubber
Spray nozzles generate droplets
  Relatively large water droplets (500 µm)
Gas passes upwards, contacting droplets
  Relies on impaction to collect PM
  Mainly used for other air pollutants (VOC, NOX, SO2)

## Slide 133: Chapter 5: Wet Scrubbers Video
PM 3.1 - Wet Scrubbers Spray.mp4

## Slide 134: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Mechanically Aided Scrubber (Induced)
Spray nozzles generate droplets
Rotors induce cyclonic flow for gas to contact droplets
  Relies on impaction to collect pollutants
Relatively high maintenance requirements

## Slide 135: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Mechanically Aided Scrubber (Cyclone)
Cyclone + Wet Scrubber
Spray nozzles generate droplets
Shell induces cyclonic flow for gas to contact droplets
  Relies on impaction to collect PM

## Slide 136: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Mechanically Aided Scrubber (Centrifugal)
Spray nozzles generate droplets
Fan causes gas contact with droplets
  Relies on impaction to collect PM

## Slide 137: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Packed Bed Scrubber
Gas passes upwards through tower, trapped in thin liquid film on packing
  Limit on upward gas velocity to keep liquid on packing
  Primarily used for vapor (VOC, NOX, SO2) control, as high PM concentration plugs scrubber
Mist eliminator usually is last layer of packing (dry)

## Slide 138: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Packed Bed Scrubber
Spray nozzles coat packing with thin liquid film
Gas passes through packing with pollutants trapped in liquid film
  Packing designed to provide largest liquid surface area
Horizontal (crossflow) is better for PM control

## Slide 139: Chapter 2: Control of Particulate Emissions​ Video
PM 3.2 - Wet Scrubbers Packed Bed.mp4
5.2 – Packed Bed Wet Scrubber

## Slide 140: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Ionizing Scrubber
Electrostatic attraction used to collect PM
  Discharge electrodes impart a negative charge onto particles in inlet gas stream
Crossflow packed bed is used to collect PM into scrubber liquid

## Slide 141: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Packed Bed Scrubber Packing

## Slide 142: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Fiber Bed Scrubber
Fabric Filter + Wet Scrubber
  Mist eliminator as a wet scrubber
Effective as a semi-dry scrubber for soluble PM (acids)
  Absorbing liquid can be a solvent for VOC control
Easily become plugged

## Slide 143: Chapter 2: Control of Particulate Emissions​ Video
PM 3.4 - Wet Scrubbers Fiber Bed.mp4

## Slide 144: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Fluidized bed: Two-phase mixture of liquid and gas, with gas passing through a mobile liquid zone to increase PM collection
  Mobile Media: Turbulent contact absorber uses movable media (ping-pong balls) to increase contact and mixing between gas and liquid
  Impingement: Liquid bubbles formed randomly on mesh / screen trays (ebulation) to increase contact and mixing between gas and liquid
  Swirling (Cyclonic): Rotation of gas and liquid causes increase turbulence and mixing; Rotation imparted by angled vanes and Coriolis effect (Earth’s rotation)

## Slide 145: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Impingement (Tray) Scrubber
Liquid flows downward, coating trays
Gas passes upwards through tower
Ebulation bubbles form, collecting PM via impaction
Susceptible to plugging, flooding, and dumping

## Slide 146: Chapter 2: Control of Particulate Emissions Wet Scrubber – Plate (Tray) Operation
Impingement Scrubbers
Liquid cascades by gravity through downcomers
  Ebulation: Gas bubbles up through the liquid forming a froth on top of the plate
Plates spaced to maximize liquid / gas contact
  Increases pollutant absorption
Design considerations:
  Diameter, number of plates, type of plates, plate configuration (layout and spacing)

## Slide 147: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Types of Trays / Plates

## Slide 148: Chapter 2: Control of Particulate Emissions Video
PM 3.3 - Wet Scrubbers Tray.mp4
5.3 – Tray Wet Scrubber

## Slide 149: Chapter 2: Control of Particulate Emissions Wet Scrubber Comparison
Packed Bed Scrubbers
More common
Can become plugged by particulate (especially crossflow)
Better for corrosive pollutants
Lighter than plate / tray scrubbers
Plate / Tray Scrubbers
Allow larger temperature changes
Allow lower liquid flow rates
Allow gas flow rates
Foaming liquors
Chemical reactions between liquor and exhaust gas
Larger systems

## Slide 150: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Catenary Scrubber
Gas passes upwards through scrubber, contacting liquid droplets on catenary grids
  Gas movement causes liquid droplets to atomize
  Liquids collect where gas pressure is greatest
  Relies on impaction to collect PM
  Less susceptible to plugging than tray / plate scrubber

## Slide 151: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Catenary Screens
Catenary describes the type of parabolic curve for the screens
  Describes the shape of hanging chain or cable
  Liquid level greatest at lowest (center) point, where air velocity is highest
  RotaBed® grid is catenary grid with angled vanes to impart cyclonic flow to exhaust air entering fluidized bed

## Slide 152: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Coriolis Scrubber
Gas passes upwards through scrubber, rotating through fluidized bed
  Gas spin imparted by static vanes and Coriolis Effect (rotation of the Earth)
  Relies on impaction to collect PM
  Less susceptible to large ebulation formation than Cantenary scrubber

## Slide 153: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Orifice Scrubber
Inlet enters gas-liquid contact zone by passing over scrubbing liquid
Gas stream atomizes liquid droplets and circulates via gravity
  Relies on inertia and diffusion to collect PM

## Slide 154: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Venturi – Fixed Throat
Inlet gas accelerated to 300 – 600 feet per second at venturi throat
  Liquid droplet size 50 – 75 µm
Particulate collected via high inertial impaction due to difference between scrubber liquid and gas velocities
Continuous inlet gas flow rate

## Slide 155: Chapter 2: Control of Particulate Emissions Wet Scrubber – Types
Venturi – Adjustable Throat
Better control for variable inlet gas flow rate
  Dampers can be set to maintain a constant pressure differential across venturi throat
  Higher pressure drop, better collection efficiency for smaller PM
Throat dampers are subject to extreme abrasion

## Slide 156: Chapter 2: Control of Particulate Emissions​ Types of Wet Scrubbers
Venturi Scrubber
Walls and bottom of venturi chamber usually wetted / flooded to reduce abrasion
Significant mist elimination to remove dirty water
Large amounts of liquid waste (wastewater) generated and must be processed
Pollutant
Gas Inlet
Water
Venturi
Throat
Flooded
Elbow
Water
Mist
Eliminator
Cleaned
Gas Out
Cyclonic
Separator
Dirty Water
(Liquid Waste)

## Slide 157: Chapter 2: Control of Particulate Emissions Video
PM 3.5 - Wet Scrubbers Venturi.mp4
5.4 – Venturi Wet Scrubber

## Slide 158: Chapter 2: Control of Particulate Emissions​ Control Efficiencies
Control Efficiency
Function of gas / liquid contact within scrubber
  Highest efficiencies for high energy venturi scrubbers (highest pressure drop)
  Lowest efficiencies for low energy tower scrubbers (lowest pressure drop)

## Slide 159: Chapter 2: Control of Particulate Emissions Wet Scrubber – Parametric Monitoring
Parametric Monitoring
Pressure Differential (ΔP)
Scrubber Liquid Flowrate
Visible Emissions (VE) Checks

## Slide 160: Chapter 2: Control of Particulate Emissions​ Wet Scrubber – Operating Problems
Scaling
  If pH gets too high (basic), scale will buildup in pipelines and scrubber
Corrosion
  Corrosive chemicals and water at high pressures can corrode or erode pipelines and scrubber shell
Droplet Re-entrainment
  Solids buildup on the mist eliminator
  Ice buildup on exhaust stack

## Slide 161: Chapter 2: Control of Particulate Emissions​ Wet Scrubber – Operating Problems
Deposits (Scaling) or Corrosion by pH

## Slide 162: Chapter 2: Control of Particulate Emissions Wet Scrubber – Operating Problems
Erosion: Leaking Components - Example

## Slide 163: Chapter 2: Control of Particulate Emissions​ Wet Scrubber – Operating Problems
Droplet Re-Entrainment – Example

## Slide 164: Chapter 2: Control of Particulate Emissions​ Wet Scrubber – Operating Problems
Plugging
  Tower scrubbers are susceptible to plugging (clogging)
  Buildup of wet particulate can plug nozzles, trays, and mist eliminators
  Exterior units can freeze during the winter
  Parametric monitoring ports can also become plugged
By-products are hard to recover
  Liquor recycling is not completely effective (some pollutants remain)
  Rely on desorption or wastewater treatment system

## Slide 165: Chapter 2: Control of Particulate Emissions Wet Scrubber – Operating Problems
Mist Eliminator Plugging – Example

## Slide 166: Chapter 2: Control of Particulate Emissions​ Wet Scrubber – Operating Problems
Flooding (Tray Scrubber)
  Upward gas velocity exceeds ability for liquid to drain (flooding velocity)
    Just before flooding occurs, control efficiency is greatest
  After flooding occurs, liquids collect into a greater mass and cause dumping (large amount of liquid deposits at once)
  Higher operating costs for higher efficiencies
Channeling (Packed Bed)
  Liquor channels along the sides of the cylinder instead of covering packing with thin film

## Slide 167: Chapter 2: Control of Particulate Emissions Wet Scrubber – Inspection Parameters
Inspection Parameters
Visible Emissions (VE)
Static Pressure Differential
Scrubber Liquid Flow Rate
Scrubber Liquid Parameters (pH)
Droplet Re-entrainment
Inlet and Outlet Temperatures
Ionizing Scrubbers: Electrical Data
□ Visible Emissions
□ Visible Inspection
□ Pressure Differential
□ Liquid Flow Rate
□ Liquid Parameters
□ Emissions Testing
□ Internal Inspections

## Slide 168: Chapter 2: Control of Particulate Emissions​ Compliance Parameters
Visible Emissions
  Exhaust plume will be saturated with water, potentially obscuring visible emissions of PM
  CEMS/Continuous Opacity Monitoring Systems (COMS) cannot be used because the presence of high concentrations of water creates erroneous readings

## Slide 169: Chapter 2: Control of Particulate Emissions​ Compliance Parameters
Scrubber Liquid Flow Rate
Scrubber liquid inlet and outlet flowrates monitored in gallons per minute
Decreasing flowrate indicates insufficient scrubber liquid to collect PM
Scrubber Liquid Parameters
Scrubber liquid must be treated if recirculated
  Solids removal (sampling)
  pH adjustment (sampling or inline sensor)

## Slide 170: Chapter 2: Control of Particulate Emissions​ Compliance Parameters
Ionizing Wet Scrubbers
Monitoring of electrical system for ionization of inlet gas stream
  Data collected on ionizers and equipment converting incoming alternating current (AC) to direct current (DC) used by ionizers
  Ionization process and electrical parametric monitoring will be discussed in Electrostatic Precipitators

## Slide 171: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Overview
ESP rely on electrical attraction for particulate removal
  Particles in exhaust stream are given an electrical charge
  Particles are attracted to collection surface with opposite electrical charge
Particles in exhaust stream must be able to hold an electrical charge
ESP works best under consistent conditions

## Slide 172: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Principles of Operation
Electrical charges are imbued onto particulates to attract them to collection surfaces

## Slide 173: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Principles of Operation
Particles are charged by gaining electrons (-) or removing electrons (+) in an electric field, attracting them to collectors with the opposing charge.

## Slide 174: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Principles of Operation
Electricity is used to impart an electrical charge (ionize) onto particles in the corona, attracting them to oppositely charged collection surface.

## Slide 175: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Examples

## Slide 176: Chapter 2: Control of Particulate Emissions Video
6.1 – 1917 ESP
PM 4.0 - ESP Intro.mp4

## Slide 177: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Operation
Dirty gas enters ESP
Particles ionized in electrode corona
Particles attracted to electrified collection plates
Collection plates de-electrified and cleaned, dust settles into hoppers
Dirty
Gas
Clean
Gas
Collection
Plates
Discharge
Electrode
(Ionizer)
Hoppers

## Slide 178: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Operation
Primary electrical power is 480 volt alternating current (AC)
Converted to secondary electrical power at 50,000 volts direct current (DC) in Transformer-Rectifier (T-R)

## Slide 179: Chapter 2: Control of Particulate Emissions Electrical Terms Explained
Electrical Terms in Water
Voltage = Water Pressure
  Higher voltage, more pushing
Current = Hose Diameter
  Higher current, more room
Resistance = Blockage
  Higher resistance, less flow
Voltage=Pressure
Current=Diameter
Resistance=Blockage
Power (watt) = Current (amps)×Voltage (volts)
Power (watt) = Current (amps)2×Resistance (ohms)
Voltage (volts) = Current (amps)×Resistance (ohms)

## Slide 180: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
ESP Design Considerations
Collecting (Charging) Particles
Gas Preparation
Cleaning
Collection Plates or Tubes
Dry or Wet
Electrode Types
Avoiding Short-Circuits

## Slide 181: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
ESP Design Requirements
High airflow rates
  200,000 – 1,000,000 scfm
High temperatures
  Up to 1,300 °F
Pollutant Loading
  1 – 50 grains/scf

## Slide 182: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Particle Charging
Particles must be electrically charged for capture by collector plates
  Discharge electrodes create an area of fast-moving electrons
  Electrons knock electrons from close particles, giving them a positive charge and attracting them to the discharge electrode
  Most of the electrons are captured by particles, giving them a negative charge and attracting them to the collection plates
Discharge Electrode
Collection Plate

## Slide 183: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Resistivity
Impacts dust layer resistivity
  How well particles stick to collection plates
  Impacts plate cleaning
  Plate charge decreases with dust buildup
Thicker dust layer increases sparking – electrical discharge between electrode and plate

## Slide 184: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Resistivity & Temperature
Particle resistivity decreases at lower temperatures
Particle resistivity, exhaust composition, and temperature must be known to establish proper ESP voltage

## Slide 185: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Resistivity & Moisture
Resistivity decreases as moisture content increases
  Water serves as a conductive agent, changing resistivity
  Sulfur in fuel can also change resistivity
  Other materials (sulfur trioxide, ammonia) can be added to change resistivity
Moisture
Content

## Slide 186: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Number of Energized Fields
Field | Control Efficiency | Inlet | Outlet
1 | 67.5% | 100 lbs. | 32.5 lbs.
2 | 65.0% | 32.5 lbs. | 11.4 lbs.
3 | 65.0% | 11.4 lbs. | 4.0 lbs.
4 | 65.0% | 4.0 lbs. | 1.4 lbs.
Overall | 98.6% | 100 lbs. | 1.4 lbs.

## Slide 187: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Cold-Side / Hot-Side ESP
Heat exchangers / pre-heaters are incorporated into boilers and heat generating processes
Hot exhaust gases are pre-heat inlet gas (combustion air)

## Slide 188: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Cleaning
ESP cleaning occurs during ESP operation
Most particles collect on collector plates, but some particles collect on discharge electrode
Thickness of dust layer affects voltage differential between electrode and plates (ESP control efficiency)
Particles should agglomerate into large clumps or sheets for low re-entrainment during cleaning

## Slide 189: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Types
Wire Discharge Electrodes
Frame Discharge Electrodes

## Slide 190: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Corona: Charge Types
Positive or negative charge can be imparted on particles by discharge electrode
Negative Corona:
  Dry ESP with Plates
  Wet ESP with Plates
  Wet ESP with Tubes
Positive Corona
  Wet ESP with Plates only

## Slide 191: Chapter 2: Control of Particulate Emissions Video
PM 4.1 - ESP Dry.mp4
6.2 - ESP
PM 4.2 - ESP Wet Negative.mp4
PM 4.3 - ESP Wet Positive.mp4

## Slide 192: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Design Considerations
Cleaning: Types
Dry Plate
  Most common, especially for larger sources
  Cement kilns, kraft pulp mills, coal-fired utility boilers, petrochemical
Wet Plate
  More complicated system used in smaller sources
  Used for sticky or carbonaceous materials
Wet Tube
  Used as secondary control for finishing or polishing (final removal of particulates)

## Slide 193: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Types
Dry Collection Plate

## Slide 194: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Cleaning Types
Rapper Types
Vibration: wires are twisted
Tumbling: electric motor turns shaft with tumbling hammers
Mechanical: hammer impact
  Pneumatic: air pressure pushes hammer
  Electromagnetic: electric current creates magnetic field, lifting plunger
Vibrating
Wires

## Slide 195: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Examples
Dry ESP Rappers
Mechanical
Pneumatic
Electromagnetic

## Slide 196: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Types of Cleaners
Sonic Horn
Uses acoustics to vibrate plates, assist in removing dust layer

## Slide 197: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Types
Wet Plate
Wet Tube

## Slide 198: Chapter 2: Control of Particulate Emissions Mist Eliminators
Chevron
Mesh / Woven Pad
Radial Vane
Cyclone

## Slide 199: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Operation
Gas Preparation
Inlet gas needs to be slowed down and evenly distributed over collection plates
Perforated gas distribution screens are used separate and slow inlet gases

## Slide 200: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Control Efficiencies
Control Efficiency
Primary determined by dust resistivity
  Newer units >99% control efficiency
  Older units 90-99% control efficiency
Factors impacting Efficiency
  Gas temperature, humidity, flow rate
  Particle resistivity
  Fly ash/Fuel composition
  Plate length
  Surface area

## Slide 201: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Control Efficiencies
Design Factors Affecting Performance
Number of Fields
Particle Resistivity
  Temperature
  Moisture Content
Collection Plate Spacing
Power Requirements/Spark Rate

## Slide 202: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Operating Problems
Ongoing changes in dust layer resistivity during operation
Changes in humidity or temperature in exhaust gas
Electric field misalignment / short circuiting
Damage to electrodes
Sneakage (exhaust gas bypassing control)
Explosion hazard from treating combustible gases
Electricity costs (and availability)

## Slide 203: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Parametric Monitoring
Parametric Monitoring
Primary voltage (V) and current (Amps)
Secondary voltage (V) and current (milliamps) or power (watts)
Spark Rate

## Slide 204: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Inspection Parameters
Inspection Parameters
Visible emissions (VE)
  Continuous Opacity Monitoring System (COMS)
Electrical Data
  Primary / Secondary Voltage
  Primary / Secondary Current
  Spark Rate
Cleaning Cycle Timing
Liquid Flowrate (Wet Only)
□ Visible Emissions
□ Visible Inspection
□ Electrical Data
□ Cleaning Cycle
□ Liquid Flowrate
□ Emissions Testing
□ Internal Inspections

## Slide 205: Chapter 2: Control of Particulate Emissions Electrostatic Precipitators – Visible Emissions
Visible Emissions (VE)
Short bursts of smoke (puffs) can be normal operation
  Particulate not captured as well during rapping
  Could be due to low resistivity or re-entrainment during rapping
Review opacity monitor data
  Duration and timing of puffs
  Long-term opacity changes
  Step changes in average opacity

## Slide 206: Chapter 2: Control of Particulate Emissions Combined Controls – Overview
Combined PM Controls
PM Controls can be combined
  Cyclone + Baghouse
  Baghouse + HEPA filter
  ESP + HEPA filter
  Wet Scrubber + Wet ESP
Best of both types of controls

## Slide 207: Chapter 2: Control of Particulate Emissions Video
6.3 – Combined Control Devices

## Slide 208: Chapter 2: Control of Particulate Emissions Review
This course answered the following questions:
  What is PM?
  What are the four types of PM controls?
  How do PM controls operate?
  How are PM controls designed?
  What is the expected control efficiency for a PM control?
  What are common problems with a PM control?
  How are PM controls monitored?

## Slide 209: Chapter 2: Control of Particulate Emissions Additional Resources
U.S. EPA Clean Air Technology Center (CATC)
Fact Sheets and Technical Bulletins: Summaries of air pollution control equipment
Air Pollution Control Cost Manual: Detailed information on air pollution control equipment and installation / operating costs
https://www.epa.gov/catc/clean-air-technology-center-products