## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 3: Volatile Organic Compounds
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 3: Volatile Organic Compounds Objective
To improve understanding of volatile organic compounds (VOC) control
  What is VOC?
  What are the five types of VOC controls?
  How do VOC controls operate?
  How are VOC controls designed?
  What is the expected control efficiency for a VOC control?
  What are common problems with a VOC control?
  How are VOC controls monitored?

## Slide 3: Chapter 3: Volatile Organic Compounds Introduction to Volatile Organic Compounds
O2
NOX
VOC
+ + =
O3
O3
Volatile Organic Compounds (VOC)
Colorless liquid organic compounds (hydrocarbons) with multiple scents (aromatic) that easily evaporate
  Volatile is any hydrocarbon evaporating at 230ºF (EPA Method 24)
Participates in a photochemical reaction to produce ozone
  VOC + NOX + Oxygen + Sunlight = Ozone (Smog)

## Slide 4: Chapter 3: Volatile Organic Compounds VOC Examples
VOCs are defined by exclusion: any organic compound not exempted in Title 40, Code of Federal Regulations, §51.100(s)
Common VOC-exempt Organic Compounds
Gases / Refrigerants | Industrial Chemicals
Carbon Dioxide | Ethane (Chemical Feedstock)
Carbon Monoxide | Acetone (Solvent)
Methane (Natural Gas) | Methylene Chloride (Solvent)
1,1,1,2-tetrafluoroethane (R-134a) | Perchloroethylene (Dry Cleaning)
Chlorodifluoromethane (R-22) | Methyl Chloroform (Degreasing)
Difluoromethane (R-32) | And many more…

## Slide 5: Chapter 3: Volatile Organic Compounds VOC Formation
VOC from evaporation in industrial processes
  Surface coating
  Synthetic organic chemical or pharmaceutical manufacturing
  Mold release (plastic, metal)
  Petroleum refinery
  Oil / gas transmission and distribution
VOC from incomplete combustion
  Engines
  Boilers

## Slide 6: Chapter 3: Volatile Organic Compounds VOC Impacts
Forms tropospheric ozone
  Triggers coughing, chest pain, airway inflammation, and throat irritation
  Damages sensitive vegetation, stunts crop growth, and increases risk of disease and insect damage
May cause damage to liver, kidneys, and nervous system
  VOC that cause health impacts likely classified as hazardous air pollutants (HAPs)

## Slide 7: Chapter 3: Volatile Organic Compounds Introduction to Hazardous Air Pollutants
Hazardous Air Pollutants (HAP): Toxic air pollutants that cause acute or chronic health effects or adverse environmental effects
  Biomagnification • Birth Defects
  Cancer • Reproductive Effects
187 toxic metals and organic compounds
  Asbestos • Benzene
  Dioxin • Hydrochloric Acid
  Mercury • Radionuclides
  Polychlorinated biphenyls (PCBs) and more…

## Slide 8: Chapter 3: Volatile Organic Compounds VOC Control Types
Five Types of VOC Control
  Minimization
  Oxidation (Combustion / Incineration)
  Condensation
  Absorption
  Adsorption

## Slide 9: Chapter 3: Volatile Organic Compounds Material Usage Minimization – Overview
Prevention Controls: Process Optimization
  Optimize the efficiency of applying VOC-containing materials reduces VOC emissions
    Increase transfer efficiency of spray coating (less coating used)
    Dip or powder coating is very efficient, but difficult to change colors

## Slide 10: Chapter 3: Volatile Organic Compounds Material Usage Minimization – Prevention
Spray Process | Transfer Efficiency
Conventional air spray | 15-40%
Conventional airless | 20-50%
Conventional air-assisted airless | 30-60%
Conventional High-Volume Low-Pressure (HVLP) | 30-60%
Electrostatic airless | 40-70%
Electrostatic air spray | 40-80%
Electrostatic air-assisted airless | 50-85%
Electrostatic HVLP | 60-90%
Electrostatic bell atomization | 70-95%
Electrostatic disk atomization | 80-95%
Electrostatic atomization | 95-98%
From Paint Technology Handbook, Roger Talbert, 2007 | 

## Slide 11: Chapter 3: Volatile Organic Compounds Material Usage Minimization – Prevention
Prevention Controls: Alternative Materials
Coatings can be reformulated to contain less VOC
  Use exempt organic compounds (acetone) from 40 CFR §51.100(s)
  Use water as a solvent (water-based paint)
Reformulation limited to coatings that are high use

## Slide 12: Chapter 3: Volatile Organic Compounds Oxidation – Overview
VOC Control: Oxidation
VOC in exhaust gas are heated above their auto-ignition temperature
  Heat provided by VOC in exhaust gas and supplemental fuel (usually natural gas)
Rapid chemical reaction where combustible air pollutants are oxidized to form CO2, water, and heat
  Includes flares, boilers, and thermal oxidizers

## Slide 13: Chapter 3: Volatile Organic Compounds Oxidation – Principles of Operation
The 3 T’s of Combustion
  Time: material is being combusted
  Temperature
  Turbulence: mixing of fuel and oxidizer (O2 in the air)

## Slide 14: Chapter 3: Volatile Organic Compounds Oxidation – Principles of Operation
Combustion generates additional pollution:
  Increase 3T’s = more CO2 and NOX (from N2 in the air)
  Decrease 3T’s = more CO and VOC (unburned hydrocarbons)

## Slide 15: Chapter 3: Volatile Organic Compounds Oxidation – Principles of Operation
Highest Efficiency
Most Power
More
Unburned Fuel
Decreased Temperature

## Slide 16: Chapter 3: Volatile Organic Compounds Video
VOC 1.0 - Combustion Intro.mp4

## Slide 17: Chapter 3: Volatile Organic Compounds Oxidation – Principles of Operation
Flare
VOC in exhaust gas are directly combusted in flame
Supplemental fuel (natural gas) can be added to the exhaust gas to increase flammability / temperature
Steam or air usually added at flare tip to increase turbulence and efficiency

## Slide 18: Chapter 3: Volatile Organic Compounds Oxidation – Flare Examples

## Slide 19: Chapter 3: Volatile Organic Compounds Video
VOC 1.1 - Combustion Flares.mp4
3.1 – Flare.wmv
3.2 - Ground Flare.wmv
3.3 – Flare.wmv

## Slide 20: Chapter 3: Volatile Organic Compounds Flare – Operation
Flare Tip
Exhaust gases are vented through holes in waste gas retention ring
  Supplemental natural gas may also be used
Steam is injected with waste gas, creating turbulence
Pilots using natural gas ignite exhaust gas

## Slide 21: Chapter 3: Volatile Organic Compounds Flare – Operation
Flare Tip

## Slide 22: Chapter 3: Volatile Organic Compounds Flare – Design Considerations
Only works on gaseous VOC
Flare height / location
  Noise
  Flame
  Temperature
  Exhaust gases
  Airfields / heliports
  Distance to property line
Airflow
  Maximum: flare tip size
  Minimum: supplemental gas

## Slide 23: Chapter 3: Volatile Organic Compounds Flare – Types
Four Types of Flares
  Steam-Assisted Flare
  Air-Assisted Flare​
  Non-Assisted Flare
  Pressure-Assisted Flare

## Slide 24: Chapter 3: Volatile Organic Compounds Flare – Types
Non-Assisted Flare
Only flare tip, no additional material for mixing
Typically used for gases with low heat content and low combustion temperatures

## Slide 25: Chapter 3: Volatile Organic Compounds Flare – Types
Steam-Assisted Flare
Single burner tips elevated above ground level for safety
Steam injected for turbulence and inducing air (reduces smoke)
Majority type of flare, predominantly used in refineries and chemical plants

## Slide 26: Chapter 3: Volatile Organic Compounds Flare – Types
Air-Assisted Flare
Air injected for turbulence and combustion (reduces smoke)
Air introduced by “spider” with many small orifices at burner tip
Generally not used when exhaust gas volume is large

## Slide 27: Chapter 3: Volatile Organic Compounds Flare – Types
Multipoint Flare
Pressure-Assisted flare with multiple flare tips
Additional tips become active in response to more pressure
From ENCORE THERMOENGINEERING S.r.l., Milano

## Slide 28: Chapter 3: Volatile Organic Compounds Flare – Types
Candlestick Flare Enclosed Flare

## Slide 29: Chapter 3: Volatile Organic Compounds Enclosed Ground Flare
Enclosed Flare (Stack)
Flare is located on the ground within the enclosure
Enclosure protects nearby area from intense noise, heat, and flame
Enclosure can have multiple flare tips (pressurized flare) for variable combustion
Stack test can be completed on enclosure

## Slide 30: Chapter 3: Volatile Organic Compounds Enclosed Ground Flare
Enclosed Flare (Ground)
Flare is located on the ground within the enclosure
Enclosure protects nearby area from intense noise, heat, and flame
Enclosure can have multiple flare tips (pressurized flare) for variable combustion
Stack test cannot be completed on enclosure

## Slide 31: Chapter 3: Volatile Organic Compounds Flare – Control Efficiencies
Control Efficiency
98% Reduction
  Exhaust gas with 300 British thermal unit (Btu) per scf
  Complies with requirements in 40 CFR §60.18(b)-(f)
  Control efficiency under review by U.S. EPA

## Slide 32: Chapter 3: Volatile Organic Compounds Flare – Operating Problems
Cannot stack test elevated flares
  May not be able to stack test enclosed flares
Flare tip subject to cracking due to heat
Pilots can be extinguished during high winds
Liquid slugs ejected as flaming fireballs
Produce undesirable noise, light, and heat
No heat recovery

## Slide 33: Chapter 3: Volatile Organic Compounds Flare – Compliance Inspection
Inspection Parameters
Visible emissions (Method 22)
Gas monitoring (Btu value)
  Addition of supplemental gas
Tip inspections
□ Visible Emissions
□ Visible Inspection
□ Gas Monitoring / Supplemental Gas
□ Tip Inspections

## Slide 34: Chapter 3: Volatile Organic Compounds Oxidation – Principles of Operation
Thermal Oxidizer
VOC in exhaust gas are combusted by increasing exhaust gas temperature above auto-ignition
  Auto-ignition temperatures 1,400ºF to 1,800ºF
Auxiliary fuel (natural gas / propane) is fired through a burner to increase exhaust gas temperature
  Large amounts of auxiliary fuel required

## Slide 35: Chapter 3: Volatile Organic Compounds Oxidation – Thermal Oxidizer Examples

## Slide 36: Chapter 3: Volatile Organic Compounds Video
VOC 1.2 - Combustion TO.mp4
3.4 – DFTO.wmv

## Slide 37: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Design Considerations
Good combustion requirements (3Ts):
Exhaust gas must reach autoignition Temperature of the VOC
  1,000-1,400ºF
Turbulent mixing with enough oxygen to fully oxidize VOC
Sufficient Time for reactions to occur
  0.2-2 seconds

## Slide 38: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Design Considerations
Thermal Oxidizer

## Slide 39: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Types
Four Types of Thermal Oxidizers
  Thermal Oxidizer (TO) – Wastes natural gas
  Recuperative Thermal Oxidizer (RCO)
  Regenerative Thermal Oxidizer​ (RTO)
  Catalytic Thermal Oxidizer (TO)

## Slide 40: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Types
Thermal Oxidizer
Burner
Waste Gas
Inlet
Refractory Brick
~1,200ºF

## Slide 41: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Types
Recuperative Thermal
Oxidizer (RCO)
Refractory Brick
Burner
Waste Gas
Inlet ~70ºF
Heat Exchanger
~650ºF
~1,200ºF

## Slide 42: Chapter 3: Volatile Organic Compounds Recuperative Thermal Oxidizer – Details
RCO
Pre-heat: heat exchanger transfers heat from hot exhaust gas stream to cool incoming gas stream
Combustion occurs at burners
  Burners can be sized smaller, as exhaust air is pre-heated

## Slide 43: Chapter 3: Volatile Organic Compounds Recuperative Thermal Oxidizer – Details
RCO
Thermal efficiency range of 30% to 70%
Shell & tube or plate-type
Usually constructed of alloy steel
Welded systems have very low leak rates
  Susceptible to leakage as heat exchanger ages
  Not used if acid gases (NOX or SO2) present; increases erosion
Susceptible to thermal shock on startup and shutdown

## Slide 44: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Types
Regenerative Thermal Oxidizer (RTO)
Waste Gas
Inlet
Clean Gas
To Stack
Valves
Burner
Ceramic
Bed
Ceramic
Bed

## Slide 45: Chapter 3: Volatile Organic Compounds Regenerative Thermal Oxidizer – Cycle
Left Combust / Right Cool
Left Cool / Right Combust

## Slide 46: Chapter 3: Volatile Organic Compounds Regenerative Thermal Oxidizer – Details
RTO
Ceramic beds are used to pre-heat incoming gas stream​
  Need pairs of regenerative beds​
Combustion occurs at burner(s)

## Slide 47: Chapter 3: Volatile Organic Compounds Regenerative Thermal Oxidizer – Cycle
Can or Rotary RTO

## Slide 48: Chapter 3: Volatile Organic Compounds Regenerative Thermal Oxidizer – Details
RTO
Heat recovery efficiency 80-95%
Resists corrosion of acid gases
  Susceptible to plugging
Highly resistant to thermal shock
  Packing can be random or structured
  Extremely tolerant of very high temperatures
Plenums switching air flow can introduce leaks
Can be used with catalysts (CO)

## Slide 49: Chapter 3: Volatile Organic Compounds Video
VOC 1.3 - Combustion RCO-RTO.mp4
3.5 - RCO.wmv
3.6 - RTO.wmv

## Slide 50: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Types
Catalytic Thermal
Oxidizer (CTO)
Catalyst
Bed
Burner
Waste Gas
Inlet
Heat Exchanger

## Slide 51: Chapter 3: Volatile Organic Compounds Catalytic Thermal Oxidizer – Details
CTO w/ Heat Exchanger

## Slide 52: Chapter 3: Volatile Organic Compounds Catalytic Thermal Oxidizer – Details
CTO
Catalyst causes oxidation to occur faster and at a lower temperature
  May use heat exchanger similar to recuperative thermal oxidizer
  Reduces autoignition temperature to 600ºF – 800ºF
  Lower temperature eliminates need for refractory lining
Combustion starts in combustion chamber (burners) and ends in the catalyst
Different catalysts work on different VOC
  Metal oxides can work on almost any compound
  Catalyst can last 2-5 years

## Slide 53: Chapter 3: Volatile Organic Compounds Catalytic Thermal Oxidizer – Details
Common Catalysts
Noble Metals​
  Platinum​
  Palladium​
  Rhodium​
Metal Oxides​
  Chromium oxide​
  Magnesium oxide​
  Cobalt oxide​
  Alumina

## Slide 54: Chapter 3: Volatile Organic Compounds Video
VOC 1.4 - Combustion CTO.mp4

## Slide 55: Chapter 3: Volatile Organic Compounds Catalytic Oxidizer – Overview
Diesel Oxidation Catalyst
Honeycomb of ceramic or metal fibers containing a precious metal catalyst for oxidation of CO and VOC

## Slide 56: Chapter 3: Volatile Organic Compounds Diesel Oxidation Catalyst – Examples

## Slide 57: Chapter 3: Volatile Organic Compounds Video
VOC 1.5 - Combustion Alternatives.mp4

## Slide 58: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Control Efficiencies
Control Efficiency
RCO: 90-99%
RTO: 95-99%
CTO: 95%
Highly dependent on VOC concentration in exhaust gas
  Increases with addition of supplemental fuel
DOC: 40-75%

## Slide 59: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Operating Problems
Thermal oxidizer shells subject to cracking due to heat
Use large amounts of natural gas
RTO subject to leaks due to gas switching
Heavy due to the use of refractory lining (except Catalytic TO)

## Slide 60: Chapter 3: Volatile Organic Compounds Catalytic Thermal Oxidizer – Operating Problems
Catalyst sensitive to thermal aging, poisoning, and masking (blinding)
  Thermal aging: elevated temperatures and relative humidity cause catalyst decomposition
  Poisoning: partial or total deactivation of catalyst by a chemical reaction (halides, sulfides, and nitriles)
  Masking / Blinding: material covering the catalyst (PM) so that it is unable to function
Catalyst replacement is very expensive
Catalyst disposal costs

## Slide 61: Chapter 3: Volatile Organic Compounds Thermal Oxidizer – Compliance Inspection
Inspection Parameters
Operating Temperature (Inlet and Outlet)
Oxygen Content (Inlet and Outlet)
Outlet VOC Concentration
  Continuous Emissions Monitoring System (CEMS)
Catalyst Life (Catalytic)
Valve timing (RTO)
Internal inspection
□ Temperatures
□ O2 Content
□ Emissions Testing
□ Internal Inspections
□ Visible Inspection
□ Catalyst Life

## Slide 62: Chapter 3: Volatile Organic Compounds Condensation – Principles of Operation
VOC Control: Condensation
VOC in exhaust are condensed (cooled) from gas to liquid​
  Change in physical state when air pollutant is cooled below its dew point by decreasing temperature and/or increasing pressure​
  Useful to recover air pollutant as a product​
Refrigerated condenser is a heat exchanger or pump​
  Absorbs heat from the exhaust gases in evaporator (causing condensation) and releases heat in chiller (another heat exchanger)​
  HFC or ODS commonly used in refrigerated condensers

## Slide 63: Chapter 3: Volatile Organic Compounds Condensation – Refrigerated Condenser Examples

## Slide 64: Chapter 3: Volatile Organic Compounds Video
VOC 2.0 - Condensation Intro.mp4
VOC 2.1 - Condensation Conventional.mp4
VOC 2.2 - Condensation Refrigeration.mp4
VOC 2.3 - Condensation Cryogenic.mp4

## Slide 65: Chapter 3: Volatile Organic Compounds Condensation – Refrigerated Condenser Cycle
Condensation: Refrigeration
VOC in exhaust are condensed (cooled) from gas to liquid​
  Change in physical state when air pollutant is cooled below its dew point by decreasing temperature and/or increasing pressure​
Refrigerated condenser is a heat exchanger or pump​
  Absorbs heat from exhaust gases in evaporator (condensation) and releases waste heat in condenser (heat exchanger)​

## Slide 66: Chapter 3: Volatile Organic Compounds Refrigerated Condenser – Design Considerations
Design Considerations
Residence Time
Exhaust Gas Temperature
Exhaust Gas Pressure
Coolant Temperature
VOC Dew Point
Surface Area (Surface Condenser)

## Slide 67: Chapter 3: Volatile Organic Compounds Refrigerated Condenser – Types
Surface Condenser
Coolant flows within tubes, does not contact air pollutant
Contact Condenser
Coolant sprayed into gas stream, contacts air pollutant

## Slide 68: Chapter 3: Volatile Organic Compounds Surface Condenser – Example

## Slide 69: Chapter 3: Volatile Organic Compounds Contact Condenser – Examples
Contact Condenser (Spray)
Contact Condenser (Ejector)

## Slide 70: Chapter 3: Volatile Organic Compounds Refrigerated Condenser – Control Efficiencies
Control Efficiency
50-95% Brine
90% Refrigerants
Highly dependent on VOC concentration (>5,000 ppm VOC) and temperature of exhaust gas

## Slide 71: Chapter 3: Volatile Organic Compounds Refrigerated Condenser – Operating Problems
Increase in exhaust gas temperature or flowrate
Decrease in VOC concentration
Change in VOC type (different dew points)
Tube plugging or fouling and erosion (brine)

## Slide 72: Chapter 3: Volatile Organic Compounds Refrigerated Condenser – Compliance Inspection
Inspection Parameters
Gas Temperature (Inlet and Outlet)
Coolant Temperature (Inlet and Outlet)
Coolant Flow Rate
Outlet VOC Concentration
Continuous Emissions Monitoring System (CEMS)
Static pressure drop
Internal inspection
□ Gas / Coolant Temp
□ Coolant Flow Rate
□ VOC Concentration
□ Pressure Drop
□ Emissions Testing
□ Visible Inspection
□ Internal Inspections

## Slide 73: Chapter 3: Volatile Organic Compounds Absorption – Principles of Operation
VOC Control: Absorption
VOC in exhaust absorbed (captured) by liquids
  Wet scrubber for VOC

## Slide 74: Chapter 3: Volatile Organic Compounds Absorption – Scrubber Examples

## Slide 75: Chapter 3: Volatile Organic Compounds Video
VOC 3.0 - Absorption Intro.mp4

## Slide 76: Chapter 3: Volatile Organic Compounds Absorption – Operation
Absorbers​
VOC in exhaust is removed by impacting liquids and being absorbed into a solvent​
  Ensure air pollutant (solute) is soluble for sorbent (solvent / liquor)
  Sorbent must be disposed of or desorbed (solute removed)​
Liquids removed from scrubber exhaust via mist eliminator
Secondary Process:
  Desorb (separate) VOC (solute) from sorbent (solvent / liquor)
  Dispose of sorbent with VOC as wastewater discharge or waste

## Slide 77: Chapter 3: Volatile Organic Compounds Absorber – Design Considerations
Same as PM Controls
  Liquid-to-Gas Ratio
  Exhaust Gas Characteristics
  Erosion / Plugging
Scrubber Liquid (Liquor)
  Absorption rate between solute (VOC) and solvent (scrubbing liquid)
  Water is most common scrubbing liquid
Wastewater treatment
  VOC in scrubber liquid is a water pollutant
    Standards for VOC oxidation and VOC content in wastewater discharges
    Must be removed before discharge to waterways

## Slide 78: Chapter 3: Volatile Organic Compounds Wet Absorption – Operation
Spray Chamber
Solvent sprayed counterflow directly into gas stream
Packed Bed
Solvent sprayed counterflow onto non-reactive packing

## Slide 79: Chapter 3: Volatile Organic Compounds Video
VOC 3.0 - Absorption Intro.mp4
VOC 3.1 - Absorption Spray.mp4
VOC 3.2 - Absorption Tray.mp4
VOC 3.3 - Absorption Packed Bed.mp4
VOC 3.5 - Absorption Mist Eliminator.mp4

## Slide 80: Chapter 3: Volatile Organic Compounds Absorber – Control Efficiencies
Control Efficiency
70-99%
Sorbent (solvent / scrubbing liquid) must be soluble for VOC (solute)

## Slide 81: Chapter 3: Volatile Organic Compounds Absorber – Operating Problems
Absorbent fouling
Desorb VOC or dispose of absorbent
Droplet Re-entrainment
  Solids buildup on the mist eliminator
  Ice buildup on exhaust stack
Wet Scrubbers
  Plugging
  Scaling
  Corrosion

## Slide 82: Chapter 3: Volatile Organic Compounds Absorber – Compliance Inspection
Inspection Parameters
Visible Emissions (VE)
Static Pressure Differential
Sorbent Flow / Addition Rate
Liquid Parameters (pH)
Droplet Re-entrainment (Wet Absorber)
Inlet and Outlet Temperatures
□ Visible Emissions
□ Pressure Drop
□ Sorbent Add Rate
□ Temperatures
□ Emissions Testing
□ Visible Inspection
□ Internal Inspections

## Slide 83: Chapter 3: Volatile Organic Compounds Adsorption – Principles of Operation
VOC Control: Adsorption
VOC in exhaust adhere to (captured by) solids (dry scrubber)

## Slide 84: Chapter 3: Volatile Organic Compounds Adsorber – Principles of Operation
Adsorption: Methods
VOC in exhaust (adsorbates) are removed by adhering to solid adsorbent via physical or chemical reaction
Physical Reaction: Adsorbate (pollutant) can be removed from adsorbent; no new chemical formed
  Physical reaction may be reversed onsite (concentrator) or offsite
Chemical Reaction: Adsorbate (pollutant) is bound to adsorbent and converted into a new chemical
  Discussed in Conversion Controls

## Slide 85: Chapter 3: Volatile Organic Compounds Adsorber – Principles of Operation
Adsorption: Saturation
Adsorbent becomes saturated with pollutant over time
  Must monitor exhaust for complete saturation (breakthrough)

## Slide 86: Chapter 3: Volatile Organic Compounds Adsorber – Examples

## Slide 87: Chapter 3: Volatile Organic Compounds Video
VOC 4.0 - Adsorption Intro.mp4
3.7 - Carbon Adsorption.mp4

## Slide 88: Chapter 3: Volatile Organic Compounds Adsorber – Design Considerations
VOC in exhaust stream
  VOC polarity: type of adsorbent
  Fouling adsorbents
VOC inlet concentration
Airflow
Temperature
  Below desorb temperature
  Carbon is flammable!
Relative humidity
Regenerative or Disposal

## Slide 89: Chapter 3: Volatile Organic Compounds Adsorber – Design Considerations
Activated Carbon
Molecular Sieve
Silica Gel
Zeolites
Adsorbents for Non-Polar Substance
Electrons shared equally by chemical bond, with no charged areas
Adsorbents for Polar Substance
Polar: Electrons shared unequally in chemical bond, with positively and negatively charged areas

## Slide 90: Chapter 3: Volatile Organic Compounds Adsorber – Design Considerations
Activated Carbon
  VOC molecular weight between 50 – 200
  Typically made from wood, coal, or plant materials
  Most common and cheapest
Zeolite / Molecular Sieve
  Crystals with uniform pores
  Pore size must match the diameter of the VOC
Silica Gel / Polymers / Alumina Oxide
  Matrix of small pores and high surface area
  High tolerance for water vapor

## Slide 91: Chapter 3: Volatile Organic Compounds Adsorber – Types
Non-regenerative Adsorbers
  Fixed Bed
  Injection
Regenerative Adsorbers
  Fixed Bed
  Moving Bed
  Fluidized Bed

## Slide 92: Chapter 3: Volatile Organic Compounds Non-Regenerative Adsorber – Types
Fixed Bed Non-Regenerative Adsorber

## Slide 93: Chapter 3: Volatile Organic Compounds Non-Regenerative Adsorber – Types
Dry Sorbent Injection (DSI)
Sorbent injected into exhaust stream
  Activated carbon injected to capture VOC
  Adsorption occurs in flue / duct
Desorption not conducted
  Activated carbon + VOC removed by PM control (filtration)

## Slide 94: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Types
Regenerative Adsorber / Concentrator:
Adsorbents with only physical binding to adsorbate can be desorbed via heat (regeneration)
Absorb Cycle: Collects air pollutants at variable concentration & flow
Desorb Cycle: Regenerates adsorbent; emits air pollutants at constant concentration and flow into secondary control device
  Pollutant “heel” builds up in adsorbent with each desorb cycle, reducing available adsorbent for collection (eventually leads to breakthrough)

## Slide 95: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Types
Fixed Bed Adsorber
Left Adsorb / Right Desorb
Fixed Bed Adsorber
Left Desorb / Right Adsorb

## Slide 96: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Types
Rotary Bed Regenerative Adsorber
Adsorbate rotates between adsorbing / desorbing
VOC Laden
Inlet Gas
VOC Laden
Outlet Gas
Cleaned Exhaust Gas to Stack
Warm Air Desorb
Clean Adsorbate
VOC Adsorbate
Rotation
Direction
To Secondary Control
From Process

## Slide 97: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Types
Moving Bed / Rotary Adsorber

## Slide 98: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Types
Fluidized Bed Regenerative Adsorber
Gas stream filtered through flowable solid adsorbent

## Slide 99: Chapter 3: Volatile Organic Compounds Regenerative Adsorber – Secondary Control
Fixed Bed Regeneration Fixed Bed Regeneration
and Recovery and Combustion

## Slide 100: Chapter 3: Volatile Organic Compounds Adsorber – Control Efficiencies
Control Efficiency
70-99%
Control efficiency separate from TO or Condenser
Breakthrough: 0% Control Efficiency

## Slide 101: Chapter 3: Volatile Organic Compounds Adsorber – Operating Problems
Channeling: exhaust air creates tunnels in adsorbent
Change in VOC
  Fouling of adsorbent
  Change in polarity may affect adsorption rate
Saturation: VOCs are not fully desorbed and eventually adsorbent must be replaced before breakthrough
Disposal of adsorbent (non-regenerative)
Secondary control:
  Thermal oxidizer or refrigerated condenser for desorbed VOC
  PM control for DSI

## Slide 102: Chapter 3: Volatile Organic Compounds Adsorber – Compliance Inspection
Inspection Parameters
Outlet VOC concentration
  Continuous Emissions Monitoring System (CEMS)
Regeneration cycle
Adsorbent replacement cycle
Inlet / Bed / Outlet temperatures
Pressure Differential
Internal Inspections
□ VOC Concentration
□ Pressure Drop
□ Regeneration / Replacement Cycles
□ Temperatures
□ Emissions Testing
□ Visible Inspection
□ Internal Inspections

## Slide 103: Chapter 3: Volatile Organic Compounds Review
This course answered the following questions:
  What is VOC?
  What are the five types of VOC controls?
  How do VOC controls operate?
  How are VOC controls designed?
  What is the expected control efficiency for a VOC control?
  What are common problems with a VOC control?
  How are VOC controls monitored?

## Slide 104: Chapter 3: Volatile Organic Compounds Additional Resources
U.S. EPA Clean Air Technology Center (CATC)
Fact Sheets and Technical Bulletins: Summaries of air pollution control equipment
Air Pollution Control Cost Manual: Detailed information on air pollution control equipment and installation / operating costs
https://www.epa.gov/catc/clean-air-technology-center-products