## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 4: Carbon Monoxide
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 4: Carbon Monoxide Objective
To improve understanding of carbon monoxide (CO) control
  What is CO?
  What are the three types of CO controls?
  How do CO controls operate?
  How are CO controls designed?
  What is the expected control efficiency for a CO control?
  What are common problems with a CO control?
  How are CO controls monitored?

## Slide 3: Chapter 4: Carbon Monoxide Introduction
Carbon Monoxide (CO)
Colorless, odorless gas that is harmful when inhaled
  Reduces amount of oxygen that can be transported in blood
No environmental effects at concentrations in ambient air
Insoluble in water
Very stable, therefore difficult to oxidize
Carbon monoxide is a result of incomplete combustion (not enough oxygen to form CO2)
  CH4 + O2 → 2CO + 2H2O

## Slide 4: Chapter 4: Carbon Monoxide Introduction
Three Types of CO Control
  Air/fuel ratio
  Catalysts
  Oxidation

## Slide 5: Chapter 4: Carbon Monoxide Air/Fuel Ratio – Principes of Operation
Air-to-Fuel Ratio (A/F Ratio or AFR)
Stoichiometric ratio of air (O2) and fuel needed for combustion
Rich Burn: Excess Fuel (lean air) with an A/F Ratio of ≤1.0
  AFR near 1.0 – lower concentration of O2
  Operates at a higher temperature
  More CO/VOC and less CO2/NOX in exhaust
Lean Burn: Excess Air (lean fuel) with an A/F Ratio >1.0
  AFR near 1.5 – higher concentration of O2 (Excess Air)
  Operates at a lower temperature
  Less CO/VOC and more CO2/NOX in exhaust
  All 2-stroke spark ignition and all compression ignition engines are inherently lean burn

## Slide 6: Chapter 4: Carbon Monoxide Air/Fuel Ratio – Operation
AFR Controller
Monitors oxygen and temperature in exhaust gas to ensure burners are operating with optimal flame
  O2 sensors
  Computer Controller
  Variable Speed Fan
  Air / Flue Gas Valves

## Slide 7: Chapter 4: Carbon Monoxide Flue Gas Recirculation – Operation
Flue Gas Recirculation (FGR)
Flue gas has a lower oxygen content than air and higher concentration of pollutants
FGR works as inert gas reducing combustion temperature and oxygen content
Exhaust
To Stack
Exhaust
To Burner

## Slide 8: Chapter 4: Carbon Monoxide Air/Fuel Ratio – Operating Problems
AFR
Engines are designed to be either rich burn or lean burn
  Compression ignition engines and 2-stroke spark ignition engines can only be lean burn
Lower limit for lean burn when flame cannot be supported
  Flameout / blowout
Decreasing CO increases NOX
FGR reintroduces air pollutants to combustion chamber, increasing (concentrating) air pollutants in ultimate exhaust

## Slide 9: Chapter 4: Carbon Monoxide Air/Fuel Ratio – Compliance Inspection
Inspection Parameters
Operating Temperature
Oxygen Content
CO Concentration
  Continuous Emissions Monitoring System (CEMS)
□ CO Concentration
□ Temperatures
□ Oxygen Content
□ Emissions Testing
□ Visible Inspection

## Slide 10: Chapter 4: Carbon Monoxide Fuel Additives – Operation
Oxygenated Fuel
By adding extra oxygen in the fuel, extra oxygen is available to ensure complete combustion
  CO is formed from incomplete combustion of hydrocarbons
  Oxygenated fuel helps CO oxidize to CO2

## Slide 11: Chapter 4: Carbon Monoxide Fuel Additives – Operating Problems
Oxygenated Fuels
Ethanol contains less energy per same unit of volume reducing energy efficiency of engine
Ethanol is corrosive to rubber and plastic (fuel lines)
Ethanol absorbs water

## Slide 12: Chapter 4: Carbon Monoxide Catalyst – Principes of Operation
Oxidation Catalyst
Catalyst causes CO oxidation to CO2
  700ºF – 1,000ºF temperature
  Transition group metals (platinum, ruthenium, rhodium, palladium, osmium, or iridum)
  May be applied as a coating over catalyst structure
CO gas must contact catalyst for conversion to CO2
Oxygen is mixed with exhaust gases in mixing chamber and flows through catalyst bed

## Slide 13: Chapter 4: Carbon Monoxide Catalyst – Example

## Slide 14: Chapter 4: Carbon Monoxide Catalyst – Design Considerations
Gas
Flow
Duct
Burner
Perforated
Plate
Outlet
Stack
SCR Catalyst
CO Catalyst

## Slide 15: Chapter 4: Carbon Monoxide Oxidation – Overview
Oxidation: Diesel Oxidation Catalyst
Honeycomb of ceramic or metal fibers containing a precious metal catalyst for oxidation of CO and VOC

## Slide 16: Chapter 4: Carbon Monoxide Diesel Oxidation Catalyst – Examples

## Slide 17: Chapter 4: Carbon Monoxide Catalyst – Compliance Inspection
Inspection Parameters
Pressure Differential
Operating Temperature
Oxygen Content
CO Concentration
  Continuous Emissions Monitoring System (CEMS)
Replacement frequency
□ CO Concentration
□ Pressure Drop
□ Replacement Cycle
□ Temperatures
□ Oxygen Content
□ Emissions Testing
□ Visible Inspection

## Slide 18: Chapter 4: Carbon Monoxide Catalyst – Control Efficiencies
Control Efficiency
90% for Catalyst
10-60% for DOC

## Slide 19: Chapter 4: Carbon Monoxide Catalyst – Operating Problems
Catalyst sensitive to thermal aging, poisoning, and masking (blinding)
Catalyst replacement expensive
Catalyst disposal costs
Plugging: Particulate control required before catalyst

## Slide 20: Chapter 4: Carbon Monoxide Oxidation – Principes of Operation
Oxidation
CO is oxidized at high temperature to CO2
  1,600ºF – 1,800ºF
  Oxidation controls generate NOX as a by-product
Three types of CO oxidizers:
Plume burners
Flares
Thermal oxidizers

## Slide 21: Chapter 4: Carbon Monoxide Oxidation – Principes of Operation
Plume Burner
No supplemental fuel (natural gas); combustion from waste gas only
Flare
Supplemental fuel (natural gas) may establish combustion
Thermal Oxidizer
Supplemental fuel (natural gas) establishes combustion
Waste
Gas
Natural
Gas
Waste
Gas
Natural
Gas
Waste
Gas
Natural
Gas
OR

## Slide 22: Chapter 4: Carbon Monoxide Oxidation – Principles of Operation
Plume Burner
CO in exhaust gas are directly combusted in self-generated flame
  No supplemental fuel is used as exhaust gas has sufficient heating value for combustion
  Waste gas ≥300 British thermal units/cubic foot
  Natural gas-fired pilot lights used to ensure combustion at stack tip

## Slide 23: Chapter 4: Carbon Monoxide Video
3.8 - Plume Burner.mp4

## Slide 24: Chapter 4: Carbon Monoxide Oxidation – Principles of Operation
Flare
CO in exhaust gas are directly combusted in self-generated or supplemented flame
  Supplemental fuel (natural gas) can be added to the exhaust gas to increase temperature
  Natural gas-fired pilot lights used to ensure combustion at flare tip
Steam or air usually added at flare tip to increase turbulence and efficiency

## Slide 25: Chapter 4: Carbon Monoxide Video
3.3 - Flare.mp4

## Slide 26: Chapter 4: Carbon Monoxide Oxidation – Principles of Operation
Thermal Oxidizer
CO in exhaust gas are combusted by increasing exhaust gas temperature above auto-ignition
  CO auto-ignition temperature 1,600ºF – 1,800ºF
Fuel (natural gas) is fired in a burner to increase exhaust gas temperature
  Large amounts of fuel required

## Slide 27: Chapter 4: Carbon Monoxide Oxidation – Examples
Flare Plume Burner Thermal Oxidizer

## Slide 28: Chapter 4: Carbon Monoxide Oxidation – Compliance Inspection
Inspection Parameters
Visible Emissions (Method 22)
Operating Temperature (TO only)
Oxygen Content (TO only)
CO Concentration (TO only)
  Continuous Emissions Monitoring System (CEMS)
□ Visible Emissions
□ CO Concentration
□ Temperatures
□ Oxygen Content
□ Emissions Testing
□ Visible Inspection

## Slide 29: Chapter 4: Carbon Monoxide Oxidation – Control Efficiencies
Oxidation Control Efficiency
95% for TO
No test data on flares / plume burners (can’t stack test)

## Slide 30: Chapter 4: Carbon Monoxide Oxidation – Operating Problems
Large amounts of supplemental fuel required for flares
Flare / Plume Burner: No heat recovery
High Maintenance
Plume Burner Flameout
  If CO concentration falls below minimum Btu to maintain a flame

## Slide 31: Chapter 4: Carbon Monoxide Review
This course answered the following questions:
  What is CO?
  What are the three types of CO controls?
  How do CO controls operate?
  How are CO controls designed?
  What is the expected control efficiency for a CO control?
  What are common problems with a CO control?
  How are CO controls monitored?

## Slide 32: Chapter 4: Carbon Monoxide Additional Resources
U.S. EPA Clean Air Technology Center (CATC)
Fact Sheets and Technical Bulletins: Summaries of air pollution control equipment
Air Pollution Control Cost Manual: Detailed information on air pollution control equipment and installation / operating costs
https://www.epa.gov/catc/clean-air-technology-center-products