## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 5: Control of Acid Gases
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 5: Control of Acid Gases Objective
To improve understanding of the acid gases nitrogen oxides (NOX) and sulfur dioxide (SO2) control
  What are NOX / SO2?
  What are the types of NOX / SO2 controls?
  How do NOX / SO2 controls operate?
  How are NOX / SO2 controls designed?
  What is the expected control efficiency for a NOX / SO2 control?
  What are common problems with a NOX / SO2 control?
  How are NOX / SO2 controls monitored?

## Slide 3: Chapter 5: Control of Acid Gases Introduction
Sulfur Dioxide (SO2)
Colorless gas with pungent odor
Irritates the respiratory system
In combustion, most of the sulfur in fuel is converted to SO2
Multiple environmental impacts:
  Forms acid rain that damages stone and decreases pH of lakes
  Damages foliage and decreases plant growth and crops from deposition
  Reacts in atmosphere to form fine particulates (PM2.5)

## Slide 4: Chapter 5: Control of Acid Gases Introduction
Nitrogen Oxides (NOX)
Reddish-brown gas with pungent, acrid odor
Irritates the respiratory system
Multiple environmental impacts:
  Forms acid rain that damages stone and decreases pH of lakes
  Contributes to nutrient pollution in coastal waters
  Reacts in atmosphere to form fine particulates (PM2.5) & ozone

## Slide 5: Chapter 5: Control of Acid Gases Introduction
NOX Formation from Combustion
NOX is formed when things burn
  Burning is oxidation reaction (materials gain oxygen and release heat)
  Nitrogen combines with oxygen during burning
  Nitrogen makes up majority of air (78%)
Three sources of NOX from combustion:
  Thermal NOX – Nitrogen from air is oxidized
  Prompt NOX – Nitrogen is oxidized by fuel
  Fuel NOX – Nitrogen in fuel is oxidized
4

## Slide 6: Chapter 5: Control of Acid Gases Acid Gas Control Types
Three Types of Acid Gas Control
Prevention
Absorption (Wet Scrubber)
Adsorption (Dry Scrubber)

## Slide 7: Chapter 5: Control of Acid Gases Prevention – Overview
NOX Prevention Strategies
Most NOX formed from combustion is thermal NOX
Thermal NOX Reduction options:
  Reduce oxygen concentration at peak flame temperature
    Reduce peak flame temperatures (<2,400°F)
    Less oxygen available to convert N2 into NOX
  Reduce residence time at peak temperature
  Decrease furnace heat release rate (energy produced)
NOX prevention interferes with the 3Ts of combustion
!

## Slide 8: Chapter 5: Control of Acid Gases Prevention – Overview
NOX Prevention Controls: Combustion (Burners)
Low excess air (LEA)
Excess Air Control
Burners Out-of-Service (BOOS)
Overfire Air (OFA)
Fuel Staging
Low NOX Burner (LNB)
Flue Gas Recirculation (FGR)
Ultra Low NOX Burner (ULNB)

## Slide 9: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Low Excess Air (LEA)
Reducing excess air (rich burn) reduces flame temperature and amount of nitrogen available for oxidation to NOX
  Lower A/F Ratio closer to 1 (stoichiometric)
  Moving from lean burn to rich burn

## Slide 10: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: LEA – Excess Air Control
Need equipment to monitor O2 and temperature in exhaust gas to ensure burners are operating with optimal flame
  Computer Controller for Air/Fuel Ratio (AFR)
  O2 sensors
  Thermometer
  Variable Speed Fan
Minimum excess air = lower NOX
  Can be combined with FGR
Sensors
AFR
Fan

## Slide 11: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Burners Out of Service (BOOS)
Unused burners continue to supply air, cooling flame temperature
  Reducing number of burners reduces NOX
  NOX reduction dependent on number of BOOS
  NOX reduction ceases, when burners
  return to service

## Slide 12: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Overfire Air (OFA)
Cooling flame temperature reduces nitrogen oxidation to NOX
Some combustion air diverted to create rich-burn fuel zone
  Primary air is mixed with fuel
  Secondary air is added in burner tip or via OFA ports
  Permanent BOOS

## Slide 13: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – OFA

## Slide 14: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Fuel Staging
Create multiple combustion zones to increase fuel combustion time
Fuel-rich zone with LEA
  Reducing excess air in the primary combustion
  zone reduces NOX
Fuel-lean zone with OFA
  Adding more air above flame
  allows combustion to finish at a lower
  temperature
Reduces NOX by 30%
Fuel Rich Zone (LEA)
Fuel Lean Zone (OFA)

## Slide 15: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Low NOX Burner (LNB)
Multiple stage combustion completely combusts fuel at a lower temperature
Primary air and fuel
  Rich burn (LEA) with 90% of fuel
  Lower NOX formation
Fuel reburning
  Lean burn with 10% of fuel
Final combustion
  Tertiary air w/ no fuel (OFA)

## Slide 16: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – LNB

## Slide 17: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention Controls: Ultra Low NOX Burner (ULNB)
Multiple stage combustion with flue gas recirculation (FGR) reduces oxygen used for a higher rich burn primary zone
Primary air and fuel
  Rich burn (LEA) with 90% of fuel & FGR
  Lower NOX formation
Fuel reburning
  Lean burn with 10% of fuel
Final combustion
  Tertiary air w/ no fuel (OFA)

## Slide 18: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – LNB/ULNB
Completely mix all fuel and expand combustion time
  Separate zones for air to fuel mixing and stratified combustion
  Fuel is burned a little in each zone over a few milliseconds, rather than combusted all at once in one zone
ULNB require:
  Separate air flow rate and swirl dampers
  Precise air flow control (AFR)

## Slide 19: Chapter 5: Control of Acid Gases Prevention – Operation
Prevention Controls: Flue Gas Recirculation (FGR)
Flue gas has a lower oxygen content than air and higher concentration of pollutants
FGR works as inert gas reducing combustion temperature and oxygen content
Exhaust
To Stack
Exhaust
To Burner

## Slide 20: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – NOX Concentration as %FGR

## Slide 21: Chapter 5: Control of Acid Gases Prevention – Operation
Prevention Controls: Air/Fuel Ratio (AFR) Controller
Equipment that monitors oxygen and temperature in exhaust gas to ensure burners are operating with optimal flame
  O2 sensors
  Computer Controller
  Variable Speed Fan
  Air / Flue Gas Valves

## Slide 22: Chapter 5: Control of Acid Gases Prevention – Combined Control Efficiencies
Combined NOX Control Efficiencies:
LNB: 50%-60%
LNB w/OFA: 70%
ULNB w/FGR: 90%
NOX can be further reduced with post-combustion controls

## Slide 23: Chapter 5: Control of Acid Gases Prevention – Operation
Steam / Water Injection
Water or steam is injected into flame area (combustion chamber of a turbine or heater)
Absorbs heat
Lowers flame temperature
Reduces NOX Formation

## Slide 24: Chapter 5: Control of Acid Gases Prevention – Example
Water / Steam Injection (Turbine)
Fuel Line
Steam Line

## Slide 25: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – Steam / Water Injection
Cooling effect of water / steam addition decreases NOX but increases CO and VOC
At a certain level, water will extinguish the flame
24

## Slide 26: Chapter 5: Control of Acid Gases Prevention – Operation
NOX Prevention – Steam / Water Injection
Rate of water/steam injection impacts thermal efficiency and power
  Water/steam injection increase mass flow rate
  Water/steam injection decreases thermal efficiency
25

## Slide 27: Course 418 – Chapter 5: Nitrogen Oxide Controls
Steam / Water Injection:
60-80% NOX Reduction

## Slide 28: Chapter 5: Control of Acid Gases Prevention – Operating Problems
Only reduces thermal NOX (prompt / fuel NOX unaffected)
Combustion modifications increase other air pollutants
  As combustion temperature decreases, products of incomplete combustion (CO and VOC) increase
Water/steam injection will eventually extinguish flame
Water/steam injection decreases thermal efficiency
Water quality must be high
Introduction of water causes rust formation

## Slide 29: Chapter 5: Control of Acid Gases Absorption – Overview
Absorption
NOX / SO2 in exhaust are absorbed (captured) by liquids or slurries (solid particles entrained in liquids)
  Wet / semi-dry scrubber

## Slide 30: Chapter 5: Control of Acid Gases Absorber – Principles of Operation
Absorbers (Wet Scrubber)​
NOX / SO2 in exhaust is removed by impacting liquids and being absorbed into a solvent​
  Ensure air pollutant (solute) is soluble for sorbent (solvent / liquor)
  Sorbent must be disposed of or desorbed (solute removed)​
Liquids removed from scrubber exhaust via mist eliminator

## Slide 31: Chapter 5: Control of Acid Gases Absorber – Scrubber Examples

## Slide 32: Chapter 5: Control of Acid Gases Absorber – Types
Wet Absorber (Scrubber)
Liquid sprayed directly onto exhaust gas
Semi-Dry Absorber
Slurry sprayed directly onto exhaust gas

## Slide 33: Chapter 5: Control of Acid Gases Absorber – Operation
NOX Absorption – Scrubbers
Semi-Dry Scrubber: Inject an alkaline slurry into an absorber chamber
  Sodium Hydrosulfide – NaHS
Wet Scrubber: Water treatment system to oxidize, then neutralize NOX
  Oxidizing Agent: Hydrogen Peroxide (H2O2) or Sodium Hypochlorite (NaClO)
  Neutralize: Sulfuric Acid (H2SO4) to lower pH or Sodium Hydroxide (NaOH) to raise pH

## Slide 34: Chapter 5: Control of Acid Gases Absorber – Operation
NOX Absorption – Wet Scrubbers Chemical Reaction
Convert NOX to water soluble compound for treatment
  Water: NOX naturally dissolves in water, forming HNO3 (nitric acid)
  Oxidation: NO / NO2 converted to NO3-, which is water soluble using an oxidizer in a slightly basic (alkaline) solution (pH 9)
  Acidification: Decreasing the pH of the scrubber liquor promotes the formation of insoluble NOX compounds
  Alkaline: Adding strong alkaline (NaOH or CaO) increases the pH and can increase the solubility of the NOX compounds
Most wet scrubbers are multi-stage with extensive wastewater treatment

## Slide 35: Chapter 5: Control of Acid Gases Absorber – Operation
SO2 Absorption – Semi-Dry Scrubber
Systems inject an alkaline slurry into an absorber chamber
  Limestone: Calcium Carbonate – CaCO3
  Slaked / Hydrated Lime: Calcium Hydroxide – Ca(OH)2
  Sodium Hydroxide - NaOH
Alkaline reagents react with acid gases to form salts
  CaCO3 + SO2 = CaSO3 + CO2
  Ca(OH)2 + SO2 = CaSO3 + H2O
  NaOH + SO2 = Na2SO3 + H2O

## Slide 36: Chapter 5: Control of Acid Gases Absorber – Operation
Flue Gas Desulfurization (FGD)
Moisture Separator: Prevents slurry from exhausting
Tank Agitator: Keeps solids in suspension
Absorption: SO2 absorbed in slurry of alkaline reagent
Quench: Saturates and cools flue (exhaust) gas

## Slide 37: Chapter 5: Control of Acid Gases Semi-Dry Absorber – Operation

## Slide 38: Chapter 5: Control of Acid Gases Wet Scrubbers – Examples

## Slide 39: Chapter 5: Control of Acid Gases Absorber – Design Considerations
Design Considerations
Exhaust gas temperature
Acid gas concentration
Presence of PM in exhaust gas
Chemical reaction with absorber
Size (wet scrubbers for NOX are LARGE)

## Slide 40: Chapter 5: Control of Acid Gases Video
5.0 - Absorption Spray Dryer.mp4

## Slide 41: Chapter 5: Control of Acid Gases Absorber – Control Efficiencies
Control Efficiency
70-99%
Solvent must be soluble for acid gases
Slurry must contain materials that chemically react with acid gases

## Slide 42: Chapter 5: Control of Acid Gases Absorber – Operating Problems
Wet / Semi-Dry Scrubbers
  Plugging
  Scaling
  Corrosion
  Droplet Re-entrainment
Semi-Dry Scrubbers
  PM control (filtration)

## Slide 43: Chapter 5: Control of Acid Gases Reduction – Overview
Reduction
NOX in exhaust is removed by chemical reduction
  Selective Catalytic Reduction (SCR)
  Selective Non-Catalytic Reduction (SNCR)
Reduction reaction requires high temperature

## Slide 44: Chapter 5: Control of Acid Gases Reduction – Operation
Selective Non-Catalytic Reduction (SNCR)
NOX is removed by mixing exhaust gas with liquid ammonia or urea in reactor chamber
No catalyst needed
NO + NO2 + 2NH3 → 2N2 + 3H2O

## Slide 45: Chapter 5: Control of Acid Gases Reduction – Operation
Selective Catalytic Reduction (SCR) / 3-Way Catalyst
NOX is removed by mixing exhaust gas with liquid ammonia or urea in exhaust stack
Catalyst causes NOX reduction to occur faster
Less ammonia used
  Less ammonia slip
Better NOX reduction than SNCR

## Slide 46: Chapter 5: Control of Acid Gases Reduction – Ammonia vs. Urea
Parameter | Ammonia | Urea
Injection Form | High Vapor Pressure Liquid Ammonia/Water Solution | Liquid Solution
Safety Concerns | Ammonia: Toxic (lungs, eyes), flammable, and corrosive | Limited Safety Concerns
Material Storage | Anhydrous: Pressure Vessel Aqueous: Atmospheric Tanks | Atmospheric Tanks (may crystalize at low temperatures)
Injectors | Needs Carrier Gas | Atomizer (Pressure or Twin Fluid)
Temperature | Peak Removal @ 1,750° F | Peak Removal @ 1,850° F Large Dilute Drops Shield Urea
System Complexity | Relatively Simple | Relatively Simple

## Slide 47: Chapter 5: Control of Acid Gases Reduction – Example
Ammonia Injectors
46

## Slide 48: Chapter 5: Control of Acid Gases Reduction – Example
Ammonia Injectors
47

## Slide 49: Chapter 5: Control of Acid Gases Reduction – Design Considerations
Design Considerations
Combustion unit size
Exhaust gas temperature / pressure
Acid gas concentration
Presence of PM in exhaust gas
Chemical reaction with absorber
Catalyst type (SCR)

## Slide 50: Chapter 5: Control of Acid Gases Reduction – Design Considerations
Gas
Flow
Duct
Burner
Perforated
Plate
Outlet
Stack
SCR Catalyst
CO Catalyst
Ammonia Injection

## Slide 51: Chapter 5: Control of Acid Gases SCR – Design Considerations
Selective Catalytic Reduction – Catalyst Types
Extruded Ceramic
Honeycomb
Plate
Corrugated
(Haldor-Topsoe)
Typical Catalysts:
Vanadium Pentoxide (V2O5)
Titanium Dioxide (TiO2)
Molybdenum
Tungsten

## Slide 52: Chapter 5: Control of Acid Gases SCR – Design Considerations
SCR Catalyst Bed (Power Plant)

## Slide 53: Chapter 5: Control of Acid Gases SCR – Design Considerations
PM Removal: Soot Blower
Uses steam / compressed air to clean catalyst
PM Removal: Sonic Horn
Uses sound
to clean catalyst

## Slide 54: Chapter 5: Control of Acid Gases Video
5.1 - SCR.wmv

## Slide 55: Chapter 5: Control of Acid Gases SCR – Other Uses
Diesel Exhaust Fluid (DEF) / SCR
DEF is aqueous urea added to diesel engines for NOX control
  Diesel engines are usually lean burn, with excess air generating NOX
DEF / SCR part of the “Diesel Catalytic Converter”

## Slide 56: Chapter 5: Control of Acid Gases SCR/SNCR – Design Considerations
Ammonia Slip
Incomplete reaction of ammonia / urea in exhaust gas
  Ammonia reacts with SO2 forming ammonia sulfates (erosion / plugging)
  Ammonia absorbed into fly ash (changing pH for disposal)
  Ammonia has a strong odor
Reaction is dependent on temperature and influenced by droplet size and loading rate

## Slide 57: Chapter 5: Control of Acid Gases SCR/SNCR – Ammonia Slip
Ammonia Slip
Ensure correct operating temperature (1,600°F to 2,000°F)
Monitor ammonia loading rate

## Slide 58: Chapter 5: Control of Acid Gases SCR/SNCR – Control Efficiencies
Control Efficiency
SNCR: 30-50%
SCR: 70-90%
SCR / SNCR Control Efficiencies

## Slide 59: Chapter 5: Control of Acid Gases SCR/SNCR – Control Efficiencies
Control Efficiency
SCR: 70-90%
SCR Catalyst Control Efficiencies

## Slide 60: Chapter 5: Control of Acid Gases SCR/SNCR – Operating Problems
SNCR/SCR
  High inlet NOX concentration
  Ammonia slip
  Exhaust gas temperature
  Reducer (ammonia vs urea)
  Formation of ammonia salts
SCR
  Fouling of catalyst
  PM covering catalyst

## Slide 61: Chapter 5: Control of Acid Gases Non-Selective Catalytic Reduction (3-Way Catalyst)
Non-Selective Catalytic Reduction (NSCR) or 3-way Catalyst
CO, NOX and hydrocarbons (VOC) are converted into CO2 and N2 via a catalyst (noble metal)
Catalyst causes CO and NOX to mutually annihilate each other
Does not need additional reagents (ammonia / urea)
60
CO
NOX
Hydrocarbons
CO2
N2
catalyst

## Slide 62: Chapter 5: Control of Acid Gases Non-Selective Catalytic Reduction (3-Way Catalyst)
NSCR / 3-Way Catalyst
Primarily used in Rich Burn engines (fuel rich / lean air)
2CO+2NO→2CO2+N2
NO+HC+O2→N2+CO2+H2O
Provides up to 98% control for CO and NOX
61

## Slide 63: Chapter 5: Control of Acid Gases Non-Selective Catalytic Reduction (3-Way Catalyst)
NSCR / 3-way Catalyst
62

## Slide 64: Chapter 5: Control of Acid Gases NSCR – Operating Problems
Requires AFR controller and O2 sensors
Inlet gas temperature must be 800-1,200ºF
Engine has to be operated within a specific range
Only available at lower sulfur levels (<200 ppmv)
  Must use low sulfur fuels

## Slide 65: Chapter 5: Control of Acid Gases Scrubbers – Compliance Inspection
Inspection Parameters
Solvent Flow / Addition Rate
Ammonia Slip (10-25 ppm)
Liquid Parameters (pH)
Droplet Re-entrainment (Wet Absorber)
Catalyst Life (SCR)
Inlet and Outlet Temperatures
□ Sorbent Add Rate
□ Ammonia Slip
□ Temperatures
□ Catalyst Life (SCR)
□ Emissions Testing
□ Visible Inspection
□ Internal Inspections

## Slide 66: Chapter 5: Control of Acid Gases Adsorption – Overview
Acid Gases Control: DSI
Acid gases in exhaust adhere to (captured by) solids
  DSI: Dry scrubber
SO2 / Hydrochloric acid (HCl)
  Hydrated Lime: CA(OH)2
  Soda Ash: NaHCO3
Mercury (Hg)
  Activated Carbon

## Slide 67: Chapter 5: Control of Acid Gases Adsorber – Principles of Operation
Adsorber: Dry Sorbent Injection
Air pollutants in exhaust (adsorbates) are removed by adhering to solid adsorbent via chemical or physical reaction
  Solid surface includes pores and cavities to trap air pollutants
  Chemical change can occur with adsorbent for HCl and SO2
  Physical capture of mercury (liquid / gaseous HAP)
Desorption not used for acid gases
Solids removed by particulate controls

## Slide 68: Chapter 5: Control of Acid Gases Adsorber – Examples

## Slide 69: Chapter 5: Control of Acid Gases Dry Adsorber – Operation
Dry Sorbent Injection
Hydrated lime or soda ash (powder) injected in gas stream to form solid salts
Particulate control required to remove salts

## Slide 70: Chapter 5: Control of Acid Gases Dry Adsorber – Operation
Dry Sorbent Injection
Activated carbon injected into exhaust stream to adsorb Hg
Particulate control required to remove activated carbon

## Slide 71: Chapter 5: Control of Acid Gases Dry Adsorber – Operation
Dry Sorbent Injection – Activated Carbon

## Slide 72: Chapter 5: Control of Acid Gases Adsorption – Control Efficiency
Control Efficiency
SO2: 50%
HCl: 98% (down to 0.002 lbs./MMBtu)
Hg: 90%

## Slide 73: Chapter 5: Control of Acid Gases Adsorption – Compliance Inspection
Inspection Parameters
Acid gas / Hg concentration
  Continuous Emissions Monitoring System (CEMS)
Gas temperatures (Inlet and Outlet)
Sorbent addition / flow rate
Pressure differential
Internal inspection
□ Concentration
□ Temperatures
□ Sorbent addition
□ Pressure Drop
□ Emissions Testing
□ Internal Inspections
□ Visible Inspection

## Slide 74: Chapter 5: Control of Acid Gases Prevention – Control Efficiencies
Technology | Control Efficiency | NOX lbs./MMBTU† | NOX ppmv‡ @ 3% O2
Standard Burners | N/A | 0.14 | 120
LNB | 60% | 0.06 | 45
1st Generation ULNB | 80% | 0.03 | 25
2nd Generation ULNB | 95% | 0.007 | 6
FGR | 55% | 0.025 | 20
Computer Controlled NOX with FGR | 90% | 0.015 | 12
SNCR | 40% | 0.033-0.085 | 27-70
Catalytic Scrubbing (Alkaline Wet Scrubber) | 70% | 0.017-0.044 | 14-36
SCR | 90-95% | 0.006-0.015 | 5-12
† Million British Thermal Units ‡ parts per million by volume |  |  | 

## Slide 75: Chapter 5: Control of Acid Gases Review
This course answered the following questions:
  What are NOX / SO2?
  What are the types of NOX / SO2 controls?
  How do NOX / SO2 controls operate?
  How are NOX / SO2 controls designed?
  What is the expected control efficiency for a NOX / SO2 control?
  What are common problems with a NOX / SO2 control?
  How are NOX / SO2 controls monitored?

## Slide 76: Chapter 5: Control of Acid Gases Additional Resources
U.S. EPA Clean Air Technology Center (CATC)
Fact Sheets and Technical Bulletins: Summaries of air pollution control equipment
Air Pollution Control Cost Manual: Detailed information on air pollution control equipment and installation / operating costs
https://www.epa.gov/catc/clean-air-technology-center-products