## Slide 1: Theory & Application of Common Air Pollution Control Devices
Chapter 6: Parametric Monitoring
Developed by:
Andrew D. Shroads, QEP
www.scainc.com

## Slide 2: Chapter 6: Parametric Monitoring Objective
To improve understanding of measuring parameters (monitoring) associated with operation of control devices
What are parametric monitors?
How do parametric monitors operate?
What are other parametric monitors?

## Slide 3: Chapter 6: Parametric Monitoring Overview
Parametric Monitoring
Control device parameters are ESSENTIAL to ensure proper operation for reducing emissions
Exhaust Gas Parameters: Ensure that the gas is within parameters for control device operation (e.g., temperature, flow rate)
Control Device Parameters: Diagnostic of control device operation (e.g., pressure drop, spark rate, pH)

## Slide 4: Chapter 6: Parametric Monitoring Monitor Requirements
Calibration
Each instrument and manufacturer has their own calibration requirements
Maintain a calibration log documenting calibrations and any manufacturer or standard calibrations
Include identification numbers for multiple units
Gas monitors usually require calibration gases, to ensure that the instrument can read within the span (high and low gas concentration)
Calibrated By:
Date:
6/18/2025

## Slide 5: Chapter 6: Parametric Monitoring Monitor Requirements
Location
Locate sampling ports to provide accurate readings and to reduce effects of plugging
  Sampling tubes must be sealed to sampling port to prevent air infiltration
  Conditions (e.g., temperature) may be different at duct edge versus duct center
  Water in exhaust stream can cause plugging / freezing

## Slide 6: Chapter 6: Parametric Monitoring Monitor Requirements
Data Collection
Data collected at the minimum frequency specified in permit
  Equipment usually provides continuous, instantaneous readings
  Digital equipment can be connected to a data logger
  Higher frequency = more data (and more deviations)

## Slide 7: Chapter 6: Parametric Monitoring Monitor Requirements
Accuracy vs. Precision
Accuracy: how close a measurement is to it’s true value
  Use the same number of significant digits as the reading
  Average of 3 and 4 is 4
  Average of 3.0 and 4.0 is 3.5
Precision: how close the measurements are to each other (random errors)
  Do not include data out of device range
  Device reads 0 to 5, so ignore <0 and >5

## Slide 8: Chapter 6: Parametric Monitoring Parametric Monitoring Equipment
Common Parametric Monitoring Equipment
Static Pressure (Differential Pressure or ΔP)
Temperature (Inlet / Outlet)
Oxygen (Inlet / Outlet)
Gas Flow (Inlet)
Gas Heat Value (Inlet)
Voltage / Amperage / Spark Rate (ESP / Ionized Scrubbers)
pH (Wet Scrubbers)
Liquid Flow (Inlet / Outlet on Wet Scrubbers)

## Slide 9: Chapter 6: Parametric Monitoring Parametric Monitoring
Static Pressure
Pressure differential (ΔP) between area measured and the atmosphere
  Gauge pressure: measurement is relative to atmospheric pressure
  Absolute pressure: measurement includes atmospheric pressure
Measured with a manometer or pressure differential gauge
  Pressure differential (ΔP) measured as before and after control device

## Slide 10: Chapter 6: Parametric Monitoring Parametric Monitoring
Temperature
Thermometers measures temperature (heat)
  Dial thermometer
  Thermocouple
  Infrared (measures surface temperature)

## Slide 11: Chapter 6: Parametric Monitoring Parametric Monitoring
Oxygen Content
Chemical Analysis: Liquid volume change due to chemical reaction
  Orsat or Fyrite® analyzer
Electromagnetic Analysis: Oxygen interferes with or generates electric current
  Electrochemical, paramagnetic, or mass spectrometer
Ultrasonic: Speed of sound is proportional to oxygen content

## Slide 12: Chapter 6: Parametric Monitoring Examples
Oxygen Content Analyzers
Orsat Fyrite

## Slide 13: Chapter 6: Parametric Monitoring Examples
Oxygen Content – Electrical Analysis Devices

## Slide 14: Chapter 6: Parametric Monitoring Parametric Monitoring
Gas Flow Meter
Flowrate through duct
Gas Heat Value / Energy Meter
Measures the heating value (British Thermal Units / Calories) of gaseous streams
Ensures gas stream meets minimum heat (Btu) value for combustion of VOC in exhaust gases
  Triggers addition of supplemental fuel to gas stream

## Slide 15: Chapter 6: Parametric Monitoring Parametric Monitoring
Ionization
ESP/Ionizing Scrubber
Primary voltage (V) and current (Amps)
Secondary voltage (V) and current (milliamps) or power (watts)
Spark Rate (ESP only)

## Slide 16: Chapter 6: Parametric Monitoring Parametric Monitoring
Wet Scrubber: pH
Electric analyzers: measures pH as electrochemical change
Chemical indicator: pH level due to chemical reaction

## Slide 17: Chapter 6: Parametric Monitoring Parametric Monitoring
pH Scale and Impacts
Basic
Acidic

## Slide 18: Chapter 6: Parametric Monitoring Parametric Monitoring
Wet Scrubber: Flow Rate
Liquid flow rate into and out of scrubber

## Slide 19: Chapter 6: Parametric Monitoring Other Monitoring Equipment
Other Monitoring Equipment
Closed Circuit Television (CCTV)
Forward Looking InfraRed (FLIR)
Leak Detectors

## Slide 20: Chapter 6: Parametric Monitoring Other Monitoring Equipment
Forward Looking InfraRed (FLIR)
Highlights areas for internal inspection by plant personnel
  Air infiltration
  Temperature differences

## Slide 21: Chapter 6: Parametric Monitoring Other Monitoring Equipment
Closed Circuit Television (CCTV)
Closed loop (not broadcast) “security” cameras
Monitor process operations and plant locations
  Tank levels
  Loading / unloading of products and raw materials
  Combustion unit interior
  Control equipment interior
  Stacks / discharges
Provide site security

## Slide 22: Chapter 6: Parametric Monitoring Other Monitoring Equipment
Bag Leak Detectors
In-stack probes that detect changes in PM stack concentration
Light Scattering / Transmittance: Light sensors detect changes of PM (opacity) in exhaust
Triboelectric: Electrical current changes with PM in exhaust
  Probe / PM should be good conductor / insulator
  Signal sensitive to gas flow rate
  Smaller particles that can be charged are more easily detected
  Probe can become clogged
  Detectors signal alarm at a pre-set high emissions level

## Slide 23: Chapter 6: Parametric Monitoring REAL Parametric Monitoring
Compliance Assurance Monitoring (CAM)
Title 40 of the Code of Federal Regulations, Part 64
Applicable to emissions units:
  Located at Title V / Part 70 major facilities
  Subject to a PM emissions limitation or standard and uses a control device to comply with emissions limitation or standard
  Potential pre-control (uncontrolled) emissions greater than major source
  Does not apply to sources subject to NSPS or NESHAP proposed after November 15, 1990
  Does not apply to sources with a CEMS

## Slide 24: Chapter 6: Parametric Monitoring REAL Parametric Monitoring
Compliance Assurance Monitoring (CAM)
Monitoring
  Continuous process, capture system, control device, or other relevant parameter monitoring system (including predictive emission monitoring systems)
  Maintenance and operating procedures
  Any other factors relevant to assessing compliance with emission limitations or standards
Permitting authority approves CAM Plan in permit renewal