## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 4: Understanding Risk Assessments

## Slide 2: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
What is Risk?
Probability of loss or injury to people, property, or the environment
  Air toxics are a source of risk, since they present a potential for harm
Risk is expressed in a probability fraction (no units)
  0: No risk of the event occurring
  1.0: Absolute certainty that the event will occur
For air toxics management programs, agencies must identify the source, probability of harm, and mitigation factors
  These influence public and environmental exposure to chemical risks

## Slide 3: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
Risk Formula
The likelihood that injury or disease may occur from exposure to air toxics can be described by combining:
  An estimate of the toxic properties of the chemical; and
  An estimate of public / environmental exposure to a chemical
“All things are poison and nothing [is] without poison. Solely the dose determines that a thing is not a poison.” - Paracelsus (1493-1541)
Air toxics are managed by developing risk assessments and determining effective controls for abating risk
!

## Slide 4: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
Dihydrogen Monoxide
Toxicity – Low
Exposure – High
>4,500 drowning deaths in U.S. annually (12 per day)
Leading cause of death for children ages 1-4
Alpha Radiation
Toxicity – Very High
Exposure – Very Low
~21,000 lung cancer deaths in U.S. annually
2nd highest cause of lung cancer behind cigarettes

## Slide 5: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
Estimating Risk
If approximately 40,000 deaths occur from automobile accidents each year in the U.S., how many fatalities could occur in a city with a population of 2 million during a 3-day weekend?
  F = 40,000 death/year ÷ 3.272×108 person = 1.22×10-4 death/person-year
  Fp = 1.22×10-4 death/person-year × 2.0×106 person = 244.5 death/year
  Fp = 244.5 death/year ÷ 365 days/year × 3-day weekend
  Fp = 2.0 deaths expected over 3-day weekend in 2 million population

## Slide 6: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
Exposures to Air Toxics
Breathing contaminated air (aerosol)
Eating contaminated food products (deposition)
Drinking contaminated water (deposition)
Skin contact with contaminated materials (deposition)

## Slide 7: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
How Stressors Lead to Negative Outcomes
Stressors
Inorganic Chemicals
Organic Chemicals
Erosion Sediments
Habitat Alteration
Groundwater Loss
Nutrients
Noise, Odor
Exotic Species
Pathogens
Endpoints
Condition of Ecosystem
Critical Species
Cancer
Noncancer diseases
Psychological Condition
Demographic Change
Ecological
Human/Societal
Community Infrastructure
Aesthetics
Loss of recreation
Property Values
Surface Water
Ingestion / Dermal
Inside / Outside Air Inhalation
Soil Contamination
Ingestion / Dermal
Terrestrial Landscape
Groundwater
Ingestion / Dermal / Inhalation
Uptake into food
Ingestion
Pathways/
Exposure Routes
Receptors
Aquatic Ecosystem
Wetland Ecosystem
Terrestrial Ecosystem
Sensitive Populations
Occupational
General Population
Disproportionate Impact
Ecological
Human Health
Quality of Life Concern

## Slide 8: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
How Air Toxics Lead to Negative Outcomes
Stressors
Inorganic Chemicals
Organic Chemicals
Noise, Odor
Endpoints
Condition of Ecosystem
Critical Species
Cancer
Noncancer diseases
Ecological
Human/Societal
Aesthetics
Property Values
Surface Water
Ingestion / Dermal
Inside / Outside Air Inhalation
Soil Contamination
Ingestion / Dermal
Uptake into food
Ingestion
Pathways/
Exposure Routes
Receptors
Aquatic Ecosystem
Wetland Ecosystem
Terrestrial Ecosystem
Sensitive Populations
Occupational
General Population
Disproportionate Impact
Ecological
Human Health
Quality of Life Concern
Community Infrastructure

## Slide 9: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
What is a Risk Assessment?
“Human health risk assessment is the process by which information is analyzed to determine if an environmental hazard might cause harm to exposed persons and ecosystems.”
      National Academy of Sciences, 1983
A risk assessment is used to understand the fundamental processes that underlie human health problems that are caused by pollutants in the environment
Risk assessments address both questions of exposure and the adverse outcomes associated with exposure

## Slide 10: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk
Risk Assessment vs. Risk Management
Risk Assessment: Tool used to support risk management decisions by providing quantitative and qualitative expressions of risk, along with attendant uncertainties
Risk Management: Regulatory and other actions taken to limit or control exposures to a chemical
  MACT / NESHAP standards
  LST air agency air toxics management programs
Risk assessments are used to identify risk and develop tools for risk management (reducing risk)
!

## Slide 11: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
Conceptual Model
Risk assessment often use a conceptual model to illustrate generation, pathways, and endpoints for air toxics
  Major Pathway: Inhalation
  Minor Pathway: Ingestion, dermal contact from deposition

## Slide 12: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
Basic Conceptual Model for Air Toxics
WIND DIRECTION
TRANSFORMATION
DRY DEPOSITION
EVAPORATION/ REENTRAINMENT
BIOACCUMULATION
WET DEPOSITION
DISPERSION
B
A
IN AIR
INHALATION
INGESTION
DERMAL
IN FOOD
INTAKE/UPTAKE
EXCRETION
Sources
Exposure Pathways
TARGET ORGAN/TISSUE
Impacts

## Slide 13: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
Risk Assessment Process
Data organization and analysis to determine if an environmental chemical might cause harm to exposed persons and ecosystems
Four primary, interrelated steps:
  Hazard Assessment
  Dose-response Assessment
  Exposure Assessment
  Risk Characterization

## Slide 14: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
Risk Assessment Process
1. Hazard Identification
Review key research to identify any potential health problems that a chemical can cause.
3. Exposure Assessment
Determine the amount, duration, and pattern of exposure.
2. Dose-Response Assessment
Estimate how much of the chemical it would take to cause varying degrees of health effects that could lead to illnesses.
4. Risk Characterization
Assess the risk for the chemical to cause cancer or other illnesses in the general population.

## Slide 15: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
Questions the Risk Assessment Process Answers:
Who is exposed to the air toxics?
What air toxics are they exposed to?
How are they exposed?
How toxic are the agents they are exposed to?
What is the likelihood that harm will occur?

## Slide 16: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
1. Hazard Identification
Determine whether the air toxics of concern can be causally linked to the health effects in question
Factors contributing to a strong hazard identification include:
  Route of exposure
  Type and quality of the effects
  Biological plausibility of findings
  Consistency of findings across studies
  Potential for bioaccumulation

## Slide 17: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
2. Dose-Response Assessment
Quantify relationship between concentration, exposure, or dose of a pollutant and the resultant health effects
Typical end-products of dose-response assessments:
  Non-cancer: Identification of a sub-threshold dose or exposure level that humans could experience daily for a lifetime without appreciable probability of ill effect
  Cancer: Estimation of a full dose-response curve for low exposures

## Slide 18: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
3. Exposure Assessment
Analyze the magnitude, frequency, duration, and route of exposure
Four major components of an exposure assessment:
  Emissions characterization
  Environmental fate and transport analysis
  Characterization of the study population
  Exposure characterization for inhalation and non-inhalation pathways

## Slide 19: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding Risk Assessments
4. Risk Characterization
Combine the information from the three previous steps
Include descriptions of uncertainties and variables

## Slide 20: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
EPA Risk Assessment Framework
EPA has developed a general framework for a human health risk assessment with the following four components:
  Hazard Identification: Planning and scoping (data evaluation)
  Exposure Assessment
  Dose-Response Assessment: Toxicity Assessment
  Risk Characterization

## Slide 21: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
EPA Risk Assessment Framework
Planning and Scoping
Is a chemical toxic?
What is the relation-ship between the dose of a chemical and the response that results?
Toxicity Assessment
What is the likelihood that the exposure will result in an adverse health effect?
How sure are we our answers are correct?
Risk Characterization
Who is exposed?
What chemicals are the exposed to?
How does the exposure occur?
Exposure Assessment

## Slide 22: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
EPA Risk Assessment Framework
Planning and Scoping
Toxicity Assessment
Risk Characterization
Exposure Assessment
Quantitative and Qualitative Expressions of Risk/Uncertainty
POPULATION CHARACTERISTICS
Measures of Exposure
CHEMICAL
CONCENTRATIONS
Air, Soil, Water, Food
(monitor/model)
Dose/ Response Assessment
Y
X
Chemical
Release
SOURCES
FATE AND TRANSPORT ANALYSIS
SOURCE IDENTIFICATION
EXPOSURE information DOSE/RESPONSE information
Hazard Identification

## Slide 23: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Tiered Approach
EPA cannot perform a time and resource-intensive risk assessment for every situation and decision
  EPA selects an approach for each risk assessment that is consistent with the nature and scope of the decision being made
  Appropriate approach depends on the needs of the decision maker and/or the role that risk information plays in the decision
  Appropriate approach balances uncertainty and resources
Uncertainty is ALWAYS inherent in the process
  Better data may reduce uncertainty, but it cannot be eliminated completely

## Slide 24: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Tiered Approach for Risk Assessments
Each successive tier represents a more characterization of variability and/or uncertainty and a corresponding increase in complexity and resource requirements
Tier 1: Simple screening-level analysis using conservative exposure assumptions and relatively simple modeling
Tier 2: Intermediate-level analysis using more realistic exposure assumptions and more detailed modeling
Tier 3: Advanced analysis using probabilistic techniques
Increasing Cost
and Complexity

## Slide 25: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Risk Assessments Tiered Approach
Tier 1: Simple Screening
Exposure = maximum offsite level
Simple modeling
Low cost
Tier 2: Intermediate Level
Exposure = residential air level
More detailed modeling
Moderate cost
Tier 3: Advanced Level
Complex exposure assessment
Detailed site-specific modeling
High cost
Increasing Complexity / Cost
Decision Point: Evaluate the adequacy of the existing risk assessment and value of additional complexity

## Slide 26: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Tiered Approach for Modeling Risk Assessments
Tier 1: Receptors are located within the area of highest estimated concentration with generic (conservative) inputs
Tier 2: Actual receptor grid and site-specific inputs
Tier 3: Advanced model with probabilistic techniques with calculations to determine probability from each data input

## Slide 27: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Examples of Risk Assessments
2014 National Air Toxics Assessment (NATA)
  Characterization of air toxics across the nation
EPA Residual Risk Assessments
  100 reviews planned; 88 completed (2005-2024)
Regional Air Toxics Assessments
  2012 Portland, OR Air Toxics Solution
  2017 California Air Toxics Assessment
  2020 / 2024 Hopedale, OH Air Monitoring Mid-Stream Natural Gas Processing Facility
  2023 Tacoma / Seattle, WA Air Toxics Study

## Slide 28: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
Conceptual Model for Air Toxics Risk Assessments

## Slide 29: TOXC102+ Chapter 4: Understanding Risk Assessments Understanding EPA Risk Assessments
§112(f): Residual Risk Assessment
8-year review of MACT standards to provide an ample margin of safety to protect public health
3-tier screening approach used to answer following questions
  How much of a stressor (air toxics) is present in an environmental media (air) over a geographical area?
  How much contact (exposure) between a receptor and stressor (air toxics) in contaminated media (air)?
  How does air toxics exposure affect human health (toxicity) and/or ecological receptors?

## Slide 30: TOXC102+ Chapter 4: Understanding Risk Assessments Review Questions
What is risk?
  Probability something harmful could happen from 0 (none) to 1 (certainty)
What is a risk assessment?
  Study to determine harm from chemical exposure
What is the major pathway for exposure to air toxics?
  Inhalation
What are the four steps to a risk assessment?
  Hazard identification, dose-response, exposure, and risk characterization
What is a residual risk assessment?
  8-year review of MACT standard to protect public health with an adequate margin of safety