## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 5: Exposure Assessment

## Slide 2: TOXC102+ Chapter 5: Exposure Assessments EPA Risk Assessments
EPA Air Toxics Risk Assessment Library (3 Volumes)
Technical Resource Manual
  Risk Assessment process and analysis
Facility-specific Assessment
  Approaches for individual sources
Community-Level Assessment
    Approaches for cumulative air toxics in a community

## Slide 3: TOXC102+ Chapter 5: Exposure Assessments EPA Risk Assessments
EPA Air Toxics Risk Assessment Library (Addenda)
Community Air Screen How-To Manual
  Detailed guide for community partnerships on using the screening level approaches in ATRA Volume 3 to improve local outdoor air quality
EPA Risk Assessment Policy, Guidelines, and Related Materials

## Slide 4: TOXC102+ Chapter 5: Exposure Assessments EPA Risk Assessments
EPA Risk Assessment Framework
Planning and Scoping
Toxicity Assessment
Risk Characterization
Exposure Assessment
Quantitative and Qualitative Expressions of Risk/Uncertainty
POPULATION CHARACTERISTICS
Measures of Exposure
CHEMICAL
CONCENTRATIONS
Air, Soil, Water, Food
(monitor/model)
Dose/ Response Assessment
Y
X
Chemical
Release
SOURCES
FATE AND TRANSPORT ANALYSIS
SOURCE IDENTIFICATION
EXPOSURE information DOSE/RESPONSE information
Hazard Identification

## Slide 5: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment
Definitions
Exposure Assessment: Evaluation of the magnitude, frequency, duration, and route of exposure to the air toxic
  Dispersion: Spread or distribution of air toxics from a source
  Transport: Processes that carry air toxics from one location to another (air / wind)
  Fate: Ultimate disposition of air toxic and how long it persists, including any chemical reactions during transport
  Exposure: Contact between a person and a stressor (air toxic)
Exposure assessments answer the questions: Who is exposed / how are they exposed?
!

## Slide 6: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment
Exposure Assessment
Generally, the most multifaceted and time-consuming part of an air toxics risk assessment
An Exposure Assessment identifies:
  Who is potentially exposed to toxic chemicals?
  What toxics they may be exposed to?
  How are they exposed (magnitude, pattern, and pathway)?

## Slide 7: TOXC102+ Chapter 5: Exposure Assessments Types of Exposure
Acute Exposure,,,,,,,,,,
Short term exposure (minutes, hours, days) to relatively high levels of contaminant
Acute exposure may result in acute effects, from relatively mild (eye irritation), to extreme (an asthma attack), to fatal
Chronic Exposure,,,,,,,,
Long term (years to lifetime) exposure to relatively low levels of contaminant
Chronic exposure may result in chronic effects (cancer, chronic obstructive pulmonary disease, neurological problems, etc.)

## Slide 8: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment Process
Exposure Assessment as a 4-step Process
Emission characterization: Quantification of the rate of emissions of and types of air toxics emitted
Environmental fate and transport: How the air toxic is transported, dispersed, and transformed
Characterization of the Study Population: the location, behavior, age, and other characteristics of the study population
Exposure Characterization: Integration of air toxics concentration with study population to characterize exposure

## Slide 9: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment Process
Air Toxics Exposure Assessments: 4-Step Process
Emission Characterization
  Identify air toxics source and rate of emissions
Environmental Fate & Transport
  Identify exposure pathways
  Exposure points and routes
Characterization of Study Population
  Identify impacted population and characteristics
Exposure Characterization
  Quantify exposure using modeling or monitoring

## Slide 10: TOXC102+ Chapter 5: Exposure Assessments Sources of Exposure
Stack (Point) Emissions
Identifiable emissions point (stack, chimney, duct, flue)
Fugitive (area) Emissions
Emissions generated over an area (roadways, valves)

## Slide 11: TOXC102+ Chapter 5: Exposure Assessments Sources of Exposure
Dispersion / Transport Parameters
Source characteristics
  Stack height, exhaust temperature, exhaust flow rate
Atmospheric and meteorological factors
  Wind speed and direction
Terrain characteristics
Wet and dry deposition rates
Chemical properties of the air toxic
  Aqueous solubility, vapor pressure, melting point, molecular diffusivity, air-water partition coefficient (Henry’s Law constant), phase partition coefficient, absorptivity

## Slide 12: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment Process
Air Toxics Exposure Assessments: 4-Step Process
Emission Characterization
  Identify air toxics source and rate of emissions
Environmental Fate & Transport
  Identify exposure pathways
  Exposure points and routes
Characterization of Study Population
  Identify impacted population and characteristics
Exposure Characterization
  Quantify exposure using modeling or monitoring

## Slide 13: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Dispersion, Fate & Transport Conceptual Model
Evaluate how air toxics get from source to receptor
Understand how air toxics move and change in environment
WIND DIRECTION
TRANSFORMATION
DRY DEPOSITION
EVAPORATION/ REENTRAINMENT
BIOACCUMULATION
WET DEPOSITION
DISPERSION
B
A
IN AIR
INGESTION
DERMAL
IN FOOD

## Slide 14: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Fate & Transport (F&T) Conceptual Model
Air Toxic Emitted
Air Toxic Concentration in Ambient Air
Plants &
Vegetables
Soil
Animals
Water
Meat Products
Dairy Products
Fish
Ingestion
Dermal
Contact
Inhalation
Total Daily
Exposure
Nursing
Infants
Cancer
Risk
Hazard
Index

## Slide 15: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Model in a Box
Fate & Transport
An F&T analysis identifies and quantifies the mechanisms that affect where air toxics will end up
K-Theory
Turbulence/Dispersion
Eddy Energy Equations
Mixing Length Theory
Molecular Friction
Richardson Number
Gaussian Plume Equation

## Slide 16: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Fate & Transport Predictions
Modeling: Computer algorithms for dispersing emissions from source to receptor
  Strengths: Relatively fast, inexpensive, large spatial domain
  Weaknesses: Requires data and predictions, measure of uncertainty
Monitoring: Determination of ambient air concentration at specific receptors
  Strengths: Real time data and low uncertainty
  Weaknesses: Time consuming, methodological limits, sampling and analysis logistics, relatively expensive, limited spatial domain

## Slide 17: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment
Fate & Transport Predictions
Modeling is the primary F&T analysis tool
  Modeling is used to locate ambient air monitors for air toxics
Monitoring is used to support modeling
  Addresses gaps in emissions inventories
  Validate model results
Each risk assessment or air toxics study will dictate what monitoring and modeling data is used

## Slide 18: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling
Clean air is diffused into plume
by turbulence along plume edges
Plume grows and diffuses as
it mixes with air (dispersion)
Air toxics mass stays the same as plume expands (i.e., concentration decreases)

## Slide 19: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling for Risk Assessments
Predicts both acute and chronic ambient air toxics levels
Can include single or multiple sources of air toxics
Scale can vary from source fence line to national
Model uses:
  Determine historical or current ambient air concentrations
  Compare different scenarios for controls and emission rates
  Site monitor locations
  Demonstrate compliance with state air toxics requirements

## Slide 20: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling for Risk Assessments
Screening Models: Conservative estimates with little inputs (AERSCREEN)
Plume Models: Steady state or normal (gaussian) distribution of plume; no variations (AERMOD)
  Limited to 50 kilometers
Puff/Particle Models: Simulate time and space variations
  Lagrangian particles (CALPUFF), Eulerian grid, atmospheric trajectory model

## Slide 21: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling Flowchart
Emissions
Quantification
Meteorological
Observations
Release
Parameters
Meteorology
Model
Emissions
Model
Processed
Meteorology
Processed
Emissions
Air Quality
Model
Model
Results
Terrain
Data
Terrain
Model
Processed
Terrain

## Slide 22: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling for Risk Assessments
Screening models provide conservative (worst-case) estimates
  Identify facilities and/or air toxics with the greatest risk
  Limited data requirements (emission rates, some stack parameters)
  Limited or no meteorological data required
  Model runs are quick and generally require few computational resources
  Only provide data for one direction

## Slide 23: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Screen Model
AERMOD Model

## Slide 24: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxics Model – Plume Models
Gaussian distribution determines plume
  Atmospheric stability impacts horizontal (σy) and vertical (σz) dispersion at distance (x) from source
Gaussian model assumptions
  Constant emissions rate (Q)
  Plume has normal distribution
  Wind speed and direction uniform

## Slide 25: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Approved Regulatory Models
American Meteorological Society (AMS) / EPA Regulatory Model (AERMOD)
  Near field plume model (<50 kilometers)
  Most common model
Complex Terrain Dispersion Model Plus Algorithms for Unstable Situations (CTDMPLUS)
  Complex terrain plume model
Offshore and Coastal Dispersion (OCD) Model
  Offshore emissions impacting coastal regions plume model

## Slide 26: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Normal (Gaussian) Distribution

## Slide 27: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Particle/Puff Models
Each puff modeled in 3 dimensions
  Can be broken down into smaller puffs
Differences from Plume Models
  Requires even more data
  Better for complex terrain, non-steady-state emissions rate, and secondary pollutants
Puff Types:
  Lagrangian: Follows the particle
  Eulerian: Observes airflow at intervals

## Slide 28: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Other (Non-Gaussian) Distribution Curves
Monte Carlo Plume Simulations
  Monte Carlo algorithms rely on repeated random sampling to create a probability distribution (not normal / Gaussian distribution)
  Not approved by EPA

## Slide 29: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Alternate Models
California Puff (CALPUFF) Model
  Multi-layer, multi-species non-steady state puff dispersion model
  Used to assess impacts beyond 50 kilometers (AERMOD limit)
Clean Air Act Assessment Package - 1988 (CAP88-PC)
  Plume model for dose and risk from radionuclide releases
  Required by 40 CFR, Part 61 to demonstrate compliance
COMPLY
  Screening model for small releases of radionuclides
  Can be used to demonstrate compliance with 40 CFR, Part 61

## Slide 30: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Modeling for Risk Assessments
Human Exposure Model (HEM) 4.2
  Only addresses inhalation pathway
  Uses AERMOD (plume model) to estimate receptor concentrations
  Includes both chronic and acute risks
    Stacks •
    Facility ■
    Receptors •••
    Alternate Receptors ■■
    Maximum Individual Risk x

## Slide 31: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxics Modeling
Meteorology: Meteorological factors influence dispersion and transport
Wind – affects plume direction and size
Atmospheric Stability – affects dry dispersion by plume mixing with surrounding air
  Screening models use “default” atmospheric stabilities
  Plume models use varying numbers of atmospheric stabilities by location
Precipitation – deposits air toxics (wet deposition)

## Slide 32: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Atmospheric Stability
Turbulence is the interaction between the atmosphere and surface
  Increased when winds blow over uneven surfaces or when the surface is much warmer than the air
  Increased in unstable atmosphere (e.g. thunderstorm, clouds, buildings)
Turbulence at the plume edges determines:
  How quickly the plume disperses by mixing with surrounding air
  How quickly air toxics hits the ground (dry deposition)

## Slide 33: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
High wind
Low plume rise
Directional dispersion
Low wind
High plume rise
Greater dispersion

## Slide 34: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Light Windspeed – Ideal Plume

## Slide 35: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Moderate Windspeed

## Slide 36: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Heavy Windspeed

## Slide 37: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Windrose
Visual grouping of wind direction and speed over time
Each bar represents compass direction wind is blowing from
Each segment is a grouping by wind speed
  The longer the segment, the greater the time the wind blows from that direction at that speed
  Longest bar is the prevailing wind direction

## Slide 38: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Building Downwash
Pollutant Settling Velocity
PM1.0 3.44×10-5 m/s
PM2.5 1.96×10-4 m/s
PM5.0 7.61×10-4 m/s
PM10 3.00×10-3 m/s
PM20 1.19×10-2 m/s
Terrain Effects
Other Factors Affecting Dispersion

## Slide 39: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Building Downwash
Buildings increase atmospheric turbulence
Horizontal flow of wind causes low pressure area in the wake of the building
  Draws plume down into low pressure area behind the stack

## Slide 40: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport

## Slide 41: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Pollutant Properties
The physical form of air toxics greatly affects dispersion, transport and atmospheric chemical reactions
  Gaseous / Vapors: Not bound to particles, exist as single molecules or very small aggregates “dissolved” in air
  Particles: Particulate matter (solids) or particle-bound (absorbed or condensed onto the surface of particles)

## Slide 42: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
PM Categories
Categorized by particle size (in micrometers - µm)
  PM12700 = Theoretical largest particle measured by Method 5 (½ inch)
  PM100 = Largest particle to suspend in air; 1971 NAAQS for Total Suspended Particulate (TSP)
  PM30 = Largest EPA emissions factor for TSP
  PM10 = 1987 NAAQS for Coarse PM
  PM2.5 = 1997 NAAQS for Fine PM (revised 2012)
1/256 inch ½ inch
Human Hair
2.5 10 30 50 100 12700

## Slide 43: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
PM Size Comparison
Fine Beach Sand (90µm Diameter)
Human Hair
(50-70µm Diameter)
PM2.5 – 2.5µm Diameter
PM10 – 10µm Diameter

## Slide 44: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
PM Size Comparison

## Slide 45: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Particle Shape
Particle shape affects settling velocity

## Slide 46: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Pollutant Properties
Dry Deposition: the rate of deposition from the atmosphere to surfaces is dependent upon particle size
As the size of particles increases, the rate at which particles fall due to gravity (the settling velocity) and distance from source increases
Fine particles (<PM1.0) may remain suspended in air indefinitely, but larger particles (>PM20) settle rapidly

## Slide 47: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Chart: Settling Time for PM by Size
| 0 | 5 | 10
PM1.0 | 0 | 2422.4806 | 4844.9612
PM2.5 | 0 | 425.1701 | 850.3401
PM5.0 | 0 | 109.505 | 219.0101
PM10 | 0 | 27.7778 | 55.5556
PM20 | 0 | 7.0028 | 14.0056
3.3 days
14 hours
3 hours
<1 hour

## Slide 48: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Condensation
Volatile metals & organic vapors are gases at high temperatures
  When these gases cool in the atmosphere, they condense (change from a gas to a liquid) to form PM
  Volatile metals include mercury, lead, cadmium, and arsenic
Condensable particulate is <PM1.0

## Slide 49: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Nucleation
Vapors (VOC / acid gases) condense on the surface of particles
  Volatile metals can be deposited on the surface of all other particles

## Slide 50: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Particle Size Distribution by Formation

## Slide 51: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Secondary Pollutants
Air toxics formed from atmospheric chemical reactions
Photochemical Reaction: VOC reacts with NOX in the presence of light to form a new ozone
Atmospheric Reaction: SO2, NOX, and ammonia form PM2.5
Air toxics can be formed in the ambient air from reactions involving toxic or non-toxic chemicals
  Formaldehyde is usually formed as a secondary pollutant
  Propylene, primarily emitted from manufacturing industries, reacts rapidly in the atmosphere to form acetaldehyde, then formaldehyde

## Slide 52: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Secondary Air Toxic | Formed From
Acetaldehyde | Propene, 2-Butene
Acrolein | 1,3-Butadiene
Carbonyl Sulfide | Carbon Disulfide
O-Cresol | Toluene
Formaldehyde | Ethene, Propene
Hydrogen chloride | Nitric Acid, Chlorinated Organics
Methyl Ethyl Ketone | Butane, Branched Alkenes
N–Nitroso-N–Methylurea | N–Methylurea
N–Nitrosodiethylamine | Dimethylamine
N–Nitrosomorpholine | Morpholine
Phosgene | Chlorinated Solvents
Propionaldehyde | 1-Butene
Source: Rosenbaum et al., 1998 | 

## Slide 53: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Terrain Effects: Plume Behavior Around Terrain Obstacles

## Slide 54: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxics Model Results
Models calculate concentrations at receptors on a grid
  Receptors are the nodes on a polar coordinate or standard Cartesian coordinate system (x,y rectangular grid)
  The smaller the distance between nodes the longer the model run
Nodes do not often correlate to locations of interest
  Can enter coordinates for specific receptors
  Interpolation used to estimate modeled ambient air concentration between nodes (not on EPA standard model)

## Slide 55: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Cartesian Coordinates
Uniform area within each grid space (receptors at nodes)
Polar Coordinates
Area within each grid space expands farther away from center (receptors at nodes)

## Slide 56: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxics Model Results
For risk characterizations, exposure concentrations (ECs) are compared to air toxics dose-response values
  Models result (ECs) reported in milligrams per cubic meter (mg/m3) or micrograms per cubic meter (μg/m3) (1,000 µg in 1 mg)
  Dose-response values usually reported in parts per million by volume (ppmbv), or parts per billion by volume (ppbbv) (1,000 ppb in 1 ppm)
  Recommend only using µg/m3 to reduce errors
To convert from mg/m3 to ppm:
  ppm = mg/m3 × 24.45 Liters/mole ÷ Molecular Weight (grams/mole)
  24.45 liters is volume of one mole ideal gas at standard conditions

## Slide 57: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Fate & Transport Predictions
Using Modeling to Locate Monitors

## Slide 58: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Monitoring
Monitors measures air toxics levels in ambient air
  Measures both acute and chronic ambient air toxics levels
Used for:
  Enforcement (Lead NAAQS)
  Verification of emissions from specific sources
  Development and/or validation of air quality models
  Identification of emissions inventory gaps

## Slide 59: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxics Monitoring
Clean Air Act does not require air toxics monitoring
  Monitoring is required for lead NAAQS
  EPA established air toxics monitoring programs in 1987 to obtain more information about air toxics in the ambient air
  EPA designed a national ambient air toxics monitoring program in 1999
EPA operates multiple air toxics monitoring networks
  Short-Term Ambient Air Toxics Monitoring
  Long-Term (Trend) Ambient Air Toxics Monitoring
  Deposition Monitoring

## Slide 60: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Reasons for Air Toxics Monitoring
Evaluate impacts of a specific source on a nearby receptor
  School Air Toxics Monitoring
Validate model predictions
  Use model to site monitor locations
Track trends in air quality levels
Identify and develop information for gaps in emissions inventories
Determine compliance with air toxics legal requirements
  Compare lead monitoring near a facility to NAAQS

## Slide 61: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
National Scale Ambient Air Monitoring
  National Air Toxics Trends System (NATTS) generates long-term ambient air toxics concentration data for fixed sites across the country
  Ambient air monitoring conducted for lead NAAQS
  RadNet and other radiation monitoring
Community Scale Ambient Air Monitoring
  EPA awards grants for short-term air toxics monitoring projects designed and operated by local, state, and tribal air agencies
Deposition Monitoring
  National Atmospheric Deposition Program (NADP) for mercury and other persistent bio-accumulative toxics (PBTs)

## Slide 62: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
NATTS
25 active monitoring sites for metal and volatile HAP
  21 urban sites, 4 rural sites
  Network first established in 2003
  Often co-located with other ambient air and meteorological monitors
  All operated and maintained by local or state air agencies
At least 19 HAP measured in 4 categories
  Typically over 100 pollutants monitored
  VOC, carbonyls, PM10 metals & polycyclic aromatic hydrocarbon (PAH)

## Slide 63: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
NATTS Sites (2020)

## Slide 64: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
NATTS – VOC |  | 
Acrolein | Benzene | Butadiene, 1,3-
Carbon tetrachloride | Chloroform | Ethylene oxide
Perchloroethylene / Tetrachloroethylene | Trichloroethylene | Vinyl chloride
NATTS – Carbonyl |  | 
Acetaldehyde | Formaldehyde | 
NATTS – Polycyclic Aromatic Hydrocarbon (PAH) |  | 
Benzo(a)pyrene | Naphthalene | 
NATTS – PM10 Metals |  | 
Arsenic compounds | Beryllium compounds | Cadmium compounds
Lead compounds | Manganese compounds | Nickel Compounds
Hexavalent Chromium (Optional) |  | 

## Slide 65: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Local Air Toxics Monitoring
Urban Air Toxics Monitoring Program (UATMP)
  Characterizes composition and magnitude of urban air toxics
  Sites are operated by LST agencies with a grant from EPA
  UATMP data is used to develop National Air Toxics Assessment (NATA)
Community-Scale Air Toxics Ambient Monitoring (CSATM)
  Conduct local-scale investigations of air toxics
  Sites are operated by LST agencies with a 1- to 3-year grant from EPA
  Sites constantly changing
  Data from UATMP is used to develop the NATA

## Slide 66: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
RadNet
Near-real time constant gamma count rates
  140 radiation air monitors in all 50 states (and Puerto Rico)
Multiple types of monitoring
  PM filter traps radionuclides which are analyzed for beta radiation
  Program includes precipitation and drinking water analyses

## Slide 67: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
NADP
Monitoring air pollution deposition and impacts
5 monitoring networks
  Mercury Deposition Network: geographic distribution and trends in precipitation (wet deposition)
  Atmospheric Mercury Network: atmospheric mercury concentrations (dry deposition)
  National Trends Network: acids, nutrients, and base cations in precipitation
  Atmospheric Integrated Research Monitoring: atmospheric processes
  Ammonia Monitoring: Passive atmospheric ammonia concentration

## Slide 68: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
NADP (2020)

## Slide 69: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Selecting Monitors
Monitoring method criteria:
  What is the scale of the assessment?
  What contaminant(s) will be analyzed?
  What will be the sampling time over which the result is derived (e.g., 15 minutes or 24 hours)?
  What are reporting limit needs?
  What are available resources and limitations?

## Slide 70: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Selecting Monitoring Locations
Different requirements for general exposures or exposures to the maximally exposed individual
  Locations too close to a source may underestimate exposure if the plume has not yet reached ground level
  Locations too far from the source may underestimate exposure due to plume dispersion between point of plume touch-down and monitoring location.

## Slide 71: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Selecting Monitoring Locations
Terrain Considerations
  Buildings, hills, and trees have shielding (underestimate exposure) & concentrating (overestimate exposure) effects
Interference Considerations
  Products of combustion from vehicles can interfere with monitor results
  Monitor 3-61 meters from major traffic arteries
Height Considerations
  Monitor between 1-2 meters above ground in personal breathable zone

## Slide 72: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Selecting Monitoring Locations
Background Concentration
  Background monitors should be placed in the predominant upwind direction (in relation to sources) in the assessment area to measure the concentrations of the chemicals of potential concern in air that is moving into the assessment area
  Background monitoring results should not be subtracted from assessment area monitoring results
  Background concentration should be included in total measured concentration with bar charts comparing to background and total measured concentrations

## Slide 73: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Fate & Transport Predictions
Using Modeling to Locate Monitors
Proposed Background Monitor Location
Proposed Background Monitor Alt. Location
Proposed Source Monitor Location

## Slide 74: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Selecting Monitoring Locations
Purposive sampling: Select monitor at a particular location of special interest
  Useful to address specialized questions, but less useful for risk assessment
Random sampling: Selecting monitor locations in a random and unbiased manner
  Establish locations by creating a grid [x and y coordinates]
  Easier to apply statistical methods to results but can miss “hot spots”
Systematic sampling: Place monitors on grid nodes
  Ensures uniform sampling but analysis is more complicated

## Slide 75: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Monitoring Uncertainty
Detection Limit: Minimum concentration that a monitor can reliably find a sample (i.e., distinguish from zero)
  Method Detection Limit (MDL) is for each instrument
  An MDL of 1μg/m3 means that a contaminant will probably not be detected by the instrument at concentrations less than 1 µg/m3
Limit of Quantification (LOQ): Minimum concentration that a monitor can reliably say is present at a specific concentration
  An LOQ of 2 μg/m3 means results may be reported as being present at a specific concentration above 2 μg/m3

## Slide 76: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Monitoring Uncertainty
Selected air toxics monitors must have the minimum sensitivity needed for concentrations of health and/or regulatory concern
  At a minimum, LOQ should be below any relevant health benchmarks
Measurements between the MDL and LOQ only indicate the presence of the substances
  “Benzene was not detected at a detection limit of 5 μg/m3” means that there was no benzene detected up to 5 μg/m3

## Slide 77: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Pathway Analyses
Systematic evaluation of potential / actual effects on air quality
  Characterization of air emission sources
  Determination of effects from atmospheric processes on transport and dilution
  Evaluation of the exposure potential at receptors of interest
Part of the CERCLA requirements for Superfund sites
  EPA published a 4-volume set, “Procedures for Air Pathway Analyses” EPA-450/1-89-002

## Slide 78: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Pathway Analyses
Collect and Review
Information
Select Monitoring
Levels
Develop Monitoring
Plan
Conduct Monitoring
Summarize and
Evaluate Results
Source data
Receptor data
Modeling data
Screening
Refined screening
Refined monitoring
Select monitoring constituents
Specify meteorological monitoring
Select methods/equipment
Develop QA/QC

## Slide 79: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Summarize and Evaluate Results
Assemble Data
Meteorological
Monitoring Data
Validate & Summarize Data
Data Listings
Statistical Summaries
Meteorological Summaries
Dispersion Modeling to Extrapolate Data
Risk Assessment / Decision Making
Air Monitoring Summaries

## Slide 80: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
HAP Classifications by Vapor Pressure
Very Volatile Inorganic / Organic Compounds (VVINC / VVOC)
  6 VVINC / 15 VVOC; Vapor pressure >380 mm Hg @ 25ºC
Volatile Inorganic / Organic Compounds (VINC / VOC)
  3 VINC / 82 VOC; Vapor pressure >0.1 and <380 mm Hg @ 25ºC
Semi-volatile Inorganic / Organic Compounds (SVINC / SVOC)
  2 SVINC / 64 SVOC; Vapor pressure >1×10-7 and <0.1 mm Hg @ 25ºC
Nonvolatile Inorganic / Organic Compounds (NVINC / NVOC)
  12 NVINC / 5 NVOC; Vapor pressure <1×10-7 mm Hg @ 25ºC

## Slide 81: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Chart: Volatile Vapor Pressure Classifications
 | 1e-07
 | 0.1
 | 380
 | 10000

## Slide 82: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
HAP | Volatility | Vapor Pressure | HAP | Volatility | Vapor Pressure
Acetaldehyde | VVOC | 952 mm Hg | Chlorine | VVINC | 4,000 mm Hg
Formaldehyde | VVOC | 2,700 mm Hg | Phosphine | VVINC | 2,000 mm Hg
Benzene | VOC | 76 mm Hg | Hydrazine | VINC | 16 mm Hg
Xylene | VOC | 5 mm Hg | Hydrochloric Acid | VINC | 23 mm Hg
Benzidine | SVOC | 1×10-5 mm Hg | Phosphorus | SVINC | 1×10-2 mm Hg
Captan | SVOC | 1×10-6 mm Hg | Mercury | SVINC | 1×10-3 mm Hg
3,3’-Dimethoxybenzidine | NVOC | 1×10-13 mm Hg | Asbestos | NVINC | Very Low
4,4’-Methylenedianiline | NVOC | 1×10-10 mm Hg | Cadmium Compounds | NVINC | Very Low

## Slide 83: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
HAP Classifications by Boiling Point
Volatiles (VV / V)
  Boiling Point <100ºC
Semi-volatiles (SV)
  Boiling Point >100ºC and <300ºC
Particles / Non-volatiles (NV)
  Boiling Point >300ºC

## Slide 84: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Silver – 2212ºC
Anthracence – 342ºC
Benzo(a)pyrene – 310ºC
Acenaphthylene – 269ºC
Napthylene – 218ºC
Dichlorobenzene – 173ºC
Chlorobenzene – 132ºC
Toluene – 110ºC
Benzene – 80ºC
Dichloromethane – 40ºC
Methylchloride – -24ºC
2482ºC – Chromium
1744ºC – Lead
765ºC – Cadmium
480ºC – Benzo(k)fluoranthene
399ºC – Pyrene
356ºC – Mercury
340ºC – Phenanthrene
294ºC – Fluorene
213ºC – 1,2,4-Trichlorobenzene
180ºC – 0-Diclorobenzene
145ºC – Styrene
131ºC – 1,2-Dibromomethane
87ºC – 1,2 Dichloropane
61ºC – Chloroform
13ºC – Ethyl Chloride
Volatiles Semi-Volatiles Particles / Non-Volatiles

## Slide 85: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Toxic Monitoring Methods
Selected Analytical Methods for Environmental Remediation and Recovery (SAM) 2017
Includes list of chemical methods for individual air toxics
EPA Methods
  IO – Toxic Inorganic Compounds (17 methods in 5 chapters)
  TO – Toxic Organic Compounds (17 methods)
  SW – Solid Waste
  OW – Office of Ground and Drinking Water
Other Methods: ASTM, NEMI, NIOSH, CARB

## Slide 86: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Gas Chromatograph / Mass Spectroscopy

## Slide 87: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Method TO-15 for Monitoring VOC at the perimeter of a Municipal Solid Waste Landfill
Notes: 86

## Slide 88: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Time Scale Basis – concentration averaged over total collection time
Grab Samples: Quasi-instantaneous measurement of a concentration
  Obtained in the field ≤24 hours or less and returned to the laboratory for analysis
  Can use automated samplers, but analysis occurs in the lab
Continuous Samples: Constant series of measurements with data collected at selected intervals
  Analysis occurs within the monitor
  Can be be fully automated versions of grab sampling
Time-integrated Samples: Collected over an extended period of time
  Samples are obtained in the field and returned to a laboratory for analysis

## Slide 89: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Sample Collection Methods – Monitor types
Integrated air sampling devices: A pump draws air continuously into the sample chamber
  For metals and carbonyls, collected samples of air are passed over a reactive medium or through a filter during a prescribed period of time
  For VOC, collected samples of air are captured in a canister
  Sample is returned to the laboratory for analysis of the filter or reactive medium
  Predominant type of monitoring used for HAP
Direct-read Monitors: Air is drawn through a measurement system for analysis; system provides a direct reading of the concentration

## Slide 90: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Sample Collection Methods – Monitor types
Automated Monitoring Systems: Automatically collect samples, perform the analysis, and report results at regular intervals in the field
Air Deposition Monitors: Rely on deposition of air toxics
  Can be active or passive and use wet and/or dry sampling methods
Passive Monitors: Allow compound to diffuse into an active material
  Analyzed in the lab, although materials can change color to indicate deposition
Grab Sampling: Air enters an evacuated chamber at a fixed rate
  Analyzed in the lab

## Slide 91: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Grab Sampling (Passive) Active Sampling
Sample Nozzle
Particulate Filter
Vacuum Gauge
Pump
Canister

## Slide 92: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Deposition Monitor
Continuous Automated

## Slide 93: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Fate & Transport Predictions
Advanced air modeling can simulate different atmospheric, building, and terrain conditions
Air modeling only estimates dry deposition
  What about other depositions?
Air modeling only estimates inhalation exposure
  What about other exposures?

## Slide 94: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Pollutant Properties
Wet Deposition: “washing out” of air toxics in the atmosphere during precipitation events (e.g. rain, snow, and hail)
Wet deposition affects both particulate and gaseous air toxics
For air toxics soluble in water, precipitation absorbs the air toxics from the air and deposits them on the earth’s surface in bodies of water (acid rain)
Wet deposition is less efficient at removing fine particulates
Wet deposition has a limited effect on the levels of gaseous air toxics with high Henry’s Law constants (i.e., air toxic does not dissolve in gas well)

## Slide 95: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Wet Deposition: Precipitation
Increases turbulence (unstable atmosphere)
Captures air toxics from plume and deposits them onto ground and surfaces

## Slide 96: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Deposition Monitoring
Network of federal, state, local, tribal, private, and collegiate monitors measuring precipitation chemistry since 1978
Mercury Deposition Network: Wet deposition of mercury
Atmospheric Mercury Network: Dry deposition of mercury
Ammonia Monitoring Networks: Atmospheric ammonia
Atmospheric Integrated Research Monitoring Network: Atmospheric and deposition processes
National Trends Network: Acids, nutrients, and base cation content in precipitation

## Slide 97: TOXC102+ Chapter 5: Exposure Assessments Dispersion, Fate & Transport
Air Quality Related Values (AQRVs)
Part of the Prevention of Significant Deterioration (PSD) program for resources sensitive to air pollution or deposition
  Biological resources: vegetation, fish, and wildlife
  Ecological resources: soils and water
  Scenic, cultural & physical resources: visibility and monuments
Federal Land Managers (FLM) identify and inventory AQRVs
  FLM review and inventory of AQRV on public lands in both PSD Class I and Class II areas
  Tribes can also establish AQRVs in Class I and Class II areas

## Slide 98: TOXC102+ Chapter 5: Exposure Assessments Exposure Assessment Process
Air Toxics Exposure Assessments: 4-Step Process
Emission Characterization
  Identify air toxics source and rate of emissions
Environmental Fate & Transport
  Identify exposure pathways
  Exposure points and routes
Characterization of Study Population
  Identify impacted population and characteristics
Exposure Characterization
  Quantify exposure using modeling or monitoring

## Slide 99: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure
Post exposure chemical effects:
  Impacts at initial point of entry in the body
  Blood circulates toxics throughout body (systemic effects)
Dose triggering toxic response is influenced by:
  Absorption
  Distribution
  Metabolism
  Storage
  Elimination

## Slide 100: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Pathway
The course a toxic chemical takes from source to the exposed receptor
Describes a unique mechanism by which an individual or population is exposed to air toxics from source(s), including:
  Inhalation - breathing contaminated outdoor and/or indoor air
  Ingestion - air toxics that can accumulate in soils, sediments, and foods, including bioaccumulation
  Skin - dermal contact or entry via puncture with deposited air toxics
Pathway analysis is linked strongly to environmental fate and transport

## Slide 101: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Overview of Multipathway Exposure Pathways/Routes

## Slide 102: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Pathways
Contact of a chemical with:
  Dermal (skin) and punctures in the skin
  Mouth
  Nostrils
Air toxics exposure assessments should include:
  Inhalation of contaminated air
  Ingestion of contaminated soil, water, or food

## Slide 103: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Mercury Fate & Transport Cycle

## Slide 104: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Intake Calculation from Exposure Pathway
Intake Calculation
Intake = EC x CR x EF x ED ÷ (BW x AT)
  Where:
  EC = Exposure Concentration of a chemical in soil, water, food at the point of exposure
  CR = Contact Rate with the contaminated medium (i.e., intake rate)
  EF = Exposure Frequency
  ED = Exposure Duration
  BW = Body Weight
  AT = Averaging Time

## Slide 105: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Inhalation Pathway
Concentration (C) of the chemical in air (µg/m3) at the point of exposure (exposure concentration or EC) can be used as a measure of exposure
Chronic Inhalation Exposure: Estimate of annual arithmetic average concentration (from modeling or monitoring) to represent long-term EC
Acute Inhalation Exposure: 1-hour or 24-hour arithmetic average to represent the short-term EC
Exposure assessments ALWAYS include inhalation exposure pathway
!

## Slide 106: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Inhalation Pathway
Frequency: we don’t breathe the same air all the time!
People are exposed to different microenvironments throughout the day
  Going to school, work, shopping, etc.
  Going on vacation
  Time spent in the car
  Time spent in the home
  Time working in the yard
  Time away from home on work travel

## Slide 107: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Inhalation Exposure Modeling
An inhalation exposure model combines information on activity patterns and microenvironment air toxics concentrations to calculate a time-weighted average of all exposures:
  Where:
  ECA = the adjusted average inhalation exposure concentration (μg/m3)
  T = total averaging time (T = ∑ tj; years)
  Cj = the average concentration for microenvironment j (μg/m3)
  tj = time spent in the microenvironment j (years)

## Slide 108: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Inhalation Exposure Modeling
This exposure profile has been developed for one year of work for a representative individual within the population of interest:
The EC for that individual is calculated as:
  EC = (0.1 × 80) + (0.5 × 20) + (0.4 × 10) = 22 μg/m3
Duration Spent in Each Microenvironment (% year) | Average Concentration of Air Toxic In Each Microenvironment (μg/m3)
10 = outside | 80
50 = at work | 20
40 = inside home | 10

## Slide 109: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
EPA ExpoBox
Toolbox for Exposure Assessors
  Includes Example Exposure Scenarios that outline various exposure pathways
www.epa.gov/expobox
Example Exposure Scenarios Assessment Tool
EPA published an Exposure Factors Handbook
  Includes Example Exposure Scenarios that outline various exposure pathways
  Used to illustrate how the Handbook can be used to estimate exposure
cfpub.epa.gov/ncea/risk/recordisplay.cfm?deid=85843

## Slide 110: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Ingestion Pathway
Measure of exposure equals the amount of chemical ingested (the intake), usually in mg of chemical ingested per kilogram of body weight per day (mg/kg-d)
For air toxics assessments, only evaluate ingestion for HAP which are persistent and which may also be bioaccumulative (mercury or dioxin)

## Slide 111: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Dermal Pathway?
Skin exposure to beryllium may result in an inflammatory skin response, including skin ulcerations
Hydrofluoric acid (HF) can cause severe, deep tissue burns and systemic toxicity
  Fatal (life threatening) dermal exposure as HF is absorbed into the skin
Not normally included in air toxics exposure assessments unless dealing with a specifically toxic dermal compound

## Slide 112: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Dermal Pathway can Kill
Karen Wetterhahn, Professor of Chemistry, Dartmouth College
  August 14, 1996, spilled several drops of dimethylmecury onto latex-gloved hand
  Latex gloves were recommended precaution at the time
    Subsequent analysis demonstrated that dimethylmercury can permeate latex gloves
  3 months post incident, experienced significant weight loss
  5 months post incident, mercury poisoning including slurred speech and loss of balance
  10 months post incident, descended into vegetative state and removed from life support; pronounced dead June 8, 1997

## Slide 113: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Characterization
Use modeling (or monitoring) to estimate air toxics concentrations in air, water, soil, food at the point of contact (the EC)
  EC in air is the quantitative measure of exposure for inhalation
  EC in water, soil, and food is used to calculate intake, the quantitative measure of exposure for ingestion
May use exposure modeling to refine the estimate of exposure to study population

## Slide 114: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Estimating Inhalation Exposure Concentration
Concentrations in the contaminated air under study vary over space and time, therefore it is important to know where and how long people spend their time in the study area
Ambient concentrations of pollutants in air can be estimated geographically and temporally through air quality modeling and monitoring
Estimates of exposure via inhalation can be adjusted from modeling data to account for the time spent in various microenvironments

## Slide 115: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Two Methods for Deriving EC in a Risk Assessment
General Air Quality Assessment
  Assume individuals spend all of their time at a given location
Microenvironment Assessment Exposure Modeling
  Analysis incorporates location and length of time into exposure
  EC is sum of the product of ambient concentrations and time at each location

## Slide 116: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Timeframes
Air toxics inhalation exposure assessments usually focus on two of these three different types of possible exposure scenarios:
Chronic exposure – exposure occurs repeatedly over a long period of time (usually years to lifetime)
Sub-chronic exposure – exposure over a time period that ranges between acute and chronic exposures
Acute exposure – exposure occurs over a short period of time (usually minutes, hours, or a day) and usually at relatively high concentrations

## Slide 117: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Common Ways to Estimate Exposure Concentrations
Analysis varies depending on the detail required for assessment
Monitoring locations: Sites where air monitors provide a direct measure of ambient air concentrations at those locations
Point of maximum modeled concentration: A modeling node where the maximum modeled ambient air concentration occurs and may be called the maximum exposed individual (MEI)
Point of maximum modeled concentration at actual receptor: A modeling node where the maximum ambient air concentration occurs at an actual location (maximum individual risk – MIR)

## Slide 118: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Concentration Gradient
Primary Wind
Direction
Monitoring
Site
Facility
Boundary
Model Results
Exposure impacts are unclear, as we do not know where the people are in relation to the facility or the area of impact
Modeling Nodes
(Receptors)
Area of Impact

## Slide 119: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Concentration Gradient
Monitoring
Site
Facility
Boundary
Model Results
Obtain and overlay demographic data (US Census Bureau)
Census data illustrates impacts to the nearby farm (MIR) and nearby towns
Census Tract Boundary
Maximum Exposed Individual (MEI)
SMALLVILLE
National
Forest
Farm Boundary
Smallville
Pop. 4000
Census Block
Internal Points
Maximum Individual Risk (MIR)

## Slide 120: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
National/State/
County Level
Community
Level
Neighborhood
Level
Personal Level
Organ Level
Exposure Assessments by Scale

## Slide 121: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Air Toxics Exposure Assessment is Difficult
Hundreds of air toxics with many different characteristics
  Difficult to model and monitor
  Multiple routes of exposure
Spatial and temporal variability
  Source dominated
  “Hot Spots”
Monitoring issues
  Costs
  Measurement methods

## Slide 122: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Models
We use exposure models to help make refined estimates of exposure
Calculate a refined measure of personal EC
Reflects activities people do in different microenvironments throughout various life stages
Often group people and activities by age, sex, ethnicity, etc. (cohorts)
General Equation for Calculating the EC for a Specific Cohort*
EC = ECiTi
Where:
ECi = exposure concentration in the microenvironment
Ti = fraction of time spent in the microenvironment
Combine cohorts to get an apparent exposure concentration for community as a whole
*Volume 1 of the ATRA Library provides the exact equations

## Slide 123: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
EPA Actions Making Exposure Assessments Easier
Ambient Air Toxics Monitoring Programs
  Air Toxics Trends Sites
  Multimedia Monitoring
Personal exposure studies
Enhanced modeling tools
  Ambient dispersion models
  Exposure models
National Air Toxics Assessments (NATA)
HEM

## Slide 124: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Personal Exposure Models
Ambient Dispersion Models
  Community Multiscale Air Quality (CMAQ)
Exposure Models
  Stochastic Human Exposure and Dose Simulation (SHEDS)
  Human Exposure Model (HEM)
  Hazardous Air Pollutant Exposure Model (HAPEM)
  Air Pollutants Exposure Model (APEX)/Total Risk Integrated Methodology (TRIM)
  California Population Indoor Exposure Model (CPIEM)

## Slide 125: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
CMAQ Model
Provide a tool for developing and evaluating strategies to reduce HAP, and examining the interactions between HAP, ozone, and PM
  Simulations especially relevant for air toxics with significant secondary formation, e.g., formaldehyde, acetaldehyde and acrolein
Community-scale modeling
  Model HAP concentrations at high resolutions and pinpoint risk “hot spots” for HAP within urban areas.
  Philadelphia pilot project with EPA Region 3

## Slide 126: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
CMAQ Benzene Results

## Slide 127: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
SHEDS Model Structure
Output
Population Exposure
Population Dose
Algorithms
Calculate Individual Exposure/Dose Profile
to
t1
TIME
E
X
P.
or
D
O
S
E
Ingestion
to
t1
TIME
E
X
P.
or
D
O
S
E
Dermal
to
t1
TIME
E
X
P.
or
D
O
S
E
Inhalation
Input Databases
Exposure Factor Distributions
Census
Human Activity
Ambient Conc.
Food Residues
Recipe/Food Diary

## Slide 128: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
SHEDS Model
Estimates human exposure and dose to multimedia, multipathway pollutants
  Predict population exposures and dose
  Characterizes variability and uncertainty in exposure and dose estimates
  Identify important exposure media, routes, pathways, and interferences
  Identify contributions from different sources (single pathway) and different routes and pathways for single (aggregate) or multiple chemicals (cumulative)
  Prioritize measurement data needs

## Slide 129: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
HEM
Risk assessment for major air toxics using AERMOD
Only addresses the inhalation pathway of exposure
  Designed to predict risks associated with inhalation exposure
Produces estimates of cancer risk and non-cancer hazards for air toxics
  Lifetime cancer risk
  Chronic noncancer hazard index
  Acute concentrations for each receptor location
Estimates hourly concentrations for chemical and receptor site

## Slide 130: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
HAPEM
Estimates inhalation exposure for selected population groups for various air toxics
  Uses ambient air concentration data, indoor/outdoor microenvironment concentration relationship data, population data, and human activity pattern data
  Estimate an expected range of inhalation exposure concentrations for defined groups of individuals
Current version is HAPEM7 from July 2015

## Slide 131: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
TRIM Components
Inhalation Risk Assessments (APEX/TRIM.Expo)
  Residual risk assessments (HAPs) – refined tier
  Ozone NAAQS exposure and risk assessment
  Lead NAAQS exposure and risk assessment
Ecological Risk Multimedia Assessments (TRIM.Risk)
  Residual risk assessments (e.g., Hg, etc.)
Ingestion Risk Assessments (TRIM.FaTE)
  Residual risk multimedia, multipathway assessments (e.g., Hg, dioxins, PAHs)
  NAAQS – Lead

## Slide 132: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
APEX/TRIM.Expo
APEX is the inhalation exposure model within TRIM
Local, urban, and consolidated metropolitan area scale
Only addresses inhalation exposure
Incorporates microenvironments
Results are hourly and summary exposures and dose estimates

## Slide 133: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
TRIM
Inhalation Risk Assessments (APEX)
  Residual risk assessments (HAP) – refined tier
  Ozone NAAQS exposure and risk assessment
  Lead NAAQS exposure and risk assessment
Ecological Risk Multimedia Assessments
  Residual risk assessments (e.g., Hg, etc.)
Ingestion Risk Assessments
  Residual risk multimedia, multipathway assessments (e.g., Hg, dioxins, PAH)
  NAAQS – Lead

## Slide 134: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
TRIM.FaTE
(Fate, Transport & Ecological Exposure)
TRIM.Risk
(Risk Characterization)
Farm
Food Chain
LIBRARY -
Inputs (e.g.,
physical/chemical properties,
site-specific data, alt algorithms, etc)
INPUTS -
Activity and population data, indoor / outdoor concentrations, etc.
HH Tox Database
Inputs:
human health
dose-response assessments
(e.g., RfC, URE)
Eco Tox Database
Inputs:
Ecological effects
Assessments
(e.g., endpoints, criteria)
Eco
HH
Multimedia Impacts
Ingestion
Inhalation
TRIM.Expo
(Human Exposure Event)
Air-ONLY Impacts
AQ Model
Or
AQ Data
[Inhalation Risk] [Ingestion Risk] [Eco Risk]
TRIM.APEX
TRIM.Expo

## Slide 135: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Comparison of Exposure Assessment Tools
 | PRO | CON
Ambient Monitoring | “True” measure of ambient concentration | Spatial and temporal gaps Costly to monitor everywhere Surrogate for personal exposure
Personal Monitoring | “True” measure of personal exposure | Spatial and temporal gaps Can’t monitor everyone all the time (costs and personal inconvenience)
Ambient Modeling | Good spatial and temporal coverage Relatively low cost | Relatively high uncertainty Surrogate for personal exposure
Human Exposure Modeling | Estimates true human exposure Relatively low cost | Relatively high uncertainty
The best approach is to utilize a combination of the above. |  | 

## Slide 136: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Model | Population Activity Data | Source of Ambient Concentrations | Spatial Resolution | Framework
HEM-3 | None (screening model) | AERMOD | Census blocks (additional points can be specified) | Deterministic
HAPEM | Micro-environment time/sequence, commuting | External model or monitoring data | Census tract | Stochastic
TRIM.Expo | Micro-environment time/sequence, commuting | External model or monitoring data | Depends on resolution of air quality and demographic inputs | Stochastic
CPIEM | Micro-environment time/sequence, commuting | External model or monitoring data | User-specified for the selection of activity patterns (i.e., state, region) | Stochastic

## Slide 137: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Data Sources for Personal Exposure Models
EPA Consolidated Human Activity Database (CHAD)
EPA Exposure Factors Handbook
Human Exposure Database System (HEDS)
National Human Exposure Assessment Survey (NHEXAS)
Other Data
U.S. Census: Data & Commuting Database for Workers
CDC National Health and Nutrition Examination Survey (NHANES)

## Slide 138: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
CHAD
Contains data obtained from pre-existing human activity studies that were collected at city, state, and national levels
Intended as an input file for exposure/intake dose modeling and/or statistical analysis
Database providing access to other human activity databases using a consistent format

## Slide 139: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
Exposure Factors Handbook
Summarizes data on behaviors and characteristics that affect exposure
Recommended values for use in exposure assessments
Updated by EPA in 2011
  Individual chapters updated since in 2017, 2018, and 2019

## Slide 140: TOXC102+ Chapter 5: Exposure Assessments Assessing Exposure
NHEXAS
Evaluated comprehensive human exposure to multiple chemicals on a community and regional scale
  Addressed some of the limitations of single-chemical, and single media exposure route studies from 1999-2002
HEDS
Database of some NHEXAS and other research studies
Other
Microenvironmental factors and other guidance can be found within models or within EPA website archives

## Slide 141: TOXC102+ Chapter 5: Exposure Assessments Review Questions
What is exposure assessment?
  Measuring how much people are exposed to air toxics
What is acute exposure?
  Short-term exposure to a usually high amount of air toxics
What is chronic exposure?
  Long-term (lifetime) exposure to a usually low amount of air toxics
What is sub-chronic exposure?
  Between acute and chronic exposure
What is a plume model (AERMOD)?
  Emissions calculated in a plume using steady-state dispersion

## Slide 142: TOXC102+ Chapter 5: Exposure Assessments Review Questions
What is a puff model (CALPUFF)?
  Emissions calculated in a discrete puffs in time and space
What is the difference between monitoring and modeling?
  Monitoring measures air pollution; modeling estimates air pollution
What kind of weather helps pollutants spread more?
  High winds and storms
Where is the receptor in an air model?
  Nodes (intersection of cartesian / polar grids) & user-defined coordinates
How does the Human Exposure Model determine exposure?
  AERMOD