## Slide 1: Air Toxics & Regulating Hazardous Air Pollutants
TOXC102+ Chapter 9: Compliance

## Slide 2: TOXC102+ Chapter 9: Compliance Emissions Testing
Source Sampling
Determining the emissions rate of air pollution from a source
  Stack testing, performance testing, air emissions testing
  Demonstrate compliance with emission limits
  Provides information for risk assessments
EPA Reference Methods
  00 series (<100) – New Source Performance Standards (40 CFR 60, Appendix A)
  100 series – NESHAP (40 CFR 61, Appendix B)
  200 series – State Implementation Plans (40 CFR 51, Appendix M)
  300 series – NESHAP-MACT (40 CFR 63, Appendix A)

## Slide 3: TOXC102+ Chapter 9: Compliance Emissions Testing
EPA Method Categories
Category A: Test methods promulgated in Federal Register
  Reference Methods in Series 00, 100, 200, or 300
Category B: Alternative methods approved by EPA
  Alternatives to Category A; option to determine compliance without EPA approval
Category C: Other test methods that are not yet part of rulemaking
  Alternative to Category A; option to determine compliance with EPA approval
Category D: Historic methods no longer part of Reference Methods
  Option to determine compliance with EPA approval

## Slide 4: TOXC102+ Chapter 9: Compliance Emissions Testing
Hazardous Waste Source Sampling
Many of the reference test methods were combined with analytical methods for hazardous materials to establish HAP sampling methods
SW-846 is the compendium of analytical and test methods used in determining regulatory compliance under RCRA

## Slide 5: TOXC102+ Chapter 9: Compliance Emissions Testing
VOHAP
Majority of HAP are VOC but testing for VOC can be confusing
  There is no straightforward way to measure the VOC emissions since there is no way to separate VOC by vapor pressure
  All reference methods for organic compounds have inherent limitations that restrict their applicability
  No one method can characterize VOC emissions from an industrial source

## Slide 6: TOXC102+ Chapter 9: Compliance Emissions Testing
VOC HAP
Reference test methods categorize organic compounds differently
  Total Organic Compounds (TOC): The sum of all volatile organic compounds and all exempted compounds.
  Total Hydrocarbons (THC): The subset of total organic compounds containing only carbon and hydrogen.
  Total Non-Methane Organic Compounds (TNMOC): The sum of all volatile organic compounds and all exempted compounds listed in 40 CFR§51.100(s)(1), except methane.

## Slide 7: TOXC102+ Chapter 9: Compliance Emissions Testing
Identifying Source Sampling Requirements
Pennsylvania Department of Environmental Protection provides a general scheme for selecting a VOC test method
  Provides two different paths, one for speciated VOC and one for non-speciated VOC (total VOC)
    www.dep.pa.gov/Business/Air/BAQ/BusinessTopics/SourceTesting/Pages/default.aspx
Ray Merrill’s Method Decision Tree
  Ray Merrill works for EPA’s Air Emission Measurement Center
  From his February 20, 2015 presentation “Speciated VOC Methods-Overview”
    www3.epa.gov/ttn/emc/meetnw/2015/speciatedvoc.pdf

## Slide 8: TOXC102+ Chapter 9: Compliance Emissions Testing
General Scheme for the Selection of a VOC
Reference Method – No Speciation

## Slide 9: TOXC102+ Chapter 9: Compliance Emissions Testing
General Scheme for the Selection of a VOC
Reference Method – Speciation

## Slide 10: TOXC102+ Chapter 9: Compliance Emissions Testing
Ray’s Decision Tree for Speciated VOC

## Slide 11: TOXC102+ Chapter 9: Compliance Emissions Testing
Reference Test Method 18
VOC by gas chromatograph (GC): Separates gas stream components in a GC column and measures separated components with suitable detector (i.e., Flame Ionization Detector – FID)
Can be used in direct sampling and bag / adsorbent tube sampling
  Cannot be used with Summa canisters, as they react with polar compounds
GC/FID determine the concentrations of individual organic compounds
Applicable to VOC concentrations >1 ppm in the sampled gas
  Problems measuring formaldehyde and gas streams with large number of VOC
  Cannot measure polymeric compounds and VOC with low vapor pressure

## Slide 12: TOXC102+ Chapter 9: Compliance Emissions Testing
Method 18 Sampling Systems
Direct Sampling Train Bag Sampling

## Slide 13: TOXC102+ Chapter 9: Compliance Emissions Testing
Reference Test Method 25
25: Measures VOC as total gaseous NMOC, both condensable and non-condensable, as total carbon in emissions
  All NMOC are converted to methane before measuring with FID
25A: FID measures total gaseous organics consisting primarily of alkanes, alkenes, and/or aromatic hydrocarbons
  Results in ppmv of carbon, propane, or other organic calibration gas
25B: Organic concentration using an infrared analyzer
25C: NMOC from landfills using FID, as methane
25D/E: VOC from waste samples using FID

## Slide 14: TOXC102+ Chapter 9: Compliance Emissions Testing
Method 25 Sampling Train

## Slide 15: TOXC102+ Chapter 9: Compliance Emissions Testing
Reference Test Methods
Method 320: VOC and Inorganics by Extractive Fourier Transform Infrared (FTIR) Spectroscopy
Used to analyze vapor phase organic or inorganic compounds which absorb energy in the mid-infrared spectral region
Wavelength of IR absorption is characteristic of chemical bond
  Unique “fingerprints” for each mixture
  Measure more than 100 of the 187 HAP

## Slide 16: TOXC102+ Chapter 9: Compliance Emissions Testing
Method 320 Example FTIR Spectra
Reference spectra for 103 compounds
Spectra available in SPC formats
www3.epa.gov/ttn/emc/ftir/index.html

## Slide 17: TOXC102+ Chapter 9: Compliance Emissions Testing
Reference Test Methods
Method 308: Methanol using GC and FID
Method 316: Formaldehyde from Mineral Wool / Wool Fiberglass
  ALT-026: Formaldehyde from source subject to the Hazardous Organics NESHAP can use Method 316
Method 323: Formaldehyde from natural gas combustion using chemical analyses and colorimeter

## Slide 18: TOXC102+ Chapter 9: Compliance Emissions Testing
Speciation VOC Methods
SW-846
  Method 0010 for SVOC
  Method 0011 is used for aldehydes and ketones
  Method 0030 is used for VOC (compounds with boiling points >30ºC and <100ºC)

## Slide 19: TOXC102+ Chapter 9: Compliance Emissions Testing
SW-846 Method 0030 Analytes: Air Toxics – VOC |  | 
Acrylonitrile | Benzene | Carbon Disulfide
Carbon Tetrachloride | Chloroform | Chloroprene
Ethyl Chloride | Ethylene Dichloride | Methyl Chloride
Methyl Chloroform | Methylene Chloride | Propylene Dichloride
Propylene Oxide | Tetrachloroethylene | Trichloroethylene
Vinyl Acetate | Vinyl Chloride | 

## Slide 20: TOXC102+ Chapter 9: Compliance Emissions Testing
Detection Limits / Limits of Quantification
Detection Limit: Minimum concentration that an instrument can reliably expect to find in a sample (i.e., distinguish from zero)
  Method Detection Limit (MDL) is established for each instrument
  An MDL of 1μg/m3 means a contaminant will not be detected by the instrument in question at concentrations less than 1 µg/m3
Limit of Quantification (LOQ): Minimum concentration that an instrument can reliably say is present at specific concentration
  An LOQ of 2 μg/m3 means results may be reported as being present at a specific concentration above 2 μg/m3

## Slide 21: TOXC102+ Chapter 9: Compliance Modeling Used for Risk Assessment
Modeling
Important to review modeling parameters
Geographical coordinates (meters)
  Universal Transverse Mercator – UTM
  Conversion from latitude / longitude
Emissions rate (lbs./hour)
Stack inside diameter (feet)
Release height (feet)
Flowrate (cubic feet) or velocity (feet/second)
Exhaust temperature (ºF)

## Slide 22: TOXC102+ Chapter 9: Compliance Modeling Used for Risk Assessment
1 pound / hour
Ambient Temp
2 feet diameter
20,000 acfm
Max: 219 µg/m3

## Slide 23: TOXC102+ Chapter 9: Compliance Modeling Used for Risk Assessment
1 pound / hour
100º F
3 feet diameter
29,000 acfm
Max: 147 µg/m3

## Slide 24: TOXC102+ Chapter 9: Compliance NESHAP Review
Anatomy of a NESHAP
Generally, NESHAP have five categories of requirements
Applicability Criteria
Emission Limits
Testing & Monitoring
Recordkeeping
Reporting

## Slide 25: TOXC102+ Chapter 9: Compliance NESHAP Review
Applicability Criteria
List the "affected source(s)" subject to regulation
May list exempted sources not subject to regulation
Applicability Criteria
Emission Limits
Testing & Monitoring
Recordkeeping
Reporting

## Slide 26: TOXC102+ Chapter 9: Compliance NESHAP Review
Emissions Limits
Emissions standards limit HAP pollution allowed to be emitted
  Expressed in mass of pollutant emitted per unit volume effluent gas (PPM, µg/m3), mass per unit time (kilograms/hour), or mass per unit volume (kilograms/liter)
Emission Limits
Testing & Monitoring
Recordkeeping
Reporting

## Slide 27: TOXC102+ Chapter 9: Compliance NESHAP Review
Testing & Monitoring
Sources (especially with control devices) may be required to perform emissions (stack) testing
  Initial emissions testing to demonstrate compliance and establish control device parameters
  Additional emissions testing on a repeating cycle
Control device parameter and process monitoring
Testing & Monitoring
Recordkeeping
Reporting

## Slide 28: TOXC102+ Chapter 9: Compliance NESHAP Review
Recordkeeping
Provisions requiring maintenance of records relevant to the requirements of the standard
  Notifications and reports submitted to agency
  Emissions test results
  Control device parameters
  Process (coating) records
Required to be kept for 5 years
Recordkeeping
Reporting

## Slide 29: TOXC102+ Chapter 9: Compliance NESHAP Review
Reporting
Compliance reports submitted to EPA and/or LST air agency regarding compliance with and deviations from the standard
  Initial Notification (applicability of standard)
  Notification of Compliance Status - semi-annual
  Emissions test results
Reporting

## Slide 30: TOXC102+ Chapter 9: Compliance NESHAP Review
40 CFR 61, Subpart M – Asbestos
Establishes control equipment and emissions standards
  Asbestos mills – converting asbestos ore into commercial asbestos
  Manufacturing – combining commercial asbestos with other materials
  Demolition and renovation – most common asbestos concern
  Spraying – operations that spray asbestos
  Fabricating – processing products that contain asbestos
  Insulating Materials – insulating asbestos other than spraying
  Waste Disposal – asbestos to the landfill
ALL alternatives must be proposed and approved in FR notices

## Slide 31: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart A – General Provisions
Construction: Onsite installation of an affected source
Reconstruction: Replacement of components to extent that:
  The fixed capital costs of the new components exceeds 50% of the fixed capital cost to construct a new source; AND
  It is technologically and economically feasible for the reconstructed source to meet the relevant standards.
Compliance Date: Date by which an affected source must comply with the applicable requirement

## Slide 32: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart M – Dry Cleaning
Only applies to perchloroethylene dry cleaning operations
  Carbon dioxide, wet cleaning, and Stoddard (petroleum), methyl siloxane, and other synthetic solvents are not included in regulation
  40 CFR, Part 60, Subpart JJJ applies to Petroleum Dry Cleaners
Major, Large Area, and Small Area categories
RTR completed on 12/09/2005
  Required closed-loop systems with refrigerated condensers or carbon adsorbers
  Enhanced leak detection and repair
  Eliminate use of transfer machines at area sources

## Slide 33: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart N – Chromium Electroplating
Only applies to chrome electroplating
  Applies to both hexavalent and trivalent chrome
  Cadmium, lead, manganese, and nickel plating and polishing at area sources subject to 40 CFR 63, Subpart WWWWWW (6W)
Major and area source categories
  Hard – thick layer of chrome to change functional properties of base material
  Decorative – thin layer of chrome for a bright surface
  Anodizing – chromic acid oxidizes aluminum for high-stress / corrosion resistance
RTR completed 10/21/2010 with more restrictive control requirements

## Slide 34: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart T – Halogenated Solvent Cleaning
Methylene chloride, perchloroethylene, trichloroethylene, trichloroethane, carbon tetrachloride, and chloroform
  Solvents must be used as a cleaning / drying agent
  Does not apply to wipe or spray cleaners
Batch (bath) and in-line (continuous) machines
  Solvents can be in liquid (cold) or vapor forms
RTR completed 12/14/2006 with facility-wide emissions limits
  No facility-wide emissions limits for continuous web solvent cleaners or solvent cleaners at narrow tube and aerospace manufacturing facilities

## Slide 35: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart HH – Oil & Natural Gas Production
Oil and natural gas production and plants that process, upgrade, or store natural gas or hydrocarbon (unrefined petroleum) liquids
Major sources: Glycol dehydrators, storage vessels, compressors and ancillary equipment (pumps, lines, valves, pressure relief devices, etc.)
  Does not apply if subject to 40 CFR 60, Subpart OOOO
Area sources: Triethylene glycol dehydration units
  Within 2 miles of an Urbanized Area (50,000 people) or within an urban cluster (10,000 people) – UA plus offset UC boundary) – major source requirements
  Outside of UA plus offset UC boundary – optimum glycol circulation rate

## Slide 36: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart HHH – Natural Gas Transmission & Storage
Glycol dehydration units within natural gas transmission and storage facilities that are major sources
RTR completed 08/23/2011 for both Subparts HH and HHH
  Expanded to include small glycol dehydrators
Note: Both Subparts HH and HHH allow the use of natural gas computer modeling programs to estimate flow and emissions
  American Petroleum Institute (API) E&P Tanks – No longer supported
  AspenTech HYSYS – Annual license ($1X,000)
  Bryan Research & Engineering ProMax – Annual license ($X,000)
  Gas Research Institute (GRI) GLY-Calc – Built in 1996 for Windows 95 ($295)

## Slide 37: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart ZZZZ – Reciprocating Internal Combustion Engines (RICE)
Applies to stationary RICE at both area and major sources
  Compression ignition (diesel, bio-diesel, dual-fuel)
  Spark ignition (gasoline, liquified petroleum gases, landfill gases)
RICE are used to provide motive power
  Provide power for backup, portable, or emergency electricity generators
  Provide power to pump natural gas, water, or other liquids and gases
Original rule was modified five times to include different RICE
  Rule contains over 66 different categories of RICE
  New sources subject to 40 CFR, Part 60, Subpart IIII (Compression Ignition) and JJJJ (Spark Ignition) with an additional 50 and 38 categories of RICE

## Slide 38: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart ZZZZ – RICE Categories
New, Existing, and Reconstructed
Digester / Landfill Gas
Compression Ignition
  Horsepower and cylinder displacement (liters)
Spark Ignition
  2-stroke / 4-stroke, Lean Burn / Rich Burn, and Horsepower
Emergency, Limited Use, Black Start
Residential, Commercial, and Institutional (see 08/09/2010 EPA memo)
  www.epa.gov/sites/production/files/2014-03/documents/9_30_2010_guidance_emergency_engine_def.pdf

## Slide 39: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart ZZZZ – RICE Issues
Emergency Demand Response
  Emergency engines cannot be used to provide electrical power to PREVENT a blackout (Delaware v. EPA, D.C. Circuit 2015 No. 13-1093)
New vs existing
  Manufacture date: date engine was manufactured
  Construction date: date engine was installed onsite
    Construction does not include removal of an affected source to a new location unless it is considered reconstruction
Stationary
  RICE cannot be used to move itself or it is a mobile source

## Slide 40: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart ZZZZ – Certified RICE
EPA issues a Certificate of Conformity to certain types of engines
  Certified engines must be configured, operated, and maintained according to manufacturer’s instructions
  Non-certified engines must have a maintenance plan and performance tests
EPA maintains a database of engines with Certificates of Conformity
www.epa.gov/compliance-and-fuel-economy-data/annual-certification-data-vehicles-engines-and-equipment

## Slide 41: TOXC102+ Chapter 9: Compliance NESHAP Review
EPA Certificate of Conformity

## Slide 42: TOXC102+ Chapter 9: Compliance NESHAP Review
Valid RICE Certification
Invalid RICE Certification

## Slide 43: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart DDDDD – Industrial, Commercial, and Institutional Boilers
Applies to boilers and process heaters located at major sources
  Boilers subject to another NESHAP are exempted from this subpart (Electric Generating Units, Recovery Boilers, hazardous waste combustor, control device)
Controls emissions of hydrogen chloride, mercury
  Filterable PM surrogate for metal HAP; CO surrogate for VOHAP
21 subcategories based on fuel type
  Solid, liquid, gaseous, biomass/bio-based solids
  Metal process furnaces, limited-use, and process heaters
One-time energy assessment

## Slide 44: TOXC102+ Chapter 9: Compliance NESHAP Review
Subpart JJJJJJ – Industrial, Commercial, and Institutional Boilers
Applies to boilers and process heaters located at area sources
  Boilers subject to another NESHAP are exempted from this subpart
  Temporary, gas-fired, electric, and residential boilers exempt
Controls emissions of mercury
  Filterable PM used as a measure of metal HAP
  CO used as a measure of VOHAP
7 subcategories by fuel and use
One-time energy assessment

## Slide 45: TOXC102+ Chapter 9: Compliance NESHAP Review
Surface Coatings (excluding printing)
Subpart JJ – Wood Furniture
Subpart IIII – Auto and Light Duty Truck
Subpart KKKK – Metal Can
Subpart NNNN – Large Appliances
Subpart MMMM – Miscellaneous Metal Parts & Products
Subpart PPPP – Plastic Parts
Subpart QQQQ – Wood Building Products
Subpart SSSS – Metal Coil
Subpart RRRR – Metal Furniture

## Slide 46: TOXC102+ Chapter 9: Compliance NESHAP Review
Surface Coatings (excluding printing)
Generally 3 compliance options
  Use only compliant coatings
  Use non-compliant coatings and compliant coatings such that the average is compliant
  Use a control device
HAP content of compliant coatings
  Pounds of VOHAP per pound of coating solids, as emitted (including cleaners)
    Comparison between weight of VOHAP per weight of solids in coating
    Calculate total weight of organic HAP emitted and divide by total weight of solids applied
  Pounds of VOHAP per gallon of coating solids, as emitted (including cleaners)
    Comparison between weight of VOHAP per volume of solids in coating
    Calculate total weight of organic HAP emitted and divide by total volume of solids applied

## Slide 47: TOXC102+ Chapter 9: Compliance NESHAP Review
Can of Coating
Can of Coating
Only solids & VOHAP
Volatile Content
Non-Volatile
Content

## Slide 48: TOXC102+ Chapter 9: Compliance NESHAP Review
Surface Coating
Many coating manufacturers have gone to low VOHAP / high solids coatings
  Still must include thinners and cleaners to determine as emitted
Manufacturers can provide certifications for VOHAP content of coatings
  VOC content may not equal VOHAP content, as not all VOC are VOHAP
  VOC / VOHAP may not equal total volatile content, as coating may contain water and exempt solvents (e.g., acetone)
Each coating NESHAP has compliance options if multiple NESHAP apply
  Each operation complies with each NESHAP separately
  Comply with NESHAP for predominant surface coating activity
  Calculate a facility-specific emissions limit that combines limits from applicable NESHAP

## Slide 49: TOXC102+ Chapter 9: Compliance NESHAP Review
Surface Coatings (excluding printing)
Generally 3 compliance options
  Use only compliant coatings
  Use non-compliant coatings and compliant coatings such that the average is compliant
  Use a control device
HAP content of compliant coatings
  Pounds of VOHAP per pound of coating solids, as emitted (including cleaners)
    Calculate total weight of organic HAP emitted and divide by total weight of solids applied
  Pounds of VOHAP per gallon of coating solids, as emitted (including cleaners)
    Calculate total weight of organic HAP emitted and divide by total volume of solids applied
  EPA established a default solids density of 10.5 lbs. solids/gallon solids for conversions

## Slide 50: TOXC102+ Chapter 9: Compliance NESHAP Review
NESHAP Applicability Process
HAP Emissions Inventory
  Determine if an Area or Major Source
Identify Applicable NESHAP
  Identify Affected Sources and Review Exemptions
Establish emission limits, control requirements, operating restrictions, work practices, and record keeping and reporting requirements
  General Provisions: Initial notification, notification of compliance status, and application for approval of construction or reconstruction
Determine LST Air Agency Delegation Status

## Slide 51: TOXC102+ Chapter 9: Compliance NESHAP Review
Points to Remember
Facilities may emit HAP but may not be included in a NESHAP
Emissions units may not match definition of affected source
Only a major source NESHAP may exist
  70 area source categories vs 174 major source categories
Changes in fuel or materials may increase or decrease HAP emissions
  Coatings have a wide range of HAP content
  Different grades of fuel have different HAP content

## Slide 52: TOXC102+ Chapter 9: Compliance NESHAP Review
Adjacent and Contiguous
EPA published two separate memoranda regarding the terms “adjacent” and “contiguous” as used in the Title V and NSR programs
  04/30/2018 Memorandum to Pennsylvania DEP regarding Meadowbrook Biogas Processing Facility and Keystone Sanitary Landfill
  09/04/2018 Draft Memorandum to Regional Air Division Directors, “Interpreting ‘Adjacent’ for NSR and Title V Source Determinations”
These memoranda do not impact NESHAP determinations
  “Contiguous” is specifically used in the Clean Air Act §112, but not Title V & NSR
  EPA has received comments requesting these policies extend to NESHAP

## Slide 53: TOXC102+ Chapter 9: Compliance NESHAP Review
NESHAP Assistance
EPA list of NESHAP Rules and Compliance Tools
www3.epa.gov/ttn/atw/eparules.html
EPA Applicability Determination Index (ADI)
cfpub.epa.gov/adi/
EPA Risk and Technology Review Schedule
www3.epa.gov/ttn/atw/rrisk/rtrpg.html

## Slide 54: TOXC102+ Chapter 9: Compliance Review Questions
What is the purpose of emissions (stack) testing?
  Measure how much and what type of pollution a source generates
What are common organic compound EPA Test Methods?
  Methods 18 and 25; Method 320
What is LOQ?
  Limit of Quantification: Minimum concentration reliably detected
How long do facilities keep MACT records?
  5-years
What is an EPA Certificate of Conformity?
  Internal combustion engine meets emissions standard (Subpart ZZZZ)